[BS-7] HVAC Performance Validation

Object Type Definition Tables

This document forms the object type definition part of the draft 4 document of IAI R3.0 Domain project [BS-7] HVAC Performance Validation. Compared to the earlier review version of the draft 4 document, in this new version of the document the latest IFC 2x model and the review comments, mainly by Phil Haves, have been taken into account. Regarding IFC 2x some property sets and attributes were already included  into IFC 2x, so they have been removed from this version. Also in IFC 2x some property sets of IFC 2.0 were defined as classes. In this document the corresponding property sets have been changed to classes. Finally, all review comments have been reviewed by the project team and taken into account if possible in the data definitions. In reviewing the comments and IFC 2x the project manager of IFC R3.0 has also been consulted.

An important question that has been left unsolved in this project concerns standard references. It's obvious that standard references are needed. Some kind of general method is needed for referring (HVAC) standards, because different standards are used in different parts of the world and standards are not permanent. So it is not necessary long lasting to include current standard names in attribute definitions. Also different attributes of a property set or class  may have different standards, so one standard for the whole property set or class is not enough. In worst case it had to be defined the corresponding standard for each attribute. This issue is more general than concerning only HVAC domain and should thus be solved on a lower level of IFC model hierarchy than domain project level.

1. ADDITIONS TO EXISTING CLASSES	2

1.1. IfcValve	2

1.2. IfcAirFilter	2

1.3. IfcCoil	2

1.4. IfcFluidMovingDevice	3

1.5. IfcBoiler	3

2. ADDITIONS TO EXISTING PROPERTY SETS	3

2.1. Pset_ControlDamper	3

2.2. Pset_ElectricActuator	4

2.3. Pset_AirHandler	4

3. ADDITIONS TO EXISTING DATA TYPES	4

3.1. IfcControllerTypeEnum	4

3.2. IfcActuatorTypeEnum	5

4. NEW CLASSES	5

4.1. IfcCooledBeam	5

4.2. IfcHumidifier	6

4.3. IfcDuctedSilencer	6

4.4. IfcHeatRecoveryUnit	7

4.5. IfcRadiator	8

5. NEW PROPERTY SETS	8

5.1. Pset_CooledBeamDesignCriteria	8

5.2. Pset_AirHandlerDesignCriteria	9

5.3. Pset_ValveCharacteristics	10

5.4. Pset_DamperCharacteristics	10

5.5. Pset_FluidMovingDeviceCharacteristics	10

5.6. Pset_ControlDamperAdjustments	11

5.7. Pset_ValveAdjustments	11

5.8. Pset_RadiatorSystemDesigCriteria	11

5.9. Pset_RadiatorDesignCriteria	12

5.10. Pset_ThermostaticActuator	12

5.11. Pset_HeatingCurve	12

5.12. Pset_BoilerAdjustments	12

5.13. Pset_RadiatorAdjustments	13

5.14. Pset_HeatingCurveAdjustments	13

5.15. Pset_MeteorologicalData	13

6. NEW TYPE DEFINITIONS	14

7. NEW DATA TYPES	15

7.1. IfcSoundMeasure	15

7.2. IfcHeatCapacityMeasure	15

7.3. IfcPowerPerVolumetricFlowRateMeasure	15

7.4. IfcTorqueMeasure	16

# ADDITIONS TO EXISTING CLASSES

## IfcValve

|  | Class Name |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Interface name |  | {{ "Ref" = relationship }} |  |  |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  | Attribute / Relation name | Definition | Data Type or Related Object Type | Min | Max | Default |
|  | IfcValve |  |  | This class defines elements of a valve, which typically is used in an HVAC piping distribution system to control or modulate the flow of the fluid. |  |  |  |  |
|  |  |  |  |  |  |  |  | I_Valve : FlowController |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | FlowCharacteristics | Flow characteristics (under a standard test) | IfcPropertySet (Pset_ValveCharacteristics) | n/a | n/a | NIL |
|  |  |  |  |  |  |  |  |  | Rangability | Ratio of fully open flow rate to minimum controllable flow rate, at constant pressure drop (under a standard test) | IfcSimplePropertyWithUnit (IfcReal) | 0 | n/a | NIL |
|  |  |  |  |  |  |  |  |  | Leakage | Ratio of leakage flow rate to fully open flow rate, at constant pressure drop (under a standard test) | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  |  |  |  |  |  | Adjustments | Reference to the Property Set defining adjustable parameters | IfcComplexProperty (SET [1:4] OF IfcPropertySet (Pset_ValveAdjustments)) | n/a | n/a | NIL |

## IfcAirFilter

| IfcAirFilter | Describes air filter product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | DustHoldingCapacity | The amount of dust by weight retained by a filter (under a standard test such as EN779) | IfcSimplePropertyWithUnit (IfcMassMeasure) | 0 | n/a | NIL |
|  |  |  |  | RegeneratedSound | Regenerated sound (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | SoundAttenuation | Sound attenuation (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | Height | Height of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Width | Width of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |

## IfcCoil

| IfcCoil | describes coil product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | EnergySource | Energy source | IfcEnergySourceEnum | n/a | n/a | NIL |
|  |  |  |  | Height | Height of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Width | Width of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Length | Length of heat transfer surface in direction of flow | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | EnteringAirTemperature | List of air temperatures of entering conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | LeavingAirTemperature | List of air temperatures of leaving conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | AirFlowRate | Air flow rate | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | AirPressureDrop | Air pressure drop at the related air flow rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | RegeneratedSound | Regenerated sound (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | SoundAttenuation | Sound attenuation (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |

## IfcFluidMovingDevice

| IfcFluidMovingDevice | Describes fluid mover product data. A Fluid mover is equipment that performs mechanical work on a fluid (e.g., pump, fan) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | FlowCharacteristics | Flow characteristics (under a standard test) | IfcPropertySet (Pset_FluidMovingDeviceCharacteristics) | n/a | n/a | NIL |

## IfcBoiler

| IfcBoiler | describes boiler product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | OperatingModeEnum | reference to the operating mode of the boiler | IfcEnumeratedProperty (Fix, TwoStep, Modulating, Other, NotKnown, Unset) | n/a | n/a | NIL |
|  |  |  |  | StandardThermalOutput | thermal output of boiler under standard test conditions | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardInletWaterTemperature | inlet water temperature under standard test conditions | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardOutletWaterTemperature | outlet water temperature under standard test conditions. | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardUpperHeatOutputRange | upper heat output range related to standard test conditions | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardLowerHeatOutputRange | lower heat output range related to standard test conditions | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | UpperHeatOutputRange | upper heat output range design 60/80 °C | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | LowerHeatOutputRange | lower heat output range design 60/80 °C | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | MaximumFlueGasTemperature | flue gas temperature at maximum load | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | Load60PercentFlueGasTemperature | flue gas temperature at part load of 60 %, design 60/80 °C | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | WaterCapacity | boiler water capacity. | IfcSimplePropertyWithUnit (IfcVolumeMeasure) | n/a | n/a | NIL |
|  |  |  |  | Lambda | stoichiometic fuel/air ratio | IfcSimpleProperty (IfcReal) | n/a | n/a | NIL |
|  |  |  |  | Adjustments | Reference to the property set defining adjustable parameters | IfcComplexProperty (SET [1:4] OF IfcPropertySet (Pset_BoilerAdjustments)) | n/a | n/a | NIL |

# ADDITIONS TO EXISTING PROPERTY SETS

## Pset_ControlDamper

| Pset_ControlDamper | describes control damper product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | FlowCharacteristics | Flow characteristics (under a standard test) | IfcPropertySet (Pset_DamperCharacteristics) | n/a | n/a | NIL |
|  |  |  |  | Height | Height of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Width | Width of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | RegeneratedSound | Regenerated sound (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | SoundAttenuation | Sound attenuation (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | MinimumOperatingTorque | Minimum operating torque (under a standard test) | IfcSimplePropertyWithUnit(IfcTorqueMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumAllowableTorque | Maximum allowable torque (under a standard test such as EN 1751) | IfcSimplePropertyWithUnit(IfcTorqueMeasure) | 0 | n/a | NIL |
|  |  |  |  | Adjustments | Reference to the Property Set defining adjustable parameters | IfcComplexProperty (SET [1:4] OF IfcPropertySet (Pset_ControlDamperAdjustments)) | n/a | n/a | empty list |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcDamper |  |  |  |  |  |

## Pset_ElectricActuator

| Pset_ElectricActuator | describes electric actuator product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Movement | Rotary or linear | IfcEnumeratedProperty (Rotary, Linear, Other, NotKnown, Unset) | Rotary | Unset | Rotary |
|  |  |  |  | HasPositioner | True if actuator has a positioner | IfcSimpleProperty (IfcBoolean) | FALSE | TRUE | FALSE |
|  |  |  |  | FailPosition | Position of actuator if power fails | IfcEnumeratedProperty (Closed, Open, CurrentPosition, Other, NotKnown, Unset) | Closed | Unset | Closed |
|  |  |  |  | Hysteresis | Hysteresis. A measure of the differences in output for a system responding to the identical steady state input when approached from different directions. | IfcSimplePropertyWithUnit (IfcReal) | 0 | n/a | NIL |
|  |  |  |  | StrokeTime | Stroke time | IfcSimplePropertyWithUnit (IfcTimeMeasure) | 0 | n/a | NIL |
|  |  |  |  | RangeAngle | Range of movement (rotary actuators only) | IfcSimplePropertyWithUnit (IfcAngleMeasure) | n/a | n/a | NIL |
|  |  |  |  | Torque | Torque (rotary actuators only) | IfcSimplePropertyWithUnit(IfcTorqueMeasure) | 0 | n/a | NIL |
|  |  |  |  | RangeLength | Range of movement (linear actuators only) | IfcSimplePropertyWithUnit (IfcLengthMeasure) | n/a | n/a | NIL |
|  |  |  |  | Force | Force (linear actuators only) | IfcSimplePropertyWithUnit(IfcForceMeasure) | 0 | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcActuator |  |  |  |  |  |

## Pset_AirHandler

| Pset_AirHandler | describes air handler product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | AirLeakageRate | Air leakage of the casing of air handler subjected to air pressure (under a standard test) | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | TransmittedSound | Noise transmitted into the ductwork (under a standard test such as ISO 3741, ISO 3744, ISO 9614, ISO 5136). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | EmittedSound | Airborne noise emitted by the casing of the unit (under a standard test such as ISO 3741, ISO 3744, ISO 3746, and ISO 9614). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | ThermalInsulation | Thermal insulation of the casing | IfcPropertySet (Pset_Insulation) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |

# ADDITIONS TO EXISTING DATA TYPES

## IfcControllerTypeEnum

| IfcControllerTypeEnum | This enumeration defines the different types of Equipment an IfcController object can fulfill. |
| --- | --- |
|  |  |  | IfcController |  |
|  |  |  |  |  | Pset_HeatingCurve |  |
|  |  |  |  |  |  | < Any value > | HEATINGCURVE |

## IfcActuatorTypeEnum

| ActuatorType | This enumeration defines the different types of discrete elements an IfcActuator object can fulfill. |
| --- | --- |
|  |  |  | IfcActuator | IfcActuator |
|  |  |  |  |  | Pset_ThermostaticActuator |  |
|  |  |  |  |  |  | < Any value > | THERMOSTATICACTUATOR |

# NEW CLASSES

## IfcCooledBeam

Subclass of IfcHeatTransferDevice

| IfcCooledBeam | describes cooled beam product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | CooledBeamTypeEnum | Cooled beam type. Passive cooled beam provides cooling (and heating) to a room or zone. Active cooled beam provides cooling (and heating) but also functions as an air terminal of ventilation system | IfcEnumeratedProperty (Active, Passive, Other, NotKnown, Unset) | Active | Unset | Active |
|  |  |  |  | AirFlowConfigurationTypeEnum | Air flow configuration type of cooled beam | IfcEnumeratedProperty (OneSideAirFlow,TwoSideAirFlow,Other, NotKnown, Unset) | OneSideAirFlow | Unset | OneSideAirFlow |
|  |  |  |  | TotalCoolingCapacity | Total cooling capacity (under a standard test). This includes cooling capacity of beam and cooling capacity of supply air | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | TotalHeatingCapacity | Total heating capacity (under a standard test). This includes heating capacity of beam and heating capacity of supply air | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | BeamCoolingCapacity | Cooling capacity of beam (under a standard test). This excludes cooling capacity of supply air | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | BeamHeatingCapacity | Heating capacity of beam (under a standard test). This excludes heating capacity of supply air | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | CoolingWaterFlowRate | Water flow rate for cooling | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | HeatingWaterFlowRate | Water flow rate for heating | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | AirFlowRate | Air flow rate | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | EnteringAirTemperature | List of entering air temperatures to cooled beam; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | NIL |
|  |  |  |  | EnteringCoolingWaterTemperature | Entering water temperature for cooling | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | LeavingCoolingWaterTemperature | Leaving water temperature for cooling | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | EnteringHeatingWaterTemperature | Entering water temperature for heating | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | LeavingHeatingWaterTemperature | Leaving water temperature for heating | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | AirsidePressureDrop | Air-side pressure drop at the related air flow rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | WatersidePressureDrop | Water-side pressure drop at the related water flow rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | Throw | Distance cooled beam throws the air at the related air flow rate, before its velocity is reduced to a specific value (under a standard test) | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | CoilLength | Length of coil | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | RegeneratedSound | Regenerated sound (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | SoundAttenuation | Sound attenuation (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | Color | Color selection from the manufacturer's color options for the body of cooled beam | IfcSimpleProperty (IfcString) | n/a | n/a | empty string |
|  |  |  |  | PipeTestPressure | Test pressure of pipes (water circuits) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |

## IfcHumidifier

Subclass of IfcHeatTransferDevice

| IfcHumidifier | describes humidifier product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | HumidifierTypeEnum | Humidifier type | IfcEnumeratedProperty (Evaporative, Steam, Spray, Other, NotKnown, Unset) | Evaporative | Unset | Evaporative |
|  |  |  |  | HumidifierControlTypeEnum | Control type of humidifier | IfcEnumeratedProperty (WithoutControl, WithStepControl, WithModulatingControl, Other, NotKnown, Unset) | Without control | Unset | Without control |
|  |  |  |  | HumidificationEfficiency | Humidification efficiency (under a standard test), ratio between the mass of water evaporated by the humidifier and the theoretical mass needed to achieve saturation at a given temperature (1 = saturation) | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | EnteringAirTemperature | List of air temperatures of entering conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | LeavingAirTemperature | List of air temperatures of leaving conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | EnteringDryAirMassFlowRate | Entering dry air mass flow rate to humidifier | IfcSimplePropertyWithUnit (IfcMassFlowRateMeasure) | 0 | n/a | NIL |
|  |  |  |  | WaterOrSteamTemperature | Water or steam temperature | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | TotalWaterOrSteamFlowRate | Total water or steam mass flow rate. This includes overflow water mass flow rate | IfcSimplePropertyWithUnit (IfcMassFlowRateMeasure) | 0 | n/a | NIL |
|  |  |  |  | OverflowWaterMassFlowRate | Overflow water mass flow rate | IfcSimplePropertyWithUnit (IfcMassFlowRateMeasure) | 0 | n/a | NIL |
|  |  |  |  | TotalHeatTransferRate | Total heat transfer rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | SensibleHeatTransferRate | Sensible heat transfer rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | Height | Height of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Width | Width of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | AirPressureDrop | Air pressure drop at the related air flow rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | RegeneratedSound | Regenerated sound (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | SoundAttenuation | Sound attenuation (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |

## IfcDuctedSilencer

Subclass of IfcTreatmentDevice

| IfcDuctedSilencer | describes ducted silencer product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | InsertionLoss | Insertion loss of ducted silencer (under a standard test such as EN ISO 7235). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | RegeneratedSound | Flow noise generated by ducted silencer (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | SilencerLength | The finished length of the ducted silencer | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Insulation | Insulation | IfcPropertySet (Pset_Insulation) | n/a | n/a | NIL |
|  |  |  |  | TotalPressureLossCoefficient | Total pressure loss coefficient (according to EN ISO 7235), the total pressure loss divided by the velocity pressure upstream of the ducted silencer | IfcSimplePropertyWithUnit (IfcReal) | 0 | n/a | NIL |
|  |  |  |  | Height | Height of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Width | Width of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | CrossSectionalArea | Cross-sectional area at the point where the velocity pressure is measured when determining the pressure loss coefficient | IfcSimplePropertyWithUnit (IfcAreaMeasure) | 0 | n/a | NIL |
|  |  |  |  | AirFlowRate | Air flow rate | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | AirPressureDrop | Air pressure drop at the related air flow rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |

## IfcHeatRecoveryUnit

Subclass of IfcHeatTransferDevice

| IfcHeatRecoveryUnit | describes heat recovery unit product data (do not apply to heat recovery units with pump and intermediary fluid) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | HeatRecoveryUnitTypeEnum | This enumeration defines different heat recovery unit types. | IfcEnumeratedProperty (AirToAirPlate,RotatingWheel,Other, NotKnown, Unset) | AirToAirPlate | Unset | AirToAirPlate |
|  |  |  |  | ByPass | Is there a bypass for airsteam? If there is, it can be used, when the capacity of heat recovery unit is not needed. TRUE=Yes, FALSE=No | IfcSimpleProperty (IfcBoolean) | FALSE | TRUE | FALSE |
|  |  |  |  | UnFrost | Is there an unfrosting system connected to heat recovery unit? TRUE=Yes, FALSE=No | IfcSimpleProperty (IfcBoolean) | FALSE | TRUE | FALSE |
|  |  |  |  | EnteringWarmAirTemperature | List of warm air temperatures of entering conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | LeavingWarmAirTemperature | List of warm air temperatures of leaving conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | WarmAirPressureDrop | Warm air pressure drop at the related warm air flow rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | WarmAirFlowRate | Warm air flow rate | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | EnteringColdAirTemperature | List of cold air temperatures of entering conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | LeavingColdAirTemperature | List of cold air temperatures of leaving conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | empty list |
|  |  |  |  | ColdAirPressureDrop | Cold air pressure drop at the related cold air flow rate (under a standard test) | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | ColdAirFlowRate | Cold air flow rate | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | HeatTransferRate | Heat transfer rate at which energy is transferred from one medium to another (under a standard test such as EN 305) | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | TemperatureEfficiency | Temperature efficiency (under a standard test). TemperatureEfficiency = (LeavingColdAirTemperature - EnteringColdAirTemperature)/(EnteringWarmAirTemperature - EnteringColdAirTemperature) | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | HumidityEfficiency | Humidity efficiency (under a standard test) | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | BypassRatio | Heat recovery unit bypass ratio. The ratio of the diverted flow to the sum of main flow and the diverted flow (0 = no bypass, 1 = total bypass) | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | Height | Height of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | Width | Width of flow cross section | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | InternalAirLeakage | The internal air leakage between two air streams (under a standard test) | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | RegeneratedSound | Regenerated sound (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | SoundAttenuation | Sound attenuation (under a standard test). Reference to a property set Pset_SoundPowerLevels | IfcPropertySet (Pset_SoundPowerLevels) | n/a | n/a | NIL |
|  |  |  |  | DefrostingHeatRatio | Defrosting heat ratio (under a standard test such as prEN 13053), ratio between the energy transferred into the supply air and the maximum recoverable energy in exhaust air, excluding the energy input for defrosting | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |

## IfcRadiator

Subclass of IfcHeatTransferDevice

| IfcRadiator | describes radiator product data. Radiator is an heating appliance which emits heat by natural convection and radiation. Radiators can be produced with different materials (e.g. steel, aluminium, cast-iron) and with different designs (e.g. plate type, column type, tube type). |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | RadiatorTypeEnum | type of the radiator design | IfcEnumeratedProperty (Panel, Column,Tube, 0ther, NotKnown, Unset) |  |  |  |
|  |  |  |  | StandardThermalOutput | the thermal output of a radiator defined for a standard reference air temperature of 20° C, the standard air pressure 101.325 kPa, an inlet water temperature of 75° C and an outlet water temperature of 65° C. | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardInletWaterTemperature | inlet water temperature related to standard test conditions. | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardOutletWaterTemperature | outlet water temperature related to standard test conditions. | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardReferenceEnvironmentalTemperature | reference environmental temperature related to standard test conditions. The environmental temperature is to be measured on vertical line at the centre of the room, 0.75 meter above the floor level. | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | StandardWaterFlowRate | water flow rate related to standard test conditions. | IfcSimplePropertyWithUnit (IfcMassFlowRateMeasure) | n/a | n/a | NIL |
|  |  |  |  | SpecificCharacteristicExponent | The characteristic equation gives the thermal output as a function of the excess temperature at constant water flow rate. The characteristic equation is a power function with a specific characteristic exponent. | IfcSimpleProperty (IfcReal) | n/a | n/a | NIL |
|  |  |  |  | RadiationRatio | ratio of radiative heat transfer rate to totla heat transfer rate. | IfcSimplePropertyWithUnit (IfcRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | BodyMaterial | reference to a material used to construct the radiator | IfcObjectReference (IfcMaterial) | n/a | n/a | NIL |
|  |  |  |  | BodyMass | overall radiator mass | IfcSimplePropertyWithUnit (IfcMassMeasure) | n/a | n/a | NIL |
|  |  |  |  | WaterContent | radiator water content. | IfcSimplePropertyWithUnit (IfcVolumeMeasure) | n/a | n/a | NIL |
|  |  |  |  | NumberOfPanels | Number of panels (panel radiators only) | IfcReal |  |  |  |
|  |  |  |  | NumberOfSections | Number of vertical sections, measured in the direction of flow | IfcReal |  |  |  |
|  |  |  |  | ConnectionPositions | Positions of connection ports, list of inlet position followed by outlet position, left and right defined looking from centre of room towards radiator | IfcComplexProperty (LIST [1:2] OF IfcEnumeratedProperty (TopLeft, TopRight, BottomLeft, BottomRight, Other, NotKnown, Unset) |  |  |  |
|  |  |  |  | Length | Horizontal extent of emitting surface in direction of water flow, excluding pipe fittngs, valves etc | IfcSimplePropertyWithUnit (IfcLengthMeasure) |  |  |  |
|  |  |  |  | Height | Vertical extent of emitting surface | IfcSimplePropertyWithUnit (IfcLengthMeasure) |  |  |  |
|  |  |  |  | Depth | Horizontal extent of emitting surface(s) perpendicular to direction of water flow, | IfcSimplePropertyWithUnit (IfcLengthMeasure) |  |  |  |
|  |  |  |  | Adjustments | reference to the property set defining adjustable parameters | IfcComplexProperty (SET [1:4] OF IfcPropertySet (Pset_RadiatorAdjustments)) | n/a | n/a | NIL |

# NEW PROPERTY SETS

## Pset_CooledBeamDesignCriteria

| Pset_CooledBeamDesignCriteria | describes design criteria used for the design of each cooled beam within the cooled beam system |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | CooledBeamTypeEnum | Cooled beam type. Passive cooled beam provides cooling and heating to a room or zone. Active cooled beam provides cooling and heating but also functions as an air terminal of ventilation system | IfcEnumeratedProperty (Active, Passive, Other, NotKnown, Unset) | Active | Unset | Active |
|  |  |  |  | TotalCoolingCapacity | Required total cooling capacity from a cooled beam | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | TotalHeatingCapacity | Required total heating capacity from a cooled beam | IfcSimplePropertyWithUnit (IfcPowerMeasure) | 0 | n/a | NIL |
|  |  |  |  | SupplyAirFlowRate | Required supply air flow rate of a cooled beam. This air flow comes from ventilation system | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | EnteringAirTemperature | List of design air temperatures of entering conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | NIL |
|  |  |  |  | EnteringCoolingWaterTemperature | Design value of entering water temperature for cooling | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | EnteringHeatingWaterTemperature | Design value of entering water temperature for heating | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | MaximumSoundPower | Maximum acceptable sound power level | IfcSimplePropertyWithUnit (IfcSoundMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumUnitLength | Maximum unit length | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumUnitWidth | Maximum unit width | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumUnitHeight | Maximum unit height | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumWatersidePressureDrop | Maximum acceptable water-side pressure drop | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumAirsidePressureDrop | Maximum acceptable air-side pressure drop at required air flow rate | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcCooledBeam |  |  |  |  |  |

## Pset_AirHandlerDesignCriteria

| Pset_AirHandlerDesignCriteria | describes design criteria used for the design of each air handler within the air handling system |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | FlowType | air flow type | ENUMERATION OF (ConstantAirVolume, VariableAirVolume, Other, NotKnown, Unset) | ConstantAirVolume | Unset | ConstantAirVolume |
|  |  |  |  | SupplyAirFlowRate | Required supply air flow rate | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | TurnDownRatio | Ratio of minimum to maximum air flow rate (variable air volume systems only) | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | MinimumOutsideAirFraction | Minimum ratio of outside air flow rate to supply air flow rate | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  |  | MinimumOutsideAirFlowRate | Minimum outside air flow rate | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  |  | SupplyAirTemperatureHeating | List of supply air temperatures at design heating conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | NIL |
|  |  |  |  | SupplyAirTemperatureCooling | List of supply air temperatures at design cooling conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | NIL |
|  |  |  |  | DesignOutsideAirTemperatureHeating | List of outside air temperatures at design heating conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | NIL |
|  |  |  |  | DesignOutsideAirTemperatureCooling | List of outside air temperatures at design cooling conditions; the list consists of dry bulb followed by wet bulb | IfcComplexProperty (LIST [1:2] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | NIL |
|  |  |  |  | DesignHeatSourceTemperature | Supply temperature of hot water or steam at design heating conditions | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | DesignChilledWaterTemperature | Supply temperature of chilled water at design cooling conditions | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | SupplyAirTotalPressure | Total pressure of supply air at discharge of air handling unit | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | ReturnAirTotalPressure | Total pressure of return air at entrance of air handling unit | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumAirsidePressureDrop | Maximum acceptable air-side pressure drop at required air flow rate | IfcSimplePropertyWithUnit (IfcPressureMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumTransmittedSound | Maximum acceptable sound power level transmitted by the unit into the ductwork | IfcSimplePropertyWithUnit (IfcSoundMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumEmittedSound | Maximum acceptable sound power level emitted by the casing of the unit | IfcSimplePropertyWithUnit (IfcSoundMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumUnitLength | Maximum unit length | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumUnitWidth | Maximum unit width | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumUnitHeight | Maximum unit height | IfcSimplePropertyWithUnit (IfcPositiveLengthMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumSpecificFanPower | Maximum acceptable fan power per unit volumumetric flow rate. Total power of fans / air flow rate. | IfcSimplePropertyWithUnit (IfcPowerPerVolumetricFlowRateMeasure) | 0 | n/a | NIL |
|  |  |  |  | MaximumLeakage | Maximum acceptable total air leakage flow of casing at fixed pressure | IfcSimplePropertyWithUnit (IfcVolumetricFlowrateMeasure) | 0 | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | Pset_AirHandler |  |  |  |  |  |

## Pset_ValveCharacteristics

| Pset_ValveCharacteristics | describes valve characteristics |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | InherentCharacteristicEnum | Inherent characteristic of the valve | IfcEnumeratedProperty (Linear, Exponential, Other, NotKnown, Unset) | Linear | Unset | Linear |
|  |  |  |  | PressureVersusFlowCharacteristicsValues | Total pressure drop versus fluid flow rate curve values (under a standard test) | IfcSimpleProperty (IfcPropertyTablevalue) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |

## Pset_DamperCharacteristics

| Pset_DamperCharacteristics | describes damper characteristics |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | InherentCharacteristicEnum | Inherent characteristic of the damper | IfcEnumeratedProperty (Linear, Exponential, Other, NotKnown, Unset) | Linear | Unset | Linear |
|  |  |  |  | PressureVersusFlowCharacteristicsValues | Total pressure drop versus fluid flow rate curve values (under a standard test) | IfcSimpleProperty (IfcPropertyTablevalue) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |

## Pset_FluidMovingDeviceCharacteristics

| Pset_FluidMovingDeviceCharacteristics | describes fluid moving device characteristics |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | InherentCharacteristicEnum | Inherent characteristic of fluid moving device | IfcEnumeratedProperty (Linear, Exponential, Other, NotKnown, Unset) | Linear | Unset | Linear |
|  |  |  |  | PressureVersusFlowCharacteristicsValues | Total pressure rise versus fluid flow rate curve values at maximum speed (under a standard test) | IfcSimpleProperty (IfcPropertyTablevalue) | n/a | n/a | NIL |
|  |  |  |  | PowerVersusFlowCharacteristicsValues | Electrical Power versus fluid flow rate curve values at maximum speed (under a standard test) | IfcSimpleProperty (IfcPropertyTablevalue) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |

## Pset_ControlDamperAdjustments

| Pset_ControlDamperAdjustments | describes the control damper in different phases of the life-cycle |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | ReferringLifeCyclePhaseEnum | Reference to the life-cycle phase in which parameters are adjusted | IfcEnumeratedProperty (Design, Commissioning, Monitoring, Maintenance, Other, NotKnown, Unset) | Design | Unset | Design |
|  |  |  |  | Authority | Authority | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | Pset_ControlDamper |  |  |  |  |  |

## Pset_ValveAdjustments

| Pset_ValveAdjustments | describes the valve in different phases of the life-cycle |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | ReferringLifeCyclePhaseEnum | Reference to the life-cycle phase in which parameters are adjusted | IfcEnumeratedProperty (Design, Commissioning, Monitoring, Maintenance, Other, NotKnown, Unset) | Design | Unset | Design |
|  |  |  |  | Authority | Authority | IfcSimpleProperty (IfcNormalisedRatioMeasure) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcValve |  |  |  |  |  |

## Pset_RadiatorSystemDesigCriteria

| Pset_RadiatorSystemDesignCriteria | describes design criteria used for the design of a radiator heating system |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | RadiatorSystemTypeEnum | installation type of the heating system | IfcEnumeratedProperty (SinglePipe, DualPipe, Other, NotKnown, Unset) | n/a | n/a | NIL |
|  |  |  |  | ThermalOutput | overall thermal output required for the system | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | InletWaterTemperature | intent inlet water temperature, the bulk temperature of the water entering an heating system component | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | OutletWaterTemperature | intent outlet temperature, the bulk temperature of the water leaving an heating system component | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | MaximumWaterFlowRate | intent maximum water flow rate for the system | IfcSimplePropertyWithUnit (IfcMassFlowRateMeasure) | n/a | n/a | NIL |
|  |  |  |  | ValveAuthority | intent valve authority in the system | IfcSimpleProperty (IfcReal) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |
|  |  |  |  | IfcSystem, IfcSpace, IfcZone |  |  |  |  |  |

## Pset_RadiatorDesignCriteria

| Pset_RadiatorDesignCriteria | describes design criteria used for the design of each radiator within the heating system |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | ThermalOutput | required thermal output for a radiator | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | InletWaterTemperature | required inlet water temperature, the bulk temperature of the water entering radiator | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | OutletWaterTemperature | required outlet temperature, the bulk temperature of the water leaving a radiator | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | RoomEnvironmentalTemperature | environmental temperature in room | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | MaximumWaterFlowRate | required maximum water flow rate for a radiator | IfcSimplePropertyWithUnit (IfcMassFlowRateMeasure) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |
|  |  |  |  | IfcSystem, IfcSpace, IfcZone |  |  |  |  |

## Pset_ThermostaticActuator

| Pset_ThermostaticActuator | describes thermostatic actuator product data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | HeatTransmittanceResistanceFromMediumToSensor | heat transfer resistance from the valve to the sensor | IfcSimplePropertyWithUnit (IfcThermalResistanceMeasure) | n/a | n/a | NIL |
|  |  |  |  | SurfaceArea | surface area of the thermostatic actuator | IfcSimplePropertyWithUnit (IfcAreaMeasure) | n/a | n/a | NIL |
|  |  |  |  | HeatCapacity | heat capacity of the thermostatic actuator | IfcSimplePropertyWithUnit (IfcHeatCapacityMeasure) | n/a | n/a | NIL |
|  |  |  |  | ConvectiveHeatTransmittanceCoefficient | convective heat transfer coefficient from air to sensor | IfcSimplePropertyWithUnit (IfcThermalTransmittanceMeasure) | n/a | n/a | NIL |
|  |  |  |  | RadiativeHeatTransmittanceCoefficientFromRadiator | radiative heat transfer coefficient from radiator to sensor | IfcSimplePropertyWithUnit (IfcThermalTransmittanceMeasure) | n/a | n/a | NIL |
|  |  |  |  | ProportionalBand | proportional band of the thermostatic actuator | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcActuator |  |  |  |  |  |

## Pset_HeatingCurve

| Pset_HeatingCurve | describes heating curve |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Adjustments | reference to the property set defining adjustable parameters | IfcComplexProperty (SET [1:4] OF IfcPropertySet (Pset_RadiatorAdjustments)) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcController |  |  |  |  |  |

## Pset_BoilerAdjustments

| Pset_BoilerAdjustments | describes parameters of the boiler adjusted in different phases of the life-cycle |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | ReferringLifeCyclePhaseEnum | Reference to the life-cycle phase in which parameters are adjusted | IfcEnumeratedProperty (Design, Commissioning, Monitoring, Maintenance, Other, NotKnown, Unset) | n/a | n/a | NIL |
|  |  |  |  | MinimumOperationTime | minimum operation time of the boiler | IfcSimplePropertyWithUnit (IfcTimeMeasure) | n/a | n/a | NIL |
|  |  |  |  | MaximumHeatLoad | maximum energy load | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | MinimumHeatLoad | minimum energy load | IfcSimplePropertyWithUnit (IfcPowerMeasure) | n/a | n/a | NIL |
|  |  |  |  | Deadband | temperature difference between start and stop operation | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | Lambda | stoichiometic fuel/air ratio | IfcSimpleProperty (IfcReal) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcBoiler |  |  |  |  |  |

## Pset_RadiatorAdjustments

| Pset_RadiatorAdjustments | describes parameters of the radiator adjusted in different phases of the life-cycle |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | ReferringLifeCyclePhaseEnum | reference to the life-cycle phase in which parameters are adjusted | IfcEnumeratedProperty (Design, Commissioning, Monitoring, Maintenance, Other, NotKnown, Unset) | n/a | n/a | NIL |
|  |  |  |  | ThermalOutputReduction | reduction of thermal power due to obstruction | IfcSimpleProperty (IfcReal) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcRadiator |  |  |  |  |  |

## Pset_HeatingCurveAdjustments

| Pset_HeatingCurveAdjustments | describes the heating curve in different phases of the life-cycle |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | ReferringLifeCyclePhaseEnum | reference to the life-cycle phase in which parameters are adjusted | IfcEnumeratedProperty (Design, Commissioning, Monitoring, Maintenance, Other, NotKnown, Unset) | n/a | n/a | NIL |
|  |  |  |  | Gradient | Describes the heating curve mathematically. It is defined as the difference of inlet water temperatures devided by the difference of outside temperatures. | IfcSimpleProperty (IfcReal) | n/a | n/a | NIL |
|  |  |  |  | InitalOutsideTemperature | temperature below which heating begins | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | InletWaterTemperatureReduction | reduction of the supply temperature (e.g. at night) | IfcComplexProperty (LIST [1:24] OF IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure)) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | Pset_HeatingCurve |  |  |  |  |  |

## Pset_MeteorologicalData

| Pset_MeteorologicalData | describes meteorological data |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | DataSourceEnum | references the source where meteorological data come from | IfcEnumeratedProperty (TestReferenceYear, ActualData, Other, NotKnown, Unset) | n/a | n/a | NIL |
|  |  |  |  | DryBulbTemperature | dry bulb outside temperature | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | WetBulbTemperature | wet bulb outside temperature | IfcSimplePropertyWithUnit (IfcThermodynamicTemperatureMeasure) | n/a | n/a | NIL |
|  |  |  |  | AtmosphericPressure | atmospheric pressure | IfcSimplePropertyWithUnit (IfcPressureMeasure) | n/a | n/a | NIL |
|  |  |  |  | DirectRadiation | direct radiation measured on a horizontal surface | IfcSimplePropertyWithUnit (IfcHeatFluxDensityMeasure) | n/a | n/a | NIL |
|  |  |  |  | DiffuseRadiation | diffuse radiation measured on a horizontal surface | IfcSimplePropertyWithUnit (IfcHeatFluxDensityMeasure) | n/a | n/a | NIL |
|  |  |  |  | WindDirection | wind direction by convention: North = 0°, East = 90°, South = 180°, West = 270° | IfcSimpleProperty (IfcInteger) | n/a | n/a | NIL |
|  |  |  |  | WindSpeed | wind speed | IfcSimplePropertyWithUnit (IfcLinearVelocityMeasure) | n/a | n/a | NIL |
|  |  |  | Target objects for this PropertySet |  |  |  |  |  |
|  |  |  |  | IfcSite, IfcProject |  |  |  |  |  |

# NEW TYPE DEFINITIONS

|  | # |  | TypeDef Name |  |  | Description |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Class being Typed |  |  |
|  |  |  |  |  | Generic Type |  |  |
| Defined |  |  |  |  |  | Specific Type / domain defining type |  |
| In |  |  |  |  |  |  | Att_Set # | Attribute Sets |  |
| CooledBeamTypeEnum |  |
|  |  |  | IfcCooledBeamTypeEnum |  |
|  |  |  |  |  | Active |  |
|  |  |  |  |  | Passive |  |
|  |  |  |  |  | Other |  |
|  |  |  |  |  | NotKnown |  |
|  |  |  |  |  | Unset |  |
| AirFlowConfigurationTypeEnum |  |
|  |  |  | IfcAirFlowConfigurationTypeEnum |  |
|  |  |  |  |  | OneSideAirFlow |  |
|  |  |  |  |  | TwoSideAirFlow |  |
|  |  |  |  |  | Other |  |
|  |  |  |  |  | NotKnown |  |
|  |  |  |  |  | Unset |  |
| HumidifierTypeEnum |  |
|  |  |  | IfcHumidifierTypeEnum |  |
|  |  |  |  |  | Evaporative |  |
|  |  |  |  |  | Steam |  |
|  |  |  |  |  | Spray |  |
|  |  |  |  |  | Other |  |
|  |  |  |  |  | NotKnown |  |
|  |  |  |  |  | Unset |  |
| HumidifierControlTypeEnum |  |
|  |  |  | IfcHumidifierControlTypeEnum |  |
|  |  |  |  |  | WithoutControl |  |
|  |  |  |  |  | WithStepControl |  |
|  |  |  |  |  | WithModulatingControl |  |
|  |  |  |  |  | Other |  |
|  |  |  |  |  | NotKnown |  |
|  |  |  |  |  | Unset |  |
| HeatRecoveryUnitTypeEnum |  |
|  |  |  | IfcHeatRecoveryUnitTypeEnum |  |
|  |  |  |  |  | AirToAirPlate |  |
|  |  |  |  |  | RotatingWheel |  |
|  |  |  |  |  | WithModulatingControl |  |
|  |  |  |  |  | Other |  |
|  |  |  |  |  | NotKnown |  |
|  |  |  |  |  | Unset |  |

# NEW DATA TYPES

## IfcSoundMeasure

|  | Defined Data Type Name | Data Type Definition | Semantic definition of this data type |
| --- | --- | --- | --- |
| Simple Types |  |  |
|  | IfcSoundMeasure | REAL | A measure of sound power or sound pressure level. Measured in desibels [dB]. |

## IfcHeatCapacityMeasure

|  | Defined Data Type Name | Data Type Definition | Semantic definition of this data type |
| --- | --- | --- | --- |
| Simple Types |  |  |
|  | IfcHeatCapacityMeasure | REAL | A measure of heat capacity. Measured in [J/K]. |

## IfcPowerPerVolumetricFlowRateMeasure

|  | Defined Data Type Name | Data Type Definition | Semantic definition of this data type |
| --- | --- | --- | --- |
| Simple Types |  |  |
|  | IfcPowerPerVolumetricFlowRateMeasure | REAL | A measure of power per volumetric flow rate. Measured in [Ws/m3]. |

## IfcTorqueMeasure

|  | Defined Data Type Name | Data Type Definition | Semantic definition of this data type |
| --- | --- | --- | --- |
| Simple Types |  |  |
|  | IfcTorqueMeasure | REAL | A measure of torque. Measured in [Nm]. |