ESNFAQV1.DOC

Essential Services Node (ESN) Frequently Asked Questions (FAQ)

Version 1 12/9/96

This document will address some of the more frequently asked questions since the ESN’s introduction.  The following questions are addressed in this version of the FAQ:

1.	What is an ESN ?

2.	Where can I get more detailed information ?

3.	What is the physical size and weight of an ESN ?

4.	What is the power dissipation of an ESN ?

5.	What GSFC programs are currently using an ESN ?

6.	What software tools are available for the ESN ?

7.	Where can I get the GSFC written Operating System ?

8.	Where can I get an ESN ?

9.	Where can I buy a board that uses an ESN ?

10.	Who should I contact if I have questions ?

1.	What is an ESN ?

The Essential Service Node (ESN) is a standard interface device between a spacecraft instrument or subsystem and the spacecraft’s Command and Data Handling (C&DH) system.  The ESN features such hardware as:

UTMC UT69R000 16-bit processor,

UTMC BCRTM 1553/1773 protocol chip,

8251 UARTs,

8255 Parallel Port,

16-bit serial interface,

various timers,

192 Kbytes of Static RAM,

and a 12-bit A/D converter

all in a 2.6” x 2.6” x 0.3” Multi-Chip Module (MCM).

The ESN was designed by Bob Caffrey (while in GSFC, Code 735) and Mike Cuvielo (of Jackson and Tull).  The ESN is fabricated by Honeywell CTO in Phoenix, AZ.

2.	Where can I get more detailed information ?

The Hardware specification describes the hardware operation, addresses, pinouts etc.  The ESN Hardware Specification can be downloaded from the ESN website at:

http://code735.gsfc.nasa.gov/phil/current.htm

The latest version of the ESN Hardware Specification is ICD-735-2827 REV 2.0, dated August 16,1996.

3.	What is the physical size and weight of an ESN ?

The ESN package is 2.6” x 2.6” x 0.3”, it is a quad flatpack type package with 392 leads, 98 on a side.  The ESN weighs 95 + 10 g.

4.	What is the power dissipation of an ESN ?

The following major modes of operation have been measured at the GSFC Facility:

Post-Reset Operation, Execution from PROM's

MCM Power Pin			Current		Power

+5VDC Digital:			86.0 mA		430 mW

+5VDC Analog:			27.0 mA		135 mW

+15VDC Analog:			19.0 mA		285 mW

-15VDC Analog			25.0 mA		375 mW

Total						1.225 W

Analog Power Disabled, Processor Active from PROM's:

MCM Power Pin			Current		Power

+5VDC Digital:			86.0 mA		430 mW

+5VDC Analog:			0 mA		0  mW

+15VDC Analog:			0 mA		0  mW

-15VDC Analog			0 mA		0  mW

Total						430 mW

Analog Power Disabled, Processor Active from instruction RAM:

MCM Power Pin			Current		Power

+5VDC Digital:			100.0 mA	500 mW

+5VDC Analog:			0 mA		0  mW

+15VDC Analog:			0 mA		0  mW

-15VDC Analog			0 mA		0  mW

Total						500 mW

Analog Power Disabled, Processor Active from instruction RAM, Operating on

Data RAM:

MCM Power Pin			Current		Power

+5VDC Digital:			145.0 mA	725 mW

+5VDC Analog:			0 mA		0  mW

+15VDC Analog:			0 mA		0  mW

-15VDC Analog			0 mA		0  mW

Total						725 mW

Analog Power Disabled, Processor Asleep, BCRTM Active:

MCM Power Pin			Current		Power

+5VDC Digital:			62.0 mA		310 mW

+5VDC Analog:			0 mA		0  mW

+15VDC Analog:	 		0 mA		0  mW

-15VDC Analog			0 mA		0  mW

Total						310 mW

5.	What GSFC programs are currently using an ESN ?

The MIDEX MAP and NMP EO-1 programs are using 4 ESNs in the spacecraft avionics.  In addition, the Fourth Generation TDRSS Transponder will include an ESN, as well as the Ka-Band Phased Array antenna that has just been specified.

In the MIDEX MAP and NMP EO-1 programs, the ESN is on a board referred to as a Remote Services Nodes (RSNs).  The five RSNs in the MIDEX MAP program are the: Tranponder RSN, the Housekeeping RSN, the Attitude Control Electronics (ACE) RSN, and the Power System Electronics (PSE) RSN.

6.	What software tools are available for the ESN ?

UTMC tool suite (available from UTMC for approx $3000)

C compiler (GNU) - generates assembly code for the UT69R000 from C, C++, or Objective C source code.  Currently supported on Sun/Solaris Unix workstations.

Assembler (RASM) - inputs assembler source files, outputs object files.  Operates on both PC and Unix hosts.

Linker (RLNK) - combines object files to and executable Intel Hex file.

Disassembler (RISCIA)

Simulator (IRSIM) - interactive simulator.  Permits the development of code without need for hardware.  Allows breakpoints, examination of memory/registers etc..

IRSIM Monitor - target resident software which communicates with simulator via an RS-232 link.

GSFC Developed Tool Suite (free)

C-Compiler (GNU) - input C source files and outputs them in object form.  Has passed 90% of Metaware validation and test suite.  Floating point still has problems.

Macro pre-processor - macro expansion

Assembler - inputs assembler source files, outputs object files.

Linker - combines multiple object files, resolves inter-file symbolic references and outputs the result in a form that may be either bound directly to the machine addresses or reprocessed in order to resolve further symbolic references.

Binder - reads the input file, evaluates all expressions, resolves all remaining symbol references, binds each section to an address, and outputs Intel hex files.

Library Management Utility - creates, appends, deletes, replaces elements in a library

Eeprom - inputs Intel Hex files defining the code and data for an executable and combines them into a single Intel Hex file used to burn EERPOMs.

7.	Where can I get the GSFC written Operating System ?

Contact Ray Whitley, Leader of the Flight Software Group, Code 735 at (301) 286-6404 or Ray.Whitley@gsfc.nasa.gov

8.	Where can I get an ESN ?

Contact Ed Roberts of Honeywell (602)0436-2658.

9.	Where can I buy a board that uses an ESN ?

Two boards are available presently, an ASIC test board and an MCM test board.

The ASIC test board was used to test the ASIC in the ESN circuit.  All parts except the ASIC are in discrete DIP form.

The MCM Test Board has been designed and has been used to test and validate the ESNs received.  It has the ESN in a fuzz button socket for ease of removal following testing.

Both boards are available from Jackson and Tull, Contact Bill Dentel at (301) 8005-6090.

10.	Who should I contact if I have questions ?

Questions can be addressed to:

Philip.Luers@gsfc.nasa.gov

Mark.Frigaard@gsfc.nasa.gov

Ray.Whitley@gsfc.nasa.gov

or Ed Roberts of Honeywell (602)0436-2658.

End of ESNFAQV1