Landsat 7 Gain Setting Strategy, as of September 2000

The currently implemented gain setting strategy for Landsat 7 consists of a fixed categorization of the surface cover types of the earth and gain setting rules that are surface cover and sun angle based.  The gains for bands 1-3 are currently always changed together as are the gains for bands 5 and 7.

The earth surface categories are as follows:

a)  Land (non-desert, non-ice)

http://ltpwww.gsfc.nasa.gov/IAS/word_files/l7_global_land.doc (Word)

http://ltpwww.gsfc.nasa.gov/IAS/pdfs/l7_global_land_doc.pdf (PDF)

b)  Desert

http://ltpwww.gsfc.nasa.gov/IAS/ascii/desert.lst  (ASCII)

c)  Ice/Snow

http://ltpwww.gsfc.nasa.gov/IAS/ascii/arctic.lst  (ASCII)

(see Table 1 of the land database for Antarctica)

d)  Water

e)  Sea Ice

(see Table 1 of the land database)

Volcano/Night

(see Table 6 of the land database)

Each Landsat-7 Path/Row of the Worldwide Reference System (WRS) is categorized into one of these six types.

For each surface cover type the gain setting rules are different and are listed below.  The gains are calculated on a daily basis (prior to this they were calculated on a monthly basis).  The base value of the gains are the default settings.  These are found in http://ltpwww.gsfc.nasa.gov/IAS/ascii/defgains.lst (ASCII)

Gain setting rules:

Land (non-desert, non-ice; does include coral reefs):

Bands 1-3 set to high gain

Band 4 set to high gain except where sun elevation is greater than 45¡(then is set to low gain) Ñ to avoid dense vegetation (reflectance > 0.66 ) saturation. (At this sun angle high gain in band 4 saturates at about a reflectance of 0.66, so switching to low gain keeps targets at this reflectance or below from saturating.)

Bands 5-7 set to high gain

Band 8 set to low gain

Desert:

Bands 1-3 set to high gain except where sun elevation is greater than 28¡ - to avoid bright desert target (reflectance >0.65 in band 3, [>0.66 in band 1 , >0.71 in band 2]) saturation

Band 4 set to high gain except where sun elevation is greater than 45¡(then is set to low gain) Ñ to avoid bright desert (reflectance > 0.66 ) saturation.

Band 5,7 set to high gain except where sun elevation is greater than 38¡ - to avoid bright desert target (reflectance >0.70 in band 5, [>0.68 in band 7]) saturation

Band 8 set to low gain

Ice/Snow and Sea Ice:

Bands 1-3 set to high gain except where sun elevation is greater than 19¡ - to avoid snow ice (reflectance > 0.95 in band 3, [ >0.94 in band 1, >1.03 in band 2]) saturation.

Band 4 set to high gain except where sun elevation is greater than 31¡ - to avoid snow/ice (reflectance >0.92) saturation.

Band 5, 7 set to high gain

Band 8 set to low gain

Night (nighttime imaging  (sun elevation <0) is only routinely performed for sites identified as ÒVolcanoÓ):

Bands 1-4, set to high gain

Bands 5,7 set to low gain to reduce saturation of volcanic hot spots and fires

Band 8 set to low gain

The actual saturation reflectances corresponding to a given sun angle are influenced by the Earth-Sun distance, which varies by ±1.5% over the year producing a ±3% irradiance variation. The current implementation does not incorporate this variability.

Band 8 is in low gain for all routine acquisitions as the noise level in this band is such that high gain provides very little improvement in performance.  This implementation is currently under review and the band 8 gain settings may be altered in the future.

Maps applying to the first day of each month are found at:  (http://ltpwww.gsfc.nasa.gov/IAS/handbook/powerpoint/defgains_4.0.ppt)