# Choosing ASF Data Products

The variables to be determined when requesting data from ASF and determining its price are listed below. These variables are discussed in some detail with reference to cost where appropriate.

Choosing ASF Data Products	1

Satellite	1

Location of ground station	1

Beam Modes	2

Resolution	2

Media type and Delivery	3

Cost	3

## Satellite

RADARSAT-1 is an advanced radar sensor called Synthetic Aperture Radar (SAR). SAR

is a microwave instrument which sends pulsed signals to the Earth and processes the

received reflected pulses.

## Location of ground station

Research emphasis is on the polar regions, though onboard tape recorders will allow imaging of any region, world-wide. Data will be down linked in real time or stored on one of the tape recorders until the spacecraft is within range of a receiving station. Data is expected to be available for users a few hours after the satellite passes over an area. Receiving stations are located at Prince Albert, Saskatchewan; Gatineau, Quebec; Tromso, Norway; and Fairbanks, Alaska.

There are additional costs (as noted below) for data acquisitions from stations outside the ASF and McMurdo station masks.

Ground Station Transcription Times and Costs

| Ground Station | ASF | McMurdo, Antarctica (MCM) | Gatineau, Canada (GSS) | Prince Albert, Canada (PASS) | Tromso, Norway (TROM) | West Freugh, Scotland (DERA) | Singapore (CRISP) | China (RSGS) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Delay Time from Acquisition to Orderable | 1 week | 3 months to 1 year depending on date | 2-3 months | 2-3 months | 2-3 months | 4-6 months | 3-4 months | 4-6 months, L0 data products only |
| FGS Cost per datatake | NA | NA | 150 | 150 | 350 | 350 | 275 | 250 |

## Beam Modes

RADARSAT-1 offers two types of data: Standard SAR and ScanSAR.

- Standard SAR

All standard data are processed to a 100 km x 100 km scene. If the actual swath is less than 100 km, such as JERS at 75 km, the remaining pixels are 0-filled. Nominally, the full-resolution images have 12.5 m pixel spacing and 30 m resolution, and the low-resolution images have 100 m pixel spacing and 240 m resolution. Each full-resolution image is 8192 x 8192 x 8 bits or 67 MB in size, and each low-resolution image is 1024 x 1024 x 8 bits or 1 MB in size. These image products represent how brightly the viewed ground targets backscattered the SARs' radar pulses. Metadata distributed with these images allows users to compute various other parameters, such as sigma-naught, from the pixel values.

Standard SAR has the following beam modes:

- Standard Beams

- Wide Beams

- Fine Resolution Beams

- Low Incidence

- High Incidence

- ScanSAR

The RADARSAT-1 ScanSAR images are somewhat different. The RADARSAT-1 SAR utilizes beam forming techniques in order to provide several different beam modes. The modes may be capable of imaging closer to or farther from the satellite, with finer resolution and accordingly smaller areas or wide areas with worse resolution. The ScanSAR mode actually combines a few of these other modes in order to obtain a very wide swath - approximately 500 km, depending on which ScanSAR sub-mode is chosen. Three resolutions are provided: 75, 150, and 600 meters. ASF can also process these data to Polar Stereographic, Lambert, or UTM map projections. Please see the documentation on RADARSAT ScanSAR Images for further information

Notes: 1) The data may be geocoded to a Polar Stereographic, Lambert, or UTM projection, however, ASF User Services recommends ordering Ungeocoded ScanSAR and using software programs to perform geocoding.

2) There is also a terrain-corrected product which is terrain corrected in addition to being geocoded but this product has not been validated. ASF provides software for geocoding, and mosaicking. The terrain correction software does not work with ScanSAR.

ScanSAR has the following beams:

- Wide A

- Wide B

- Narrow A

- Narraow B

For details on the characteristics of these different beams, see the following websites: http://www.asf.alaska.edu/2_3.html, http://www.asf.alaska.edu/R1ScanSAR.pdf

For suggestions on how to choose the appropriate beam mode, see http://www.asf.alaska.edu/R1beamChoice.pdf.

## Resolution

The following Standard resolutions are available:

- Low Resolution

- Full Resolution

- Complex-Format Data-Full Scene

The following ScanSAR resolutions are available, more details at http://www.asf.alaska.edu/R1ScanSAR.pdf :

  - Low

  - Medium

  - Full

Notes on prices based on resolution for both Standard SAR and ScanSAR beams are given below.

Standard Processing Prices for ERS-1, ERS-2, JERS-1, and RADARSAT-1 Standard-Beam SAR Data

| Product | Price | Size |
| --- | --- | --- |
| Low Resolution | $2.00 | 1.1 MB |
| Full Resolution | $15.00 | 64.1 MB |
| ERS-1, ERS-2, JERS, RADARSAT-1 Complex-Format Data-Full scene | $100.00 | 525 – 550 MB |

Processing Prices for RADARSAT-1 ScanSAR Data Products

| Product | Price | Size |
| --- | --- | --- |
| Low Resolution | $5.00 | 1.6 MB |
| Medium Resolution | $15.00 | 26.0 MB |
| Full Resolution | $30.00 | 104.0 MB |

## Media type and Delivery

Media can be delivered via file transfer protocol or mailed on a tape. Prices are listed below.

Media Price Addition

| Type | Cost |
| --- | --- |
| Disk Space (for files transferred via ftp) | 50 per product |
| Tapes: |  |
| 4mm 2GB, 8mm 2.5 GB, 8mm 5GB | 1.00 per product |
| Digital Linear Tape (DLT) at 20GB, 35GB | 10.00 per product |

## Cost

Here is an example of the costing for a data order.

Example 1:

For an order of a non-foreign ground station RADARSAT-1 ScanSAR Full Res Product, delivered via ftp:

| Product Processing Cost= Media Cost= Total= | 30.00 .50 30.50 | Data Credits Data Credits Data Credits |
| --- | --- | --- |

See http://www.asf.alaska.edu/4_3_1.html for more guidelines to estimate costs for data acquisition.