POLAR Spacecraft Status As of: Weds, 7 Sept, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:51=AN STIP data only | NOAA-14J AM: 20:39=AN STIP data only | NOAA-15K AM: 18:06=AN GAC data only | NOAA-16L PM: 14:41=AN GAC&LAC data | NOAA-17M AM: 22:25=AN GAC&LAC data | NOAA-18N PM 14:00=AN GAC & LAC data Operational 30Aug05 |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) Safestate recorder changes planned | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=DTR 1B | SSRs 1,2,3,4,5 Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 Conflict with N17 No turnon date | #1 ON 137.50 MHZ Since 30 Aug End N12 Conflict | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ Conflict with N14 | #2 ON 137.9125 MHZ Change under consdieration |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ Since 8/30/05 | #2 137.77 MHZ | #1 137.35 MHZ Since 8/30/05 |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT Power drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback Swapped 8/30 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback Swapped 8/30 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/04 Full Sun Eclipse season ended 20Aug Sun Angle 25 downtrend to 12 mid-Oct 05 Batts 1&2=LRC Batt !&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 48 Steady trend Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 18 downtrend to 2 degs on 10 Oct 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 51 Downtrend to 41 on 30 Oct 05 Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Array 360 slew test planned for 20 & 21 Sept Eclipse all year Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 PSSS enabled 30May |
| AVHRR | Nominal | Nominal Channels 2 & 4 to APT 8/2/05 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Improving TCE24 OFF 4/14/04 Imagery sporadic bar codes since 6 Aug Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal TOAR 445 CLOSED 7/12/05 FW mode=Hi Powr FW Heater OFF | Operational High levels of imagery radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | Operational Status downgraded to Yellow 15 Aug 05 TOAR 448 Noise in long wave channels 1-12. Some improvement reported. |
| MHS/MIU |  |  |  |  |  | Nominal Final config 6/4/05 |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU-8 TOAR 449 turned off 6/13 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations No data reported by products division 7/25/05 “transient” hit |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Thermal downtrend occurring on spacecraft | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12	No change from last week.  N12 supports have increased to average one per day which improves the analytical

situation somewhat.  EMOSS Power subsystem engineer Carl Gliniak is not recommending any reconfigurations to the power balance equation at this time, therefore no failed payloads will be turned on for use as resisters in the foreseeable future, subject to short notice change based on situational changes.

NOAA-14:	At 1 Sept at 18:16z the NOAA-14 SBUV (a significantly less than nominal payload) suddenly dropped out of its

normal operating mode (discrete mode).  The instrument should always have one of its four operational modes selected (the modes are discrete, sweep, position and wavelength calibration), but after discrete mode was autonomously switched off, there was no operational mode selected and the grating drive stopped scanning and remained at grating position -673.  The on-duty AET detected the problem on 2 Sept at 00:27 (even though there was no flag indicating the problem had occurred) and notified engineering. After investigating the situation, EMOSS engineers determined that even though the grating position remained fixed in place, it was merely “parked” at that location and not stuck as has been the case on several occasions with this payload.  The primary reason for this deduction was that the various SBUV temperatures (both analog and DIG-A) showed no marked increase contrary to what occurs when the grating drive is stuck.  Therefore, EMOSS recommended that the payload should simply be commanded back to discrete mode, a recommendation that was approved by both NOAA and NASA personnel.  This command, (SBGM1) was sent to the SBUV on a pass at 14:33z on 2 Sept and the instrument immediately resumed normal operations.  The SBUV was monitored during N14’s next pass at 17:50z and was observed to be still operating in discrete mode, as expected, with grating positions updating nominally.  It has remained nominal since that time.  At the time of the event, just about every SBUV Dig-A telemetry point jumped to a “pegged” value, for a single update before, in most cases returning to its previous, nominal values.  Because of these surges, it is believed that a single event upset or some kind of transient electrical event occurred within the spacecraft electronics that caused the mode to “drop out”.  SBUV analog values, SEM science telemetry and solar activity were all investigated, but show nothing out of the ordinary that might explain this anomaly.  An event report was generated and submitted by Jim Walters who led the EMOSS effort to recover this SBUV supported by Will Chadwick, and Sally House.  Procedures are being put in place by EMOSS engineers to improve the controllers ability to detect this problem (developing a pseudo telemetry value for SBUV mode) as well as resolve it (developing an SET COP) should it reoccur.  (See Illustrations 1 and 2)

N14 power balance remains nominal as does the AVHRR health although there are some small instabilities starting to be exhibited by the scan motor current.  Notwithstanding those minor instabilities, the N14 AVHRR imagery (only HRPT currently available) remains nominal as does its component temperatures and synch delta (illustration 3).  VTX-2 (APT) remains off until TBD because of an RF conflict with N17.

NOAA-15:	The N15 spacecraft remains in a thermal downtrend which should continue as the sun angle on the spacecraft works its way down to approximately 2 degrees in mid-October (which is not as low as the zero degrees angle it reached at this time last year).  The N15 AMSU’s were nominal during the past week (illustration 4) while the AVHRR scan motor current actually improved as it got cooler and the HIRS remained the same, completely nominal (illustration 5).  All other N15 subsystems were performing nominally, from an engineering perspective, at the time of this report.

NOAA-16:	On 1 Sept at 17:30z, engineering was notified by users that N16 AVHRR imagery was "continuously fully bar

coded".  EMOSS conducted an investigation into this issue and saw no problems with the AVHRR hardware.  However, further investigation determined that starting at the beginning of the day on 30 Aug (the same time N18 was declared operational) all MIRP Rephase Enable commands for N16 had been omitted from the stored command load.  These omitted commands were not the cause of the bar coded imagery.  As long as the AVHRR scan motor current remained below 280 mAMps, bar codes are unlikely to happen.  If the current goes above that threshold (which it has done numerous times in the past 2 months), bar coded imagery is a typical result.  In bar code cases, the rephase enable command, which is always executed out of stored commands over the South Pole (N16 only) usually clears the imagery until the next threshold breach when the process occurs all over again. (Technical Note: actual MIRP rephasing is triggered by synch delta values which, until recently, were usually “pegged” within 30 minutes of a rephase occurring.)   On 31 Aug between 01:14 and 02:20Z (the exact time cannot be determined because of an N16 data gap that occurred at this very time) the scan motor current must have risen past this threshold before going back to its previous range where it has since remained.  This quick rise was enough to cause bar code imagery.  Normally, within a half hour or so the spacecraft would have gone over the South Pole, rephase would have been enabled by stored commands and the imagery would have been cleared.  However, since no rephase enable commands were in the N16 stored command table the bar coded imagery persisted.  Upon isolating the cause of the problem, engineering directed the AET to invoke a realtime COP to manually command an N16 MIRP rephase enable.  This commanding was done at 19:30z on 1 Sept and immediately cleared up the imagery.  In the meantime, the Scheduling Group was notified of this omission and are investigating its cause.  On 2 Sept the Scheduling Group regenerated the stored command table with the required rephase enable commands and there has not been a reoccurrence of this situation (or bar coded imagery) since that time (although imagery wave patterns still persist).   Jeff Devine and Will Chadwick were POC’s for the investigation and resolution into this event.  Otherwise, the N16 AVHRR scan motor current appears to be trending very slowly downward (a positive development) while synch delta is also showing signs of

N16 (cont)

improving as evidenced by the increasing amount of time it is taking before it becomes “pegged”.   (See illustrations 6 through 10).  The remainder of N16’s subsystems (including HIRS; illustration 11 and all three AMSU’s  illustration 12) were nominal and stable during the past week, from an engineering perspective as were all other subsystems.

NOAA-17:	There were no changes from last week.  The remaining N17 AMSU’s, the AVHRR and HIRS were all nominal and

stable during the past week (illustration 13 and 14).  In addition, the gyros on N17, which had recently shown some tendencies toward instability remained stable during the past week (illustration 15).  Regardless, both the gyros on N17 are operating at, or near all time highs and increased vigilance over them will be maintained by EMOSS into the foreseeable future.  Jim Sheperd is EMOSS POC for this subsystem.

NOAA-18:	N18 is officially operational as of 30Aug at 00:30.  There were no changes to N18 configurations or health during the

past week.  The N18 payload suite performed in a nominal and stable manner during the past week (illustrations 16-18) as did the rest of the subsystems on N18 (illustrations 19-21).  In addition, EMOSS engineers have received reports that some (not all) of the less than nominal HIRS channels which resulted in a TOAR been generated have been improving recently.

The investigation into the pitch oscillation TOAR continues.  To support this investigation, a test is currently being discussed among NOAA and NASA engineers that will result in the N18 solar array being slewed completely around (360 degrees) while in the dark/eclipse portion of its orbit.  If implemented, this slew will be performed twice, once in each direction over two separate days.  EMOSS engineer Jon Woodward is supporting the planning stage of this operation by identifying and preparing spacecraft macros and CPU telemetry changes that will be necessary to support the operations.  The test is tentatively planned for 20 Sept and will also use TDRSS and McMurdo to support in addition to the CDA’s.   To prepare for this implementation, NASA has requested that McMurdo have a readiness test  ensure they can support this array slew operation.  EMOSS engineer Will Chadwick is leading the effort to support this McMurdo readiness test.  This test was originally going to have the NOAA-18 STX4 transmitter turned on and configured for AIP during Wallops Rev. 1555  (7 Sept at 1807Z) while McMurdo tried to lock on the downlink.  It has since slipped until Monday 12 Sept.  This configuration will last for several revs until NASA requests the transmitter be deconfigured.

Discussions regarding the possible swap of N18’s VTX (APT) assignment are also underway among the engineering and scheduling divisions.  Apparently, the VTX currently in operation (#2 at 137.9125 MHZ) on N18 is often interfered with by cellular devises while orbiting over the European continent.  To alleviate this condition a swap to VTX#1 (137.1 MHZ) is under consideration.  No date has yet been determined for this reconfiguration, if it should occur.

Misc:	Engineers are currently discussing the efficacy of swapping out a number of the safe state recorders throughout the

POES constellation.  The reasons behind this possibility is that the safe state recorders remain idle for very long periods

of time and there is some belief that “exercising them” and “resting” other playback recorders might prolong all of these components.  No date is planned as yet for this operation.  Will Chadwick and Jon Woodward are EMOSS POC’s.

Illustration 1:  NOAA-14 SBUV Autonomous Mode Switch Analysis

(Dozens DIG-A values spiked at exactly the same time then returned to nominal, except MODE stayed at an error value and instrument stopped scanning.)

Illustration 2:  N14 SBUV Recovery Analysis

(One command and Mode went back to where it belonged while scanning resumed.)

Illustration 3:  N14 AVHRR Health Analysis

(Nominal and generally stable but not as stable as it has been for the past several weeks as evidenced by the stability analysis graph in lower left.)

Illustration 4:  N15 AMSU Health Analysis

(Nominal and stable with a pronounced thermal downtrend that should continue for another several weeks.)

Illustration 5:  N15 HIRS and AVHRR Health Analysis

(Note the continued improvement in scan motor current [lower right] as the payload continues to cool down [upper right].  Synch delta remains nominal as does AVHRR imagery.  HIRS remains rock solid.

Illustration 6:  N16 AVHRR Synch Delta Analysis

Originally the lack of a rephase frame loss on the right image (*) would have been considered a favorable development.  See next page synch delta plot.

ILLUSTRATION 7:  N16 AVHRR Health Analysis

(Seem to be improving, no bar codes since 2 Sept.  On the synch delta graph [lower left] the red X designates the time frame where the GAC image without the rephase frame loss, on the previous page, was obtained.  Since, at that time the synch delta was basically “pegged” there should have been a Rephase frame loss on that GAC image, but there was not.  This was the primary clue that allowed EMOSS engineers to determine that MIRP rephases were no longer in the stored command table.

ILLUSTRATION 8:  Rephase Imagery Analysis

The first image was taken AFTER Rephase Enable commands were taken out of stored command table.  No bar codes indicates scan motor current was below threshold.  An hour later, bar codes appeared and remained there until 1.5 days later when the MIRP was manually rephased over Wallops.  This cleared the bar codes which haven’t returned since.

Illustration 9:  N16 AVHRR Health Analysis

(The cause of the bar codes that started on 31 Aug after 02:00 may never be known since the data is missing during the time of the last good image and the start of bar coded images.

Illustration 10:  N16 AVHRR Current Imagery Analysis

(No bar codes today, wave patterns persist.)

Illustration 11:  N16 HIRS Health Analysis

(About the same as last week.)

Illustration 12:  N16 AMSU Health Analysis

(Nominal and stable, like last week.)

Illustration 13:  N17 AMSU Health Analysis

(About the same as last week, nominal and stable.)

Illustration 14:  N17 HIRS and AVHRR Analysis

(About the same as last week, nominal and stable.)

Illustration 15:  N17 ADACS Analysis

(About the same as last week, nominal and stable.)

Illustration 16:  N18 AMSU Health Analysis

(About the same as last week, nominal and stable.)

Illustration 17:  N18 HIRS and AVHRR Health Analysis

(About the same as last week, nominal and stable.)

Illustration 18:  N18 MHS Health Analysis

(About the same as last week, nominal and stable.)

Illustration 19:  N18 Power Health Analysis

(About the same as last week, nominal and stable.)

Illustration 20:  N18 DHS/Comm Health Analysis

(DDR’s still spiking, STX-1 operating nominally as the new HRPT transmitter.)

Illustration 21:  N18 ADACS Analysis

(About the same as last week.  Pitch investigation continues)

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING September 2, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 08/26 | N/A | +237 msec | -264 msec | +166 msec | +101 msec | 0 msec |
| SAT. 08/27 | N/A | +237 msec | -266 msec | +166 msec | +103 msec | +002 msec |
| SUN. 08/28 | N/A | +238 msec | -265 msec | +166 msec | +103 msec | +003 msec |
| MON. 08/29 | N/A | +233 msec | -266 msec | +165 msec | +104 msec | +004 msec |
| TUE. 08/30 | -308 msec | +233 msec | -269 msec | +167 msec | +105 msec | +005 msec |
| WED. 08/31 | -310 msec | +234 msec | -267 msec | +170 msec | +105 msec | +008 msec |
| THU. 09/01 | -314 msec | +235 msec | -269 msec | +171 msec | +104 msec | +009 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of -500 milliseconds on 04/17/05 due to fractional second daily ETCUP. A clock

jump of +500 milliseconds on 07/01/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 09/15/05.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Mickey Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead 	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015