Progress Update - Western Wind and Solar Integration Study

6/26/08

Wind mesoscale modeling

3TIER completed development of time-series wind speed and power data for the Western US. The wind speed dataset includes wind speeds at 5 hub heights for 10 minute intervals for 2004-2006 at a 2 km resolution. These 1.2 million sites were down-selected to 32,000 sites for wind power profile development, based on specific criteria (transmission access, load correlation, resource quality). Public webinars were held in March to receive feedback on sites selected and to request modeling of additional sites. Ten Vestas V90 3 MW turbines at 100m hub height (totaling 30 MW) were modeled on each 2km x 2km site (for a total of 960 GW) using 3TIER’s SCORE methodology. In addition, 3TIER has modeled day-ahead wind power forecasts for each hour. 3TIER has completed a user-friendly web interface that will be made public this summer so that wind power profiles for specific sites will be publicly available for research, studies, and prospecting. 3TIER has completed validation reports that compare the mesodata to measured data and NREL and others are reviewing accuracy prior to public release of data.

Solar mesoscale modeling and preliminary site selection

NREL has received solar direct normal and global insolation data at 10km resolution and at hourly intervals for 2004-6 from Richard Perez of SUNY. 3TIER has generated solar forecasts as part of their mesomodel. NREL has developed over 200 GW of power profiles for concentrating solar power (CSP) plants based on parabolic trough technology with 6 hours of thermal storage. NREL has also modeled distributed PV profiles for 150 sites.

Scenarios

Based on the output of the August Stakeholder Meeting, GE will run production simulations on the selected scenarios in the latter half of 2008. The high renewables basecase for 2017 is detailed in the table below. Plant capacities are approximate and depend on the actual capacity factor of each individual site.

|  | Wind | Solar PV | CSP | Total |
| --- | --- | --- | --- | --- |
| Study footprint (WestConnect) | 30% by energy | 1.5% | 3.5% | 35% |
|  | 28,256 MW | 2472 MW | 2884 MW | 33,613 MW |
| Rest of WECC | 20% | 0.9% | 2.1% | 23% |
|  | 36,767 MW | 2895 MW | 3378 MW | 43,040 MW |
| Total | 65,023 MW | 5368 MW | 6262 MW | 76,654 MW |

Site selection

GE is undertaking a detailed site selection process to down-select from the 960GW of wind and 200 GW of CSP profiles to the needed capacities according to the above table. They are developing two “bookend” scenarios, based on 1) each transmission area using in-area renewables, and 2) development of the best quality resources available in the WestConnect footprint. They will also develop a more realistic scenario, in which the transmission costs trade off with lowered wind energy costs.

Statistical Analysis

GE is undertaking statistical analysis of a 2008 baseline scenario and the first “bookend” scenario described above. They will present results on this analysis at the August Stakeholder Meeting. Based on this analysis, other scenarios will be developed and proposed. These may include a “load correlation” scenario and a high solar scenario.

The study year is 2017, to line up with WECC transmission planning. Loads, utility plant portfolios, and planned transmission will all be projected out to 2017. We will model 2017 three times, using historical weather (solar, wind) and load data from 2004, 2005, and 2006, to get a sense of interannual variability.

Stakeholder Meeting

The next Stakeholder Meeting (open to all) is August 14 and will be held at a hotel near the Denver International Airport. This will include statistical analysis results of the first bookend scenario and the baseline scenario as well as a description of proposed scenarios for the production simulation analysis. We expect preliminary production simulation analysis results at the end of 2008.

Information about the study can be found at

http://westconnect.com/

Please feel free to contact me if you have any questions or further input.

Debbie Lew

National Wind Technology Center

National Renewable Energy Laboratory

1617 Cole Blvd

Golden, CO 80401

work: 303-384-7037

email: debra_lew@nrel.gov