# PART X – TURFING

### ITEM T-901  SEEDING

DESCRIPTION

901-1.1   This item shall consist of soil preparation, seeding [    ] the areas shown on the plans or as directed by the Engineer in accordance with these specifications.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

The Engineer shall specify fertilizing or liming or both as needed for a specific project.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

MATERIALS

901-2.1  SEED  The species and application rates of grass, legume, and cover-crop seed furnished shall be those stipulated herein.  Seed shall conform to the requirements of Fed. Spec. A-A-2671.

Seed shall be furnished separately or in mixtures in standard containers with the seed name, lot number, net weight, percentages of purity and of germination and hard seed, and percentage of maximum weed seed content clearly marked for each kind of seed.  The Contractor shall furnish the Engineer duplicate signed copies of a statement by the vendor certifying that each lot of seed has been tested by a recognized laboratory for seed testing within 6 months of date of delivery.  This statement shall include:  name and address of laboratory, date of test, lot number for each kind of seed, and the results of tests as to name, percentages of purity and of germination, and percentage of weed content for each kind of seed furnished, and, in case of a mixture, the proportions of each kind of seed.

Seeds shall be applied as follows:

Seed 		Minimum Seed		Minimum Germination		Rate of Application

Purity (Percent)		(Percent)				lb./acre (or lb./1,000 S.F.)

Seeding shall be performed during the period between [   ] and [    ] inclusive, unless otherwise approved by the Engineer.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

Seeding dates, species and seeding rates must be specified that are compatible with local climate and soil conditions.  Due consideration must be given to longevity of plants, resistance to traffic and erosion, and attraction of birds or large animals.  More than one seeding season may be specified, if appropriate.  Local offices of the USDA Soil Conservation Service and the State University Agricultural Extension Service (County Agent or equivalent) shall be consulted for assistance and recommendations.  These agencies shall also be consulted for liming and fertilizer recommendations.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

901-2.2  LIME.  Lime shall be ground limestone containing not less than 85% of total carbonates, and shall be ground to such fineness that 90% will pass through a No. 20 mesh sieve and 50% will pass through a No. 100 mesh sieve.  Coarser material will be acceptable, providing the rates of application are increased to provide not less than the minimum quantities and depth specified in the special provisions on the basis of the two sieve requirements above.  Dolomitic lime or a high magnesium lime shall contain at least 10% of magnesium oxide.  Lime shall be applied at the rate of [    ].  All liming materials shall conform to the requirements of ASTM C 602.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

The Engineer shall specify the application rate in pounds per acre.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

**

901-2.3  FERTILIZER.  Fertilizer shall be standard commercial fertilizers supplied separately or in mixtures containing the percentages of total nitrogen, available phosphoric acid, and water-soluble potash.  They shall be applied at the rate and to the depth specified herein, and shall meet the requirements of Fed. Spec. A-A-1909 and applicable state laws.  They shall be furnished in standard containers with name, weight, and guaranteed analysis of contents clearly marked thereon.  No cyanamide compounds or hydrated lime shall be permitted in mixed fertilizers.

The fertilizers may be supplied in one of the following forms:

a.  A dry, free-flowing fertilizer suitable for application by a common fertilizer spreader;

b.  A finely-ground fertilizer soluble in water, suitable for application by power sprayers; or

c.  A granular or pellet form suitable for application by blower equipment.

Fertilizers shall be [    ] commercial fertilizer and shall be spread at the rate of [    ].

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

The Engineer shall specify the analysis and the application rate in pounds per acre.  Paragraphs 2.2 and 2.3 shall be deleted if not applicable.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

901-2.4  SOIL FOR REPAIRS.  The soil for fill and topsoiling of areas to be repaired shall be at least of equal quality to that which exists in areas adjacent to the area to be repaired.  The soil shall be relatively free from large stones, roots, stumps, or other materials that will interfere with subsequent sowing of seed, compacting, and establishing turf, and shall be approved by the Engineer before being placed.

CONSTRUCTION METHODS

901-3.1  ADVANCE PREPARATION AND CLEANUP.  After grading of areas has been completed and before applying fertilizer and ground limestone, areas to be seeded shall be raked or otherwise cleared of stones larger than 2 inches (50 mm) in any diameter, sticks, stumps, and other debris that might interfere with sowing of seed, growth of grasses, or subsequent maintenance of grass-covered areas.  If any damage by erosion or other causes has occurred after the completion of grading and before beginning the application of fertilizer and ground limestone, the Contractor shall repair such damage.  This may include filling gullies, smoothing irregularities, and repairing other incidental damage.

An area to be seeded shall be considered a satisfactory seedbed without additional treatment if it has recently been thoroughly loosened and worked to a depth of not less than 5 inches (125 mm) as a result of grading operations and, if immediately prior to seeding, the top 3 inches (75 mm) of soil is loose, friable, reasonably free from large clods, rocks, large roots, or other undesirable matter, and if shaped to the required grade.

However, when the area to be seeded is sparsely sodded, weedy, barren and unworked, or packed and hard, any grass and weeds shall first be cut or otherwise satisfactorily disposed of, and the soil then scarified or otherwise loosened to a depth not less than 5 inches (125 mm).  Clods shall be broken and the top 3 inches (75 mm) of soil shall be worked into a satisfactory seedbed by discing, or by use of cultipackers, rollers, drags, harrows, or other appropriate means.

901-3.2  DRY APPLICATION METHOD.

a.  Liming.  Lime shall be applied separately and prior to the application of any fertilizer or seed and only on seedbeds that have previously been prepared as described above.  The lime shall then be worked into the top 3 inches (75 mm) of soil after which the seedbed shall again be properly graded and dressed to a smooth finish.

b.  Fertilizing.  Following advance preparations and cleanup fertilizer shall be uniformly spread at the rate that will provide not less than the minimum quantity stated in paragraph 901-2.3.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

Delete paragraphs a. and b. if not applicable.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

c.  Seeding.  Grass seed shall be sown at the rate specified in paragraph 901-2.1 immediately after fertilizing, and the fertilizer and seed shall be raked within the depth range stated in the special provisions.  Seeds of legumes, either alone or in mixtures, shall be inoculated before mixing or sowing, in accordance with the instructions of the manufacturer of the inoculant.  When seeding is required at other than the seasons shown on the plans or in the special provisions, a cover crop shall be sown by the same methods required for grass and legume seeding.

d.  Rolling.  After the seed has been properly covered, the seedbed shall be immediately compacted by means of an approved lawnroller, weighing 40 to 65 pounds per foot (60 to 97 kg per meter) of width for clay soil (or any soil having a tendency to pack), and weighing 150 to 200 pounds per foot (223 to 298 kg per meter) of width for sandy or light soils.

901-3.3  WET APPLICATION METHOD.

a.  General.  The Contractor may elect to apply seed and fertilizer (and lime, if required) by spraying them on the previously prepared seedbed in the form of an aqueous mixture and by using the methods and equipment described herein.  The rates of application shall be as specified in the special provisions.

b.  Spraying Equipment.  The spraying equipment shall have a container or water tank equipped with a liquid level gauge calibrated to read in increments not larger than 50 gallons (190 liters) over the entire range of the tank capacity, mounted so as to be visible to the nozzle operator.  The container or tank shall also be equipped with a mechanical power-driven agitator capable of keeping all the solids in the mixture in complete suspension at all times until used.

The unit shall also be equipped with a pressure pump capable of delivering 100 gallons (380 liters) per minute at a pressure of 100 pounds per square inch (690 kPa).  The pump shall be mounted in a line that will recirculate the mixture through the tank whenever it is not being sprayed from the nozzle.  All pump passages and pipe lines shall be capable of providing clearance for 5/8 inch (15 mm) solids.  The power unit for the pump and agitator shall have controls mounted so as to be accessible to the nozzle operator.  There shall be an indicating pressure gauge connected and mounted immediately at the back of the nozzle.

The nozzle pipe shall be mounted on an elevated supporting stand in such a manner that it can be rotated through 360 degrees horizontally and inclined vertically from at least 20 degrees below to at least 60 degrees above the horizontal.  There shall be a quick-acting, three-way control valve connecting the recirculating line to the nozzle pipe and mounted so that the nozzle operator can control and regulate the amount of flow of mixture delivered to the nozzle.  At least three different types of nozzles shall be supplied so that mixtures may be properly sprayed over distance varying from 20 to 100 feet (6 to 30 m).  One shall be a close-range ribbon nozzle, one a medium-range ribbon nozzle, and one a long-range jet nozzle.  For case of removal and cleaning, all nozzles shall be connected to the nozzle pipe by means of quick-release couplings.

In order to reach areas inaccessible to the regular equipment, an extension hose at least 50 feet (15 m) in length shall be provided to which the nozzles may be connected.

c.  Mixtures.  Lime, if required, shall be applied separately, in the quantity specified, prior to the fertilizing and seeding operations.  Not more than 220 pounds (100 kg) of lime shall be added to and mixed with each 100 gallons (380 liters) of water.  Seed and fertilizer shall be mixed together in the relative proportions specified, but not more than a total of 220 pounds (100 kg) of these combined solids shall be added to and mixed with each 100 gallons (380 liters) of water.

All water used shall be obtained from fresh water sources and shall be free from injurious chemicals and other toxic substances harmful to plant life.  Brackish water shall not be used at any time.  The Contractor shall identify to the Engineer all sources of water at least 2 weeks prior to use.  The Engineer may take samples of the water at the source or from the tank at any time and have a laboratory test the samples for chemical and saline content.  The Contractor shall not use any water from any source that is disapproved by the Engineer following such tests.

All mixtures shall be constantly agitated from the time they are mixed until they are finally applied to the seedbed.  All such mixtures shall be used within 2 hours from the time they were mixed or they shall be wasted and disposed of at locations acceptable to the Engineer.

d.  Spraying.  Lime, if required, shall be sprayed only upon previously prepared seedbeds.  After the applied lime mixture has dried, the lime shall be worked into the top 3 inches (8 cm), after which the seedbed shall again be properly graded and dressed to a smooth finish.

Mixtures of seed and fertilizer shall only be sprayed upon previously prepared seedbeds on which the lime, if required, shall already have been worked in.  The mixtures shall be applied by means of a high-pressure spray that shall always be directed upward into the air so that the mixtures will fall to the ground like rain in a uniform spray.  Nozzles or sprays shall never be directed toward the ground in such a manner as might produce erosion or runoff.

Particular care shall be exercised to insure that the application is made uniformly and at the prescribed rate and to guard against misses and overlapped areas.  Proper predetermined quantities of the mixture in accordance with specifications shall be used to cover specified sections of known area.  Checks on the rate and uniformity of application may be made by observing the degree of wetting of the ground or by distributing test sheets of paper or pans over the area at intervals and observing the quantity of material deposited thereon.

On surfaces that are to be mulched as indicated by the plans or designated by the Engineer, seed and fertilizer applied by the spray method need not be raked into the soil or rolled.  However, on surfaces on which mulch is not to be used, the raking and rolling operations will be required after the soil has dried.

901-3.4  MAINTENANCE OF SEEDED AREAS.  The Contractor shall protect seeded areas against traffic or other use by warning signs or barricades, as approved by the Engineer.  Surfaces gullied or otherwise damaged following seeding shall be repaired by regrading and reseeding as directed.  The Contractor shall mow, water as directed, and otherwise maintain seeded areas in a satisfactory condition until final inspection and acceptance of the work.

When either the dry or wet application method outlined above is used for work done out of season, it will be required that the Contractor establish a good stand of grass of uniform color and density to the satisfaction of the Engineer.  A grass stand shall be considered adequate when bare spots are one square foot or less, randomly dispersed, and do not exceed 3% of the area seeded.  If at the time when the contract has been otherwise completed it is not possible to make an adequate determination of the color, density, and uniformity of such stand of grass, payment for the unaccepted portions of the areas seeded out of season will be withheld until such time as these requirements have been met.

METHOD OF MEASUREMENT

901-4.1  The quantity of seeding to be paid for shall be the number of units [1,000 square feet (square meters)][   acres (square meters)] measured on the ground surface, completed and accepted.

BASIS OF PAYMENT

901-5.1  Payment shall be made at the contract unit price per [1,000 square feet (square meters)][acre (square meters)] or fraction thereof, which price and payment shall be full compensation for furnishing and placing all material and for all labor, equipment, tools, and incidentals necessary to complete the work prescribed in this item.

Payment will be made under:

Item 901-5.1		Seeding—per [1,000 square feet (square meters)][acre (square meters)]

MATERIAL REQUIREMENTS

ASTM C 602		Agricultural Liming Materials

ASTM D 977		Emulsified Asphalt

FED SPEC A-A-1909	Fertilizer

FED SPEC A-A-2671	Seeds, Agriculture

END OF ITEM T-901

Intentionally Left Blank