# Slide 4-1: Module 4 Clean Up and Check Your Work

- This is the module title slide.

- Announce the module title move quickly to the next slide.

Overview of this module:  The table below summarizes the content and teaching methods for this module.  This is for your reference.  Do not cover this with the participants.

| Module 4: Clean up and check your work 1 hour |
| --- |
| What is effective clean up? Clean-up tool kit Interior clean up Exterior clean-up Checking your work Safe disposal (optional demo or exercise) Activity: Hands on clean-up exercise Activity: Clearance demonstration | Key message: Clean up right. Use wet mops and HEPA vacuums. Traditional methods don’t do the job. Notes: Slides followed by an exercise Slides (30 minutes) Hands-on Exercise (30 minutes) Preparing for this module: Prepare materials for hands-on exercise and clearance demonstration. Materials needed: Dust wipe sampling materials and tools listed in the Clean-Up toolkit. Options: The trainer may choose to use the hands-on clean-up exercise later, as part of a comprehensive hands-on exercise (as shown in Lesson Plan #2). The trainer can also choose to demonstrate gooseneck sealing or have participants do it themselves. (Have necessary materials ready.) |

Slide 4-2 : Module 4 Overview

- Effective clean-up includes using specific techniques and following the proper order when cleaning.  In this section participants will learn:

- What an effective clean-up includes

- What tools to always keep in your truck and at the work site

- Effective techniques to clean after both interior and exterior jobs

- Safe disposal methods

- How to check your work

- This module focuses on how to clean to pass a visual check.  Visual check means that an area has been cleaned to the point that no dust, debris or paint chips can be seen with the naked eye, and it is the goal of every clean-up.

- Remember, because lead dust can be invisible, a visual check does not guarantee that you will pass a dust sample test.

# Slide 4-3: What is Effective Clean-up?

- Discuss the similarities of clean-up and approaching a job.  Explain that, just as you approach a job with planning, set-up and containment, you must approach cleaning by first having effective containment, then carefully following specific procedures to best clean the work area.  The techniques outlined in this section should make your clean-up faster, more efficient, and more effective.

- Remember:

- Always pass a visual check.

- Proper disposal and checking your work are essential to the process of cleaning.

- The most effective cleaning will follow this sequence:

1.	Pick up all visible paint chips and debris.

2.	Clean and dispose of protective sheeting.

3.	Slowly HEPA vacuum the work area, working from high to low.

4.	Thoroughly wet clean, working from high to low.

5.	If necessary repeat HEPA vacuuming or wet cleaning.

6.	Visually inspect your work.

- Bag all waste in heavy duty plastic bags, Agooseneck@ seal and dispose according to Federal, State and local regulations.

- Clearance

- Demonstrate how to Agooseneck seal@ a heavy duty plastic bag and note that this will again be covered in the disposal section.

- Discuss why this clean-up sequence should work well.

- Picking up all visible debris and paint chips prepares a work area for the first HEPA vacuum.

- Clean and dispose of protective sheeting.  This step should come before HEPA vacuuming in order to collect any dust that may escape from the protective sheeting.

- HEPA vacuum the area from high to low.  This first HEPA vacuum will collect dust and debris not visible to the naked eye.

- Wet cleaning the area will further dislodge any lead contaminated dust or debris not collected by the first HEPA vacuum.  Wet cleaning also gets dust and debris that is Astuck@ to surfaces.

- If necessary, a final pass with the HEPA vacuum or wet clean will capture any remaining dust or debris left after the wet cleaning.

- The last step should be to check your work and make sure that a visual check is achieved and  all waste is bagged, sealed and disposed of in accordance with Federal, State and local laws.  Performing a dust wipe test is recommended for all work.

- Clearance is required by HUD in homes receiving Federal housing assistance.  (See p. 4-7).

Slide 4-4 : Clean Up Toolkit

- This slide shows a list of cleaning tools that you should always keep in your truck.

- Some tips:

- Be sure to change mop heads when necessary.  You do not want to be mopping and cleaning with a dirty, used mop head as this could spread dust into other areas.

- You need either a two-sided bucket or two single buckets to keep your wash and rinse water separate.  Be sure to change your detergent and rinse water often.  You will not clean successfully if you clean with dirty water.

- Heavy duty garbage bags are heavy duty plastic bags.

- For small jobs, disposable wipes are a good cleaning method.

- Ask participants if anyone uses tools that are not included in the list.

- If so, what are they and what do they use them for?

- This is a good time to mention that a shop-vac is not adequate for cleaning up lead dust.

Slide 4-5: Interior Clean-up Techniques

- Ask: Why should you pick up paint chips and other debris before picking up the protective sheeting?  Why should you mist down and wet wipe the protective sheeting before picking it up?

[Answer to both questions: to prevent accidental spreading of lead-contaminated paint chips and dust off of the protective sheeting]

- After the first visual inspection of the work area, cleaning, folding and disposing of the protective sheeting is the next step. Clean your protective sheeting with a HEPA vacuum and wet wipe if necessary.  Once cleaned, fold and seal the sheeting and dispose with the rest of your waste.  When you pick up and fold the protective sheeting be careful not to spread any dust that may remain on the sheeting.

- This process is followed by the HEPA vacuuming and wet cleaning (discussed on next slide) in order to get any dust that escaped the protective sheeting.

Slide 4-6: Interior Clean-up Techniques

- Emphasize that workers should always clean at least two feet beyond the work area.

- Also, discuss why clean-up should always proceed from high to low.

- [Answer:  Cleaning from high to low is more efficient and effective because any dust or debris dislodged will fall down to the floor.  Just as one would clean steps working from the top down, cleaning a work area should work from high to low to Apush@ all dust not collected down to the floor, which should be cleaned last.]

- These cleaning techniques and this sequence ensure that you pass a visual check.  While there is no guarantee that you will pass a dust sample analysis, this process is highly effective in cleaning a work area and if followed, significantly decreases the risk of not passing a dust sample analysis.  This will be discussed in greater detail later in the module.

Slide 4-7: Interior Checking Your Work

- Always conduct a visual check after your clean-up is completed.  If you find any dust or debris, make another pass with the HEPA vacuum and, if necessary, wet clean again.  You should continue these steps until the site passes a visual check.

- After passing a visual check you can perform clearance (dust sampling) to check your work.  In some instances dust sampling may be required.

- Discuss the following instances where clearance (dust sampling) may be required or requested:

- HUD requires clearance after certain kinds of jobs in housing receiving Federal housing assistance.  Ask if the property receives Federal assistance.  If so, ask if clearance is required.

- In some states, dust wipe sampling by a certified or trained person may be required by law.  Supervisors should be aware of laws regarding dust wipe sampling and renovation and remodeling work.

- In some instances, the owner may request dust wipe samples be taken to locate lead hazards and ensure cleaning has been effective.  If you follow the techniques outlined in this section, you should pass any dust wipe analysis.

- Emphasize that clean-up should always be performed as if a dust wipe analysis were going to be conducted after clean-up.

Slide 4-8: Exterior Clean-up Techniques

- The main point of cleaning after an exterior job is not to let dust spread beyond the work area and to focus specifically on the areas that children could have access to such as bare soil, play areas, exterior porches and exterior window sills.

- Always inspect beyond the work area.  Collect and dispose of all paint chips, dust and debris.

Slide 4-9: Exterior Clean-up Techniques

- Plastic protective sheeting can kill plants and other vegetation if used for an extended period of time.  Therefore, on many exterior jobs landscape fabric, screen tarp, or screen mesh is used.  This material must be fine enough to catch any debris or paint chips.  Although it is recommended to be disposed of after each use, because this material can be more expensive per square foot than plastic sheeting, many contractors reuse the material.

- In the case of reuse, the material must be cleaned thoroughly and pass a visual check before being folded and stored securely.  One method is to HEPA vacuum the material after the job is completed.  Washing the fabric may also prove effective; however, waste water and debris may be produced using this method.  The most effective way to clean exterior protective sheeting will be a slow HEPA vacuum followed, if necessary, by a wet clean and rinse.

Slide 4-10: Exterior Checking Your Work

- Discuss why another visual inspection for checking your work is necessary.

- Discussion:  A visual check should always occur before cleaning and focus on collecting all visible debris, large components, and paint ships.  This should be followed by your cleaning activities which in the case of exterior work consists mainly of a visual check and inspection.  However, after any cleanup activity another visual inspection is always necessary and should include areas not covered by the protective sheeting, areas outside the containment area, and all areas in the work area.

- Emphasize that contractors should focus on child access areas such as bare soil or ground, exterior porches, and exterior window sills.

Slide 4-11: Disposal

Have bags and tape ready for the demonstration and the hands-on activity if you choose to perform it.

- Demonstrate Agooseneck@ seal of disposal bags.

- Waste should be stored in a secure area to prevent children from getting into it and being exposed to lead dust.

- Discuss methods to handle waste water.

- Waste water produced during the job from mopping, wet cleaning or misting should not be poured down the sink, in the yard, down a storm drain or in a tub.

- Waste water should be poured down the toilet if local regulations allow for such disposal.  Before disposal, waste water should be filtered.

- Always be aware of Federal, State, and local regulations regarding waste water disposal.

- All waste should be handled carefully and sealed in heavy duty plastic bags.

- Supervisors must be aware of the components of the waste produced at the job site and the proper method of disposal.  Again, always be aware of Federal, State and local waste disposal regulations.

Optional Hands-On Activity (3 minutes)

- After demonstrating, give each participant a garbage bag and a strip of duct tape.

- Ask participants to practice making the gooseneck seal.

Walk around and make sure that each participant is doing it properly.

Slide 4-12: Disposal - Local and Federal Information

- Waste disposal is regulated under the Resource Conservation and Recovery Act (RCRA) and various associated State laws and regulations.

- Some waste generated from lead work may meet the definition of Ahazardous waste@ because it is toxic, corrosive, ignitable, or explosive.  Therefore, it is important for contractors to segregate waste into categories that are likely to be hazardous and non-hazardous.  Examples of hazardous waste may include: paint chips, vacuum debris, sludge or chemical waste from stripper and HEPA filters.

- Generators of less than 220 pounds of waste per job site per month are exempt from Federal waste disposal regulations and most State regulations.

- Many states have more stringent regulations than Federal requirements.  It is, therefore, important for contractors to understand their obligations under these laws and regulations.

- You should always be aware of how much waste you are generating per job site per month.

- EPA=s website has a list of telephone numbers for State information on solid and hazardous waste disposal at http://www.epa.gov/epaoswer/hotline/states.txt.

- In a memorandum to RCRA Senior Policy Advisors and EPA Regions 1-10, dated July 31, 2000, EPA=s Office of Solid Waste stated that lead-based paint waste from households may be disposed of as household garbage subject to applicable State regulations.  However, although EPA considers lead-based paint waste commonly generated during renovation, remodeling, and painting to be household waste, most states have not yet adopted this interpretation.  Until states do adopt EPA=s interpretation, they may continue to regulate lead-based paint waste as potentially hazardous if generated in large enough quantities as indicated on the slide. (U.S. EPA ARegulatory Status of Work Generated by Contractors and Residents from Lead-based Paint Activities Conducted in Households@ Memorandum from Elizabeth A. Cotsworth, Director, Office of Solid Waste, to RCRA Senior Policy Advisors and EPA Regions 1-10. July 31, 2000)

Slide 4-13: Exercise: Clean-Up

For this exercise you’ll need baby powder, water, and the Clean-Up Tool Kit (see Notes to Instructor).

Prepare this exercise in advance. Things to prepare are:

- Have appropriate tools and supplies ready.   Necessary tools and supplies include: buckets, mops, water, detergent, HEPA vacuum, wipes, plastic sheeting, plastic bags, tape, and other items in the Clean-Up Tool Kit.

- You’ll need access to water.

- Sprinkle each work area with baby powder to simulate the dust.

- Refer to the Skills Checklist in Appendix 9 for a list of skills that participants should practice.

When conducting the exercise:

- Instruct participants to stay in their groups.

- Circulate while they work to ensure they are doing the work properly.

- Coach them as necessary to correct any incorrect behaviors (refer to the Skills Checklist in Appendix 9).

- Give them a five minute warning.

- At 15 minutes, tell them to stop.

Debrief using the next slide.

## Option

You may also consider performing this set-up exercise later in the course as part of a larger comprehensive hands-on module as described in Lesson Plan 2 in the Notes to the Instructor at the front of this manual.  The comprehensive hands-on module combines the hands-on components from Modules 2, 3, and 4.

Note:  In some training facilities, such as hotels, you may not have access to water in the training room.  In such cases, instruct participants to walk through the process – practicing the order of the steps – HEPA vac, two bucket wash, cleaning from high to low, etc.  As a demonstration of how hard it is to clean up dust, consider sprinkling baby powder on a tabletop and experimenting with different methods for cleaning it up – broom and dust pan, HEPA vac, wet wipe, etc.

Slide 4-14: How Clean is Clean?

Have dust wipe materials ready for this slide.

- Ask participants if they can see any remaining baby powder. Chances are they can.

Demonstrate how a dust wipe is done and show them the surface of the wipe.  Highlight how clean the floor must be to pass this test.

Slide 4-15: Keep in Mind

- The items listed on the slide are important for planning and managing work efficiently.

- Remember, you should either clean the work site thoroughly at the end of each day or completely seal off the area and not allow re-occupation.

- Also remember to consider clearance testing by an independent person.  Even if clearance is not performed, you should always clean up as if it were.

- Note the checklist for cleaning procedures in the participant notes below the slide.  Ask participants whether they would add or change anything in the checklist.