Fermilab

ELECTRICAL HAZARD ANALYSIS / WORK PERMIT (EHAWP)

For Selected Work Activities on the AC Power Distribution System or Electrical Utilization Equipment

JOB NAME & LOCATION:

EFFECTIVE DATES OF PERMIT:	Start:	   		End:

WORK TO BE PERFORMED BY:

QUALIFIED PERSON IN CHARGE:	   		PHONE:

Does the Work Involve Diagnostic Energized Work?	Yes	    	 No	    		(Includes LOTO Verification)

Does the Work Involve Manipulative Energized Work?	Yes	    	 No	    		(Justification Required)

Is an Inspection Required After Work is Completed?	Yes	    	 No	    		(Reqd for New AC Pwr Installs)

If the Work Activity Involves Manipulative Energized Work, State the Justification Here.

DESCRIPTION OF WORK:

ASSOCIATED HAZARDS:

HAZARD MITIGATION:	Indicate Hazard/Risk Category ( -1, 0, 1, 2, 2*, 3 or 4 ):

SHOCK PROTECTION BOUNDARIES for ENERGIZED WORK

from NFPA 70E Table 130.2(C) for Fixed Circuit Parts and Article 130.3(A).  Indicate if Otherwise.

For 120/208 VAC: Shock Protection: Limited Approach: 3' 6".   Restricted & Prohibited Approach: Avoid Contact

For 480/277 VAC: Shock Protection: Limited Approach: 3' 6".   Restricted Approach:. 1 Ft.   Prohibited Approach: 1"

Class 	     	    Voltage-Rated Gloves and Leather Protectors Required for Subject Work Activity

ARC-FLASH PROTECTION BOUNDARY and REQUIRED PPE for ENERGIZED WORK

PPE Requirements for Shock & Arc Flash Protection are Fully Described in NFPA 70E, Article 130.7.  Indicate if Otherwise.

Clothing Must be Non-Melting or Untreated Natural Fiber, Unless Specified as Flame-Resistant (FR).

The Fermilab Default Flash Protection Boundary is 4 Feet   (as Qualified by Article 130.3(A) at 300 kA Cycles)

If Calculated, Indicate Flash Protection Boundary:	   	   feet and/or inches

If Calculated, Indicate Incident Energy Level for Arc Flash Protection:	   	   cal/cm2

HRC -1	Short-Sleeve Cotton T-Shirt, Long Cotton Pants, Safety Glasses  (0 to 1.2 cal/cm2)

HRC 0	Long-Sleeve Cotton Shirt, Long Cotton Pants, Safety Glasses  (0 to 1.2 cal/cm2)

HRC 1	FR Coverall, Safety Glasses, Hard Hat, Leather Protectors or Gloves  (>1.2 to 4 cal/cm2)

HRC 2	Cotton Clothing under FR Coverall, Safety Glasses, Hard Hat, Arc-Rated Face Shield, Hearing Protection, Leather Protectors or Gloves, Leather Work Shoes  (>4 to 8 cal/cm2)

HRC 2*	Cotton Clothing under FR Coverall, Safety Glasses, Hard Hat, Double-Layer Switching Hood, Hearing Protection, Leather Protectors or Gloves, Leather Work Shoes  (>4 to 8 cal/cm2)

HRC 3	Cotton Clothing under 2 FR Coveralls, Safety Glasses, Hard Hat, Flash Suit Hood, Hearing Protection, Leather Protectors or Gloves, Leather Work Shoes  (>8 to 25 cal/cm2)

HRC 4	Cotton Clothing under Multilayer FR Flash Suit Jacket and Pants Safety Glasses, Hard Hat, Flash Suit Hood, Hearing Protection, Leather Protectors or Gloves, Leather Work Shoes  (>25 to 40 cal/cm2)

PREPARED BY:	    		Date:

APPROVED BY:	    		Date:

ADDITIONAL APPROVALS FOR MANIPULATIVE ENERGIZED WORK

Approval of D/S Electrical Coordinator

Approval of Area Division/Section Head

(FESS Head Must Sign if FESS Electricians are Performing Manipulative Energized Work Under this Permit for Another D/S)

Approval of Fermilab Directorate

Job Briefing Signature Sheet

Person(s) Conducting Briefing:	   		Date:

Personnel Present at the Job Briefing will Sign Below, thereby Indicating their Understanding of the Scope of Work and Associated Hazard Mitigation Requirements.

Print Name	    Fermi ID #	    Div/Sec or Company	     Signature