| UNITED STATES ENVIRONMENTAL PROTECTION AGENCY REGION III 1650 Arch Street Philadelphia, Pennsylvania 19103-2029 |
| --- |
|  |  | DATE: May 1, 2006 |  |
| SUBJECT: | Approval of Amendments to Virginia’s Existing Regulation Provisions Concerning Maintenance, Nonattainment, and PSD Areas [EPA-R03-OAR-2005-0010] |  |  |
| FROM: | Ellen Wentworth |
| TO: | File |
| THRU: | Makeba Morris Branch Chief |

I.  Background

This technical support document (TSD) evaluates the August 15, 17, 19, September 28, and October 3, 2005 Commonwealth of Virginia, Department of Environmental Quality (VADEQ) revisions to the Commonwealth of Virginia State Implementation Plan (SIP). These revisions consist of amendments to existing regulations concerning maintenance, nonattainment, and prevention of significant deterioration (PSD) areas found in 9 VAC 5, Chapter 20 of Virginia’s regulations for the Control and Abatement of Air Pollution.

Listed below is a summary of each of the SIP revisions submitted by the Commonwealth of Virginia on those dates.

II.   Summary of SIP Revisions

A.  On August 15, 2005, the Commonwealth of Virginia submitted a revision to its SIP (Revision 097).  This revision consists of formatting changes to Virginia’s regulation, 9 VAC 5-20-203, Maintenance Areas; the removal of the Hampton Roads Area from the list of nonattainment areas found in 9 VAC 5-20-204, Nonattainment Areas; and the removal of the exemption of the Hampton Roads Area from the list of PSD areas found in 9 VAC 5-20-205.

The August 15, 2005 revision to 9 VAC 5-20-203, Maintenance Areas, eliminates the air quality maintenance area (AQMA) concept which was promulgated by the EPA in the 1970's and replaces it with the maintenance area concept consistent with the 1990 Clean Air Act Amendments (CAAA).  The revised format consists of geographically defined maintenance areas categorized by pollutants (ozone, carbon monoxide and other pollutants). This revision will not result in the backsliding of any control measures that have been submitted by the Commonwealth and approved by EPA into the Commonwealth of Virginia SIP. The AQMAs originated in a SIP submittal made by the Commonwealth on May 7, 1974 and approved by EPA in 40 CFR 52.2465 (c)(13).  The AQMAs for Virginia were codified as federal regulations in 40 CFR 52.2449 but that section was later repealed. The AQMAs were added to the state regulations effective August 9, 1975.  This was done to have the areas in the state regulations in case the Commonwealth did want to use them for SIP regulatory purposes at a later time. The AQMAs were, however, used in the open burning rule, but that rule was not submitted as a SIP revision until some time later. The only provisions of the open burning rule in the SIP are those necessary to implement the seasonal restrictions which originated to address nonattainment issues after the 1990 CAAA and the Commonwealth uses the VOC and NOx emissions control areas to implement those provisions.

The August 15, 2005 revision also reflects the redesignation of the Hampton Roads Area to attainment of the 1-hour ozone NAAQS, by deleting the area from the list of 1-hour ozone nonattainment areas found in 9 VAC 5-20-204.1(c) and adding it to the list of ozone maintenance areas found in 9 VAC 5-20-203.1. Additionally, the revision removes the exclusion of the Hampton Roads Area from the list of PSD areas found in 9 VAC 5-20-205.A.4(f).  Under section 107(d)(1) of the CAAA of 1990, EPA was required to designate the Hampton Roads Area as nonattainment because the area violated the 1-hour ozone standard during the years 1987-1989 (November 6, 1991, 56 FR 56694, as amended November 30, 1992, 57 FR 56762).  The Hampton Roads Area consists of the localities of James City County, York County, Chesapeake City, Hampton City, Newport News City, Norfolk City, Poquoson City, Portsmouth City, Suffolk City, Virginia Beach City, and Williamsburg City.  This area was able to achieve the 1-hour ozone standard and was redesignated a maintenance area on June 26, 1997 (62 FR 34408).

In addition, the August 15, 2005 revision adds the Northern Virginia Carbon Monoxide Area to the list of carbon monoxide maintenance areas found in 9 VAC 5-20-203.2 since this area was redesignated to attainment for the carbon monoxide NAAQS on January 30, 1996 (62 FR 2931).  The Metropolitan Washington DC-MD-VA Area (including the Northern Virginia Area) was a pre-1990 carbon monoxide nonattainment area. When the CAAA were passed in 1990, this area was classified as a moderate nonattainment area. The Metropolitan Washington DC-MD-VA Area attained the carbon monoxide standard in the 1990s and, in accordance with CAAA section 175(a), submitted a CO maintenance plan covering the period 1996-2007.  EPA approved the redesignation and maintenance plan for the Virginia portion on January 30, 1996 (61 FR 2931), effective March 15, 1996.  In accordance with section 175(b), the region was required to submit a second maintenance plan within eight years of its redesignation. This second maintenance plan provides for maintenance of the carbon monoxide standard through March 16, 2016.  EPA approved this second maintenance plan on April 4, 2005 (70 FR 16958), effective on June 3, 2005.  The revision also adds a subsection to 9 VAC 5-20-203.3, Maintenance Areas, to include all other pollutants.

It should be noted that this rulemaking action is not amending 9 VAC 5-20-204.1(a) of the August 15, 2005 submittal, since this submittal shows the Washington Area as a “serious” area, and EPA approved a change on August 9, 2004 (69 FR 48150) that designated the Northern Virginia Ozone Nonattainment Area as “severe.”  Nor did the August 15, 2005 submittal amend 9 VAC 5-20-206.1(a).  As a result, 9 VAC 5-20-204.1(a) should not be amended as part of this rulemaking action since at the time of the effective date of this SIP revision (January 1, 1998), the area was still classified as “serious.”

The August 15, 2005 SIP revision was adopted by the Virginia State Air Pollution Control Board on September 11, 1997, and became effective on January 1, 1998.

B.  On August 17, 2005, the Commonwealth of Virginia submitted a revision to its SIP (Revision R97).  This revision consists of amendments to Virginia’s regulations 9 VAC 5-20-203, Maintenance Areas, 9 VAC 5-20-204, Nonattainment Areas, and 9 VAC 5-20-205, PSD Areas.  The August 17 revision amends 9 VAC 5-20-203.1 Maintenance Areas, by adding the Richmond Area, to the list of ozone maintenance areas since this area was redesignated to attainment for the 1-hour ozone standard on November 17, 1997 ( 62 FR 61237). The Richmond Area was designated as nonattainment under the CAAA of 1990 under operation of law, and classified as a moderate 1-hour ozone nonattainment area (56 FR 56694).  The Richmond Area consists of a portion of Charles City County, Chesterfield County, Hanover County, Henrico County, Colonial Heights City, Hopewell City, and Richmond City. As a result of the Richmond Area being redesignated to attainment for the ozone NAAQS, the August 17, 2005 SIP revision also removes the Richmond Area from the list of ozone nonattainment areas found in 9 VAC 5-20-204.1(b), and removes the exclusion of the Richmond Area from the list of PSD areas found in 9 VAC 5-20-205 A.4(e).

It should be noted that this rulemaking action is not amending 9 VAC 5-20-204.1(a) of the August 17, 2005 submittal, since this subsection indicates the Washington Area as a “serious” area, and EPA approved a change on August 9, 2004 (69 FR 48150) that designated the Northern Virginia Ozone Nonattainment Area as “severe.”  Nor did the August 17, 2005 submittal amend 9 VAC 5-20-206.1(a).  As a result, 9 VAC 5-20-204.1(a) should not be amended as part of this rulemaking action since at the time of the effective date of this SIP revision (April 1, 1998), the area was still classified as “serious.”

The August 17, 2005 SIP revision was adopted by the State Air Pollution Control Board on January 8, 1998, and became effective on April 1, 1998.

C.  On August 19, 2005, the Commonwealth of Virginia submitted a revision to its SIP (Revision A98).  This revision consists of amendments to Virginia’s regulations 9 VAC 5-20-204, Nonattainment Areas, and 9 VAC 5-20-205, PSD Areas, and reflects the first repeal of the 1-hour ozone NAAQS. The August 19, 2005 revision amends 9 VAC 5-20-204.1(b), by removing the White Top Mountain Area from the areas regulated as ozone nonattainment areas, and amends 9 VAC 5-20-205.A.4(a) to remove the exemption of the White Top Mountain Area from the areas subject to regulation as a PSD area.

On November 6, 1991 (56 FR 56694), EPA designated the White Top Mountain, Virginia Area as nonattainment of the 1-hour ozone NAAQS and classified the area as a rural transport area (marginal).  The White Top Mountain Area is the portion of White Top Mountain above the 4,500 foot elevation in Smyth County.  In a July 18, 1997 (62 FR 38856) final rule, EPA promulgated a regulation that replaced the 1-hour ozone NAAQS with an 8-hour standard at a level of 0.08 parts per million (ppm).  The new standard became effective on September 16, 1997, and provided increased protection to the public, especially children and other at-risk populations.  On July 18, 1997, EPA announced that revocation of the 1-hour ozone NAAQS would be delayed until areas achieved attainment of the 1-hour NAAQS.  This was done in order to facilitate continuity in public health protection during the transition to the new NAAQS.  In a June 5, 1998 final rule  (63 FR 31014), EPA identified ozone areas where the 1-hour standard  was no longer applicable because these areas had not measured a current violation of the 1-hour standard.  For all other areas, the 1-hour standard continued to apply.  The June 5, 1998 final rule was promulgated to assist in the phasing-out of the 1-hour standard since the then newly promulgated 8-hour standard was in effect and was more protective of the public health than the 1-hour ozone standard.  All of Smyth County, Virginia including the White Top Mountain Area, was one of the areas where the 1-hour standard was no longer applicable (63 FR 31087, June 5, 1998). On January 1, 1999, Virginia amended 9 VAC 5-20-204.1(b) to remove the White Top Mountain area from the areas regulated as ozone nonattainment areas and amended 9 VAC 5-20-205.A.4 (a) to remove the exemption of the White Top Mountain area from the areas subject to regulations as a PSD area.  The August 19, 2005 SIP revision submittal reflects this change.

On May 14, 1999, the U.S. Court of Appeals for the District of Columbia remanded the 8-hour NAAQS for ozone and curtailed EPA’s authority to enforce it.  The May, 1999 court decision undermined the basis for EPA’s previous determinations on the applicability of the 1-hour ozone standard.  In that ruling, the court remanded the 8-hour NAAQS for ozone and curtailed EPA’s authority to enforce it.  The effectiveness of the 8-hour standard served as the underlying basis for EPA’s regulations governing the June, 1998 applicability determinations, and thus for EPA’s finding that the 1-hour standard no longer applied in areas that EPA determined were attaining the 1-hour standard.  As a result, on October 25, 1999 (64 FR 57424), EPA proposed the 1-hour ozone standard would be reinstated in areas where it had previously been revoked and the associated designations and classifications that previously applied in such areas with respect to the 1-hour NAAQS would also be reinstated.

On July 20, 2000 (65 FR 45182), EPA issued a final rule rescinding the prior findings in the June 1998 final rule that the 1-hour ozone NAAQS, and, the accompanying designations and classifications no longer applied in certain areas.  EPA reinstated the 1-hour ozone NAAQS because the public health protection afforded by the 8-hour ozone standard was being delayed due to continued litigation regarding the 8-hour ozone standard.  The 1-hour ozone NAAQS  again became applicable and the designations and classifications that previously applied in areas with respect the 1-hour standard were also reinstated.  The July 20, 2000 final rule reinstated the White Top Mountain Area as a rural transport (marginal) ozone nonattainment area under the 1-hour ozone NAAQS.  The effective date for the reinstatement of the 1-hour ozone NAAQS in the White Top Mountain Area was January 16, 2001.  See 65 FR 45182 at 45182 (effective date under “DATES” and 65 FR at 45190 (Table 1), July 20, 2000.

On April 30, 2004 (69 FR 23951), EPA published the first phase of its final rule to implement the 8-hour ozone NAAQS (Phase I Rule). 1 Also on April 30, 2004 (69 FR 23858), EPA published 8-hour ozone designations for all areas of the country.  For most areas, including the White Top Mountain Area, the designations under the 8-hour ozone NAAQS became effective on June 15, 2004.  The Phase I Rule provided that the 1-hour ozone NAAQS would no longer apply for an area one year following the effective date of the area’s designation for the 8-hour ozone NAAQS.  On August 3, 2005 (70 FR 44470), EPA issued a final rule that codified the revocation of the 1-hour standard for those areas with effective 8-hour ozone designations.  On June 15, 2005, all of Smyth County, Virginia was no longer subject to the 1-hour ozone NAAQS and was designated attainment of the 8-hour ozone NAAQS.

When Virginia amended 9 VAC 5-20-204.1(b) and 9 VAC 5-20-205.A.4(a) to remove the White Top Mountain Area from the areas regulated as ozone nonattainment areas, and added the White Top Mountain Area to the areas subject to regulation as PSD areas, the White Top Mountain Area was no longer subject to the 1-hour ozone NAAQS under EPA’s June 5, 1998 final rule (63 FR 31014) as discussed previously.  In addition, the White Top Mountain Area had not been designated nonattainment under the 8-hour ozone NAAQS.  However, between January 16, 2001, the applicable effective date for the July 20, 2000 final rule (65 FR 45182) reinstating the 1-hour ozone NAAQS, and June 15, 2005 when the 1-hour ozone NAAQS was revoked, the White Top Mountain Area was subject to the 1-hour ozone NAAQS.  During this period, EPA would not have been able to approve the August 19, 2005 revision (Rev. A98) of 9 VAC 5-20-204.1(b) and 9 VAC 5-20-205.A.4(a) into the Virginia SIP because such a revision would have had the effect of removing the applicability of Virginia’s nonattainment NSR program in the White Top Mountain Area which was once again a 1-hour nonattainment area.  Now that the 1-hour standard has been revoked and the White Top Mountain Area is designated attainment for all NAAQS, the only permitting program Virginia must have under Title I of the CAA is the PSD program.  Therefore, EPA can now approve these changes to 9 VAC 5-20-204.1(b) and 9 VAC 5-20-205.A.4(a) for the White Top Mountain Area that were submitted on August 19, 2005 into the Virginia SIP.

It should be noted that this rulemaking action is not amending 9 VAC 5-20-204.1(a) of the August 19, 2005 submittal, since the submittal indicates the Washington Area as a “serious” area, and EPA approved a change on August 9, 2004 (69 FR 48150) that designated the Northern Virginia Ozone Nonattainment Area as “severe.”  Nor did the August 19, 2005 submittal amend 9 VAC 5-20-206.1(a).  As a result, 9 VAC 5-20-204.1(a) should not be amended as part of this rulemaking action since at the time of the effective date of this SIP revision (January 1, 1999), the area was still classified as “serious.”

The August 19, 2005 SIP revision was adopted on September 17, 1998, and became effective on January 1, 1999.

D.  On September 28, 2005, the Commonwealth of Virginia submitted a revision to its SIP (Revision B04).  The revision consists of amendments to Virginia’s regulations 9 VAC 5-20- 204, Nonattainment Areas, and 9 VAC 5-20-205, PSD Areas.  The September 28, 2005 SIP revision amends Virginia’s SIP by reformatting 9 VAC 5-20-204, Nonattainment Areas, to include subsections A. and B.  Subsection A.1.includes an updated list of 1-hr ozone nonattainment areas.  Subsection A.2.contains a list of areas designated under the new 8-hour ozone NAAQS.  Subsection B. reflects the revocation of the 1-hour standard for all areas listed in 9 VAC 5-20-204 A.1. (Ozone -1 hour, June 15, 2004, effective June 15, 2005).  As of the effective date of this submittal, August 25, 2004, the ozone nonattainment designations read as follows:  For 9 VAC 5-20-204.A.1. (1-hr ozone):  the Northern Virginia area (severe); for 9 VAC 5-20-204.A.2 (8-hr ozone):  the Fredericksburg area, including Stafford County (moderate); the Northern Virginia area (moderate); the Hampton Roads area (marginal); the Richmond area (moderate); the Shenandoah National Park area (basic).  The revision also amends the list of PSD areas in 9 VAC 5-20-205.A by deleting the list of specific localities and making the list generic, by stating that all areas are subject that are not designated as nonattainment.  It should be noted that since the September 28, 2005 SIP revision submittal, EPA has redesignated the Fredericksburg (December 23, 2005, 70 FR 76165), and Shenandoah National Park (January 3, 2006, 71 FR 24) ozone nonattainment areas as attainment for the 8-hour ozone standard.

The September 28, 2005 submittal also amends 9 VAC 5-20-205.B., by removing mercury, beryllium, asbestos, and vinyl chloride from the list of pollutants for which all areas of the state are geographically defined as PSD areas.  The 1990 Amendments to the CAA at section 112(b)(6) exempted hazardous air pollutants (HAPs) listed under section 112(b)(1) from the PSD requirements in part C of the CAA.  These HAPs include:  arsenic, asbestos, benzene, beryllium, mercury, radionuclides, and vinyl chloride, all of which were previously regulated under the PSD rules.  Virgina has consequently removed these pollutants from 9 VAC 5-20-205.B to conform to the 1990 CAA amendments.

This revision was adopted on June 29, 2004, and became effective on August 25, 2004.

On April 30, 2004, EPA amended 40 CFR Part 81 by adding a list of areas that were nonattainment for the 8-hour ozone NAAQS.  The new ozone nonattainment areas became effective on June 15, 2004.  In addition to providing the basis for broadbased nonregulatory plans for attainment and maintenance of the standards, the nonattainment area designations and classifications are also part of the legally enforceable means by which the state implements the new source review (NSR) program for nonattainment areas.  On April 30, 2004, EPA promulgated a final rule to implement Phase I of the 8-hour ozone standard.  40 CFR 50.9 has been revised to indicate that the 1-hour standard is no longer effective one year after the effective date of the rule, which means that the 8-hour standard replaces the 1-hour standard on June 15, 2005.

The September 28 revision adds a provision to 9 VAC 5-20-204.B. which removes the severe area program in the Northern Virginia Ozone Nonattainment area under the 1-hour standard.  The Virginia portion of the Ozone Transport Region (OTR) is the same area in Virginia that constituted the Northern Virginia Ozone Nonattainment area under the 1-hour standard.  Because the severe area program imposed more stringent requirments than required under section 184 in that area, Virginia did not need to have a separate NSR program meeting the section 184 requirements.  As a result, on January 6, 2006 (71 FR 890), EPA published a proposed rulemaking implementing the NSR program required under section 184 of the CAA in Virginia’s portion of the (OTR).  No comments were received on this proposed rulemaking and EPA is in the process of issuing a final rulemaking on this proposed action.  Therefore, not withstanding the nonattainment designations in 9 VAC 5-20-204, the Virginia portion of the OTR (Arlington County, Fairfax County, Loudoun County, Prince William County, Stafford County, Alexandria City, Fairfax City, Falls Church City, Manassas City, and Manassas Park City) will be subject to OTR NSR contingent upon EPA issuing a final action approving the January 6, 2006 (71 FR 890) rulemaking.

E.  On October 3, 2005, the Commonwealth of Virginia submitted a revision to its SIP. (Revision N04).  This revision reflects the reclassification of the Richmond 8-hour Ozone Nonattainment Area found in 9 VAC 5-20-204.2, Nonattainment Areas, from “moderate” to “marginal.”  EPA’s final rulemaking reclassifying the Richmond Area from an 8-hour “moderate” ozone nonattainment area, to a “marginal” 8-hour ozone nonattainment area, was published on September 22, 2004 (69 FR 56697), and became effective on November 22, 2004.

The Richmond Area was designated nonattainment by operation of law under the CAAA of 1990, and classified as a “moderate” 1-hour ozone nonattainment area (56 FR 56694).  The Richmond Area consists of a portion of Charles City County, Chesterfield County, Hanover County, Henrico County, Prince George County, Colonial Heights City, Hopewell City, Petersburg City, and Richmond City.  The area was able to achieve the 1-hour ozone NAAQS and was redesignated attainment on November 17, 1997 (62 FR 61237), effective December 17, 1997.

On July 18, 1997, EPA promulgated a revised ozone standard of 0.08 parts per million (ppm), measured over an 8-hour period, i.e., the 8-hour standard (62 FR 38856).  The 8-hour rule was challenged by numerous litigants, but in March 2002, the D.C. Circuit rejected all remaining challenges to the 8-hour standard.  The process for designations following promulgation of a NAAQS is contained in section 107(d)(1) of the CAA.  The final rule establishing designations for all areas of the country was signed by the EPA Administrator on April 15, 2004 and published in the Federal Register on April 30, 2004 (69 FR 23858).  The rule also sets forth the classifications for certain ozone nonattainment areas.  The EPA designated the Richmond Area as “moderate” for the 8-hour ozone NAAQS based upon its design value of 94 parts per billion (ppb).

Under section 181(a)(4), an ozone nonattainment area may be reclassified if the design value of the area is 5 percent greater or 5 percent less than the level on which such a classification was based.  The provisions of section 181(a)(4) set out general criteria and grant the Administrator broad discretion in making or determining to make a reclassification.  The EPA described these criteria in the April 30, 2004 (69 FR 23858) final rule.  The April 30, 2004 action invited states to submit the reclassification requests within 30 days of the effective date of the designations and classifications which was June 15, 2004, which meant that reclassification requests were to be submitted by July 2004.  On July 12, 2004, the Virginia Department of Environmental Quality submitted a request to reclassify the Richmond Area from a “moderate” to “marginal” 8-hour ozone nonattainment area.

In summary, the following factors supported the request for reclassification of the Richmond Area to “marginal”:  the design value 94 ppb meets EPA’s criteria to qualify for consideration of a bump down, local and regional modeling together with declining emissions from local, regional and national regulations support the conclusion that the Richmond Area is likely to attain by 2007.  Thus the request met the criteria EPA established and did not violate any of the criteria.  Therefore EPA approved the reclassification request to bump down the Richmond Area from a “moderate” 8-hour ozone nonattainment area, to a “marginal” 8-hour ozone nonattainment area on September 22, 2004 (69 FR 56697), effective November 22, 2004.

III. Conclusion and Recommended Agency Action

EPA has reviewed the August 15, 17, 19, September 28, and October 3, 2005 SIP revisions and has determined that these revisions strengthen the Commonwealth’s SIP and support protection of the NAAQS.  Therefore, approval of these SIP revisions is recommended.

# Footnotes

1The Phase I rule was amended on May 26, 2005 (70 FR 30592).  This amendment addressed two issues raised in a petition for reconsideration of the Phase I Rule and clarified two aspects of that implementation rule.  On July 8, 2005 (70 FR 39413), another final rule addressed other issues raised in a petition for reconsideration of the April 30, 2004, Phase 1 Rule.