TABLE OF CONTENTS

# Executive Summary											1

Summary of Storm Event										1

Recurrence Interval Analysis										2

# TABLES

Table 1 – Flow Recurrence Intervals for October 7 – 10, 2005						3

Table 2 – Flow Recurrence Intervals for October 14 – 15, 2005						4

Table 3 – Hourly Precipitation October 7 – 15, 2005							5

# FIGURES

# Figure 1 – Friday/Saturday and Storm Total Rainfall	 						9

# Figure 2 -  Connecticut Dams Which Breached or Partially Breached					10

# Figure 3 -  Map of Flood Recurrence Intervals for October 8 – 15, 2005					11

APPENDIX

Hydrographs of rivers monitored by the USGS in Connecticut.

# EXECUTIVE SUMMARY

During the week of October 7 – 15, 2005 the State of Connecticut was struck by two very heavy rainfall events.  Combined, the rainfall from these two events totaled 9 – 16 inches across the state.  This rainfall resulted in major flooding of several sub-regional river basins in Hartford and Tolland Counties on October 14 – 15, 2005.   Widespread moderate flooding occurred across the rest of the Connecticut.  This has already been the wettest October on record since 1905 as measured at Bradley International Airport in Windsor Locks, Connecticut.

A total of 10 dams breached, were partially breached or were damaged mainly in Hartford and Tolland Counties.  Several bridges failed and several dozen roads were washed out or undermined.  Many homes suffered flooded basements, and evacuations were conducted in some towns due to severe flooding of urban areas and small streams.   In addition the Natural Resources Conservation Service reported that they were investigating four potential Emergency Watershed Protection Projects.

Since the major flooding of June, 1982 the State of Connecticut has undertaken several measures which have greatly improved the State’s ability to respond to this flooding event.  The installation of an Automated Flood Warning system in 1986, and it’s subsequent expansions in 1992, 1996, and 1998  proved invaluable during this flooding event.  Recent projects that also provided critical information during the storm include the creation of an electronic inventory of high hazard dams in Connecticut and Critical Facilities Mapping.   The sharing of river stage and rainfall data between Connecticut agencies, the National Weather Service and the United States Geological Survey greatly enhanced the effectiveness of the state and local flood response effort.

Since 1988 Connecticut has suffered from three major disasters requiring presidential disaster declarations.  The receipt of federal funds has brought with it a commitment by the State to mitigate the effects of these disasters.   The State completed Hazard Mitigation Plans in 1990, 1993 and 1999 as a result of these disasters.  In 2004, Connecticut received approval from the Federal Emergency Management Agency for the most recent update of our State Natural Hazard Mitigation Plan as per the requirements of the Disaster Mitigation Act of 2000.  This makes Connecticut potentially eligible for hazard mitigation funding equal to 7.5% of the total public assistance damages after a Presidentially declared natural disaster.

SUMMARY OF THE STORM EVENT

On October 7th, 2005, a low pressure system (the remnants of Hurricane Tammy) moved slowly up the eastern seaboard along a stalled frontal boundary.  A wide band of heavy rainfall developed along the U.S. East Coast stretching from South Carolina to Northern New England.  Heavy rainfall associated with the remnants of Tammy and a surface low that formed south of Tammy moved into Connecticut at 7:00 PM on Friday evening on October 7th.  Rainfall continued heavy at times for the next 36 hours and ended on Sunday morning around 3:00 AM.  Rainfall totals during the first part of this storm ranged from 4 inches in Southeastern Connecticut up to 12 inches in the Northwest Hills.   Flooding from this first rainfall event was minor across most areas with flood frequencies of less than 5-years in most areas.  Flooding was minor during the October 7 – 9 event due to very dry antecedent soil and river conditions prior to the storm.  However, this first event set the stage for the second event leaving saturated soils and river basins at ½ to ¾ bank full conditions.

Light to moderate rainfall continued across Connecticut during the next 4 days keeping soils saturated and river channels running at ½ to ¾ bank full.   On Friday October 14th, a surface low pressure system formed suddenly along a frontal boundary south of Long Island and moved Northeastward into Southern New England.   A wide area of very heavy rainfall developed Friday evening and overspread all of Southern New England.   Rain began falling at a rate of nearly an inch an hour at 9:00 PM in Western Connecticut.  This heavy rainfall continued for 2 – 3 hours over Western Connecticut resulting in 2 – 4 inches of rainfall.  As the area of heavy rain moved East it intensified and rainfall rates exceeded one

inch per hour in Central and Northeastern Connecticut late Friday night and into the early hours of Saturday morning.  Rainfall totals in Central and Northeastern Connecticut ranged from 6 – 8 inches during a 7-hour period Friday night from approximately 10:00 PM to 5:00 AM Saturday morning.  This extremely heavy rainfall combined with the total saturation of soils resulted in a very rare (100-year) flooding event in North Central and Northeastern Connecticut.

RECURRENCE INTERVAL ANALYSIS1

First Event October 7 – 10, 2005

Rainfall recurrence intervals1 were much greater than recurrence intervals for flows during the first event due to the abnormally dry conditions prior to the event.  Approximately 5 inches of rainfall was absorbed by the abnormally dry soils during the first event.  The average recurrence intervals for rainfall ranged from 10 – 100 years in western Connecticut, however the resulting flows only averaged between 2 – 10 years.    In central and eastern Connecticut rainfall recurrence intervals ranged from 1 – 5 years with flow recurrence intervals generally below the 2 year storm.  No dam failures were reported and a significant slope failure occurred in Montville, Connecticut at the Montville Commons construction site.

Second Event October 14 – 15, 2005

In the second event, the recurrence intervals for flow (see map on page 11) were generally very close to the recurrence intervals for rainfall (only seen in saturated soils).   No significant soil absorption occurred and all of the heavy rainfall immediately ran off into brooks and streams.  The average recurrence intervals for rainfall in Hartford, Tolland and Windham Counties met or exceeded the 100-year storm in most locations.  Rainfall recurrence intervals ranged from 2 – 50 years across the rest of the state.  The resulting stream flows in Hartford and Tolland counties ranged from 10 – 100+ years on several sub-regional drainage basins.  Recurrence intervals generally ranged from 5 – 20 years on the remaining rivers in Connecticut.

1 Recurrence intervals for rainfall were calculated using National Weather Service Technical Paper #40 (1963) rainfall

distribution curves for Connecticut.   Recurrence intervals for flows were determined by the United States Geological Survey

office in East Hartford, Connecticut.

Table 1 - Flow Recurrence Intervals1 for October 7 – 10, 2005

| Station Number | Station Name | Flow (CFS) | Recurrence Interval Comments |
| --- | --- | --- | --- |
| 01118300 | PENDLETON HILL BROOK NEAR CLARKS FALLS, CT. | NA | Equipment Failure |
| 01119040 | POQUONOCK RIVER NEAR GROTON, CT. | NA | Not Available |
| 01119500 | WILLIMANTIC RIVER NEAR COVENTRY, CT. | 1160 | <2-year |
| 01121000 | MOUNT HOPE RIVER NEAR WARRENVILLE, CT. | 463 | <2-year |
| 01122000 | NATCHAUG RIVER AT WILLIMANTIC, CT. | Controlled | Flood Control |
| 01122500 | SHETUCKET RIVER NEAR WILLIMANTIC, CT. | Controlled | Flood Control |
| 01123000 | LITTLE RIVER NEAR HANOVER, CT. | 130 | <2-year |
| 01124000 | QUINEBAUG RIVER AT QUINEBAUG, CT. | Controlled | Flood Control |
| 01125500 | QUINEBAUG RIVER AT PUTNAM, CT | Controlled | Flood Control |
| 01127000 | QUINEBAUG RIVER AT JEWETT CITY, CT. | Controlled | Flood Control |
| 01127500 | YANTIC RIVER AT YANTIC, CT. | 251 | <2-year |
| 01172010 | CONNECTICUT R AT HOLYOKE | NA | Not Available |
| 01184000 | CONNECTICUT RIVER AT THOMPSONVILLE, CT. | 114,000 | <5-year |
| 01184100 | STONY BROOK NEAR WEST SUFFIELD, CT. | 393 | ≈2-year |
| 01184490 | BROAD BROOK AT BROAD BROOK, CT. | 226 | <2-year |
| 01186000 | WEST BRANCH FARMINGTON RIVER AT RIVERTON, CT | Controlled | Flood Control |
| 01186500 | STILL RIVER AT ROBERTSVILLE, CT. | Controlled | Flood Control |
| 01188000 | BURLINGTON BROOK NEAR BURLINGTON, CT. | 403 | ≈5-year |
| 01188090 | FARMINGTON RIVER AT UNIONVILLE, CT. | Controlled | Flood Control |
| 01189995 | FARMINGTON RIVER AT TARIFFVILLE, CT. | Controlled | Flood Control |
| 01190070 | CONNECTICUT RIVER AT HARTFORD, CT. | Tidal | Stage 20.9 Feet |
| 01192500 | HOCKANUM RIVER NEAR EAST HARTFORD, CT. | 1330 | ≈2-year |
| 01192883 | COGINCHAUG RIVER AT MIDDLEFIELD, CT | 320 | <2-year |
| 01193000 | CONNECTICUT RIVER AT MIDDLETOWN, CT. | Tidal | Stage 11.9 Feet |
| 01193500 | SALMON RIVER NEAR EAST HAMPTON, CT. | 729 | <2-year |
| 01194500 | EAST BRANCH EIGHTMILE RIVER NEAR NORTH LYME, CT. | 66 | Not Ranked |
| 01194796 | CONNECTICUT RIVER AT OLD LYME, CT | NA | Not Available |
| 01195100 | INDIAN RIVER NEAR CLINTON, CT. | 50 | <2-year |
| 01195490 | QUINNIPIAC RIVER AT SOUTHINGTON, CT. | 506 | <2-year |
| 01196500 | QUINNIPIAC RIVER AT WALLINGFORD, CT. | 2260 | 2-year |
| 01199000 | HOUSATONIC RIVER AT FALLS VILLAGE, CT. | 10300 | 10-year |
| 01199050 | SALMON CREEK AT LIME ROCK, CT. | 2020 | ≥10-year |
| 01200000 | TENMILE RIVER NEAR GAYLORDSVILLE, CT | 4610 | 5-year |
| 01200500 | HOUSATONIC RIVER AT GAYLORDSVILLE, CT. | 11100 | =2-year |
| 01201487 | STILL RIVER AT ROUTE 7 AT BROOKFIELD CENTER, CT. | 1290 | =2-year |
| 01202501 | SHEPAUG RIVER AT PETERS DAM AT WOODVILLE, CT | NA | Not Available |
| 01203600 | NONEWAUG RIVER AT MINORTOWN, CT. | 1220 | <2-year |
| 01203805 | WEEKEEPEEMEE RIVER AT HOTCHKISSVILLE, CT | NA | Not Available |
| 01204000 | POMPERAUG RIVER AT SOUTHBURY, CT. | 1810 | <2-year |
| 01205500 | HOUSATONIC RIVER AT STEVENSON, CT. | 29500 | ≈5-year |
| 01206900 | NAUGATUCK RIVER AT THOMASTON, CT. | NA | Not Available |
| 01208500 | NAUGATUCK RIVER AT BEACON FALLS, CT. | 7820 | Flood Control |
| 01208950 | SASCO BROOK NEAR SOUTHPORT, CT. | 228 | ≤2-year |
| 01208990 | SAUGATUCK RIVER NEAR REDDING, CT. | 266 | <2-year |
| 01209761 | FIVEMILE RIVER NEAR NEW CANAAN, CT. | 30 | No Statistics |
| 01209901 | RIPPOWAM RIVER AT STAMFORD, CT. | 910 | No Statistics |

Table 2 - Flow Recurrence Intervals for October 14 – 5, 2005

| Station Number | Station Name | Flow (CFS) | Recurrence Interval Comments |
| --- | --- | --- | --- |
| 01118300 | PENDLETON HILL BROOK NEAR CLARKS FALLS, CT. | 290 | 20-year |
| 01119040 | POQUONOCK RIVER NEAR GROTON, CT. | Tidal | Not Available |
| 01119500 | WILLIMANTIC RIVER NEAR COVENTRY, CT. | 12,300 | 100-year |
| 01121000 | MOUNT HOPE RIVER NEAR WARRENVILLE, CT. | 5,120 | +100-year |
| 01122000 | NATCHAUG RIVER AT WILLIMANTIC, CT. | Controlled | Flood Control |
| 01122500 | SHETUCKET RIVER NEAR WILLIMANTIC, CT. | Controlled | Flood Control |
| 01123000 | LITTLE RIVER NEAR HANOVER, CT. | 1,080 | 5-year |
| 01124000 | QUINEBAUG RIVER AT QUINEBAUG, CT. | Controlled | Flood Control |
| 01125500 | QUINEBAUG RIVER AT PUTNAM, CT | Controlled | Flood Control |
| 01127000 | QUINEBAUG RIVER AT JEWETT CITY, CT. | Controlled | Flood Control |
| 01127500 | YANTIC RIVER AT YANTIC, CT. | 2,920 | 5-year |
| 01172010 | CONNECTICUT R AT HOLYOKE | NA | Not Available |
| 01184000 | CONNECTICUT RIVER AT THOMPSONVILLE, CT. | 114,000 | 2-year (On 10/10/2005) |
| 01184100 | STONY BROOK NEAR WEST SUFFIELD, CT. | 1,700 | 40-year |
| 01184490 | BROAD BROOK AT BROAD BROOK, CT. | NA | +100-year (Gauge Destroyed) |
| 01186000 | WEST BRANCH FARMINGTON RIVER AT RIVERTON, CT | Controlled | Flood Control |
| 01186500 | STILL RIVER AT ROBERTSVILLE, CT. | Controlled | Flood Control |
| 01188000 | BURLINGTON BROOK NEAR BURLINGTON, CT. | 1,810 | +100-year |
| 01188090 | FARMINGTON RIVER AT UNIONVILLE, CT. | 1,620 | Flood Control |
| 01189995 | FARMINGTON RIVER AT TARIFFVILLE, CT. | 10,400 | Minor Flood Control |
| 01190070 | CONNECTICUT RIVER AT HARTFORD, CT. | Tidal | Stage 20.7 Feet |
| 01192500 | HOCKANUM RIVER NEAR EAST HARTFORD, CT. | 3,140 | 25-year |
| 01192883 | COGINCHAUG RIVER AT MIDDLEFIELD, CT | 1,640 | 10-year |
| 01193000 | CONNECTICUT RIVER AT MIDDLETOWN, CT. | Tidal | Stage 12.2 Feet |
| 01193500 | SALMON RIVER NEAR EAST HAMPTON, CT. | 5,170 | 5-10-year |
| 01194500 | EAST BRANCH EIGHTMILE RIVER NEAR NORTH LYME, CT. | 639 | 2-year |
| 01194796 | CONNECTICUT RIVER AT OLD LYME, CT | Tidal | Not Available |
| 01195100 | INDIAN RIVER NEAR CLINTON, CT. | 329 | 5-year |
| 01195490 | QUINNIPIAC RIVER AT SOUTHINGTON, CT. | 837 | 20-year |
| 01196500 | QUINNIPIAC RIVER AT WALLINGFORD, CT. | 3,940 | 10-year |
| 01199000 | HOUSATONIC RIVER AT FALLS VILLAGE, CT. | 10300 | 10-year (On 10/10/2005) |
| 01199050 | SALMON CREEK AT LIME ROCK, CT. | 2020 | 20-year (On 10/10/2005) |
| 01200000 | TENMILE RIVER NEAR GAYLORDSVILLE, CT | 7,380 | 10-20-year |
| 01200500 | HOUSATONIC RIVER AT GAYLORDSVILLE, CT. | 20,700 | Not Determined |
| 01201487 | STILL RIVER AT ROUTE 7 AT BROOKFIELD CENTER, CT. | 1,820 | Not Determined |
| 01202501 | SHEPAUG RIVER AT PETERS DAM AT WOODVILLE, CT | NA | Not Available |
| 01203600 | NONEWAUG RIVER AT MINORTOWN, CT. | 3,250 | 10-year |
| 01203805 | WEEKEEPEEMEE RIVER AT HOTCHKISSVILLE, CT | 3,300 | 10-year |
| 01204000 | POMPERAUG RIVER AT SOUTHBURY, CT. | 4,490 | 5-year |
| 01205500 | HOUSATONIC RIVER AT STEVENSON, CT. | 40,900 | 5-year |
| 01206900 | NAUGATUCK RIVER AT THOMASTON, CT. | NA | Flood Control |
| 01208500 | NAUGATUCK RIVER AT BEACON FALLS, CT. | NA | Flood Control |
| 01208950 | SASCO BROOK NEAR SOUTHPORT, CT. | 252 | 2-year |
| 01208990 | SAUGATUCK RIVER NEAR REDDING, CT. | 487 | <2-year |
| 01209761 | FIVEMILE RIVER NEAR NEW CANAAN, CT. | NA | No Statistics |
| 01209901 | RIPPOWAM RIVER AT STAMFORD, CT. | 903 | No Statistics |

| TABLE 3 - STORM OF OCTOBER 7 - 15, 2005 Page 1 of 4 |  |
| --- | --- |
|  |  |  |  |  |  |  | HOURLY PRECIPITATION |  |  |  |  |  |  |  |
| DATE |  | A.M. HOUR ENDING |  |  | P.M. HOUR ENDING |  |  |
|  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | TOTALS |
|  |  | SHARON WS DEVICE #705 - CONNECTICUT ALERT SYSTEM - 41:49:38 N 73:25:12 W ELEVATION 1160 FEET |  |
|  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  | .04 | .04 | .08 | .08 | .08 | .08 | 0.44 |
|  | 8 | .08 | .08 | .20 | .08 | .20 | .24 | .20 | .43 | .43 | .31 | .08 | .20 | .55 | .28 | .20 | .31 | .47 | .39 | .31 | .35 | .63 | .71 | .75 | .75 | 8.23 |
|  | 9 | .31 | .04 | .16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.51 |
|  | 10 |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.04 |
|  | 11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.00 |
|  | 12 |  | .04 |  | .04 | .04 | .08 |  | .04 |  |  | .04 | .12 | .12 | .20 | .04 | .16 | .04 |  | .04 |  |  |  |  |  | 1.00 |
|  | 13 |  | .08 |  | .12 | .08 | .04 |  | .04 | .08 | .04 | .04 | .04 | .04 | .04 |  |  |  |  |  |  |  |  | .08 |  | 0.72 |
|  | 14 | .08 |  |  |  |  |  |  |  |  |  |  | .04 | .04 | .16 | .31 | .24 | .35 | .24 | .08 | .35 | .87 | .79 | .20 | .08 | 3.83 |
|  | 15 | .04 |  |  | .04 | .04 | .04 |  | .04 |  |  |  |  |  |  |  | .08 |  |  |  |  |  |  |  |  | 0.28 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 15.05 |
|  | RIDGEFIELD PRECIP. DEVICE #575 - CONNECTICUT ALERT SYSTEM - 41:17:30 N 73:29:30 W ELEVATION 580 FEET |  |
|  | 7 |  |  |  |  |  |  |  | .04 |  |  |  |  | .16 | .12 |  |  |  |  | .08 | .08 |  | .04 | .04 | .04 | 0.60 |
|  | 8 | .04 | .04 | .08 | .20 | .08 | .24 | .20 | .28 | .51 | .16 | .04 | .24 | .12 | .08 | .16 | .51 | .24 | .39 | .28 | .28 | .35 | .51 | .47 | .35 | 5.85 |
|  | 9 | .24 | .08 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.32 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  | .04 |  | 0.08 |
|  | 11 |  |  | .08 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.08 |
|  | 12 |  | .16 | .20 | .20 | .31 | .20 | .24 | .20 | .20 | .08 | .16 | .31 | .28 | .28 | .08 | .16 | .16 |  |  | .08 | .04 | .04 | .08 |  | 3.46 |
|  | 13 | .08 | .04 |  |  | .12 | .12 | .20 | .20 | .20 | .16 | .16 | .16 | .04 | .04 |  |  |  |  |  |  |  | .04 | .04 | .24 | 1.84 |
|  | 14 | .12 | .20 | .16 | .04 | .04 | .08 | .08 |  |  |  | .08 |  | .16 | .12 |  | .20 | .12 | .24 | .24 | .28 | .24 | .24 | .16 | .12 | 2.92 |
|  | 15 |  |  |  |  | .04 | .04 | .04 | .04 | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.20 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 15.35 |
|  | WILTON PRECIP. DEVICE #570 - CONNECTICUT ALERT SYSTEM - 41:13:45 N 73:03:30 W ELEVATION 500 FEET |  |
|  | 7 |  |  |  |  |  |  | .04 |  |  |  |  |  | .04 |  |  |  |  |  | .16 | .04 |  | .04 | .04 | .04 | 0.40 |
|  | 8 |  | .08 | .04 | .16 | .04 | .08 | .08 | .20 | .51 | .08 | .08 | .24 | .08 | .08 | .08 | .51 | .28 | .39 | .16 | .16 | .28 | .75 | .67 | .35 | 5.38 |
|  | 9 | .16 | .12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.28 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  | .08 |  |  |  |  |  |  |  | 0.12 |
|  | 11 |  | .04 | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.08 |
|  | 12 | .04 | .20 | .16 | .20 | .20 | .12 | .24 | .16 | .20 | .08 | .08 | .28 | .20 | .16 | .16 | .04 | .12 |  |  | .08 |  | .08 |  |  | 2.80 |
|  | 13 | .08 |  | .04 |  | .04 | .12 | .16 | .12 | .08 | .24 | .16 | .12 |  |  |  |  |  |  |  |  | .04 |  |  | .24 | 1.44 |
|  | 14 | .16 | .16 | .04 |  |  | .31 | .08 | .08 | .04 |  |  | .08 | .12 | .08 |  | .08 | .16 | .20 | .08 | .20 | .20 | .12 | .12 | .08 | 2.39 |
|  | 15 |  |  |  |  | .04 |  | .04 |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.12 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 13.01 |
|  | FACTORY POND PRECIP. DEVICE #565 - CONNECTICUT ALERT SYSTEM - 41:15:30 N 73:26:00 W ELEVATION 329 FEET |  |
|  | 7 |  |  |  |  |  |  | .04 |  |  |  |  |  | .04 |  |  |  |  |  | .12 |  | .04 | .08 | .08 | .04 | 0.44 |
|  | 8 |  | .04 | .12 | .08 | .16 | .08 | .12 | .28 | .59 | .24 | .08 | .20 | .12 | .12 | .16 | .51 | .28 | .31 | .16 | .28 | .20 | .79 | .47 | .39 | 5.78 |
|  | 9 | .16 | .12 |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.32 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  | 0.04 |
|  | 11 |  | .04 | .08 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.12 |
|  | 12 | .04 | .12 | .12 | .24 | .35 | .08 | .24 | .16 | .16 | .04 | .20 | .20 | .20 | .12 | .12 | .16 | .08 |  |  |  |  | .12 | .04 |  | 2.79 |
|  | 13 | .08 | .04 |  |  | .08 | .16 | .20 | .12 | .12 | .24 | .16 |  |  |  |  |  |  |  |  |  | .20 |  |  | .08 | 1.48 |
|  | 14 | .16 | .20 | .08 | .12 |  | .16 | .04 | .16 |  |  |  |  | .20 | .04 | .08 | .08 | .20 | .08 | .16 | .20 | .24 | .04 | .24 | .08 | 2.56 |
|  | 15 |  |  |  |  | .04 |  | .04 |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  | 0.16 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 13.69 |

| TABLE 3 - STORM OF OCTOBER 7 - 15, 2005 Page 2 of 4 |  |
| --- | --- |
|  |  |  |  |  |  |  | HOURLY PRECIPITATION |  |  |  |  |  |  |  |
| DATE |  | A.M. HOUR ENDING |  |  | P.M. HOUR ENDING |  |  |
|  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | TOTALS |
|  | SILVERMINE PRECIP. DEVICE #555 - CONNECTICUT ALERT SYSTEM - 41:08:00 N 73:26:15 W ELEVATION 580 FEET |  |
|  | 7 |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  | .08 | .04 |  | .12 | .04 |  | 0.32 |
|  | 8 | .04 | .20 | .12 | .24 |  | .16 | .04 | .16 | .12 | .20 |  | .16 | .12 |  | .04 | .28 | .20 | .20 | .08 | .08 | .12 | .47 | .87 | .35 | 4.25 |
|  | 9 | .28 | .08 |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.40 |
|  | 10 |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.04 |
|  | 11 | .04 | .08 | .12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.24 |
|  | 12 | .16 | .12 | .20 | .16 | .31 | .16 | .28 | .35 | .20 | .08 | .20 | .24 | .24 |  | .20 | .04 | .20 | .04 |  | .04 |  |  | .04 |  | 3.26 |
|  | 13 |  |  |  |  | .08 | .12 | .08 |  | .16 | .12 | .16 | .08 |  | .08 |  |  |  |  |  |  |  | .04 |  | .04 | 0.96 |
|  | 14 | .20 | .20 | .16 |  | .04 | .16 | .20 | .04 | .04 |  |  | .12 | .12 | .04 | .08 | .12 | .12 | .04 | .12 | .20 | .12 | .12 | .20 |  | 2.44 |
|  | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.00 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 11.91 |
|  | ORANGE PRECIP. DEVICE #3280 - REGIONAL WATER AUTHORITY - 41:18:12 N 73:01:50 W ELEVATION 183 FEET |  |
|  | 7 |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .28 | .04 | 0.36 |
|  | 8 |  |  | .35 | .12 | .12 | .16 | .08 | .04 | .24 | .28 |  | .08 | .08 | .08 | .12 | .08 | .12 | .39 | .20 | .16 | .16 | .35 | .67 | .59 | 4.47 |
|  | 9 | .55 | .20 | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.79 |
|  | 10 | .04 |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  | .16 |  |  |  |  | .08 | .16 | .12 | 0.60 |
|  | 11 | .47 | .20 | .08 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 | 0.79 |
|  | 12 | .08 | .12 | .28 | .12 | .08 | .00 | .08 | .16 | .20 | .20 | .20 | .20 | .20 | .12 | .24 | .08 | .04 | .04 |  |  |  |  | .12 | .04 | 2.60 |
|  | 13 | .12 | .16 | .24 | .12 | .16 | .31 | .16 | .12 | .16 | .20 | .16 |  | .04 |  |  | .04 | .04 |  |  | .04 |  |  |  | .04 | 2.11 |
|  | 14 | .20 | .20 | .12 | .08 | .04 | .12 | .12 | .12 | .04 |  |  |  | .04 | .08 | .04 | .12 | .04 | .12 | .16 | .12 | .24 | .12 | .24 | .20 | 2.56 |
|  | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.00 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 14.28 |
|  | WHITNEY PRECIP. DEVICE #3190 - REGIONAL WATER AUTHORITY - 41:20:14 N 72:54:38 W ELEVATION 360 FEET |  |
|  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .35 | 0.35 |
|  | 8 |  |  | .04 | .16 | .16 | .04 | .12 | .04 | .28 | .20 | .04 | .04 | .08 | .04 | .08 | .12 | .08 | .28 | .16 | .12 | .12 | .28 | .55 | .71 | 3.74 |
|  | 9 | .35 | .35 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.70 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  | .04 | .04 | .04 |  | 0.16 |
|  | 11 | .08 | .28 | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .08 | 0.48 |
|  | 12 | .12 | .16 | .08 | .16 | .04 | .04 |  | .08 | .04 | .04 | .12 | .28 | .04 | .12 | .20 | .04 | .04 | .04 |  |  |  | .04 | .04 | .08 | 1.80 |
|  | 13 | .16 | .24 | .16 | .08 | .16 | .20 | .04 | .08 | .16 | .08 | .08 | .04 |  |  |  | .04 |  |  | .08 |  | .04 |  |  | .04 | 1.68 |
|  | 14 | .12 | .20 | .08 | .12 | .08 | .12 | .08 | .08 | .08 |  |  |  | .04 | .08 | .08 | .08 | .12 | .20 | .12 | .16 | .12 | .31 | .16 | .47 | 2.90 |
|  | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  | .08 | 0.12 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 11.93 |
|  | MERIDEN PRECIP. DEVICE #545 - CONNECTICUT ALERT SYSTEM - 41:23:05 N 72:45:05 W ELEVATION 460 FEET |  |
|  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .35 | 0.35 |
|  | 8 |  |  | .04 | .08 | .12 |  | .08 | .08 | .16 | .43 | .04 |  | .12 | .04 | .08 | .04 | .08 | .12 | .16 | .20 | .08 | .28 | .31 | 1.18 | 3.72 |
|  | 9 | .83 | .63 | .04 | .04 |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.58 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  |  | .04 | .04 |  |  | .12 |  |  | .04 |  | .04 | .16 | .16 | 0.60 |
|  | 11 | .08 | .35 | .24 |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  | .04 |  |  |  |  |  |  | 0.75 |
|  | 12 | .08 | .12 | .08 | .04 |  | .04 |  |  | .04 |  | .16 | .20 | .12 | .04 |  | .08 |  | .08 | .04 | .20 |  |  |  | .08 | 1.40 |
|  | 13 | .20 | .08 | .24 | .20 | .16 | .12 | .08 | .08 | .04 | .08 | .04 | .08 | .08 |  |  |  |  | .08 |  |  | .08 | .04 |  | .04 | 1.72 |
|  | 14 | .20 | .16 | .12 |  | .04 | .08 | .20 | .16 | .12 | .20 | .04 |  |  | .08 | .08 |  | .16 | .20 | .20 | .24 | .28 | .51 | .31 | .39 | 3.77 |
|  | 15 | .75 | .08 |  |  |  |  | .08 | .08 | .04 | .04 |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  | 1.11 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 15.00 |

| TABLE 3 - STORM OF OCTOBER 7 - 15, 2005 Page 3 of 4 |  |
| --- | --- |
|  |  |  |  |  |  |  | HOURLY PRECIPITATION |  |  |  |  |  |  |  |
| DATE |  | A.M. HOUR ENDING |  |  | P.M. HOUR ENDING |  |  |
|  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | TOTALS |
|  | PLAINVILLE PRECIP. DEVICE #755 - CONNECTICUT ALERT SYSTEM - 41:40:00 N 72:51:21 W ELEVATION 180 FEET |  |
|  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 | .04 |  | .08 | .04 | 0.20 |
|  | 8 | .16 |  | .20 | .08 | .20 | .12 | .12 | .08 | .04 | .12 | .04 |  | .16 | .04 | .04 | .04 | .04 | .12 | .20 | .16 | .20 | .16 | .43 | .94 | 3.69 |
|  | 9 | .75 | .28 | .28 | .08 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.39 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  | .04 |  |  |  | .04 | .08 | 0.20 |
|  | 11 |  | .04 | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  | 0.12 |
|  | 12 | .04 |  |  | .04 | .08 | .12 | .04 | .04 | .04 | .08 | .04 | .12 | .16 | .08 |  |  |  | .04 |  |  | .08 | .08 | .04 |  | 1.12 |
|  | 13 |  |  |  |  | .04 | .04 | .04 |  | .04 |  | .04 | .04 | .04 | .08 |  |  | .12 | .16 | .20 | .16 | .16 | .12 | .08 | .12 | 1.48 |
|  | 14 | .08 | .04 | .04 | .04 |  | .12 | .16 | .16 | .04 | .08 | .04 | .04 |  | .04 | .08 | .12 | .20 | .20 | .24 | .20 | .55 | .43 | .47 | .51 | 3.88 |
|  | 15 | .55 | .08 |  |  |  | .04 | .08 |  | .04 |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  | 0.83 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 12.91 |
|  | GAILLARD PRECIP. DEVICE #3130 - REGIONAL WATER AUTHORITY - 41:20:14 N 72:46:16 W ELEVATION 203 FEET |  |
|  | 7 |  | .04 |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 | .20 | .16 | 0.48 |
|  | 8 |  |  | .04 | .12 | .16 | .04 | .12 | .04 | .16 | .16 |  | .08 | .08 | .04 | .08 | .08 | .04 | .20 | .16 | .20 | .12 | .35 | .55 | .75 | 3.57 |
|  | 9 | .20 | .12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.32 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 | .12 | .04 |  |  |  | .04 |  |  |  | 0.24 |
|  | 11 |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .08 | .04 |  | .12 | 0.28 |
|  | 12 | .08 | .16 | .12 | .04 |  |  |  | .04 |  |  | .04 | .35 |  |  | .08 | .04 | .04 | .08 |  | .04 |  | .04 | .04 | .08 | 1.27 |
|  | 13 | .24 | .12 | .20 | .08 | .16 | .16 | .08 | .04 | .16 | .08 | .08 |  |  |  |  |  | .04 | .04 | .08 |  |  |  | .04 |  | 1.60 |
|  | 14 | .16 | .20 | .12 | .04 | .12 | .08 | .08 | .12 | .08 |  |  | .04 | .04 | .04 |  | .04 | .04 | .24 | .20 | .16 | .12 | .16 | .12 | .24 | 2.44 |
|  | 15 | .28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.28 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 10.48 |
|  | MENUNGATUCK PRECIP. DEVICE #3110 - REGIONAL WATER AUTHORITY - 41:22:40 N 72:42:48 W ELEVATION 253 FEET |  |
|  | 7 | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.04 |
|  | 8 | .08 | .04 |  |  | .04 | .08 | .12 | .08 | .08 | .04 | .08 | .04 | .04 | .08 | .91 | .08 | .04 | .24 | .16 | .28 | .16 | .20 | .35 | 1.10 | 4.32 |
|  | 9 | .24 | .20 | .12 | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.60 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  | .04 |  | .04 |  | .04 | .04 |  | .04 | 0.24 |
|  | 11 |  | .04 |  |  | .04 |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  | .04 |  |  | .08 | 0.24 |
|  | 12 | .16 | .20 | .20 | .12 |  |  | .04 |  |  |  |  | .39 | .04 |  |  | .04 |  | .20 | .04 | .04 |  | .04 | .04 | .12 | 1.67 |
|  | 13 | .16 | .31 | .24 | .16 | .16 | .12 | .12 | .04 | .08 | .08 | .04 | .08 |  |  |  |  | .04 | .04 | .04 | .08 | .08 |  |  | .08 | 1.95 |
|  | 14 | .08 | .20 | .28 | .08 | .08 | .12 | .12 | .08 | .08 | .12 |  | .04 |  | .04 |  | .04 | .04 | .24 | .28 | .28 | .24 | .31 | .35 | .31 | 3.41 |
|  | 15 | .63 | .59 |  |  |  |  |  | .04 | .04 |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  | 1.34 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 13.81 |
|  | HAMMONASSETT PRECIP. DEVICE #3100 - CONNECTICUT ALERT SYSTEM - 41:22:30 N 72:37:10 W ELEVATION 273 FEET |  |
|  | 7 |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  | .04 | .08 | 0.16 |
|  | 8 |  | .04 |  | .16 | .16 | .08 | .08 | .04 | .16 | .20 | .08 |  | .12 | .04 | .08 | .12 | .04 | .16 | .24 | .28 | .08 | .16 | .79 | .94 | 4.05 |
|  | 9 | .28 | .12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.40 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  | .08 |  |  |  |  | .04 | 0.16 |
|  | 11 |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  | .04 |  | .04 | .20 | 0.32 |
|  | 12 | .08 | .20 | .08 | .04 |  |  |  |  |  | .04 |  | .16 |  |  |  |  | .04 | .12 |  | .08 |  |  | .04 | .12 | 1.00 |
|  | 13 | .20 | .12 | .16 | .12 | .12 | .04 |  | .08 | .08 | .04 | .04 | .04 |  |  |  |  |  | .08 | .12 | .04 |  |  | .04 |  | 1.32 |
|  | 14 | .16 | .16 | .08 | .08 | .04 | .04 | .12 | .04 | .12 | .04 |  |  | .04 |  |  | .04 | .16 | .24 | .20 | .12 | .12 | .24 | .24 | .20 | 2.48 |
|  | 15 | .71 | .55 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  | 1.30 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 11.19 |

| TABLE 3 - STORM OF OCTOBER 7 - 15, 2005 Page 4 of 4 |  |
| --- | --- |
|  |  |  |  |  |  |  | HOURLY PRECIPITATION |  |  |  |  |  |  |  |
| DATE |  | A.M. HOUR ENDING |  |  | P.M. HOUR ENDING |  |  |
|  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | TOTALS |
|  | STAFFORD WS DEVICE #790 - CONNECTICUT ALERT SYSTEM - 41:58:35 N 72:23:11 W ELEVATION 880 FEET |  |
|  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0.00 |
|  | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  | .04 |  | .04 | 0.12 |
|  | 9 |  | .04 | .04 | .04 | .08 | .04 | .08 | .08 | .08 | .08 | .08 | .08 | .12 | .08 | .12 | .08 | .12 | .08 | .12 | .08 | .08 | .08 | .08 | .04 | 1.80 |
|  | 10 | .08 | .04 | .08 |  | .08 | .08 | .04 | .04 | .04 | .04 | .04 | .04 | .04 |  | .04 | .04 |  | .04 |  | .04 |  | .04 |  | .04 | 0.88 |
|  | 11 |  | .04 |  | .04 |  | .04 | .04 |  | .04 |  | .04 | .04 |  | .04 | .04 |  |  | .04 |  |  | .04 |  | .04 |  | 0.48 |
|  | 12 | .04 |  | .04 |  | .04 |  |  | .04 |  | .04 |  |  | .04 |  |  |  |  | .04 |  |  |  |  | .04 |  | 0.32 |
|  | 13 |  |  |  | .04 |  |  |  | .04 |  |  | .04 | .04 |  | .04 | .04 |  | .04 | .04 | .04 |  | .04 |  | .04 |  | 0.44 |
|  | 14 | .04 | .04 | .04 | .04 | .04 | .04 | .04 | .08 | .04 | .04 | .08 | .04 | .08 | .08 | .04 | .08 | .08 | .08 | .12 | .08 | .16 | .16 | .16 | .20 | 1.88 |
|  | 15 | .20 | .20 | .28 | .31 | .31 | .31 | .28 | .31 | .28 | .28 | .24 | .28 | .24 | .24 | .20 | .20 | .20 | .16 | .16 | .12 | .12 | .12 | .12 | .08 | 5.24 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 11.16 |
|  | PACHAUG WS DEVICE #850 - CONNECTICUT ALERT SYSTEM - LAT. LONG NEEDED W ELEVATION NEEDED FEET |  |
|  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .04 | 0.04 |
|  | 8 | .16 |  |  | .04 | .08 | .04 |  |  | .04 |  | .12 | .04 |  |  | .04 |  | .04 |  |  |  |  |  | .04 | .28 | 0.92 |
|  | 9 | .87 | .43 | .35 | .08 | .04 | .04 |  |  |  |  |  |  | .04 |  | .04 |  |  |  |  |  |  |  |  |  | 1.89 |
|  | 10 |  |  |  |  |  |  |  |  |  | .04 |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  | 0.08 |
|  | 11 |  |  |  |  |  |  | .04 |  |  | .04 |  | .04 |  |  |  |  |  |  |  |  |  | .12 | .08 | .04 | 0.36 |
|  | 12 |  | .04 | .04 |  |  |  |  |  |  |  |  |  | .04 |  |  |  | .04 |  |  |  |  |  |  | .04 | 0.20 |
|  | 13 | .04 | .08 | .08 | .08 | .12 | .20 | .12 |  | .04 | .04 | .04 |  |  |  |  |  |  |  |  | .04 |  |  | .04 |  | 0.92 |
|  | 14 | .04 | .12 | .20 | .12 | .08 | .04 | .08 |  | .04 | .08 | .16 | .08 |  |  |  |  | .04 | .08 | .28 | .20 | .12 | .16 | .35 | .24 | 2.51 |
|  | 15 | .28 | .71 | .75 | .71 | .31 | .20 |  | .04 |  | .04 | .08 | .16 |  |  |  |  |  |  |  |  |  |  |  |  | 3.28 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 10.20 |
|  | DEEP RIVER RES. PRECIP. DEVICE #805 - CONNECTICUT ALERT SYSTEM - 41:33:33 N 72:14:25 W ELEVATION 310 FEET |  |
|  | 7 |  |  | .04 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | .08 | 0.12 |
|  | 8 | .24 |  |  | .04 | .20 | .12 | .04 | .12 | .04 | .08 | .16 | .04 | .04 | .04 |  | .08 | .04 |  | .08 | .08 | .04 |  | .12 | .71 | 2.31 |
|  | 9 | .71 | .35 | .12 | .04 | .04 |  |  |  |  |  |  |  |  | .04 |  |  |  |  |  |  |  |  |  |  | 1.30 |
|  | 10 |  |  |  |  |  |  |  |  |  |  |  | .04 | .04 | .04 |  |  | .04 |  |  |  | .04 |  |  |  | 0.20 |
|  | 11 |  |  |  |  |  |  | .04 |  | .04 |  |  |  |  |  |  |  |  |  |  |  | .04 | .04 | .04 | .12 | 0.32 |
|  | 12 | .04 | .12 | .04 | .04 |  |  |  |  |  |  | .08 |  | .04 |  |  |  |  |  |  |  |  |  |  | .08 | 0.44 |
|  | 13 | .12 | .12 | .12 | .16 | .04 | .08 | .20 |  |  | .04 | .12 |  | .04 |  |  |  |  |  |  | .08 | .04 |  |  | .16 | 1.32 |
|  | 14 | .24 | .12 | .12 | .12 | .16 | .04 | .04 | .04 | .16 | .12 | .08 | .04 |  |  |  | .04 | .04 | .20 | .31 | .08 | .28 | .28 | .47 | .35 | 3.33 |
|  | 15 | .39 | .79 | .71 | .08 |  |  |  | .04 | .04 |  |  | .08 | .04 |  |  |  |  |  |  |  |  |  |  |  | 2.17 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | STORM TOTAL | 11.51 |

APPENDIX A – USGS HYDROGRAPHS OF STATE RIVERS

# Text boxes

Jane Stahl

Deputy

Commissioner

Yvonne Bolton

Bureau Chief

Water Management

Bureau

Denise Ruzicka

Director

Inland Water Resources Division

Arthur Christian

State Hazard Mitigation Officer

Douglas Glowacki

Environmental

Analyst III

Author:

Douglas Glowacki

State Of Connecticut

Department Of Environmental

## Protection

Gina McCarthy, Commissioner							      October,  2005

### Bureau of Water Management

Reviewed Draft

### Heavy Rains & Flooding of Sub-Regional Drainage Basins

##### October 7 – 15, 2005

###### Inland Water Resources Division

Water Management Bureau

79 Elm Street, Hartford, Connecticut 06106			              Phone: 860-424-3706

( Silvermine 2.44” F/S

11.91” ST

( South Cheshire 4.37” F/S

16.49” ST

Thomaston 4.18” F/S

13.43” ST (

D

( Sharon 4.11” F/S

15.05” ST

( New Haven 2.36” F/S

12.05” ST

D

5

10

10

Gina McCarthy

Commissioner

DATA SOURCES

(  DEP Alert System Gauge

( NWS Co-op Observers

(  NWS Automated Stations

10

25

+

100

+

100

5

Staffordville

Reservoir #3

P

Windsorville Dam

Somersville

Pond Dam

B

D

DAM NAME			OWNERSHIP	LOCATION

Somerville Pond Dam	DEP 			Somers

Windsorville Dam		Private		East Windsor

Mile Creek Dam		Private		Old Lyme

Staffordville Reservoir #3	CT Water Co.		Union

Hanover Pond Dam		City			Meriden

ABB Pond Dam		Private		Bloomfield

Springborn Dam		DEP 			Enfield

Cains Pond			Private		Suffield

Schwartz Pond Dam		Private		Suffield

Sessions Meadow Dam	DEP			Union

P

(

Stafford 7.12” F/S

11.16 ST

Pomfret 6.04” F/S

13.90 ST (

( Farmington 4.29” F/S

11.61” ST

(  Wethersfield 5.26” F/S

13.22” ST

( Glastonbury 6.71” F/S

13.27” ST

Burlington 7.74” F/S (

15.61” ST

( Groton 5.55” F/S

9.33” ST

Enfield 7.50” F/S (

15.90” ST

(  South Windsor 8.40” F/S

15.90” ST

Gauge Washed Out

Plainfield 5.35” F/S

10.47” ST (

( Plainville 4.71” F/S

12.91” ST

State Police 4.88” F/S

(  15.00” ST

Menungatuck 4.75” F/S

13.81” ST

(

( Lake Gaillard 2.72” F/S

10.48” ST

North Cheshire 4.20” F/S (

14.29” ST

Whitney 3.02” F/S

11.93” ST (

Orange 2.56” F/S

14.28” ST (

( Factory Pond 2.72” F/S

13.69” ST

( Wilton 2.51” F/S

13.01” ST

( Ridgefield 2.94” F/S

15.35” ST

( Bridgeport 1.34” F/S

9.73” ST

( Danbury 2.40” F/S

12.87” ST

( Meriden 2.80” F/S

13.27” ST

( Hartford 4.33” F/S

10.51” ST

( Windsor Locks 5.90” F/S

13.12” ST

FIGURE 1 - FRIDAY/SATURDAY (F/S) 10/14 – 15 & STORM TOTAL (ST) RAINFALL FOR WEEK OF OCTOBER 7 - 15

( Staffordville 6.85” F/S

16.20 ST

( Mansfield 3.90” F/S

9.88” ST

Pachaug 5.79” F/S (

10.20” ST

Deep River Res. 5.50” F/S

11.51” ST (

( Hammonassett 3.78” F/S

11.19” ST

Gina McCarthy,

Commissioner

ABB Pond Dam

D

Sessions

Meadow Dam

FULLY BREACHED

PARTIALLY BREACHED

DAMAGED

Schwartz Pond

Dam

P

Hanover Pond Dam

P

B

P

Cains Pond

Dam

B

Springborn Dam

D

FIGURE 2 - CONNECTICUT DAMS WHICH BREACHED OR PARTIALLY BREACHED

+

100

100

Pendleton Hill Brook

20

Five Mile River

<2

Saugatuck River

2

Sasco Brook

Stevenson Dam

Weekeepeemee

River

Pomperaug

River

5

Nonewaug

River

5

Ten Mile River

10

20

20

Salmon

Creek

10

10

20

Indian River

5

Eight Mile   River

2

Salmon  River

10

Coginchaug

River

Burlington

Brook

Broad Brook

Voluntown 9.80” ST (

16

14

12

10

8

6

4

2

0

R

I

V

E

R

S

T

A

G

E

I

N

F

E

E

T

Quinnipiac River Crested in Southington at 6.76 FT at 6:45 AM, September 17th

Quinnipiac River Crested in Wallingford at 9.43 FT at 5:03 PM, September 17th

( Brookfield 12.79” ST

(  White Plains 12.68” ST

AREA OF VERY HEAVY RAINFALL

WILLIMANTIC RIVER

AT COVENTRY

MOUNT HOPE  RIVER

NEAR WARRENVILLE

R

A

I

N

F

A

L

L

I

N

C

H

E

S

/

2

H

O

U

R

S

HYDROGRAPHS FOR WILLIMANTIC AND MOUNT HOPE RIVERS

###### October 7th – 17th, 2005

AREA OF VERY HEAVY RAINFALL

2.00

1.75

1.50

1.25

1.00

0.75

0.50

0.25

0.00

New Canaan 11.45” ST

(

Rainfall readings from Staffordville Co-op Observer

Corrected to hourly readings using Pachaug and Plainville gauges.

##### 7                       8                      9                     10                    11                    12                    13                    14                    15                    16                     17

1Recurrence and stream flow data provided by the United States Geological Survey in East Hartford, Connecticut.  This is provisional data.

GAUGE OPENING PARTIALLY OBSTRUCTED

1Recurrence and stream flow data provided by the United States Geological Survey in East Hartford, Connecticut.  This is provisional data.

Stony Brook

2

Mile Creek Dam

40

Yantic

River

5

Little River

Mount Hope

River

Willimantic

River

MINOR FLOODING

2 – 10 Year Recurrence Interval

MODERATE FLOODING

Greater than 10-Year Recurrence Interval

SIGNIFICANT FLOODING

Greater than 50-Year Recurrence Interval

MAJOR FLOODING

Greater than 100-year Recurrence Interval

50

10

5

100

Gina McCarthy,

Commissioner

FIGURE 3 - FLOOD RECURRENCE INTERVALS FOR OCTOBER 8 – 15, 2005

Gaylordsville

Housatonic River

Connecticut River

Still River

Quinnipiac River

Falls  Village

Hokanum

River

Quinnipiac River Crested in Southington at 6.76 FT at 6:45 AM, September 17th

Quinnipiac River Crested in Wallingford at 9.43 FT at 5:03 PM, September 17th

THURSDAY

SEPTEMBER 16, 1999

FRIDAY

SEPTEMBER 17, 1999

SATURDAY

SEPTEMBER 18, 1999

QUINNIPIAC RIVER

AT SOUTHINGTON

QUINNIPIAC RIVER

AT WALLINGFORD

R

A

I

N

F

A

L

L

I

N

C

H

E

S

/

H

O

U

R

HYDROGRAPH FOR THE QUINNIPIAC RIVER

###### September 15 – 18, 1999

WEDNESDAY

SEPTEMBER 15, 1999

2.4

2.0

1.6

1.2

0.8

0.4

0.0

Flood Stage at Wallingford = 7.0 FT