09SQ170361A

STATEMENT OF WORK

The Bureau of Reclamation, Grand Coulee Power Office, Grand Coulee WA, has two shooting ranges that are approximately two years old that need to be cleaned.  This is the second cleaning for both of the shooting ranges.  There are collection buckets for the lead bullets that need to be emptied and wiped down of any lead dust as well as Back-stop/Bullet traps and the pop-up targets that require wipe down for any lead dust that may have accumulated.

BACK-STOP/BULLET TRAP CLEANING:

The large back-stop/bullet trap is approximately 70 feet x 24 feet.  There are 12 targets positions.  This area includes approximately 350 square feet of concrete and wood that will also have to be cleaned of any lead particles.  This large back-stop/bullet trap contains 54 buckets to catch the spent lead bullets.  Each of these buckets will need to be emptied and cleaned and any immediate surface area inside and out shall be wiped down as well.  No water is to be used; this cleaning is to be performed with straight solution only.

The small back-stop/bullet trap is approximately 35 feet by 16 feet.  There are 6 target positions.  This area includes approximately 175 square feet of concrete and wood that will also have to be cleaned of any lead particles.  This small back-stop/bullet trap contains 24 buckets to catch the spent lead bullets.  Each of these buckets will need to be emptied and cleaned and any immediate surface area inside and out shall be wiped down as well.  No water is to be used; this cleaning is to be performed with straight solution only.

DISPOSAL:

The actual disposal of any hazardous by-product from this procurement will be the responsibility of the Government.  All spent lead bullets are to be collected in Contractor-supplied 16-gallon drums.  Any and all additional contaminated materials not listed above, including, but not limited to: rags used in the cleaning, Personnel Protective Equipment worn by the Contractors employees, are to be disposed of in Government-owned 55-gallon drums.  Full drums shall be staged in front of the work area for easy disposal by the Government.

SUPPLIES:

The Government shall provide to the Contractor the 55-gallon drums for disposal of all items except the lead bullets. The Government shall also supply the Super Big Tex, an encapsulating chemical needed for the clean up.

The Contractor shall supply and include in their pricing all Personnel Protective Equipment, HEPA vacuum, 12-gallon drums, and rags.  If it is determined by the Contractor that more than one day is going to be required for this procurement, any and all travel and per diem costs are to be included in the price quoted.

PERSONNEL REQUIREMENTS:

Personnel Protective Equipment shall consist of disposable full-body coveralls and head and foot covers (“Tyvek”, or approved), steel toed safety boots, eye, hearing, hard hats, and applicable respiratory protection should be available and provided by the Contractor.

Contractor is to ensure personnel and subcontractors that are on site are trained in accordance with 29 CFR Parts 1926 and 1910, and WAC 296-62, as they apply.

LEAD TESTING:

29 Code of Federal Regulation (CFR) Part 1910, Occupational Safety and Health Standards, Revision dated July 1, 2006:

  - Surface areas shall be considered clean and “lead free” when wiped using wet methods, visibly clean, and wipe samples are less than 500 micrograms per square foot.  This testing will be accomplished by the Government.  It will have to be coordinated with the Project Safety Office 24 hours in advance.  The coordination will be accomplished through the Contracting Officer’s Representative (COR).

The COR shall conduct the lead wipe testing as specified.

REQUIRED DOCUMENTATION:

The following documents shall be submitted with proposals:

- 40 Hour HAZWOPER Certification

- Quality Assurance Surveillance Plan

- Contractor’s Licenses – All business licenses will be required before award.

- Insurance Certificates – Proof of insurance will also be required before award.

- A minimum of three references with current phone numbers from customers for whom your firm has provided Lead clean up jobs for.

- Develop and submit to COR specifications addressing components requiring compliance with lead-related regulations (WAC 296-155), and references to other specification sections by June 27, 2008.  It will be highly recommended that an Industrial Hygienist prove the method of cleaning is satisfactory for the protection to employees. Or show a past history, with a minimum of three years of past practice similar to the task at hand, to prove the method chosen will suffice Federal, State, and Local Regulations for lead cleaning and employee protection.

- Develop and submit to COR clearance levels in accordance with 29 CFR parts 1926.1101 and 1910.1001, and WAC 296-62 as they may apply.

Ensure that Washington State and Federal regulations are enforced, and that technical issues are properly addressed.

Contractor shall not begin work until submittals are complete, reviewed, and accepted by the Government.  Allow a 24 hour review period.

WORKDAYS AND HOURS:

The Contractor’s work hours will be limited to a schedule approved by the COR, but not less than 40 hours per week.  The Contractor will only be allowed on-site when an authorized Government Representative (such as the Government inspector) is available due to security precautions.

PREWORK MEETING:

A pre-work/safety meeting shall be held the Project Administration Building after award of the Contract and prior to the beginning of the work, at a time mutually agreeable to the Contractor and the COR.  The purpose will be to review the contract, work, and safety issues to be performed. The Bureau will explain the Lockout/Tagout procedures (if any) at that time.

In addition, the Contractor will be required to submit to the COR the following listed items:

- The list of all employees who will be working on the Contract

- Complete work schedules

- List of types and quantity of equipment to be used

- Certification of employees

- Submit a local emergency phone number at which the Contractor or on-site foreman can be reached on a twenty-four hour basis during the course of the work.

SITE VISIT:

A site visit will be held on February 26, 2009 at 9:00 AM PDT, prior to proposal submission.  Fax Stephen Clements at 509-633-9175 with your name, address, phone number, fax number, Dun & Bradstreet number and Federal Tax ID Number if you plan to attend the site visit.  Identification will be required in order to be admitted to the project.  This will be in the form of a valid driver’s license, military ID, or other State Identification.

QUESTIONS:

All questions regarding this solicitation must be in writing, and faxed to Stephen Clements at (509) 633-9175, or e-mailed to sclements@pn.usbr.gov  no later than 03/02/2009.

.