# UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

# WASHINGTON, DC 20460

OFFICE OF  PREVENTION, PESTICIDES,  AND TOXIC SUBSTANCES

Memorandum								Feb.14, 2008

Subject:	 Product Chemistry Science Chapter for Creosote (P1/P13 and P2 Fractions) Reregistration Eligibility Decision (RED) Process

From:		A. Najm Shamim, PhD, Chemist

Regulatory Management Branch II

Antimicrobials Division (7510P)

To:		Tim McMahon, PhD, Senior Toxicologist, and Risk Assessor

For Creosote RED

Antimicrobials Division (7510P)

And

Jackie McFarlane, CRM for Creosote RED

Regulatory Management Branch I

Antimicrobials Division (7510P)

Thru:		Mark Hartman, Chief

Regulatory Management Branch II

Antimicrobials Division (7510P)

DP Barcode:

Product Chemistry Science Chapter on

Creosote

Introduction:

The product chemistry science chapter for Creosote is unique and different from other Pesticides that Agency presents here. Since very little product  physical/chemical data on creosote ( PI/P13 and P2 fractions of coal tar creosote), Agency has used the data submitted by the registrants and has used the open literature data available.

Heavy Duty Wood Preservative Creosote is a heterogeneous mixture of polycyclic aromatic hydrocarbons and other heteronuclear aromatic substances. US EPA ‘s document Guidance for the Reregistration of Pesticide Products Containing CoalTar/Creosote

( Document 540-RS-88-066)1 recognizes  that  “hundreds of individual chemicals have been  identified in coal tar/creosote and Lorenz & Gjovik2 and McNeil3 have identified eight classes of compounds commonly found in creosote and coal tar products.” These  are listed as follows:

1.	Non-substituted six-membered rings

2.	Heterocyclic nitrogen bases

3.	Heterocyclic oxygen and sulfur compounds

4.	Alkyl substituted compounds( including polycyclic rings)

5.	Hydroxy compounds

6.	Aromatic amines

7.	Paraffins

8.	Naphthenes

Creosote as a pesticide used for wood preservation has no manufacturing source.  This Science Chapter deals with the Creosote mixture solution derived from tar which is produced from carbonization of bituminous coal. This is a coal tar fractional distillation process and from this  two fractions namely P1/P13 and P2 are obtained. In general fractions are collected when the temperatures are between 210 o C and 355 o C.4

Creosote Council, which represents the Creosote Industry,  submitted the product chemistry data for the P2 and P1/P13 creosote fractions in 1992 and resubmitted the data again in 1999  in compliance to the EPA’s Reregistration Standard and Data-Call-In issued for pesticide products containing coal tar creosote. In the absence of EPA methodology to determine the physical/chemical characteristics of mixtures like creosote fractions, the Industry has supplied the data based on the analysis performed by using the methods described by the American Wood Preservers Association (AWPA) Standard Method for Analysis of Creosote and Oil-Type Preservatives, specifically to analyze the creosote P2 and P1/P13 fractions for determination of xylene insolubles, determination of specific gravity, distillation fractions and determination of water content in the respective fractions.

AWPA has stated that the P1/P13  and P2 (creosote)fractions for use as heavy duty wood preservatives ‘shall be  a pure coal tar product, derived entirely from tar produced by carbonization of bituminous coal.  Carbonization of coal is accomplished by distlling coal and coal tar fraction is collected. The coal tar fraction itself consists of: light oil, middle oil and heavy (oil) anthracene. It is the middle oil fraction that is further distilled and various fractions from this distillation are collected  between the temperatures of 210 o and 355 o C.

Open literature search shows ( James Mueller et. al )5 soil contaminated with coal tar creosote consists of: 85% polycyclic aromatic hydrocarbons (PAHs), 10% phenolic compounds and 5% N-, S-, and O- heterocyclics. Table 1 lists some Polycyclic aromatic  hydrocarbons found in the P2 and P1/P13 fractions of creosote and have been reported by the Creosote Council in its product chemistry data submissions. Table 2 lists the  phenolic compounds and Table 3 lists the heterocyclic compounds 5 . These components of Tables 1,2 and 3  represent 95% of the total constituents in coal tar creosote. It must be pointed out that among the PAHs listed in Table 1, sixteen are on the EPA’s List of Priority Pollutants.

Table 1

Polycyclic Aromatic Hydrocarbons ( PAHs) in Coal Tar Creosote

| Compound | Relative Percentage | Molecular Weight |
| --- | --- | --- |
| Naphthalene | 13 | 128.2 |
| 2-Methylnaphthalene | 13 | 142.2 |
| Phenanthrene | 13 | 178.2 |
| Anthracene | 13 | 178.2 |
| 1-Methylnaphthalene | 8 | 142.2 |
| Biphenyl | 8 | 154.2 |
| Fluorene | 8 | 166.2 |
| 2,3-Dimethyl naphthalene | 4 | 156.2 |
| 2,6-Dimethyl naphthalene | 4 | 156.2 |
| Acenaphthene | 4 | 154.2 |
| Fluoranthene | 4 | 202.3 |
| Chrysene | 2 | 228.2 |
| Pyrene | 2 | 202.3 |
| Antraquinone | 1 | 208.2 |
| 2-Methyl anthracene | 1 | 192.3 |
| 2,3-Benzo[b]fluorene | 1 | 216.3 |
| Benzo[a]pyrene | 1 | 252.3 |

Table 2

Phenolic Constituents in Coal Tar Creosote

| Compound | Relative Percentage | Molecular Wt. |
| --- | --- | --- |
| Phenol | 20 | 94.1 |
| o-Cresol | 10 | 108.1 |
| m-Cresol | 10 | 108.1 |
| p-Cresol | 10 | 108.1 |
| Pentachlorophenol | 10 | 266.4 |
| 2,5-Xylenol | 7.5 | 122.2 |
| 3,5-Xylenol | 7.5 | 122.2 |
| 2,3-Xylenol | 5 | 122.2 |
| 2,4-Xylenol | 5 | 122.2 |
| 2,6-Xylenol | 5 | 122.2 |
| 3,4-Xylenol | 5 | 122.2 |
| 2,3,5-Trimethylphenol | 5 | 136.0 |

Table 3

Heterocyclics in Coal Tar Creosote

| Compound | Relative Percentage | Molecular Wt. |
| --- | --- | --- |
| Heterocyclics & N-Containing Aromatics: |  |  |
| Quinoline | 10 | 129.2 |
| Isoquinoline | 10 | 129.2 |
| Carbazole | 10 | 167.2 |
| 2,4-Dimethylpyridine | 10 | 107.2 |
| Acridine | 5 | 179.2 |
| Aniline | 5 | 93.1 |
| 2-Methyl quinoline | 5 | 143.2 |
| 4-Methyl quinoline | 5 | 143.2 |
| Pyrrole | 5 | 67.1 |
| Pyrrolidine | 5 | 71.2 |
| S-Heterocyclics: |  |  |
| Benzo[b]thiophene | 10 | 134.2 |
| Dibenzothiophene | 10 | 184.3 |
| O-Heterocyclics: |  |  |
| Dibenzofuran | 10 | 168.2 |

Table 4

Analytical Results of Creosote P2 and P1/P13 Fractions

| Molecular ion (M+) | Compound | CAS # | P2 fraction% (mean) | P1/P13 fraction % (mean) |
| --- | --- | --- | --- | --- |
| 117 | Indole | 120-72-9 | 0.20 |  |
|  | Indene |  | 0.5 | NC |
| 128 | Naphthalene | 91-20-3 | 17.3 | 6.2 |
| 129 | Quinoline | 91-22-5 | 0.50 | 1.0 |
| 134 | Benzo[c]thiophene |  | 0.40 | NC |
| 142 | 1-Methylnaphthalene | 90-12-0 | 1.3 | 2.5 |
| 142 | 2-Methylnaphthalene | 91-57-6 | 2.80 | 5.6 |
| 154 | Biphenyl | 92-52-4 | 0.71 | 1.6 |
| 154 | Acenaphthene | 83-32-9 | 4.40 | 7.7 |
| 156 | Naphthalene | 91-20-3 | 17.3 | 6.2 |
| 156 | 1,3-Dimethyl naphthalene | 575-41-7 | 0.60 | 0.80 |
| 166 | Fluorene | 86-73-7 | 4.03 | 6.0 |
| 167 | 9H-Carbazole | 86-74-8 | 1.4 | 1.7 |
| 168 | 3-Methyl biphenyl ( 3-phenyl toluene) | 643-93-6 | 0.61 | 0.30 |
| 168 | Dibenzofuran | 132-64-9 | 2.3 | 4.3 |
|  | 1-Ethylnaphthalene |  | 0.50 | 0.60 |
| 178 | Phenenthrene | 85-01-8 | 9.60 | 12.8 |
| 178 | Anthracene | 120-12-7 | 2.90 | 3.1 |
| 179 | Benzoquinoline-1(7,8-benzoquinoline) | 230-27-3 | 0.70 |  |
| 180 | 9H-Fluorene |  | 3.5 | 6.0 |
| 182 | 4-Methyldibenzofuran |  | 0.40 | 0.80 |
| 184 | Dibenzothiophene | 132-65-0 | 0.94 | 1.3 |
| 190 | 4H-Cyclopenta[def]phenanthrene | 203-64-5 | 1.74 | 1.5 |
|  | Pyrene |  | 4.0 | 4.7 |
| 192 | 2-Methylphenanthrenes |  | 0.60 |  |
|  | Chrysene |  | 0.10 | 1.4 |
| 202 | Fluoranthene | 206-44-0 | 4.60 | 5.5 |
| 202 | Pyrene(benzo[def]phenanthrene | 129-00-00 | 3.64 |  |
| 204 | 2-Phenylnaphthalene | - | 0.47 | 0.20 |
|  | Benz[e]pyrene |  | 0.50 | 0.3 |
|  | Benzo[ghi]perylene |  | 0.10 | <0.1 |
| 216 | 1,2-Benzofluorene(benzo[a]fluorene | - | 0.73 |  |
| 216 | 2,3-Benzofluorene | 243-17-4 | 0.80 | 0.90 |
|  | Methylpyrene |  | 0.30 | 0.20 |
| 228 | Benz[a]anthracene | 56-55-3 | 0.20 | 0.40 |
| 228 | Chrysene(benz[a]phenanthrene) | 218-01-9 | 1.4 |  |
| 252 | Benz[b]fluoranthene | 205-99-2 | 0.51 | 0.80 |
|  | Benzo[a]pyrene |  |  | 0.40 |

Notes:

1.	As most of the creosote constituents are polyaromatic hydrocarbons (PAHs) and  solubilities in water or non-aqueous media is not high, exact and accurate quantitation is not possible. The registrants conducted a quantitation method for the PAHs based on the calibration curves generated on four PAHs: naphthalene, ( two ring compound), phenanthrene ( 3 ring compound) and two four ring compounds: pyrene and chrysene. Calibaration curves were generated for these substances over a concentration range of 2 to 1000μg/ml. These substances work as markers for lesser known and identified PAHs in the creosote fractions. First GC was used to separate the components and then quadruple Mass Spectrometry was to obtain the mass spectra of individual substances. The registrants reported the presence of components to levels less than 0.10%. The Table 4 identifies the components that are over 0.10 % in both the P2 and P1/P13 fractions. The list also includes the presence of non-PAH components

Product Chemistry Assessment

The physical and chemical properties of both distillate fractions creosote  P1/P13 and P2 are described in the following

P1/P13 Fraction

Chemical Name:	          Coal Tar Creosote

Molecular Wt.:		No Applicable

Color:				2.5Y2/2 to 2.5Y4/2 (   Based on Munsell color scheme)

Odor:				Sharp, aromatic, wood-like

Solubility:			313  μg/ml

Vapor Pressure:		11.1 mm Hg at 24.4 oC

Log P:				3.247

Stability:			Short term( accelerated )stability was performed on four constituents of the mixture: naphthalene, phenanthrene pyrene and chrysene for a period of 30 days at 60 o C. At the end of thirty day period, naphthalene remaining was : 96.5%, phenanthrene: 87.2%, pyrene: 86.9% and chrysene: 92.4%

Viscosity;		14.60 mm/s

Storage Stability:	Not determined.

Notes:		1.	The P1/P13  samples,  provided by the Industry to Research Triangle Institute, were distilled, within 95% confidence limit, residues remaining were less than 1.1% as required by the AWPA Standard A1-91 ( This test is similar to the EPA’s Certified Limit Test required for other pesticides).

2.	Insoluble mass in Xylenes:	Duplicate determinations showed that this fraction contained between 0.21 to 0.23% insoluble materials.

3.	Specific gravity of the fraction, for the industry sample ( single determination) is 1.0934 ( corrected to 38oC)

4.	Moisture ( water) content for the industry sample ( single determination) is 0.4%.

All these results were obtained by using the AWPA Method A1-91 Series.

P2 Fraction

Chemical Name:	Coal Tar Creosote

Color:			10YR2/1 to 2.5Y5/5 ( Munsell color scheme)

Odor:			 Strong aromatic, Petroleum-like

Solubility:		306 μg/ml

Vapor Pressure:	8.6 mm Hg at 24.4 to 24.5 oC

Log P			3.311

Stability:

Viscosity:		15.5 mm/s at 25 oC

The chemical structure of sixteen PAHs ( EPA Priority Pollutants ) are provided below in the order of increasing complexity.

Some of the physical properties of selected PAHs are listed in Table 6 ( Illustrated Handbook of Physical-Chemical Properties and Environmental Fate for Organic Chemicals by D. Mackay et al., Lewis Publishers, 1992). Many of these are measured and a number of them ( particularly the KOW) are estimated values.

Table 6

| SELECTED PHYSICO-CHEMICAL PROPERTIES OF PAHs AT 25OC |
| --- |
| Compound | v.p (s), mm Hg | Log KOC | Solubility mg/L | Log KOW | Henry Law constant Pa m3/mol |
| Indan | 15.1 | - | 0.10 | 3.33 | 232.82 |
| Naphthalene | 7.8 x 10-2 | 3.29 | 3.1x10-2 | 3.37 | 43.01 |
| 1-Methyl Naphthalene | 6.6 x 10-2 | 2.96 | 2.8x10-2 | 3.87 | 44.90 |
| 2-Methyl Naphthalene | 6.7 x10-2 | 3.93 | 2.5x10-2 | 3.86 | 51.19 |
| Biphenyl | 9.97 x 10-3 | 3.57-3.77 | 7x10-3 | 3.90 | 28.64 |
| Bibenzyl | 3.0 x 10-3 | - | 4.3x10-3 | 4.70 | 16.93 |
| Acenaphthene | 2.2 x 10-3 | 3.79 | 3.8x10-3 | 3.92 | 12.17 |
| Acenaphthylene | 6.7 x10-3 | 3.75, 3.83 | 1.6x10-2 | 4.00 | 8.40 |
| Fluorene | 6.7 x 10-4 | 3.76 | 1.9x10-3 | 4.18 | 7.87 |
| Phenanthrene | 1.5 x10-4 | 4.42 | 1.1x10-3 | 4.57 | 3.24 |
| Anthracene | 7.5 x10-6 | 4.42 | 4.5x10-5 | 4.54 | 3.96 |
| Pyrene | 4.5 x 10-6 | 4.92 | 1.3x10-4 | 5.18 | 0.92 |
| Fluoranthene | 9.0 x 10-6 | 4.74 | 2.6x10-4 | 5.22 | 1.037 |
| Benzo[a]fluorene | - | - | 4.5x10-5 | 5.40 |  |
| Benzo[b]fluorene | - | - | 2.0x10-6 | 5.75 |  |
| Chrysene | 4.2 x 10-9 | 4.89 | - | 1.649 | 5.86 |
| Benz[a]anthracene | 2.0 x 10-5 | 4.57 | 1.1x10-5 | 5.91 | 0.581 |
| Benzo[a] pyrene | 5.2 x 10-9 | 5.48 | 3.8x10-6 | 6.04 | 0.046 |
| Benzo[e] pyrene | 5.5 x 10-9 | 4.00 | 4.0x10-6 |  | 0.020 |
| Perylene | 1.0 x 10-9 | - | 4.0x10-7 | 6.25 | 0.003 |
| Benzo[b]fluoranthene | - | 5.74 | 1.5x10-6 | 5.80 | - |
| Benzo[k]fluoranthene | 3.9 x 10-9 | 5.92 | 8.0x10-7 | 6.00 | 0.016 |
| Benzo[ghi]perylene |  | 6.20 | 2.6x10-7 | 6.50 | 0.075 |
| Dibenz[ah]anthracene | 2.7 x 10-12 | 6.52 | 6.0x10-7 | 6.75 | - |

Product Chemistry Chapter References

MRID			CITATION

None			American Wood Preservers’ Association Standards, 1998, pp 3-4.

None			MacKay D. et al., 1992. Illustrated Handbook of Physical-Chemical Properties and Environmental Fate for Organic Chemicals, Lewis Publishers.

None			Mueller J.G. et al., 1989. Environ. Sci. Technol., Volume 23(10): 1197-1201.

None			USEPA Document 540-RS-88-066. Guidance for the Registration of Pesticide Products containing Coal Tar/Creosote.

None			Cited  in reference 4 above.

None			Cited in reference 4 above.

44141101		Wade, Terry L. 1992. Product Chemistry Methods Development and Validation for Creosote. Analysis and Certification of Product Ingredients: Aristech Creosote P1/P13. Pesticide Assessment Guidelines Reference Series 62. U.S.E.P.A. Pesticide Assessment Guidelines Subdivision D: Product Chemistry. Unpublished study prepared by Geochemical and Environmental Research Group, Texas A&M University, for Aristech Chemical Corporation and John H. Butala, Technical Advisor, Creosote Council II. July 23, 1992.

44141102		Wade, Terry L. 1992. Product Chemistry Methods Development and Validation for Creosote. American Wood Preservers Association (AWPA) Standard Physical Characteristics: Aristech Creosote P1/P13. AWPA Standard Methods for Analyses of Creosote and Oil-Type Preservatives (A1-89). U.S.E.P.A. Pesticide Assessment Guidelines Subdivision D: Product Chemistry. Unpublished study prepared by Geochemical and Environmental Research Group, Texas A&M University, for Aristech Chemical Corporation and John H. Butala, Technical Advisor, Creosote Council II. August 29, 1992.

44141103		Wade, Terry L. 1992. Product Chemistry Methods Development and Validation for Creosote. Analyses of Physical and Chemical Characteristics: Aristech Creosote P1/P13. Pesticide Assessment Guidelines Reference Series 63. U.S.E.P.A. Pesticide Assessment Guidelines Subdivision D: Product Chemistry. Unpublished study prepared by Geochemical and Environmental Research Group, Texas A&M University, for Aristech Chemical Corporation and John H. Butala, Technical Advisor, Creosote Council II. September 15, 1992.

44141104		Wade, Terry L. 1992. Product Chemistry Methods Development and Validation for Creosote. Analysis and Certification of Product Ingredients: Aristech Creosote P2. Pesticide Assessment Guidelines Reference Series 62. U.S.E.P.A. Pesticide Assessment Guidelines Subdivision D: Product Chemistry. Unpublished study prepared by Geochemical and Environmental Research Group, Texas A&M University, for Aristech Chemical Corporation and John H. Butala, Technical Advisor, Creosote Council II. July 23, 1992.

44141105		Wade, Terry L. 1992. Product Chemistry Methods Development and Validation for Creosote. American Wood Preservers Association (AWPA) Standard Physical Characteristics: Aristech Creosote P2. AWPA Standard Methods for Analyses of Creosote and Oil-Type Preservatives (A1-89). U.S.E.P.A. Pesticide Assessment Guidelines Subdivision D: Product Chemistry. Unpublished study prepared by Geochemical and Environmental Research Group, Texas A&M University, for Aristech Chemical Corporation and John H. Butala, Technical Advisor, Creosote Council II. August 29, 1992.

44141106		Wade, Terry L. 1992. Product Chemistry Methods Development and Validation for Creosote. Analyses of Physical and Chemical Characteristics: Aristech Creosote P2. Pesticide Assessment Guidelines Reference Series 63. U.S.E.P.A. Pesticide Assessment Guidelines Subdivision D: Product Chemistry. Unpublished study prepared by Geochemical and Environmental Research Group, Texas A&M University, for Aristech Chemical Corporation and John H. Butala, Technical Advisor, Creosote Council II. September 15, 1992.

45355601		Sparacino, Charles M. 2000. Product Chemistry for North American CTM Creosote P1/P13 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45355602		Sparacino, Charles M. 2000. Product Chemistry for North American CTM Creosote P2 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45355701		Sparacino, Charles M. 2000. Product Chemistry for Western Tar Products Corp. Creosote P1 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45355702		Sparacino, Charles M. 2000. Product Chemistry for Western Tar Products Corp. Creosote P2 Storage Stability and Corrosion Characteristics.  Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45355801		Sparacino, Charles M. 2000. Product Chemistry for KMG-Bernuth, Inc. Creosote P2 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45355802		Sparacino, Charles M. 2000. Product Chemistry for KMG-Bernuth, Inc. Creosote P1/P13 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45355901		Sparacino, Charles M. 1998. Product Chemistry for Trenton Sales, Inc. Creosote P1/P13 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. October 15, 1998.

45356001		Sparacino, Charles M. 2000. Product Chemistry for Coopers Creek Chemical Corp. Creosote P2 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45356002		Sparacino, Charles M. 2000. Product Chemistry for Coopers Creek Chemical Corp. Creosote P1/P13 Storage Stability and Corrosion Characteristics.  Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45356101		Sparacino, Charles M. 2000. Product Chemistry for Koppers Industries, Inc. Creosote P1/P13 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45356102		Sparacino, Charles M. 1999. Product Chemistry for Koppers Industries, Inc. Creosote P2 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. October 26, 1999.

45356201		Sparacino, Charles M. 2000. Product Chemistry for Reilly Industries, Inc. Creosote P1/P13 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45356202		Sparacino, Charles M. 2000. Product Chemistry for Reilly Industries, Inc. Creosote P2 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45363901		Sparacino, Charles M. 2000. Product Chemistry for Allied Signal Incorporated Creosote P1/P13 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.

45363902		Sparacino, Charles M. 2000. Product Chemistry for Allied Signal Incorporated Creosote P2 Storage Stability and Corrosion Characteristics. Unpublished study prepared by Research Triangle Institute. March 31, 2000.