November 21, 1997

Contract # TW-0928

SPECIAL SPECIFICATION

SECTION 02950-S

TREES, PLANTS, AND GROUND COVERS

PART 1 - GENERAL	Page

1.01	Description of Work	2

1.02	References	2

1.03	Quality Assurance	3

1.04	Submittals	4

1.05	Delivery, Storage and Handling	5

1.06	Job Conditions	....................................................................................6

1.07	Warranty	............................................................................................6

PART 2 - PRODUCTS

2.01	Plant Materials	.....................................................................................7

2.02	Soil Amendments and Surfacings	...............................................................8

2.03	Planting Backfill Mixture	........................................................................9

2.04	Miscellaneous Landscaping Materials	...........................................................10

PART 3 - EXECUTION

3.01	Examination	......................................................................................12

3.02	Preparation	.......................................................................................12

3.03	Installation	........................................................................................12

3.04	Field Quality Control	............................................................................13

3.05	Maintenance	......................................................................................14

3.06	Cleanup and Protection	..........................................................................14

3.07	Inspection and Acceptance	......................................................................14

SPECIAL SPECIFICATION

SECTION 02950

TREES, PLANTS, AND GROUND COVERS

PART 1 - GENERAL

1.01	DESCRIPTION OF WORK

A.	This Section includes provisions for the following items:

1.	Trees.

2.	Shrubs.

3.	Plants.

4.	Ground cover.

5.	Soil amendments.

6.	Initial maintenance of landscape materials.

B.	Related Sections:  The following sections contain requirements that relate to this Section.

1.	Underground irrigation system is specified in Division 2 Section, "Underground Irrigation System".

2.	Excavation, filling, and rough grading required to establish elevations shown on drawings are specified in Division 2 Section "Earthwork".

1.02	REFERENCES

A.	The following publications are referenced in this Section:

1.	Dirr, Michael A. 1983. Manual of Woody Landscape Plants Stipes Publishing Co., Champaign, IL.

2.	Krussmann, G. 1976 Manual of Cultivated Broad Leafed Trees and Shrus, Vol I, II and II. Timber Press, Beaverton, OR.

3.	Krussmann, G. 1985. Manual of Cultivated Conifers. Timber Press, Beaverton, OR.

4.	Brenzel, K. 1995. Western Garden Book. Sunset Publishing Corp., Menlo Park, CA.

5.	American National Standards Institute (ANSI), American Standard for Nursery Stock; American Association of Nurserymen, Inc., ANSI Z60, 1-1980.

6.	ANSI, Safety Requirements for Tree Pruning, Trimming, Repairing or Removal, ANSI Z133, 1-72.

1.03	QUALITY ASSURANCE

A.	Installer Qualifications:  Licensed landscape contracting firm with not less than 5 years experience in the type and amount of work required in the Section.

B.	Source Quality Control:

1.	General:  Ship landscape materials with certificates of inspection required by governing authorities.  Comply with regulations applicable to landscape materials.

2.	Do not make substitutions.  If specified landscape material is not obtainable, submit to the SDR proof of nonavailability and proposal for use of equivalent material.

3.	Analysis and Standards:  Package standard products with manufacturer's certified analysis.  For other materials, provide analysis by recognized laboratory made in accordance with methods established by the Association of Official Agricultural Chemists, wherever applicable.

4.	Trees and Shrubs:

a.	Label each tree, shrub and ground cover with securely attached waterproof tag bearing legible designation of botanical or common name.

b.	Grade plant material in accordance with the codes and standards of American Association of Nurserymen.  Use nomenclature conforming to References above.  If names are not present in these listings, conform to accepted botanical nomenclature in the nursery trade.

5.	Planting Backfill Mixture:  Test organic portion of the planting backfill mixture at an approved soil testing laboratory.  Test to verify characteristics listed under "Products" portion of this specification and include recommendations from the testing laboratory.  The SDR may also test the final product as delivered or installed to verify the mixture matches the listed characteristics and the submitted soil report. Test data may up to one year old.

a.	Acceptable Backfill Testing Laboratories:

(1)	IAS (Inter Ag Services)

2643 East University Drive

Station 113

Phoenix, AZ  85034

(602) 273-7248

(2)	ASSAGAI Labs

P. O. Box 90430

Albuquerque, NM  87199-0430

(505) 345-8964

6.	Inspection:  The SDR may inspect trees, shrubs and ground covers either at place of growth or at site before planting, for compliance with requirements for genus, species, variety, size and quality.  The SDR retains right to further inspect plant material for size and condition of balls and root systems, insects, injuries and latent defects, and to reject unsatisfactory or defective material at any time during progress of work.  Remove rejected trees or shrubs immediately from project site.

1.04	SUBMITTALS

A.	Samples:

1.	Submit a one-eighth cubic foot sample of each type of mulch for approval.

B.	Plant and Material Certifications:

1.	Manufacturer's or vendor's certified analysis and material safety data sheets for soil amendments, herbicides, and fertilizer materials.

2.	Planting Backfill Mixture:  Submit test results to the SDR prior to delivery.

C.	Maintenance Manuals:

1.	Submit two copies of typewritten instructions recommending landscape maintenance procedures to be followed by the SDR for one full year.  Write instructions specifically for this project and note tasks by site area.  Submit prior to expiration of required maintenance period.

2.	Record Drawings:  Submit record prints with any variations from the plans clearly and professionally marked in red pencil.

D.  	Submit all of the above in accordance with Specification 1300.

1.05	DELIVERY, STORAGE AND HANDLING

A.	Delivery and Storage of Materials:

1.	The SDR will inspect and accept plant materials prior to delivery to site and incorporation into the work.

2.	Packaged Materials:  Deliver packaged materials in containers showing weight, analysis and name of manufacturer.  Protect materials from deterioration during delivery and while stored at site.

3.	Plant Backfill Materials:  Collect and provide load tickets to the SDR for each delivery.  List the following information on the ticket:

a.	Source of material.

b.	Approximate volume of load.

c.	Date of delivery or loading.

d.	Typed name of individual representing the source.

e.	Inked original signature of individual representing the source.

f.	Area of site of the product delivery.

4.	Trees and Shrubs:  Provide freshly dug or containerized trees and shrubs.  Do not prune prior to delivery.  Do not bend or bind-tie trees or shrubs in such manner as to damage bark, break branches or destroy natural shape.  Provide protective covering during delivery.  Do not drop balled and burlapped stock during delivery.  Handle container-grown materials by container only.

5.	Deliver trees and shrubs after preparations for planting have been completed and plant immediately.  If planting is delayed more than 6 hours after delivery, set trees and shrubs in shade, protect from weather and mechanical damage, and keep roots moist.

B.	Handling Materials

1.	Lift trees only by methods that will not damage bark.  Lift trees 3 inches in caliper and larger with chains triangulated around the rootball.  Do not lift trees 3 inches in caliper or larger by straps around the trunk.

2.	Do not remove container-grown stock from containers until planting time.

1.06	JOB CONDITIONS

A.	Existing Conditions:

1.	Utilities:  Determine location of underground utilities and perform work in manner which will avoid possible damage.  Hand excavate as required.  Maintain grade stakes set by others until removal is mutually agreed upon by parties concerned.

2.	Excavation:  When conditions detrimental to plant growth are encountered, such as rubble fill, adverse drainage conditions, or obstructions, notify the SDR before planting.

B.	Sequencing and Scheduling:

1.	Planting Time:  Proceed with and complete landscape work as rapidly as portions of site become available, working within seasonal limitations for each kind of landscape work required.

2.	Plant or install material during normal planting seasons for each type of landscape work required.  Correlate planting with specified maintenance periods to provide maintenance from date of substantial completion until final acceptance.

3.	Determine the acceptability of subgrade preparation prior to the start of landscaping work.  Protect all existing items to remain and new work of other trades to ensure proper timing of each phase of work.

1.07	WARRANTY

A.	Warranty trees, shrubs and ground cover through specified maintenance period and until final acceptance.

B.	Warranty trees, shrubs and ground cover for a period of one year after date of final completion, against defects including death and unsatisfactory growth as determined by the SDR, unless defects are due to SNL's negligence in following the Contractor's recommended maintenance procedure.

C.	Remove and replace trees, shrubs or other plants found to be dead or in unhealthy condition during warranty period.  Replace plant materials during the dormant season following the end of warranty period or as directed by the SDR.  The dormant season is defined as September 30 through May 1.  Replace trees and shrubs which are in doubtful condition at the end of the warranty period; unless, in opinion of the SDR, it is advisable to extend warranty period for a full-growing season.

PART 2 - PRODUCTS

2.01	PLANT MATERIALS

A.	General:

1.	Provide trees, shrubs and plants of quantity, size, genus, species, and variety shown and scheduled for landscape work and complying with recommendations and requirements of ANSI Z60.1 "American Standard for Nursery Stock" unless specific approval is obtained for particular plant material.

2.	Provide healthy, vigorous stock, grown in recognized nursery in accordance with good horticultural practice and free of disease, insects, egg, larvae, and defects such as knots, girdling roots, sun-scald, injuries, abrasions, or disfigurement.

3.	Size:  Equal to or greater than the minimum size indicated.  Remove undersized plants prior to substantial completion.

4.	Container and Boxed Stock:  Grown in its delivery container for not less than six months for shrubs and one year for trees, but for not more than two years.  Rootbound material is unacceptable.

B.	Trees:  Provide container or nursery grown (not collected or plantation grown) trees 2-inch caliper and larger from an approved nursery.  The SDR will tag trees at the nursery unless otherwise indicated.  Provide trees that are first-class representatives of their species, well-shaped and full, with straight and plumb trunks.  Trees  with irregular branching patterns or with branching patterns more highly developed on one side than on the other sides shall not be accepted.  Trees with double leaders or trees that have been "headed back" or "topped" are unacceptable.  The SDR reserves the right to reject any trees not meeting these criteria.  Balled and burlapped (B&B) material wrapped with plastic burlap or plastic twine is unacceptable.  Properly root prune B&B material.  Acceptance at nursery does not preclude the possibility of rejection of material on site.

C.	Deciduous Shrubs:  Provide shrubs as scheduled, with not less than the minimum number of canes required by ANSI Z60.1 for the type and size of shrub required.  Provide container grown deciduous shrubs.

D.	Coniferous and Broadleafed Evergreens:  Provide evergreens of sizes shown or listed, nursery grown except for Ponderosa and Pinon pines.  Provide Grade XX evergreen trees.  Provide container grown or balled and burlapped evergreen shrubs.

E.	Ground Cover:  Provide plants established and well rooted in removable containers or integral peat pots, with not less than minimum number and length of runners required by ANSI Z60.1 for the pot size shown or listed.

2.02	SOIL AMENDMENTS AND SURFACINGS

A.	Commercial Fertilizers:  Subject to compliance with State and Federal regulations, the following fertilizers shall be used:

1.	Actual Nitrogen:  2 pounds per 1000 square feet.

2.	Actual Phosphate: 2 pounds per 1000 square feet.

3.	Actual Potassium: 2 pounds per 1000 square feet.

4.	Agricultural Sulfur: 4 pounds per 1000 square feet.

5.	Root Stimulant:  "Superthrive"; available from Southwest Seabeach Inc.

B.	Enzymes:  Subject to compliance with State and Federal regulations, EPA-NCP (National Contingency Program) and NM Environmental Department groundwater discharge acceptance of approved live organisms/enzymes, manufacturers offering products which may be incorporated in the work include, but are not limited to, the following:

1.	SuperBio as provided by Organic Technology Inc., 12017 Skyline NE, Suite B, Albuquerque, New Mexico  87123, (505) 291-1100, or 291-1400, or facsimile at 271-1600 is considered approved.  Apply at a rate of 1/2 gallon per 1000 square feet of Planting Backfill Area.  Mix into subgrade and loosened soil.  Provide with a 20% solution of humic acid integral with the SuperBio.

C.	Super Absorber:  Provide and install a super absorber.  Super absorber shall be a cross linked polyacrylamide.  Polyacrylate materials are not acceptable.  Apply at a rate of 5 pounds per 1000 square feet of planting backfill mix.  The following is considered approved:

1.	Stockosorb :	Organic Technology, Inc.

12017 Skyline NE, Suite B

Albuquerque, New Mexico  87123

(505) 291-1100, or 291-1400, or facsimile at 271-1600

2.	Polyacrylamide :	Western Polyacrylamide, Inc.

P.O. Box 790

Castle Rock, Colorado  80104

(303) 688-3814

3.	Terra-Sorb HB :	American Excelsior Co.,

4018 Edith Boulevard., NE

Albuquerque, New Mexico  87107

(505) 345-7807

D.	Mulch:  Provide mulch material as indicated on the drawings.

1.	Gravel:  Clean, fractured, and ¾” in diameter.  Material to be Santa Ana Tan  as sold by Western Mobile Inc. or an approved equivalent brown aggregate.

2.	Crusher Fines:  Greyish-brown crushed stone ranging from dust to 3/8” diameter. Material to be Santa Ana Tan Crusher Fines as sold by Western Mobile Inc. or an approved equivalent brown crusher fine.

3.	Cobble:  Stones not less than 4 inches in any direction and not more than 8 inches in any direction with less than 15% broken fragments.  Color to be gray with tan colors.  Material shall be from the Santa Ana pit and as sold by Western Mobile Inc. or an approved equivalent cobble.

4.	Bark:  Shredded ground fir, hemlock or ponderosa bark of uniform color and free of weeds, seed, sawdust, wood splinters, resin tannin, wood fiber, or other compounds detrimental to plant life.  Provide bark mulch consisting of long shredded pieces that interlock and resist erosion.  Screen bark mulch to eliminate particles less than 1/8 inch and pieces greater than 3 inches across.

E.	Anti-Desiccant:  Emulsion-type, film-forming agent designed to permit transpiration but retard excessive loss of moisture from plants.  Deliver in manufacturer's fully identified containers and mix in accordance with manufacturer's instructions.

1.	Acceptable Product:  "Wilt-Pruf" or approved substitute.

F.	Inorganic Amendment:  Provide zeolite material as sold by Western Organics Inc. or an approved equivalent product.

2.03	PLANTING BACKFILL MIXTURE

A.	Provide a premixed, homogenous soil consisting of native soil, organic matter and soil amendments and fertilizers as noted above, meeting the following performance characteristics.

1.	Native Soil:  80% by volume of clean native soil from the SNL fill area or a non-sterilized area of the site.

2.	Inorganic Amendment:  10% by volume of inorganic amendment.

3.	Organic Matter:  10% by volume of compost material and as follows:

a.	Compost or Mulch:  A combination of organic carbon sources such as straw, hay, bark, sawdust, or wood shavings and nitrogen sources such as manure, blood meal, or chemical fertilizers.  Add nitrogen sources prior to composting.  Aerobically compost mixture at temperatures between 120 degrees F and 160 degrees F for a period of not less than 100 days.  Destroy weed seeds during composting and minimize urea ammonia from nitrogen.  Screen finished compost to provide less than 2% remaining on a 1/2" screen.  Provide a carbon-to-nitrogen ratio of less than 50 parts carbon to one part nitrogen.

b.	Miscellaneous Characteristics of the Organic Matter:

(1)	Potash (potassium) present at a rate of at least 200 parts per million of exchangeable potassium.

(2)	Salinity (EGXK) not to exceed 3 MNHOS/CM.

(3)	Nitrate nitrogen (NO3-N) present at a rate of at least 30 parts per million.

(4)	Phosphorous as measured by Olson sodium bicarbonate measurement method not less than 15 parts per million.

(5)	PH shall be between 6.0 and 7.5.

(6)	TKN2 or Total Kjeldahlnitrogen 250 ppm or greater.

(7)	NH4 25 ppm or less.

c.	Potential Sources of the Organic Matter.

(1)	Western Organics Inc.

RR 9, Box 862

2nd and Bates Rd. SW

Albuquerque, NM  87105

(505) 877-8670

(2)	New Mexico Compost Products

From Soilutions

9008 Bates Rd. SE

Albuquerque, NM  87105

(505) 877-0220

2.04	MISCELLANEOUS LANDSCAPING MATERIALS

A.	Filter Fabric:  Non-woven polypropylene or polyester material, meeting the following requirements.

1.	Tensile strength per ASTM D1682:	90 lbs. minimum

2.	Elongation percent per ASTM D1682:	65% maximum

3.	Equivalent open size (US Sieve NO.):	50-100

4.	Permeability coefficient (CM/SEC):	.05 minimum

5.	Flow in gallons per square feet per minute per ASTM D-4491:	80 minimum

6.	Weight in ounces per square yard:	3.0 minimum

7.	Acceptable Products:

a.	Soil-Check, manufactured by Brighton By-Products Company, Inc., P.O. Box 23, New Brighton, PA 15066; 1-800-245-3502.

b.	Propex 4545, manufactured by Amoco Fabric Co., 550 Interstate North Parkway, Suite 150, Atlanta, GA 30099; (404) 955-0935.

c.	Mirafi Miriscape II, manufactured by Celanese Fibers Marketing Co., 1211 Avenue of the Americas, New York, NY 10036; (212) 764-7640; or Box 32414, Charlotte, NC 28232; (704) 554-2000.

d.	Warren's Terrabond, sold by Warren's Seed and Special Products Division, P.O. Box 459, Suisun City, CA 94585.

e.	DUON by Phillips Petroleum, available from Blunk's Wholesale Supply, Inc.

B.	Staking Materials (required only when indicated on drawings and for evergreens):

1.	Tree Support Stakes:  #5 reinforcing rod, 10'-0" long, or as indicated on drawings.

2.	Wire:  12 gauge annealed galvanized steel.

3.	Chafing Guards:  New or used 2-ply reinforced rubber hose.

C.	Tree Wrap:  Two thicknesses of crinkled paper cemented together with a layer of bituminous material.  Provide wrapping material a minimum of 4 inches wide, with a stretch factor of 33-1/3 percent.  Provide a lightly tarred medium or coarse sisal twine for tying tree wrap to tree.  Wrap trees if planted between September 1 and February 1.

PART 3 - EXECUTION

3.01	EXAMINATION

A.	Obtain approval of grading from the SDR prior to plant and mulch placement, excavation, or filter fabric installation.

3.02	PREPARATION

A.	Measurements and Plant Material Locations:  Tree and shrub locations shown on the planting plan are approximate.  Stake all plant material locations shown on the planting plan, and, as directed by the SDR, adjust the position and orientation of trees.  Obtain approval of final positions of plant material from the SDR.

B.	Preparation of Ground Surface:  Remove rocks, stones greater than one inch across, trash and other debris from areas to be planted or mulched.  Grade areas smooth, to the appropriate subgrade. See planting installation notes for soil modifications near trees and shrubs.

3.03	INSTALLATION

A.	Trees:  Excavate tree pits 6 feet beyond the spread of the root ball or box or to the edge of adjacent paving for a depth of one foot.  Excavate for a depth of 10".  Backfill entirely with Planting Backfill Material as noted above.  Planting Backfill Material will include enzymes, fertilizer, humates, superabsorber, organic and inorganic components and native soil.  When soil conditions detrimental to plant growth are encountered, such as rubble fill, adverse drainage conditions or obstructions, notify the SDR before planting.  Place backfill in pit to proper depth so top of root ball will be one inch below adjacent soil grade (on slopes, one inch shall be the depth below surrounding grade on the downhill side).  Set root ball  in center of pit with top of ball one inch lower than surrounding grade.  Align trunks where trees are in rows on the plan.  Remove burlap from the top one-third of root ball.  Remove all wire from the top one-third of root ball.  Remove all mesh smaller than a 3” square from the entire root ball.  Backfill in carefully tamped layers.  Continue backfilling and flood with water after two-third backfilled.  After water is absorbed, continue backfilling and tamping to grade, leaving no voids or air pockets.  Water again after placing final layer on backfill.  All tree pits are to form a depression (one inch below adjacent grade or turf) with sides neatly sloped inward to top of ball.  Fill depressions with mulch and wrap trees.  Stake and/or guy evergreen trees and other trees as indicated on drawings and as shown in details.  Apply antidesiccant to all leafed out trees and evergreens.

B.	Shrub Planting:  Cut all circling or potentially girdling roots.  Place individual shrubs in pits a minimum of 6 inches deeper and 12 inches wider in diameter than the container or ball size.  Excavate for a distance of 2 feet from the center of the shrub and backfill with Planting Backfill Mixture as noted above.  Place planting backfill material to finish grade level and thoroughly soak.  Apply antidesiccant to all leafed out shrubs and evergreen material.

C.	Mulch and Filter Fabric:  Spread a uniform layer of mulch as specified, on all planting beds as noted and detailed on drawings.  Maintain a smooth and consistent subgrade under the entire mulch area.  Obtain SDR approval of mulch area subgrades prior to mulch and/or filter fabric installation.  Install filter fabric only under gravel or cobble mulched areas.

D.	Tree Wrapping:  The SDR will inspect the trunks of the trees for physical damage or insect infestation to determine the required treatment or rejection prior to the wrapping operation.  For trees planted between September 1 and February 1, wrap all deciduous trees spirally from bottom to top with specified tree wrap, or first quality burlap not less than six inches nor more than ten inches wide and of suitable strength.  Wrap tree to overlay and entirely cover the trunk from the ground to the height of the second branches and shall be neat and snug.  Overlap approximately two inches.

E.	Staking and Guying:

1.	Guy and stake for plantings if indicated on the drawings and as noted above.  Stake all evergreens.  If no staking is noted, staking is a contractor option.  The trees shall be reviewed at the end of the warranty period to see if the trunks are out of plumb.  If trunks are out of plumb, corrective actions acceptable to the SNL Delegated Representative shall be taken by the contractor.

2.	Drive standard stakes vertically into the ground to a depth in such a manner as not to injure the ball or roots.

3.	Hold plants firmly between the stakes with a double strand of 12 gauge wire.  Use hose chafing guards, as specified, where wire will contact the plant.  Twist hose and wire assembly between tree and stake as required to hold tree securely yet allow some movement.

3.04	FIELD QUALITY CONTROL

A.	Utility Coordination:  Locate existing utilities.  Repair damage to utilities at Contractor's expense as directed by the SDR.

B.	Pruning:  Prune plant materials as directed by the SDR and in compliance with ANSI Z133.1.  Remove dead and broken branches.  Prune deciduous trees and shrubs to reduce total amount of branching structure by no more than one-third.  Retain typical growth habit of individual plants with as much height and spread as is practicable.  Do not pole or remove the leader from the trees.  Remove trimmings from site.  Prune plant materials between October 1 and May 15.  Trim trees near walks to 8'-0" height above walk, as directed by SDR.

3.05	MAINTENANCE

A.	Begin maintenance immediately after planting.

B.	Maintain trees, shrubs and other plants until final acceptance of all planting work but in no case less than 30 days after substantial completion of planting.

C.	Maintain trees, shrubs and other plants by pruning, cultivating and weeding as required for healthy growth.  Restore planting saucers.  Tighten and repair stake and guy supports and reset trees and shrubs to proper grades or vertical position as required.  Restore or replace damaged wrappings.  Spray as required to keep trees and shrubs free of insects and disease.  Replace dead plant material.  Protect from damage resulting from trespass, erosion, weather, vandalism, disease, and other hazards.

3.06	CLEANUP AND PROTECTION

A.	During landscape work and maintenance period, keep pavements clean and work area in an orderly condition.

B.	Upon completion of all planting operations, clean the portion of the project site used for storing materials and equipment of all debris, superfluous materials, and equipment.  Remove materials and equipment from the project site.  Sweep or wash clean walks and pavements upon completion of work in this Section.

C.	Protect landscape work and materials from damage due to landscape operations, operations by other contractors and trades, erosion and trespassers.  Maintain protection during installation and maintenance periods.  Treat, repair, or replace damaged landscape work as directed by the SDR.

3.07	INSPECTION AND ACCEPTANCE

A.	When landscape work is completed, including maintenance, the SDR will, upon request, make an inspection to determine acceptability.

B.	When inspected landscape work does not comply with requirements,  replace rejected work and continue specified maintenance until reinspected by the SDR and found to be acceptable.  Remove rejected plants and materials promptly from project site.

END OF SECTION