96M03/29/06

S209-96M.doc

Use on all projects with culverts.

Section 209. - STRUCTURE EXCAVATION AND BACKFILL

Construction Requirements

209.09  Bedding.

(b) Culverts.  Delete the third sentence and substitute the following:

When no class is specified, use bedding material that conforms to class C and to Table 2 of AASHTO M 145 for Classifications A-1, A-2, or A-3 soils.

Add the following:

If lean concrete backfill is used, the bedding requirements for (2) Class B and (3) Class C are waived.

Where installing plastic pipe, use Class B.

(c) Pre-Cast and Cast In Place Concrete Box Culverts.  Construct bedding according to 209.09(a).  Use Class B bedding.

209.10  Backfill.

(b) Culvert.  Delete the first sentence and substitute the following:

Where installing plastic pipe, use backfill material conforming to the requirements of Class B bedding.

Add the following:

As an alternative to backfill material, the Contractor may use lean concrete backfill for backfill of pipe culverts.  When utilizing lean concrete backfill, furnish materials and perform the work according to Section 614.  Do not use lean concrete backfill with aluminum or aluminum-coated structures or plastic culverts.

Use on 4R projects that have concrete retaining walls.

209.12  Acceptance.  Add the following:

Structural excavation (walls) work will be evaluated under Subsections 106.02 and 106.04.

Measurement and Payment

209.13  Add the following:

Do not measure structural excavation (walls) for payment.