INSTRUCTIONS FOR USE OF OREGON CONSTRUCTION SPECIFICATION (CS-13)

EVACUATION AND BACKFILL OF TRENCHES FOR CONDUITS

1.	Applicability

Construction Specification CS-13 is applicable for the excavation and backfill of trenches for pipelines and conduits.

2.	Material Specifications

The NRCS material specifications complementary to Oregon State, Construction Specification CS-13 are MS-204, Concrete Pipe; MS-205, Corrugated Metal Pipe; MS-206, Plastic Pipe;

MS-207, Steel Pipe; MS-208, Corrugated Plastic Tile; MS-209, Fabric Filters, MS-210, Aggregate Filters; MS-211, Bedding; and MS-220, Corrugated Polyethylene Pipe.

3.	Items to be Included in the Specifications and on the Drawings:

a.	Required cross-section locations and grades are to be shown on the drawings.

b.	Specify conduit or pipeline material which includes dimensions, grade, strength and/or

class and show on the drawings.

c.	Specify bedding and select backfill requirements and show on the drawings.

d.	Depth, width, side slopes and cover for the trench should be specified and shown on the drawings.

e.	Bracing, sheeting or other support installations should be shown on the drawings, if applicable.

f.	Specify backfill provisions.

g.	The approximate location and limits of utility right-of-way or easements should be shown on the drawings, if applicable.

h.	Specify special requirements for control of erosion, sedimentation water pollution and

air pollution.

i.	Specify method measurement and payment, if applicable.