ON ABILITY OF A COMMUNICATION CHANNEL TO ACCOMMODATE MULTIMEDIA TRAFFIC

V. Marbukh
Wireless Communications Technologies Group
National Institute of Standards and Technology
100 Bureau Drive, Stop 8920
Gaithersburg, MD 20899-8920

# Abstract

The throughput of a communication system serving bursty multimedia traffic can be characterized by the admission region: all possible sets of multimedia sources the system can accommodate given the sources statistical characteristics and Quality of Service () requirements.  Since throughput depends on the system resources (bandwidth and buffering space) as well as the resource management strategies, it is natural to define the system capacity as the upper limit on the admission region over all physically feasible strategies.  This paper estimates the capacity of a buffered communication channel serving multimedia traffic with  requirements on the maximum allowable traffic delay and loss.  The buffer is assumed large enough to make the channel capacity the limiting resource.  Given the set of multimedia sources within the system capacity, the paper also discusses the scheduling disciplines that provide the required .

# 1. Introduction

Emerging multimedia networks will statistically multiplex bursty multimedia traffic sources with vastly different statistical characteristics and Quality of Service () requirements.  In presence of multimedia traffic, different classes of resource (bandwidth and buffer space) management strategies can be compared on the basis of the admission region.  The admission region represents all possible sets of multimedia sources the system can accommodate with the corresponding strategies, given the system resources, and  requirements.  We consider a single buffered communication channel serving multimedia traffic with  requirements on maximum allowable cell loss probability and delay.  Due to limited paper space we assume that the buffer is large enough to make the channel capacity (not the buffering space) the limiting resource.  This situation is typical for wireless communication.  We assume that  Classes of Service () are statistically multiplexed through a large buffer on a communication link with a constant bit rate .   includes  identical sources with the following  requirements:

(1)     ,

where  and  are the traffic loss probability and delay respectively.  Given the scheduling discipline  and  requirements (1), the admission region  represents all possible sets of multimedia users  the system can accommodate.  We assume the buffer management strategy which accepts all arriving traffic into the buffer and drops a cell of class  from the buffer once the cell current delay exceeds the limit  to prevent wasting the channel capacity on an outdated traffic.  Obviously, this buffer management strategy is optimal in terms of maximizing the admission region for a sufficiently large buffer but can be improved for small buffers.

It is natural to define the system capacity region as the upper limit of the admission region  over all scheduling disciplines :

Assuming that the statistical properties of the sources are known, the paper approximates the capacity region (2) as a function of the channel bit rate  and  requirements (1):         .  The paper also discusses scheduling disciplines  which closely approach the capacity region (1).  We consider the following large deviations asymptotic regime:   ,      .  It is known [1] that under this regime the statistical properties of the sources can be characterized by the effective bandwidths:

(3)

whereis the amount of traffic generated by a source  of class  during time interval .    We assume that processes  have stationary increments and are jointly statistically independent for   The average rate of a source of class  is .

The paper is organized as follows. Section 2 conjectures the distributional version of the Little theorem.  Section 3 approximates the capacity region in a case of uniform loss and  specific delay requirements:  .  Section 4 approximate the capacity region in a case of  (1).  Finally, section 5 illustrates our results in a case of  classes of service and Brownian traffic sources.

# 2. The Conservation Laws

In a case of uniform  requirements , , the corresponding capacity region  can be realized with the First In First Out () scheduling.  It is known [1] that the boundary of this region  is closely approximated by an appropriately chosen linear hyperplane.  Following [2]-[3], we may pick a point  on  and obtain the tangent hyperplane to  which tauches  at :

(4)

where a parameter  can be justifiably called the effective rate of a source of class .  The effective rates   depend on the traffic mixture  and can be calculated if the effective bandwidths (3) are known [1].

Consider a system that statistically multiplexes a traffic mixture  on a channel of capacity  through an infinite buffer. Assuming that scheduling discipline treats all sources of the same class equally, let  and  be given by  and   where  and   are the delay and backlog respectively for a traffic generated by a source  of class , and  is the total backlog.  Given a traffic mixture  and a pair () such that

(5)

we conjecture the following inequality:

(6)

for any scheduling discipline.  This inequality can be interpreted as a distributional version of the Little theorem [4].  If , , then , ,  and, as a result, (6) reduces to the Little theorem: .  Inequality (6) also holds if the traffic mixture includes only identical sources.  In this particular case equality in (6) can be realized with the First In First Out () scheduling discipline.  There is a number of arguments which can be put forward to suggest that (6) holds (at least approximately) in a general case and the boundaries in (6) can be closely approached for all  simultaneously with the Earliest Due Date scheduling discipline  [5].

We will use (5)-(6) to derive upper bounds on the capacity region under the large deviations asymptotic regime when , and consequently, (5)-(6) take the following form:

(7)     where

3. The Capacity Region for Uniform Losses

Combining (4) with (7) we obtain the following system:

(8)

(9)

for any  subset .  Solving (9) for  and then substituting this  into (8) we obtain a region (a simplex exterior)   in a parameter space .  Intersection of these regions   for all subsets

upper bounds the attainable  region  in a case of uniform loss probabilities: .  Our hypotheses are that region  in fact closely approximates region : , and the  region can be closely approached with the  scheduling discipline.

Consider a case of uniform loss and service specific delay requirements: , , .  Without loss of generality assume the  are arranged according to the stringency of the  requirements:  .  All traffic mixtures  for which the attainable  region (8)-(9)  contains the  parameters , ,  form the following region:  where   is the solution to the following fixed point equation:      . Regions , and, consequently, their intersection,  upper bound the capacity region (2) in a case of uniform losses

(10)

Upper bound (10) is obtained by considering the attainable  regions (8)-(9) for  subsets ,  of the set of services .  It can be shown that applying conservation laws to all possible subsets of the set of services  would not produce a tighter upper bound on the capacity region than (10).  We expect that the intersection , in fact, closely approximates the capacity region (2) for uniform losses:

(11)

and that the capacity region (11) can be closely approached with the  scheduling.

4. The Capacity Region in a General Case

First, consider a "homogeneous "case when the traffic mixture consists only of sources of the same class : .  Given the  requirements (1), the corresponding capacity region  is  where  is the corresponding "homogeneous" effective rate.  Consider all pairs  for which: = , or, equivalently,

(12)        =

Equation (12) describes the trade-off between the  requirements on loss and delay  in a homogeneous case: .  Assuming that this trade-off holds in a heterogeneous case, when a mixture of different services is multiplexed on the channel, one may try to approximate the heterogeneous capacity region as follows:

(13)

where region  is approximated according to (11), and  are determined by (12) for some .  After implementing this procedure for general traffic sources the resulting approximate capacity region will depend on the arbitrary parameter  since the trade-off between the loss and delay depends on the traffic mixture.  However, for Brownian traffic sources [1] the effective rate is  , equation (12) takes the following form:  and, consequently, the right-hand side of approximation (12) is independent of the parameter .  Arrange services as follows: , where  . Using (11)-(13) we can approximate the capacity region in a case of  requirements (1) and Brownian traffic sources as follows:

(14)

where regions  are as follows:    and  are easily obtained from the following quadratic equations:

We expect that for Brownian sources approximation (14) is in fact an identity and for general traffic sources (14) closely approximates the capacity region.  We also expect that for Brownian (arbitrary) sources the capacity region can be realized (closely approached) with the scheduling discipline .  This discipline can be interpreted as a generalization of the  with service  specific time scale:  and assuming that service  specific deadline with respect to the time scale  is .

It can be shown that the region  can be closely approximated by an appropriately chosen simplex:

, and, consequently, the capacity region (13) can be approximated by the -dimensional polyhedron:

.  This approximation is consistent with theoretical and simulation results for specific scheduling disciplines [6]-[7].

5. Example: Two Classes of Service, Brownian Traffic Sources

As an example consider a case of  classes of service, and Brownian traffic sources.  We use the same notations as in the previous section and assume that .  Fig. 1 shows regions ,  and their intersection  in the following three cases: (a) , (b)  , and (c)   where

(15)

Figure 1: Schematic view of the capacity region in a case of two classes of service.

If , then the capacity region  has linear boundary since this case in effect is a case of uniform  requirements.  If  , then still , but the capacity region has non-linear boundary.  If  then , and the boundary () of the capacity region  contains a linear segment ().  The trapezoidal shape of the capacity region in a case  indicates that even when the system is serving the maximum possible number of high priority sources of class , the channel still has enough residual capacity to accommodate certain number of sources of class  as low priority.  Examination of (15) shows that this is possible if the high priority sources are burty and the difference in the  requirements for different services is sufficiently large to allow for a squeezing of the low priority traffic between the bursts of the high priority traffic.

References

- F.P. Kelly, "Notes on effective bandwidth," Stochastic Networks, F.P. Kelly, S. Zachary, I. Ziedins, Eds., Oxford: Clarendon Press, 1996, pp. 141-68.

- J.Y. Hui, Switching and Traffic Theory for Integrated Broadband Networks, Boston, MA: Kluwer, 1990.

- F.P. Kelly, "Effective bandwidth at multi-type queues," Queueing Syst., vol. 9, pp. 5-15, 1991.

- W. Whitt, "A review of ," Queueing Systems, vol. 9, 1991, pp. 235-68.

- S.S Panwar, D. Towsley, and J.K. Wolf, "Optimal scheduling policies for a class of queues with customer deadlines to the beginning of service," J. Ass. Comput. Mach., pp. 832-844, 1988.

- A.W. Berger and W. Whitt, "Extending the effective bandwidth concept to networks with priority classes," IEEE Comm. Magazine, vol. 36, no.8, Aug. 1998, pp.78-83.

- A.I. Elwalid and D. Mitra, "Analysis, approximations and admission control of a multi-service multiplexing system with priorities," Proc. IEEE INFOCOM'95, pp. 463-72, 1995

# Text boxes

.

.

.