USPS

Intelligent Mail Container Barcode

Specification

(For Use on Mailer-generated Pallet Labels)

Version 12

Revised September 17, 2007

Table of Contents

About this document	1

Comments and Feedback	1

Intelligent mail Container Barcode Specifications	2

General Barcode Requirements	2

Human-Readable Text	3

Barcode Quality	3

Barcode Placement	4

Barcode Data Constructs	4

6-digit Mailer ID Format	4

9-digit Mailer ID Format	5

Barcode Examples	5

# About this document

This document provides specifications for printing the USPS Intelligent Mail Container Barcode.  The Intelligent Mail Container Barcode is used on mailer-generated pallet labels to identify the mail owner and uniquely identify the unit load (pallet, container, or rolling stock).  Other human-readable data elements, beyond the Intelligent Mail Container Barcode, such as text identifying the mail owner, destination, and type of mail are also required on the placard (see Section 705 of the Domestic Mail Manual for more information).  Certain USPS programs may also have additional program-specific requirements.  Contact your USPS account representative or the PostalOne! helpdesk at (800) 522-9085 if you need assistance in determining these requirements.

This specification may periodically be revised.  A current version of this specification is available for download along with other related guidance documents on the USPS Rapid Information Bulletin Board System (RIBBS) at http://ribbs.usps.gov.

# Comments and Feedback

Comments or suggestions regarding the content of this document should be directed to:

Himesh Patel

Program Manager

USPS Intelligent Mail - Planning & Standards

703-280-7498

HPatel@usps.gov

# Intelligent mail Container Barcode Specifications

## General Barcode Requirements

| Barcode Symbology: | Barcodes shall be produced using the GS1-128 (formerly UCC/EAN Code 128) symbology. Only Subsets B and C are permitted for this application. NOTE: Subset C allows for more efficient encoding of numeric values (i.e. can shorten the overall barcode length) than Subset B; however, Subset C does not support encodation of alpha characters. Subset B allows for encoding of numeric values plus it supports encoding of both “upper” and “lower” cases alpha characters. Special shift characters must be used to toggle between subsets. Some commercial barcode applications may have automatic subset-selection functionality designed to construct the most compressed (i.e. shortest length) barcode. Care should be taken to ensure that Subset A is not inadvertently used. Additionally, customers are cautioned to encode alpha characters in the same case as provided to the USPS in any other medium (physical or electronic) (e.g. Mail.dat file). |
| --- | --- |
| Barcode Data: | Barcodes must encode 21 characters conforming to one of the approved barcode constructs defined in the Barcode Data Constructs section of this document. |
| X-Dimension: | The barcode’s X-dimension shall measure greater than or equal to 15.8 mils (≥ 15.8 mils), but not more than 19.5 mils (≤ 19.5 mils). NOTE: X-dimension is an industry recognized term that specifies the width of the narrowest bar or space within the barcode. A barcode’s X-dimension is expressed in “mils” which corresponds to the width of this narrowest bar or space in thousands of an inch (i.e. 0.001”). A value of 19.5 mils is equivalent to 0.0195”. |
| Barcode Length: | The overall length of the barcode, measured from the leading edge of the first bar to the trailing edge of the last bar, shall not exceed 5.00 inches. |
| Barcode Height: | The minimum barcode height shall not be less than 15% of the barcode’s length. Under no circumstance, regardless of barcode length, shall the barcode height be less than 0.54”. The maximum height of the barcode shall not exceed 1.00 inch. |

## Human-Readable Text

| USPS Banner: | The phrase “USPS BARCODE” shall be printed in all uppercases letters centered above the barcode. A clear zone of at least 0.125”, but not more than 0.5”, shall be observed between the bottom edge of this text and the top of the barcode. A clear zone of at least 0.125” shall be observed in all directions around this text. The text shall be printed in a boldface sans serif font. The text should be printed in at least 12-point type. |
| --- | --- |
| Human-Readable Representation of Encoded Barcode Data: | The human-readable representation of the barcode shall be centered below the barcode. A clear zone of at least 0.125”, but not more than 0.5”, shall be observed between the lower edge of the barcode and the top of this text. A clear zone of at least 0.125” shall be observed in all directions around this text. The text shall be printed in a boldface sans serif font. The text should be printed in at least 10-point type. To enhance readability, the human readable representation of the barcode data shall be “parsed” or separated by data field. Two blank spaces shall be left between each field. |

## Barcode Quality

| Minimum Scan Grade: | At least 70% of a mailer’s barcodes must have an Overall Symbol Grade of “B” or better based upon the American National Standards Institute (ANSI) Guideline for Barcode Print Quality [ANSI INCITS 182-1990]. The remainder can grade no less than a “C”. NOTE: More information and/or a copy of the guideline can be obtained from: American National Standards Institute 25 West 43rd Street 4th Floor New York, NY 10036 Tel: 212-642-4900 www.ansi.org |
| --- | --- |

## Barcode Placement

| Barcode Location: | The barcode shall be printed on the front side of the mailer pallet label. A clear zone of at least 0.25” shall be observed directly to the left and right of the barcode. No text, images, or other markings shall appear in this area. A vertical clear zone of at least 0.125” shall be observed directly above and below the barcode. No text, images, or other markings shall appear in this area. |
| --- | --- |

## Barcode Data Constructs

Two distinct data constructs are permitted.  Both formats are 21-characters in length and will require mailers to encode their respective USPS-assigned Mailer ID.  The length of the mailer’s Mailer ID (6 or 9 digits) will dictate which format to follow.  Contact your USPS account representative or the PostalOne! helpdesk at (800) 522-9085 if you have not yet been assigned a Mailer ID or have other questions.

| 6-digit Mailer ID Format |
| --- |
| Field No. | Field Description | Field Size | Character Position | Logical Values | Allowable Values |
| 1 | Application Identifier | 2 | 1-2 | Numeric | “99” (Only) |
| 2 | Type Indicator | 1 | 3 | Alpha | “M” (Only) |
| 3 | Mailer ID | 6 | 4-9 | Numeric | USPS-assigned ID with the leading digit ranging from “0” through “8” |
| 4 | Serial Number | 12 | 10-21 | Alphanumeric | Mailer-defined (1) |

(1)  NOTE:  The Serial Number field shall be padded with leading “-“ characters or dashes (ASCII value 0045) if the mailer-defined value is less than the required 12 characters.  For example, if the mailer opts for a container identifier of “123456”, a value of “------123456” should be encoded.

| 9-digit Mailer ID Format |
| --- |
| Field No. | Field Description | Field Size | Character Position | Logical Values | Allowable Values |
| 1 | Application Identifier | 2 | 1-2 | Numeric | “99” (Only) |
| 2 | Type Indicator | 1 | 3 | Alpha | “M” (Only) |
| 3 | Mailer ID | 9 | 4-12 | Numeric | USPS-assigned ID with the leading digit being “9” |
| 4 | Serial Number | 9 | 13-21 | Alphanumeric | Mailer- defined (2) |

(2)  NOTE:  The Serial Number field shall be padded with leading “-“ characters or dashes (ASCII value 0045) if the mailer-defined value is less than the required 9 characters.  For example, if the mailer opts for a container identifier of “123456”, a value of “---123456” should be encoded.

## Barcode Examples

Figure 1 - 6-digit Mailer ID Barcode

Figure 2 - 9-digit Mailer ID Barcode

# Text boxes

- 10-point or larger

- Bold sans-serif font

- Centered below barcode

- 10-point or larger

- Bold sans-serif font

- Centered below barcode

- 12-point or larger

- Bold sans-serif font

- Centered above barcode

- Two spaces between fields

- Serial number padded with dashes

- 0.125” minimum clearance

- Not more than 0.5”

- 0.125” minimum clearance

- Not more than 0.5”

- 12-point or larger

- Bold sans-serif font

- Centered above barcode

- Two spaces between fields

- Serial number padded with dashes

- 0.125” minimum clearance

- Not more than 0.5”

- 0.125” minimum clearance

- Not more than 0.5”

- Two spaces between fields

- Serial number padded with dashes

- 0.125” minimum clearance

- Not more than 0.5”

- 10-point or larger

- Bold sans-serif font

- Centered below barcode

- 12-point or larger

- Bold sans-serif font

- Centered above barcode

- 0.125” minimum clearance

- Not more than 0.5”