Fermilab Particle Physics Division/CDF Upgrade Project

Specification for

TRACER_LITE

Theresa M. Shaw

8/24/99

TRACER LITE Differences from TRACER

The TRACER LITE is a 6U version of the TRACER.  It is reduced in functionality as well as size.

The TRACER LITE will NOT provide Clock signals and clock gates to the backplane

The TRACER LITE will NOT provide Trigger signals to the backplane.

The TRACER LITE will NOT provide any Local Calibration control.

The TRACER LITE wil NOT provide onboard Flash RAM for any constants storage.

The TRACER Lite will NOT provide a path to a Transition module or to the TBUS lines of the backplane.

# Important Modifications to Memory Map

The memory map of TRACER LITE was kept identical to the TRACER; but, be aware that many of the registers used for deleted functionality will now have no purpose.

The TRACER LITE is hardwired with a logical address of:

A31 - high

A30 - low

A29 - low

A28 - low

A27 - low

Also be aware, that the FIFO flags of TRACER LITE are different from that of the TRACER.  The TRACER used a Cypress CY7C470 FIFO which is now obsolete.  The TRACER LITE uses a Cypress CY7C260A FIFO.

1.0 Introduction

The TRigger And Clock + Event Readout Module (TRACER) performs the role of system interface for the front end crates to the rest of the  upgraded CDF system.  It will be assumed that the reader is familiar with the readout system described in CDF/DOC/TRIGGER/CDFR/2288 “A Standard Front-End and Trigger VMEbus Based Readout Crate for the CDF Upgrade - The CDF Readout Crate”.

One of the TRACER's functions is to provide an interface to the Master Clock.  The TRACER is used to fanout the precision 132ns clock and three clocking gates: Beam Zero, Beam Crossing, and Abort. The TRACER does this by driving the signals it receives from the Master Clock onto the CDF custom backplane where they are then readily available to all modules plugged into the crate.  No timing adjustment is done to any signals from the Master Clock.  Any custom tuning of the arrival of the signals will be done in the Clock Fanout Modules.

A second TRACER function is to provide an interface to the Trigger System Interface (TSI).  The TRACER is used to fanout all trigger and control information received from the TSI.  The TRACER receives encoded information from an optical link, decodes it and passes it onto the CDF custom backplane. These signals are used by the ADMEMs and other front-end modules to either  pass an event fragment into one of four Level 2 readout buffers or to throw it away.

The TRACER also provides a path for sending the event data to the VMEbus Readout Boards (VRBs).  Event data may be transmitted in two ways: the TRACER may act as a "spy" on the backplane and place backplane data into its Event FIFO, or it can receive data written directly into its Event FIFO from the VRC (VME Readout Controller).  Once data exists in the Event FIFO,  a sequencer onboard the TRACER will readout the event data, serialize it and then transmit the data to the VRB modules over fiber optic cables.  The VRB will transmit the signal VRB_BUSY back to the TRACER if at any time it cannot accept the next event.  If VRB_BUSY is detected by the TRACER, data transmission will be held off until the condition clears.

Finally,  the TRACER provides a means by which to issue a crate reset.  The VMEbus signal SYSRESET* will be pulsed low on the backplane if a reset pulse is detected from the CDF Reset Crate.  An RS-422 signal is sent from the Reset Crate to a TRACER front panel connection if a crate reset is desired.  A crate reset ability is required in the event of a CPU board hanging.  NOTE that this reset ability is separate from the TSI CDF_RECOVER~ signal which serves to reset L1 pipeline pointers.

Figure 1 provides a system overview and shows where the TRACER fits in.  Figure 2 provides a block diagram of the TRACER.

Figure 1.  Block Diagram of Calorimetry DAQ System

Figure 2  Block Diagram of Trigger Fanout/Crate Monitor/Spy Module

2.0 Interface to the Master Clock

The TRACER provides a front panel connection to receive a cable from the Master Clock.  The Master Clock will provide the precisely timed 132 ns clock signal as well as gates which indicate the Beam Zero Crossing, Beam Crossing and Abort Gaps.  The Master Clock signals are received as differential LVDS signals.  The TRACER will provide a 100 ohm terminating input resistor for each of the signals.  A 8-pin Shielded Data Link style connector will be provided to receive the cable from the Master Clock (see Appendix C).  The shield of this connector will not be connected to the TRACER’s digital ground.  The front panel connector pinout will be as follows:

Pin	Signal

1	Master_Clock		(132 ns clock)

2	Master_Clock*

3	Beam_Crossing

4	Beam_Crossing*

5	Beam_Zero		(once around marker)

6	Beam_Zero*

7	Abort_Gap

8	Abort_Gap*

The TRACER will receive these signals and drive the following backplane signals:

CDF_CLK

CDF_CLK* 	- 132 ns clock; accurately timed differential PECL signal delivered by the Master Clock.

CDF_CLK is the only precisely timed signal.  All other signals are considered gates to the rising edge of CDF _CLK.  All CDF backplane signals are guaranteed to be valid for 10ns on either side of the rising edge of CDF_CLK.

CDF_BC*	- Beam Crossing (TTL)

CDF_B0*	- Bunch 0 (TTL)

CDF_ABORT*	- Abort Gap (TTL)

The TRACER will simply buffer these signals to the backplane - No timing adjustments will be done.  CDF_B0~, CDF_BC~ and CDF_ABORT~ are active low gates to the rising edge of the CDF_CLK signal.  They are guaranteed to have at least a 10 ns setup (see Figure 3) and hold time with respect to the clock edge.

Figure 3. Backplane Timing Example of CDF_CLOCK and a Clock Gate

3.0 Interface to Trigger System Interface(TSI)

3.1 TSI <-> TRACER Optic Link

The TRACER will provide an interface to the TSI.  An optical link using TAXIchip (AM7969-175JC)  protocol, AMP optical receivers (AMP 269050-1),  and operating at two times the CDF_CLK,  provides the means for the TSI to issue commands.  The TRACER will take the signals that it receives from the TSI, decode them and drive the appropriate trigger signals out onto the custom CDF VMEbus backplane.  The TSI <-> TRACER protocol is described in the note "Trigger Supervisor Protocols for Run II" written by the CDF Group of Yale University.

The following backplane trigger signals will be driven by the TRACER as the result of TSI commands:

FROM TSI			Backplane Signal driven by TRACER

L1 Word	bit 2		CDF_L1A*		- Level 1 Accept

bit 3		CDF_L1R*		- Level 1 Reject						bit 4		CDF_L2B0*		- Level 1 Accept Buffer Address 0

bit 5		CDF_L2B1*		- Level 1 Accept Buffer Address 1

bit 6		CDF_GLIVE*		- Level 1 Accept corresponds to live Beam

Crossing

bit 7		CDF_L1_CALIB*	- Indicates L1A event is from a Calibration

bit 8		RSVD_L1W2*		- TSI reserved L1 word bit(8)

L2 Word	bit 2		CDF_L2DB0*		- Level 2 Accept Decision Buffer Address 0

bit 3		CDF_L2DB1*		- Level 2 Accept Decision Buffer Address 1

bit 4		CDF_L2A_EN*		- Level 2 Accept Enable signal

bit (8:5)		CDF_EVID(3:0)*	- Event Identifier(0)

Calib Word	bit (8:2)		CDF_CALIB(6:0)*	- Calibration bits which may be sent by TSI;  							   these currently have no definition

Control Word	bit 2		CDF_STOP*		- Set Halt Condition

bit 3		CDF_RECOVER*	- Reset FIFOs/pipelines

bit 4		CDF_TEST*		- Diagnostic bit which will cause TRACER 								   to capture TAXI link (TSI <-> TRACER) 							   data

bit 5		CDF_RUN*		- Clear Halt Condition

bit (8:6)		CDF_RL(2:0)*		- Readout List Identifier

(the following signals are generated by TRACER using above TSI info)

CDF_HALT*		- Halt filling L1 FIFO/pipelines

- the HALT condition is set by CDF_STOP* and cleared by CDF_RUN*

CDF_CALEN*		- Calibration Enable

- this is set whenever a TSI Calibration Word is received

CDF_L2A*		- Level 2 Accept

- this is set whenever a TSI L2 Word is recieved and CDF_L2A_EN* is true

CDF_L2R*		- Level 2 Reject

- this is set whenever a TSI L2 Word is recieved and CDF_L2A_EN* is false

All of the above signals are gates to the rising edge of the CDF_CLK signal.  They are guaranteed to have at least a 10 ns setup and hold time with respect to the clock edge.

3.2  The Start Scan and Done Registers

The TRACER will also provide Start Scan and Done Registers which will be used in communications protocol with the TSI.  When the TSI indicates it is time to read out an event (Start Event Scan), the “Start Scan” bit will be set in the TRACER’s Start Scan Register.

The VMEbus Readout Controller (VRC) can poll this register and begin readout when it sees the Start Scan bit set, or an interrupt mode may be enabled by setting the “Interrupt Mode Enable” bit of the TRACER’s Control Register.  Interrupt mode causes the TRACER to initiate an Interrupt cycle upon the reception of Start Scan.

When the VRC has finished its readout cycle, it will write to the Done Register and set the “Done” bit.  The “Done” bit is cleared upon the reception of the next Start Scan.

Start Scan Register

Description:   Event tagging data for this register comes from the TSI “Level 2” word.

The “Start Scan” bit is set when a L2 Accept is indicated, and cleared when the “Done” bit is set in the Done Register.

Bit 16 reflects the state of the open-collector backplane signal CDF_TDC_DONE.

Bit	Function

0-15	Undefined

16	CDF_TDC_DONE

19-17	Undefined

20	Readout List 0

21	Readout List 1

22	Readout List 3

23	Undefined

24	Start Scan

25	L2 Decision Buffer Address 0

26	L2 Decision Buffer Address 1

27	Undefined

28	Event ID 0

29 	Event ID 1

30	Event ID 2

31	Event ID 3

Done Register

Description:  The Done bit can be set to a logic high by the VRC, over VMEbus, when readout is complete.  The VMEbus path does not allow the bit to be set to a logic low.  The Done bit will also be set to a logic high by the “recover” command in the event of a Halt-Recover-Run sequence.

The Done bit will be set to a logic low with the issuance of a new Start Event Scan command by the TSI.

The End of Block(EOB) maker may be written over VMEbus.  When it is set, it will cause an EOB to be appended to the data in the Event FIFO.  It is a self-clearing bit and cannot be read back.  The EOB marker is an optional feature - its usage is optional.

Done and EOB have been placed in the same register in order to reduce the number of VMEbus cycles which the VRC must do at the end of a readout cycle.  Typical usage would have the VRC set both Done and EOB at the end of a readout cycle.  However, if an “early” done is sent to the TSI, the EOB marker could be sent later, after the data has been transferred to the Event FIFO.

Bit	Function

23-0	Undefined

24	Done (VMEbus can set DONE when bit 24 equals “1”,

no reset capability over VMEbus)

30-25	Undefined

31	End of Block (EOB) (write only - self clearing bit)

3.3 DONE, ERROR and BUSY Signals

TSI <-> TRACER protocol also relies on a parallel copper link which will allow the TRACER to drive the signals DONE, ERROR and BUSY to the TSI.

The DONE signal is simply the buffered “Done” bit in the Done Register.

The ERROR signal will be asserted whenever some module in the CDF Crate is asserting CDF_ERROR~ on the open-collector backplane signal.  The assertion of ERROR is meant to occur only in the case of a catastrophic error.  It is possible to mask ERROR with a bit in the control register.

The BUSY signal can be asserted to two different ways.  The default is to have the TRACER return BUSY to the TSI whenever the Event FIFO status flags indicate that the FIFO is greater than half full.

Alternatively, the BUSY signal can be asserted whenever the buffer space in the VRB (CDF's VMEbus Readout Board) becomes full by setting the Bit 0 of the Control Register.  A direct optical link between the VRB and the TRACER, informs the TRACER when the higher level DAQ readout has become clogged.

This BUSY signal will not be cleared with a Halt-Recover-Run sequence.  In order to clear BUSY, the problem with the status of the Event FIFOs or with the clogged VRB readout buffers must be fixed.

An eight pin Shielded Modular Data Link Connectors (see Appendix C) will be provided on the TRACER’s Front Panel.  The shield of this connector will be connected to the TRACER’s digital ground.  The conncector has the following pinout:

Pin	Signal

1	DONE

2	DONE~

3	ERROR

4	ERROR~

5	BUSY

6	BUSY~

7	NC

8	NC

3.4  TEST Mode

It is possible for the TSI to turn on input to the TSI Diagnostic FIFO by sending the “TEST” bit in the TSI Control Word.  When “TEST” is sent, the FIFO is flushed and the next 8K data words received from the TSI are clocked into a FIFO.  In its this operating mode, once the FIFO is full, no further data recording will be done.  In order to repeat the test, the original “TEST” state must be cleared by toggling the “Reset TSI Diagnostic FIFO TEST mode” bit in the Control Register.

A second diagnostic mode possible - it will, however, be overriden by any “TEST” message written from the TSI.  In the second mode, it is possible to save the last ~8K of TSI commands by setting the “Enable TSI Diagnostic FIFO Save Mode” bit of the Control Register.  When this bit is set the TSI Diagnostic FIFO will be filled by incoming TSI commands.  As the FIFO limit is approached,  automatic readout is begun to clear space for new commands.  If at any time a CDF_ERROR* condition occurs, the state of the FIFO will be frozen. Hopefully, this will aid in determining what was going on in the crate at the time of the error.

4.0 Data Transmission

The TRACER has an optical data link to the VRB.  This link uses the TAXIchip (AM7968-175JC) protocol and AMP optical driver (AMP 269049-1).  It operates at two times the CDF_CLK.

An 8K by 32 bit Event FIFO feeds this data link.  It is possible to fill this Event FIFO in two ways.  One way is to simply do a VMEbus write into the FIFO.  If the VRC is used to do zero suppression and data formatting, this method would be used.  The VRC would first read in raw event data, do the formatting and then write the formatted data to the Event FIFO.

A second method for getting event data to the VRB would involve using the TRACER's Spy capability.  The TRACER will have the capability to spy on the data as the VMEbus Readout Controller (VRC) reads it out.  During event readout, the TRACER has the ability to clock data into the Event FIFO.  The data which gets clocked into the event FIFO includes any VMEbus reads of data in the L2 Buffer Space (specified in CDF/DOC/TRIGGER/CDFR/2288), and any write to the TRACER’s Done Register which sets the EOB marker.  This Spy mode would be used only if there is no need for the VRC to do data formatting.

A sequencer on the TRACER will detect when data is present in the FIFO, serialize the data through the use of a TAXIchip, and transmit it upstairs to the Readout Memory (VRB) module via an optical link.  The data can be transmitted to the VRB at a rate of up to one byte every 66 ns (twice the CDF clock).  A Taxi Sync signal is sent up at least every 5 bytes;  thus,  a data rate of 4 Bytes/(5 x66ns), or 12.1 MB/s is achievable out of the crate.

It is possible to append set an End of Block (EOB) marker on the transmitted data stream.  This is done by writing to the EOB bit in the Done register.  Whenever a logic high is written to this bit,  the equivalent of a 33 bit word will be clocked into the Event FIFO.  The most significant bit will be set high and will indicate the EOB.  This EOB bit will be passed to the TaxiChip as the 9th data bit, which can then be decoded as EOB by the VRB.

5.0 Event Data Header Information

The TRACER will have registers to hold header information which should be applied to all event fragments which are transmitted to the VRB.  The following header information should mark all events:

Word Count		(32 bits)	;downloaded from system or calculated by 							 VRC

Partition ID		(3 bits)		;downloaded from system

Crate ID		(8 bits)		;downloaded from system

Event ID		(4 bits)		;obtained from TSI

L2 Buffer Address	(2 bits)		;obtained from TSI

Readout List #		(3 bits)		;obtained from TSI

Calibration Type #	(6 bits)		;obtained from TSI

The Word Count will be used by the VRB as a way of identifying Event fragments as they pass through it.

This header information can get into the Event FIFO in two ways.  If the VRC is doing event formatting and transmitting the formatted event to the TRACER's Event FIFO, the VRC should apply the header to the formatted data.  In this case, the VRC would need to be told the Partition ID and Crate ID at start-up.  The rest of the header information would be available to the VRC through (1) reading the Start Scan register which is being polled in order to know when to initiate Event readout or (2) reading the Start Scan register upon receiving a Start Scan interrupt if  interrupt mode is enabled.

In the case where the TRACER is in spy mode, and directly stores the raw event data into its Event FIFO, it is necessary to include the TRACER word count and header Registers in the beginning of the readout list.  As they are read out, they will be written into the Event FIFO like all other Event data.

Word Count Register

Description:  this register contains the number of 32 bit words (inclusive) which make up the event fragment.  It must be downloaded if "Spy" mode is used.

Bit	Function

31-0	Word Count(31:0)

Event Header Register

Description:  this register contains the minimum amount of information which must be applied as a header to all event fragments read out into L3.

Bit	Function

7-0	Crate ID(7:0) (r/w)

10-8	Partition ID(2:0) (r/w)

11-15	Undefined

19-16	Event ID(3:0) (r)

21-20	L2 Buffer Address(1:0) (r)

24-22	Scan List #(2:0) (r)

31-25	Calibration #(6:0) (r)

It may also be desirable to mark the end of an event.  To do this we could repeat the Word Count and Event Header information.  Two possible pattern words of A’s and 5’s will also be available as tags to be added to these words to aid in the descrambling of event blocks.

6.0 Reset Function

It is necessary to provide a remote reset capability for front end VMEbus crates. The main purpose of the reset will be to reboot a CPU which has hung. This will be done through the use of a dedicated reset line which will come in through a front panel connector and be driven by the CDF Reset Crate.

The reset signal will be driven and received as an RS-422 signal.  When the reset line is pulsed low it will drive the SYSRESET* line low on the VMEbus backplane.  This will cause all boards to do a reset.

7.0  TRACER Interrupt Mode

The TRACER has an interrupt feature which may be used to indicate that a Start Event Scan message has been received.  The enabling of this interrupt mode is controlled via the “Interrupt Mode Enable” bit of the TRACER’s Control Register.  The interrupt feature is provided as an alternative method to the polling of the Start Event Scan Register.

The Interrupt Level is settable via switches on board, and the set level is readable through the Control Register.

A separate Interrupt Return Vector Register will allow the user to set the interrupt return vector.

8.0 TRACER Front Panel

The TRACER Front Panel will contain the following LED indicators:

+5V			;LED (red) on when module is powered

Module Select	;LED (green) on during VMEbus access

TSI_DONE		;LED (green) on when DONE is being returned to TSI

TSI_ERROR		;LED (red) on when ERROR is being returned to TSI

TSI_BUSY		;LED (yellow) on when BUSY is being returned to TSI

The TRACER Front Panel will also hold

8-pin Shielded Data Link connector for TSI return signals

Connector Ground Shield connected to Board Ground

8-pin Shielded Data Link connector to receive Master Clock Signals

Connector Ground Shield not connected to Board Ground

An optical cable receiver for TSI TAXI-protocol data

An optical cable driver for data link to VRB

An optical cable receiver for the Busy signal from the VRB

An 8-pin module jack to receive a reset signal from the CDF RESET Crate

No ground shield

Two 34 pin headers to spy on the special CDF backplane signals (see Table2)

Logic Analyzer Port - On the TRACER

Tracer Front Panel Ports J will provide ports for easy access to the CDF backplane trigger and clock signals.  These ports will bring TTL level signals to four 20 pin right angle box headers on the  front panel.  The ports can be used by a wide range of oscilloscopes or logic analyzers, but are specifically designed for ease of use with HP logic analyzers and the HP Terminator Adapter.

Hewlett Packard Pinout on Terminator Adapter (HP part number 01650-63203)

| Pin | Signal | Pin | Signal |
| --- | --- | --- | --- |
| 20 | GND | 19 | D0 |
| 18 | D1 | 17 | D2 |
| 16 | D3 | 15 | D4 |
| 14 | D5 | 13 | D6 |
| 12 | D7 | 11 | D8 |
| 10 | D9 | 9 | D10 |
| 8 | D11 | 7 | D12 |
| 6 | D13 | 5 | D14 |
| 4 | D15 | 3 | CLK1 |
| 2 | CLK2 | 1 | +5V |

CDF Signals are connected to the Port as follows:

Port J4 - POD 1

| Pin | Signal | Pin | Signal |
| --- | --- | --- | --- |
| 20 | GND | 19 | CDF_L2R* |
| 18 | CDF_L2DB0* | 17 | CDF_L2DB1* |
| 16 | CDF_EVID0* | 15 | CDF_L2_EN* |
| 14 | CDF_EVID2* | 13 | CDF_EVID1* |
| 12 | CDF_STOP1* | 11 | CDF_EVI31* |
| 10 | CDF_TEST1* | 9 | CDF_RECOVER* |
| 8 | CDF_RL0* | 7 | CDF_RUN* |
| 6 | CDF_RL2* | 5 | CDF_RL1* |
| 4 | CDF_HALT* | 3 | CDF_CLOCK |
| 2 | No Connect | 1 | No Connect |

Port J5 - POD 2

| Pin | Signal | Pin | Signal |
| --- | --- | --- | --- |
| 20 | GND | 19 | CDF_CLOCK* |
| 18 | CDF_ABORT* | 17 | CDF_B0* |
| 16 | CDF_BC* | 15 | CDF_L1A* |
| 14 | CDF_L1R* | 13 | CDF_L2B0* |
| 12 | CDF_GLIVE* | 11 | CDF_L2B1* |
| 10 | CDF_L1RSVD* | 9 | CDF_CALIB* |
| 8 | CDF_CAL0* | 7 | CDF_CALEN* |
| 6 | CDF_CAL2* | 5 | CDF_CAL1* |
| 4 | CDF_L2A* | 3 | CDF_CLOCK |
| 2 | No Connect | 1 | No Connect |

9.0 Power Requirements

The TRACER uses approximately 5Amps @ 5V for a power consumption of 25 Watts.

10.0 VMEbus Slave Interface

The TRACER will implement a modified version of a VMEbus slave interface.  Only 32 bit aligned data transfers will be supported; these may be either single word transfers or block transfers.  Only extended (32-bit) addressing modes will be supported.  All boards will be assigned a unique geographical address through use of backplane pins on the CDF Custom J2 backplane.  The TRACER will respond to all address spaces.  Therefore, TRACER modules will respond to the following address modifier codes:  09, and 0B.

Memory Map

YY00 0000	Diagnostic Register (32 bit Read/Write) (r/w)

YY00 0004   	Control Register

Please Note all reset lines must be toggled by the user - they are not self-clearing.

Bit	Function

0	Select VRB busy as Trigger System Return Busy source (r/w)

default state - low

0 - TS Busy will be derived from Event FIFO status

1 - TS Busy will be derived from VRB busy

- Undefined

- Undefined

- Undefined

6-4	Interrupt Level (2:0) (r)

allows readback of the Jumper settings of the interrupt level

7	Error (r)

reflects the active state (inverted) of  CDF_ERROR* on the 					backplane

8	VRB Busy (r)

reflects the state of VRB_Busy signal coming from the VRB

9	TSI Diagnostic FIFO FF~ (r) (Full Flag)

10	TSI Diagnostic FIFO EF~ (r) (Empty Flag)

11	TSI Diagnostic FIFO HF~ (r) (Half Full Flag)

12	TSI Taxi Error (r)

TaxiChip violation has been detected

13	Event FIFO FF~ (r) (Full Flag)

14	Event FIFO EF~ (r) (Empty Flag)

15	Event FIFO HF~ (r) (Half Full Flag)

16	Undefined

17 	Enable TBUS Divers (r/w)

default state - low

set high to drive output of TBUS Register onto Backplane (P0) TBUS lines

18	Reset the Event FIFO (r/w)

default state - low

toggle hi-lo to clear the Event FIFO

19	Reset the TSI TaxiChip Receiver (r/w)

default state - low

toggle hi-lo to reset TaxiChip

20	Reset the Event Data TaxiChip Transmitter (r/w)

default state - low

toggle hi-lo to reset TaxiChip

21	Enable TSI Diagnostic FIFO Save Mode (r/w)

default state - high

when set, TSI Diagnostic FIFO will save last 8K TSI commands

22 	Reset TSI Diagnostic FIFO “TEST” mode (r/w)

default state - low

toggle hi-lo to reset “TEST” message from TSI

23	Reset TSI Diagnostic FIFO (r/w)

default state - low

toggle hi-lo to reset the TSI Diagnostic FIFO

24	Reset TSI Taxi Error (r/w)

default state - low

toggle hi-lo to clear TSI Taxi violation error state, and reset the 					TSI TAXI Violation Counter Register

25 	Undefined

26  	Select CDF Trigger Signal source (r/w)

default state - low

0 - TSI Interface

1 - Local Calibration Sequencer

27  	Interrupt Mode Enable (r/w)

default state - low

when set, enables interrupts when Start Event Scan received from 					TSI

28	Mask CDF_ERROR (r/w)

default state - low

when set, will mask out any errors being sent to the TSI

29	Event Data Taxi Enable (r/w)

default state - high

when set, the onboard sequencer will begin reading out the Event 					FIFO and streaming the data to the VRB

30	Spy Mode Enable (r/w)

default state - low

when set, L2 buffer space data will be captured from the backplane 					and put into the Event FIFO

31	Software Reset (r/w)

default state - low

resets TSI interface registers

YY00 0008	Start Scan Register (r)

Bit	Function

0	Calibration 0

1	Calibration 1

2	Calibration 2

3	Calibration 3

4	Calibration 4

5	Calibration 5

6	Calibration 6

15-7	Undefined

16	CDF_TDC_DONE

19-17	Undefined

20	Readout List 0

21	Readout List 1

22	Readout List 3

23	Undefined

24	Start Scan

25	L2 Decision Buffer Address 0

26	L2 Decision Buffer Address 1

27	Undefined

28	Event ID 0

29 	Event ID 1

30	Event ID 2

31	Event ID 3

YY00 000C	Done Register (r/w)

Bit	Function

23-0	Undefined

24	Done (VMEbus can set DONE when bit 24 equals “1”,

no reset capability over VMEbus)

30-25	Undefined

31	End of Block (EOB) (write only - self clearing bit)

YY00 0024	Interrupt Return Vector Register (32 bit Read/Write) (r/w)

YY10 0000 - YY10 007C	ID PROM (upper 8 bits) (r)

YY40 XXXX 		TSI_Diagnostic FIFO (r)

bits (31:23) represent Taxi bits (8:0)

(holds first 8K data words sent down TSI optic link after 					the receipt of the TEST signal)

YY50 XXXX		Event Data FIFO (r/w)

YY80 0000 	Word Count Register (r/w)

Bit	Function

31-0	Count of 32 bit Words in Event Record

YY80 0004	Event Header Register

Bit	Function

7-0	Crate ID(7:0) (r/w)

10-8	Partition ID(2:0) (r/w)

11-15	Undefined

19-16	Event ID(3:0) (r)

21-20	L2 Buffer Address(1:0) (r)

24-22	Scan List #(2:0) (r)

31-25	Calibration #(6:0) (r)

YY80 0008	TSI TAXI Violation Counter Register

YY80 000C	A’s Pattern Register (r)

This word will contain (hex)AAAAAAAA

YY80 0010	5’s Pattern Register (r)

This word will contain (hex)55555555