Bay Area Air Quality Management District

939 Ellis Street

San Francisco, CA  94109

(415) 771-6000

# Proposed

# Major Facility Review Permit

# Issued To:

# USS-POSCO Industries

# Facility #A2371

# Facility Address:

# 900 Loveridge Road

# Pittsburg, CA  94565

# Mailing Address:

# P. O. Box 471

# Pittsburg, CA  94565

Responsible Official 	Facility Contact

Sal S. Sbranti, Vice President	Dave Allen, Regulations Manager

Operations Environmental & Technology

925-439-6513	925-439-6290

Type of Facility:	Production of Rolled Steel Product	BAAQMD Contact:

Primary SIC:	3312	Donald P. Van Buren, PE

Product:	Steel coils finished by pickling, cold-rolling, tempering, annealing,

tin-plating, and/or galvanizing

# ISSUED BY THE BAY AREA AIR QUALITY MANAGEMENT DISTRICT

William C. Norton, Executive Officer/Air Pollution Control Officer		Date

# TABLE OF CONTENTS

I.	STANDARD CONDITIONS	3

II.	EQUIPMENT	7

III.	GENERALLY APPLICABLE REQUIREMENTS	18

IV.	SOURCE-SPECIFIC APPLICABLE REQUIREMENTS	20

V.	SCHEDULE OF COMPLIANCE	57

VI.	PERMIT CONDITIONS	57

VII.	APPLICABLE LIMITS & COMPLIANCE MONITORING REQUIREMENTS	96

VIII.	TEST METHODS	128

IX.	PERMIT SHIELD	131

X.	GLOSSARY	132

XI.	APPLICABLE STATE IMPLEMENTATION PLAN	139

# STANDARD CONDITIONS

## Administrative Requirements

The permit holder shall comply with all applicable requirements in the following regulations:

BAAQMD Regulation 1 - General Provisions and Definitions

(as amended by the District Board on 5/2/01);

SIP Regulation 1 - General Provisions and Definitions

(as approved by EPA through 6/28/99);

BAAQMD Regulation 2, Rule 1 - Permits, General Requirements

(as amended by the District Board on 8/1/01);

SIP Regulation 2, Rule 1 - Permits, General Requirements

(as approved by EPA through 1/26/99);

BAAQMD Regulation 2, Rule 2 - Permits, New Source Review

(as amended by the District Board on 5/17/00);

SIP Regulation 2, Rule 2 - Permits, New Source Review and Prevention of Significant Deterioration

(as approved by EPA through 1/26/99);

BAAQMD Regulation 2, Rule 4 - Permits, Emissions Banking

(as amended by the District Board on 5/17/00);

SIP Regulation 2, Rule 4 - Permits, Emissions Banking

(as approved by EPA through 1/26/99); and

BAAQMD Regulation 2, Rule 6 - Permits, Major Facility Review

(as amended by the District Board on 4/16/03).

## Conditions to Implement Regulation 2, Rule 6, Major Facility Review

This Major Facility Review Permit was issued on [          ] and expires on [when issued, enter 5th anniversary of issue date].  The permit holder shall submit a complete application for renewal of this Major Facility Review Permit no later than [when issued, enter date 6 months prior to permit expiration date] and no earlier than [when issued, enter date 12 months prior to expiration date].  If a complete application for renewal has not been submitted in accordance with this deadline, the facility may not operate after  [when issued, enter 5th anniversary of issue date].  (Regulation 2-6-307, 404.2, & 409.6; MOP Volume II, Part 3, §4.2)

The permit holder shall comply with all conditions of this permit.  The permit consists of this document and all appendices.  Any non-compliance with the terms and conditions of this permit will constitute a violation of the law and will be grounds for enforcement action; permit termination, revocation and re-issuance, or modification; or denial of a permit renewal application.  (Regulation 2-6-307; MOP Volume II, Part 3, §4.11)

In the event any enforcement action is brought as a result of a violation of any term or condition of this permit, the fact that it would have been necessary for the permittee to halt or reduce the permitted activity in order to maintain compliance with such term or condition shall not be a defense to such enforcement action. (MOP Volume II, Part 3, §4.11)

This permit may be modified, revoked, reopened and reissued, or terminated for cause.  (Regulation 2-6-307, 409.8, 415; MOP Volume II, Part 3, §4.11)

The filing of a request by the facility for a permit modification, revocation and re-issuance, or termination, or the filing of a notification of planned changes or anticipated non-compliance does not stay the applicability of any permit condition.  (Regulation 2-6-409.7; MOP Volume II, Part 3, §4.11)

This permit does not convey any property rights of any sort, or any exclusive privilege.  (Regulation 2-6-409.7; MOP Volume II, Part 3, §4.11)

The permit holder shall supply within 30 days any information that the District requests in writing to determine whether cause exists for modifying, revoking and reissuing, or terminating the permit or to determine compliance with the permit.  (Regulation 1-441, Regulation 2-6-409.4 & 501; MOP Volume II, Part 3, §4.11)

Any records required to be maintained pursuant to this permit that the permittee considers to contain proprietary or trade secret information shall be prominently designated as such.  Copies of any such proprietary or trade secret information which are provided to the District shall be maintained by the District in a locked confidential file, provided, however, that requests from the public for the review of any such information shall be handled in accordance with the District's procedures set forth in Section 11 of the District’s Administrative Code.  (Regulation 2-6-419; MOP Volume II, Part 3, §4.11)

Proprietary or trade secret information provided to EPA will be subject to the requirements of 40 CFR Part 2, Subpart B - Public Information, Confidentiality of Business Information.  (40 CFR Part 2)

The emissions inventory submitted with the application for this Major Facility Review Permit is an estimate of actual emissions or the potential to emit for the time period stated and is included only as one means of determining applicable requirements for emission sources.  It does not establish, or constitute a basis for establishing, any new emission limitations.  (MOP Volume II, Part 3, §4.11)

The responsible official shall certify all documents submitted by the facility pursuant to the major facility review permit.  The certification shall state that based on information and belief formed after reasonable inquiry, the statements and information in the document are true, accurate, and complete.  The certifications shall be signed by a responsible official for the facility. (MOP Volume II, Part 3, §4.11)

## Requirement to Pay Fees

The permit holder shall pay annual fees in accordance with District Regulation 3, including Schedule P.  (Regulation 2-6-402 & 409.13, Regulation 3; MOP Volume II, Part 3, §4.12)

## Inspection and Entry

Access to Facility:  The permit holder shall provide reasonable access to the facility and equipment that is subject to this permit to the APCO and/or to his or her designee.  (Regulation 1-440, Regulation 2-6-409.3; MOP Volume II, Part 3, §4.14)

## Records

1.	The permit holder must provide any information, records, and reports requested or specified by the APCO.  (Regulation 1-441, Regulation 2-6-409.4)

2.	Notwithstanding the specific wording in any requirement, all records for federally enforceable requirements shall be maintained for at least five years from the date of creation of the record.  (Regulation 2-6-501, Regulation 3; MOP Volume II, Part 3, §4.7)

## Monitoring Reports

Reports of all required monitoring must be submitted to the District at least once every six months, except where an applicable requirement specifies more frequent reporting. The first reporting period for this permit shall be [date of issuance] to [six months later].  The report shall be submitted by [one month after end of reporting period].  Subsequent reports shall be for the following periods:  [_____ 1st through ______ 30th or 31st] and [_____ 1st through ______ 30th or 31st], and are due on the last day of the month after the end of the reporting period.  All instances of non-compliance shall be clearly identified in these reports.  The reports shall be certified by the responsible official as true, accurate, and complete.  In addition, all instances of non-compliance with the permit shall be reported in writing to the District’s Compliance and Enforcement Division within 10 calendar days of the discovery of the incident.  Within 30 calendar days of the discovery of any incident of non-compliance, the facility shall submit a written report including the probable cause of non-compliance and any corrective or preventative actions. The reports shall be sent to the following address:

Director of Compliance and Enforcement

Bay Area Air Quality Management District

939 Ellis Street

San Francisco, CA 94109

Attn:  Title V Reports

(Regulation 2-6-502, Regulation 3; MOP Volume II, Part 3, §4.7)

## Compliance Certification

Compliance certifications shall be submitted annually by the responsible official of this facility to the Bay Area Air Quality Management District and to the Environmental Protection Agency.  The certification period will be _______ 1st to ________ 30th or 31st.  The certification shall be submitted by _______ 30th or 31st of each year.  The certification must list each applicable requirement, the compliance status, whether compliance was continuous or intermittent, the method used to determine compliance, and any other specific information required by the permit.  The permit holder may satisfy this requirement through submittal of District-generated Compliance Certification forms.  The certification should be directed to the District’s Compliance and Enforcement Division at the address above, and a copy of the certification shall be sent to the Environmental Protection Agency at the following address:

# Director of the Air Division

USEPA, Region IX

75 Hawthorne Street

San Francisco, CA   94105

Attention:  Air-3

(MOP Volume II, Part 3, §4.5 and 4.15)

## Emergency Provisions

- The permit holder may seek relief from enforcement action in the event of a breakdown, as defined by Regulation 1-208 of the District's Rules and Regulations, by following the procedures contained in Regulations 1-431 and 1-432.  The District will thereafter determine whether breakdown relief will be granted in accordance with Regulation 1-433.  (MOP Volume II, Part 3, §4.8)

- The permit holder may seek relief from enforcement action for a violation of any of the terms and conditions of this permit by applying to the District's Hearing Board for a variance pursuant to Health and Safety Code Section 42350.  The Hearing Board will determine after notice and hearing whether variance relief should be granted in accordance with the procedures and standards set forth in Health and Safety Code Section 42350 et seq.  (MOP Volume II, Part 3, §4.8)

The granting by the District of breakdown relief or the issuance by the Hearing Board of a variance will not provide relief from federal enforcement.  (MOP Volume II, Part 3, §4.8)

## Severability

In the event that any provision of this permit is invalidated by a court or tribunal of competent jurisdiction, or by the Administrator of the EPA, all remaining portions of the permit shall remain in full force and effect.  (Regulation 2-6-409.5; MOP Volume II, Part 3, §4.10)

J.	Miscellaneous Conditions

- The maximum capacity for each source as shown in Table II-A is the maximum allowable capacity.  Exceedance of the maximum allowable capacity for any source is a violation of Regulation 2, Rule 1, Section 301.  (Regulation 2-1-301)

## Accidental Release

This facility is subject to 40 CFR Part 68, Chemical Accident Prevention Provisions.  The permit holder submitted a risk management plan (RMP) by the date specified in §68.10.  The permit holder shall also certify compliance with the requirements of Part 68 as part of the annual compliance certification, as required by Regulation 2, Rule 6.  (40 CFR Part 68, Regulation 2, Rule 6)

# EQUIPMENT

| Table II A - Permitted Sources Each of the following sources has been issued a permit to operate pursuant to the requirements of BAAQMD Regulation 2, Permits. The capacities in this table are the maximum allowable capacities for each source, pursuant to Standard Condition I.J and Regulation 2-1-301. |
| --- |
| S-# | Description | Make or Type | Model | Capacity |
| 43 | #1 Continuous Annealing Line - Annealing Furnace, Natural gas only | Surface Combustion | Custom | 53 MMbtu/hr |
| 65 | #1 Continuous Galvanizing Line - Zinc Coating Pot | Wean Engineering Co. | Custom | 30 tph |
| 70 | #2 Continuous Galvanizing Line - Annealing Furnace, Natural gas only | Surface Combustion |  | 39.9 MMbtu/hr |
| 72 | #2 Continuous Galvanizing Line - Zinc Coating Pot | Blaw-Knox, Reliance Electric | Custom | 90 tph |
| 80 | #1 Electro-Tinning Line – Pickling Section | Blaw-Knox Equipment Inc. | Custom | 50 tph |
| 82 | #1 Electro-Tinning Line - Chemical Treatment Section | Blaw-Knox Equipment Inc. | Custom | 5k amp-hours/hr, 50 tph |
| 91 | #3 Electro-Tinning Line – Pickling Section | Wean Engineering Co. | Custom | 50 tph |
| 93 | #3 Electro-Tinning Line - Chemical Treatment Section | Wean Engineering Co. | Custom | 4k amp-hours/hr, 50 tph |
| 97 | Tin Finishing - Tin Anode Casting Pot | Wean Engineering Co. | Unknown |  |
| 130 | Oil Separation Unit | EIMCO Corp. | Custom | 1000 gpm |
| 133 | Terminal Water Treatment Plant | U.S. Steel Corp; | Custom | 30,000,000 gpd |
| 134 | Terminal Water Treatment Plant - Lime Handling | U.S. Steel Corp. | Custom | 1 tph |
| 149 | Paint Shop Spray Booth (With Filters) | Binks And Dispo Spray Booth, 12000 cfm | Q-114-7M-125 |  |
| 155 | No. 1 Electro-tinning (tin free steel cell) | Aetna Standard; hi-density plating cell |  | 34k amp-hours/hr |
| 158 | Gasoline Dispensing Island (Service Station G6331) | Custom | Emco/ Wheaton Nozzle, Model A3003 /A3005 | 1 gasoline nozzle, 10,000 gallon underground storage tank |
| 166 | Pickling Line Coil Processor | MDS – 1800 fpm |  | 535 tph |
| 167 | Pickling Line Butt Welder | Miebach |  | 535 tph |
| 168 | Pickling Line Stretch Leveler | MDS, 820 fpm | Custom | 535 tph |
| 169 | Acid Pickling Line | MDS, 820 fpm | Custom | 535 tph |
| 171 | Tandem Cold Mill | Hitachi - 7000 fpm |  | 535 tph |
| 173 | HCD Alkaline Cleaner | Mitsubishi - USX Design - 2300 fpm |  | 175 tph |
| 174 | KM Continuous Annealing Furnace, Natural gas | Kawasaki Multipurpose; 95.7E6 BTU/HR | Custom | 96 MMbtu/hr |
| 176 | Roll Etch Machine | Jet Wheelblast | RE12 | 18 tph |
| 177 | Iron Oxide Production Roaster - 40 gpm, Natural gas, | ARUS | Spray Roaster | 40 gpm, 27.6 MMbtu/hr |
| 178 | Iron Oxide Silo #1 | ARUS | Custom | 100 tons |
| 179 | Iron Oxide Bagging Station | ARUS - Expanding Ring Fill Spout |  | 12 tph |
| 180 | Acid Gas Absorber #1 | ARUS, 2.5 tph - 18% HCl | Custom | 2.5 tph |
| 181 | Acid Gas Absorber #2 | ARUS, 0.3 tph 18% HCl | Custom | 0.3 tph |
| 182 | Iron Oxide Silo #2 | Arus | Custom | 100 tons |
| 190 | Cold Cleaner | Inland Technology | IT-32, S/N 19933144 | 32 gallons |
| 191 | Cold Cleaner | Inland Technology | IT-32, S/N 39623161 | 32 gallons |
| 194 | Cold Cleaner | Inland Technology | SXL48, S/N 49830035 | 48 gallons |
| 195 | Cold Cleaner | Inland Technology | IT-32, S/N 39829721 | 32 gallons |
| 196 | Cold Cleaner | Inland Technology, | IT-32, S/N 39829724 | 32 gallons |
| 202 | Cold Cleaner | Inland Technology | IT-32 | 32 gallons |
| 206 | Cold Cleaner | System One | 500, S/N 5006196 | 35 gallons |
| 208 | Cold Cleaner | System One | 500, S/N 050011971003956 | 35 gallons |
| 210 | Cold Cleaner | Inland Technology | IT-32, S/N 39829722 | 32 gallons |
| 214 | Cold Cleaner | Inland Technology | IT-32, S/N 39829725 | 32 gallons |
| 215 | Cold Cleaner | Inland Technology | IT-32, S/N 39829726 | 32 gallons |
| 217 | Solvent Cleaning Operation | Graymills Liftkleen | T2420 | 47 gallons |
| 218 | Solvent Cold Cleaner | Inland Technology | Model 30 | 30 gallons |
| 285 | Cold Cleaner | Custom Bearing Parts Cleaner | Custom |  |
| 286 | #1 CRU Evaporator - TFS Operation | Eco-Tec, 75 gph H2O Evaporator | E-75 | 75 gph |
| 287 | #2 Evaporator - ETL Lines | Eco-Tec, 75 gph H2O Evaporator | E-75 | 75 gph |
| 289 | #1 Continuous Galvanize Line-Strip Stenciller | Pannier Rotary Printer | DH1- 1616-S |  |
| 290 | #2 Continuous Galvanize Line-Strip Stenciller | Matthews Jet-A-Mark | Model 1104 |  |
| 292 | KMCAL Horizontal Electrostatic Oiler | Trion | Horizontal EFD | 68" Width |
| 293 | Emergency Standby Generator-TWTP, diesel fueled | Cummins 400 kW Diesel Eng; 3.9e6 btu/hr | KTA19-C | 600 bhp |
| 294 | Emergency Standby Generator-KMCAL, diesel fueled | Cummins 125 kW, Diesel Eng.; 1.4e6 btu/hr | 6CT-8.3 | 207 bhp |
| 295 | Emergency Generator-Filter Plant, diesel fueled | Detroit Diesel 220 kW Engine; 2.1e6 btu/hr |  | 300 bhp |
| 296 | Standby Generator - #2 CC Line, diesel fueled | Cummins 350 kW Diesel Eng; 3.5e6 btu/hr | NTTA-855-GS2 | 535 bhp |
| 297 | Emergency Standby Generator-Computer Bldg, diesel fueled | Cummins 150 kW Diesel Eng; 2.5e6 btu/hr | HT85562 | 355 bhp |
| 299 | Diesel Fire Pump Packaged System, 2500 gpm, diesel fueled | John Deere Diesel Engine; 1.5E6 BTU/HR | 6068 | 240 bhp |
| 300 | Solvent Cleaner | System One | 570 | 35 gallons |
| 301 | Solvent Cleaner | System One | 570 | 35 gallons |
| 302 | Solvent Cleaner | System One | 570 | 35 gallons |
| 303 | Solvent Cleaner | System One | 570 | 35 gallons |
| 304 | Solvent Cleaner | System One | 570 | 35 gallons |
| 305 | Solvent Cleaner | System One | 570 | 35 gallons |
| 306 | Solvent Cleaner | System One | 570 | 35 gallons |
| 307 | Solvent Cleaner | System One | 570 | 35 gallons |
| 308 | Solvent Cleaner | System One | 570 | 35 gallons |
| 309 | Solvent Cleaner | System One | 570 | 35 gallons |
| 310 | Solvent Cleaner | System One | 570 | 35 gallons |
| 311 | Solvent Cleaner | System One | 570 | 35 gallons |
| 312 | Solvent Cleaner | Zep | 9066 | 45 gallons |
| 400 | S-400 Contaminated Soils (SWMUs) – “Out” | Contaminated soil in Custom Solid Waste Management Units (landfills) | Not applicable | Approximately 100,000 cubic yards to be removed |
| 401 | S-401 Contaminated Soils (CAMU) – “In” | Contaminated soil to Custom Corrective Action Management Unit (landfill) | Not applicable | Approximately 100,000 cubic yards to be added |

| Table II B – Abatement Devices |
| --- |
| A-# | Description | Source(s) Controlled | Applicable Requirement | Operating Parameters | Limit or Efficiency |
| 21 | TWTP-Lime Handling-Dust Collector | S134 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
| 26 | Pickling Line Baghouse | S166, S167, S168 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #7216, part B. 1 | Allowable pressure drop range to be determined | 0.670 lb PM10/hr |
| 27 | Pickling Line Scrubber | S169 and exempt sources | None | Allowable pressure drop range to be determined | None |
| 28 | Pickling Line Mist Eliminator | S169 and exempt sources via A27 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #7216, part C. 3 | Allowable pressure drop range to be determined | 0.506 lb PM10/hr and 30 ppmv HCl |
| 29 | Tandem Cold Mill Mist Eliminator | S171 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #7216, part D. 4 | Allowable pressure drop range to be determined | 1.642 lb PM10/hr and 2.42 lb POC/hr |
| 30 | HCD Scrubber | S173 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #7216, part E. 1 | Allowable pressure drop range to be determined | 0.035 lb PM10/hr |
| 32 | NOx Catalytic Reduction Unit | S174 | BAAQMD Condition #7216, part F. 1 | None | 100 lb/day NOx from S174 plus S177 |
|  |  |  | BAAQMD Condition #7216, part F. 4 | None | < 10 ppmv NOx @ 3% O2 or > 90 % NOx reduction by wt or > 80 % NOx reduction by wt for thin gauge |
| 33 | Roll Etch Dust Collector | S176 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #7216, part H. 1 | Allowable pressure drop range to be determined | 0.01 gr PM10/dscf |
| 34 | Venturi Scrubber | S177 via A36 and A37, S178, S179, and S182 via A35 and A38, S180 via S181 | None | Allowable pressure drop range to be determined | None |
| 35 | Silo #2 Baghouse | S178, S179, S182 | None | Allowable pressure drop range to be determined | None |
| 36 | Hot Gas Cyclone #1 | S177 | None | None | None |
| 37 | Hot Gas Cyclone #2 | S177 | None | None | None |
| 38 | Silo #1 Baghouse | S178, S179, S182 | None | Allowable pressure drop range to be determined | None |
| 39 | Venturi Recuperator | S177 via A36, A37 | None | None | None |
| 40 | Iron Oxide/HCI Plant Demister | S177 via A36 and A37, S178, S179, and S182 via A35 and A38, S180 via S181, all via A34 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #7216, part G. 5 | Allowable pressure drop range to be determined | 2 ppmv HCl |
|  |  |  | BAAQMD Condition #7216, part G. 10 | Allowable pressure drop range to be determined | 0.46 lb PM10/hr |
| 41 | ETL Enforcer III Scrubber #1 | S82, S155 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | Regulation 11, Rule 8, Section 93102, part (c) (2) | Allowable pressure drop range to be determined | < 0.01 mg of hexavalent chromium per dscm |
|  |  |  | BAAQMD Condition #7579, part 3 | Allowable pressure drop range to be determined | < 0.006 mg of hexavalent chromium per amp-hr |
| 42 | ETL Enforcer III Scrubber #2 | S93 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | Regulation 11, Rule 8, Section 93102, part (c) (2) | Allowable pressure drop range to be determined | < 0.01 mg of hexavalent chromium per dscm |
|  |  |  | BAAQMD Condition #7579, part 3 | Allowable pressure drop range to be determined | < 0.006 mg of hexavalent chromium per amp-hr |
| 43 | #1 CRU Evaporator Mist Eliminator | S286 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #12194, part 1 | Allowable pressure drop range to be determined | < 0.87 lb of hexavalent chromium per year from this source and S287 |
| 44 | #2 CRU Evaporator mist Eliminator | S287 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
|  |  |  | BAAQMD Condition #12194, part 1 | Allowable pressure drop range to be determined | < 0.87 lb of hexavalent chromium per year from this source and S286 |
| 45 | Dust Collector | S96, S97 | Regulation 6-301 | Allowable pressure drop range to be determined | Ringelmann 1 for < 3 minutes/hr |
|  |  |  | Regulation 6-310 | Allowable pressure drop range to be determined | 0.15 gr/dscf |
|  |  |  | Regulation 6-311 | Allowable pressure drop range to be determined | 4.10P0.67 lb/hr, where P is process weight, ton/hr |
| 46 | Oil Mist Precipitator | S292 | BAAQMD 8-11-304 | Allowable DC milliamps and DC kilovolts ranges to be determined | Abatement to no more than 1.0 lb VOC/gal and abatement device efficiency of at least 90% if VOC of coating > 1.7 lb/gal |
|  |  |  | BAAQMD Condition #16682, part 3 | Allowable DC milliamps and DC kilovolts ranges to be determined | < 0.05 lb VOC/gal of coating applied |

# GENERALLY APPLICABLE REQUIREMENTS

The permit holder shall comply with all applicable requirements, including those specified in the BAAQMD and SIP rules and regulations and other federal requirements cited below.  These requirements apply in a general manner to the facility and/or to sources exempt from the requirement to obtain a District Permit to Operate.  The District has determined that these requirements will not be violated under normal, routine operations, and that no additional periodic monitoring or reporting to demonstrate compliance is warranted.  In cases where a requirement, in addition to being generally applicable, is also specifically applicable to one or more sources, the requirement and the source are also included in Section IV, Source-Specific Applicable Requirements, of this permit.

The dates in parentheses in the Title column identify the versions of the regulations being cited and are, as applicable:

- BAAQMD regulation(s):  The date(s) of adoption or most recent amendment of the regulation by the District Board of Directors

- Any federal requirement, including a version of a District regulation that has been approved into the SIP:  The most recent date of EPA approval of any portion of the rule, encompassing all actions on the rule through that date

The full language of SIP requirements is on EPA Region 9’s website.  The address is included at the end of this permit.

NOTE:

There are differences between the current BAAQMD rules and the versions of the rules in the SIP. All sources must comply with both versions of a rule until US EPA has reviewed and approved the District’s revision of the regulation.

| Table III Generally Applicable Requirements |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) |
| BAAQMD Regulation 1 | General Provisions and Definitions (5/2/01) | N |
| SIP Regulation 1 | General Provisions and Definitions (6/28/99) | Y |
| BAAQMD Regulation 2, Rule 1 | General Requirements (8/1/01) | N |
| BAAQMD 2-1-429 | Federal Emissions Statement (6/7/95) | Y |
| SIP Regulation 2, Rule 1 | General Requirements (1/26/99) | Y |
| BAAQMD Regulation 4 | Air Pollution Episode Plan (3/20/91) | N |
| SIP Regulation 4 | Air Pollution Episode Plan (8/06/90) | Y |
| BAAQMD Regulation 5 | Open Burning (3/6/02) | N |
| SIP Regulation 5 | Open Burning (9/4/98) | Y |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) | Y |
| BAAQMD Regulation 7 | Odorous Substances (3/17/82) | N |
| BAAQMD Regulation 8, Rule 1 | Organic Compounds - General Provisions (6/15/94) | Y |
| BAAQMD Regulation 8, Rule 2 | Organic Compounds – Miscellaneous Operations (6/15/94) | Y |
| BAAQMD Regulation 8, Rule 3 | Organic Compounds - Architectural Coatings (11/21/01) | N |
| SIP Regulation 8, Rule 3 | Organic Compounds - Architectural Coatings (2/18/98) | Y |
| BAAQMD Regulation 8, Rule 4 | Organic compounds - General Solvent and Surface Coating Operations (10/16/02) | N |
| SIP Regulation 8, Rule 4 | Organic compounds - General Solvent and Surface Coating Operations (12/23/97) | Y |
| BAAQMD Regulation 8, Rule 49 | Organic Compounds - Aerosol Paint Products (12/20/95) | N |
| SIP Regulation 8, Rule 49 | Organic Compounds - Aerosol Paint Products (3/22/95) | Y |
| BAAQMD Regulation 8, Rule 51 | Organic Compounds - Adhesive and Sealant Products (7/17/02) | N |
| SIP Regulation 8, Rule 51 | Organic Compounds - Adhesive and Sealant Products (2/26/02) | Y |
| BAAQMD Regulation 11, Rule 2 | Hazardous Pollutants - Asbestos Demolition, Renovation and Manufacturing (10/7/98) | Y |
| BAAQMD Regulation 12, Rule 4 | Miscellaneous Standards of Performance - Sandblasting (7/11/90) | N |
| SIP Regulation 12, Rule 4 | Miscellaneous Standards of Performance - Sandblasting (9/2/81) | Y |
| California Health and Safety Code Section 44300 et seq. | Air Toxics “Hot Spots” Information and Assessment Act of 1987 | N |
| 40 CFR Part 61, Subpart M | National Emission Standards for Hazardous Air Pollutants – National Emission Standard for Asbestos (6/19/95) | Y |
| EPA Regulation 40 CFR 82 | Protection of Stratospheric Ozone (2/21/95) |  |
| Subpart F, 40 CFR 82.156 | Leak Repair | Y |
| Subpart F, 40 CFR 82.161 | Certification of Technicians | Y |
| Subpart F, 40 CFR 82.166 | Records of Refrigerant | Y |

# SOURCE-SPECIFIC APPLICABLE REQUIREMENTS

The permit holder shall comply with all applicable requirements, including those specified in the BAAQMD and SIP rules and regulations and other federal requirements cited below.  The requirements cited in the following tables apply in a specific manner to the indicated source(s).

The dates in parentheses in the Title column identify the versions of the regulations being cited and are, as applicable:

1.	BAAQMD regulation(s):  The date(s) of adoption or most recent amendment of the regulation by the District Board of Directors

2.	Any federal requirement, including a version of a District regulation that has been approved into the SIP:  The most recent date of EPA approval of any portion of the rule, encompassing all actions on the rule through that date

The full text of each permit condition cited is included in Section VI, Permit Conditions, of this permit.  The full language of SIP requirements is on EPA Region 9’s website.  The address is included at the end of this permit.  All other text may be found in the regulations themselves.

| Table IV - A Source-specific Applicable Requirements S43 - #1 CONTINUOUS ANNEALING LINE - ANNEALING FURNACE S70 - Annealing Furnace |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation |  |  |
| 6-310.3 | Particulate Weight Limitation, Heat Transfer Operation | Y |  |
| BAAQMD Regulation 9, Rule 1 | Sulfur Dioxide (3/15/95) |  |  |
| 9-1-301 | Limitations on Ground Level Concentrations | Y |  |
| 9-1-302 | General Emission Limitation | Y |  |

| Table IV - B Source-specific Applicable Requirements S65 - #1 CONTINUOUS GALVANIZING LINE - ZINC COATING POT |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 11, Rule 15 | Hazardous Pollutants – Airborne Toxic Control Measure for Emissions of Toxic Metals From Non-Ferrous Metal Melting (4/6/94) – Adoption of Section 93107, Subchapter 7.5, Chapter 1, Division 3, Title 17 of the California Code of Regulations |  |  |
| 93107(c)(2) | Metal or Alloy Purity Exemption | N |  |
| 93107(d)(1) | Application for Exemption from Control Requirements | N |  |
| 93107(e)(2) | Recordkeeping for Facilities Seeking Exemption from Control Requirements | N |  |
| BAAQMD Condition #7216 |  |  |  |
| part I. 1 | Throughput limitation (Basis: Cumulative increase) | Y |  |
| part I. 2 | Recordkeeping requirement (Basis: Cumulative increase, BAAQMD Regulation 2-6-501) | Y |  |

| Table IV - C Source-specific Applicable Requirements S72 - #2 Continuous Galvanizing Line – Zinc Coating Pot |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 11, Rule 15 | Hazardous Pollutants – Airborne Toxic Control Measure for Emissions of Toxic Metals From Non-Ferrous Metal Melting (4/6/94) – Adoption of Section 93107, Subchapter 7.5, Chapter 1, Division 3, Title 17 of the California Code of Regulations |  |  |
| 93107(c)(2) | Metal or Alloy Purity Exemption | N |  |
| 93107(d)(1) | Application for Exemption from Control Requirements | N |  |
| 93107(e)(2) | Recordkeeping for Facilities Seeking Exemption from Control Requirements | N |  |

| Table IV - D Source-specific Applicable Requirements S80 - #1 Electro-Tinning Line – Pickling Section S91 - #3 Electro-Tinning Line – Pickling Section |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |

| Table IV - E Source-specific Applicable Requirements S82 - #1 Electro-Tinning Line – Chemical Treatment Section S93 - #3 Electro-Tinning Line – Chemical Treatment Section S155 - No. 1 Electro-tinning (tin free steel cell) |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 11, Rule 8 | Hazardous Pollutants – Hexavalent Chromium Airborne Toxic Control Measure for Chrome Plating and Chromic Acid Anodizing Operations (11/4/98) – Adoption of Section 93102, Subchapter 7.5, Chapter 1, Division 3, Title 17 of the California Code of Regulations |  |  |
| 93102(a) | Applicability |  |  |
| 93102(a)(1) | Regulation applies to decorative chromium electroplating | Y |  |
| 93102(a)(4) | Breakdown relief possible | Y |  |
| 93102(c) | Standards |  |  |
| 93102(c)(2) | Decorative Chrome Electroplating and Chromic Acid Anodizing Facilities, Emission Limits or Use of fume suppressant with wetting agent | Y |  |
| 93102(e) | Parameter Monitoring |  |  |
| 93102(e)(1) | Ampere-hour Meters | Y |  |
| 93102(e)(2) | Pressure Drop Monitoring for Add-on Control Device | Y |  |
| 93102(f) | Inspection and Maintenance Requirements |  |  |
| 93102(f)(1) | Table (f)(1) Summary of Inspection and Maintenance Requirements for Sources Using Add-on Air Pollution Control Devices | Y |  |
| 93102(g) | Operation and Maintenance Plan Requirements |  |  |
| 93102(g)(1) | Prepare O&M Plan | Y |  |
| 93102(g)(1) (A) | Standardized Checklist | Y |  |
| 93102(g)(1) (B) | Maintenance Procedures | Y |  |
| 93102(g)(2) | Retain O&M Plan On Site | Y |  |
| 93102(g)(3) | Changes to the O&M Plan | Y |  |
| 93102(g)(4) | Revisions to Address Breakdowns | Y |  |
| 93102(h) | Recordkeeping |  |  |
| 93102(h)(1) | Air Pollution Control Device Inspection Records | Y |  |
| 93102(h)(3) | Performance Test Records | Y |  |
| 93102(h)(4) | Monitoring Data Records | Y |  |
| 93102(h)(5) | Breakdown Records | Y |  |
| 93102(h)(6) | Records of Excesses | Y |  |
| 93102(h)(11) | Records Retention | Y |  |
| 93102(i) | Reporting |  |  |
| 93102(i)(1) | Performance Test Documentation |  |  |
| 93102(i)(3) | Ongoing Compliance Status Reports | Y |  |
| 93102(i)(4) | Reports of Breakdowns | Y |  |
| BAAQMD Condition #7579 |  |  |  |
| part 1 | Annual Amp-hr Limitation (Basis: Voluntary) | Y |  |
| part 2 | Abatement Requirement (Basis: Regulation 11-8-93102(c)(2)) | Y |  |
| part 3 | Hexavalent Chromium Emission Limit (Basis: Regulation 11-8-93102(c)(2)) | Y |  |
| part 4 | Source testing protocol (Basis: Regulation 11-8-93102(d)(4)) | Y |  |
| part 5 | Record keeping (Basis: Regulation 11-8-93102(h)(4)(A)) | Y |  |
| part 6 | Source Test Requirement Every Two Years (Basis: Regulation 2-1-304) | Y |  |

| Table IV - F Source-specific Applicable Requirements S97 – Tin Finishing – Tin Anode Casting Pot S134 - Terminal Treatment Plant – Lime Handling |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #20790 | Inspection and Maintenance Requirements for Baghouses |  |  |
| part 1 | Proper Baghouse Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Pressure Drop Monitor (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Visual Baghouse Inspection (Basis: Regulation 2-1-403) | Y |  |
| part 5 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - G Source-specific Applicable Requirements S130 - Oil Separation Unit and S133 - Terminal Water Treatment Plant |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 8 | Organic Compounds – Wastewater (Oil-Water) Separators (6/15/94) |  |  |
| 8-8-112 | Exemption, Wastewater Critical OC Concentration and/or Temperature | Y |  |
| 8-8-502 | Wastewater sample and test requirements | Y |  |

| Table IV - H Source-specific Applicable Requirements S149 - Paint Shop Spray Booth |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 19 | Surface Coating of Miscellaneous Metal Parts and Products (10/16/02) |  |  |
| 8-19-302 | Limits |  |  |
| 8-19-302.2 | Air-Dried Coatings | Y |  |
| 8-19-307 | Prohibition of Specification | Y |  |
| 8-19-312 | Specialty Coating Limitations |  |  |
| 8-19-312.2 | High Gloss | Y |  |
| 8-19-312.3 | Heat Resistant | Y |  |
| 8-19-312.4 | High Performance Architectural | Y |  |
| 8-19-312.5 | Metallic Topcoat | Y |  |
| 8-19-312.7 | Pretreatment Wash Primer | Y |  |
| 8-19-312.8 | Silicone Release | Y |  |
| 8-19-312.9 | Solar Absorbant | Y |  |
| 8-19-312.12 | Extreme Performance | Y |  |
| 8-19-312.13 | High Temperature | Y |  |
| 8-19-313 | Spray Applications Equipment Limitations | Y |  |
| 8-19-320 | Solvent Evaporative Loss Minimization | Y |  |
| 8-19-321 | Surface Preparation Standards | Y |  |
| 8-19-501 | Records | Y |  |
| SIP BAAQMD Regulation 8, Rule 19 | Surface Coating of Miscellaneous Metal Parts and Products (12/20/95) |  |  |
| 8-19-302 | Limits |  |  |
| 8-19-302.2 | Air-Dried Coatings | Y |  |
| 8-19-307 | Prohibition of Specification | Y |  |
| 8-19-312 | Specialty Coating Limitations |  |  |
| 8-19-312.2 | High Gloss | Y |  |
| 8-19-312.3 | Heat Resistant | Y |  |
| 8-19-312.4 | High Performance Architectural | Y |  |
| 8-19-312.5 | Metallic Topcoat | Y |  |
| 8-19-312.7 | Pretreatment Wash Primer | Y |  |
| 8-19-312.8 | Silicone Release | Y |  |
| 8-19-312.9 | Solar Absorbant | Y |  |
| 8-19-312.12 | Extreme Performance | Y |  |
| 8-19-312.13 | High Temperature | Y |  |
| 8-19-313 | Spray Applications Equipment Limitations | Y |  |
| 8-19.-320 | Solvent Evaporative Loss Minimization | Y |  |
| 8-19-501 | Records | Y |  |

| Table IV - I Source-specific Applicable Requirements S158 - Gasoline Dispensing Island |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| SIP BAAQMD Regulation 8, Rule 7 | Organic Compounds, Gasoline Dispensing Facilities (11/6/02) |  |  |
| 8-7-113 | Tank Gauging and Inspection Exemption | Y |  |
| 8-7-114 | Stationary Tank Testing Exemption | Y |  |
| 8-7-301 | Phase I Requirements |  |  |
| 8-7-301.1 | Requirements for Transfers into Stationary Tanks, Cargo Tanks, and Mobile Refuelers | Y |  |
| 8-7-301.2 | CARB Certification Requirements | Y |  |
| 8-7-301.3 | Submerged Fill Pipe Requirement | Y |  |
| 8-7-301.5 | Maintenance and Operating Requirement | Y |  |
| 8-7-301.6 | Leak-Free and Vapor Tight Requirement for Components | Y |  |
| 8-7-301.7 | Fitting Requirements for Vapor Return Line | Y |  |
| 8-7-301.8 | Coaxial Phase I Systems Certified by CARB prior to January 1, 1994 may not be installed on New or Modified Systems | Y |  |
| 8-7-301.9 | Anti-rotational Coupler or Swivel Adapter Required | Y |  |
| 8-7-301.10 | Vapor Recovery Efficiency Requirements for New and Modified Systems | Y |  |
| 8-7-301.11 | CARB-certified Spill Box Required | Y |  |
| 8-7-301.12 | Spill Box Drain Valve Limitation | Y |  |
| 8-7-301.13 | Annual Vapor Tightness Test Requirement | Y |  |
| 8-7-302 | Phase II Requirements |  |  |
| 8-7-302.1 | Requirements for Transfers into Motor Vehicle Fuel Tanks | Y |  |
| 8-7-302.2 | Maintenance Requirement | Y |  |
| 8-7-302.3 | Proper Operation and Free of Defects Requirements | Y |  |
| 8-7-302.4 | Repair Time Limit for Defective Components | Y |  |
| 8-7-302.5 | Leak-Free and Vapor Tight Requirement for Components | Y |  |
| 8-7-302.6 | Requirements for Bellows Nozzles | Y |  |
| 8-7-302.7 | Requirements for Vapor Recovery Nozzles on Balance Systems | Y |  |
| 8-7-302.8 | Minimum Liquid Removal Rate | Y |  |
| 8-7-302.9 | Coaxial Hose Requirement | Y |  |
| 8-7-302.10 | Construction Materials Specifications | Y |  |
| 8-7-302.12 | Liquid Retain Limitation | Y |  |
| 8-7-302.13 | Nozzle Spitting Limitation | Y |  |
| 8-7-302.14 | Annual Back Pressure Test Requirements for Balance Systems | Y |  |
| 8-7-303 | Topping Off | Y |  |
| 8-7-304 | Certification Requirements | Y |  |
| 8-7-306 | Prohibition of Use | Y |  |
| 8-7-307 | Posting of Operating Instructions | Y |  |
| 8-7-308 | Operating Practices | Y |  |
| 8-7-309 | Contingent Vapor Recovery Requirement | Y |  |
| 8-7-316 | Pressure Vacuum Valve Requirements, Aboveground Storage Tanks and Vaulted Below Grade Storage Tanks | Y |  |
| 8-7-401 | Equipment Installation and Modification | Y |  |
| 8-7-407 | Periodic Testing Requirements | Y |  |
| 8-7-408 | Periodic Testing Notification and Submission Requirements | Y |  |
| 8-7-501 | Burden of Proof | Y |  |
| 8-7-502 | Right of Access | Y |  |
| 8-7-503 | Record Keeping Requirements | Y |  |
| 8-7-503.1 | Gasoline Throughput Records | Y |  |
| 8-7-503.2 | Maintenance Records | Y |  |
| 8-7-503.3 | Records Retention Time | Y |  |
| BAAQMD Condition #12997 | Gasoline Throughput Limit (Basis: Toxic Risk Management Policy) | N |  |

| Table IV - J Source-specific Applicable Requirements S166 - Pickling Line Coil Processor S167 - Pickling Line Butt Welder S168 - Pickling Line Stretch Leveler |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part B. 1 | Emission limitations (Basis: Cumulative increase, BACT) | Y |  |
| part B. 2 | Proper baghouse maintenance (Basis: RACT) | Y |  |
| part B. 3 | Proper particulate capture (Basis: RACT) | Y |  |
| part B. 4 | Annual operation limitation (Basis: Cumulative increase) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part J. 3 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part J. 4 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part M. | Hours of operation recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20790 | Inspection and Maintenance Requirements for Baghouses |  |  |
| part 1 | Proper Baghouse Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Pressure Drop Monitor (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Visual Baghouse Inspection (Basis: Regulation 2-1-403) | Y |  |
| part 5 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - K Source-specific Applicable Requirements S169 - Acid Pickling Line |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part C. 1 | Tank cover requirement (Regulation 2-1-403) | Y |  |
| part C. 2 | Proper capture (Regulation 2-1-403) | Y |  |
| part C. 3 | HCl and PM10 Emission limitations (Basis: Cumulative increase, BACT) | Y |  |
| part C. 4 | Annual operation limitation (Basis: Cumulative increase) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part J. 3 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part J. 4 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part K. 1 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part K. 2 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part M | Hours of operation recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20791 | Inspection and Maintenance Requirements for Wet Scrubbers |  |  |
| part 1 | Proper Scrubber Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Operating Parameters (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - L Source-specific Applicable Requirements S171 - Tandem Cold Mill |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 8, Rule 2 | Miscellaneous Operations (6/15/94) |  |  |
| 8-2-301 | Miscellaneous Operations | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part D. 1 | Rolling oil VOC content limit (Basis: Cumulative increase) | Y |  |
| part D. 2 | Rolling oil usage record keeping (Basis: Regulation 2-1-403) | Y |  |
| part D. 3 | Annual operation limitation (Basis: Cumulative increase) | Y |  |
| part D. 4 | Abatement requirement and POC and PM10 emission limits (Basis: Cumulative increase) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part J. 3 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part J. 4 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part L. 1 | Periodic POC Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part L. 2 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part M | Hours of operation recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20791 | Inspection and Maintenance Requirements for Wet Scrubbers |  |  |
| part 1 | Proper Scrubber Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Operating Parameters (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - M Source-specific Applicable Requirements S173 - HCD Alkaline Cleaner |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part E. 1 | PM10 Emission limitations (Basis: Cumulative increase, BACT) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part J. 3 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part J. 4 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20791 | Inspection and Maintenance Requirements for Wet Scrubbers |  |  |
| part 1 | Proper Scrubber Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Operating Parameters (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - N Source-specific Applicable Requirements S174 - KM Continuous Annealing Furnace |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation |  |  |
| 6-310.3 | Particulate Weight Limitation, Heat Transfer Operation | Y |  |
| BAAQMD Regulation 9, Rule 1 | Sulfur Dioxide (3/15/95) |  |  |
| 9-1-301 | Limitations on Ground Level Concentrations | Y |  |
| 9-1-302 | General Emission Limitation | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part F. 1 | NOx Emission limitations (Basis: BACT, Cumulative increase) | Y |  |
| part F. 2 | CEM requirement (Basis: Regulation 1-521) | Y |  |
| part F. 3 | Required use of selective catalytic reduction unit (Basis: BACT, Cumulative increase) | Y |  |
| part F. 4 | NOx emission concentration or reduction requirements (Basis: BACT, Cumulative increase) | Y |  |

| Table IV - O Source-specific Applicable Requirements S176 - Roll Etch Machine |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part H. 1 | Abatement required (Basis: BACT, Cumulative increase) | Y |  |
| part H. 2 | PM10 emission limitation (Basis: BACT, Cumulative increase) | Y |  |
| part H. 3 | Annual operation limitation (Basis: Cumulative increase) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part M | Hours of operation recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20790 | Inspection and Maintenance Requirements for Baghouses |  |  |
| part 1 | Proper Baghouse Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Pressure Drop Monitor (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Visual Baghouse Inspection (Basis: Regulation 2-1-403) | Y |  |
| part 5 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - P Source-specific Applicable Requirements S177 - Iron Oxide Production Roaster |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 1 | Sulfur Dioxide (3/15/95) |  |  |
| 9-1-301 | Limitations on Ground Level Concentrations | Y |  |
| 9-1-302 | General Emission Limitation | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part G. 1 | NOx emission limitation (Basis: BACT, Cumulative increase) | Y |  |
| part G. 2 | CEM requirement Basis: (Regulation 1-521) | Y |  |
| part G. 3 | Ammonium chloride injection requirement Basis: (BACT, Cumulative increase) | Y |  |
| part G. 4 | Fuel limited to natural gas (Basis: BACT, Cumulative increase) | Y |  |
| part G. 5 | HCl emission concentration limitation (Basis: BACT, Cumulative increase) | Y |  |
| part G. 9 | Annual operation limitation (Basis: Cumulative increase) | Y |  |
| part G. 10 | PM10 emission limitation (Basis: Cumulative increase) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part J. 3 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part J. 4 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part K. 1 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part K. 2 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part M | Hours of operation recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20791 | Inspection and Maintenance Requirements for Wet Scrubbers |  |  |
| part 1 | Proper Scrubber Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Operating Parameters (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - Q Source-specific Applicable Requirements S178 - Iron Oxide Silo #1 S179 - Iron Oxide Bagging Station S182 - Iron Oxide Silo #2 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (7/11/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particles | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part G. 5 | HCl emission concentration limitation (Basis: BACT, Cumulative increase) | Y |  |
| part G. 6 | Abatement requirement (Basis: BACT, Cumulative increase) | Y |  |
| part G. 7 | Material handling requirement (Basis: RACT, Cumulative increase) | Y |  |
| part G. 8 | No visible emission requirement (Basis: Regulation 6-301) | Y |  |
| part G. 9 | Annual operation limitation (Basis: Cumulative increase) | Y |  |
| part G. 10 | PM10 emission limitation (Basis: Cumulative increase) | Y |  |
| part G. 11 | Annual Visible Emission Check (Basis: Regulation 2-6-503) | Y |  |
| part G. 12 | Record keeping requirements (Basis: Regulation 2-6-503) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part J. 3 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part J. 4 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part K. 1 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part K. 2 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part M | Hours of operation recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20790 | Inspection and Maintenance Requirements for Baghouses: A35 and A38 |  |  |
| part 1 | Proper Baghouse Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Pressure Drop Monitor (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Visual Baghouse Inspection (Basis: Regulation 2-1-403) | Y |  |
| part 5 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20791 | Inspection and Maintenance Requirements for Wet Scrubbers |  |  |
| part 1 | Proper Scrubber Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Operating Parameters (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - R Source-specific Applicable Requirements S180 - Acid Gas Adsorber #1 S181 - Acid Gas Adsorber #2 |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particulates | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-311 | General Operations | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #7216 |  |  |  |
| part G. 5 | HCl emission concentration limitation (Basis: BACT, Cumulative increase) | Y |  |
| part G. 9 | Annual operation limitation (Basis: Cumulative increase) | Y |  |
| part G. 10 | PM10 emission limitation (Basis: Cumulative increase) | Y |  |
| part J. 1 | PM10 source test options (Basis: Regulation 2-1-403) | Y |  |
| part J. 2 | Source test methods (Basis: Regulation 2-1-403) | Y |  |
| part J. 3 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part J. 4 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part K. 1 | Periodic Source Test Requirement (Basis: Regulation 2-1-403) | Y |  |
| part K. 2 | Record keeping (Basis: Regulation 2-6-501) | Y |  |
| part M | Hours of operation recordkeeping (Basis: Regulation 2-6-501) | Y |  |
| BAAQMD Condition #20791 | Inspection and Maintenance Requirements for Wet Scrubbers |  |  |
| part 1 | Proper Scrubber Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Operating Parameters (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - S Source-specific Applicable Requirements S190, S191, S194 through S196, S202, S206, S208, S210, S214, S215, S218 - Cold Cleaners |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 16 | Organic Compounds – Solvent Cleaning Operations (10/16/02) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-303.5 | Repair and Maintenance Cleaner Requirements |  |  |
| 8-16-303.5.1 | VOC Content Limitation | N |  |
| 8-16-303.5.2 | VMS solvent allowance | N |  |
| 8-16-303.5.3 | VOC Content Limitation plus VMS solvent allowance | N |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, monthly records | N |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| 8-16-502 | Burden of Proof (to Demonstrate exemption per Regulation 8-16-118) | N |  |
| SIP BAAQMD Regulation 8, Rule 16 | Solvent Cleaning Operations (9/16/98) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, annual records | Y |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| BAAQMD Condition #16920 |  |  |  |
| part 1 | Solvent usage allowance (Basis: Cumulative increase) | Y |  |
| part 2 | Optional solvent emission allowance (Basis: Cumulative increase and Toxic Risk Screen) | Y |  |
| part 3 | Recordkeeping (Basis: Cumulative increase and Toxic Risk Screen) | Y |  |

| Table IV – T Source-specific Applicable Requirements S217 - Cold Cleaner |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 16 | Organic Compounds – Solvent Cleaning Operations (10/16/02) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-303.5 | Repair and Maintenance Cleaner Requirements |  |  |
| 8-16-303.5.1 | VOC Content Limitation | N |  |
| 8-16-303.5.2 | VMS solvent allowance | N |  |
| 8-16-303.5.3 | VOC Content Limitation plus VMS solvent allowance | N |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, monthly records | N |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| 8-16-502 | Burden of Proof (to Demonstrate exemption per Regulation 8-16-118) | N |  |
| SIP BAAQMD Regulation 8, Rule 16 | Solvent Cleaning Operations (9/16/98) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, annual records | Y |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| BAAQMD Condition #12790 |  |  |  |
| part 1 | Solvent usage allowance (Basis: Cumulative increase and Toxic Risk Screen) | Y |  |
| part 2 | Optional solvent emission allowance (Basis: Cumulative increase, Toxic Risk Screen and Regulation 8-16-118.2) | Y |  |
| part 3 | Recordkeeping (Basis: Cumulative increase, Toxic Risk Screen and Regulation 1-441, RACT) | Y |  |

| Table IV - U Source-specific Applicable Requirements S285 - Cold Cleaner |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 16 | Organic Compounds – Solvent Cleaning Operations (10/16/02) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-303.5 | Repair and Maintenance Cleaner Requirements |  |  |
| 8-16-303.5.1 | VOC Content Limitation | N |  |
| 8-16-303.5.2 | VMS solvent allowance | N |  |
| 8-16-303.5.3 | VOC Content Limitation plus VMS solvent allowance | N |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, monthly records | N |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| 8-16-502 | Burden of Proof (to Demonstrate exemption per Regulation 8-16-118) | N |  |
| SIP BAAQMD Regulation 8, Rule 16 | Solvent Cleaning Operations (9/16/98) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, annual records | Y |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| BAAQMD Condition #6818 |  |  |  |
| part 1 | Solvent usage allowance (Basis: Cumulative increase) | Y |  |
| part 2 | Optional solvent emission allowance (Basis: Cumulative increase and Toxic Risk Screen) | Y |  |
| part 3 | Recordkeeping (Basis: Cumulative increase and Toxic Risk Screen) | Y |  |

| Table IV - V Source-specific Applicable Requirements S286 - #1 CRU Evaporator - TFS Operation S287 - #2 Evaporator - ETL Lines |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particulates | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #12194 |  |  |  |
| part 1 | Hexavalent chromium emission limitation (Basis: Toxic Risk Screen) | Y |  |
| part 2 | Source test requirement every two years (Basis: Regulation 2-1-304) | Y |  |
| part 3 | Ongoing Compliance Monitoring (Basis: Toxic Risk Screen) | Y |  |
| part 4 | Non-resettable clock requirement (Basis: Toxic Risk Screen) | Y |  |
| part 5 | Recordkeeping (Basis: Toxic Risk Screen) | Y |  |
| BAAQMD Condition #20791 | Inspection and Maintenance Requirements for Wet Scrubbers |  |  |
| part 1 | Proper Scrubber Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 2 | Operating Parameters (Basis: Regulation 2-1-403) | Y |  |
| part 3 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 4 | Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - W Source-specific Applicable Requirements S289 - #1 Continuous Galvanize Line-Strip Stenciller |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 4 | Organic Compounds – General Solvent and Surface Coating Operations (10/16/02) |  |  |
| 8-4-302 | Solvents and Surface Coating Requirements |  |  |
| 8-4-302.1 | VOC emissions not more than 5 tpy per source | Y |  |
| 8-4-501 | Coating Records | Y |  |
| SIP Regulation 8, Rule 4 | Organic Compounds – General Solvent and Surface Coating Operations (12/23/97) |  |  |
| 8-4-302 | Solvents and Surface Coating Requirements |  |  |
| 8-4-302.1 | VOC emissions not more than 5 tpy per source | Y |  |
| 8-4-501 | Coating Records | Y |  |
| BAAQMD Regulation 8, Rule 20 | Organic Compounds – Graphic Arts Printing and and Coating Operations (3/3/99) |  |  |
| 8-20-110 | Exemption, Small User | Y |  |
| 8-20-507 | Burden of Proof | Y |  |
| BAAQMD Condition #13634 |  |  |  |
| part 1 | Coating usage limitations (Basis: Cumulative increase) | Y |  |
| part 2 | Optional POC emission allowance (Basis: Cumulative increase, Risk Management Policy) | Y |  |
| part 3 | Recordkeeping (Basis: Cumulative increase, Risk Management Policy) | Y |  |
| part 4 | Cumulative increase refund option (Basis: Cumulative increase) | Y |  |

| Table IV - X Source-specific Applicable Requirements S290 - #2 Continuous Galvanize Line-Strip Stenciller |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 4 | Organic Compounds – General Solvent and Surface Coating Operations (10/16/02) |  |  |
| 8-4-302 | Solvents and Surface Coating Requirements |  |  |
| 8-4-302.1 | VOC emissions not more than 5 tpy per source | Y |  |
| 8-4-501 | Coating Records | Y |  |
| SIP Regulation 8, Rule 4 | Organic Compounds – General Solvent and Surface Coating Operations (12/23/97) |  |  |
| 8-4-302 | Solvents and Surface Coating Requirements |  |  |
| 8-4-302.1 | VOC emissions not more than 5 tpy per source | Y |  |
| 8-4-501 | Coating Records | Y |  |
| BAAQMD Condition #13634 |  |  |  |
| part 1 | Coating usage limitations (Basis: Cumulative increase) | Y |  |
| part 2 | Optional POC emission allowance (Basis: Cumulative increase, Risk Management Policy) | Y |  |
| part 3 | Recordkeeping (Basis: Cumulative increase, Risk Management Policy) | Y |  |
| part 4 | Cumulative increase refund option (Basis: Cumulative increase) | Y |  |

| Table IV - Y Source-specific Applicable Requirements S292 - KMCAL Horizontal Electrostatic Oiler |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 11 | Organic Compounds – Metal Container, Closure and Coil Coating (11/19/97) |  |  |
| 8-11-303 | Coil Coating Limitation | Y |  |
| 8-11-304 | Emission Control Device Limitation for Coil Coating | Y |  |
| 8-11-501 | Coating Records | Y |  |
| BAAQMD Condition #16682 |  |  |  |
| part 1 | Coating usage limitations (Basis: Cumulative increase, toxic risk screen) | Y |  |
| part 2 | Optional POC emission allowance (Basis: Cumulative increase, toxic risk screen) | Y |  |
| part 3 | Abatement required and allowed emission rate per gallon (Basis: Cumulative increase) | Y |  |
| part 4 | Recordkeeping (Basis: Cumulative increase, toxic risk screen) | Y |  |
| part 5 | Source test requirement every two years (Basis: Cumulative increase, toxic risk screen) | Y |  |
| part 6 | Proper Oil Mist Precipitator Maintenance/Operation (Basis: Regulation 2-1-403) | Y |  |
| part 7 | Normal Oil Mist Precipitator Voltage and Current to Be Determined | Y |  |
| part 8 | Monthly Inspection Items (Basis: Regulation 2-1-403) | Y |  |
| part 9 | Inspection Recordkeeping (Basis: Regulation 2-6-501) | Y |  |

| Table IV - Z Source-specific Applicable Requirements S293 - Emergency Standby Generator-TWTP, diesel fueled S294 - Emergency Standby Generator-KMCAL, diesel fueled S295 - Emergency Generator-Filter Plant, diesel fueled S296 - Standby Generator - #2 CC Line, diesel fueled S297 - Emergency Standby Generator-Computer Bldg, diesel fueled |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-303 | Ringelmann No. 2 Limitation | Y |  |
| 6-305 | Visible Particulates | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 1 | Inorganic Gaseous Pollutants, Sulfur Dioxide (3/15/95) |  |  |
| 9-1-301 | Limitations on Ground Level Concentrations | Y |  |
| 9-1-304 | Fuel Burning (Liquid and Solid Fuels) | Y |  |
| BAAQMD Regulation 9, Rule 8 | Inorganic Gaseous Pollutants (8/1/01) |  |  |
| 9-8-330 | Emergency Standby Engines, Hours of Operation | N |  |
| 9-8-530 | Emergency standby engines, monitoring and recordkeeping | N |  |
| BAAQMD Condition #18544 |  |  |  |
| Part 1 | Allowable hours of operation (Basis: Regulation 9-8-330) | Y |  |
| Part 2 | Non-Resettable Counter Requirement (Regulation 9-8-530) | Y |  |
| Part 3 | Hours of Operation Recordkeeping Requirement (Regulations 9-8-530) | Y |  |

| Table IV – AA Source-specific Applicable Requirements S299 - Diesel Fire Pump Packaged System, 2500 gpm, diesel fueled |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-303 | Ringelmann No. 2 Limitation | Y |  |
| 6-305 | Visible Particulates | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Regulation 9, Rule 1 | Inorganic Gaseous Pollutants, Sulfur Dioxide (3/15/95) |  |  |
| 9-1-301 | Limitations on Ground Level Concentrations | Y |  |
| 9-1-304 | Fuel Burning (Liquid and Solid Fuels) | Y |  |
| BAAQMD Regulation 9, Rule 8 | Inorganic Gaseous Pollutants (8/1/01) |  |  |
| 9-8-330 | Emergency Standby Engines, Hours of Operation | N |  |
| 9-8-530 | Emergency standby engines, monitoring and recordkeeping | N |  |
| BAAQMD Condition #19380 |  |  |  |
| Part 1 | Fuel sulfur limit (Basis: BACT) | Y |  |
| Part 2 | Allowable hours of operation (Basis: Cumulative increase) | Y |  |
| Part 3 | Non-Resettable Counter Requirement (Regulation 9-8-530) | Y |  |
| Part 4 | Hours of Operation Recordkeeping Requirement (Regulations 9-8-530) | Y |  |

| Table IV – BB Source-specific Applicable Requirements S300 through 312 - Solvent Cleaners |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 8, Rule 16 | Organic Compounds – Solvent Cleaning Operations (10/16/02) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-303.5 | Repair and Maintenance Cleaner Requirements |  |  |
| 8-16-303.5.1 | VOC Content Limitation | N |  |
| 8-16-303.5.2 | VMS solvent allowance | N |  |
| 8-16-303.5.3 | VOC Content Limitation plus VMS solvent allowance | N |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, monthly records | N |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| 8-16-502 | Burden of Proof (to Demonstrate exemption per Regulation 8-16-118) | N |  |
| SIP BAAQMD Regulation 8, Rule 16 | Solvent Cleaning Operations (9/16/98) |  |  |
| 8-16-118 | Limited Exemption, Compounds of Low Volatility | Y |  |
| 8-16-303 | Cold Cleaner Requirements |  |  |
| 8-16-303.1 | General Operating Requirements | Y |  |
| 8-16-303.1.1 | Operate and Maintain in Proper Working Order | Y |  |
| 8-16-303.1.2 | Leak Repair Requirement | Y |  |
| 8-16-303.1.3 | Solvent Storage or Disposal – Evaporation Prevention | Y |  |
| 8-16-303.1.4 | Waste Solvent Disposal | Y |  |
| 8-16-303.1.4(a) | Covered Containers for Waste Solvent Awaiting Pick-up | Y |  |
| 8-16-303.1.4(b) | On-site Waste Treatment | Y |  |
| 8-16-303.1.5 | Solvent Evaporation Minimization Devices shall not be Removed | Y |  |
| 8-16-303.1.6 | Solvent Spray Requirements | Y |  |
| 8-16-303.2 | Cold Cleaner Operating Requirements |  |  |
| 8-16-303.2.1 | Solvent shall be Drained from Cleaned Parts | Y |  |
| 8-16-303.2.2 | No Solvent Agitation by Air | Y |  |
| 8-16-303.2.3 | Solvent Cleaning of Porous or Absorbent Materials is Prohibited | Y |  |
| 8-16-303.3 | Cold Cleaner General Equipment Requirements |  |  |
| 8-16-303.3.1 | Container | Y |  |
| 8-16-303.3.2 | Solvent Evaporation Reduction for Idle Equipment | Y |  |
| 8-16-303.3.3 | Used Solvent Returned to Container | Y |  |
| 8-16-303.3.4 | Label Stating Operating Requirements | Y |  |
| 8-16-501 | Solvent Records |  |  |
| 8-16-501.2 | Facility-wide, annual records | Y |  |
| 8-16-501.5 | Twenty-four month record retention | Y |  |
| BAAQMD Condition #20866 |  |  |  |
| part 1 | Solvent usage allowance (Basis: Cumulative increase) | Y |  |
| part 2 | Optional solvent emission allowance (Basis: Cumulative increase and Toxic Risk Screen) | Y |  |
| part 3 | Recordkeeping (Basis: Cumulative increase and Toxic Risk Screen) | Y |  |

| Table IV - CC Source-specific Applicable Requirements S400 - Contaminated Soils (SWMUs) – “Out” S401 - Contaminated Soils (CAMU) – “In” |
| --- |
| Applicable Requirement | Regulation Title or Description of Requirement | Federally Enforceable (Y/N) | Future Effective Date |
| BAAQMD Regulation 6 | Particulate Matter and Visible Emissions (12/19/90) |  |  |
| 6-301 | Ringelmann No. 1 Limitation | Y |  |
| 6-305 | Visible Particulates | Y |  |
| 6-310 | Particulate Weight Limitation | Y |  |
| 6-401 | Appearance of Emissions | Y |  |
| BAAQMD Condition #20038 |  |  |  |
| Part 1 | Follow corrective action plan (Basis: CEQA) | Y |  |
| Part 2 | No visible emissions (Basis: BACT, Regulation 1-301) | Y |  |
| Part 3 | Cover trucks or maintain minimum freeboard and/or water top layer (Basis: BACT) | Y |  |
| Part 4 | Recordkeeping requirements (Basis: Cumulative increase) | Y |  |

# SCHEDULE OF COMPLIANCE

The permit holder shall comply with all applicable requirements cited in this permit.  The permit holder shall also comply with applicable requirements that become effective during the term of this permit on a timely basis.

# PERMIT CONDITIONS

Any condition that is preceded by an asterisk is not federally enforceable.

Condition # 840

For S159 & S160 - Fresh HCl Tanks:

*1)  This tank shall be vented to scrubber A-27.

(basis: voluntary limit)

Condition # 6818

For S285 - Cold Cleaner (Custom, Bearing Parts Cleaner):

1. The net amount of "Safety-Kleen 105” and/or “Safety-Kleen Premium" used at S-285, Cold Cleaner, shall not exceed 200 gallons in any consecutive twelve-month period.

(Basis: cumulative increase, toxic risk screen)

2. Solvents other than the materials specified in part condition #1 may be used at S-285, provided that the owner/operator can demonstrate that all of the following are satisfied:

a. Total VOC emissions from S-285 do not exceed 1,340 pounds in any consecutive twelve month period; and

b. The use of these materials do not increase toxic emissions above any risk screening trigger level; and

c. All solvents used shall meet the definition of a "Compound with Low Volatility" in Regulation 8, Rule 16.

(Basis: cumulative increase, toxic risk screen, Regulation 8-16-118.2)

3. In order to demonstrate compliance with the above parts condition, the following records shall be maintained on a District approved log.  Entries shall be made to the records whenever solvent is added or removed from the source.  These records shall be kept on site, summarized on a quarterly basis, and made available for District inspection for a period of 60 months from the date on which a record is made.

a. Type and monthly usage of all VOC containing materials used;

b. If a material other than that specified in part condition #1 is used, VOC and toxic component contents of each material used; and mass emission calculations to demonstrate compliance with part condition #2, on a monthly basis;

c. Monthly usage and/or emission calculations shall be totaled for each consecutive twelve-month period;

d. Quantities of each type of solvent recovered for disposal or recycling

e. Net usage of each type of solvent

(Basis: toxic risk screen, cumulative increase, reasonably available control technology)

Condition # 7216

For S65 - Zinc Coating Pot

S166 - Pickling Line Coil Processor

S167 - Pickling Line Butt Welder

S168 - Pickling Line Stretch Leveler

S169 - Acid Pickling Line

S171 - Tandem Cold Mill

S173 - HCD Alkaline Cleaner

S174 - KM Continuous Annealing Furnace

S176 - Roll Etch Machine

S177 - Iron Oxide Production Roaster

S178 - Iron Oxide Silo #1

S179 - Iron Oxide Bagging Station

S180 - Acid Gas Absorber #1

S181 - Acid Gas Absorber #2:

S182 - Iron Oxide Silo #2:

(Amended 7/95, AN 14797; 11/96, AN 16832; 5/97, AN 16977; 2/99, AN 19031; 5/02, AN 32; 2/03, AN 6628)

A.  Conditions on the entire modernization project and ship and train activity are:

*1.  UPI's future cargo emissions shall not exceed the maximum annual mass emissions baseline set forth below.  As used herein, "cargo emissions" shall be the emissions resulting from: (1) truck, rail or ship deliveries of steel coil to the UPI facility, (2) truck, rail or ship shipments of finished steel product and scrap steel from the UPI facility, and (3) truck or rail movements of steel coil, finished products, or scrap steel within the UPI facility. "Cargo emissions" shall not include emissions resulting from the transportation of steel coil, finished products, or scrap material to, from or within existing public ports which are not contiguous to the UPI facility, including, but not limited to, the Port of Richmond or the Port of Oakland. (amended 5/97, AN 16977; 2/99, AN 19031; 5/02, AN 32)

Annual

Tons per year

Particulate Matter                     3.427

NOx                                      100.334

SO2                                           8.433

Organic Compounds                 6.069

CO                                           12.942

(Basis: Cumulative increase, CEQA)

*2.  The determination of cargo emissions specified in part A. condition number 1 above shall be based on monthly reports submitted by UPI to the District detailing cargo emissions and other information in the format attached as Appendix A, or in such other format as the District may require or approve.  Such reports shall be submitted to the Director of Compliance and Enforcement within 30 days after the end of the calendar month which that the report relates.  UPI shall maintain the records used to prepare such monthly reports for a period of five consecutive calendar years following the calendar year that which each such monthly report was prepared, and shall be made available for inspection by the District upon request. (Appendix A revised 5/02, AN 32)

(Basis: Cumulative increase, CEQA)

*3.  The monthly report shall include a running total of the cargo emissions for the current calendar year.  If, at the end of any calendar month, the total cargo emissions accumulated to date in that calendar year exceed the annual mass emissions baseline (set forth in part A. condition number 1 above) prorated to the number of months elapsed to date for that year, UPI shall inform the District in writing within 30 days of the end of that calendar month as to what steps or measures will be taken to ensure that the annual mass emissions baseline is not exceeded. (amended 5/97, AN 16977)

(Basis: Cumulative increase, CEQA)

*4a. Calculations of mass cargo emission shall be based on:

(1) the emission factors set forth for ship, tugs and specific locomotive engine types in Appendix A; (2) District approved locomotive fuel usage factors; and (3) the truck emission factors in Condition part A. 4c.  In the event UPI wishes to use a locomotive engine type for deliveries to and shipments from the UPI facility for which no emission factors are listed on Appendix A, UPI shall obtain prior District approval of the emissions factors to be used with respect to such locomotive engine type.  In the event new emission factors are determined by the District, the CARB, or the EPA for locomotive engine types used for deliveries to and from the UPI facility, UPI shall obtain prior District approval to use such new emission factors for purposes of calculating annual mass cargo emissions.

Current District-approved line-haul locomotive fuel usage factors are listed below.  These factors supersede the factors in Appendix A.  Unless a specific factor is listed below, the Appendix A factors are still valid.

Union Pacific     1.37 gal/KGTM

BNSF                 1.45 gal/KGTM

In lieu of using the calculation method in Appendix A for the Unit Train, UPI may use the emissions factors in part A. Condition 4b. (amended 5/97, AN 16977)

(Basis: Cumulative increase, CEQA)

*4b. Calculations of mass cargo emissions from the Unit Train shall be based on the emission factors listed below.  These factors, in the units of pounds of emission/ton  steel shipped, are based on the parameters listed below, and the line haul engine emission factors listed in Appendix A.  If UPI uses these factors, then UPI must keep monthly records of the tonnage of steel hauled by the Unit Train.  These records shall be summarized in the monthly report. These records shall be retained on site for five years from the date of entry, and shall be made available to the District upon request.

If a change occurs to one or more of the parameters that were used to derive the emission factors (such as haul distance, railcar tare weight, etc.), and that change results in higher emission factors, UPI shall notify the District in writing and shall use the higher emissions factors effective from the date the change occurred.  If a change results in lower emission factors, UPI may petition the District, in writing, for permission to use the lower factors. UPI may not use any lower emission factor, unless authorized to do so by the District, in writing.

(added 5/97, AN 16977; amended 5/02, AN 32)

Unit Train Parameters:

1-way haul distance     39.7 miles

Empty railcar weight    34 tons

Loaded railcar weight  134 tons

Railcars per train      50

UP fuel usage factor     1.37 gal/1000 gross ton mi KGTM

Unit Train Emission Factors

(lb emissions/ton of steel hauled):

NOx             0.0490

CO               0.0048

POC             0.0018

PM10           0.0012

SO2              0.0065

(Basis: Cumulative increase, CEQA)

*4c. Calculations of mass cargo emissions from hauling raw steel, product or scrap by truck shall be calculated by multiplying vehicle mileage and the "lb/mile" emission factors listed below.  [The emission factors are the average ARB 2002 heavy-heavy duty truck (> 33,000 lb) emission factors for the San Francisco air basin.]  UPI shall summarize truck mileage and cargo carrier emissions in their monthly report.

(added 5/97, AN 16977; amended 5/02, AN 32)

Pollutant       (lb/mile)

NOx            0.0345

CO             0.0059

POC            0.0014

PM10           0.0009

SO2            0.0004

(Basis: Cumulative increase, CEQA)

5.  Deleted due to an amendment to the District NSR which supercedes this condition as required in condition number 7 below.

6.  Deleted due to an amendment to the District NSR which supercedes this condition as required in condition number 7 below.

5 7.  UPI shall not be exempt from the application of any future amendment to the District's Rules and Regulations.

(Basis: Regulation 1-103)

*6 8.  Only steel coil shall be delivered by 37,000 dead weight ton (DWT) or less ships and offloaded at the UPI dock.

(Basis: Cumulative increase, CEQA)

*7 9.  The steel coil shall only be delivered by ocean going bulk cargo ships of 37,000 DWT or less.

(Basis: Cumulative increase, CEQA)

8a 10. The total number of SCR plus non-SCR-equipped ship deliveries to UPI shall not exceed 50 in any consecutive 365 day period.

*8b. The total number of non-SCR-equipped ship deliveries shall not exceed 25 in any consecutive 365-day period.  (amended AN 32, 5/02)

(Basis: Cumulative increase, CEQA)

9 11. In no event shall the limits set forth in part A. 8 condition 10 result in a total combined annual throughput of unfinished steel coil in excess of 2,200,000 tons at UPI. (amended AN 16832, 11/96; AN 32, 5/02)

(Basis: Cumulative increase, CEQA)

*10 12. While a SCR-equipped ship is transiting in District boundary waters the following shall occur:

a 1.  The main engine exhaust shall be abated by a selective catalytic reduction (SCR) system.

b 2.  Only fuel oil with a sulfur content not to exceed 0.05% sulfur by weight shall be burned.

(amended AN 32, 5/02)

(Basis: Cumulative increase, CEQA)

*11 13. For SCR-equipped ships, the main engine exhaust shall be equipped with a NOx continuous emission monitor (CEM) and recording device. The CEM system shall be used to determine and record the daily NOx emission from the ship main engine during a ship transit in District boundary water.  (amended AN 32, 5/02)

(Basis: Cumulative increase, CEQA)

*12 14. For SCR-equipped ships, in no event shall ammonia emissions to the atmosphere exceed 50 ppmv, averaged over a two hour period. (amended AN 32, 5/02)

(Basis: Cumulative increase)

15. (deleted AN 32, 5/02; required source tests previously performed)

*13 16. For SCR-equipped ships, each ship shall use on-shore electrical power when hoteling at the UPI facility.  The main propulsion engine, generators and boiler shall shutdown during hoteling at the UPI facility. (amended AN 32, 5/02)

(Basis: Cumulative increase, CEQA)

14 17. UPI shall maintain daily records, in a District approved log, for the following:

a  1.   Date and time of a shipping docking at the UPI terminal.

*b  2.   Fuel usage for each ship transit through District boundary water.  Fuel usage shall be automatically recorded on a District approved continuous fuel recording system.

*c  3.   Delivery receipts for the type of fuel burned.

*d  4.   Hours of ship operation in District boundary water.

*e  5.   Loading capacity of ship in DWT.

f  6.   Tonnage of steel coil delivered to UPI by ship.

*g  7.   Date and time of a ship departure from the UPI terminal.

(Basis: Cumulative increase, CEQA)

15.  All records shall be retained on the ship until docking at UPI at which time they shall retained at UPI for at least two five years from date of recording.  These records shall be kept on site at UPI and made available to District staff upon request.

(Basis: Cumulative increase, CEQA)

18. Deleted.

19. (deleted AN 32, 5/02)

20. (deleted AN 32, 5/02)

*16. The procedures and methodology to be used in calculating transportation emissions set forth in Appendix A which that is attached hereto are incorporated as part of the Permit to Operate.

(Basis: Cumulative increase, CEQA)

CEQA Conditions 1 through 6

1. (deleted AN 32, 5/02)

2. (deleted AN 32, 5/02)

3. (deleted AN 32, 5/02)

4. (deleted AN 32, 5/02)

5. (deleted AN 32, 5/02)

6. (deleted AN 32, 5/02)

B.     Conditions for S-166, S-167 and S-168

1.  When in operation these sources shall be vented at all times to A-26 Baghouse.  PM10 emissions from A-26 shall not exceed 0.670 lb/hr, as measured by a District- approved PM10 source test method.  As an alternative, source test results which show TSP less than the above PM10 limit shall be adequate to demonstrate compliance.

(amended AN 32, 5/02)

(Basis: Cumulative increase, BACT)

2.  The Baghouse, A-26 shall be properly maintained and kept in good operating condition at all times.  A differential pressure indicator shall be installed at the baghouse to indicate the differential pressure across the baghouse.

(Basis: RACT)

3.  The exhaust systems must be maintained at sufficient negative pressure to capture the particulate emissions generated at this source.

(Basis: RACT)

4.  The hours of operation of these sources shall not exceed 8640 hours per calendar year. (amended 11/96, AN 16832)

(Basis: Cumulative increase)

C.     Conditions for S-169 and S-170

1.  In no event shall the tanks be uncovered when pickle liquor is present in the tanks, except when necessary for ordinary maintenance and product quality control.

(Basis: BACT, Cumulative increase)

2.  The exhaust for this source area must be maintained at sufficient negative pressure to capture all fugitive HCL fumes at all times.

(Basis: BACT, Cumulative increase)

3.  When in operation this source shall be vented to A-27 Pickling Line Packed Bed Scrubber utilizing caustic solution.  The emissions of HCL emitted to the atmosphere from the scrubber shall not exceed 30 ppmv.  PM10 emissions from A-27 shall not exceed 0.506 lb/hr, as measured by a District-approved PM10 source test method.  As an alternative, source test results which show TSP less than the above PM10 limit shall be adequate to demonstrate compliance.

(amended AN 32, 5/02)

(Basis: BACT, Cumulative increase)

4.  The hours of operation of these sources shall not exceed 8640 hours per calendar year. (amended 11/96, AN 16832)

(Basis: Cumulative increase)

D.     Conditions for S-171

1.  (A/C Condition deleted)

12.  No rolling oil shall be used which contains more than 0.3% by weight of precursor organic compounds.

(Basis: Cumulative increase)

23.  The applicant shall maintain records of the supplier, composition, and quantities of the rolling oil used at the tandem cold mill.  These records shall be available for inspection by District personnel.

(Basis: Cumulative increase)

34.  The hours of operation of S-171 shall not exceed 8640 hours per calendar year. (amended 11/96, AN 16832)

(Basis: Cumulative increase)

45.  When in operation, S-171 shall be vented at all times to A-29, Tandem Cold Mill Mist Eliminator.  PM10 emissions from A-29 shall not exceed 1.642 lb/hr, as measured by a District-approved PM10 source test method.  As an alternative, source test results which show TSP less than the above PM10 limit shall be adequate to demonstrate compliance.  POC emissions from A-29 shall not exceed 2.42 lb/hr, as measured by a District-approved source test.

(amended AN 32, 5/02)

(Basis: Cumulative increase)

E.     Conditions for S-173

1.  At all times the exhaust from this source area must be maintained at sufficient negative pressure for A-30, HCD Scrubber, to capture the fumes and particulate emissions generated at this source.  PM10 emissions from A-30 shall not exceed 0.035 lb/hr, as measured by a District-approved PM10 source test method.  As an alternative, source test results which show TSP less than the above PM10 limit shall be adequate to demonstrate compliance. (amended AN 32, 5/02)

(Basis: BACT, Cumulative increase)

2.  (deleted 11/96, AN 16832)

F.     Conditions for S-174

1.  (deleted 3/4/97)

1 2.  In no event shall the combined daily emissions from S-174 and S-177 exceed 100 lbs/day of nitrogen oxides (measured as NO2).

(Basis: BACT, Cumulative increase)

2 3.  For the purpose of demonstrating compliance with part F. Condition 4 a, b, and c 8 A, B and C for S-174, UPI shall install, calibrate and operate District approved continuous in-stack emission monitors and recorders for oxides of nitrogen, and either oxygen or carbon dioxide.  Daily emissions shall be reported to the District on a monthly basis, the format of which shall be subject to approval by the APCO.

(Basis: Regulation 1-521)

3 4.  The Selective Catalytic Reduction Unit (SCR) shall be operated during all periods of the annealing furnace operation, with the exception of during a cold startup of the annealing furnace, which is not to exceed 3 hours, and during furnace idling.  A cold startup includes periods when the SCR temperature is less than 375 F. Furnace idling includes periods when natural gas is being fired but at a rate of less than 17 scfm (approximately 1 thousand scfh).

(Basis: BACT, Cumulative increase)

5.  (A/C Condition deleted)

6.  (A/C Condition deleted)

7.  (deleted 11/96, AN 16832)

4 8.  Excluding periods of cold startup and furnace idling, The NOx emissions in the exhaust from this source shall meet one of the following:

a A.   Not exceed 10 ppmv at 3% oxygen, averaged over 3 consecutive hours;

b B.   Be reduced by at least a 90%, by weight, averaged over 3 consecutive hours, by the A-32 Selective Catalytic Reduction (SCR) Unit; or

c C.   For a period when UPI is running a thin gauge coil (<0.0300 inch), NOx shall be reduced by at least 80%, by weight, averaged over three consecutive hours, by the A-32 Selective Catalytic Reduction (SCR) Unit.  If the duration of the thin gauge run is less than three hours, the averaging period shall be the entire run period.

(Basis: BACT, Cumulative increase)

9.  (A/C Condition deleted)

10. (A/C Condition deleted)

11. (deleted 2/28/03)

G. Conditions for the Iron Oxide/HCL Regeneration Facility, S-177, S-180, S-181, S-178, S-182 and S-179.

1.  (deleted 3/4/97)

1 2.  In no event shall the combined daily emissions from S-174 and S-177 exceed 100 lbs/day NOx (measured as NO2).

(Basis: BACT, Cumulative increase)

2 3.  For this operation (S-177 exhaust), UPI shall install, calibrate and operate District approved continuous in-stack emission monitors and recorders for oxides of nitrogen, and either oxygen or carbon dioxide.  Daily emissions shall be reported to the District on a monthly basis, the format of which shall be subject to approval by the APCO.

(Basis: Regulation 1-521)

3 4.  The ammonium chloride injection system shall be properly maintained and kept in good operating condition at all times.  The ammonium chloride injection system shall be in full use during all periods of the roaster operation, with the exception of during a cold startup of the roaster.  UPI shall, during the startup period perform tests to determine the actual ammonium chloride injection rate necessary to assure compliance with part condition number 1.  The ammonium chloride injection rate shall be automatically activated and controlled at all times during the roaster operation.  UPI shall submit final design specifications for the ammonium chloride injection system to the APCO for is approval one month prior to the commencement of construction at the site of the roaster S-177.

(Basis: BACT, Cumulative increase)

5.  (A/C Condition deleted)

6.  (A/C Condition deleted)

4 7.  The roaster shall be fired on natural gas only.

(Basis: BACT, Cumulative increase)

5 8.  The HCL emissions from A40, Iron Oxide/HCl Plant Demister, this source shall not exceed 2 ppmv.

(Basis: TRMP)

6 9.  The silos S-178 and S-182 shall be controlled at all times by A-38 Baghouse or A-35 Baghouse.  The A38 Baghouse and A35 Baghouse shall each be controlled at all times by the A34 Venturi Scrubber. PM10 emissions from each baghouse shall not exceed 0.01 gr/dscf, as measured by a District-approved source test method, during all periods of operation.  As an alternative, source test results which show TSP less than the above PM10 limit shall be adequate to demonstrate compliance.

(Basis: BACT, Cumulative increase)

7 10. The iron oxide shall be pneumatically conveyed for storage in an entirely enclosed system.

(Basis: RACT, Cumulative increase)

8 11. There shall be no visible emissions from the iron oxide bagging operation.

(Basis: BACT)

9 12. The hours of operation of each of these sources (S-166, S-167, S-168, S-169, S-170, S-171 and S-177, S-178, S-179, S-180, S-181, and S-182) shall not exceed 8640 hours per calendar year. (amended 11/96, AN 16832)

(Basis: Cumulative increase)

10 13. PM10 emissions from A40, Iron Oxide/HCl Plant Demister A-34, Venturi Scrubber, shall not exceed 0.46 lb/hr. (amended AN 32, 5/02; AN 6628, 2/03)

(Basis: BACT, Cumulative increase)

11.  The iron oxide bagging operation shall be checked for visible emissions once every calendar year.  If any visible emissions are detected by an untrained observer, the operator shall take corrective action to eliminate any visible emissions, and check for visible emissions again with an untrained observer.  If visible emissions cannot be eliminated, the operator shall perform a certified visible emissions evaluation in accordance with BAAQMD 6-601 to determine compliance with part G. 8 of this condition and with Regulation 6-301.  Any non-compliance shall be reported in accordance with Standard Condition I.F of the Title V permit.  All visible emissions observations (both certified and uncertified) shall take place while the equipment is operating and during daylight hours.  If no visible emissions are detected, the operator shall continue to check for visible emissions every year.  If the equipment has not operated during a calendar year, no inspection is required.  (basis:  Regulation 2-6-503)

12.  The operator shall keep records of all visible emissions checks and the person performing the check.  The records shall be retained for five years and shall be made available to District personnel upon request.  (basis:  Regulation 2-6-501)

H.     Conditions for Source 176

1.  S-176 shall be vented to A-33 Roll Etch Dust Collector during all periods of operation.

(Basis: BACT, Cumulative increase)

2.  The emissions of PM10 from S-176 shall not exceed 0.01 grains/dscf at 12% CO2.  As an alternative, source test results which show TSP less than the above PM10 limit shall be adequate to demonstrate compliance.

(Basis: BACT, Cumulative increase)

3.  The hours of operation of S-176 shall not exceed 8640 hours per calendar year. (amended 11/96, AN 16832; 5/02, AN 32)

(Basis: Cumulative increase)

I.     Conditions for Source 65 (added 5/02, AN 32)

1.  The total steel throughput for S-65 shall not exceed 218,776 tons in any consecutive 12-month period.  (added 5/02, AN 32)

(Basis: Cumulative increase)

2.  The owner/operator of S65 shall maintain records of daily steel throughput summarized on a monthly basis in a District-approved log.  These records shall be retained on site for a minimum of five years from the date of entry and made available to District personnel upon request.  (basis:  cumulative increase, BAAQMD Regulation 2-6-501)

J.  PM10 Source Testing

1.  Source testing options to demonstrate compliance with the PM10 concentration and mass emission rate limits in the above parts of this condition are listed below.  The purpose of this condition is to provide an option for a less costly modified Filterable Particulate (FP) test to demonstrate compliance with the PM10 limits.  (basis: Regulation 2-6-503)

a. Conduct a PM10 source test (including condensable particulate (CP)).

b. Conduct a FP source test plus a CP source test incorporated into the FP source test train.  If results exceed the PM10 limit, conduct a PM10 source test (including condensable).

The test results shall be delivered to the District no later than 30 days from the date of sampling.

2. Particulate matter emissions will be determined by a. or b. below: (basis: Regulation 2-6-503)

a. Emissions of PM10 will be determined by using the following:

1). Emissions of PM10 including CP will be determined in accordance with California Air Resources Board (CARB) Method 501 or

2). Emissions of PM10 including CP will be determined in accordance with California Air Resources Board (CARB) Method 501 plus CARB Method 5 (including CP) or

3). Emissions of PM10 will be determined in accordance with EPA Method 201/201A plus EPA Method 202.  The EPA Method 202 sample train shall be incorporated into the Method 201/201A sample train.

b. Emissions of FP plus CP emissions will be determined by using:

1). Emissions of FP plus CP will be determined in accordance with CARB Method 5 (including CP) or

2). Emissions of FP plus CP will be determined in accordance with either EPA Method 5 or BAAQMD ST-15 plus EPA Method 202. The EPA Method 202 sample train shall be incorporated into the EPA Method 5 or BAAQMD ST-15 sample train, as appropriate.

3. In order to demonstrate compliance with each PM10 concentration and mass emission rate limits in the above parts B through E and G of this condition, the owner/operator shall perform District approved source tests:

a. in calendar year 2004.

b. in every fifth calendar year thereafter.

The owner/operator shall notify the Manager of the District’s Source Test Section at least seven (7) days prior to the test, to provide the District staff the option of observing the testing.  (basis:  Regulation 2-6-503)

4. To demonstrate compliance with Part J. 3, the owner/operator shall maintain the following records in a District approved log: (basis: Regulation 2-6-501)

a. All source test results for FP, CP and PM10 emissions.

These records shall be kept on site for a minimum of 5 years from the date of entry and shall be made available to District personnel upon request. (basis: Regulation 2-6-501)

K.  HCl Source Testing

1.	In order to demonstrate compliance with each HCl concentration and mass emission rate limits in the above parts C and G of this condition, the owner/operator shall perform District approved source tests:

a. in calendar year 2004.

b. in every fifth calendar year thereafter.

The owner/operator shall notify the Manager of the District’s Source Test Section at least seven (7) days prior to the test, to provide the District staff the option of observing the testing.  (basis:  Regulation 2-6-503)

2.	To demonstrate compliance with Part J. 3, the owner/operator shall maintain the following records in a District approved log: (basis: Regulation 2-6-501)

a. All source test results for HCl concentration and emissions.

These records shall be kept on site for a minimum of 5 years from the date of entry and shall be made available to District personnel upon request. (basis: Regulation 2-6-501)

L.  POC Source Testing

1.	In order to demonstrate compliance with the POC mass emission rate limit in the above part D of this condition, the owner/operator shall perform a District approved source test:

a. in calendar year 2004.

b. in every fifth calendar year thereafter.

The owner/operator shall notify the Manager of the District’s Source Test Section at least seven (7) days prior to the test, to provide the District staff the option of observing the testing.  (basis:  Regulation 2-6-503)

2.	To demonstrate compliance with Part J. 3, the owner/operator shall maintain the following records in a District approved log: (basis: Regulation 2-6-501)

a. All source test results for HCl concentration and emissions.

These records shall be kept on site for a minimum of 5 years from the date of entry and shall be made available to District personnel upon request. (basis: Regulation 2-6-501)

M.  Hours of Operation Record Keeping

In order to demonstrate compliance with each calendar-year operating limit, in hours, in the above parts B through D, G and H of this condition, the owner/operator shall maintain records of the days and hours of operation.  The owner/operator shall total the hours of operation on both a monthly and calendar-year basis.  These records shall be retained on site in a District-approved log for a minimum of five years from the date of entry and made available to District personnel upon request.  (basis:  BAAQMD Regulation 2-6-501)

*APPENDIX A TO PERMIT CONDITION #7216, FOR TRAINS

The procedures and methodology to be used in calculating transportation emissions for the purpose of demonstrating compliance with the USS-Posco permit condition.

The methodology and calculation procedures require gathering the raw data (STEP 1), determining fuel usage rates (STEP 2), applying pollutant specific emission factors  (STEP 3).

Calculated monthly emissions shall be reported in tons and calculated daily emissions shall be reported in pounds (STEP 4).

STEP 1.

Collection of Raw Data Regarding Train Activity at USS-POSCO, Pittsburg, CA

INCOMING TRAIN SHIPMENTS.   The following information, associated with each locomotive, shall be collected, recorded, and used in subsequent calculations:

- Arrival Date and Time

- Specify as to Type of Delivery  (ex. steel coil)

- Carrier and Train Number

- Number of Locomotives Used

- Engine Type

- Number of Cars

- Idle Time in Minutes

- Quantity of Product Shipped (in tons)

- Random Check of Car Weight determined by UPI scale

- Distance Traveled in District

- Invoice Records

OUTGOING TRAIN SHIPMENTS.   The following information, associated with each locomotive, shall be collected, recorded, and used in subsequent calculations:

- Departure Date and Time

- Specify as to Type of Delivery (ex. steel coil, scrap, iron oxide)

- Carrier and Train Number

- Number of Locomotives Used

- Engine Type

- Type of Cars

- Number of Cars

- Quantity of Product Shipped (in tons)

- Distance Traveled in District

- Invoice Records

OUTGOING TRAINS CARRYING UPI MATERIAL AS PART OF A SECTION TRAIN WITHIN DISTRICT.  The following information, associated with each locomotive, shall be collected, recorded, and used in subsequent calculations:

- Departure Date and Time

- Specify as to Type of Delivery (ex. steel coil, scrap, iron oxide)

- Carrier and Train Number

- Number of Locomotives Used for UPI Cars

- Engine Type

- Type of Cars

- Number of Cars

- Quantity of Product Shipped (in tons)

- Distance Traveled in District

- Invoice Records

SWITCHING ACTIVITY.  The following information, associated with each locomotive, shall be collected, recorded, and used in subsequent calculations:

UPI switching locomotives:

- fuel loaded into locomotive

- invoice records

FOR switching at SF/SP switch yard:

- Switching Invoice Records

- Same information required for SP line haul

STEP 2.

DETERMINING FUEL USAGE RATES

The District approved railroad system factors:

Union Pacific  (laden & unladen):      1.37 gallon/KGTM

Southern Pacific (laden & unladen):  1.67 gallon/KGTM

Santa Fe (laden & unladen):              1.78 gallon/KGTM

LINE HAUL TRAINS  (incoming raw coils, outgoing finished product and scrap):

((number of cars) * (gross weight of cars) * (miles traveled within District) /(1000)) * (Railroad carrier system factor, in gal/KGTM) * (Emission Factor for Pollutant)

UNLADEN LINE HAUL TRAINS:

The miles traveled by a returning unladen train from UPI to Union Pacific or receiving an incoming unladen train to carry UPI shipments are assumed to be identical to the miles traveled within the District for the laden train.  The method of calculation for line haul trains is then followed.

UPI SWITCH ENGINES

(Fuel usage) * (Emission Factor for Pollutant)

Santa Fe/Southern Pacific Switching:

(5% of the SP fuel usage due to UPI outbound cars)

STEP 3.

EMISSION FACTORS

The District approved emission factors for baseline calculations at the UPI facility are as follows:

Switch	Line-Haul

Engines	Engines

(lb/Kgallons)	(lb/Kgallons)

Nitrogen Oxides (NOx)	718.3	535.7

Carbon Monoxide (CO)	75.6	52.8

Hydrocarbons (HC)	41.7	19.8

Sulfur Oxides (SOx)	71.0	71.0

PM10	18.3	13.3

(1)  SOx emission factor:  (7.1#/gal) (%S by wt) (2) (1000) as SO2

(note: sulfur content of 0.5% is being used based on line haul fuel)

STEP 4.

CALCULATED MONTHLY AND DAILY EMISSIONS

To be kept by USS-Posco on a daily record keeping basis.  The records which are required to be submitted to the District pursuant to Condition 2 on the entire modernization project may be submitted in the form of the attached summary sheets or in such other format as the Air Pollution Control Officer may approve.

DAILY RECORD OF RAIL TRANSPORT

RAW COILS

Note:   Use one Daily Record form for each shipment.

(1)   Date of receipt				______________________

(2)   Name of cargo carrier				______________________

(If the carrier is other than Union Pacific, give name of carrier.)

(3)   Number of cars				__________

(4)   Tare weight of average car                    		__________  tons

(5)   Total tare weight, (3) x (4)			__________  tons

(6)   Net weight of coils				__________  tons

(7)   Gross weight of rail cars, (5) + (6)           		__________  tons

(8)   Number of engines used by incoming train		__________

Note:   Rail Car is assumed to be a flatcar with average tare weight of 68,400 pounds.  If a different kind of rail car is used, enter the new tare weight.

DAILY RECORD OF RAIL TRANSPORT

FINISHED PRODUCTS

Sheet Steel

Note:   Use one Daily Record form for each shipment.

(1)   Date shipped				______________________

(2)   Destination (City,  State)			______________________

(3)   Type of rail cars used				______________________

(4)   Average tare weight of car	       		__________  tons

(5)   Number of cars 				__________

(6)   Total tare weight, (4) x (5)			__________  tons

(7)   Net weight of product				__________  tons

(8)   Gross weight of product, (6) + (7)			__________  tons

Note: Rail Car is assumed to be a covered gondola with an average tare weight of 75,000 pounds.  If a different kind of rail car is used, enter the new tare weight.

DAILY RECORD OF RAIL TRANSPORT

FINISHED PRODUCTS

Tinplate

Note:   Use one Daily Record form for each shipment.

(1)   Date shipped				______________________

(2)   Destination (City,  State)			______________________

(3)   Type of rail cars used				______________________

(4)   Average tare weight of car        			__________  tons

(5)   Number of cars 				__________

(6)   Total tare weight, (4) x (5)			__________  tons

(7)   Net weight of product				__________  tons

(8)   Gross weight of product, (6) + (7)			__________  tons

Note:   Rail car is assumed to be a box car with an average tare weight of 78,300 pounds.  If a different kind of car is used, enter the new tare weight.

DAILY RECORD OF RAIL TRANSPORT

SCRAP STEEL

Note:   Use one Daily Record form for each shipment.

(1)   Date shipped				______________________

(2)   Destination (City,  State)			______________________

(3)   Type of rail cars used				______________________

(4)   Average tare weight of car 			__________  tons

(5)   Number of cars 				__________

(6)   Total tare weight, 	(4) x (5)			__________  tons

(7)   Net weight of scrap				__________  tons

(8)   Gross weight of scrap, (6) + (7)			__________  tons

Note:   Rail car is assumed to be a gondola with an average tare weight of 65,900 pounds.  If a different kind of car is used, enter the new tare weight.

DAILY RECORD OF RAIL TRANSPORT

UPI SWITCH ENGINES

Fuel Deliveries

(1)   Date of delivery				______________________

(2)   Engine 1					____________  gallons

(3)   Engine 2					____________  gallons

(4)   Engine 3					____________  gallons

(5)   Engine 4	 				____________  gallons

(6)   Fuel delivered for switch engines, (2) + (3) + (4) + (5)	____________  gallons

SUMMARY OF MONTHLY RAIL TRANSPORT

FUEL USAGE  --  RAW COILS

## Line-haul transport by Union Pacific

(1)   Tare weight of rail cars				____________  tons

(2)   Gross weight of rail cars			____________  tons

(3)   Distance traveled in BAAQMD			         19.3____  miles

(4)   Unit fuel usage  (laden)				         1.37____  gal/KGTM

(5)   Unit fuel usage  (unladen)			         1.37____  gal/KGTM

(6)   Fuel usage  (inbound), (2) x (3) x (4) + 1000		____________  gallons

(7)   Fuel usage (outbound), (1) x (3) x (5) + 1000		____________  gallons

Positioning  -  Union Pacific

(8)   Number of shipments				____________

(9)   Fuel per shipment				_____10_____  gallons

(10)  Fuel Usage, (8) x (9)				____________  gallons

Idling  -  Union Pacific

(11)  Number of engines				____________

(12)  Fuel per engine				_____1.67_ __  gallons

(13)  Total Usage				____________  gallons

(14)  Total Union Pacific fuel usage, (6) + (7) + (10) + (13)	____________  gallons

SUMMARY OF MONTHLY RAIL TRANSPORT

FUEL USAGE  --  FINISHED PRODUCTS

## Transport from UPI to SF/SP Yard by Santa Fe Switch Engines

(1)   Tare weight of rail cars				____________  tons

(2)   Gross weight of rail cars			____________  tons

(3)   Distance traveled in BAAQMD			         2.0_____  miles

(4)   Unit fuel usage  				         1.78____  gal/KGTM

(5)   Fuel usage  (inbound), (1) x (3) x (4) + 1000		____________  gallons

(6)   Fuel usage  (outbound), (2) x (3) x (4) + 1000		____________  gallons

(7)   Total Santa Fe fuel usage, (5) + (6)			____________  gallons

### Transport to destination by Southern Pacific line-haul engines

Northern Route  (toward Roseville)

(8)   Distance traveled in BAAQMD			___ __37.7___  miles

(9)   Unit fuel usage				_____1.67 _ _   gal/KGTM

(10)   Fuel usage  (inbound), (1) x (8) x (9) + 1000		____________  gallons

(11)   Fuel usage  (outbound), (2) x (8) x (9) + 1000		____________  gallons

Southern Route (toward Tracy)

(12)   Distance traveled in BAAQMD			_____25.7____  miles

(13)   Unit fuel usage				_____1.67 ___  gal/KGTM

(14)   Fuel usage  (inbound), (1) x (12) x (13) + 1000	____________  gallons

(15)   Fuel usage  (outbound), (2) x (12) x (13) + 1000	____________  gallons

#### Both Routes

(16)  Total SP line-haul fuel usage, (10) + (11) + (14) + (15)	____________  gallons

Transport at SF/SP yard by Southern Pacific switch engines

(17)  Switching fuel usage as a fraction

of line-haul fuel usage				______ 0.0526

(18)   Total SP switching fuel usage, (17) x (16)		____________  gallons

Note:   Switching fuel usage is assumed to be 5 percent of the railroad’s total fuel usage in the BAAQMD.  The remaining 95 percent is for line-hauling.  Switching usage is 5.26 percent of line-hauling usage.

SUMMARY OF MONTHLY RAIL TRANSPORT

FUEL USAGE  --  SCRAP STEEL

## Transport from UPI to SF/SP Yard by Santa Fe Switch Engines

(1)   Tare weight of rail cars				____________  tons

(2)   Gross weight of rail cars			____________  tons

(3)   Distance traveled in BAAQMD			         2.0_____  miles

(4)   Unit fuel usage  				         1.78____  gal/KGTM

(5)   Fuel usage  (inbound), (1) x (3) x (4) + 1000		         ___   ___  gallons

(6)   Fuel usage  (outbound), (2) x (3) x (4) + 1000		____________  gallons

(7)   Total Santa Fe fuel usage, (5) + (6)			____________  gallons

### Transport to destination by Southern Pacific line-haul engines

Northern Route  (toward Roseville)

(8)   Distance traveled in BAAQMD			___ __37.7___  miles

(9)   Unit fuel usage				_____1.67 _ _   gal/KGTM

(10)   Fuel Usage  (inbound), (1) x (8) x (9) + 1000		____________  gallons

(11)   Fuel Usage  (outbound), (2) x (8) x (9) + 1000	____________  gallons

Southern Route (toward Tracy)

(12)   Distance traveled in BAAQMD			_____25.7____  miles

(13)   Unit fuel usage				_____1.67 ___  gal/KGTM

(14)   Fuel usage  (inbound), (1) x (12) x (13) + 1000	____________  gallons

(15)   Fuel usage  (outbound), (2) x (12) x (13) + 1000	____________  gallons

#### Both Routes

(16)  Total SP line-haul fuel usage, (10) + (11) + (14) + (15)	____________  gallons

Note:   If any scrap steel is shipped within the Bay Area Air Quality Management District, the mileage from UPI to the receiving location must be determined and entered on Line (8) or (12).

Transport at SF/SP yard by Southern Pacific switch engines

(17)   Switching fuel usage as a fraction of line-haul fuel usage	______ 0.0526

(18)   Total SP switching fuel usage, (17) x (16)		____________  gallons

Note:   Switching fuel usage is assumed to be 5 percent of the railroad’s total fuel usage in the BAAQMD.  The remaining 95 percent is for line-hauling.  Switching usage is 5.26 percent of line-hauling usage.

MONTHLY SUMMARY OF RAIL TRANSPORT

FUEL USAGE  --  UPI SWITCH ENGINES

UPI Switch Engines

(1)   Fuel delivered for switch engines		____________  gallons

SUMMARY OF MONTHLY RAIL TRANSPORT

TOTAL FUEL USAGE

ALL TRANSPORT METHODS

Line-haul engines

(1)   Union Pacific, (Page 1,  Line 14)			_____________  gallons

(2)   Southern Pacific, (Page 3,  Line 16) +(Page 5,  Line 16)	_____________  gallons

(3)   Total line-haul engines, (1) + (2)			_____________  gallons

Switch engines

(4)   Santa Fe, (Page 2,  Line 7) + (Page 4,  Line 7)		_____________  gallons

(5)   Southern Pacific, (Page 3,  Line 18) + (Page 5,  Line 18)	_____________  gallons

(6)   UPI  (Page 6,  Line 1)				_____________  gallons

(7)   Total switch engines, (4) + (5) + (6)			_____________  gallons

SUMMARY OF MONTHLY RAIL TRANSPORT

EMISSION CALCULATIONS

ALL TRANSPORT METHODS

Operation		NOx	CO	HC	SOx	PM10

Line-haul engines

Fuel use		___________  gallons  (Page 7,  Line 3)

Emission factor, (lb/1000 gal)535.7	52.8	19.8	71.0	13.3

Emissions  (tons/mo)	_____	_____	_____	_____	_____

Switch engines

Fuel use		___________  gallons  (Page 7,  Line 7)

Emission factor, (lb/1000 gal)718.3	75.6	41.7	71.0	18.3

Emissions  (tons/mo)	_____	_____	_____	_____	_____

Monthly Total

Actual Emissions, (tons/mo)_____	_____	_____	_____	_____

Prorated Baseline

Emissions (tons/mo)	_____	_____	_____	_____	_____

Calculations:

(1) Divide each category’s fuel use from previous summary sheets by 1,000 to compute 1000’s of gallons of fuel used per month.

(2) Multiply fuel use by emission factor and divide result by 2,000 to compute emissions in tons per month.

*APPENDIX A TO PERMIT CONDITION #7216, FOR SHIPS

The procedures and methodology to be used in calculating transportation emissions for the purpose of demonstrating compliance with the USS-POSCO permit condition.

The methodology and calculation procedures require gathering the raw data (STEP 1), determining fuel usage rates (STEP 2), applying pollutant specific emission factors (STEP 3).

Calculated monthly emissions shall be reported in tons and calculated daily emissions shall be reported in pounds (STEP 4).

STEP 1.

Collection of Raw Data regarding Ship Activity at USS-POSCO, Pittsburg, CA

INCOMING SHIP SHIPMENTS.  The following information, associated with each ship, shall be collected, recorded, and used in subsequent calculations:

- Arrival Date and Time

- Specify as to Type of Delivery (ex. steel coil)

- Ship Name

- DWT

- Quantity of Product Shipped (in tons)

- Distance Traveled in District

- Invoice Records for fuel oil

- CEM Charts for Main Engine for SCR-equipped ships

OUTGOING SHIP SHIPMENTS.  The following information, associated with each ship, shall be collected, recorded, and used in subsequent calculations:

- Departure Date and Time

- Specify as to Type of Delivery (empty)

- Ship Name

- DWT

- Quantity of Product Shipped (in tons, if any)

- Distance Traveled in District

- CEM Charts for Main Engine for SCR-equipped ships

STEP 2.

DETERMINING FUEL USAGE RATES

For the Main Engine use the recorded rate from the ship recorder.

For the Diesel Generator use AP-42 Equation of (0.0959 gal/Kw-Hr) (Generator Load, in Kw-Hr)

Generator Load is determined as follows:  2 generators operate at 25% load during the transit time.  During docking of the ship the 3 generators are assumed to operate at 50% power.  After docking, 1 generator is assumed to operate at 25% load. Switching to shore power for SCR-equipped ships is assumed to take 0.5 hours.

Boiler fuel usage is 30 gal/hr times the length of the voyage.

STEP 3.

EMISSION FACTORS

For Main Engines:

NOx:	lbs/day from CEM Chart for SCR-equipped ships and 750 lbs NOx/Mgal for non-SCR-equipped ships

CO:	(56.9 lbs CO/Mgal)

PM10:	(20 lbs PM10/Mgal)

POC:	(32.8 lbs POC/Mgal)

SO2:	is calculated based on 5% S in fuel calculation to be:

(Fuel Rate, gals) (7.2 lbs/gal) (0.05/100) (64/32) = SO2

For Diesel Generator:

NOx:	(222 lbs NOx/Mgal)

CO:	(53.4 lbs CO/Mgal)

POC:	(109 lbs POC/Mgal)

PM10:	(50 lbs PM10/Mgal)

SO2:	is calculated based on 0.5% S in fuel calculation to be:

(Fuel Rate, gals) (7.2 lbs/gal) (0.005/100) (64/32) = SO2

For Boiler:

NOx:	(20 lbs NOx/Mgal)

CO:	(5.0 lbs CO/Mgal)

PM10:	(2.0 lbs PM10/Mgal)

POC:	(0.2 lbs POC/Mgal)

SO2:	is calculated based on 0.5% S in fuel calculation to be:

(Fuel Rate, gals) (7.2 lbs/gal) (0.005/100) (64/32) = SO2

STEP 4.

##### CALCULATED MONTHLY AND DAILY EMISSIONS

To be kept by USS-Posco on a daily record keeping basis. The records which are required to be submitted to the District pursuant to Condition 2 on the entire modernization project may be submitted in the form of the attached summary sheets or in such other format as the Air Pollution Control Officer may approve.

End of Appendix A for permit condition # 7216

Condition # 7579

For S82, 93, 155 - Electro-Tinning Lines:

1).  Throughput           .

The total annual combined throughput at sources S-82, S-93, and S-155 shall not exceed 114.5 million amp-hr in any consecutive twelve month period.

(Basis: Voluntary Limit)

2).  Abatement

This source shall not be operated unless emissions are vented to either A-41 or A-42, Mapco Enforcer III High Efficiency Scrubber.

(Basis: Regulation 11-8, Section 93102 (c)(2))

3).  Emission Limits

Emissions of hexavalent chromeium shall not exceed 0.006 mg/amp-hr after abatement.

(Basis: Regulation 11-8, Section 93102 (c)(2))

4).  Source Test

Source Testing Protocol:  A written source test protocol shall be submitted for District approval prior to conducting any  source test for compliance. This source test protocol shall include testing methods, length  of sample period, sampling equipment and methods, as well as the planned date for the source test.

(Basis: Regulation 11-8, Section 93102 (d)(4))

5).  Record Keeping

To comply with the above parts, monthly records of current applied to this source integrated over time, in units of amp-hrs, and records of chemical addition to the source shall be kept (onsite) and maintained.  Such records shall be submitted to the BAAQMD on an annual basis via the annual update program.  These  records shall be maintained at the plant site for at least one five years.

(Basis: Regulation 11-8, Section 93102 (h)(4)(A))

6.  In order to demonstrate compliance with the emission limit is part 3, the owner/operator of this equipment shall conduct District approved source testing of both scrubber systems every two years. The initial source test required by this part shall be conducted no later than July 1, 2004. Subsequent testing shall be performed no later than 24 months from the previous test. The Director of the Compliance and Enforcement Division of the District shall be contacted to obtain approval of the source test procedures at least 14 days in advance of each source test. The Director of the Compliance and Enforcement Division shall be notified of the scheduled test date at least 7 days in advance of each source test. The source test report shall be submitted to the Compliance and Enforcement Division and to the Director of the Compliance and Enforcement Division within 45 days of the test date.

(basis: Regulation 2-1-304)

Condition # 12194

For S286, 287 - Chrome Recovery Unit (CRU) Evaporators

1). Total combined emissions of hexavalent chromeium from chrome recovery unit evaporators S-286 and S-287, shall not exceed 0.87 lb in any consecutive twelve month period.  The ventilation and exhaust systems shall be properly maintained and kept in good operative condition.

(Basis: Toxic Risk Screen)

2). To demonstrate compliance with part Condition 1, above, a District-approved source test shall be performed (according to an approved protocol) on the evaporator system. The owner/operator of this equipment shall conduct District approved source testing of both scrubber systems every two years. The initial source test required by this part for each source shall be conducted the later of July 1, 2004 or within six months of any operation occurring on or after the Major Facility Review Permit issuance date.   Subsequent testing shall be performed no later than 24 months from the previous test.

This source test shall be conducted according to the requirements of either CARB Method 425 or EPA Method 306.  This source test shall determine the mass emissions of both total and hexavalent chromium in units of g/hr and mg/dscm as emitted after abatement.  A complete report shall be submitted within 45 days of the test date to the Director of the Compliance and Enforcement Division District's Source Test Manager and Permit Services Division Manager and shall demonstrate compliance with part Condition 1, above.

Source Testing Protocol:  A written source test protocol shall be submitted at least 14 days in advance of each source test to the Director of the Compliance and Enforcement Division for District approval prior to conducting any source test for compliance.  This source test protocol shall include testing methods, length of sample period, facilities to be operated during the source test, parameters to be monitored during the source test, sampling equipment and  methods, as well as the planned date for the source test. The Director of the Compliance and Enforcement Division shall be notified of the scheduled test date at least 7 days in advance of each source test.

(Basis: Toxic Risk Screen)

3). Ongoing Compliance Monitoring

To demonstrate ongoing compliance with part Condition 1, above, USS Posco shall keep monthly records of hexavalent and total chrome emissions.  Emissions of total and hexavalent chrome shall be estimated by multiplying the chrome emission rates in grams per hour as determined by the source test required in part Condition 2, by the monthly evaporator system hours of operation.

(Basis: Toxic Risk Screen)

4). Evaporator System Hours of Operation

To comply with part Condition 3, above, USS Posco shall install, maintain, and utilize a non-resettable clock on the evaporators to track and record the hours of operation.

(Basis: Toxic Risk Screen)

5). Recordkeeping

Source Test  Results:  USS Posco shall keep and maintain onsite records of all source tests performed on the exhaust stream for sources S-286 and S-287.

Hours of Operation:  USS Posco shall keep and maintain onsite records of monthly hours of operation of the chrome recovery unit evaporator system.

Retention of Records:  All of the above records shall be maintained for at least two five years following the close of the recording year.

(Basis: Toxic Risk Screen)

Condition # 12790

For S217 - Cold Cleaner, Graymills, Liftkleen T2420, 47 gallon capacity

1. The net amount of "Safety-Kleen 105” and/or “Safety-Kleen Premium" used at S-217, Cold Cleaner, shall not exceed 55 gallons in any consecutive twelve-month period.

(Basis: cumulative increase, toxic risk screen)

2. Solvents other than the materials specified in part condition #1 may be used at S-217, provided that the owner/operator can demonstrate that all of the following are satisfied:

a. Total VOC emissions from S-217 do not exceed 358 pounds in any consecutive twelve month period; and

b. The use of these materials do not increase toxic emissions above any risk screening trigger level; and

c. All solvents used shall meet the definition of a "Compound with Low Volatility" in Regulation 8 Rule 16.

(Basis: cumulative increase, toxic risk screen, Regulation 8-16-118.2)

3. In order to demonstrate compliance with the above condition, the following records shall be maintained on a District approved log.  Entries shall be made to the records whenever solvent is added or removed from the source.  These records shall be kept on site, summarized on a quarterly basis, and made available for District inspection for a period of 60 months from the date on which a record is made.

a. Type and monthly usage of all VOC containing materials used;

b. If a material other than that specified in part condition #1 is used, VOC and toxic component contents of each material used; and mass emission calculations to demonstrate compliance with part condition #2, on a monthly basis;

c. Monthly usage and/or emission calculations shall be totaled for each consecutive twelve-month period;

d. Quantities of each type of solvent recovered for disposal or recycling

e. Net usage of each type of solvent

(Basis: toxic risk screen, cumulative increase, reasonably available control technology, Regulation 1-441)

Condition # 12997

For S158 (G6331) - Gasoline Dispensing Island

Pursuant to BAAQMD Toxic Section policy, this facility's annual gasoline throughput shall not exceed 1.01 million gallons in any consecutive 12 month period.

(Basis: toxic risk screen)

Condition # 13634

For S289 and 290 - Continuous Galvanize Line Stenciller:

1. Combined usage of ink and cleanup solvent at sources S-289, and S-290 and S291 shall not exceed the following limits, in any calendar year:

a.   Matthews JAM-4013 Black Ink   900 gallons

b.   Pannier #1001 Black Ink               60 gallons

c.   Marsh T-Grade Dye                        5 gallons

d.   Matthews JAM-4500 Cleaner       60 gallons

e.   Pannier 1060 Solvent                  180 gallons

(Basis: Cumulative increase)

2. Inks and solvents other than the materials specified in part Condition 1 may be used at sources S-289, and S-290 and S-291, provided that the Permit Holder can demonstrate that both of the following are satisfied:

a.   Total combined POC emissions from S-289, and 290 and 291, do not exceed 7800 pounds per calendar year; and

b.   The use of these materials does not increase toxic emissions above any risk screening trigger level.

(Basis: Cumulative increase, risk management policy)

3. To determine compliance with the above conditions, the Permit Holder shall maintain the following records and provide all of the data necessary to evaluate compliance with the above conditions parts, including the following information:

a.   Type and quarterly usage of all POC containing materials used;

b.   If a material other than those specified in part Condition 1 is used, POC and toxic component

contents of each material used; and mass emission calculations to demonstrate compliance with part Condition 2, on a quarterly basis;

All records shall be retained on-site for two five years, from the date of entry, and made available for inspection by District staff upon request.

(Basis: Cumulative increase, risk management policy)

4. The cumulative emission increase for this application is 6189.6 lb/yr POC.  This increase is partially offset by contemporaneous emission reductions totaling 4400.2 lb/yr POC.  The remaining balance of 1789.4 lb/yr (0.895 TPY) is offset at a ratio of 1.15:1.0 with 1.03 TPY of NOx credits from Banking Certificate No. 490. If UPI wishes to reduce the emission limit of 7800 lb/yr in part Condition 2a, the District will refund the corresponding NOx emission credits that were used to offset this application, less the 15% incremental offset ratio, up to a total of 0.895 TPY.  If the Permit Holder can demonstrate that emissions from S-289, 290 and 291 never reached 7800 lb/yr, the District will also refund the 15% incremental offset ratio, based on the difference between highest actual emissions and 7800 lb/yr.

(Basis: Cumulative increase)

Condition # 13910

For S -96, Tin Anode Casting Furnace, and S-97, Tin Anode Casting Pot

1.   Source 96, Tin Anode Casting Furnace, and Source 97,

Tin Anode Casting Pot, are approved to operate the

Regulation 11, Rule 15, Section (g) Alternate

Compliance Option in lieu of Regulation 11, Rule 15,

Sections (b) (2) (A) and (b) (2) (C), provided the

permit holder complies with the following parts conditions 2

through 5.

2.   Source 96 and Source 97 shall be abated by A-45, Tin

Anode Casting Dust Collector, during all periods of

operation.

3.   A-45, Tin Anode Casting Dust Collector, shall meet one

of the following:

a.   Particulate grain loading in the exhaust of A-45

shall not exceed 0.01 grains/dscf; or

b.   The particulate removal efficiency [(inlet-outlet)

/ inlet] shall be greater than or equal to 99%, on

a mass basis.

4.   In order to demonstrate compliance with part Condition 3

above, the permit holder shall perform a District

approved source test annually, in accordance with the

District's Manual of Procedures.  The permit holder

shall notify the Manager of the District's Source Test

Section at least seven (7) days prior to the test, to

provide the District staff the option of observing the

testing.  Within 45 days of test completion, a

comprehensive report of the test results shall be

submitted to the Manager of the District's Source Test

Section for review and disposition.  In the event that

the District performs a source test that demonstrates

compliance with part Condition 3, the Permit Holder need not

conduct another test that year.  Following three

consecutive annual source tests which demonstrate

compliance, subsequent tests shall be performed at

least once every two years.  If any source test

confirms a violation of part Condition 3, future source

testing shall be conducted annually until such time as

three consecutive annual tests demonstrate compliance.

The District, in agreement with the applicant, may

elect to discontinue or further decrease the frequency

of the source testing requirement of this part condition,

provided that adequate demonstration of historical

compliance has been documented, to the satisfaction of

the Manager of the District's Toxic Section.

5.   Compliance with the emission limits and source testing

requirements in parts Conditions 3 and 4 shall be determined

by District source test procedure ST-15, or other

District-approved method.

Condition # 16682

For S292 - KMCAL Horizontal Electrostatic Oiler:

1. Usage of lubricating and rust preventative oils (coatings) at S-292 shall not exceed the following limits, in any consecutive twelve-month period:

a. Ferrocote EGL     35,000 gallons

b. Ferrocote HCL     12,000 gallons

(Basis:  Cumulative Increase or Toxic Risk Screen)

2. Coatings and cleanup solvents other than the materials specified in part Condition 1, and/or usages in excess of those specified in part Condition 1, may be used at S-292, provided that the owner/operator can demonstrate that all of the following are satisfied:

a. Total POC emissions do not exceed 1.175 tons in any consecutive twelve-month period; and

b. Total NPOC emissions do not exceed 1.175 tons in any consecutive twelve-month period; and

c. The use of these materials does not increase toxic emissions above any risk screening trigger level.

(Basis:  Emission Offsets, Toxic Risk Screen)

3. S-292 shall be abated at all times by A-46.  The overall efficiency of A-46 shall be sufficient to result in emissions of no more than 0.05 pounds of VOC per gallon of coating applied.

(Basis: Emission Offsets)

4. To determine compliance with the above parts conditions, the Permit Holder shall maintain the following records and provide all of the data necessary to evaluate compliance with the above parts conditions, including the following information:

a. Type and monthly usage of all POC containing materials used;

b. Type and monthly usage of all NPOC containing materials used

c. If a material other than those specified in part condition 1 is used, POC and toxic component contents of each material used; and mass emission calculations to demonstrate compliance with part condition 2, on a monthly basis;

d. Monthly usage and/or emission calculations shall be totaled for each consecutive twelve-month period.

e. All source tests of S-292 performed by or for the Permit Holder.

All records shall be retained on-site for five years, from the date of entry, and made available for inspection by District staff upon request.  These recordkeeping requirements shall not replace the recordkeeping requirements contained in any applicable District Regulations.

(Basis:  Emission Offsets, Toxic Risk Screen)

5. In order to demonstrate compliance with the emission limit is parts 2 and 3, the owner/operator of this equipment shall conduct District approved source testing every two years. The initial source test required by this part shall be conducted no later than July 1, 2004. Subsequent testing shall be performed no later than 24 months from the previous test. The Director of the Compliance and Enforcement Division of the District shall be contacted to obtain approval of the source test procedures at least 14 days in advance of each source test. The Director of the Compliance and Enforcement Division shall be notified of the scheduled test date at least 7 days in advance of each source test. The source test report shall be submitted to the Compliance and Enforcement Division and to the Director of the Compliance and Enforcement Division within 45 days of the test date. (basis: Regulation 2-1-304)

6. The oil mist precipitator A46 shall be properly maintained and properly operated at all times that S292 is in operation. (Basis:  Emission Offsets)

7. Within 3 months of the issuance of the Title V permit, the acceptable ranges for oil mist  precipitator voltage in DC kilovolts and current in DC milliamps shall be recorded and kept on file. Thereafter, the oil mist  precipitator shall be operated within the range of normal operating parameters for the equipment as established by the facility. (basis: Regulation 2-1-403)

8. In order to ensure the proper operation of the oil mist precipitator A46, the following items shall be inspected on at least a monthly basis. (basis: Regulation 2-1-403)

a.  oil mist  precipitator operating parameters including voltage and current

b.  evidence of visible emissions of lubricating and rust preventative oils from the exhaust of the oil mist precipitator

9. In order to demonstrate compliance with part 3, the permit holder shall keep monthly inspection records for each affected wet scrubber in a District approved log. These records shall include the following information for each unit inspected:

a. the time and date of each inspection

b. the name of the person conducting the inspection

c. the oil mist  precipatator voltage versus the established range

d. the oil mist  precipatator current versus the established current range

e. the results of each visible emissions check

f. any corrective action taken as a result of the inspection

All records shall be kept on-site and made available for District inspection for a period of five years from the date on which a record is made. (basis: Regulation 2-6-501)

Condition # 16920

For S190, 191, 194 through 196, 202, 206, 208, 210, 214, 215, and 218 - Cold Cleaners

1. Net usage at this source of:

a. Safety-Kleen 105 Solvent Recycled plus

b. Safety-Kleen Premium Solvent-California plus

c. Inland Technology Breakthrough plus

d. Ashland Chemical Company Solvent 140 3% Aromatics

shall not exceed 150 gallons per source in any consecutive 12-month period.

(basis:  Cumulative Increase)

2. Cleanup solvent other than the materials specified in part condition 1, and/or usage in excess of that specified in part condition 1, may be used, provided that the Permit Holder can demonstrate that all of the following are satisfied:

a. Total POC emissions from this source do not exceed 1,000 pounds in any consecutive 12-month period; and

b. Total NPOC emissions from this source do not exceed 1,000 pounds in any consecutive 12-month period; and

c. The use of these materials does not increase toxic emissions above any risk screening trigger level.

(basis:  Cumulative Increase and Toxic Risk Screen)

3. To determine compliance with the above conditions, the Permit Holder shall maintain the following records and provide all of the data necessary to evaluate compliance with the above conditions, including the following information:

a. Type and monthly usage of all POC and NPOC containing materials used;

b. If a material other than those specified in part condition 1 is used, POC, NPOC and toxic component contents of each material used; and mass emission calculations to demonstrate compliance with part condition 2, on a monthly basis;

c. Monthly usage and/or emission calculations shall be totaled for each consecutive 12-month period.

All records shall be retained on-site for two years, from the date of entry, and made available for inspection by District staff upon request.  These requirements shall not replace the recordkeeping requirements contained in any applicable District Regulations.

(basis:  Cumulative Increase and Toxic Risk Screen)

Condition # 18544

For S293 through 297 - Emergency Standby Generators

1. Hours of Operation:  Each source shall only be operated to mitigate emergency conditions or for reliability-related activities.  Operation for reliability-related activities shall not exceed 100 hours in any calendar year. Operation while mitigating emergency conditions is unlimited.  (Basis:  Reg. 9-8-330)

2. "Emergency Conditions" is defined as any of the following: (Basis:  Reg. 9-8-231)

a. Loss of regular natural gas supply.

b. Failure of regular electric power supply.

c. Flood mitigation.

d. Sewage overflow mitigation.

e. Fire.

f. Failure of a primary motor, but only for such time as needed to repair or replace the primary motor.

3. "Reliability-related activities" is defined as any of the following:  (Basis:  Reg. 9-8-232)

a. Operation of an emergency standby engine to test its ability to perform for an emergency use, or

b. Operation of an emergency standby engine during maintenance of a primary motor.

24. Each emergency standby engine shall be equipped with a non-resettable totalizing meter that measures and records the hours of operation for the engine.  (Basis:  Reg. 9-8-530)

35.  Records: The following monthly records shall be maintained in a District-approved log for at least 25 years and shall be made available for District inspection upon request:  (Basis:  Reg. 9-8-530)

a. Total hours of operation for each source.

b. Hours of operation under emergency conditions for each source and a description of the nature of each emergency condition.

c. Fuel usage for each source.

4. S293 through 297 shall be fired exclusively on diesel fuel having sulfur content no greater than 0.5% by weight.  The sulfur content of the fuel oil shall be certified by the fuel oil vendor.  (Basis: Reg. 9-1-304)

Condition # 19380

For S299 - Diesel Fire Pump Packaged System, 2500 gpm with John Deere 6068 diesel engine, 240 HP

1. The Emergency Generator (S-299) shall be fired exclusively on diesel fuel having sulfur content no greater than 0.05% by weight.  The sulfur content of the fuel oil shall be certified by the fuel oil vendor.  (Basis: BACT, Cumulative Increase)

2. Hours of Operation:  S-299 shall only be operated to mitigate emergency conditions or for reliability-related activities.  Operation for reliability-related activities shall not exceed 26 hours in any calendar year. Operation while mitigating emergency conditions is unlimited.  (Basis:  Cumulative Increase)

3. "Emergency Conditions" is defined as any of the following: (Basis:  Reg. 9-8-231)

a. Loss of regular natural gas supply.

b. Failure of regular electric power supply.

c. Flood mitigation.

d. Sewage overflow mitigation.

e. Fire.

f. Failure of a primary motor, but only for such time as

needed to repair or replace the primary motor.

4. "Reliability-related activities" is defined as any of the following:  (Basis:  Reg. 9-8-232)

a. Operation of an emergency standby engine to test its

ability to perform for an emergency use, or

b. Operation of an emergency standby engine during

maintenance of a primary motor.

35. The emergency standby engine shall be equipped with a non-resettable totalizing meter that measures and records the hours of operation for the engine. (Basis: Reg. 9-8-530)

46. Records: The following monthly records shall be maintained in a District-approved log for at least 25 years and shall be made available for District inspection upon request:  (Basis:  Reg. 9-8-530)

a. Total hours of operation.

b. Hours of operation under emergency conditions and a description of the nature of each emergency condition.

c. Fuel usage.

Condition # 20038

For S400 - Contaminated Soils (SWMUs) “Out” and S401 - Contaminated Soils (CAMU) “In”:

GENERAL

1. The owner/operator shall perform the remediation project in accordance with the "California Environmental Quality Act Initial Study for USS-POSCO Industries Soil Remediation/Unit I Corrective Action Management Unit, Pittsburg, California," dated June 2002.  The Department of Toxic Substances Control (DTSC) prepared this document.  Specific mitigation measures required by the BAAQMD include the "Mitigation Measures During Remedial Activity" contained in Section IV, Environmental Impact Analysis, Part 3, Air Quality, except the BAAQMD does not:

a. require the use of a safety officer.

b. limit personnel entrances into excavations.

c. limit access to construction area(s) to approved

personnel with adequate protective equipment.

d. require air-monitoring equipment.

(basis: CEQA)

FUGITIVE PARTICULATE AND VISIBLE EMISSIONS

2. The owner/operator shall ensure that visible dust emissions from any operation of this project shall not exceed 0.5 on Ringelmann chart, for a period or periods aggregating more than 3 minutes in any hour. The owner/operator shall also ensure that dust emissions shall not result in fallout on non-USS-POSCO-owned adjacent property in any quantities as to cause annoyance to any person, or public nuisance per Regulation 1-301. This part condition shall not apply to an emission from an engine used to propel a motor vehicle.

(basis: BACT, Regulation 1-301)

3. The owner/operator shall ensure that trucks hauling material on-site are covered, and/or maintain a two-foot minimum freeboard, and/or have the top layer watered. If any one of these abatement techniques is not effective to comply with part condition #2, then the District will require additional control measures as deemed necessary by the District. (basis: BACT)

4. The owner/operator shall retain the following records in a District approved logbook. These records shall be kept on site for a period of at least 5 years from the date on which a record is made, and shall be made available to the District staff for inspection.

(basis: Cumulative increase}

a. Daily hours of operation at each Solid Waste Management Unit (SWMU).

b. Daily amount of material placed into a stockpile(s) at each SWMU.

c. Daily throughput of material removed from each SWMU

d. Daily amount of material received at the Corrective Action Management Unit (CAMU).

e. Daily number of trucks used to haul material from a SWMU to the CAMU.

f. Daily number of trucks used to haul material from a SWMU to an off-site location.

Condition #20790

General Conditions for Sources Abated by Baghouses: S97, S134, S166, S167, S168, S176, S178, S179, S182

1.	Each baghouse shall be properly maintained and properly operated at all times that its associated PM emissions source(s) is/are in operation. (basis: Regulation 2-1-403)

2.	Within 6 months of the issuance of the Title V permit, each baghouse shall be equipped with a magnahelic gauge or other approved device to measure the pressure drop across the filter bags. The pressure drop across the baghouse shall be maintained within the range recommended by the manufacturer or normal operating range established by the facility. The established pressure drop range for each baghouse shall be recorded and kept on file. (basis: Regulation 2-1-403)

3.	In order to ensure the proper operation of each affected baghouse, the following items shall be inspected on at least a monthly basis. (basis: Regulation 2-1-403)

a.	the measured pressure drop across the baghouse is within the established pressure drop range

b.	evidence of visible particulate emissions from the exhaust of the baghouse

4.	If a baghouse is found to be operating outside of the established pressure drop range or if there is evidence of visible particulate emissions from the exhaust of the baghouse, a visual inspection of the filter bags shall be conducted. Filter bags exhibiting holes, tearing, or significant wear shall be replaced. After any corrective action has been taken, the baghouse shall be re-inspected in accordance with part 3. (basis: Regulation 2-1-403)

5.	In order to demonstrate compliance with parts 3 and 4, the permit holder shall keep monthly inspection records for each affected baghouse in a District approved log. These records shall include the following information for each baghouse:

a. the time and date of each inspection

b the name of the person conducting the inspection

c. the measured pressure drop versus the established pressure drop range

d. the results of each visible particulate emissions check

e. the observed condition of the filter bags when a visual inspection is performed

f. any corrective action taken as a result of the inspection

All records shall be kept on-site and made available for District inspection for a period of five years from the date on which a record is made. (basis: Regulation 2-6-501)

Condition #20791

General Conditions for Sources Abated by Wet Scrubbers: S169, S171, S173, S177 through S182, S286, S287

1.	Each wet scrubber shall be properly maintained and properly operated at all times that its associated PM emissions source(s) is/are in operation. (basis: Regulation 2-1-403)

2.	Within 9 months of the issuance of the Title V permit, each wet scrubber shall be equipped with devices to measure the scrubber liquid flow rate and the gas stream pressure drop across the scrubber. If a demister is downstream of a scrubber, the Owner/Operator may consider the demister to be part of the wet scrubber and measure the gas stream pressure drop across the scrubber plus demister.  Within 12 months of the issuance of the Title V permit, the acceptable ranges for scrubber liquid flow rate and gas stream pressure drop across the unit shall be recorded for each affected wet scrubber and kept on file. Thereafter, each scrubber shall be operated within the range of normal operating parameters for the equipment as established by the facility. (basis: Regulation 2-1-403)

3.	In order to ensure the proper operation of each affected wet scrubber, the following items shall be inspected on at least a monthly basis. (basis: Regulation 2-1-403)

a.	scrubber operating parameters including liquid flow rate and gas stream pressure drop (following the installation of monitoring equipment in accordance with part 2)

b.	evidence of visible particulate emissions from the exhaust of the scrubber

4.	In order to demonstrate compliance with part 3, the permit holder shall keep monthly inspection records for each affected wet scrubber in a District approved log. These records shall include the following information for each unit inspected:

a. the time and date of each inspection

b. the name of the person conducting the inspection

c. the liquid flow rate versus the established range

d. the measured gas stream pressure drop versus the established pressure drop range

e. the results of each visible particulate emissions check

f. any corrective action taken as a result of the inspection

All records shall be kept on-site and made available for District inspection for a period of five years from the date on which a record is made. (basis: Regulation 2-6-501)

Condition #20866

For S300 through S311, Solvent Cleaners, System One, Model 570, 35 Gal and S312, Solvent Cleaner, ZEP, Model 9066, 45 Gal

1.	The Owner/Operator of Cold Cleaners S300 through S312 shall not exceed the following usage limits for each cleaner during any consecutive twelve-month period:

Methylated Siloxane	40 gallons/year/cleaner

(Basis:  Cumulative Emissions)

2.	The Owner/Operator of sources S300 through S312 may use solvent other than the material specified in Part 1 above, and/or usages in excess of those specified in Part 1 above, provided that the Owner Operator can demonstrate that all of the following are satisfied:

a.	S300 through S312 Cold Cleaners comply with Regulations 8-16-303.4 and 8-16-303.5;

b.	The total NPOC combined emissions from S300 through S312 do not exceed 4108 pounds in any consecutive twelve-month period; and

c.	The use of these materials does not increase toxic emissions above any risk screening trigger level.

(Basis:  Cumulative Emissions)

3.	To determine compliance with the above conditions, the Owner/Operator shall maintain the following records and provide all of the data necessary to evaluate compliance with the above conditions, including the following information:

a.	Quantities of solvent used at each source on a monthly basis.

b.	If a material other than that specified in Part 1 above is used, NPOC and toxic component contents of each material used; and mass emission calculations to demonstrate compliance with Part 2, on a monthly basis,

c.	Monthly usage and/or emission calculations shall be totaled for each consecutive twelve-month period.

(Basis:  Cumulative Emissions)

# APPLICABLE LIMITS & COMPLIANCE MONITORING REQUIREMENTS

This section has been included to summarize the applicable emission limits contained in Section IV, Source-Specific Applicable Requirements, of this permit.  The following tables show the relationship between each emission limit and the associated compliance monitoring provisions, if any.  The monitoring frequency column indicates whether periodic (P) or continuous (C) monitoring is required.  For periodic monitoring, the frequency of the monitoring has also been shown using the following codes: annual (A), quarterly (Q), monthly (M), weekly (W), daily (D), hourly (H), or on an event basis (E).  No monitoring (N) has been required if the current applicable rule or regulation does not require monitoring, and the operation is unlikely to deviate from the applicable emission limit based upon the nature of the operation.

| Table VII – A Applicable Limits and Compliance Monitoring Requirements S43 #1 Continuous Annealing Line – Annealing Furnace S70 - Annealing Furnace |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr |  | N |  |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 gr/dscf @ 6% oxygen |  | N |  |
| SO2 | BAAQMD Regulation 9-1-301 | Y |  | ground level concentrations shall not exceed: 0.5 ppm for 3 consecutive minutes AND 0.25 ppm averaged over 60 consecutive minutes AND 0.05 ppm averaged over 24 hours |  | N |  |
|  | BAAQMD Regulation 9-1-302 | Y |  | 300 ppmdv |  | N |  |

| Table VII - B Applicable Limits and Compliance Monitoring Requirements S65 - #1 Continuous Galvanizing Line – Zinc Coating Pot |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr |  | N |  |
| FP | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr |  | N |  |
| Arsenic and cadmium | BAAQMD 11-15-93107(c)(2) | N |  | < 0.002% arsenic and < 0.004% cadmium | BAAQMD 11-15-93107(e)(2) | P/Each batch | Vendor certification |
| Steel Through-put | BAAQMD Condition #7216, part I. 1 | Y |  | 218,776 tons/yr | BAAQMD Condition #7216, part I. 2 | P/D | Record keeping |

| Table VII - C Applicable Limits and Compliance Monitoring Requirements S72 - #2 Continuous Galvanizing Line – Zinc Coating Pot |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr |  | N |  |
| FP | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr |  | N |  |
| Arsenic and cadmium | BAAQMD 11-15-93107(c)(2) | N |  | < 0.002% arsenic and < 0.004% cadmium | BAAQMD 11-15-93107(e)(2) | P/Each batch | Vendor certification |

| Table VII - D Applicable Limits and Compliance Monitoring Requirements S80 - #1 Electro-Tinning Line – Pickling Section S91 - #3 Electro-Tinning Line – Pickling Section |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr |  | N |  |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf |  | N |  |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr |  | N |  |

| Table VII - E Applicable Limits and Compliance Monitoring Requirements S82 - #1 Electro-Tinning Line – Chemical Treatment Section S93 - #3 Electro-Tinning Line – Chemical Treatment Section S155 - No. 1 Electro-tinning (tin free steel cell) |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD 11-8-93102(e)(2) plus (h)(4) | P/Weekly | Pressure drop monitoring |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD 11-8-93102(e)(2) plus (h)(4) | P/Weekly | Pressure drop monitoring |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD 11-8-93102(e)(2) plus (h)(4) | P/Weekly | Pressure drop monitoring |
| Hexavalent Chromium | BAAQMD 11-8-93102(c)(2) | Y |  | 0.01 mg/dscm of air | BAAQMD 11-8-93102(e)(1) plus (h)(4) | P/Monthly | Ampere-hour meter |
|  | BAAQMD 11-8-93102(c)(2) | Y |  | 0.01 mg/dscm of air | BAAQMD 11-8-93102(e)(2) plus (h)(4) | P/Weekly | Pressure drop monitoring |
|  | BAAQMD 11-8-93102(c)(2) | Y |  | 0.01 mg/dscm of air | BAAQMD Condition #7579, part 6 | P/Every two years | Source test |
|  | BAAQMD Condition #7579, part 3 | Y |  | 0.006 mg/amp-hr | BAAQMD Condition #7579, part 6 | P/Every two years | Source test |
|  | BAAQMD Condition #7579, part 3 | Y |  | 0.006 mg/amp-hr | BAAQMD 11-8-93102(e)(2) | C | Pressure drop monitoring |
| Annual Amp-hr limit | BAAQMD Condition #7579, part 1 | Y |  | 114.5 million amp-hr/12 months | BAAQMD 11-8-93102(h)(4) (A) and BAAQMD Condition #7579, part 1 | P/Monthly | Ampere-hour meter |

| Table VII - F Applicable Limits and Compliance Monitoring Requirements S97 – Tin Finishing – Tin Anode Casting Pot S134 – Terminal Treatment Plant – Lime Handling |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  |  | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  |  | Y |  | 0.15 gr/dscf | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  |  | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |

| Table VII - G Applicable Limits and Compliance Monitoring Requirements S130 – Oil Separation Unit and S133 – Terminal Water treatment Plant |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| VOC | BAAQMD 8-8-112 | Y |  | 1.0 ppmv critical organic compounds | BAAQMD 8-8-502 | P/6 months | Sample analysis |

| Table VII - H Applicable Limits and Compliance Monitoring Requirements S149 – Paint Shop Spray Booth |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic compounds | BAAQMD 8-19-302 | Y |  | 275 grams/liter for baked coatings and 340 grams/liter for air-dried coatings | BAAQMD 8-19-501 | P/W | Record keeping |
|  | BAAQMD 8-19-312 | Y |  | 360 to 420 grams/liter for baked coatings and 420 grams/liter for air-dried coatings | BAAQMD 8-19-501 | P/W | Record keeping |
|  | BAAQMD 8-19-321 | N |  | 50 grams/liter for surface preparation solvent | BAAQMD 8-19-501 | P/M | Record keeping |

| Table VII - I Applicable Limits and Compliance Monitoring Requirements S158 – Gasoline Dispensing Island |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Gasoline Through-put | BAAQMD Condition # 12997 | N |  | 1.01 million gallons per 12-month period | BAAQMD 8-7-503.1 | P/A | Records |
| Through-put (exempt from Phase I) | BAAQMD 8-7-114 | Y |  | 1000 gallons per facility for tank integrity leak checking | BAAQMD 8-7-501 and 8-7-503.2 | P/E | Records |
| Organic Com-pounds | BAAQMD 8-7-301.6 | Y |  | All Phase I Equipment (except components with allowable leak rates) shall be leak free (<3 drops/minute) and vapor tight | BAAQMD 8-7-301.13 and 8-7-503.2 | P/A | Static Pressure Performance Test, ST-30 |
| Organic Com-pounds | BAAQMD 8-7-302.5 | Y |  | All Phase II Equipment (except components with allowable leak rates or at the nozzle/fill-pipe interface) shall Be: leak free (<3 drops/minute) and vapor tight | BAAQMD 8-7-302.14 and 8-7-503.2 | P/A | Dynamic Back Pressure Performance Test, ST-27 |

| Table VII - J Applicable Limits and Compliance Monitoring Requirements S166 - Pickling Line Coil Processor S167 - Pickling Line Butt Welder S168 - Pickling Line Stretch Leveler |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Hours of Operation | BAAQMD Condition #7216, part B. 4 | Y |  | 8640 hours per calendar year | BAAQMD Condition #7216, part M | P/M | Record keeping |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
| PM10 | BAAQMD Condition #7216, part B. 1 | Y |  | 0.670 lb/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |

| Table VII - K Applicable Limits and Compliance Monitoring Requirements S169 – Acid Pickling Line |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Hours of Operation | BAAQMD Condition #7216, part C. 4 | Y |  | 8640 hours per calendar year | BAAQMD Condition #7216, part M | P/M | Record keeping |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
| PM10 | BAAQMD Condition #7216, part C. 3 | Y |  | 0.506 lb/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| HCl | BAAQMD Condition #7216, part C. 3 | Y |  | 30 ppmv | BAAQMD Condition #7216, part K. 1 | P/5 years | Source test |

| Table VII - L Applicable Limits and Compliance Monitoring Requirements S171 – Tandem Cold Mill |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Hours of Operation | BAAQMD Condition #7216, part D. 3 | Y |  | 8640 hours per calendar year | BAAQMD Condition #7216, part M | P/M | Record keeping |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| PM10 | BAAQMD Condition #7216, part D. 4 | Y |  | 1.642 lb/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| Organic compounds | BAAQMD 8-2-301 | Y |  | Not more than 10 lbs/day VOC and not more than 300 ppmdv as C1 (either but not both can be exceeded) | BAAQMD Condition #7216, part L. 1 and 2 | P/5 years | Source test |
|  | BAAQMD Condition #7216, part D. 1 | Y |  | Maximum of 0.3 % VOC by weight | BAAQMD Condition #7216, part D. 2 | P/E | Record keeping |
|  | BAAQMD Condition #7216, part D. 4 | Y |  | 2.42 lb/hr VOC | BAAQMD Condition #7216, parts L. 1 and 2 | P/5 years | Source test |

| Table VII - M Applicable Limits and Compliance Monitoring Requirements S173 - HCD Alkaline Cleaner |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| PM10 | BAAQMD Condition #7216, part E. 1 | Y |  | 0.035 lb/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |

| Table VII - N Applicable Limits and Compliance Monitoring Requirements S174 - KM Continuous Annealing Furnace |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr |  | N |  |
| FP | BAAQMD 6-310.3 | Y |  | 0.15 gr/dscf @ 6% oxygen |  | N |  |
| SO2 | BAAQMD Regulation 9-1-301 | Y |  | ground level concentrations shall not exceed: 0.5 ppm for 3 consecutive minutes AND 0.25 ppm averaged over 60 consecutive minutes AND 0.05 ppm averaged over 24 hours |  | N |  |
|  | BAAQMD Regulation 9-1-302 | Y |  | 300 ppmdv |  | N |  |
| NOx | BAAQMD Condition #7216, part F. 1 | Y |  | Not to exceed 100 lbs/day from S174 plus S177 | BAAQMD Condition #7216, part F. 2 | C | CEMs |
|  | BAAQMD Condition #7216, part F. 4 | Y |  | Not to exceed, except during cold startup and furnace idling, 10 ppm at 3% oxygen or 90% reduction by weight or 80% reduction by weight if running thin gauge | BAAQMD Condition #7216, part F. 2 | C | CEMs |

| Table VII - O Applicable Limits and Compliance Monitoring Requirements S176 - Roll Etch Machine |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Hours of Operation | BAAQMD Condition #7216, part H. 3 | Y |  | 8640 hours per calendar year | BAAQMD Condition #7216, part M | P/M | Record keeping |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |
| PM10 | BAAQMD Condition #7216, part H. 2 | Y |  | 0.01 grain/dscf | BAAQMD Condition #20790, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD Condition #7216, part H. 2 | Y |  | 0.01 grain/dscf | BAAQMD Condition #20790, part 3 | P/M | Visual Observation |

| Table VII - P Applicable Limits and Compliance Monitoring Requirements S177 - Iron Oxide Production Roaster |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Hours of Operation | BAAQMD Condition #7216, part G. 9 | Y |  | 8640 hours per calendar year | BAAQMD Condition #7216, part M | P/A | Record keeping |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| PM10 | BAAQMD Condition #7216, part G. 10 | Y |  | 0.46 lbs/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| SO2 | BAAQMD Regulation 9-1-301 | Y |  | ground level concentrations shall not exceed: 0.5 ppm for 3 consecutive minutes AND 0.25 ppm averaged over 60 consecutive minutes AND 0.05 ppm averaged over 24 hours |  | N |  |
|  | BAAQMD Regulation 9-1-302 | Y |  | 300 ppmdv |  | N |  |
| NOx | BAAQMD Condition #7216, part G. 1 | Y |  | Not to exceed 100 lbs/day from S174 plus S177 | BAAQMD Condition #7216, part G. 2 | C | CEMs |
| HCl | BAAQMD Condition #7216, part G. 5 | Y |  | 2 ppmv | BAAQMD Condition #7216, part K. 1 | P/5 years | Source test |

| Table VII - Q Applicable Limits and Compliance Monitoring Requirements S178 - Iron Oxide Silo #1 S179 - Iron Oxide Bagging Station S182 - Iron Oxide Silo #2 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Hours of Operation | BAAQMD Condition #7216, part G. 9 | Y |  | 8640 hours per calendar year | BAAQMD Condition #7216, part M | P/M | Record keeping |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  |  | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  |  | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #7216, part K. 1 | P/5 years | Source test |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  |  | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  |  | Y |  | 0.15 gr/dscf | BAAQMD Condition #7216, part K. 1 | P/5 years | Source test |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  |  | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  |  | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #7216, part K. 1 | P/5 years | Source test |
| PM10 | BAAQMD Condition #7216, part G. 10 | Y |  | 0.46 lbs/hr | BAAQMD Condition #7216, part J. 3 | P/5 years | Source test |
| HCl | BAAQMD Condition #7216, part G. 5 | Y |  | 2 ppmv | BAAQMD Condition #7216, part K. 1 | P/5 years | Source test |

| Table VII - R Applicable Limits and Compliance Monitoring Requirements S180 - Acid Gas Adsorber #1 S181 - Acid Gas Adsorber #2 |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Hours of Operation | BAAQMD Condition #7216, part G. 9 | Y |  | 8640 hours per calendar year | BAAQMD Condition #7216, part M | P/M | Record keeping |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #7216, part J3 | P/5 years | Source test |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #7216, part J3 | P/5 years | Source test |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #7216, part J3 | P/5 years | Source test |
| PM10 | BAAQMD Condition #7216, part G. 10 | Y |  | 0.46 lbs/hr | BAAQMD Condition #7216, part J3 | P/5 years | Source test |
| HCl | BAAQMD Condition #7216, part G. 5 | Y |  | 2 ppmv | BAAQMD Condition #7216, part K. 1 | P/5 years | Source test |

| Table VII - S Applicable Limits and Compliance Monitoring Requirements S190, S191, S194 through S196, S202, S206, S208, S210, S214, S215, S218 - Cold Cleaners |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic com-pounds | BAAQMD Condition #16920, part 1 | Y |  | Net solvent usage of certain solvents not to exceed 150 gallons per 12 months | BAAQMD Condition #16920, part 3 | P/M | Record keeping |
|  | BAAQMD Condition #16920, part 2 | Y |  | Allowed usage of other solvents provided POC and NPOC emissions each less than 1,000 pounds per 12 months | BAAQMD Condition #16920, part 3 | P/M | Record keeping |

| Table VII - T Applicable Limits and Compliance Monitoring Requirements S217 - Cold Cleaner |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic com-pounds | BAAQMD Condition #12790, part 1 | Y |  | Net solvent usage of Safety Kleen solvents not to exceed 55 gallons per 12 months | BAAQMD Condition #12790, part 3 | P/M | Record keeping |
|  | BAAQMD Condition #12790, part 2 | Y |  | Allowed usage of other solvents provided POC plus NPOC emissions less than 358 pounds per 12 months | BAAQMD Condition #12790, part 3 | P/M | Record keeping |

| Table VII - U Applicable Limits and Compliance Monitoring Requirements S285 - Cold Cleaner |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic com-pounds | BAAQMD Condition #6818, part 1 | Y |  | Net solvent usage of Safety Kleen solvents not to exceed 200 gallons per 12 months | BAAQMD Condition #6818, part 3 | P/M | Record keeping |
|  | BAAQMD Condition #6818, part 2 | Y |  | Allowed usage of other solvents provided POC plus NPOC emissions less than 1,340 pounds per 12 months | BAAQMD Condition #6818, part 3 | P/M | Record keeping |

| Table VII - V Applicable Limits and Compliance Monitoring Requirements S286 - #1 CRU Evaporator - TFS Operation S287 - #2 Evaporator - ETL Lines |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-301 | Y |  | Ringelmann 1.0 for < 3 minutes/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
| FP | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-310 | Y |  | 0.15 gr/dscf | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 2, part 3 | P/M | Pressure Drop Inspection |
|  | BAAQMD 6-311 | Y |  | 4.10P0.67 lb/hr but not to exceed 40 lb/hr, where P is process weight, ton/hr | BAAQMD Condition #20791, part 3 | P/M | Visual Observation |
| Hexa-valent chromium | BAAQMD Condition #12194, part 1 | Y |  | 0.87 lbs/yr | BAAQMD Condition #12194, part 3 | P/M | Recordkeeping |
|  | BAAQMD Condition #12194, part 1 | Y |  | 0.87 lbs/yr | BAAQMD Condition #12194, part 2 | P/2 years | Source test |

| Table VII - W Applicable Limits and Compliance Monitoring Requirements S289 - #1 Continuous Galvanize Line-Strip Stenciller |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic com-pounds | BAAQMD 8-4-302.1 | Y |  | 5 tpy of POC plus NPOC | BAAQMD 8-4-501 | P/Annual | Recordkeeping |
|  | BAAQMD 8-20-110 | Y |  | < 175 pounds of POC plus NPOC per month | BAAQMD 8-20-507 | P/Monthly | Recordkeeping |
|  | BAAQMD Condition #13634, part 1 | Y |  | Combined net usage with S290 of: 900 gpy Matthews ink 60 gpy Pannier ink 5 gpy Marsh dye 60 gpy Matthews cleaner 180 gpy Pannier solvent | BAAQMD Condition #13634, part 3 | P/Q | Recordkeeping |
|  | BAAQMD Condition #13634, part 2 | Y |  | Optional emission allowance of 7,800 lbs/yr with S290 | BAAQMD Condition #13634, part 3 | P/Q | Recordkeeping |

| Table VII - X Applicable Limits and Compliance Monitoring Requirements S290 - #2 Continuous Galvanize Line-Strip Stenciller |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic com-pounds | BAAQMD 8-4-302.1 | Y |  | 5 tpy of POC plus NPOC | BAAQMD 8-4-501 | P/Annual | Recordkeeping |
|  | BAAQMD Condition #13634, part 1 | Y |  | Combined net usage with S289 of: 900 gpy Matthews ink 60 gpy Pannier ink 5 gpy Marsh dye 60 gpy Matthews cleaner 180 gpy Pannier solvent | BAAQMD Condition #13634, part 3 | P/Q | Recordkeeping |
|  | BAAQMD Condition #13634, part 2 | Y |  | Optional emission allowance of 7,800 lbs/yr with S289 | BAAQMD Condition #13634, part 3 | P/Q | Recordkeeping |

| Table VII - Y Applicable Limits and Compliance Monitoring Requirements S292 - KMCAL Horizontal Electrostatic Oiler |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic com-pounds | BAAQMD 8-11-303 | Y |  | Not more than 1.7 lb VOC/gal OR | BAAQMD 8-11-501 | P/Daily | Recordkeeping |
|  | BAAQMD 8-11-304 | Y |  | Abatement to no more than 1.0 lb VOC/gal and abatement device efficiency of at least 90% | BAAQMD 8-11-501 | P/Daily | Recordkeeping |
|  | BAAQMD 8-11-304 | Y |  | Abatement to no more than 1.0 lb VOC/gal and abatement device efficiency of at least 90% | BAAQMD Condition #16682, part 8 | P/M | Voltage and current monitoring |
|  | BAAQMD 8-11-304 | Y |  | Abatement to no more than 1.0 lb VOC/gal and abatement device efficiency of at least 90% | BAAQMD Condition #16682, part 8 | P/M | Visual Observation |
|  | BAAQMD Condition #16682, part 3 | Y |  | Control to no more than 0.05 lb/gal | BAAQMD Condition #16682, part 5 | P/2 years | Source test |
|  | BAAQMD Condition #16682, part 3 | Y |  | Control to no more than 0.05 lb/gal | BAAQMD Condition #16682, part 8 | P/M | Voltage and current monitoring |
|  | BAAQMD Condition #16682, part 3 | Y |  | Control to no more than 0.05 lb/gal | BAAQMD Condition #16682, part 8 | P/M | Visual Observation |
|  | BAAQMD Condition #16682, part 1 | Y |  | Combined net usage of: 35,000 gpy Ferrocote EGL 12,000 gpy Ferrocote HCL | BAAQMD Condition #16682, part 4 | P/M | Recordkeeping |
|  | BAAQMD Condition #16682, part 2 | Y for POC |  | Optional emission allowance of 1.175 tpy each for POC and NPOC | BAAQMD Condition #16682, part 4 | P/M | Recordkeeping |
|  | BAAQMD Condition #16682, part 2 | Y |  | Optional emission allowance of 1.175 tpy each for POC and NPOC | BAAQMD Condition #16682, part 5 | P/2 years | Source test |

| Table VII - Z Applicable Limits and Compliance Monitoring Requirements S293 - Emergency Standby Generator-TWTP, diesel fueled S294 - Emergency Standby Generator-KMCAL, diesel fueled S295 - Emergency Generator-Filter Plant, diesel fueled S296 - Standby Generator - #2 CC Line, diesel fueled S297 - Emergency Standby Generator-Computer Bldg, diesel fueled |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD Regulation 6-303 | Y |  | Ringelmann No. 2 for < 3 minutes/hour |  | N |  |
| FP | BAAQMD Regulation 6-310 | Y |  | < 0.15 grains/dscf |  | N |  |
| SO2 | BAAQMD Regulation 9-1-301 | Y |  | Property Line Ground Level Limits: < 0.5 ppm for 3 minutes and < 0.25 ppm for 60 min. and <0.05 ppm for 24 hours |  | N |  |
| SO2 | BAAQMD Regulation 9-1-304 | Y |  | Fuel Sulfur Limit: 0.5% | BAAQMD Condition # 18554, Part 4 | P/E | Vendor certification |
| Operating Hours | BAAQMD Regulation 9-8-330.2 and BAAQMD Condition # 18544, Part 1 | N |  | Operating Hours for Reliability-Related Activities: < 100 hours in a calendar year | BAAQMD Regulation 9-8-530 and BAAQMD Condition # 18554, Parts 2 and 3a | P/C, M | Meter to record operating hours |

| Table VII - AA Applicable Limits and Compliance Monitoring Requirements S299 - Diesel Fire Pump Packaged System, 2500 gpm, diesel fueled |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD Regulation 6-303 | Y |  | Ringelmann No. 2 for < 3 minutes/hour |  | N |  |
| FP | BAAQMD Regulation 6-310 | Y |  | < 0.15 grains/dscf |  | N |  |
| SO2 | BAAQMD Regulation 9-1-301 | Y |  | Property Line Ground Level Limits: < 0.5 ppm for 3 minutes and < 0.25 ppm for 60 min. and <0.05 ppm for 24 hours |  | N |  |
| SO2 | BAAQMD Regulation 9-1-304 | Y |  | Fuel Sulfur Limit: 0.5% | BAAQMD Condition # 19380, Part 1 | P/E | Vendor certification |
|  |  | Y |  | Fuel Sulfur Limit: 0.05% | BAAQMD Condition # 19380, Part 1 | P/E | Vendor certification |
| Operating Hours | BAAQMD Regulation 9-8-330.2 and BAAQMD Condition # 19380, Part 2 | N |  | Operating Hours for Reliability-Related Activities: < 26 hours in a calendar year | BAAQMD Regulation 9-8-530 and BAAQMD Condition # 19380, Parts 3 and 4a | P/C, M | Meter to record operating hours |

| Table VII - BB Applicable Limits and Compliance Monitoring Requirements S300 through 312 - Solvent Cleaners |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Organic com-pounds | BAAQMD Condition #20866, part 1 | Y |  | Methylated siloxane usage not to exceed 40 gallons per 12 months | BAAQMD Condition #20866, part 3 | P/M | Record keeping |
|  | BAAQMD Condition #20866, part 2 | Y |  | Allowed usage of other NPOC solvents provided NPOC emissions less than 4,108 pounds per 12 months for all sources | BAAQMD Condition #20866, part 3 | P/M | Record keeping |

| Table VII - CC Applicable Limits and Compliance Monitoring Requirements S400 - Contaminated Soils (SWMUs) – “Out” S401 - Contaminated Soils (CAMU) – “In” |
| --- |
| Type of Limit | Citation of Limit | FE Y/N | Future Effective Date | Limit | Monitoring Requirement Citation | Monitoring Frequency (P/C/N) | Monitoring Type |
| Opacity | BAAQMD Regulation 6-301 | Y |  | Ringelmann No. 1 for < 3 minutes/hour |  | N |  |
|  | BAAQMD Condition# 20038, Part 2 | Y |  | Ringelmann No. 0.5 for < 3 minutes/hour |  | N |  |

# TEST METHODS

The test methods associated with the emission limit of a District regulation are generally found in Section 600 et seq. of the regulation.  The following table indicates only the test methods associated with the emission limits included in Section VII, Applicable Limits & Compliance Monitoring Requirements, of this permit.

| Table VIII Test Methods |
| --- |
| Applicable Requirement | Description of Requirement | Acceptable Test Methods |
| BAAQMD 6-301 | Ringelmann No. 1 Limitation | Manual of Procedures, Volume I, Evaluation of Visible Emissions |
| BAAQMD 6-303 | Ringelmann No. 2 Limitation | Manual of Procedures, Volume I, Evaluation of Visible Emissions |
| BAAQMD 6-310 | Particulate Weight Limitation | Manual of Procedures, Volume IV, ST-15, Particulates Sampling |
| BAAQMD 6-311 | General Operations | Manual of Procedures, Volume IV, ST-15, Particulates Sampling |
| BAAQMD 8-1-110.3 | Exemption, Process Subject to Regulation 8, Rule 2 or 4 | Manual of Procedures, Volume IV, ST-7, Non-Methane Organic Carbon Sampling or EPA Method 25 or 25A. |
| BAAQMD 8-4-112 | Exemption, Organic Diluents | Manual of Procedures, Volume III, Method 9, Determination of Compliance of Solvents, Coatings, and Related Products |
| BAAQMD 8-4-302 | Limitation on Solvents and Surface Coatings (3/17/82) | Manual of Procedures, Volume IV, ST-7, Non-Methane Organic Carbon Sampling |
| BAAQMD 8-7-301.1 | Phase I Requirements | Manual of Procedures, Volume III, Method 13, Determination of the Reid Vapor Pressure of Petroleum Products |
| BAAQMD 8-7-301.2 | Phase I Requirements | Manual of Procedures, Volume IV, ST-36, Gasoline Dispensing Facility Phase I Volumetric Efficiency |
| BAAQMD 8-7-301.6 | Phase I Requirements | Manual of Procedures, Volume IV, ST-30, Gasoline Vapor Recovery Leak Test Procedure |
| BAAQMD 8-7-302.1 | Phase II Requirements | Manual of Procedures, Volume III, Method 13, Determination of the Reid Vapor Pressure of Petroleum Products |
| BAAQMD 8-7-302.5 | Phase II Requirements | Manual of Procedures, Volume IV, ST-30, Gasoline Vapor Recovery Leak Test Procedure |
| BAAQMD 8-7-311 | Exempt Tank Requirements | Manual of Procedures, Volume III, Method 13, Determination of the Reid Vapor Pressure of Petroleum Products |
| BAAQMD 8-7-312 | Removal of Gasoline | Manual of Procedures, Volume III, Method 13, Determination of the Reid Vapor Pressure of Petroleum Products |
| BAAQMD 8-7-404 | Certification of New Installations | Manual of Procedures, Volume IV, ST-27, Gasoline Dispensing Facility Dynamic Back Pressure |
| BAAQMD 8-8-112 | Exemption, Wastewater Critical OC Concentration. and/or Temperature | Manual of Procedures, Volume III, Method 33, Determination of Dissolved Critical Volatile Organic Compounds in Wastewater Separators |
| BAAQMD 8-8-303 | Gauging and Sampling Devices | EPA Reference Method 21 (40 CFR 60, Appendix A). |
| BAAQMD 8-8-305.2 | Oil-water Separator and/or Air Flotation Unit Slop Oil Vessels | Manual of Procedures, Volume IV, ST-7, Non-Methane Organic Carbon Sampling or EPA Method 25 or 25A |
| BAAQMD 8-16-114 | Exemption, Emulsion or Solution Cleaners | Manual of Procedures, Volume III, Method 31, Determination of Precursor Organic Compounds in Paint Strippers for Aerospace Assembly and Component Coating Operations |
| BAAQMD 8-16-205 | Compounds with Low Volatility | ASTM D-1078-78 |
| BAAQMD 8-16-303.1.4 | Waste Solvent Residues | Manual of Procedures, Volume III, Method 21, Determination of Compliance of Volatile Organic Compounds for Water Reducible Coatings or Manual of Procedures, Volume III, Method 22, Determination of Compliance of Volatile Organic Compounds for Solvent Based Coatings |
| BAAQMD 8-19-210 | Pretreatment Wash Primer | Measurement of acid content: ASTM Method D-613-85 |
| BAAQMD 8-19-302 | Limits | Manual of Procedures, Volume III, Method 21, Determination of Compliance of Volatile Organic Compounds for Water Reducible Coatings or Manual of Procedures, Volume III, Method 22, Determination of Compliance of Volatile Organic Compounds for Solvent Based Coatings Manual of Procedures, Volume III, Method 31, Determination of Precursor Organic Compounds in Paint Strippers for Aerospace Assembly and Component Coating Operations |
| BAAQMD 8-19-312 | Specialty Coating Limitations | Manual of Procedures, Volume III, Method 21, Determination of Compliance of Volatile Organic Compounds for Water Reducible Coatings or Manual of Procedures, Volume III, Method 22, Determination of Compliance of Volatile Organic Compounds for Solvent Based Coatings |
| BAAQMD 8-19-313 | Spray Application Equipment Limitations | Manual of Procedures, Volume IV, ST-7, Non-Methane Organic Carbon Sampling, or EPA Method 25 or 25A. |
| BAAQMD 9-1-302 | General Emission Limitation | Manual of Procedures, Volume IV, ST-19A, Sulfur Dioxide, Continuous Sampling, or ST-19B, Total Sulfur Oxides Integrated Sample |
| BAAQMD 9-1-304 | Fuel Burning (Liquid and Solid Fuels) | Manual of Procedures, Volume III, Method 10, Determination of Sulfur in Fuel Oils. |
| BAAQMD 11-8-403 | Demonstration of Compliance, Hexavalent Chrome Plating Standard | Manual of Procedures, Volume IV, ST-35, Total and Hexavalent Chromium |
| BAAQMD 11-8-404 | Initial Demonstration of Compliance, Hexavalent Chrome Plating Standard | Manual of Procedures, Volume IV, ST-35, Total and Hexavalent Chromium |
| BAAQMD Condition #7216, Part K. 1 | HCl Emission Concentration Determination | Method 26A, “Determination of Hydrogen Halide and Halogen Emissions from Stationary Sources – Isokinetic Method |

# PERMIT SHIELD

Not applicable

# GLOSSARY

# ACT

# Federal Clean Air Act

# APCO

# Air Pollution Control Officer

# ARB

# Air Resources Board

# BAAQMD

# Bay Area Air Quality Management District

# BACT

# Best Available Control Technology

# BARCT

# Best Available Retrofit Control Technology

Basis

The underlying authority that allows the District to impose requirements.

# C5

# An Organic chemical compound with five carbon atoms

# C6

# An Organic chemical compound with six carbon atoms

# CAA

# The federal Clean Air Act

# CAAQS

# California Ambient Air Quality Standards

# CAPCOA

# California Air Pollution Control Officers Association

# CEQA

# California Environmental Quality Act

CEM

A "continuous emission monitor" is a monitoring device that provides a continuous direct measurement of some pollutant (e.g. NOx concentration) in an exhaust stream.

# CFR

The Code of Federal Regulations.  40 CFR contains the implementing regulations for federal environmental statutes such as the Clean Air Act.  Parts 50-99 of 40 CFR contain the requirements for air pollution programs.

# CO

# Carbon Monoxide

# CO2

# Carbon Dioxide

# Cumulative Increase

The sum of permitted emissions from each new or modified source since a specified date pursuant to BAAQMD Rule 2-1-403, Permit Conditions (as amended by the District Board on 7/17/91) and SIP Rule 2-1-403, Permit Conditions (as approved by EPA on 6/23/95).  Used to determine whether threshold-based requirements are triggered.

# DC

# Direct Current

# DWT

# Dead Weight Ton

# District

# The Bay Area Air Quality Management District

dscf

Dry Standard Cubic Feet

dscm

Dry Standard Cubic Meter

E 6, E 9, E 12

Very large or very small number values are commonly expressed in a form called scientific notation, which consists of a decimal part multiplied by 10 raised to some power.  For example, 4.53 E 6 equals (4.53) x (106) = (4.53) x (10 x 10 x 10 x 10 x 10 x 10) = 4,530,000.  Scientific notation is used to express large or small numbers without writing out long strings of zeros.

# EPA

# The federal Environmental Protection Agency.

# Excluded

# Not subject to any District Regulations.

# Federally Enforceable, FE

All limitations and conditions which are enforceable by the Administrator of the EPA including those requirements developed pursuant to 40 CFR Part 51, subpart I (NSR), Part 52.21 (PSD), Part 60 (NSPS), Part 61 (NESHAPs), Part 63 (HAP), and Part 72 (Permits Regulation, Acid Rain), and also including limitations and conditions contained in operating permits issued under an EPA-approved program that has been incorporated into the SIP.

# FP

Filterable Particulate as measured by BAAQMD Method ST-15, Particulate.

FR

Federal Register

# GDF

# Gasoline Dispensing Facility

# GLM

# Ground Level Monitor

# grains

# 1/7000 of a pound

# HAP

Hazardous Air Pollutant.  Any pollutant listed pursuant to Section 112(b) of the Act.  Also refers to the program mandated by Title I, Section 112, of the Act and implemented by 40 CFR Part 63.

H2S

Hydrogen Sulfide

H2SO4

Sulfuric Acid

Hg

Mercury

HHV

Higher Heating Value.  The quantity of heat evolved as determined by a calorimeter where the combustion products are cooled to 60F and all water vapor is condensed to liquid.

LHV

Lower Heating Value.  Similar to the higher heating value (see HHV) except that the water produced by the combustion is not condensed but retained as vapor at 60F.

# Lighter

# "Lightering" is a transfer operation during which liquid is pumped from an ocean-going tanker vessel to a smaller vessel such as a barge.  Like any liquid transfer operation, lightering of organic liquids produces organic vapor emissions.

# Major Facility

A facility with potential emissions of: (1) at least 100 tons per year of any regulated air pollutant, (2) at least 10 tons per year of any single hazardous air pollutant, and/or (3) at least 25 tons per year of any combination of hazardous air pollutants, or such lesser quantity of hazardous air pollutants as determined by the EPA administrator.

# MFR

Major Facility Review.  The District's term for the federal operating permit program mandated by Title V of the Act and implemented by District Regulation 2, Rule 6.

# MOP

# The District's Manual of Procedures

# MSDS

# Material Safety Data Sheet

# NA

# Not Applicable

# NAAQS

# National Ambient Air Quality Standards

# NESHAPs

# National Emission Standards for Hazardous Air Pollutants.  See in 40 CFR Parts 61 and 63.

# NMHC

# Non-methane Hydrocarbons

# NMOC

Non-methane Organic Compounds (Same as NMHC)

# NOx

# Oxides of nitrogen.

# NSPS

Standards of Performance for New Stationary Sources.  Federal standards for emissions from new stationary sources.  Mandated by Title I, Section 111 of the Act, and implemented by 40 CFR Part 60 and District Regulation 10.

# NSR

New Source Review.  A federal program for pre-construction review and permitting of new and modified sources of air pollutants for which the District is classified "non-attainment".  Mandated by Title I of the Clean Air Act and implemented by 40 CFR Parts 51 and 52 as well as District Regulation 2, Rule 2.  (Note:  There are additional NSR requirements mandated by the California Clean Air Act.)

# O2

# The chemical name for naturally-occurring oxygen gas.

# Offset Requirement

A New Source Review requirement to provide federally enforceable emission offsets at a specified ratio for the emissions from a new or modified source and any pre-existing cumulative increase minus any onsite contemporaneous emission reduction credits.  Applies to emissions of POC, NOx, PM10, and SO2.

# Phase II Acid Rain Facility

A facility that generates electricity for sale through fossil-fuel combustion and is not exempted by 40 CFR 72 from Titles IV and V of the Clean Air Act.

# POC

# Precursor Organic Compounds

# PM

# Total Particulate Matter

# PM10

# Particulate matter with aerodynamic equivalent diameter of less than or equal to 10 microns

# PSD

Prevention of Significant Deterioration.  A federal program for permitting new and modified sources of air pollutants for which the District is classified "attainment" of the National Air Ambient Quality Standards.  Mandated by Title I of the Act and implemented by both 40 CFR Part 52 and District Regulation 2, Rule 2.

# SCR

# A "selective catalytic reduction" unit is an abatement device that reduces NOx concentrations in the exhaust stream of a combustion device.  SCRs utilize a catalyst, which operates at a specific temperature range, and injected ammonia to promote the conversion of NOx compounds to nitrogen gas.

# SIP

State Implementation Plan.  State and District programs and regulations approved by EPA and developed in order to attain the National Air Ambient Quality Standards.  Mandated by Title I of the Act.

# SO2

# Sulfur dioxide

# SO3

# Sulfur trioxide

THC

Total Hydrocarbons (NMHC + Methane)

therm

100,000 British Thermal Unit

# Title V

Title V of the federal Clean Air Act.  Requires a federally enforceable operating permit program for major and certain other facilities.

TOC

Total Organic Compounds (NMOC + Methane, Same as THC)

TRMP

Toxic Risk Management Plan

# TRS

# "Total reduced sulfur" is a measure of the amount of sulfur-containing compounds in a gas stream, typically a fuel gas stream, including, but not limited to, hydrogen sulfide.  The TRS content of a fuel gas determines the concentration of SO2 that will be present in the combusted fuel gas, since sulfur compounds are converted to SO2 by the combustion process.

# TSP

# Total Suspended Particulate

# TVP

# True Vapor Pressure

# TWTP

# Terminal Water Treatment Plant

# VOC

# Volatile Organic Compounds

# Units of Measure:

bbl	=	barrel of liquid (42 gallons)

bhp	=	brake-horsepower

btu	=	British Thermal Unit

C	=	degrees Celsius

F	=	degrees Fahrenheit

f3	=	cubic feet

g	=	grams

gal	=	gallon

gpd	=	gallons per day

gph	=	gallons per hour

gpm	=	gallons per minute

hp	=	horsepower

hr	=	hour

lb	=	pound

in	=	inches

kgtm	=	1000 gross ton miles

max	=	maximum

m2	=	square meter

min	=	minute

M	= 	thousand

Mg	=	mega-gram, one thousand grams

g	=	micro-gram, one millionth of a gram

MM	=	million

mm	=	millimeter

MMbtu	=	million btu

mm Hg	=	millimeters of Mercury (pressure)

MW	=	megawatts

ppmv	=	parts per million, by volume

ppmw	=	parts per million, by weight

psia	=	pounds per square inch, absolute

psig	=	pounds per square inch, gauge

scfh	=	standard cubic feet per hour

scfm	=	standard cubic feet per minute

tph	=	tons per hour

yr	=	year

# Symbols:

<		=	less than

>		=	greater than

<		=	less than or equal to

>		=	greater than or equal to

# APPLICABLE STATE IMPLEMENTATION PLAN

The Bay Area Air Quality Management District’s portion of the State Implementation Plan can be found at EPA Region 9’s website.  The address is:

http://yosemite1.epa.gov/r9/r9sips.nsf/California?ReadForm&Start=1&Count=30&Expand=3.1