About this resource:

EPA is providing this resource solely for informational purposes. The agency can not attest to the accuracy, effectiveness, legality or usefulness of the information provided, nor does the inclusion or reference of such language constitute an endorsement by EPA.

Document Name:

Walsh Bros. Dana Farber Project Specifications

Organization/Agency Responsible:

Massachusetts Dana Farber Cancer Institute

Contact:  	Joseph Breen

Associate Vice President

Walsh Brothers

Dana Farber Field Office

617-878-4800

fax:  617-582-8395

jbreen@walshbrothers.com

or

Joe Bassi

Senior Project Manager

Dana Farber Institute

617-582-8390

fax:  617-582-8395

Joe_Bassi@DFCI.HARVARD.EDU

Description:  	Dana Farber Cancer Institute – Walsh Brothers

Emission control devices are required for all diesel-powered non-road construction equipment used on the project for more than 30 days. Contractors shall use methods to control nuisance odors associated with diesel emissions from construction equipment, implement dust control measures, and comply with idling reduction requirements.

Dana Farber Cancer Institute OXIDATION CATALYST AND NO-IDLING SPECIFICATIONS

All Contractor and Sub-Contractor diesel-powered non-road construction equipment with engine horsepower (HP) ratings of 60 HP and above, which is used on the project for a period in excess of 30 days, shall be retrofitted with Emission Control Devices in order to reduce diesel emissions.  In addition, all motor vehicles and construction equipment shall comply with all pertinent local, state and federal regulations covering exhaust emission control and safety.

The reduction of emissions of volatile organic compounds (VOCs), carbon monoxide (CO), and particulate matter (PM) from diesel-powered equipment shall be accomplished by installing Retrofit Emission Control Devices.

The acceptable Retrofit Emission Control Devices for the project shall consist of oxidation catalysts that (1) are included on the Environmental Protection Agency (EPA) Verified Retrofit Technology List; and (2) are verified by EPA or certified by the manufacturer to provide a minimum emissions reduction of 42 percent for VOCs, 31 percent for CO and 20 percent for PM.  Attainment of the required reduction in PM emissions can also be accomplished by using less polluting Clean Fuels (e.g. PuriNOx).

Construction shall not proceed until the Contractor has submitted a certified list of the non-road diesel –powered construction equipment that will be retrofitted with emission control devices.  The list shall include (1) the equipment number, type, make and Contractor/Sub-Contractor; and (2) the emission control device make, model and EPA verification number.  The Contractor shall also identify any vehicles that will use Clean Fuels.  Equipment that has been retrofitted with an emission control device shall be stenciled or otherwise clearly marked as “Low Emission Equipment”

The Contractor shall submit monthly reports, updating the same information state above, including the quantity of Clean Fuel utilized.  The addition or deletion of non-road diesel equipment shall be indicated in the report.

In addition to installing the required emission control devices, the contractor shall use methods to control nuisance odors associated with diesel emissions from construction equipment including without limitation the following:  (1) turning off diesel combustion engines on construction equipment not in active use, and on trucks that are idling while waiting to load or unload material for five minutes or more; (2) locating diesel equipment away from the general public and sensitive receptors (e. g., fresh air intakes, air conditioners and windows); and (3) utilizing electronically-powered scissor/man lifts.

Any costs associated with implementing the dust control and diesel equipment emissions controls as specified in this section shall be included in the general cost of the contract, provided as an add/deduct alternate as requested on Bid Form.

Page 1 of 1