Salmonid Effects Determination Criteria

Northwest National Fire Plan Project Design and Consultation Process

January 2005

Explanatory Note:  An executive memo was sent out on XX/YY/2004 explaining the decision to not commit additional resources to updates of the Northwest National Fire Plan Project Design and Consultation Process.  This final update to the Salmonid Criteria portion of the process was done with the intent of prolonging the criteria’s utility.  Several minor comments were provided in early 2004, and this update addresses those comments.  In addition, this version of the criteria was converted to Microsoft Word.  Concerns regarding activity descriptions and other elements of the process in general are not addressed here, based on the executive decision.  Necessary supporting materials, including instructions, activity descriptions, and several relevant attachments, are available online at www.or.blm.gov/esa and should be used with this document.

TABLE OF CONTENTS

(CTRL button and mouse click will link to individual pages)

Activity Type: Abandoned Mine Restoration	1

Activity Component: 	Mine Site/Abandoned Mine Reclamation	1

Work Element:	All except where otherwise noted	1

Work Element: 	Close mine opeinings, adits, and stopes - gates, foam sealant, backfilling, blasting	2

Work Element: 	Dredge tailings restoration - aerial surveys	3

Work Element: 	Groundwater control - test	4

Work Element: 	Mine waste dump removal - Inventory and monitor	5

Work Element: 	Mine waste dump removal - test	6

Work Element: 	Mine waste dump removal - treat	7

Activity Component: 	Mining Waste Cleanup	8

Work Element:	All except where otherwise noted	8

Activity Type: 	Access and Equipment Maintenance	9

Activity Component: 	Access to work site	9

Work Element: 	Access by foot or pack animals	9

Work Element: 	Access by helicopter/aircraft	10

Work Element: 	Access by vehicle on roads, within normal use patterns	11

Work Element: 	Access by vehicle or ATV off roads or outside of normal use patterns	12

Activity Component: 	Fueling/Maintenance	13

Work Element:	All except where otherwise noted	13

Activity Type: 	Defensible Space	14

Activity Component: 	Fuels reduction	14

Work Element: 	Remove plants or plant parts	14

Work Element: 	Replace flammable plants with less flammable plants	15

Activity Component: 	Structure modifications	17

Work Element:	All except where otherwise noted	17

Activity Type: 	Forest Products	18

Activity Component: 	All except where otherwise noted	18

Work Element:	All except where otherwise noted	18

Activity Component: 	Firewood collection	19

Work Element: 	Collect firewood from already downed sources	19

Activity Component: 	Tree and Shrub Removal	20

Work Element: 	Complete or partial removal of trees or shrubs	20

Activity Type: 	Insect and Disease Suppression	21

Activity Component:	Aerial survey and application of insecticides and pesticides	21

Work Element:	 All except where otherwise noted	21

Activity Component: 	Fertilization	22

Work Element: 	Hand application of N frells	22

Activity Component: 	Ground application of pesticides	23

Work Element: 	 All except where otherwise noted	23

Activity Component: 	Ground Survey	24

Work Element: 	Walking survey	24

Activity Component: 	Manual Treatments	25

Work Element: 	 All except where otherwise noted	25

Activity Component: 	Mechanical Treatments	26

Work Element: 	Harvest/removal of fire-damaged or other high-risk trees	26

Work Element: 	Slash disposal debark/chip/or fragment, machine pile and burn	27

Work Element: 	Young stand destruction, chaining, roller chopping	29

Activity Component: 	Population Assessment and Trapping	30

Work Element: 	Sampling and trapping	30

Activity Component: 	Use of Fire	31

Work Element: 	Pulling back duff from legacy trees	31

Activity Component: 	Use of Pheromones	32

Work Element:	 All except where otherwise noted	32

Activity Type: 	Mechanical Treatments	33

Activity Component: 	Dust Abatement	33

Work Element: 	Water drafting	33

Activity Component: 	Harvest Prescription/Implementation	34

Work Element:	 All except where otherwise noted	34

Work Element: 	Dead trees: salvage, hazard tree removal	35

Work Element: 	Understory/single story treatments:  thinning	36

Activity Component: 	Killing submerchantable trees	38

Work Element:	 All except where otherwise noted	38

Activity Component: 	Logging Systems and Operations	40

Work Element:	 All except where otherwise noted	40

Activity Component: 	Reducing Soil Compaction	41

Work Element: 	Subsoiling	41

Activity Component:	Rehabilitation, removal of excess vegetation and slash	43

Work Element:	 All except where otherwise noted	43

Activity Component: 	Skid Trail/Landing Rehab	45

Work Element: 	Water bars	45

Activity Component: 	Tree Felling	46

Work Element:	 All except where otherwise noted	46

Activity Type: 	Prescribed Fire – Miscellaneous Activities	47

Activity Component: 	Fire Support	47

Work Element: 	Fire/spike camp	47

Activity Component: 	Fireline Construction/Holding Actions	48

Work Element: 	“Black” line	48

Work Element: 	“Wet” line-foam line	49

Work Element: 	Drafting to fill engines/tenders	50

Work Element: 	Explosive built fireline	51

Work Element: 	Hand built fireline	52

Work Element: 	Helicopter dipping	53

Work Element: 	Machine built fireline	54

Work Element: 	Natural barriers riparian/wetlands	55

Work Element: 	Pumping from streams/ponds using portable pumps	56

Activity Component: 	Helicopter Landing Sites and other Operational Facilities	57

Work Element: 	Helicopter support sites; refuel, alumigel mix sites, etc.	57

Activity Component: 	Ignition	58

Work Element:	 All except where otherwise noted	58

Activity Component: 	Mop-up	59

Work Element:	 All except where otherwise noted	59

Activity Type: 	Prescribed Fire – Vegetation Types	60

Activity Component: 	Aspen, Fire Regime III	60

Work Element: 	Broadcast burn, High intensity	60

Work Element: 	Broadcast burn, Low intensity	63

Work Element: 	Broadcast burn, Moderate intensity	66

Work Element: 	Thin/Broadcast Burn, High intensity	69

Work Element: 	Thin/Broadcast Burn, Low intensity	72

Work Element: 	Thin/Broadcast Burn, Moderate intensity	75

Activity Component: 	Basin big sagebrush, Fire Regime III	78

Work Element: 	Broadcast burn, High intensity	78

Work Element: 	Broadcast burn, Low intensity	81

Work Element: 	Broadcast burn, Moderate intensity	84

Work Element: 	Brushbeating/mow, High intensity	87

Work Element: 	Brushbeating/mow, Low intensity	88

Work Element: 	Brushbeating/mow, Moderate intensity	89

Work Element: 	Herbicide (Spike), High intensity	90

Work Element: 	Herbicide (Spike), Low intensity	92

Work Element: 	Herbicide (Spike), Moderate intensity	94

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III	96

Work Element: 	Broadcast burn, High intensity	96

Work Element: 	Broadcast burn, Low intensity	98

Work Element: 	Broadcast burn, Moderate intensity	101

Work Element: 	Thin/Broadcast Burn, High intensity	104

Work Element: 	Thin/Broadcast Burn, Low intensity	106

Work Element: 	Thin/Broadcast Burn, Moderate intensity	110

Work Element: 	Thin/machine pile/burn piles, High intensity	113

Work Element: 	Thin/machine pile/burn piles, Low intensity	115

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	119

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V	123

Work Element: 	Broadcast burn, High intensity	123

Work Element: 	Broadcast burn, Low intensity	125

Work Element: 	Broadcast burn, Moderate intensity	128

Work Element: 	Thin/Broadcast Burn, High intensity	131

Work Element: 	Thin/Broadcast Burn, Low intensity	134

Work Element: 	Thin/Broadcast Burn, Moderate intensity	137

Work Element: 	Thin/machine pile/burn piles, High intensity	140

Work Element: 	Thin/machine pile/burn piles, Low intensity	143

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	147

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III	151

Work Element: 	Broadcast burn, High intensity	151

Work Element: 	Broadcast burn, Low intensity	153

Work Element: 	Broadcast burn, Moderate intensity	156

Work Element: 	Thin/Broadcast Burn, High intensity	159

Work Element: 	Thin/Broadcast Burn, Low intensity	161

Work Element: 	Thin/Broadcast Burn, Moderate intensity	164

Work Element: 	Thin/machine pile/burn piles, High intensity	167

Work Element: 	Thin/machine pile/burn piles, Low intensity	169

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	173

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V	177

Work Element: 	Broadcast burn, High intensity	177

Work Element: 	Broadcast burn, Low intensity	179

Work Element: 	Broadcast burn, Moderate intensity	182

Work Element: 	Thin/Broadcast Burn, High intensity	185

Work Element: 	Thin/Broadcast Burn, Low intensity	187

Work Element: 	Thin/Broadcast Burn, Moderate intensity	190

Work Element: 	Thin/machine pile/burn piles, High intensity	193

Work Element: 	Thin/machine pile/burn piles, Low intensity	195

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	199

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III	203

Work Element: 	Broadcast burn, High intensity	203

Work Element: 	Broadcast burn, Low intensity	205

Work Element: 	Broadcast burn, Moderate intensity	208

Work Element: 	Thin/Broadcast Burn, High intensity	211

Work Element: 	Thin/Broadcast Burn, Low intensity	213

Work Element: 	Thin/Broadcast Burn, Moderate intensity	216

Work Element: 	Thin/machine pile/burn piles, High intensity	219

Work Element: 	Thin/machine pile/burn piles, Low intensity	223

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	227

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V	231

Work Element: 	Broadcast burn, High intensity	231

Work Element: 	Broadcast burn, Low intensity	233

Work Element: 	Broadcast burn, Moderate intensity	236

Work Element: 	Thin/Broadcast Burn, High intensity	239

Work Element: 	Thin/Broadcast Burn, Low intensity	241

Work Element: 	Thin/Broadcast Burn, Moderate intensity	244

Work Element: 	Thin/machine pile/burn piles, High intensity	247

Work Element: 	Thin/machine pile/burn piles, Low intensity	249

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	253

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III	257

Work Element: 	Broadcast burn, High intensity	257

Work Element: 	Broadcast burn, Low intensity	261

Work Element: 	Broadcast burn, Moderate intensity	264

Work Element: 	Thin/Broadcast Burn, High intensity	267

Work Element: 	Thin/Broadcast Burn, Low intensity	271

Work Element: 	Thin/Broadcast Burn, Moderate intensity	274

Work Element: 	Thin/machine pile/burn piles, High intensity	277

Work Element: 	Thin/machine pile/burn piles, Low intensity	280

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	284

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V	288

Work Element: 	Broadcast burn, High intensity	288

Work Element: 	Broadcast burn, Low intensity	291

Work Element: 	Broadcast burn, Moderate intensity	295

Work Element: 	Thin/Broadcast Burn, High intensity	299

Work Element: 	Thin/Broadcast Burn, Low intensity	302

Work Element: 	Thin/Broadcast Burn, Moderate intensity	306

Work Element: 	Thin/machine pile/burn piles, High intensity	309

Work Element: 	Thin/machine pile/burn piles, Low intensity	312

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	316

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III	320

Work Element: 	Broadcast burn, High intensity	320

Work Element: 	Broadcast burn, Low intensity	324

Work Element: 	Broadcast burn, Moderate intensity	327

Work Element: 	Thin/Broadcast Burn, High intensity	330

Work Element: 	Thin/Broadcast Burn, Low intensity	334

Work Element: 	Thin/Broadcast Burn, Moderate intensity	337

Work Element: 	Thin/machine pile/burn piles, High intensity	340

Work Element: 	Thin/machine pile/burn piles, Low intensity	343

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	347

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V	351

Work Element: 	Broadcast burn, High intensity	351

Work Element: 	Broadcast burn, Low intensity	354

Work Element: 	Broadcast burn, Moderate intensity	358

Work Element: 	Thin/Broadcast Burn, High intensity	362

Work Element: 	Thin/Broadcast Burn, Low intensity	365

Work Element: 	Thin/Broadcast Burn, Moderate intensity	368

Work Element: 	Thin/machine pile/burn piles, High intensity	371

Work Element: 	Thin/machine pile/burn piles, Low intensity	374

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	378

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III	382

Work Element: 	Broadcast burn, High intensity	382

Work Element: 	Broadcast burn, Low intensity	386

Work Element: 	Broadcast burn, Moderate intensity	389

Work Element: 	Thin/Broadcast Burn, High intensity	392

Work Element: 	Thin/Broadcast Burn, Low intensity	396

Work Element: 	Thin/Broadcast Burn, Moderate intensity	399

Work Element: 	Thin/machine pile/burn piles, High intensity	402

Work Element: 	Thin/machine pile/burn piles, Low intensity	405

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	409

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V	413

Work Element: 	Broadcast burn, High intensity	413

Work Element: 	Broadcast burn, Low intensity	417

Work Element: 	Broadcast burn, Moderate intensity	420

Work Element: 	Thin/Broadcast Burn, High intensity	423

Work Element: 	Thin/Broadcast Burn, Low intensity	426

Work Element: 	Thin/Broadcast Burn, Moderate intensity	429

Work Element: 	Thin/machine pile/burn piles, High intensity	432

Work Element: 	Thin/machine pile/burn piles, Low intensity	435

Work Element: 	Thin/machine pile/burn piles, Moderate intensity	439

Activity Component: 	Mountain big sagebrush, Fire Regime II	443

Work Element: 	Broadcast burn, High intensity	443

Work Element: 	Broadcast burn, Low intensity	446

Work Element: 	Broadcast burn, Moderate intensity	449

Work Element: 	Brushbeating/mow, High intensity	452

Work Element: 	Brushbeating/mow, Low intensity	453

Work Element: 	Brushbeating/mow, Moderate intensity	454

Activity Component: 	Mountain big sagebrush, Fire Regime III	455

Work Element: 	Broadcast burn, High intensity	455

Work Element: 	Broadcast burn, Low intensity	458

Work Element: 	Broadcast burn, Moderate intensity	460

Work Element: 	Brushbeating/mow, High intensity	462

Work Element: 	Brushbeating/mow, Low intensity	463

Work Element: 	Brushbeating/mow, Moderate intensity	464

Activity Component: 	Oak woodlands/oak-maple/interior chaparral/mountain brush, Fire Regime II	465

Work Element: Activity fuel/pile/burn piles, Low intensity	465

Work Element: Activity fuels/pile/burn piles, High intensity	467

Work Element: Activity fuels/pile/burn piles, Moderate intensity	469

Work Element: 	Broadcast burn, High intensity	471

Work Element: 	Broadcast burn, Low intensity	472

Work Element: 	Broadcast burn, Moderate intensity	473

Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II	474

Work Element: Activity fuels/pile/burn piles, High intensity	474

Work Element: Activity fuels/pile/burn piles, Low intensity	476

Work Element: Activity fuels/pile/burn piles, Moderate intensity	478

Work Element: Activity fuels/scattered/ broadcast burn, High intensity	480

Work Element: Activity fuels/scattered/ broadcast burn, Low intensity	484

Work Element: Activity fuels/scattered/ broadcast burn, Moderate intensity	488

Work Element: 	Broadcast burn, High intensity	492

Work Element: 	Broadcast burn, Low intensity	495

Work Element: 	Broadcast burn, Moderate intensity	498

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Reg. I	501

Work Element: 	Broadcast burn, High intensity	501

Work Element: 	Broadcast burn, Low intensity	505

Work Element: 	Broadcast burn, Moderate intensity	508

Work Element: 	Broadcast burn, Riparian areas	511

Work Element: 	Thin/pile/burn piles, High intensity	513

Work Element: 	Thin/pile/burn piles, Low intensity	516

Work Element: 	Thin/pile/burn piles, Moderate intensity	520

Work Element: 	Thin/pile/burn piles, Riparian areas	524

Work Element: 	Thin/scatter/broadcast burn, High intensity	527

Work Element: 	Thin/scatter/broadcast burn, Low intensity	531

Work Element: 	Thin/scatter/broadcast burn, Moderate intensity	535

Work Element: 	Thin/scatter/broadcast burn, Riparian areas	539

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III	542

Work Element: 	Broadcast burn, High intensity	542

Work Element: 	Broadcast burn, Low intensity	546

Work Element: 	Broadcast burn, Moderate intensity	549

Work Element: 	Broadcast burn, Riparian areas	552

Work Element: 	Thin/pile/burn piles, High intensity	553

Work Element: 	Thin/pile/burn piles, Low intensity	556

Work Element: 	Thin/pile/burn piles, Moderate intensity	560

Work Element: 	Thin/pile/burn piles, Riparian areas	564

Work Element: 	Thin/scatter/broadcast burn, High intensity	567

Work Element: 	Thin/scatter/broadcast burn, Low intensity	571

Work Element: 	Thin/scatter/broadcast burn, Moderate intensity	575

Work Element: 	Thin/scatter/broadcast burn, Riparian areas	579

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Seedling/sapling objective, Fire Regime III	582

Work Element: 	Broadcast burn, High intensity	582

Activity Component: 	Riparian mid/upper elevation, Condition Class 1, Fire Regimes III, IV, V	586

Work Element: 	Broadcast burn (thinned or not), High intensity	586

Work Element: 	Broadcast burn (thinned or not), Low intensity	590

Work Element: 	Broadcast burn (thinned or not), Moderate intensity	593

Work Element: 	Thin small trees/hand pile/burn piles, High intensity	596

Work Element: 	Thin small trees/hand pile/burn piles, Low intensity	599

Work Element: 	Thin small trees/hand pile/burn piles, Moderate intensity	603

Activity Component: 	Riparian mid/upper elevation, Condition Class 2, Fire Regimes III, IV, V	607

Work Element: 	Broadcast burn (thinned or not), High intensity	607

Work Element: 	Broadcast burn (thinned or not), Low intensity	611

Work Element: 	Broadcast burn (thinned or not), Moderate intensity	614

Work Element: 	Thin small trees/hand pile/burn piles, High intensity	618

Work Element: 	Thin small trees/hand pile/burn piles, Low intensity	621

Work Element: 	Thin small trees/hand pile/burn piles, Moderate intensity	625

Activity Component: 	Riparian mid/upper elevation, Condition Class 3, Fire Regimes III, IV, V	629

Work Element: 	Broadcast burn (thinned or not), High intensity	629

Work Element: 	Broadcast burn (thinned or not), Low intensity	633

Work Element: 	Broadcast burn (thinned or not), Moderate intensity	636

Work Element: 	Thin small trees/hand pile/burn piles, High intensity	639

Work Element: 	Thin small trees/hand pile/burn piles, Low intensity	642

Work Element: 	Thin small trees/hand pile/burn piles, Moderate intensity	646

Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV	650

Work Element: 	Broadcast burn/seed (aerial), High intensity	650

Work Element: 	Broadcast burn/seed (aerial), Low intensity	653

Work Element: 	Broadcast burn/seed (aerial), Moderate intensity	656

Work Element: 	Broadcast burn/seed (drill), High intensity	659

Work Element: 	Broadcast burn/seed (drill), Low intensity	662

Work Element: 	Broadcast burn/seed (drill), Moderate intensity	665

Work Element: 	Brushbeating/mow/seed (drill), High intensity	668

Work Element: 	Brushbeating/mow/seed (drill), Low intensity	670

Work Element: 	Brushbeating/mow/seed (drill), Moderate intensity	672

Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV	674

Work Element: 	Broadcast burn, High intensity	674

Work Element: 	Broadcast burn, Low intensity	677

Work Element: 	Broadcast burn, Moderate intensity	680

Work Element: 	Brushbeating/Mowing, High intensity	683

Work Element: 	Brushbeating/Mowing, Low intensity	684

Work Element: 	Brushbeating/Mowing, Moderate intensity	685

Work Element: 	Herbicide (Spike), High intensity	686

Work Element: 	Herbicide (Spike), Low intensity	688

Work Element: 	Herbicide (Spike), Moderate intensity	690

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III	692

Work Element: 	Broadcast burn, High intensity	692

Work Element: 	Broadcast burn, Low intensity	695

Work Element: 	Broadcast burn, Moderate intensity	698

Work Element: 	Brushbeating/mow, High intensity	701

Work Element: 	Brushbeating/mow, Low intensity	702

Work Element: 	Brushbeating/mow, Moderate intensity	703

Work Element: 	Herbicide (Spike), High intensity	704

Work Element: 	Herbicide (Spike), Low intensity	706

Work Element: 	Herbicide (Spike), Moderate intensity	708

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV	710

Work Element: 	Broadcast burn, High intensity	710

Work Element: 	Broadcast burn, Low intensity	713

Work Element: 	Broadcast burn, Moderate intensity	716

Work Element: 	Brushbeating/mow, High intensity	719

Work Element: 	Brushbeating/mow, Low intensity	720

Work Element: 	Brushbeating/mow, Moderate intensity	721

Work Element: 	Herbicide (Spike), High intensity	722

Work Element: 	Herbicide (Spike), Low intensity	724

Work Element: 	Herbicide (Spike), Moderate intensity	726

Activity Type: 	Range Infrastructure	728

Activity Component: 	Fence Construction/Reconstruction/Maintenance	728

Work Element: 	Building rock jacks	728

Work Element: 	Clearing right of way	729

Work Element: 	Digging post holes - manual/mechanical	731

Work Element: 	Onsite material cutting, gathering rocks, etc	732

Work Element: 	Stringing wire	733

Activity Component: 	Rangeland Restoration	734

Work Element: 	Chaining	734

Work Element: 	Seeding - aerial	735

Work Element: 	Seeding  disking, drilling, fertilizing, plowing	736

Activity Component: 	Water Development Construction/Reconstruction	737

Work Element: 	All water developments - clearing	737

Work Element: 	All water developments - constructing apron - rubber, metal, asphalt	738

Work Element: 	All water developments - installing troughs, storage tanks, or pits	739

Work Element: 	All water developments - transporting materials	740

Work Element: 	Earthwork  - cat, dragline, scraper	741

Work Element: 	Pipelines - Trenching	742

Work Element: 	Rock haul/material haul	743

Activity Type: 	Recreation Facilities and Operations	744

Activity Component: 	Existing Facilities Developed and Dispersed	744

Work Element:	 All except where otherwise noted	744

Activity Component: 	Install/Remove toilets	746

Work Element:	 All except where otherwise noted	746

Activity Component: 	Installation of other site amenities	747

Work Element: 	Remove trees and ground vegetation, excavate, backfill	747

Activity Component: 	Obliteration/Rehabilitation of Recreation Sites	749

Work Element: 	Install barriers (boulders, fencing, signs, etc.)	749

Work Element: 	Remove any existing site furniture	750

Work Element: 	Rip surface, re-contour, topsoil, seed, mulch	751

Activity Component: 	Water development	753

Work Element:	 All except where otherwise noted	753

Activity Type: 	Reforestation	754

Activity Component: 	Access for Reforestation Activities	754

Work Element: 	Opening closed roads, including snowplowing	754

Activity Component: 	Animal Damage Control	755

Work Element:	All except where otherwise noted	755

Activity Component: 	Artficial Shade	756

Work Element: 	Shade cards	756

Activity Component: 	Collection of Plant Propagation Materials	757

Work Element:	 All except where otherwise noted	757

Activity Component: 	Hand plant upland/riparian	758

Work Element: 	Plant trees and shrubs with hoe, bar, auger	758

Activity Component: 	Natural Regeneration Surveys	759

Work Element:	All except where otherwise noted	759

Activity Component: 	On site tree storage	760

Work Element: 	Building and maintaining snow cache	760

Activity Component: 	Return visits after planting	761

Work Element:	 All except where otherwise noted	761

Activity Component: 	Site preparation	762

Work Element:	 All except where otherwise noted	762

Work Element: 	Hand scalp/grubbing	763

Activity Type: 	Roads & Road Maintenance	764

Activity Component: 	Decommissioning Roads	764

Work Element:	 All except where otherwise noted	764

Activity Component: 	New Construction/Reconstruction	767

Work Element:	 All except where otherwise noted	767

Activity Component: 	Road Maintenance	768

Work Element: 	Adding crossdrain culverts	768

Work Element: 	Blading and grading	769

Work Element: 	Bridge maintenance - riprap, deck cleaning, guard rail repair, abutment repair	770

Work Element: 	Culvert maintenance	771

Work Element: 	Disposal site use	773

Work Element: 	Ditch cleanout	774

Work Element: 	Dust abatement - water or chemical	776

Work Element: 	Roadside brushing	778

Work Element: 	Slide removal	779

Work Element: 	Surface rocking (rock replacement)	780

Work Element: 	Traffic control	781

Activity Component: 	Road Restoration	782

Work Element: 	Bridge replacement	782

Work Element: 	Culvert installation and upgrade	783

Work Element: 	Installation of drainage dips and waterbars	785

Work Element: 	Storm proofing	786

Work Element: 	Surface material processing - in place rock crushing	787

Work Element: 	Surface shaping and draining	788

Activity Type: 	Threatened, Endangered Species Habitat Restoration	789

Activity Component: 	Aspen Restoration	789

Work Element: 	Mechanical root shearing	789

Activity Component: 	Fish population Recovery/Enhancement	790

Work Element:	 All except where otherwise noted	790

Activity Component: 	Instream Restoration	791

Work Element:	 All except where otherwise noted	791

Work Element: 	Powersaw operation	792

Activity Component: 	Interpretation/Conservation Education	793

Work Element:	 All except where otherwise noted	793

Activity Component: 	Meadow Restoration	794

Work Element: 	Mowing	794

Activity Component: 	Monitoring Fish and Wildlife	795

Work Element:	 All except where otherwise noted	795

Activity Component: 	Quarry Restoration	796

Work Element: 	Waste storage	796

Activity Component: 	Riparian Improvement	797

Work Element:	 All except where otherwise noted	797

Activity Component: 	Snag Creation	798

Work Element:	 All except where otherwise noted	798

Activity Type: 	Trails & Trail Maintenance	799

Activity Component: 	Construction/Reconstruction/Heavy Maintenance	799

Work Element: 	Blasting - surface, subsurface, and aerial	799

Work Element: 	Bridge building	800

Work Element: 	Camping	801

Work Element: 	Culvert installation	802

Work Element: 	Ford maintenance/construction	803

Work Element: 	Gravel borrowing/borrow pit	804

Work Element: 	Horses/weed-free hay	805

Work Element: 	Puncheon/turnpike construction	806

Work Element: 	Reseeding edges/banks	807

Work Element: 	Trail decommissioning	808

Work Element: 	Trail relocation away from meadows	809

Work Element: 	Tread construction	810

Activity Component: 	Light Maintenance	812

Work Element: 	Debris removal (slough, rocks, roots)	812

Work Element: 	Excavating material (borrow pits, trenches)	813

Work Element: 	Excavating material near water (gravel bar)	814

Work Element: 	Installation, clean out, and repair of drainage feature (waterbars, dips, etc)	815

Work Element: 	Log clearing and brushing - mechanical	817

Work Element: 	Log clearing and brushing - non mechanical	818

Work Element: 	Minor tread reconstruction	819

Work Element: 	Repair of land structures (punches, turnpike, steps)	820

Work Element: 	Repair of structures near water (bridges, stream fords)	821

Work Element: 	Signing (blazes, rock cairns, sign posts)	822

Activity Type: 	Watershed Restoration	823

Activity Component: 	Hillslope Erosion Control	823

Work Element:	 All except where otherwise noted	823

Work Element: 	Contour felling	824

Work Element: 	Road/landing ripping	825

Work Element: 	Terracing	826

Work Element: 	Trenching	827

Activity Component: 	In-Channel Erosion Control	828

Work Element:	 All except where otherwise noted	828

Activity Component: 	Revegetation	829

Work Element:	 All except where otherwise noted	829

Work Element: 	Site prep - surface scarification, tilling, ripping	830

Activity Component: 	Sediment Control	831

Work Element:	 All except where otherwise noted	831

Activity Component: 	Watershed Monitoring	832

Work Element:	 All except where otherwise noted	832

Work Element: 	Install gage	833

Work Element: 	Instream water/sediment collection	834

Activity Type: 	Weeds and Chemical Treatments	835

Activity Component: 	Biological Control	835

Work Element	 All except where otherwise noted	835

Work Element: 	Competitive seeding	836

Activity Component: 	Cultural Control	837

Work Element: 	Chaining	837

Work Element: 	Fertilize - by hand, machine, or aerial	838

Work Element: 	Injection/cut stump	839

Work Element: 	Mulch - by hand or machine	840

Work Element: 	Use grazing to control weeds, fencing or herding	841

Activity Component: 	Herbicide Control	842

Work Element: 	Aerial application by fixed wing or helicopter	842

Work Element	 All except where otherwise noted	843

Activity Component: 	Information	845

Work Element: 	Education/outreach	845

Activity Component: 	Manual Control	846

Work Element: 	Hand clip seed heads or pull weeds	846

Activity Component: 	Mechanical Control/Restoration	847

Work Element:	 All except where otherwise noted	847

Activity Component: 	Weed prevention	849

Work Element: 	Wash vehicles, water drafting	849

Supporting Information

Background and Instructions

Activity Descriptions

Activity Type Lists

Attachments 1-15

### Activity Type: Abandoned Mine Restoration

###### Activity Component: 	Mine Site/Abandoned Mine Reclamation

Work Element:	All except where otherwise noted	This Work Element includes:• Restore surface flow / Floodplain reclamation • Mine shaft backfilling • Removal of hazardous waste (Hazmat) • Wetlands reclamation – Remove contaminated soil • Wetlands reclamation – Restore stream channel • Wetlands reclamation – Construct repository • Tailings impoundment rehab – Water management • Tailings impoundment rehab – Cap impoundment • Dredge tailings restoration – Tailings redistribution • Dredge tailings restoration – Restore channel flow • Groundwater control – Reroute • Groundwater control – Treat

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of these activities requires site specific information. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mine Site/Abandoned Mine Reclamation

Work Element: 	Close mine opeinings, adits, and stopes - gates, foam sealant, backfilling, blasting

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No foam sealant applications, no blasting, and no backfilling within RHCAs. Prevent and minimize erosion from closing mine activities by designing and maintaining proper BMPs. No refueling with RHCA | Foam sealants are potentially toxic to salmonids. Blasting and backfilling has potential for debris/sediment to impact waters. Shock waves from blasting has potential impacts to Salmonids. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Blasting and backfiling will only be allowed in areas where materials (rocks) and or sediment may not potentially reach live waters. Prevent and minimize erosion from closing mine activities by designing and maintaining proper BMPs. For fueling, SEE: Access and Equipment Maintenance Activity Type, Fueling/Maintenance, Fueling/Maintenance of light equipment on site. | RHCAs are adequate as a buffer to prevent foam sealant applications from adversely affecting (contaminating) streams. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mine Site/Abandoned Mine Reclamation

Work Element: 	Dredge tailings restoration - aerial surveys

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | This action is small enough and located where effects would not be expected. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mine Site/Abandoned Mine Reclamation

Work Element: 	Groundwater control - test

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No drilling or heavy equipment use within the RHCA. | Sampling and testing is small enough and located where effects would not be expected. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mine Site/Abandoned Mine Reclamation

Work Element: 	Mine waste dump removal - Inventory and monitor

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Inventories and analyses have no ground disturbances. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mine Site/Abandoned Mine Reclamation

Work Element: 	Mine waste dump removal - test

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No drilling or heavy equipment within the RHCA. | Sampling and testing is small enough and located where effects would not be expected. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mine Site/Abandoned Mine Reclamation

Work Element: 	Mine waste dump removal - treat

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria | Consult locally Mine-wastes and related contaminants have the potential to produce serious/severe adverse affects. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria | Risks of contamination/transport to streams are minimal but toxicity of contaminants is great enough to justify local consultation - consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mining Waste Cleanup

Work Element:	All except where otherwise noted	This Work Element includes:• Junk removal • Preliminary Assessments, Inventories, Analyses •  Contaminated soil removal •  Barrel removal • Reclamation plan implementation

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. Mine-wastes and related contaminants have the potential to produce serious/severe adverse affects. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. Risks of contamination/transport to streams are minimal but toxicity of contaminants is great enough to justify local consultation. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Access and Equipment Maintenance

###### Activity Component: 	Access to work site

Work Element: 	Access by foot or pack animals

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Sediment and turbidity | Potentially Adverse | Stay on designated trails. Stock handling facilities, camp facilities and improvements will be located at least 300 feet from lakes, streams, and springs. Stock handlers will be educated on at-risk fish including identification, Endangered Species Act, and how to minimize adverse affects to the species and their assiociated habitat. | Criteria are sufficient to avoid potential adverse affects. Avoids sediment delivery by keeping facilities well away from streams. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Sediment and turbidity | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Access to work site

Work Element: 	Access by helicopter/aircraft

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Sediment and turbidity | Potentially Adverse | No landing of helicopters or aircraft within RHCAs. No construction of helicopter pads within RHCAs. No fueling within RHCAs. | Criteria are sufficient to avoid potential adverse affects. Avoids sediment delivery (see Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Sediment and turbidity | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Access to work site

Work Element: 	Access by vehicle on roads, within normal use patterns

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Sediment and turbidity | Potentially Adverse | Access is only allowed on existing open roads. Travel must cease when damage to the road surface will result or is occurring. No ground disturbances during spawning and incubation periods. | Criteria are sufficient to avoid potential adverse effects. Avoids sediment delivery. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Sediment and turbidity | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Access to work site

Work Element: 	Access by vehicle or ATV off roads or outside of normal use patterns

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Sediment and turbidity | Potentially Adverse | Off-road activities by vehicle or ATV are not allowed within RHCA. Outside the RHCA, activities will only be conducted on slopes of 20% or less. (see Attachment 1 - Riparian Area (RHCA) Literature Summary). No fueling of machines within RHCA's | Criteria are sufficient to avoid potential adverse affects. Avoids sediment delivery (see Attachment 1) and fuel delivery (see Attachment 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Sediment and turbidity | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Fueling/Maintenance

Work Element:	All except where otherwise noted	This Work Element includes:• Fueling/Maintenance of small equipment on site • Fueling/Maintenance of heavy equipment on site

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of these activities requires site specific knowledge. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| Action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | All helicopter fueling operations require an approved transportation, storage, and emergency spill plan. Other heavy equipment fueling operations will consist of a slip-tank not greater than 250 gallons. Maintenance operations must have spill containment and cleanup provisions. Apply PACFISH/INFISH Standard and Guideline RA-4 (fuel storage within RHCAs) for activities outside the RHCA. | Criteria are sufficient to avoid potential adverse effects. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, take, channel morphology and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Defensible Space

###### Activity Component: 	Fuels reduction

Work Element: 	Remove plants or plant parts

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. This is anticipated to be an infrequent action requiring formal consultation. Removal of plant materials could have an adverse effect on the attainment of RMOs. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | The small scale (30 to 120 feet surrounding a facility), limits the potential for adverse affects. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fuels reduction

Work Element: 	Replace flammable plants with less flammable plants

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No plant removal within RHCA. No removal of riparian vegetation. Where possible, replant using native species. For water withdrawl: No instream alteration of substrate. Water withdrawal via hose pipes (less than 1" diameter) will not reduce stream flow from the original wetted width. Screen pump or hose intake. Drafting of water for will be restricted to an area identified by a fishery biologist and/or hydrologist to prevent the potential for "take”. For plant removal, SEE: Defensible Space Activity Type, Fuels Reduction Activity Component, Remove Plants Work Element. | Planting and watering vegetation would not adversely affect at risk fish. Riparian plant species are resistant to fire. As native species are replaced by exotic plants, alterations in habitat can result from reduced streambank protection, loss of undercut bank cover, loss of overhanging vegetation cover, reduced pool depth and volume, increased erosion and fine sediment deposition on the substrate, increased stream width and thermal relationships, and decreased detrital and nutrient inputs to the stream (see Attachment 4). Screening of pump intake will prevent juvenile entrainment. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not replace riparian plant species. Where possible, use native species within RHCAs. No instream alteration of substrate. Water withdrawal via hose pipes will not reduce stream flow from the original wetted width. Screen pump or hose intake. Drafting of water for will be restricted to an area identified by a fishery biologist and/or hydrologist to prevent "take”. For plant removal, SEE: Defensible Space Activity Type, Fuels Reduction Component, Remove Plants Work Element. | Planting and watering vegetation would not adversely affect at risk fish. Riparian plant species are resistant to fire. As native species are replaced by exotic plants, alterations in habitat can result from reduced streambank protection, loss of undercut bank cover, loss of overhanging vegetation cover, reduced pool depth and volume, increased erosion and fine sediment deposition on the substrate, increased stream width and thermal relationships, and decreased detrital and nutrient inputs to the stream (see Attachment 4). Screening of pump intake will prevent juvenile entrainment. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Structure modifications

Work Element:	All except where otherwise noted	This Work Element includes: • Replace flammable roof materials •  Remove ignitable materials surrounding structures

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Removing flammable and ignitable products does not pose a risk to salmonids or habitat. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Removing flammable and ignitable products does not pose a risk to salmonids or habitat. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Forest Products

###### Activity Component: 	All except where otherwise noted

Work Element:	All except where otherwise noted	This Work Element includes all Work Elements within the following Activity Components:• Fruits, berries and nut harvest • Greenery harvest – total removal • Moss harvesting • Mushroom harvesting • Seed collection

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No camping within RHCAs. For Access: SEE - Access and Equipment Maintenance Activity Type, Access to Work Sites Activity Component. | The scale of this activity small enough to avoid potential adverse affects, with the exceptiong of camping and access. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Scale of activity is small enough to have no potential adverse affects. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Firewood collection

Work Element: 	Collect firewood from already downed sources (e.g. hazard tree removal, road maintenance, etc.)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No firewood cutting within the RHCA. SEE: Mechanical Treatment Activity Type; Harvest Prescription/Implementation Activity Component; Dead Trees; Salvage and Hazard Tree Removal Work Element | Criteria are sufficient to avoid potential adverse effects. Prevents disturbances that potentially impact LWD recruitment, erosion/sedimentation, and root strength/bank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse effect to at-risk fish species. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Tree and Shrub Removal

Work Element: 	Complete or partial removal of trees or shrubs

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Criteria for these activities cannot be developed at this scale because of the complexity. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not exceed an Equivalent Clearcut Area (ECA) of 15% (NMFS 1995 LRMP BO). | These activities do not pose the potential for adverse affect to at-risk fish species, because the RHCA is adequate to buffer effects from ground disturbances associated with the activity. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Insect and Disease Suppression

###### Activity Component:	Aerial survey and application of insecticides and pesticides

Work Element:		All except where otherwise noted	This Work Element includes:• Fixed wing/helicopter flights and application below 1500 foot altitude • Fixed wing/helicopter flights and application above 1500 foot altitude

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | The complexity of this action within RHCAs requires local consultation. Only Aerial surveys are allowed. | Consult locally. For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, and may be mediated by site specific landscape and climatic conditions. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | The complexity of this action requires local consultation. Only Aerial surveys are allowed. | Consult locally. For programmatic application of this action, the complexity of the activity requires extreme precautions, and may be mediated by site specific landscape and climatic conditions. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No Criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Fertilization

Work Element: 	Hand application of N frells

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Chemical contaminants and nutrients | Potentially Adverse | When PACFISH/INFISH standards & guidelines RA3 and RA4 are met, then add the following: do not apply within 25 feet of streams and supersaturated soils. Apply by following labeling instructions. | Implementing this criteria avoids adverse affects to fish by preventing application into water. This is not a ground disturbing activity and therefore not require a sediment buffer. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Chemical contaminants and nutrients | No Effect | No criteria. | Hand application outside the RHCA will not result in delivery of fertilizer to the stream. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Chemical contaminants and nutrients | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Ground application of pesticides

Work Element: 		All except where otherwise noted	This Work Element includes:• Backpack spraying or inoculation of individual trees with insecticide • Borax treatment of freshly cut stumps

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The range of conditions and chemical compounds requires site-specific analysis. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with listed fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The range of conditions and chemical compounds requires site-specific analysis. Until such time as the risk assessments and fate and transport models are available, broad criteria cannot be provided. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Ground Survey

Work Element: 	Walking survey

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | The scale of this activity is small enough to have no potential adverse affects. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Manual Treatments

Work Element: 		All except where otherwise noted	This Work Element includes:• Thin, selecting against species/conditions • Burning infested tree • Topping or otherwise killing and removing infested trees • Slash disposal, lop and scatter, pile or cover hand pile and burn • Pruning

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

|  | For mechanical removal of infested trees SEE: Activity Type - Mechanical Treatments; Activity Component - Harvest Prescription/Implementation; Work Element - Dead trees: salvage and hazard tree removal; thinning understory/single story treatments. For burning SEE: Activity Type - Prescribed Fire; Activity Components - all Vegetation types; Work Element - burning piles |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

###### Activity Component: 	Mechanical Treatments

Work Element: 	Harvest/removal of fire-damaged or other high-risk trees

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | Consult locally on these activities: regeneration harvest, clearcutting, seed tree harvest, shelterwood, overstory removal, partial overstory removal, sanitation, or selection harvest. See Silvicultural Considerations in Attachment 1 - RHCA Silvicultural Management Options | Criteria for these activities cannot be developed at this scale because of the complexity. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not exceed an Equivalent Clearcut Area (ECA) of 15% (NMFS 1995 LRMP BO). | Harvest activities will not alter the timing, magnitude duration, and spatial distribution of peak, high, and low flows. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mechanical Treatments

Work Element: 	Slash disposal debark/chip/or fragment, machine pile and burn

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Treatment will be conducted to avoid adverse affects to streambanks and riparian vegetation and affects to streamside shade. Treatment will occur at least one site-potential tree height from the active channel or 100 feet (whichever is greater); (See Attachment 2 - Extent of effect for stream side disturbances). Hand piling or lopping and scattering only, one site potential tree height away from the active channel, and covering no more than 10 percent of the RHCA within the action area. To avoid compaction, soils will be dry and/or frozen during treatment. | Criteria are sufficient to avoid potential adverse affects by filtering sediment produced by the disturbance (see Attachment 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Dozer piling on slopes < or equal to 40% will be limited to: ·Excavator; ·Rubber-tire skidder with grapple; ·Low soil compacting /ground disturbing equipment. Piling on slopes >40% will be limited to: ·Hand pile only. | Activities associated with piling using these criteria, will reduce potential for sediment to reach streams. The RHCA acts as an adequate buffer. See Attachment 1, Figure 4.26. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mechanical Treatments

Work Element: 	Young stand destruction, chaining, roller chopping

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Riparian veg. condition, temperature, large woody debris, water yield and sediment yield. For water drafting (SEE: Activity Type - Prescribed Fire; Activity Component - Water Drafting). | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site- specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Riparian veg. condition, temperature, large woody debris, water yield and sediment yield | Potentially Adverse | No on-site draining of antifreeze from roller drums used for roller-chopping. | These activities do not pose the potential for adverse affect to at-risk fish species because the RHCA is large enough to prevent adverse affects of erosion/sedimentation. Changes in flow regime would not result from the loss of young stands which have minimal or no influence on site hydrology/evapotranspiration. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Riparian veg. condition, temperature, large woody debris, water yield, and sediment yield. | No Effect | No criteria | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Population Assessment and Trapping

Work Element: 	Sampling and trapping

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | The scale of this activity is small enough to have no potential adverse affects. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Use of Fire

Work Element: 	Pulling back duff from legacy trees

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Using rakes and shovels would create little or no disturbance. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Use of Pheromones

Work Element:		All except where otherwise noted	This Work Element includes:• Anti-aggregate bubble caps • Trap tree baiting and removal

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Use of insect pheromones will have no effect on Salmonids or their habitats. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Mechanical Treatments

###### Activity Component: 	Dust Abatement

Work Element: 	Water drafting

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Drafting of water for dust abatement and road compacting will be restricted to an area identified by a fishery biologist and/or hydrologist to prevent "take”. Any draft suction hose used will be equipped with a screen of 3/32 inch mesh or less and will have an intake flow of less than 1 foot/second to prevent entraining juvenile fish. Also SEE Prescribed Fire Activity Type; Fireline Construction/Holding Actions Activity Component; Drafting to fill engines/tenders Work Element. | Applies National Marine Fisheries Service criteria for entrainment avoidance. These criteria were derived from previous programatic consultations (Salmonid Species Team). They were designed to avoid adverse affects to the pathway elements. There will be a negligible risk of incidental take caused by pump entrainment or screen impingement. Water drafting/pumping will maintain a continuous surface flow of the stream, without altering the original wetted width. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Harvest Prescription/Implementation

Work Element:		All except where otherwise noted	This Work Element includes:• Regeneration harvest: clearcut, seed tree, shelterwood • Overstory treatments:  overstory removal, partial overstory removal, sanitation • Selection  - all stand layers

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | Consult locally on these activities: regeneration harvest, clearcutting, seed tree harvest, shelterwood, overstory removal, partial overstory removal, sanitation, or selection harvest. See Silvicultural Considerations in Attachment 1 - RHCA Silvicultural Management Options. | Criteria for these activities cannot be developed at this scale because of the complexity. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not exceed an Equivalent Clearcut Area (ECA) of 15% (NMFS 1995 LRMP BO). | Harvest activities will not alter the timing, magnitude duration, and spatial distribution of peak, high, and low flows. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Harvest Prescription/Implementation

Work Element: 	Dead trees: salvage, hazard tree removal

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No felled trees within 25 feet of the edge of the bankfull channel, or .3 site-potential tree height, whichever is greater, (Attachment 1). Felled trees will not be removed from the RHCA (See Attachments 1 and 2). Directionally fell trees towards the stream and retain fallen trees on site. Follow PACFISH/INFISH Standard and Guideline RA-2 for reference to hazard tree removal. FOR SALVAGE: No salvage activities within the RHCA. | Leaving felled trees retains nutrients and potential LWD; other actions avoid erosion and sediment delivery. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not exceed an Equivalent Clearcut Area (ECA) of 15% (NMFS 1995 LRMP BO). No skid trails and/or landings located where erosion/sedimentation would intercept road drainage ditches. | Criteria avoids sediment delivery from skid trails and landings - RHCA buffer plus disconnection from road-related flow paths. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Harvest Prescription/Implementation

Work Element: 	Understory/single story treatments:  thinning

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No thinning, except: thinning in RHCAs will be only where present and future woody debris needs are met, and where harvest will not prevent attainment of RMOs, and adverse affects to at-risk fish can be avoided (PACFISH/INFISH TM1a). The requirement to complete a watershed analysis for this activity shall include key questions relevant to achieving RMOs and acquiring required vegetation characteristics within the RHCA Apply silvicultural practices to acquire desired characteristics needed to attain RMOs (PACFISH/INFISH TM1b). To achieve shade and woody debris needs, thinning should not be allowed within 1 site-potential tree height of the stream channel (Attachment 1). No skidding and no landings within the RHCA. SLASH: Hand piling or lopping and scattering only, one site potential tree height away from the active channel. All fueling and fuel storage areas as well as service landings will be located outside the RHCA. See Silvicultural Considerations in Attachment 1 - RHCA Silvicultural Management Options. | These criteria were derived from previous programatic consultations. They were designed to avoid adverse affects to the pathway elements. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not exceed an Equivalent Clearcut Area (ECA) of 15% (NMFS 1995 LRMP BO). | Harvest activities will not alter the timing, magnitude duration, and spatial distribution of peak, high, and low flows. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Killing submerchantable trees

Work Element:		All except where otherwise noted	This Work Element includes ALL activities within this Activity Component

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No thinning, except: thinning in RHCAs will be only where present and future woody debris needs are met, and where harvest will not prevent attainment of RMOs, and adverse affects to at-risk fish can be avoided (PACFISH/INFISH TM1a). The requirement to complete a watershed analysis for this activity shall include key questions relevant to achieving RMOs and acquiring required vegetation characteristics within the RHCA. Apply silvicultural practices to acquire desired characteristics needed to attain RMOs (PACFISH/INFISH TM1b). To achieve shade and woody debris needs, thinning should not be allowed within 1 site-potential tree height of the stream channel (Attachment 1). No skidding and no landings within the RHCA. SLASH: Hand piling or lopping and scattering only, one site potential tree height away from the active channel. All fueling and fuel storage areas as well as service landings will be located outside the RHCA. | These criteria were derived from previous programatic consultations. They were designed to avoid adverse affects to the pathway elements. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not exceed an Equivalent Clearcut Area (ECA) of 15% (NMFS 1995 LRMP BO). | Harvest activities will not alter the timing, magnitude duration, and spatial distribution of peak, high, and low flows. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Logging Systems and Operations

Work Element:		All except where otherwise noted	This Work Element includes:• Ground based logging • Helicopter • High Lead • Skyline • Hauling  • Loading • Landing 	construction and location

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria | The complexity of these activities requires site specific knowledge. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside of RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Skidding trails will not be located on slopes exceeding 40%. No skid trails perpendicular to the RHCA within 500'. No skid trails or landings on unstable slopes. Avoid sediment routing from skid trails and landings into streams. No sediment routing from skid trails landings into streams. Prevent sediment production and delivery to streams by using standard erosion and sediment control measures. No log hauling during wet weather on non-paved roads. | The RHCA is adequate as a buffer for potential sediment delivery associated with the activity (see Attachments 1 and 2). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Reducing Soil Compaction

Work Element: 	Subsoiling

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Ensure that PACFISH/INFISH standards & guidelines RM1 through RM3 are met. Avoid ground disturbances during spawning and incubation periods, then add the following: Avoid applying this action within 25' away from the bankful channel or .3 site potential tree height (whichever is greater). Avoid erosion (e.g. ripping on steep slopes) and transport that have the potential to deliver sediment to the stream (i.e. use silt fences). Use the following buffers: <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Use ripping and re-contouring only if it would lessen the existing erodability. For mulching, SEE: Watershed Restoration Activity Type; Revegetation Activity Component; Mulch application Work Element. | Criteria will prevent significant sediment input into the stream, and potential adverse affects on rooting strength so important to bank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Dozer subsoiling will only be conducted on slopes of 20% or less. | Activity outside the RHCA on gentle slopes does not pose the potential for adverse effect to at-risk fish species by restricting potential erosion and sediment delivery (Attachment 1, Figure 4.26). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component:	Rehabilitation, removal of excess vegetation and slash

Work Element:		All except where otherwise noted	This Work Element includes:• Furrowing • Patch scarification, mechanically or by hand • Dozer scarification • Dozer piling • Grapple piling • Hand piling • Piling at landings

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Treatment will be conducted to avoid adverse affects to streambanks and riparian vegetation and affects to streamside shade. Treatment will occur at least one site-potential tree height from the active channel or 100 feet (whichever is greater);(See Attachment 2 - Extent of effect for stream side disturbances). Hand piling or lopping and scattering only, one site potential tree height away from the active channel, and covering no more than 10 percent of the RHCA within the action area. To avoid compaction, soils will be and/or frozen during treatment. | Criteria are sufficient to avoid potential adverse affects by filtering sediment produced by the disturbance (see Attachment 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Dozer piling on slopes < or equal to 40% will be limited to: ·Excavator; ·Rubber-tire skidder with grapple; ·Low soil compacting /ground disturbing equipment. Piling on slopes >40% will be limited to: ·Hand pile only. | Activities associated with piling using these criteria, will reduce potential for sediment to reach streams. The RHCA acts as an adequate buffer. See Attachment 1, Figure 4.26. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Skid Trail/Landing Rehab

Work Element: 	Water bars

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | WATER BARRING or installing drain dips is allowed only within spacing specifications from the edges of the stream channel as prescribed by the Riparian Road Guide (1994) in Attachment 7 (page 11). | Water barring reduces sediment delivery potential if applied as per the criteria (Riparian Road Guide 1994). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Waterbars are intended to improve road surface drainage. RHCAs are adequate to buffer any associated sediment production. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Tree Felling

Work Element:		All except where otherwise noted	This Work Element includes:• Hand • Mechanical

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No felled trees within 25 feet of the edge of the bankfull channel, or .3 site-potential tree height, whichever is greater, (Attachment 1). Felled trees will not be removed from the RHCA (See Attachments 1 and 2). Directionally fell trees towards the stream and retain fallen trees on site. Follow PACFISH/INFISH Standard and Guideline RA-2 for reference to hazard tree removal. | Leaving felled trees retains nutrients and potential LWD; other actions avoid erosion and sediment delivery. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not exceed an Equivalent Clearcut Area (ECA) of 15% (NMFS 1995 LRMP BO). | Harvest activities will not alter the timing, magnitude duration, and spatial distribution of peak, high, and low flows. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Prescribed Fire – Miscellaneous Activities

###### Activity Component: 	Fire Support

Work Element: 	Fire/spike camp

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCA's in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Take, water quality and habitat elements | Potentially Adverse | No criteria. | Activity is too complex to develop criteria at this scale. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Take, water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	“Black” line

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Shade, sediment and temperature | Potentially Adverse | No blackline construction perpendicular to the stream channel. Non-mechanized black line construction is allowed within the RHCA but within the fire severity guidelines in Attachment 12 (and summarized below). Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). | The criteria prevent adverse affects to salmonids because: the extent of the burn is not sufficient to elevate sediment delivery; does not consume (size or amount) of large woody debris to a level that would affect stream function; does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Shade, sediment and temperature | Potentially Adverse | No blackline construction perpendicular to the RHCA (up the slope) within 500 feet of any stream channel (see Attachment 1). | Blackline running upslope has the potential to create erosion paths with delivery to stream channels. The buffer of 500 feet is based upon concentrated delivery distances from research (Attachment 1). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Shade, sediment and temperature | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	“Wet” line-foam line

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | Potentially Adverse | No foam lines or water with surfactants (wet lines) within RHCAs. For water drafting, SEE: Prescribed Fire Activity Type; Fireline Construction/Holding Actions Activity Component; Drafting to fill engines/tenders Work Element. | Criteria is sufficient to avoid potential adverse effects because it would prevent the introduction of chemical additives to the water column. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	Drafting to fill engines/tenders

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | The determination of whether the pumping activity would occur in streams with at-risk fish, will require fisheries biologist review and approval. Water drafting/pumping will maintain a continuous surface flow of the stream, without altering the original wetted width. Follow the National Marine Fisheries Service guidelines for screening pump intakes (May 1996: Juvenile Fish Screen Criteria for Pump Intakes). No dams or channel alterations for pumping in streams occupied by at risk fish. | These criteria were derived from previous programatic consultations. They were designed to avoid adverse affects to the pathway elements. There should be a negligible risk of incidental take caused by pump entrainment or screen impingement. Water drafting/pumping will maintain a continuous surface flow of the stream, without altering the original wetted width. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | No Effect | No criteria. | Pumping/drafting cannot occur outside of the RHCA. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, take, channel morphology and habitat element | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	Explosive built fireline

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No criteria | The complexity of this activity requires knowledge of site specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | Blasting will only be allowed in areas where materials (rocks and dirt) and or sediment may not potentially reach live waters. | These activities do not pose the potential for adverse affects to at-risk fish species. RHCA buffers are adequate to prevent delivery of sediment. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, take, channel morphology and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	Hand built fireline

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No fireline within RHCAs, except: Natural barriers, hand-build line parallel to the stream channel and at least one-site potential tree or 100 feet distance from the stream (whichever is greater). Or, Hand-build fireline perpendicular to the stream channel with waterbars and located at least one site-potential tree height or 100 feet from the edges of the channel (whichever is greatest). | Hand-built firelines built perpendicular to the stream and lacking water bars have the potential to deliver sediment. See Attachment 2 (sediment delivery). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	Helicopter dipping

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Take | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No helicopter dipping from waters that are known to be (or may be) contaminated with diseases or exotic species (including: whirling disease, zebra mussels, noxious aquatic weeds). | No at risk salmonids and/or habitat present. | Not Likely to Adversely Affect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	Machine built fireline

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No machine built fireline within 500 feet of any channel, including intermittent channels (see Figure 4.26 and "Importance of small streams" in Attachment 1). No machine built firelince construction perpendicular to the RHCA (up the slope) within 500 feet of any stream channel (see Attachment 1). | With these criteria, these activities do not pose the potential for adverse effect to at-risk fish species because minimal disturbances beyond 500 feet of the stream channel has extremely small chance of delivering sediment. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	Natural barriers riparian/wetlands

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | Using natural barriers to design fuel breaks should not require any mechanical or hand-built firelines. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fireline Construction/Holding Actions

Work Element: 	Pumping from streams/ponds using portable pumps

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | The determination of whether the pumping activity would occur in streams with at-risk fish, will require fisheries biologist review. Water drafting/pumping will maintain a continuous surface flow of the stream, without altering the original wetted width. Follow the National Marine Fisheries Service guidelines for screening pump intakes (May 1996: Juvenile Fish Screen Criteria for Pump Intakes). No dams or channel alterations for pumping in streams occupied by at risk fish. | These criteria were derived from previous programatic consultations. They were designed to avoid adverse affects to the pathway elements. There should be a negligible risk of incidental take caused by pump entrainment or screen impingement. Water drafting/pumping will maintain a continuous surface flow of the stream, without altering the original wetted width. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside RHCAs, in any watershed (those both with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery; and in watersheds without at-risk fish species or with no designated critical | Water quality, take, channel morphology and habitat elements | No Effect | No criteria. | Pumping/drafting cannot occur outside of the RHCA. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, channel morphology and habitat element | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Helicopter Landing Sites and other Operational Facilities

Work Element: 	Helicopter support sites; refuel, alumigel mix sites, etc.

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs within the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of the action requires site-specific analysis. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No hauling during wet weather on non-paved roads. Short spurs with no instability concerns, will be obliterated and re-vegetated immediately after activity is completed. All helicopter fueling/mixing operations require an approved transportation, storage, and emergency spill plan. Other fueling operations will consist of a slip-tank not greater than 250 gallons. | Criteria is sufficient to avoid potential adverse affects because it would prevent the introduction of chemicals and/or fuels to the water column. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Ignition

Work Element:		All except where otherwise noted	This Work Element includes:• Hand ignition • Mechanical ignition • Aerial ignition

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Shade, sediment and temperature | Potentially Adverse | Intentional ignition in RHCAs will be designed so as not to prevent attainment of RMOs. No aerial ignition within RHCA. No refueling within any RHCA. SEE: Prescribed Fire Activity Type; All Vegetation Treatments for the effects of prescribed fire to vegetation. | These activities do not pose the potential for adverse affects to at risk salmonid species or their habitats. (References: SEE Attachment 2 for information on prescribed fire). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Shade, sediment and temperature | Potentially Adverse | SEE: Prescribed Fire Activity Type; All Vegetation Treatments for project criteria of prescribed fire to vegetation. | SEE: Prescribed Fire Activity Type; All Vegetation Treatments for the rationale of prescribed fire to vegetation. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Shade, sediment and temperature | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mop-up

Work Element:		All except where otherwise noted	This Work Element includes:• Engine • Hand tool • Hose lays

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Shade, sediment and temperature | Potentially Adverse | The determination of whether the pumping activity would occur in streams with at-risk fish, will require fisheries biologist review. Water drafting/pumping will maintain a continuous surface flow of the stream, without altering the original wetted width. Follow the National Marine Fisheries Service guidelines for screening pump intakes (May 1996: Juvenile Fish Screen Criteria for Pump Intakes). No dams or channel alterations for pumping in streams occupied by at risk fish. | These criteria were designed to avoid adverse affects to the pathway elements. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Shade, sediment and temperature | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Prescribed Fire – Vegetation Types

###### Activity Component: 	Aspen, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | Killing above-ground aspen by burning would have an adverse short-term effect on shade, temperature, and nutrient input to the stream. See Attachment 13 for information on effects of fire to aspen. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 25% in the watershed. An ECA limitation of 15% will be applied within the range of listed anadromous salmonids addressed within the 1995 & 1998 Biological opinions for Snake and Upper Columbia Rivers Chinook & Steelhead. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For fencing, SEE: Range Infrastructure Activity Type; Fence Construction/Reconstruction Activity Component. For aspen restoration, SEE Threatened & Endangered Species Habitat Restoration Activity Type; Aspen Restoration Activity Component | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present.. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment, sediment, water quality, habitat elements, water yield | Treat aspen stands in riparian areas to achieve desired vegetation characteristics that have the following beneficial effects (both long and short term): 1. Increases potential shade long-term; 2. Increases LWD recruitment short-term; 3. Increases pool frequency short-term; 4. Increases width/depth ratio long-term; 5. Improves sediment regime long-term; 6. Improves stream flow regime long-term; 7. Increases nutrient input long-term. See Attachment 13 for information on effects of fire on aspen. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The INFISH/PACFISH goals emphasize diverse and productive riparian vegetation characteristic of natural ecosystems, or characteristic of conditions under which the riparian communities developed. Therefore prescribed fires should be designed to move natural, seral aspen communities, from their present condition dominated by conifers and shrubs, back to their historic natural condition of even-aged stands reflective of fire disturbance regimes under which they developed. See Attachment 13 for information on the beneficial effects of treating aspen stands. |
| --- | --- | --- | --- |

###### Activity Component: 	Aspen, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | Killing above-ground aspen by burning would have an adverse short-term effect on shade, temperature, and nutrient input to the stream. See Attachment 13 for information on effects of fire to aspen. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 25% in the watershed. An ECA limitation of 15% will be applied within the range of listed anadromous salmonids addressed within the 1995 & 1998 Biological opinions for Snake and Upper Columbia Rivers Chinook & Steelhead. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For fencing, SEE: Range Infrastructure Activity Type; Fence Construction/Reconstruction Activity Component. For aspen restoration, SEE Threatened & Endangered Species Habitat Restoration Activity Type; Aspen Restoration Activity Component | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment, sediment, water quality, habitat elements, water yield | Treat aspen stands in riparian areas to achieve desired vegetation characteristics that have the following beneficial effects (both long and short term): 1. Increases potential shade long-term; 2. Increases LWD recruitment short-term; 3. Increases pool frequency short-term; 4. Increases width/depth ratio long-term; 5. Improves sediment regime long-term; 6. Improves stream flow regime long-term; 7. Increases nutrient input long-term. See Attachment 13 for information on effects of fire on aspen. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The INFISH/PACFISH goals emphasize diverse and productive riparian vegetation characteristic of natural ecosystems, or characteristic of conditions under which the riparian communities developed. Therefore prescribed fires should be designed to move natural, seral aspen communities, from their present condition dominated by conifers and shrubs, back to their historic natural condition of even-aged stands reflective of fire disturbance regimes under which they developed. See Attachment 13 for information on the beneficial effects of treating aspen stands. |
| --- | --- | --- | --- |

###### Activity Component: 	Aspen, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | Killing above-ground aspen by burning would have an adverse short-term effect on shade, temperature, and nutrient input to the stream. See Attachment 13 for information on effects of fire to aspen. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 25% in the watershed. An ECA limitation of 15% will be applied within the range of listed anadromous salmonids addressed within the 1995 & 1998 Biological opinions for Snake and Upper Columbia Rivers Chinook & Steelhead. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For fencing, SEE: Range Infrastructure Activity Type; Fence Construction/Reconstruction Activity Component. For aspen restoration, SEE Threatened & Endangered Species Habitat Restoration Activity Type; Aspen Restoration Activity Component | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment, sediment, water quality, habitat elements, water yield | Treat aspen stands in riparian areas to achieve desired vegetation characteristics that have the following beneficial effects (both long and short term): 1. Increases potential shade long-term; 2. Increases LWD recruitment short-term; 3. Increases pool frequency short-term; 4. Increases width/depth ratio long-term; 5. Improves sediment regime long-term; 6. Improves stream flow regime long-term; 7. Increases nutrient input long-term. See Attachment 13 for information on effects of fire on aspen. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The INFISH/PACFISH goals emphasize diverse and productive riparian vegetation characteristic of natural ecosystems, or characteristic of conditions under which the riparian communities developed. Therefore prescribed fires should be designed to move natural, seral aspen communities, from their present condition dominated by conifers and shrubs, back to their historic natural condition of even-aged stands reflective of fire disturbance regimes under which they developed. See Attachment 13 for information on the beneficial effects of treating aspen stands. |
| --- | --- | --- | --- |

Activity Component: 	Aspen, Fire Regime III

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | Killing above-ground aspen by burning would have an adverse short-term effect on shade, temperature, and nutrient input to the stream. See Attachment 13 for information on effects of fire to aspen. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 25% in the watershed. An ECA limitation of 15% will be applied within the range of listed anadromous salmonids addressed within the 1995 & 1998 Biological opinions for Snake and Upper Columbia Rivers Chinook & Steelhead Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For fencing, SEE: Range Infrastructure Activity Type; Fence Construction/Reconstruction Activity Component. For aspen restoration, SEE Threatened & Endangered Species Habitat Restoration Activity Type; Aspen Restoration Activity Component For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment, sediment, water quality, habitat elements, water yield | Treat aspen stands in riparian areas to achieve desired vegetation characteristics that have the following beneficial effects (both long and short term): 1. Increases potential shade long-term; 2. Increases LWD recruitment short-term; 3. Increases pool frequency short-term; 4. Increases width/depth ratio long-term; 5. Improves sediment regime long-term; 6. Improves stream flow regime long-term; 7. Increases nutrient input long-term. See Attachment 13 for information on effects of fire on aspen. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The INFISH/PACFISH goals emphasize diverse and productive riparian vegetation characteristic of natural ecosystems, or characteristic of conditions under which the riparian communities developed. Therefore prescribed fires should be designed to move natural, seral aspen communities, from their present condition dominated by conifers and shrubs, back to their historic natural condition of even-aged stands reflective of fire disturbance regimes under which they developed. See Attachment 13 for information on the beneficial effects of treating aspen stands. |
| --- | --- | --- | --- |

Activity Component: 	Aspen, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | Killing above-ground aspen by burning would have an adverse short-term effect on shade, temperature, and nutrient input to the stream. See Attachment 13 for information on effects of fire to aspen. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 25% in the watershed. An ECA limitation of 15% will be applied within the range of listed anadromous salmonids addressed within the 1995 & 1998 Biological opinions for Snake and Upper Columbia Rivers Chinook & Steelhead Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For fencing, SEE: Range Infrastructure Activity Type; Fence Construction/Reconstruction Activity Component. For aspen restoration, SEE Threatened & Endangered Species Habitat Restoration Activity Type; Aspen Restoration Activity Component For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment, sediment, water quality, habitat elements, water yield | Treat aspen stands in riparian areas to achieve desired vegetation characteristics that have the following beneficial effects (both long and short term): 1. Increases potential shade long-term; 2. Increases LWD recruitment short-term; 3. Increases pool frequency short-term; 4. Increases width/depth ratio long-term; 5. Improves sediment regime long-term; 6. Improves stream flow regime long-term; 7. Increases nutrient input long-term. See Attachment 13 for information on effects of fire on aspen. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The INFISH/PACFISH goals emphasize diverse and productive riparian vegetation characteristic of natural ecosystems, or characteristic of conditions under which the riparian communities developed. Therefore prescribed fires should be designed to move natural, seral aspen communities, from their present condition dominated by conifers and shrubs, back to their historic natural condition of even-aged stands reflective of fire disturbance regimes under which they developed. See Attachment 13 for information on the beneficial effects of treating aspen stands. |
| --- | --- | --- | --- |

Activity Component: 	Aspen, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | Killing above-ground aspen by burning would have an adverse short-term effect on shade, temperature, and nutrient input to the stream. See Attachment 13 for information on effects of fire to aspen. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 25% in the watershed. An ECA limitation of 15% will be applied within the range of listed anadromous salmonids addressed within the 1995 & 1998 Biological opinions for Snake and Upper Columbia Rivers Chinook & Steelhead Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For fencing, SEE: Range Infrastructure Activity Type; Fence Construction/Reconstruction Activity Component. For aspen restoration, SEE Threatened & Endangered Species Habitat Restoration Activity Type; Aspen Restoration Activity Component For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment, sediment, water quality, habitat elements, water yield | Treat aspen stands in riparian areas to achieve desired vegetation characteristics that have the following beneficial effects (both long and short term): 1. Increases potential shade long-term; 2. Increases LWD recruitment short-term; 3. Increases pool frequency short-term; 4. Increases width/depth ratio long-term; 5. Improves sediment regime long-term; 6. Improves stream flow regime long-term; 7. Increases nutrient input long-term. See Attachment 13 for information on effects of fire on aspen. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The INFISH/PACFISH goals emphasize diverse and productive riparian vegetation characteristic of natural ecosystems, or characteristic of conditions under which the riparian communities developed. Therefore prescribed fires should be designed to move natural, seral aspen communities, from their present condition dominated by conifers and shrubs, back to their historic natural condition of even-aged stands reflective of fire disturbance regimes under which they developed. See Attachment 13 for information on the beneficial effects of treating aspen stands. |
| --- | --- | --- | --- |

###### Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer - Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. This criteria ensures that plants are left in the burned area to take up excess nitrates that would otherwise be delivered to the stream. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer - Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer - Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Brushbeating/mow, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Brushbeating/mow, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Brushbeating/mow, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Herbicide (Spike), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Herbicide (Spike), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Basin big sagebrush, Fire Regime III

Work Element: 	Herbicide (Spike), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity (See Attachment 12, page 5, for descriptions of fire severity ratings). No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%.. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity (See Attachment 12, page 5, for descriptions of fire severity ratings). No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%.. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity (See Attachment 12, page 5, for descriptions of fire severity ratings). No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%.. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at-risk species present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, riparian veg condition, large woody debris | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at-risk species present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. No more than 5% of the treated acres within the RHCA will be burned. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regime III

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at-risk species present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cedar/Hemlock/fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements, water yield | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. SEE ID 410 MECHANICAL TREATMENT--ALL AREAS UNLESS OTHERWISE NOTED SEE ID 398, ACTIVITY TYPE: MECHANICAL TREATMENTS; COMPONENT REHAB OF EXCESS VEGETATION AND SLASH; ID 500 ACTIVITY TYPE: MECHANICAL TREATMENTS; HARVEST PRESCRIPTION/ IMPLEMENTATION; ; ID 427 ACTIVITY TYPE: PRESCRIBED FIRE, COMPONENT: IGNITION. For blackline construction SEE ID 425 ACTIVITY TYPE: PRESCRIBED FIRE; COMPONENT: FIRELINE CONSTRUCTION/HOLDING ACTIONS | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. SEE ID 410 MECHANICAL TREATMENT--ALL AREAS UNLESS OTHERWISE NOTED SEE ID 398, ACTIVITY TYPE: MECHANICAL TREATMENTS; COMPONENT REHAB OF EXCESS VEGETATION AND SLASH; ID 500 ACTIVITY TYPE: MECHANICAL TREATMENTS; HARVEST PRESCRIPTION/ IMPLEMENTATION; ; ID 427 ACTIVITY TYPE: PRESCRIBED FIRE, COMPONENT: IGNITION. For blackline construction SEE ID 425 ACTIVITY TYPE: PRESCRIBED FIRE; COMPONENT: FIRELINE CONSTRUCTION/HOLDING ACTIONS | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%.(See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For blackline construction SEE: Prescribed Fire Activity Type; Fireline Construction Activity Component; Holding Actions | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 1, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. Condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (non-anadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at-risk species/habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment,sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. SEE ID 410 MECHANICAL TREATMENT--ALL AREAS UNLESS OTHERWISE NOTED SEE ID 398, ACTIVITY TYPE: MECHANICAL TREATMENTS; COMPONENT REHAB OF EXCESS VEGETATION AND SLASH; ID 500 ACTIVITY TYPE: MECHANICAL TREATMENTS; HARVEST PRESCRIPTION/ IMPLEMENTATION; ; ID 427 ACTIVITY TYPE: PRESCRIBED FIRE, COMPONENT: IGNITION. For blackline construction SEE ID 425 ACTIVITY TYPE: PRESCRIBED FIRE; COMPONENT: FIRELINE CONSTRUCTION/HOLDING ACTIONS | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. SEE ID 410 MECHANICAL TREATMENT--ALL AREAS UNLESS OTHERWISE NOTED SEE ID 398, ACTIVITY TYPE: MECHANICAL TREATMENTS; COMPONENT REHAB OF EXCESS VEGETATION AND SLASH; ID 500 ACTIVITY TYPE: MECHANICAL TREATMENTS; HARVEST PRESCRIPTION/ IMPLEMENTATION; ; ID 427 ACTIVITY TYPE: PRESCRIBED FIRE, COMPONENT: IGNITION. For blackline construction SEE ID 425 ACTIVITY TYPE: PRESCRIBED FIRE; COMPONENT: FIRELINE CONSTRUCTION/HOLDING ACTIONS | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 2, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (non-anadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes III

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/Broadcast Burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Lodgepole pine/Douglas-fir/true fir, Condition Class 3, Fire Regimes IV, V

Work Element: 	Thin/machine pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mountain big sagebrush, Fire Regime II

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. This criteria ensures that plants are left in the burned area to take up excess nitrates that would otherwise be delivered to the stream. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mountain big sagebrush, Fire Regime II

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mountain big sagebrush, Fire Regime II

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mountain big sagebrush, Fire Regime II

Work Element: 	Brushbeating/mow, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mountain big sagebrush, Fire Regime II

Work Element: 	Brushbeating/mow, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mountain big sagebrush, Fire Regime II

Work Element: 	Brushbeating/mow, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mountain big sagebrush, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mountain big sagebrush, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mountain big sagebrush, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5 for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mountain big sagebrush, Fire Regime III

Work Element: 	Brushbeating/mow, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mountain big sagebrush, Fire Regime III

Work Element: 	Brushbeating/mow, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Mountain big sagebrush, Fire Regime III

Work Element: 	Brushbeating/mow, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Oak woodlands/oak-maple/interior chaparral/mountain brush, Fire Regime II

Work Element: Activity fuel/pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, chemical contaminants | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No piling and burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No piles on road berms.Piles not to exceed 10’ x 10’. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Buffer widths are adequate to prevent delivery of fine sediment and minimizes the potential leaching of nutrients to the stream (based on Attachment #1). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Oak woodlands/oak-maple/interior chaparral/mountain brush, Fire Regime II

Work Element: Activity fuel/pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, chemical contaminants | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No piling and burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No piles on road berms.Piles not to exceed 10’ x 10’. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Buffer widths are adequate to prevent delivery of fine sediment and minimizes the potential leaching of nutrients to the stream (based on Attachment #1). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Oak woodlands/oak-maple/interior chaparral/mountain brush, Fire Regime II

Work Element: Activity fuel/pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, chemical contaminants | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No piling and burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No piles on road berms.Piles not to exceed 10’ x 10’. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Buffer widths are adequate to prevent delivery of fine sediment and minimizes the potential leaching of nutrients to the stream (based on Attachment #1). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Oak woodlands/oak-maple/interior chaparral/mountain brush, Fire Regime II

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Oak woodlands/oak-maple/interior chaparral/mountain brush, Fire Regime II

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Oak woodlands/oak-maple/interior chaparral/mountain brush, Fire Regime II

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: Activity fuels/pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, chemical contaminants | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No piling and burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No piles on road berms.Piles not to exceed 10’ x 10’. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Buffer widths are adequate to prevent delivery of fine sediment and minimizes the potential leaching of nutrients to the stream (based on Attachment #1). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: Activity fuels/pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, chemical contaminants | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No piling and burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No piles on road berms.Piles not to exceed 10’ x 10’. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Buffer widths are adequate to prevent delivery of fine sediment and minimizes the potential leaching of nutrients to the stream (based on Attachment #1). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: Activity fuels/pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, chemical contaminants | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No piling and burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No piles on road berms.Piles not to exceed 10’ x 10’. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Buffer widths are adequate to prevent delivery of fine sediment and minimizes the potential leaching of nutrients to the stream (based on Attachment #1). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: Activity fuels/scattered/ broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (Attachment 12, page 5). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. This criteria ensures that plants are left in the burned area to take up excess nitrates that would otherwise be delivered to the stream. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: Activity fuels/scattered/ broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: Activity fuels/scattered/ broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For chaining SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Chaining Work Element. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (Attachment 12, page 5). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. This criteria ensures that plants are left in the burned area to take up excess nitrates that would ot | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Pinyon-juniper and juniper woodlands, Fire Regime II

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Reg. I

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Reg. I

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Reg. I

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Reg. I

Work Element: 	Broadcast burn, Riparian areas

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, riparian veg. Condition, large woody debris | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. Condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. Condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (non-anadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/pile/burn piles, Riparian areas

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, riparian veg. condition, large woody debris | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/scatter/broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/scatter/broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | B Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/scatter/broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Fire Regime I

Work Element: 	Thin/scatter/broadcast burn, Riparian areas

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Broadcast burn, Riparian areas

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, riparian veg. Condition, large woody debris | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. Condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, riparian veg. Condition, large woody debris | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. Condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (non-anadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/pile/burn piles, Riparian areas

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, riparian veg. Condition, large woody debris | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/scatter/broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/scatter/broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/scatter/broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | B Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Open forest objective, Fire Regime III

Work Element: 	Thin/scatter/broadcast burn, Riparian areas

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, riparian veg. Condition, large woody debris | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Ponderosa pine/Douglas fir/western larch/Jeffrey pine/lodgepole pine, Seedling/sapling objective, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 1, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 1, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 1, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Riparian mid/upper elevation, Condition Class 1, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Riparian mid/upper elevation, Condition Class 1, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (non-anadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Riparian mid/upper elevation, Condition Class 1, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 2, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 2 – Prescribed Fire). |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 2, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 2, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Riparian mid/upper elevation, Condition Class 2, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Riparian mid/upper elevation, Condition Class 2, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (non-anadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Riparian mid/upper elevation, Condition Class 2, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. No more than 5% of the treated acres within the RHCA will be burned. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 3, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at high intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Ensure that project contributes toward attainment, or progress towards attainment of RMOs (as listed below), is consistent with appropriate biological opinions and falls within a watershed which is "properly functioning" (as described within NMFS and FWS matrices of pathways and indicators). Completed matrices will be attached to the completed biological analysis. Livestock grazing will be excluded from prescribed burn units for at least two years, or a time period previously agreed upon during consultation, or the riparian vegetation has recovered sufficiently to achieve natural rates of surface erosion (whichever is greatest). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria reduce adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. |
| --- | --- | --- | --- |
| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 3, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 10%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Riparian mid/upper elevation, Condition Class 3, Fire Regimes III, IV, V

Work Element: 	Broadcast burn (thinned or not), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Fire severity should not exceed a rating of “low” for 90% of the RHCA. No more than 10% in a moderate severity. No more than 5% mortality of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, mortality of overstory trees shall not exceed 20%. (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Non-mechanized blackline construction is allowed with the RHCA but within the fire severity guidelines listed above. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | The criteria prevent adverse affects to salmonids because: 1.Does not result in death or injury to individual fish. 2.Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3.Does not consume (size or amount) large woody debris to level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area (References: see Attachment 12 – Prescribed Fire). Criteria will enhance longterm channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements, water yield | Potentially Adverse | Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Mortality shall not exceed 10-30% of the remaining overstory trees in the project area. Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Riparian mid/upper elevation, Condition Class 3, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | sediment, water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | Hydrologist will insure that the overstory mortality will not adversely alter the flow regimes at the project scale. No more than 5% mortality of overstory trees. Overstory mortality shall not cause the ECA to exceed 15% in the watershed. Burned acres cannot exceed 3% of the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | Activities will not alter the timing, magnitude, duration, and spatial distribution of peak, high, and low flows. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | large woody debris recruitment | For the RHCAs of intermittent streams, limit overstory mortality to no more than 30%. Apply a silvicultural prescription that maximizes growth and reproduction of trees over 12” dbh within the intermittent RHCAs. Within intermittent RHCAs, do not remove by fire or other related treatment, boles greater than 12” dbh. Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Criteria will enhance long-term channel stability and sediment storage by managing for a silvicultural condition that maximizes large woody debris recruitment. (See Attachment 1 – Riparian Area [RHCA] Literature Summary) |
| --- | --- | --- | --- |

Activity Component: 	Riparian mid/upper elevation, Condition Class 3, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg. condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 10%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 5% of the total watershed acres in a 5th (anadromous) or 6th (non-anadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at low intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Riparian mid/upper elevation, Condition Class 3, Fire Regimes III, IV, V

Work Element: 	Thin small trees/hand pile/burn piles, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, riparian veg condition, large woody debris | Potentially Adverse | Burn piles at a time when fuel moisture levels are sufficient to limit creep to within 10 feet of a pile. Minimize disturbance to riparian ground cover and vegetation. Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer No more than 5% of the treated acres within the RHCA will be burned. No more than 5% scorch damage of overstory trees within the RHCA of perennial streams. In the RHCA of intermittent streams, scorch damage of overstory trees shall not exceed 20%. Pile burning will cover no more than 5% of the RHCA within the project area. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | The streamside buffer and minimal area treated are sufficient to avoid delivery of sediment to the stream by controlling erosion and delivery. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, habitat elements | Potentially Adverse | No more than 5% mortality of overstory trees. Burned acres cannot exceed 3% of the total watershed acres in a 5th (anadromous) or 6th (nonanadromous) code HUC in a given year. Understory vegetation must be adequate to prevent erosion associated with the treatment prior to additional treatments in stands within the watershed. Burned area does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. For thinning - SEE: Mechanical Treatments Activity Type; Harvest Prescription/Implementation Activity Component; Understory/single story treatments: thinning Work Element. For piling - SEE: Mechanical Treatments Activity Type; Rehabilitation, removal of excess vegetation and slash Activity Component. | RHCA widths are adequate to buffer the stream (based on Attachment #1). The amount of area expected to be treated at moderate intensity is not expected to result in adverse erosion and sediment delivery to stream channels. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Broadcast burn/seed (aerial), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For aerial seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Aerial Seeding Work Element. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. For aerial seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Aerial Seeding Work Element. | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Broadcast burn/seed (aerial), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For aerial seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Aerial Seeding Work Element. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For aerial seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Aerial Seeding Work Element. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Broadcast burn/seed (aerial), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For aerial seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Aerial Seeding Work Element. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For aerial seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Aerial Seeding Work Element. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Broadcast burn/seed (drill), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Broadcast burn/seed (drill), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Broadcast burn/seed (drill), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Brushbeating/mow/seed (drill), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Brushbeating/mow/seed (drill), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Sagebrush/cheatgrass, Fire Regimes II, III, IV

Work Element: 	Brushbeating/mow/seed (drill), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). For seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding - disking, drilling, fertilization and plowing Work Element | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Brushbeating/Mowing, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Brushbeating/Mowing, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Brushbeating/Mowing, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Herbicide (Spike), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Herbicide (Spike), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Wyoming big sagebrush - Great Basin, Fire Regime IV

Work Element: 	Herbicide (Spike), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

###### Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. In stream systems with elevated nutrient levels, do not exceed a fire severity rating of “moderate”. See Attachment 12, page 5. | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Brushbeating/mow, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Brushbeating/mow, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Brushbeating/mow, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Herbicide (Spike), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Herbicide (Spike), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime III

Work Element: 	Herbicide (Spike), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

###### Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Broadcast burn, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. RMOs: -Pool frequency -Water temperature -Large woody debris -Bank stability -Lower bank angle -Width/depth ratio -Surface fine sediment -Cobble embeddedness Project will be timed to avoid disturbance to spawning fish, redds, and pre-emergent fry. Project will be timed to ensure that local refugia are available. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality (ash) | Potentially Adverse | No burning unless native perennial plants are adequately present to respond. Limit area of burn to <25% of watershed. Use approved ignition techniques to moderate fire intensity adjacent to the RHCA. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | Fire does not expose or disturb land areas sufficient to affect sediment delivery or water quality. Nitrate nitrogen is the primary component of post-fire nutrient increases in streams. This effect is associated with a large amount of burned biomass. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Broadcast burn, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Broadcast burn, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, temperature, turbidity, shade, riparian veg. condition, channel morphology, large woody debris, habitat elements (in-stream), take | Potentially Adverse | Within the RHCAs having slopes greater than 10%, do not exceed a fire severity rating of “moderate” (See Attachment 12, page 5, for descriptions of fire severity ratings). Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Burning within RHCAs will require hydrologist/fish biologist review and approval to determine that the project will be timed to avoid disturbance of all life stages of listed salmonids. No burning within the following buffers from the edge of the bankfull channel. <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | The criteria prevent adverse affects to salmonids because: 1. Does not result in death or injury to individual fish. 2. Fire does not expose or disturb land areas sufficient to elevate sediment delivery such that habitat/fish are harmed. 3. Does not consume (size or amount) large Woody debris to a level that would affect stream function. 4. Does not cause mortality to overstory or other vegetation such that stream temperatures and water yield are significantly affected. 5. Does not impact the ecological (potential natural condition) conditions in riparian area. 6. By controlling the severity of fire on steeper slopes, erosion and transport of sediment to fish-bearing streams would be avoided. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | sediment, water quality, water yield, turbidity, temperature, chemical contaminants | Potentially Adverse | Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the riparian vegetation to regeneration to a stage that can withstand grazing, especially in riparian sites with woody shrubs. In no case shall either of the above time period be less than two years. | These activities do not pose the potential for adverse effects to at-risk fish. Because the RHCA is an adequate buffer so that there is no measurable effect from disturbances associated with the activity. | Not Likely To Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | sediment, water quality, water yield, chemical contaminants | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Brushbeating/mow, High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Brushbeating/mow, Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Brushbeating/mow, Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements, sediment | Potentially Adverse | No brushbeating/mowing within 100 feet or one site-potential tree height (whichever is greater) from the stream channel. (See Attachment 2 - Extent of effect for stream side disturbances). To avoid compaction, soils will be dry and/or frozen during treatment. Cutting equipment is to be held at 12" or higher above the soil surface. Ensure that the project does not prevent or retard attainment of RMOs and is consistent with appropriate biological opinions. Ensure that the project does not retard progress towards "properly functioning" condition of the following relevant indicators in the Watershed Condition Pathway: Road Density, Disturbance History, Riparian Condition, and Disturbance Regime (see Attachment 3). | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. Brushbeating/Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and effects to streamside shade. | Not Likely To Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements, sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Herbicide (Spike), High intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Herbicide (Spike), Low intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

Activity Component: 	Wyoming big sagebrush - Intermountain west, Fire Regime IV

Work Element: 	Herbicide (Spike), Moderate intensity

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | water quality, habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site-specific conditions and project design. Consult locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | water quality, habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

### Activity Type: 	Range Infrastructure

###### Activity Component: 	Fence Construction/Reconstruction/Maintenance

Work Element: 	Building rock jacks

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No material gathering within the RHCA (e.g. fence posts, braces, stays, rock, etc.). Only hand work is allowed. Rock hauling will be non-motorized unless motorized access will cause no ground distrubance. No vegetation removal. No fueling within RHCAs. | This criteria reduces potential for sediment production and delivery. Criteria limit potential for reducing streambank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | This activity has no potential for adverse affects outside of the RHCA. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fence Construction/Reconstruction/Maintenance

Work Element: 	Clearing right of way

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Hand brushing only with a maximum of five feet either side of fence line. No ground disturbance. Hazard trees will be retained on site. No fueling within RHCAs. Construct fences to avoid adverse concentrated cattle use of riparian area, streambanks, or areas sensitive to eriosion and sediment delivery. | This criteria avoid erosion and sediment delivery and other risks associated with sediment production and delivery. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No perpendicular-to the stream fenceline can be cleared on slopes greater than 20% and within 500 feet of stream channels. No ground surface disturbance (e.g. use high blading for clearing fenceline. Avoid sediment production and delivery to live water by using standard erosion and sediment control measures. Avoid scarification on slopes over 20% (see Attachment 1 - Importance of Hill Slope Steepness). | Clearing fenceline up-slope has the potential to create erosion paths with delivery to stream channels. The buffer of 500 feet is based upon concentrated delivery distances from research (Attachment 1). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fence Construction/Reconstruction/Maintenance

Work Element: 	Digging post holes - manual/mechanical

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Water quality and habitat elements | Potentially Adverse | No post hole digging within 25 feet from the stream channel. No tractor-mounted (large equipment) post hole digging within RHCA. No fueling within RHCAs. Construct fences to avoid adverse concentrated cattle use of riparian area, streambanks, or areas sensitive to eriosion and sediment delivery. Constructed fence lines should not concentrate cattle presence on slopes directing paths and gullies perpendicular to the stream channel. All other fence construction within RHCAs requires local consultation. | This activity reduces potential for sediment production and delivery. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Constructed fence lines should not concentrate cattle presence on slopes directing paths and gullies perpendicular to the stream channel. | This activity reduces potential for sediment production and delivery. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fence Construction/Reconstruction/Maintenance

Work Element: 	Onsite material cutting, gathering rocks, etc

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No material gathering within the RHCA (e.g. fence posts, braces, stays, rock, etc.). Only hand work is allowed. Rock hauling will be non-motorized unless motorized access will cause no ground distrubance. No vegetation removal. No fueling within RHCAs. | This criteria reduces potential for sediment production and delivery. Criteria limit potential for reducing streambank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | This activity has no potential for adverse affects outside of the RHCA. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Fence Construction/Reconstruction/Maintenance

Work Element: 	Stringing wire

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Only hand work is allowed. No mechanized equipment within RHCAs. No fueling within RHCAs. | This criteria reduces potential for sediment production and delivery. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | This activity has no potential for adverse affects outside of the RHCA. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Rangeland Restoration

Work Element: 	Chaining

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria | Activity is too complex to develop criteria at this scale. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | The RHCA is an adequate buffer to prevent sediment delivery from erosion associated with chaining (Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Rangeland Restoration

Work Element: 	Seeding - aerial

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | This assumes that the seeds are not mixed with fertilizer. If fertilizer is used, SEE: Insect Suppression Activity Type, Fertilization Activity Component, Aerial Application of N pellets Work Element. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | his assumes that the seeds are not mixed with fertilizer. If fertilizer is used, SEE: Insect Suppression Activity Type, Fertilization Activity Component, Aerial Application of N pellets Work Element. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Rangeland Restoration

Work Element: 	Seeding  disking, drilling, fertilizing, plowing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No ground disturbing activity (disking, drilling,and plowing) within RHCAs. SEE: Insect Suppression Activity Type, Fertilization Activity Component, for work elements and associated criteria for fertilization. | Criteria is sufficient to avoid potential adverse effects because the potential for introduction of fertilizer will be negligble (See Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Not Likely to Adversely Affect | No criteria. | The RHCA is an adequate buffer to prevent sediment delivery (Attachment 1). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | Not Likely to Adversely Affect | No criteria. | No at risk salmonids and/or habitat present. | Not Likely to Adversely Affect |

Activity Component: 	Water Development Construction/Reconstruction (springs, guzzlers, tanks, ponds, reservoirs, wells)

Work Element: 	All water developments - clearing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | No clearing for or construction of water For springs or seeps, restrict clearing to slopes of 20% using only non-mechanical methods. | Criteria is sufficient to avoid potential adverse effects because the disturbance limits avoid erosion and sediment delivery (Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Not Likely to Adversely Affect | No criteria. | The RHCA is an adequate buffer to prevent sediment delivery from erosion associated with clearing (Attachment 1). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Water Development Construction/Reconstruction (springs, guzzlers, tanks, ponds, reservoirs, wells)

Work Element: 	All water developments - constructing apron - rubber, metal, asphalt

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | No criteria | Activity is too complex to develop criteria at this scale. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | The RHCA is an adequate buffer to prevent sediment delivery from erosion associated with the activity (Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Water Development Construction/Reconstruction (springs, guzzlers, tanks, ponds, reservoirs, wells)

Work Element: 	All water developments - installing troughs, storage tanks, or pits

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | No criteria. | Activity is too complex to develop criteria at this scale. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | All stock watering should be removed as far as practical from the edges of the RHCA to minimize trailing of livestock within this area. Troughs must be equipped with a float valve. No above-ground storage tanks (except guzzlers) within the watershed. | The RHCA is an adequate buffer to prevent sediment delivery from erosion associated with troughs designed with a float valve (Attachment 1). Storage tank failures have the potential to erode and deliver sediment over long slope distances (beyond the limits of the RHCA). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Water Development Construction/Reconstruction (springs, guzzlers, tanks, ponds, reservoirs, wells)

Work Element: 	All water developments - transporting materials

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Motorized transport must occur on designated roads. | This criteria reduces potential for sediment production and delivery (See Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | This activity has no potential for adverse effects outside of the RHCA (See Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Water Development Construction/Reconstruction (springs, guzzlers, tanks, ponds, reservoirs, wells)

Work Element: 	Earthwork  - cat, dragline, scraper

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | No criteria. | Consult locally. Action is too complex - requires site-specific criteria. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | No Effect | No criteria. | Wells and small constructed stock ponds (those that do not contain salmonids and often dry up), are not in the RHCA and can be constructed without adverse affects to at-risk salmonids. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Water Development Construction/Reconstruction (springs, guzzlers, tanks, ponds, reservoirs, wells)

Work Element: 	Pipelines - Trenching

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | No trenching within the RHCAs of perennial and intermittent streams. For springs and seeps, no pipelines or trenching within the lotic portion of the RHCA, or the RHCA associated with any stream channel. | Springs and seeps associated with lentic RHCAs can be developed without affecting salmonids, however lotic RHCAs with connectivity to habitat have the potential to result in adverse affects. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | No Effect | No criteria. | Wells and small constructed stock ponds (those that do not contain salmonids and often dry up), are not in the RHCA and can be constructed without adverse affects to at-risk salmonids. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Water Development Construction/Reconstruction (springs, guzzlers, tanks, ponds, reservoirs, wells)

Work Element: 	Rock haul/material haul

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Motorized transport must occur on designated roads. Rocks and other material will not be excavated from the RHCA. No refueling within RHCA. | This criteria reduces potential for sediment production and delivery (See Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | This activity has no potential for adverse effects outside of the RHCA (See Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Recreation Facilities and Operations

###### Activity Component: 	Existing Facilities Developed and Dispersed

Work Element:		All except where otherwise noted	This Work Element includes:• Install site furniture • Remove trees and ground vegetation, blade to create smooth surface, apply gravel, asphalt or concrete to harden site

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | Potentially Adverse | To avoid root damage, no graveling and asphalt surfacing within 25 feet or .3 site-potential tree height, whichever is greater (FEMAT, page V-6 or Attachment 1) of the edge of the stream. Gravelling/asphalt will not expand beyond existing footprint of the disturbed area. Prevent human uses within this zone using barrier placements. For tree removal, SEE: Mechanical Treatment Activity Type; Harvest Prescription/Implementation Activity Component; Dead Trees salvage Work Element For vegetation removal, SEE: Mechanical Treatments Activity Type, Rehab, removal of excess vegetation and slash Activity Component | Criteria will prevent introducing adverse materials into the stream. It encourages human uses away from the streambank. The criteria distance would provide adequate protection for root strength of vegetation immediately adjacent to the stream channel, important to maintaining bank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | Not Likely to Adversely Affect | No criteria. | RHCA are adequate to buffer the stream from disturbance effects. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Install/Remove toilets

Work Element:		All except where otherwise noted	This Work Element includes:• Harden entry to building • Remove trees, excavate, construct building • Collapse building into vaults or haul structures off-site

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Ensure that PACFISH/INFISH standards & guidelines RM1 through RM3 are met. STRUCTURE REMOVAL: Allow only structure removal by collapse into the vault. CONSTRUCT BUILDING INCLUDING FOUNDATION: No foundation construction and/or installation of toilet vaults within RHCAs. Replacement of existing structure without excavation of a new foundation/vault is allowed within the RHCA. For Harden Entry to Building, and tree removal SEE: Recreation Facilitiies & Operations Activity Type; Existing Facilities Developd and Dispersed Activity Component. | Toilet vault excavations, foundation construction, and vault removal activities are associated with significant disturbances that have the potential to deliver sediment to streams (See Attachments 1 and 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Installation of other site amenities

Work Element: 	Remove trees and ground vegetation, excavate, backfill

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | Potentially Adverse | If PACFISH/INFISH standards & guidelines RM1 through RM3 are met, then add the following: prevent implementing these activities within 25 feet of the edge of the bankful channel, or .3 site-potential tree height, whichever is greater, (Attachment 2). Prevent vehicle uses within this zone by placing barriers at least 25 feet from the edge of the bankful channel. For Water Developments, SEE: Recreation Facilities & Operations Activity Type; Water Development Activity Component. For culverts and ditches, SEE: Roads & Road Maintenance Activity Type; Road Maintenance Activity Component; Adding cross drain culverts Work Element. | Criteria will prevent introducing adverse materials into the stream. It encourages human uses away from the streambank. The distance of 25 feet would be adequate protection for root strength of vegetation immediately adjacent to the stream channel and important to maintaining bank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | For Water Developments, SEE: Recreation Facilities & Operations Activity Type; Water Development Activity Component. For culverts and ditches, SEE: Roads & Road Maintenance Activity Type; Road Maintenance Activity Component; Adding cross drain culverts Work Element. | The RHCA is adequate to buffer effects from installation of site amenities. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Obliteration/Rehabilitation of Recreation Sites

Work Element: 	Install barriers (boulders, fencing, signs, etc.)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No boulder excavation or removal within RHCAs. FENCING: No post hole digging within 25 feet from the active stream channel. No tractor-mounted post hole digging within RHCA. No fueling within RHCAs. | Disturbance associated with boulder removal/excavation has the potential to deliver sediment. Fencing criteria would avoid potential sediment and fuel delivery to streams. | Not Adversely Affect Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | Potentially Adverse | For fencing, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Fence construction/reconstruction Work Element | RHCA widths are adequate to buffer the stream (based on Attachment 1). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Obliteration/Rehabilitation of Recreation Sites

Work Element: 	Remove any existing site furniture

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Ensure that PACFISH/INFISH standards & guidelines RM1 through RM3 are met. STRUCTURE REMOVAL: Allow only structure removal by collapse into the vault. CONSTRUCT BUILDING INCLUDING FOUNDATION: No foundation construction and/or installation of toilet vaults within RHCAs. Replacement of existing structure without excavation of a new foundation/vault is allowed within the RHCA. For Harden Entry to Building, and tree removal SEE: Recreation Facilitiies & Operations Activity Type; Existing Facilities Developd and Dispersed Activity Component. | Toilet vault excavations, foundation construction, and vault removal activities are associated with significant disturbances that have the potential to deliver sediment to streams (See Attachments 1 and 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Obliteration/Rehabilitation of Recreation Sites

Work Element: 	Rip surface, re-contour, topsoil, seed, mulch

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Ensure that PACFISH/INFISH standards & guidelines RM1 through RM3 are met. Avoid ground disturbances during spawning and incubation periods, then add the following: Avoid applying this action within 25' away from the bankful channel or .3 site potential tree height (whichever is greater). Avoid erosion (e.g. ripping on steep slopes) and transport that have the potential to deliver sediment to the stream (i.e. use silt fences). Use the following buffers: <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Use ripping and re-contouring only if it would lessen the existing erodability. For mulching, SEE: Watershed Restoration Activity Type; Revegetation Activity Component; Mulch application Work Element. | Criteria will prevent significant sediment input into the stream, and potential adverse affects on rooting strength so important to bank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Not Likely To Adversely Affect | No criteria. | The RHCA is adequate to buffer sediment transport/delivery to stream channels. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Water development

Work Element:		All except where otherwise noted	This Work Element includes:• Excavate hole, pump installation • Trenching for distribution line

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | If PACFISH/INFISH standards & guidelines RM1 through RM3 are met, then add the following: Avoid trenching and pipeline installation within 25 feet of the bankful channel or .3 site-potential tree height (whichever is greater) to avoid impacts to roots of the riparian vegetation (FEMAT, Murphy - NOAA 1995, etc.). Use trenching methods that avoids sediment delivery (ie. Pipe pulling equipment). | Avoids delivery of sediment to the stream. Avoids disturbance to streamside vegetation (See FEMAT, page V-6 or Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Reforestation

###### Activity Component: 	Access for Reforestation Activities

Work Element: 	Opening closed roads, including snowplowing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Sediment and turbidity | Potentially Adverse | Opening roads includes only opening gates and snow plowing roads. This activity will occur only on existing roads. Requires minimal brushing, ditch maintenance,& existing culvert maintenance. No disturbance of existing cuts and fills. Leave a minimum of 6 to 8" of snow on road surface when opening roads for planting. Ditches and culverts will be made functional. Side-cast material will not include dirt and gravel. Snow berms will not be left on the shoulder unless drainage holes are open and maintained. Travel must cease when damage to the road surface will result or is occurring, and roads must be allowed to melt out and surfaces dry and harden before traffic is allowed on them. For road maintenance, SEE: Roads and Road Maintenance Activity Type; Road Maintenance Activity Component | Criteria are sufficient to avoid potential adverse effects because design measures minimize road disturbance and avoid sediment delivery (see Attachment 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Sediment and turbidity | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Animal Damage Control

Work Element:	All except where otherwise noted	This Work Element includes:• Chemical application above and below ground • Netting and associated devices for protection • Use of snap traps for animal removal

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Water quality and chemical contamination | Potentially Adverse | No criteria. | Until more information is available on sub-lethal effects, consultation must be conducted locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and chemical contamination | Potentially Adverse | No criteria. | Until more information is available on appropriate buffer widths, consultation must be conducted locally. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and chemical contamination | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Artficial Shade

Work Element: 	Shade cards

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk fish species. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Collection of Plant Propagation Materials

Work Element:		All except where otherwise noted	This Work Element includes:• Climb to access or mechanically pick cones • Fire arm use • Pollen, scion material • Collection of seeds or other vegetative materials

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No mechanized equipment for cone collection within the RHCA. | These activities do not pose the potential for adverse effect to at-risk fish species, except collection of cones using ground-based equipment. The RHCA is adequate as a buffer to prevent sediment delivery associated with disturbances of this type. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Hand plant upland/riparian

Work Element: 	Plant trees and shrubs with hoe, bar, auger

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | All fueling and fuel storage areas as well as service landings will be located outside the RHCA. Use only hand augers within the RHCA. | The RHCA is adequate as a buffer to prevent fuel from entering streams. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Natural Regeneration Surveys

Work Element:	All except where otherwise noted	This Work Element includes ALL activities within this Activity Component

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Sediment and turbidity | Potentially Adverse | Stay on designated trails. Stock handling facilities, camp facilities and improvements will be located at least 300 feet from lakes, streams, and springs. Stock handlers will be educated on at-risk fish including identification, Endangered Species Act, and how to minimize adverse effects to the species and their associated habitat. | Criteria are sufficient to avoid potential adverse affects. Avoids sediment delivery by keeping facilities well away from streams. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Sediment and turbidity | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	On site tree storage

Work Element: 	Building and maintaining snow cache

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | For CACHE CONSTRUCTION: Do not build within the RHCA. Opening roads includes only opening gates and snow plowing roads. This activity will occur only on existing roads. Requires minimal brushing, ditch maintenance,& existing culvert maintenance. No disturbance of existing cuts and fills. Leave a minimum of 6 to 8" of snow on road surface when opening roads for planting. Ditches and culverts will be made functional. Side-cast material will not include dirt and gravel. Snow berms will not be left on the shoulder unless drainage holes are open and maintained. Travel must cease when damage to the road surface will result or is occurring, and roads must be allowed to melt out and surfaces dry and harden before traffic is allowed on them. | These activities do not pose the potential for adverse affect to at-risk fish species, except cache construction and snow plowing using ground-based equipment. The RHCA is adequate as a buffer to prevent sediment delivery associated with disturbances of this type. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Return visits after planting

Work Element:		All except where otherwise noted	This Work Element includes ALL activities within this Activity Component

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Sediment and turbidity | Potentially Adverse | Stay on designated trails. Stock handling facilities, camp facilities and improvements will be located at least 300 feet from lakes, streams, and springs. Stock handlers will be educated on at-risk fish including identification, Endangered Species Act, and how to minimize adverse effects to the species and their associated habitat. | Criteria are sufficient to avoid potential adverse affects. Avoids sediment delivery by keeping facilities well away from streams. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Sediment and turbidity | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Site preparation

Work Element:		All except where otherwise noted	This Work Element includes:• Mechanical scarification • Hand mechanized scarifier • Spot application of herbicides

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Furrowing, patch scarification, and dozer scarification will only be conducted on slopes of 20% or less. Avoid sediment production and delivery to live water by using standard erosion and sediment control measures. Avoid scarification on slopes over 20% (see Attachment 1 - Importance of Hill Slope Steepness). For spot application of herbicides SEE: Weeds/Chemical Treatments Activity Type; Herbicide Control Activity Component | Minimum disturbance avoids sediment transport/delivery. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Site preparation

Work Element: 	Hand scalp/grubbing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Hoeing of plant roots allowed outside of 25 feet or .3 site-potential tree height from the stream (whichever is greatest). | The buffer is adequate to avoid potential sediment delivery (Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Not Likely To Adversely Affect | No criteria. | No potential adverse affect outside the RHCA. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Roads & Road Maintenance

###### Activity Component: 	Decommissioning Roads

Work Element:		All except where otherwise noted	This Work Element includes:• Re-contouring • Water barring • Roadbed ripping • Culvert removal • Berm/barrier construction • Side cast pullback

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | No criteria. | Activity is too complex to develop criteria at this scale. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | For RE-CONTOURING AND SIDECAST PULLBACK AND EXCAVATION - No activity would be permitted within 300 feet of any stream channel at slopes greater than 30 percent. No activity would be allowed within 500 feet of any stream channel at slopes greater than 70% FOR BERM/BARRIER CONSTRUCTION - . Materials for berms (rock, logs, etc.) will not be removed from the RHCA. Include erosion controls and containment structures to avoid the increased risk of sediment delivery. Revegetation measures will help to reduce erosion. Road drainage ditches will not be directly connected to the stream. Cross drainage should remove sediment from the road at a distance sufficient to avoid delivery. | The Interior Columbia Basin Science Assessment addressed sediment delivery potential for land disturbing actions. For worst case, the 5% exceedance potential was used to predicate not likely to adversely affect. (See Figure 4.27, Attachment 1; Attachment 10, pages 16, 21, and C-3). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | RECONTOURING AND SIDECAST PULLBACK are desired long-term. Pull back to original contour, use filter cloth to minimize erosion, and seed native vegetation. Pull back material should be end hauled out of the RHCA. WATER BARRING is suggested to be located 25 feet of the edges of the stream channel at a spacing prescribed by the Riparian Road Guide (1994) in Attachment 7. CULVERT REMOVAL for intermittent channels: 1). Activity occurs during the dry season and the channel is dry (applies to intermittent streams only), 2). Reduce fill grade to < 30% adjacent to the stream channel. 3). Use filter cloth or other erosion controls to prevent erosion on, and sediment delivery from the road fill. For perennial streams, SEE Road and Road Maintenance Activity Type; Road Maintenance Activity Component; Culvert Maintenance. BERM CONSTRUCTION: Prevent implementing these activities within 25 feet or .3 site-potential tree height, whichever is greater. (See Attachment 1) of the edge of the bankful channel. ROADBED RIPPING: SEE Watershed Restoration Activity Type, Hillslope Erosion Control, Road/Landing Ripping. | The Interior Columbia Basin Science Assessment addressed sediment delivery potential for land disturbing actions. For worst case, the 5% exceedance potential was used to predicate negligible potential effect. (See Figure 4.27, Attachment 1). Water barring reduces sediment delivery potential if applied as per the criteria. Roadbed ripping reduces erosion potential and therefore reduces the likelihood of increasing sediment delivery, except where the road has naturally re-vegetated. CULVERT REMOVAL would be restricted to reduce the potential for sediment delivery. Criteria will prevent introducing adverse materials into the stream. It encourages human uses away from the streambank. The distance of 25 feet would be adequate protection for root strength of vegetation immediately adjacent to the stream channel and important to maintaining bank stability (See Attachment 1). |
| --- | --- | --- | --- |

###### Activity Component: 	New Construction/Reconstruction

Work Element:		All except where otherwise noted	This Work Element includes:• Vegetation clearing – pioneering activities • Installation of drainage features - includes bridge construction • Earthwork • Finish • Surfacing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Activities are too complex - consult locally Most work elements are associated with potential for increased sediment delivery and alteration of streamflow regimes. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Road Maintenance

Work Element: 	Adding crossdrain culverts

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Water quality and habitat elements | Potentially Adverse | No criteria | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Adding cross drains is often designed to decrease sediment delivery potential. Assure that new cross-drains outside of the RHCA are not linked to any stream channel (perennial and/or intermittent). Drainage of existing road systems can be redesigned to substantially reduce sediment delivery, often to only a fraction of the original amount, by increasing the frequency of relief. See Attachment 10. | Cross drains that remove water and fine sediment from the road and inside ditch have the potential to decrease sedimentation to the stream system by: 1). Decreasing the amount of concentrated runoff on the road, and 2). Delivering road runoff to natural vegetative filters that hold the sediment on the landscape. |
| --- | --- | --- | --- |

Activity Component: 	Road Maintenance

Work Element: 	Blading and grading

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | Blading is restricted to outside 25 feet distance from the edges of any stream channel. Do not undercut cut slopes. Sidecasting is not allowed. No road side berms allowed. Include erosion controls and containment structures to avoid the increased risk of sediment delivery. SEE: Roads and Road Maintenance Activity Type, Road Maintained, Ditch Clean-out. | Criteria is sufficient to avoid potential adverse effects because the 25 foot no-action zone would minimize risks of sediment delivery from the road surface disturbance. Sidecasting may result in unintentional sediment delivery. Berms may concentrate road runoff which, within the RHCA, has the potential to be delivered directly to the stream. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | Leave no outside berms. Do not undercut cut slopes. | Berms may concentrate road runoff which has the potential to be delivered, via the road, to the stream system. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Bridge maintenance - riprap, deck cleaning, guard rail repair, abutment repair

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria | The complexity of this activity requires knowledge of site specific conditions and project design, consult locally. Bridge maintenance activities may require the use of equipment that has the potential to increase erosion and sediment delivery. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Culvert maintenance

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Culvert replacement within RHCAs has the potential to adversely affect at-risk fish. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Culvert cleanout should be used to remove sediment and debris (and other blockages) which impede culvert functionality. For cross drain culverts, SEE: Roads and Road Maintenance Activity Type, Road Maintenance Component, Adding cross drain culverts Work Element. | Outside the RHCA, only cross drain (relief) culverts occur. Where road ditches are linked to the channel network, these serve to remove water and sediment from the channel system. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Consider using the following criteria to reduce short-term effects of culvert replacements on perennial streams: - Dewater stream channel associated with the culvert - Maximize sediment/erosion controls on road fills (silt fences, straw bales, geotextile), - Any settling basins will be constructed off-channel. - Collect sediment behind strawbales, silt fences, etc. will be removed from the channel prior to restoring streamflow. For example, see Goat Creek Culvert Replacement (Attachment 6). Ensure that the following CFR is used in project design: Clean Water Act, 40 CFR 232.3(c)(6)(vii) - "the design, construction and maintenance of the road crossing shall not disrupt the migration or other movement of those species of aquatic life inhabiting the water body." Culvert cleanout should be used to remove sediment and debris (and other blockages) which impede culvert functionality. Avoid ground disturbances during spawning and incubation periods. For cross drain culverts, SEE: Roads and Road Maintenance Activity Type, Road Maintenance Component, Adding cross drain culverts Work Element. | Culvert cleanout should be routine maintenance. Cross-drainage culvert form pathways for sediment transport. Culvert cleanout can reduce the amount of sediment available for transport to streams. Functioning ditches effectively direct water and sediment away from the road surface, and with cross-drains, minimizes erosion and delivery to stream channels. |
| --- | --- | --- | --- |

Activity Component: 	Road Maintenance

Work Element: 	Disposal site use

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | No Effect | No criteria. | The RHCA buffer is adequate to prevent adverse effects. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Ditch cleanout

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No ditch cleanout within 25 feet from the edges of any stream channel or crossing (see Attachment 9). No cleanout within any ditch that drains directly to a stream channel. Ditches directly connected to a stream channel require adequate cross drainage to avoid sediment delivery. Use care to not undercut the ditch back slope. Where needed, add ditch armor to reduce potential erosion/sedimentation. No road-edge berms will be left after cleanout. | Cleaning roadside ditches usually results in a net decrease of sediment available for transport to streams. Roadside ditches form pathways for sediment storage and transport. Cleanout can reduce the amount of sediment available, however ditch grading, which is one type of cleanout, has been found to increase erosion, sedimentation significantly (Luce 2001 - see Attachment 9). By preventing ditch cleanout within 25 feet from the stream edge, those ditches that are connected forces increased sediment into the vegetative buffer. Functioning ditches effectively direct water away from the road surface, and ith crossdrains, minimizes erosion and delivery to stream channels. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Ditches directly connected to a stream channel require adequate cross drainage to avoid sediment delivery. Use care to not undercut the ditch back slope. Where necessary, add ditch armor to reduce potential erosion & sedimentation. No road-edge berms will be left after cleanout. | Any potential ground disturbing activity and delivery of sediment via road ditches would be avoided. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Dust abatement - water or chemical

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No Chemical dust abatement allowed in RHCA's. For water drafting, SEE: Mechanical Treatment Activity Type; Dust abatement Activity Component; Water Drafting Work Element. | Use of chemical abatements can be toxic to fish and riparian vegetation. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside of RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Outside of the RHCA and in areas with no drainage to stream, the following chemcial dust abatements are allowed: MgCl2 or CaCl2 salts. Apply dust-abatement additives and stabilization chemicals so as to minimize the likelihood that they will enter streams, (see e.g., Heffner 1996, Attachment 5). Spill containment equipment will be available during chemical dust abatement application. Do not apply dust abatement chemical during rainfall. For water drafting, SEE: Mechanical Treatment Activity Type; Dust abatement Activity Component; Water Drafting Work Element. | Chemical palatives bind the road surface sediments and reduce the potential for erosion and sediment delivery. It is unlikely that receiving waters can have concentrations of chloride salts high enough to cause growth or survival problems for fishes or riparian vegetation (Heffner 1996 -Attachment 5). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Roadside brushing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No brushing within 25 feet of stream crossings or of any stream channel. All Large Woody Debris (LWD) must remain on site. Brushing (cutting vegetation) will be minimal along roads where the vegetation is stabilizing slopes. No ground surface disturbance (use high blading). For Refueling, SEE: Access and Equipment Maintenance Activity Type, Fueling/Maintenance Activity Component. | Any potential ground disturbing activity would be avoided. Action would not affect stream shade provided by plants near the channel. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No ground surface disturbance (use high blading). | Any potential ground disturbing activity and delivery of sediment via road ditches would be avoided. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Slide removal

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Refer to PACFISH/INFISH Standards and Guidelines RF3 (page C-11 in PACFISH). Apply activity where slide damage does not degrade the road prism. Slide material is to be end-hauled off-site if no further mass movement would result from removal of the slide materials. Include erosion controls and containment structures to avoid the increased risk of sediment delivery. Revegetation measures will help to reduce erosion. | These actions can reduce potential sediment delivery post-slide. Allows action on small slides (those that do not degrade the road prism). Removing slide material decreases the potential for sediment delivery because the material is no longer available for transport. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Surface rocking (rock replacement)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Road surfaces may be upgraded with surface rock to reduce erosion and sedimentation so long as cut and fill-slopes are not enlarged or disturbed. Gravel used for this purpose should be washed and cleaned of fines off-site. For blading SEE: Roads and Road Maintenance Activity Type; Road Maintenance Component; Blading and grading Work Element. | Rocking stabilizes the road surfaces and reduces the potential for erosion and sedimentation. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside of RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Road surfaces may be upgraded with surface rock to reduce erosion and sedimentation so long as cut and fill-slopes are not enlarged or disturbed. Gravel used for this purpose should be cleaned of fines. For blading SEE: Roads and Road Maintenance Activity Type; Road Maintenance Component; Blading and grading Work Element. | Rocking stabilizes the road surfaces and reduces the potential for erosion and sedimentation. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Maintenance

Work Element: 	Traffic control

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | No Effect | No criteria. | The activity does not contribute any turbidity or sediment to the environment. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Turbidity and suspended sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Road Restoration

Work Element: 	Bridge replacement

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | The complexity of this activity requires knowledge of site specific conditions and project design. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Consider using the "required mitigation" measures in the Burgdorf Bridge replacement example to reduce effects (See Burgdorf Bridge Replacement example - Attachment 8). | New bridges may restore channel integrity and flood capacity condition. The example "mitigations" were designed to accomplish these restoration objectives. |
| --- | --- | --- | --- |

Activity Component: 	Road Restoration

Work Element: 	Culvert installation and upgrade

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Effects of this activity must be addressed at the local level. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Culvert cleanout should be used to remove sediment and debris (and other blockages) which impede culvert functionality. SEE: Roads and Road Maintenance Activity Type, Road Maintained Component, Adding cross drain culverts Work Element. Avoid ground disturbances during spawning and incubation periods. Consider using the following criteria to reduce short term effects of culvert replacements on perennial streams: - Dewater stream channel associated with the culvert - Maximize sediment/erosion controls on road fills (silt fences, straw bales, geotextile) - Any settling basins will be constructed off-channel. - Collect sediment behind strawbales, silt fences, etc. will be removed from the channel prior to restoring streamflow. See, for example, Goat Creek Culvert Replacement (Attachment 9). Ensure that the following CFR is used in project design: Clean Water Act, 40 CFR 232.3(c)(6)(vii) - "the design, construction and maintenance of the road crossing shall not disrupt the migration or other movement of those species of aquatic life inhabiting the water body." | Culvert cleanout should be routine maintenance. Cross-drainage culvert form pathways for sediment transport. Culvert cleanout can reduce the amount of sediment available for transport to streams. Functioning ditches effectively direct water and sediment away from the road surface, and with crossdrains, minimizes erosion and delivery to stream channels. |
| --- | --- | --- | --- |

Activity Component: 	Road Restoration

Work Element: 	Installation of drainage dips and waterbars

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Building of water bars or installation of drain dips is allowed 25 feet outside of bankfull stream channel. Include erosion controls and containment structures to avoid the increased risk of sediment delivery. Spacing of water barrs should meet specifications as prescribed by the Riparian Road Guide (1994) in Attachment 7 (page 11). | Water barring reduces sediment delivery potential if applied as per the criteria (Riparian Road Guide 1994). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Spacing of water barrs should meet specifications as prescribed by the Riparian Road Guide (1994) in Attachment 7 (page 11). Include erosion controls and containment structures to avoid the increased risk of sediment delivery. | Waterbars are intended to improve road surface drainage. RHCAs are adequate to buffer any associated sediment production. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Restoration

Work Element: 	Storm proofing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements SEE all work elements under Roads & Road Maintenance Activity Type, Roads Maintained and Decommissioning Components. | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Restoration

Work Element: 	Surface material processing - in place rock crushing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | No rock pits or crushing operations within the RHCA. For road surfacing SEE: Roads and Road Maintenance Activity Type; Roads Maintenance Activity Component; Surface Rocking/Rock Replacement Work Element. | Rock pits and crushing opertions within RHCAs has the potential to deliver sediment to stream channels. Road surfacing reduces erosion by stabilizing the road surface and reduces potential sediment delivery. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | No Effect | No criteria. | RHCAs are adequate as buffers of sedimentation from activities associated with this Work Element. Road surfacing increases infiltation capacity and decreases road runoff (potential sediment delivery). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Road Restoration

Work Element: 	Surface shaping and draining

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat element | Potentially Adverse | Blading restricted to outside 25 feet distance from the edges of any stream channel. No sidecasting bladed material within RHCA No road side berms allowed within the RHCA. For ditch cleanout - SEE: Roads and Road Maintenance Activity Type; Road Maintenance Activity Component; Ditch Clean-out Work Element. | Criteria is sufficient to avoid potential adverse effects because the 25 foot no-action zone would minimize risks of sediment delivery from the road surface disturbance. Sidecasting may result in unintentional sediment delivery. Berms may concentrate road runoff which, within the RHCA, has the potential to be delivered directly to the stream. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Leave no outside berms. For ditch cleanout - SEE: Roads and Road Maintenance Activity Type; Road Maintenance Activity Component; Ditch Clean-out Work Element. | Berms may concentrate road runoof which has the potential to be delivered, via the road to the stream system. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this condition assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. would not be | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Threatened, Endangered Species Habitat Restoration

###### Activity Component: 	Aspen Restoration

Work Element: 	Mechanical root shearing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

|  | SEE: Activity Type - Mechanical Treatments; Activity Component - Subsoiling. |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

###### Activity Component: 	Fish population Recovery/Enhancement

Work Element:		All except where otherwise noted	This Work Element includes:• Fish barrier installation or removal •  Exotic species removal – trapping •  Exotic species removal - Rotenone and Antimycin A (Fintrol)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. FISH BARRIER CONSTRUCTION is too complex for application of broad criteria - consult locally. Fish barrier installations, removals, and other instream structures require local design considerations to assess affect because they can pose long-term consequences for channel structure and function. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, Take, and habitat elements | FISH REMOVALS: Follow terms and conditions of the 10(a)(1) or Section 6 State permits for listed, and other State permits for non-listed salmonids. | Fish population recovery activities require attention to terms and conditions to exempt "take" under ESA, or to reduce the adverse effects of fish toxicants such as rotenone. |
| --- | --- | --- | --- |

###### Activity Component: 	Instream Restoration

Work Element:		All except where otherwise noted	This Work Element includes:• Helicopter operations • Hilti drill operations • Mulching for erosion control • Placement of boulders or large woody material

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Instream Restoration

Work Element: 	Powersaw operation

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No refueling within the RHCA. | Criteria are sufficient to avoid potential adverse affects. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | No Effect | No criteria. | The RHCA is an adequate buffer. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Interpretation/Conservation Education

Work Element:		All except where otherwise noted	This Work Element includes:• Signing • Viewing construction • Trail access / building

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | Potentially Adverse | Placement of signs will not expand beyond the footprint of existing disturbed area. SEE Recreation and Facilitities Operations Activity Type, Existing facilities Developed and Dispersed Activity Component. SEE Trails and Trail Maintenance Activity Type | Criteria will prevent introducing adverse materials into the stream. It encourages human uses away from the streambank. The criteria distance would provide adequate protection for root strength of vegetation immediately adjacent to the stream channel, important to maintaining bank stability. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality | Not Likely to Adversely Affect | No criteria. | RHCA are adequate to buffer the stream from disturbance effects. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Meadow Restoration

Work Element: 	Mowing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

|  | SEE: Prescribed Fire Activity Type; Sagebrush Activity Component(s), Mowing / Brushbeating Work Elements |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

###### Activity Component: 	Monitoring Fish and Wildlife

Work Element:		All except where otherwise noted	This Work Element includes:• Fish snorkeling or underwater video •  Channel conditions survey, fish habitat inventory •  Wildlife and fish telemetry •  Wildlife denning/nesting surveys •  Direct wildlife observation •  Aerial wildlife counts •  Redd counts •  Fish electroshocking

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| In RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No criteria | Consult locally. Consultation related to Incidental Take has been completed through State and regulatory agency processes. Follow appropriate State and Federal permits that permit 'take' under 10(a)(1a). | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Quarry Restoration

Work Element: 	Waste storage

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements, and chemical contamination | Potentially Adverse | No criteria | Consult locally. Mine-wastes and related contaminants have the potential to produce serious/severe adverse affects. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside of RHCA's in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements, and chemical contamination | Potentially Adverse | For toxic waste, consult locally. For non toxic waste, quarry restoration is allowed outside of RHCA's | Criteria are sufficient to avoid potential adverse affects because design measures avoid sediment delivery (see Attachment 2). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements, and chemical contamination | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Riparian Improvement

Work Element:		All except where otherwise noted	This Work Element includes ALL Work Elements within this Activity Component

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No ground disturbing activity (disking, drilling,and plowing) within RHCAs. For Planting - Use only hand augers within the RHCA. All fueling and fuel storage areas as well as service landings will be located outside the RHCA. For fertilization, SEE: Insect Suppression Activity Type, Fertilization Activity Component. | Criteria is sufficient to avoid potential adverse effects because the potential for introduction of fertilizer will be negligble (See Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Not Likely to Adversely Affect | No criteria. | The RHCA is an adequate buffer to prevent sediment delivery (Attachment 1). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Snag Creation

Work Element:		All except where otherwise noted	This Work Element includes:• Tree climbing • Inoculation • Girdling trees • Tree topping

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No fueling of equipment within RHCAs. | Criteria are sufficient to avoid potential adverse affects because design measures avoid sediment delivery (see Attachment 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Trails & Trail Maintenance

###### Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Blasting - surface, subsurface, and aerial

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No criteria | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | Blasting will only be allowed in areas where materials (rocks) and or sediment may not potentially reach live waters. Prevent and minimize erosion from trail construction activities by designing and maintaining proper BMPs. Route trails away from crossings to minimize length of trail sections perpendicular to stream that may direct sediment toward stream. For fueling, SEE: Access and Equipment Maintenance Activity Type, Fueling/Maintenance, Fueling/Maintenance of light equipment on site. | These activities do not pose the potential for adverse affects to at-risk fish species. RHCA buffers are adequate to prevent delivery of sediment. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, channel morphology and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Bridge building

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Camping

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Take, water quality and habitat elements | Potentially Adverse | No criteria. | Activity is too complex to develop criteria at this scale. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | RHCA widths are adequate to buffer the stream (based on Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Culvert installation

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, channel morphology and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affects to at-risk fish species. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Ford maintenance/construction

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, take and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Gravel borrowing/borrow pit

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, channel morphology and habitat elements | No Effect | No criteria. | The RHCAs are adequate as a buffer to prevent the small amount of sediment potentiall produced from reaching the stream. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Horses/weed-free hay

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk fish species. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. For access, SEE: Activity Type - Access & Equipment Maintenance; Activity Component - Access to Worksite; Work Element - Access by foot or pack animals. | These activities do not pose the potential for adverse affect to at-risk fish species. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Puncheon/turnpike construction

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

|  | SEE: Activity Type - Trails & Trail Maintenance; Activity Component - Light Maintenance; Work Element - Minor Tread Reconstruction. SEE: Activity Type -Trail Maintenance; Activity Component - Light Maintenance; Work Element - Repair of land structures (puncheons, turnpike, step). |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Reseeding edges/banks

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs within RHCAs, in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Avoid hydro-mulch within 1 site-potential tree height or 100 feet of stream. Hand planting only. No aerial seeding if mixed with any chemicals, such as fertilizers. | Avoiding direct application of mulch to the stream avoids adding sediment, nutrients, and increasing turbidity. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | No Effect | No criteria. | The RHCA is an adequate buffer. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Trail decommissioning

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

|  | SEE: Activity Type - Trails & Trail Maintenance; Activity Component - Light Maintenance; Work Element - Installation of drainage features (water bars, dips, etc.). SEE: Activity Type - Trails & Trail Maintenance; Activity Component - Construction/ Reconstruction/ Heavy Maintenance; Work Element –Tread Construction. |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Trail relocation away from meadows

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

|  | SEE: Activity Type - Trails & Trail Maintenance; Activity Component - Construction/ Reconstruction/ Heavy Maintenance; Work Element - Tread construction. SEE: Activity Type - Trails & Trail Maintenance; Activity Compoment - Light Maintenance; Work Element - Installation of drainage features (water bars, dips, etc.) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

Activity Component: 	Construction/Reconstruction/Heavy Maintenance

Work Element: 	Tread construction

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | Heavy equipment will not be used within the RHCA. Mechanized equipment will stay on the existing tread. Gravel excavation is not allowed inside the RHCA, OR IN THE STREAM CHANNEL! Minimize adverse effects of brushing (loss of shade, bank stability, etc.) when trails or facilities occur within RHCA by leaving as large of an uncut buffer as possible, usually at least a 10 foot buffer along intermittent and ephemeral streams, and a 25 foot buffer along perennial streams. Prevent and minimize erosion from trails by designing and maintaining proper drainage structures with adequate spacing of waterbars especially before stream crossings. Dispose of small (<3 cubic meters) slide and slump materials in stable areas and away from stream channels. Do not remove downed wood from sites (except to clear trails) within 1 site potential tree of a stream channel, unless fisheries personnel determine that large wood objectives for stream and RHCAs in the proposed project area are met. Alternative methods are available to recruit gravel into fords. Hazard trees within one site distance will be kept on site and directionally felled towards the stream when possible. Crews will be trained to avoid adverse take impacts to fish. Pack stock will not be picketed or high lined within RHCA. Camps will be located outside the RHCA. Side casting of soil/sediment from trails directly into stream channels will not occur. No fueling within the RHCA. | Avoids adverse loss of shade,sediment production/delivery, and potential for take. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, channel morphology and habitat elements | Potentially Adverse | Prevent and minimize erosion from trails by designing and maintaining proper drainage structures with adequate spacing of waterbars. | RHCA buffers are adequate to prevent delivery of sediment. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality, channel morphology and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Light Maintenance

Work Element: 	Debris removal (slough, rocks, roots)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Apply erosion control measures to avoid sediment delivery to the stream. Repair materials (rock, logs, etc.) will not be taken from the RHCA. | Small scale of activies avoids potential adverse affects. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk fish species. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Excavating material (borrow pits, trenches)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Potentially Adverse | Apply erosion control measures to avoid sediment delivery to the stream. | The RHCAs are adequate as a buffer to prevent the small amount of sediment potentiall produced from reaching the stream. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Excavating material near water (gravel bar)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, channel morphology and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk fish species. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Installation, clean out, and repair of drainage feature (waterbars, dips, etc)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Rolling dips and/or waterbars will be placed as needed in newly constructed and existing trails, and near bridge crossings to minimize water travel lengths and erosion, which will reduce the potential for sediment delivery to streams. Avoid ground disturbances during spawning and incubation periods. Side casting of soil/sediment from trails directly into stream channels will not occur. To dissipate surface runoff, place woody debris (>3" diameter) perpendicular to the downhill end of rolling dips and/or waterbars. Route trails away from crossings to minimize length of trail sections perpendicular to stream that may direct sediment toward stream. Place rolling dips/waterbars such that water and material potentially moving down trails is directed off the trail and filtered by intervening vegetation. | Drainage features on trails help to reduce erosion and potential sediment delivery. Drainage features that direct water and sediment away from trails are necessary to prevent direct delivery via the trail and potential trail-generated channel system. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, and habitat elements | No Effect | No criteria. | The RHCAs are adequate as a buffer to prevent sediment from reaching the stream. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Log clearing and brushing - mechanical

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, channel morphology and habitat elements | Potentially Adverse | No fueling within the RHCA. | Small scale of activies avoids any adverse affects. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk salmonids. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Log clearing and brushing - non mechanical

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, channel morphology and habitat elements | No Effect | No criteria. | Small scale of activies avoids any adverse affects. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk salmonids. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Minor tread reconstruction

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Apply erosion control measures to avoid sediment delivery to the stream. Repair materials (rock, logs, etc.) will not be taken from the RHCA. Mechanized equipment will stay on the existing tread. No fueling within the RHCA. | Criteria will avoid sediment and fuels from entering the stream. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | No Effect | No criteria. | The RHCAs are adequate as a buffer to prevent the small amount of sediment potentiall produced from reaching the stream. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Repair of land structures (punches, turnpike, steps)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, channel morphology and habitat elements | Potentially Adverse | Apply erosion control measures to avoid sediment delivery to the stream. Repair materials will not be taken from the RHCA. Mechanized equipment will stay on the existing tread. No fueling will occur within the RHCA. | Near water, repair actions have potential to adversely affect at-risk salmonids. Project criteria avoid pathways for potential effects. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk fish species. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Repair of structures near water (bridges, stream fords)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology, and habitat elements | Potentially Adverse | No Criteria | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk salmonids. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Light Maintenance

Work Element: 	Signing (blazes, rock cairns, sign posts)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not collect rocks and/or trees for signing from within the RHCA. No fueling within the RHCA. SEE: Access & Equipment Maintence Activity Type; Fueling/Maintenance Activity Component. | Removing rocks/boulders from the stream, and risk of fuel spills with potential adverse affects are avoided by application of the criteria. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk fish species. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Watershed Restoration

###### Activity Component: 	Hillslope Erosion Control

Work Element:		All except where otherwise noted	This Work Element includes:• Gully check structures: install straw bales, logs, silt fences •  Erosion control mulch or blankets •  Contour felling •  Install wattles

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, Turbidity and suspended sediment | Potentially Adverse | No off-road vehicle transport of waddles, bales, blankets, mulch, etc. within the RHCA. No stream fording by vehicles. Do not use straw bale, log, or rock/gabion check-dams. | The RHCA is adequate as a buffer for sediment produced by all except the listed check dams which have a high incidence of failure. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Turbidity and suspended sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Hillslope Erosion Control

Work Element: 	Contour felling

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Activity is too complex to develop criteria at this scale. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk salmonids. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Hillslope Erosion Control

Work Element: 	Road/landing ripping

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity/suspended sediment | Potentially Adverse | No road or landing ripping within 25 feet of stream channel. Outside of the 25 foot buffer, apply the following criteria: Erosion and sediment controls e.g. sediment barriers and/or straw bales are in place. Avoid work during precipitation events and wet soil conditions. Must be on road grades less than 8 percent (see Attachment 7) and not encroaching on the streambank. Avoid ground disturbances during spawning and incubation periods. No refueling within RHCAs. | These criteria were designed to avoid delivery of sediment to the stream by controlling erosion and transport. Ripping normally renders the site at lower than existing sediment potential because it results in higher infiltration immediately after the project (see Attachment 15). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity/suspended sediment | Potentially Adverse | Disturbed areas are to be seeded with all necessary erosion control measures in place upon completion of activity. | The RHCA is an adequate buffer which prevents transport of fine sediment to streams. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Turbidity/suspended sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Hillslope Erosion Control

Work Element: 	Terracing

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside of RHCAs in watersheds with at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Ground disturbing activities associated with these actions will be conducted with buffer widths sufficient to prevent delivery of sediment to streams by slope gradient <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Include erosion controls and containment structures to avoid the increased risk of sediment delivery. Revegetation measures will help to reduce erosion. | Criteria will prevent significant sediment input into the stream by providing adequate sediment delivery buffer and erosion control (see Attachment 1 - Importance of Hill Slope Steepness). | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Turbidity and suspended sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Hillslope Erosion Control

Work Element: 	Trenching

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | No criteria | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Ground disturbing activities associated with these actions will be conducted with buffer widths sufficient to prevent delivery of sediment to streams by slope gradient <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer Avoid work during wet periods. No trenching on unstable slopes. No sediment routing from trenches into streams. | Potential sediment effects will be filtered by the RHCA. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Turbidity and suspended sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	In-Channel Erosion Control

Work Element:		All except where otherwise noted	This Work Element includes:• Log, root wad or willow bundle revetments • Reshape stream banks and incised channels •  Lay back vertical banks •  Install barbs •  Structural bank controls (riprap, etc.)

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Take and sediment | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Take and sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Revegetation

Work Element:		All except where otherwise noted	This Work Element includes:• Seeding – aerial or hand application •  Planting , upland and riparian – grass, forb, shrub, tree •  Mulch application •  Hanson dibble

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs within RHCAs watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Avoid hydro-mulch within 1 site-potential tree height or 100 feet of stream. Hand planting only. No aerial seeding if mixed with any chemicals, such as fertilizers. | Avoiding direct application of mulch to the stream avoids adding sediment, nutrients, and increasing turbidity. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | No Effect | No criteria. | The RHCA is an adequate buffer. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Revegetation

Work Element: 	Site prep - surface scarification, tilling, ripping

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Turbidity and suspended sediment | Potentially Adverse | No criteria. | Need consideration of site specific conditions - consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Avoid sediment production and delivery to streamsr by using standard erosion and sediment control measures. Avoid scarification on slopes over 20% (see Attachment 1 - Importance of Hill Slope Steepness). To prevent sediment movement into stream channel use the following buffers: <5% slope, 115 ft. buffer 6% - 10% slope, 165 ft. buffer 11% - 15% slope, 210 ft. buffer 16% - 20% slope, 250 ft. buffer 21% - 25% slope, 300 ft. buffer 26% - 30% slope, 325 ft. buffer 31% - 40% slope, 350 ft. buffer 41% - 50% slope, 400 ft. buffer 51% - 60% slope, 430 ft. buffer >60% slope, 450 ft. buffer | Potential sediment effects will be filtered by the RHCA. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Turbidity and suspended sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Sediment Control

Work Element:		All except where otherwise noted	This Work Element includes:• Maintain instream basin •  Construct instream basin (impoundment) •  Instream log structure

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | No criteria. | Need consideration of site specific conditions. Consult locally. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Turbidity and suspended sediment | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Watershed Monitoring

Work Element:		All except where otherwise noted	This Work Element includes:• Establish/monitor erosion plots •  Manual instream measurements •  Monument plots

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Take and habitat elements, turbidity and sediment | Potentially Adverse | Streamside monitoring adjacent to actively spawning at-risk fish would be acceptable as long as duration is brief and infrequent (usually less than 15 minutes). Crews will be trained to avoid adverse impacts to fish. No erosion plots within the RHCA. | The criteria minimize the potential for harassment and/or disturbance of redds. RHCA buffers are adequate. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside of RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery | Take and habitat elements, turbidity and sediment | No Effect | No Criteria | The RHCA is adequate as a buffer for sediment produced by these activities. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Watershed Monitoring

Work Element: 	Install gage

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Take, water quality, habitat | Potentially Adverse | No mechanized equipment within RHCA. Do not install gages during spawning/incubation periods. Project will be designed to avoid modifying habitat, including channel morphology. Crews will be trained to avoid adverse effects to fish. | Criteria avoid in-channel disturbance during critical spawning/incubation period, and modifications of habitat. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Take, water quality, habitat | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Watershed Monitoring

Work Element: 	Instream water/sediment collection

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Take, water quality, habitat | Potentially Adverse | No mechanized equipment within RHCA. No substrate sampling allowed. No installation of instream equipment during spawning and incubation periods. Sampling activities will be conducted during times when spawning fish are not present. Do not conduct any activities over established redds. Fisheries Biologist will survey areas for redds. Crews will be trained to avoid adverse impacts to fish and redds. | Criteria avoid harm to listed fish by avoiding sampling during critical spawning/incubation periods. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Take, water quality, habitat | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

### Activity Type: 	Weeds and Chemical Treatments

###### Activity Component: 	Biological Control

Work Element		All except where otherwise noted	This Work Element includes:• Collection and release of insects or other biological controls •  Monitoring by sweep netting •  Transport of bio-control agents by vehicle

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk salmonids. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Biological Control

Work Element: 	Competitive seeding

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not make aerial application of fertilizer within 300 feet of perennial streams. Fertilizer applications within 300 feet of intermittent drainages will be done only when dry. When PACFISH/INFISH standards & guidelines RA3 and RA4 are met, then add the following: do not apply within 25 feet of streams and supersaturated soils. Apply by following labeling instructions. | Criteria will prevent nitrogen spike event into water. Only high concentrations from spills are potentially toxic to fish. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Cultural Control

Work Element: 	Chaining

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No ground disturbing activity (chaining) within RHCAs. | Criteria is sufficient to avoid potential adverse effects because the potential for introduction of sediment will be avoided (See Attachment 1). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | The RHCA is an adequate buffer to prevent sediment delivery from erosion associated with weed chaining (Attachment 1). | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cultural Control

Work Element: 	Fertilize - by hand, machine, or aerial

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | Do not make aerial application within 300 feet of perennial streams. Applications within 300 feet of intermittent drainages will be done only when dry. When PACFISH/INFISH standards & guidelines RA3 and RA4 are met, then add the following: do not apply within 25 feet of streams and supersaturated soils. Apply by following labeling instructions. | Criteria will prevent nitrogen spike event into water. Only high concentrations from spills are potentially toxic to fish. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Not Likely To Adversely Affect | No criteria. | No potential adverse affect outside the RHCA. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cultural Control

Work Element: 	Injection/cut stump

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No application of injection herbicides within 25 feet of stream channel. No application of herbicides within or adjacent to roadside ditches or other possible pathways to water (eg. irrigation ditches). Herbicide application will be designed and implemented to avoid introduction into live water. | The buffer will insure protection of stream bank stabilitiy and prevent contamination of live water with herbicide. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality, take, channel morphology and habitat elements | Not Likely To Adversely Affect | No criteria. | RHCAs, by definition, provide an adequate buffer for filtering sediments and chemicals. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cultural Control

Work Element: 	Mulch - by hand or machine

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs within RHCAs, in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | Potentially Adverse | Avoid hydro-mulch within 1 site-potential tree height or 100 feet of stream. Hand planting only. No aerial seeding if mixed with any chemicals, such as fertilizers. | Avoiding direct application of mulch to the stream avoids adding sediment, nutrients, and increasing turbidity. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Turbidity and suspended sediment | No Effect | No criteria. | The RHCA is an adequate buffer. | No Effect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Cultural Control

Work Element: 	Use grazing to control weeds, fencing or herding

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No grazing allowed in RHCAs for biological control. | Criteria is sufficient to avoid potential adverse affects (see Attachment 2, livestock grazing). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | For grazing after area has been burned - Livestock grazing will be excluded from prescribed burn units for a time period previously agreed upon during consultation, or a time period which would allow the vegetation to regeneration to a stage that can withstand grazing effects sufficiently to achieve and maintain natural rates of surface erosion. In no case shall either of the above time period be less than two years. | Grazing for biological control outside of the RHCA does not pose a risk for salmonids. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Herbicide Control

Work Element: 	Aerial application by fixed wing or helicopter

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | The complexity of this action within RHCAs requires local consultation. For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, and may be mediated by site specific landscape and climatic | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | The complexity of this action requires local consultation. For programmatic application of this action, the complexity of the activity requires extreme precautions, and may be mediated by site specific landscape and climatic conditions. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

Activity Component: 	Herbicide Control

Work Element		All except where otherwise noted	This Work Element includes:• Hand crank granular spreader •  Liquid application •  Spray from ATV • Granular Application •  Back pack sprayer with spray wand •  Spray from truck mounted boom or spray • Hand controlled wand with soaked wick

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria. | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No criteria | Consult locally. The complexity of this activity requires knowledge of site specific conditions and project design. | Potentially Adverse |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No Criteria. | No at risk salmonids and/or habitat present. | No Effect |

Conditional Statement	Effects Pathway	Conservation Recommendation	Rationale

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Use the Herbicide Risk Assessments (2002) to develop BAs. (Consider using the following criteria to reduce effects: No application of herbicides, except: use only wipers for herbicide application within RHCAs. Restricted to the following herbicides: Rodeo. Within 15 feet of live waters or shallow water table, the only herbicide authorized is Rodeo, without surfactants. Equipment used for transportation, storage, or application of chemicals shall be maintained in a leak proof condition. No herbicide storage, mixing or post-application cleaning would be authorized within the RHCA. Trained personnel would monitor weather conditions at spray sites during application. ●All herbicide labels would be strictly enforced ●No broadcast spraying would occur when wind velocity exceeds 5 miles per hour within 100 feet of open water. ●No broadcast spraying would occur when wind velocity exceeds 8 miles per hour. ●No spraying would occur if precipitation is occurring or is imminent (within 24 hours). ●No spraying would occur if air turbulence were sufficient to affect the normal spray pattern.) | For programmatic application of this action in RHCAs, the complexity of the activity requires extreme precautions, thus the need to restrict methods and types of herbicide application. See Attachment 4 (Glyphosate Risk Assessment & Noxious Weed Risk Assessment). |
| --- | --- | --- | --- |

###### Activity Component: 	Information

Work Element: 	Education/outreach

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | No Effect | No criteria. | These activities do not pose the potential for adverse affect to at-risk salmonids. | No Effect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Manual Control

Work Element: 	Hand clip seed heads or pull weeds

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water Quality and Habitat | Potentially Adverse | No fueling of equipment within RHCAs. | Criteria are sufficient to avoid potential adverse affects because design measures avoid sediment delivery (see Attachment 2). | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Mechanical Control/Restoration

Work Element:		All except where otherwise noted	This Work Element includes:• Weed whacker use •  Plowing – transport of heavy equipment •  Mowing of weeds •  Drill seeding •  Aerial application of seeds

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in RHCAs in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | No plowing within the RHCA. Mowing will be conducted to avoid adverse effects to streambanks and riparian vegetation and significant effects to streamside shade. No mowing within 100 feet or 1 site-potential tree height (whichever is greater) from the stream channel. (see Attachment 2 – Extent of effect for stream side disturbances). For drill seeding, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding-disking, drilling, fertilizing and plowing Work Element For Aerial Application of Seed, SEE: Range Infrastructure Activity Type; Rangeland Restoration Activity Component; Seeding – Aerial Work Element | The buffer is designed to avoid potential sediment transport and reduced rooting strength of riparian vegetation adjacent to streams. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs outside the RHCA in watersheds with at-risk fish species or with designated critical habitat or unoccupied habitat critical to species recovery. | Water quality and habitat elements | Potentially Adverse | The timing of plowing would be limited to mid-late summer when intermittent stream channels are normally dry. | The RHCA is adequate to buffer the potential for sediment transport to streams. | Not Likely to Adversely Affect |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |

###### Activity Component: 	Weed prevention

Work Element: 	Wash vehicles, water drafting

Conditional Statement	Effects Pathway	Potential Effect	Project Criteria	Rationale	Final Effect

| The action occurs in watersheds with at-risk fish species, or with designated critical habitat or unoccupied habitat critical to species recovery. | Water Quality and Habitat | Potentially Adverse | No vehicle washing within RHCAs. The determination of whether the pumping activity would occur in streams with at-risk fish, will require fisheries biologist review. Water drafting/pumping will maintain a continuous surface flow of the stream, without altering the original wetted width. Follow the National Marine Fisheries Service guidelines for screening pump intakes (May 1996: Juvenile Fish Screen Criteria for Pump Intakes). | Criteria are sufficient to avoid potential adverse affects by preventing the potential for any contaminants to enter waterways. | Not Likely to Adversely Affect |
| --- | --- | --- | --- | --- | --- |
| The action occurs in watersheds without at-risk fish species or with no designated critical habitat or unoccupied habitat critical to species recovery. Criteria applied using this conditional statement assume that activity effects inside these watersheds would not be transferred downstream and affect at-risk fish or their occupied habitats. | Water quality and habitat elements | No Effect | No criteria. | No at risk salmonids and/or habitat present. | No Effect |