Table of Contents

SECTION A – REQUIREMENTS AND PRICES	2

CONTRACT ACRONYMS	2

A1.  General.	3

A2  Bid Items	3

A3  Item 1 Pricing	4

SECTION B. TECHNICAL SPECIFICATIONS	6

B1.  General Requirements	6

B2.  Operations	6

B3.  Personnel Requirements	9

B4.   Aircraft Requirements	11

B5.  Avionics Requirements	14

B6.  Maintenance Requirements	17

B7.  Servicing Requirements	19

SECTION C – CONTRACT TERMS AND CONDITIONS	19

C1  Contract Terms and Conditions – Commercial Items (52.212-4 SEPT 2005) [Tailored SEPT 2005]	19

C2  Contract Terms and Conditions Required to Implement Statutes or Executive Orders-Commercial Items (52.212-5 NOV 2006)	22

ADDENDA TO CONTRACT TERMS AND CONDITIONS	24

C3  Inspection/Acceptance (52.212-4(a)), the following is added:	24

C4  Personal Identity Verification of Contractor Personnel (52.204-9 NOV 2006)	25

C5  Availability of Funds for the Next Fiscal Year  (52.232-18 APR 1984)	26

C6  Aircraft Insurance	26

C7  Government Furnished Property	26

C8  Prework Meeting	26

C9 Authority of Government Representatives	26

ADMINISTRATIVE MATTERS	27

C10  Personnel Conduct	27

C11  Safety and Accident Prevention	27

C12  Mishaps	27

C13  Federal Airport and Airway Excise Taxes	29

C14   Fuel	29

CONTRACT PERIOD AND RENEWAL	29

C15  Contract Period	29

C16  Option to Extend the Term of the Contract (48 CFR 52.217-9, Mar 2000)	29

C17  Reserved	29

C18  Exclusive Use Period	29

C19   Mutual Extension of Exclusive Use Period	29

AVAILABILITY REQUIREMENTS	30

C20  Availability Requirements	30

C21  Schedule of Operations and Reaction Time	30

C22   Maintenance During Availability Period	30

C23  Unavailability and Damages	30

MEASUREMENT AND PAYMENT	30

C24  Daily Availability	30

C25  Flight Time	30

C26  Mobilization/Demobilization	31

C27  Additional Pay Items (from Schedule of Items)	31

C28  Government Miscellaneous Charges	32

BILLING AND REPORTING REQUIREMENTS	32

C29  Billing Office	32

C30  Invoice Submissions	32

C31  Aircraft Use Report	32

C32  Department Of Defense Approval To Utilize Military Airfields Within The State Of Alaska.	32

C33.  Contractor Responsibilities — Conduct of Business on a Military Installation.	34

C34 EXHIBITS	35

Unacceptable Lap Belt and Shoulder Harness Conditions	36

Acceptable Paint Schemes	37

First Aid & Survival Kits	38

Auxiliary FM Radio Interface	39

Helicopter Like Makes and Models	40

Standard Interagency Load Calculation Method and Form	41

Helicopter Fuel Consumption and Weight Reduction Chart	43

Statement of Equivalent Rates for Federal Hires (48 CFR 52.222.42)	44

Wage Determination No. 2003-0344 Rev 2, dated 02/02/2005	45

Wage Determination No.  2005-2017 Rev. 2 Dated 12/08/2006	46

Unavailability Conversion Chart	48

Transportation Worksheet	49

section d – instructions to offerors	51

INTRODUCTION	51

D1.  General Information	51

INSTRUCTIONS TO OFFERORS--COMMERCIAL ITEMS (52.212-1 JAN 2006) [Tailored JAN 2005]	51

D2 North American Industry Classification System (NAICS) Code and Small Business Size Standard	51

D3  Proposals	51

D4   Offer Contents	51

D5  Late Submissions, Modifications, Revisions, and Withdrawals of Offers	52

D6  Data Universal Numbering System (DUNS) Number)	52

D7  Special Notice to Offerors	52

EVALUATION--COMMERCIAL ITEMS (48 CFR 52.212-2 JAN 1999)	52

D8  Offer Acceptability	52

D9  Evaluated Price	52

D10  Aircraft  Requirements	53

D11 Pilot Qualifications And Past Performance.	53

D12  Offeror Capability	53

D13  Tradeoff Analysis and Contractor Selection	53

D14  Notice of Award	54

section e – offeror’s representations, certifications and other statements	55

52.212-3 OFFEROR REPRESENTATIONS AND CERTIFICATIONS—COMMERCIAL ITEMS (NOV 2006)	55

SECTION E EXHIBITS	57

OFFEROR’S MISCELLANEOUS INFORMATION	57

AIRCRAFT QUESTIONNAIRE	58

REFERENCE QUESTIONNAIRE	59

PILOT QUESTIONNAIRE –	60

# SECTION A – REQUIREMENTS AND PRICES

# CONTRACT ACRONYMS

AC	Advisory Circular

AD	Airworthiness Directive

AMD	Aviation Management Directorate

A&P	airframe and power plant

APCO	Association of Public-Safety Communications Officials

ASM	Aviation Safety Manager

ASO	Aviation Safety Office

ASTM	American Society for Testing and Material

ATC	air traffic control

CFR	Code of Federal Regulations

CO	Contracting Officer

COR	Contracting Officer’s Representative

COTR	Contracting Officer’s Technical Representative

CFR	Code of Federal Regulations

CTCSS	continuous tone coded squelch system

DM	degrees/minutes/decimal minutes

DOI	Department of Interior

DOT	Department of Transportation

ELT	emergency locator transmitter

EPA	Environmental Protection Agency

ERG	Emergency Response Guidebook

FAA	Federal Aviation Administration

FAR	Federal Acquisition Regulations

FS	Forest Service

FTR	Federal Travel Regulations

GVW	gross vehicle weight

GPM	gallons per minute

GPS	global positioning system

HIGE	hover-in-ground effect

HOGE	hover-out-of-ground effect

IAT	interagency aviation training

ICAO	International Civil Aviation Organization

ICS	intercom system

IFR	instrument flight rules

IP	Institute of Petroleum

MMSB	Manufacturer’s Mandatory Service Bulletins

NBC	National Business Center

NFPA	National Fire Protection Association

NTSB	National Transportation Safety Board

NWCG	National Wildfire Coordinating Group

PA	public address system

PFD	personal flotation device

PIC	pilot-in-command

PPE	personal protective equipment

PSD	plastic sphere dispenser

PSI	pounds per square inch

PTT	push to talk

RFP	Request for Proposals

SFI	Safety Foundation Incorporated

STEP	Single-skid, Toe-In and Hover Exit/Entry Procedures

TBO	time between overhaul

TSO	technical service order

UL	Underwriter’s Laboratory

USDA	United States Department of Agriculture

VFR	visual flight rules

VNE	velocity not to exceed

VOX	voice activation

VSWR	voltage standing wave radio

## A1.  General.

Furnish flight services consisting of one helicopter, fully contractor maintained with pilot.  Services shall be for the exclusive use of the Bureau of Land Management, Anchorage Field Office in support of transportation of Government personnel and cargo for remote radio site maintenance, and other interagency governmental work. (See Exhibit entitled, Project Description, for more information.)

## A2  Bid Items

ITEM	DESCRIPTION

1.	Designated Base:              	All equipment, facilities, and personnel required under this contract shall be delivered  to and removed from   Anchorage,  Alaska  (BLM Anchorage District Office, Campbell Tract Facility) (N1)

Aircraft Requirement:		One Light Helicopter equipped as specified in Section B (N2)

Fuel  Servicing Vehicle:  		 None

Requirement

Crew Requirements: 	Pilot-in-Command (PIC) and, Mechanic

Target Aircraft Characteristics:	-- Seating: Five passenger seats

-- Cruising airspeed:  115 nautical miles per hour at sea level

-- Useful load:  (HIGE) 1,500 pounds at 80 degrees F at 4,000 feet pressure altitude

-- Range:  280 statute miles at sea level (not including 20 minutes reserve fuel.

-- Turbine engine rated at 641 shaft horsepower exclusive of installation

limitations.

N1.    Contractor may be required to operate from an alternate base(s) when dispatched by the government.

N2. The AS350BA, AS350B1, BH206L3, BH206L/C30-P (with STC #SH296NM) or equal should fulfill the above target requirements; however, offerors should assure their specific helicopter is capable of meeting the above target requirements.  Offers which propose use of a different type helicopter should submit sufficient information to the Contracting Officer to demonstrate that the above requirements will be met or exceeded.

## A3  Item 1 Pricing

BUREAU:			Bureau of Land Management, Anchorage District Office

DESIGNATED BASE:		BLM Campbell Tract, Anchorage, Alaska,

EXCLUSIVE USE PERIOD:	May 22, 2007  through August 19, 2007 (90 Calendar Days)

ITEM 1 – Complete shaded areas only.

| DESIGNATED BASE | BLM Campbell Tract, Anchorage | EXCLUSIVE USE PERIOD | May 22, 2007 to Aug 19, 2007 |
| --- | --- | --- | --- |

| OFFEROR NAME |  |
| --- | --- |
| AIRCRAFT FOR THIS PRICING SCHEDULE | Make/Model | FAA Registration # |

BELOW INFORMATION SHALL BE COMPLETED BY THE CONTRACTING AGENCY AT AWARD

| Aircraft payload is an element of your offer. The hover-in-ground effect (HIGE) payload that was confirmed for the above aircraft is made a part of the contract. Payload is computed using the Section A payload requirement and will be verified at the time of aircraft inspection. |
| --- |
| GOVERNMENT USE ONLY |
| CONFIRMED HIGE PAYLOAD AMOUNT |  |
| PERFORMANCE REFERENCE (FLIGHT MANUAL PAGE/CHART) |  |

| ITEM | DESCRIPTION | AMD-23 PAY ITEM CODE | QUANTITY | UNIT | UNIT PRICE | EXTENDED AMOUNT |
| --- | --- | --- | --- | --- | --- | --- |
| 2.a. | DAILY AVAILABILITY PRICE PER DAY – GUARANTEED SUBJECT TO BEING AVAILABLE (C24) |
| 2007 | 1st year – 5/22-8/19 | AV | 90 | DAYS | $ | $ |
| 2008 | 2nd year – 5/22-8/19 | AV | 90 | DAYS | $ | $ |
| 2009 | 3rd year – 5/22-8/19 | AV | 90 | DAYS | $ | $ |
| 2010 | 4th year – 5/22-8/19 | AV | 90 | DAYS | $ | $ |
|  | TOTAL PRICE – AVAILABLITY- 4 YEARS | $ |

| 1. | VARIABLE PAY ITEMS | AMD-23 PAY ITEM CODE | QUANTITY | UNIT | UNIT PRICE |
| --- | --- | --- | --- | --- | --- |
| 1.b. | FLIGHT TIME - HOURLY RATE (C25) Dry Rate |
| 2007 | 1st YEAR – 5/22-8/19 | FT | * INDEFINITE | HOUR | $ |
| 2008 | 2nd YEAR – 5/22-8/19 | FT | * INDEFINITE | HOUR | $ |
| 2009 | 3rd YEAR – 5/22-8/19 | FT | * INDEFINITE | HOUR | $ |
| 2010 | 4th YEAR – 5/22-8/19 | FT | * INDEFINITE | HOUR | $ |

| c. | Subsistence Allowance | PD | INDEFINITE | Overnight | Per FTR Schedule |
| --- | --- | --- | --- | --- | --- |
| d. | Contractor Miscellaneous Costs | SC | INDEFINITE | EACH | Actual Cost |

*See D9.1 – The Government workload estimate identified in Section D will be applied to the flight rates  and other contractor bid variable rates offered.  The totals for availability and estimated flight and other variable bid items for all years will be added together to arrive at the estimated evaluated price for each offeror.

WILL BE COMPLETED BY AGENCY AT TIME OF AWARD

Aircraft payload is an element of your offer. The hover-in ground effect (HIGE) payload that was confirmed for the below aircraft is made a part of the contract. Payload is computed using the Section A payload requirement and will be verified at the time of aircraft inspection.

| Aircraft Make and Model |  |
| --- | --- |
| Serial Number |  |
| FAA Registration Number |  |
| Confirmed Aircraft Payload - HIGE |  |
| Performance Reference (Flight manual page/chart) |  |

# SECTION B. TECHNICAL SPECIFICATIONS

## B1.  General Requirements

B1.1  Scope of Contract

B1.1.1  The intent of this contract is to obtain flight services to support transportation of personnel and/or cargo in support of natural resource missions; administrative and related activities as directed by the Government.  Helicopter operations are usually in response to activities in flat to rolling terrain as well as steep and rugged terrain at altitude. Personnel will be required to maintain a level of confidence relative to the work accomplished under this contract.  Fulfillment of these programs can only be accomplished through an effective working relationship between the Government and Contractor.  Employees of the Contractor are an integral element to assure mission accomplishment.  The Contractor’s employees’ cooperation, professionalism and positive attitude towards accomplishment of the mission and aviation safety is essential to establish the necessary relationship that must exist to successfully complete this contract.

B1.1.2  Aircraft furnished under this contract shall be operated and maintained by the Contractor.

B1.1.3  Aircraft furnished under this contract shall be subject to the exclusive use and control of the Government, 24 hours per day, 7 days per week throughout the periods specified under Section A, Deliveries or Performance.  The aircraft shall not be operated except as directed by the Contracting Officer or an authorized representative of the Contracting Officer.

B1.1.4	The Government has interagency and cooperative agreements with other federal agencies, state agencies and private landholders, and may dispatch aircraft under this contract for such cooperative use.

B1.1.5  Aircraft furnished under this contract may be required to perform in Alaska, Canada, or any of the 48 conterminous United States.  (See Section B Supplements for additional technical specifications)

B1.1.6  Aircraft may be used in support of law enforcement activities.  Refer to Subsection B2.3.12 for information on flight operations.

B1.2  Certification

B1.2.1  The Contractor shall be certified under the provisions of Federal Aviation Regulations (14 CFR) Part 119, "Certification: Air Carriers and Commercial Operators."  The Contractor's approved operation specifications shall authorize the following operation:  category and class of aircraft and conditions of flight required under this contract which are: VFR day/night, passengers, and cargo.

B1.2.1.1 Aircraft used on this contract will be operated and maintained under provisions of 14 CFR Part 135 and carried on the list required by 14 CFR 135.63 unless otherwise authorized by the Contracting Officer (CO).

B1.2.2 The Contractor shall be certificated under 14 CFR Part 133, Rotorcraft External Load Operations which authorizes Class B loads, as a minimum.

B1.2.3 The Contractor shall be certificated under 14 CFR Part 137, Agricultural Aircraft Operations for flight activities requiring water/retardant bucket operations.

B1.2.4 The Contract aircraft shall have a Standard Airworthiness Certificate.  The installation of any equipment required by this contract must be Federal Aviation Administration (FAA) approved.

B1.3  Order of Precedence (Specifications) In the event of inconsistencies within the technical specification, the following order shall be used in such resolution: (i) Typed provisions of these specifications; (ii)  OAS Supplements incorporated by reference; (iii) 14 CFR incorporated by reference; (iv) Aircraft manufacturer’s specifications; (v) Other documents incorporated by reference.

B1.4 Contracts.  The Contractor shall keep a copy of the contract and all modifications in each contract aircraft while operating the aircraft for the government.

B1.5 Substitution of Aircraft or Personnel  At the discretion of the Government, the Contractor may substitute aircraft or personnel during performance of the contract provided each substitution is inspected and accepted in accordance with  Section C.

## B2.  Operations

B2.1  Security of Aircraft and Equipment

B2.1.1 The Contractor is responsible for the security of their aircraft, vehicles and associated equipment used in support of this contract.

B2.1.2  Physical Security.  Any aircraft used under this contract will be physically secured and disabled via a dual-lock method whenever the aircraft is unattended.  Any combination of anti-theft devices designed to lock aircraft flight control surfaces when not in use, or designed to secure an aircraft to the ground, is acceptable, provided they are appropriate for the aircraft.  Operational environments and personnel safety must be considered when selecting the locking devices and methods to be used.

B2.1.2.1  Removal and/or disabling of locking devices and methods must be incorporated into preflight checklists to prevent accidental damage to the aircraft and must be installed in a manner which precludes its inadvertent interference with in-flight operations.

B2.1.2.2  Examples of Acceptable Locking Devices & Methods are identified below:

Keyed Magneto

Keyed Starter Switch

Keyed Master Power Switch

Hidden Battery Cut-Off Switches

Hidden Start Relay Switches

Throttle/Power Lever Lock

Mixture/Fuel Lever Lock

Locking Fuel Cut-Off

Locking Tie-Down Cable

B2.1.2.3Examples of Unacceptable Locking Devices & Methods

Locking aircraft doors

Fenced or gated parking area

B2.2  Pilot Authority and Responsibility

The Contractor shall ensure that the pilot is responsible for operating the aircraft within its operating limits, safety of the aircraft, its occupants, and cargo.  The contract pilot shall:

B2.2.1 Comply with Government directions, except, when in the pilot's judgment, such compliance would violate Federal or State regulations or contract terms and conditions.   The pilot has final authority to determine whether the flight can be accomplished safely and shall refuse any flight or landing which is considered hazardous or unsafe.

B2.2.2  Not permit any passenger to ride in the aircraft or any cargo to be loaded therein unless authorized by the CO or his/her authorized representative.

B2.2.3  Be responsible for computing the aircraft’s weight and balance for all flights and for ensuring that the gross weight and center of gravity do not exceed the aircraft's limitations.  The pilot shall also properly secure all cargo.  When required by the Government, the pilot shall utilize the Standard Interagency Load Calculation Method and its forms.  A sample of the form is included as an exhibit to this section.

B2.2.4 The pilot may perform preventive maintenance in accordance with the Contractor’s operations specifications.

B2.2.5   The pilot may function as a mechanic when the aircraft is not available due to required maintenance, provided he/she has met the following requirements:

B2.2.5.1 The pilot has met all of the mechanic qualifications and experience requirements specified herein.

B2.2.5.2  Any time that the pilot is engaged in mechanic duties will apply against the pilot's duty limitations.  All time in excess of 2 hours (not necessarily consecutive) will apply against the pilot's flight limitations.

B2.2.5.3  A pilot functioning as a mechanic shall not accomplish scheduled maintenance, such as 50- and 100-hour inspections.

B2.2.6  All maintenance shall be recorded in accordance with 14 CFR Part 43.9.

B2.3 Flight Operations

B2.3.1  Regardless of any status as a Public Aircraft Operation, the Vendor shall operate in accordance with his approved FAA Operations Specifications, and all portions of 14 CFR Part 91, and each certification required under Sub-section B1.2 unless otherwise authorized by this contract or the CO. The Contractor shall ensure that all personnel operate in compliance with the following requirements:

B2.3.2  Pilot shall remain at flight controls while rotors are turning with the following exception. For post-flight procedures and/or preventative maintenance purposes only and after engine(s) have been shut down, the pilot may exit the aircraft while the rotor(s) are turning, if the Rotorcraft Flight Manual allows and if the pilot remains within the arc of the rotor(s).  The pilot shall coordinate this action with the helicopter manager prior to exiting the aircraft.  No passengers shall be on board or inside the arc of the rotor(s) when the pilot exits the aircraft.

B2.3.3 Hazardous Materials.  The Contractor may be required to transport hazardous materials.  Such transportation shall be in accordance with 49 CFR, Exemption DOT-SP-9198, and the Department's Aviation Transport of Hazardous Materials Handbook.  A copy of the current exemption, DOI handbook, and DOT Emergency Response Guidebook (ERG) must be carried aboard each aircraft transporting hazardous materials.  It is the vendor’s responsibility to ensure that each employee that may perform a function subject to this DOT exemption receives required training.  The required training is only satisfied by completing the DOI’s Module A-110, Aviation Transportation of Hazardous Materials.  The training can be completed online at http://www.iat.gov.  Documentation of this training shall be retained in the employee’s records and be made available to the Government when requested.

B2.3.4  Day/Night Use (Single-Engine Helicopters at Night).  Pilots of single-engine helicopters shall be limited to flight during daylight hours and under VFR conditions only.  Daylight hours are defined as 30 minutes before official sunrise to 30 minutes after official sunset, or, in Alaska, during extended twilight hours when terrain features can be readily distinguishable from a distance of at least 1 mile.

B2.3.5  Flight Plans.  Pilots shall file and operate on a FAA, ICAO, or a DOI bureau flight plan.  Contractor flight plans are not acceptable.  Flight plans shall be filed prior to takeoff when possible.

B2.3.6  Flight Following.  Pilots are responsible for flight following with the FAA, ICAO, and/or in accordance with the DOI bureau’s approved flight following procedures.  Check-in intervals shall not exceed one-hour intervals under normal circumstances.  (Note: see Avionics section for Satellite Phone/AFF requirements)

B2.3.7 Manifesting.  The pilot-in-command shall ensure that a manifest of all crewmembers and passengers on board has been completed.  A copy of this manifest shall remain at the point of initial departure.  Manifest changes will be left at subsequent points of departure when practical.  In those instances where multiple short flights will be made in a specific geographical area which involves frequent changes of passengers, a single manifest of all passengers involved may be left with an appropriate person to preclude unreasonable administrative burden.

B2.3.8  Passenger Briefing.  Before each takeoff, the pilot-in-command shall ensure that all passengers have been briefed in accordance with the briefing items contained in 14 CFR Part 135.  In those instances where short flights are made, the briefing does not need to be repeated unless new passengers come aboard.  Additionally, the briefing should include location/use of the following:

a.  Emergency Locator Transmitter (ELT).

b.  First Aid Kit.

c. Personal Protective Equipment.

d. Battery Cutoff Switch

e. Fuel Shutoff Valve

f. Operation of doors and emergency exits

g. Operation and use of seat belts/shoulder harnesses

B2.3.9  There shall be NO SMOKING in the aircraft.

B2.3.10  Toe-in, Single –Skid, Step-out Landings  Due to the hazardous nature of these types of landings; toe-in, single-skid, step-out landings are prohibited.

B2.3.11  Flights with doors open or removed.  The Government may request the pilot to fly aircraft with any door(s) removed or opened (sliding doors).  The aircraft external registration number shall be displayed in such a manner as not to be compromised by this requirement.  The pilot shall be responsible for removing and securing the doors. The flight manual supplement approving flight with doors off must be in the flight manual and current.

B2.3.12 Upon offer by the government and acceptance by the contractor, aircraft shall fly law enforcement missions. Missions include transporting federal personnel to a law enforcement location, low-level reconnaissance or surveillance flying, and prisoner transportation. The pilot is the final authority for the conduct of flight operations.

B2.3.13   Personal Protective Equipment  The following items will be furnished by the Contractor and inspected for condition at the start of the contract and anytime during the contract:

B2.3.13.1 Aviator’s flight helmet, consisting of a one-piece hard shell made of polycarbonate, Kevlar, carbon fiber, or fiberglass, must cover the top, sides (including the temple area and to below the ears), and the rear of the head.  The helmet shall be equipped with a chinstrap and shall be appropriately adjusted for proper fit.  Flight helmets for helicopter usage must conform to a national certifying agency standard, such as DOT, Snell-95, SFI, or an appropriate military standard, and be compatible with required avionics (see section B5.2.3.2). "Shorty" (David Clark style) helmets are not approved.  Flight helmets meeting this requirement include but are not limited to, the SPH-4, SPH-5, SPH-4B, HGU-56 and HGU-84.  Helmets designed for use in fixed wing aircraft do not provide adequate protection for helicopter occupants and are not approved for helicopter use.

B2.3.13.2  Pilots shall wear long-sleeved shirt and trousers (or long-sleeved flight suit) made of fire-resistant polyamide or aramide material or equal.  Pilots shall wear boots made of all-leather uppers that come above the ankles and leather or polyamide or aramide gloves. The shirt, trousers, boots and gloves shall overlap when seated to prevent exposure to flash burns. Clothing must contain labels identifying the material either by brand name or MIL-Spec.

B2.3.13.3 A personal flotation device (PFD) shall be worn when conducting flight operations (water bucket dipping, snorkeling) over water sources such as ponds, streams, lakes, rivers, and coastal waters.  This equipment may, but is not required to, meet the standards of 14 CFR Part 135.167(a) (1).  Automatic inflation (water-activated) PFD’s are not authorized.

B2.3.13.3.1 Personal Flotation Devices (PFD) required by 14 CFR 91 or Life Preserver(s) (TSO-C13) required by 14 CFR 135 shall be on board all aircraft operated over water and beyond power-off gliding distance to shore.

B2.3.13.3.2  All occupants of aircraft operated over water and beyond power-off gliding distance to shore shall wear an FAA approved PFD or Life Preserver, or a U.S. Coast Guard Type III PFD except in multiengine aircraft.

B2.3.14 Anti-exposure suits will be worn in all single-engine aircraft (readily available to occupants of multi-engine aircraft) when conducting extended over water flights (as defined in 14 CFR 1.1) and when the water temperature is estimated to be 50 degrees Fahrenheit or less.

B2.3.15  Personal Protective Equipment For Ground Operations

B2.3.15.1  While within the safety circle of an operating (rotors turning) helicopter, all personnel will wear the following PPE:

B2.3.15.2 Shirt with sleeves overlapping gloves and pants with legs overlapping boots, hard hat with chin strap, hearing protection (i.e., ear plugs, noise suppression "earmuffs"), and eye protection (i.e., goggles, helmet visor down).

B2.3.15.3 During all fueling operations, fuel-servicing personnel shall wear a long-sleeved shirt, long trousers, leather boots, and gloves. The shirt and pants must be made of 100% cotton or other natural fiber, or labeled as non-static.

## B3.  Personnel Requirements

B3.1   Pilot Qualifications

B3.1.1 The Contractor shall provide a pilot(s) who meets the following minimum qualifications and who possesses the required certificate or evidence of having satisfactorily passed the evaluations for the required tasks:

B3.1.2  An FAA commercial pilot certificate with appropriate category, class, and type rating if required.

B3.1.3  A current second class medical certificate issued in accordance with  14 CFR Part 67.

B3.1.4 An FAA currency competency check completed  in accordance with 14 CFR Part 135.293 in the make and model aircraft offered for this contract .

B3.1.5  Pilot flying hours shall be verified from certified pilot records.  Further verification of flying hours may be required at the discretion of the CO.

B3.1.6  An agency flight evaluation  to be flown at the discretion of the COTR in make and model of aircraft to be flown under this contract.  The flight evaluation will be in an aircraft supplied by the Contractor, at no expense to the Government.

B3.1.7  Proficient operation of all equipment identified in Section B (e.g., water retardant bucket, GPS).  The agencies may require pilots to demonstrate this proficiency during an evaluation flight.

B3.1.7.1  Pilots shall demonstrate their ability to perform the following functions with the required GPS. The pilot may use only an abbreviated checklist in the performance of this evaluation.

B3.1.7.2  Determine the geographic coordinates of a destination identified on a sectional aeronautical chart.

B3.1.7.3  Install destination coordinates.

B3.1.7.4  Acquire distance/bearing information to a destination.

B3.1.7.5  Record as a waypoint, coordinates of various locations while en route to a primary destination.

B3.1.7.6  Navigate from a present position to a selected recorded waypoint or between two recorded waypoints.

B3.2 The precision placement of externally carried cargo is an operational requirement of this contract when requested by the government. Any combination of load and line that is 50 feet or less in length will require a basic external load endorsement. Sling loads that have a combined length greater than 50 feet will require a Vertical Reference Longline endorsement. Pilots will be required to demonstrate their ability during an agency evaluation flight. Pilots will be required to demonstrate vertical reference skills with a 150’ longline to an AMD Inspector pilot. Pilots shall provide written evidence of qualification in accordance with 14 CFR 133 to transport Class A, B, or C external loads as appropriate. Pilots must show evidence of 5 hours of external load experience within the last 120 days.

Note:  Vertical Reference:  A term used to describe the pilot technique of controlling the aircraft while looking down vertically at the load attached to the cargo hook.

B3.3 Not Used

B3.4  Pilots shall have logged minimum flying time as pilot-in-command as follows:

Minimum pilot-in-command time accumulated as follows:

B3.4.1    1,500 hours . . . in helicopters.

B3.4.2      100 hours . . . in helicopters in the last 12 months.

B3.4.3    100 hours . . .in the weight class of the helicopter offered.  Defined as: “small” - up to an approved gross weight of 7,000 pounds; “medium” -  above 7,000 pounds up to 12,500 pounds; “large” - above 12,500 pounds.

B3.4.4         100 hours . . . in turbine engine helicopters.

B3.4.5        50 hours . . .in the make and model of the helicopter offered.  Pilot flight hour requirements in make and model may be reduced by 50 percent if the pilot shows evidence of satisfactorily completing the manufacturer's approved ground school and flight check in make, model, and series of the helicopter used on this contract.  (See exhibit).

B3.4.6   10 hours in make, model, and series of helicopter offered in the last 12 months.  (See exhibit)

.

B3.4.7   Last 90 days Compliance with 14 CFR 61.57 or 135.247 as appropriate.

B3.4.8    10 hours in designated mountainous areas in the make and model helicopter offered.

B3.4.9  200 hours Total mountain flying. Defined as experience in operating helicopters in mountainous terrain as identified in 14 CFR 95 Subpart B – Designated Mountainous Area.  Operating includes maneuvering and numerous takeoffs and landings to ridgelines, pinnacles, and confined areas.

B3.5  The Contractor shall make available a complete Pilot Information Form (AMD-64B) for each pilot that will be utilized during the Availability Period on any helicopter covered by this contract.  The Pilot Information Form, available from the Contracting Officer, shall list the pilot's qualifications with reference to the specifications listed.

B3.6  Flight Crew Members Duty and Flight Limitations

B3.6.1 Assigned duty of any kind shall not exceed 14 hours in any 24-hour period.  “Duty” includes flight time, ground duty of any kind, and standby.  Local travel up to a maximum of 30 minutes each way between the work site and place of lodging will not be considered duty time. Flight crewmembers shall be subject to the following duty hour limitations:

B3.6.2 A maximum of 14 consecutive duty hours during any assigned duty period.

B3.6.3 Pilots are required to have two 24-hour periods off duty within any 14 consecutive calendar days.  Pilots shall have 2 calendar days off duty when involved in fire management activity in the 48 conterminous states within any 14 consecutive calendar days.

B3.6.4  The pilot shall be given a minimum of ten consecutive hours of rest (off duty) prior to any assigned duty period.

B3.7  Each crewmember shall report all flight time, regardless of how or where performed, except personal pleasure flying. This record shall be used to administer flight and duty time limitations.  Pilots reporting for duty under this contract may be required to furnish this record of all duty and flight time during the previous 14 days.

B3.7.1  Flight time to and from a duty station as a flight crewmember (commuting) shall be reported and counted toward limitations if it is flown on a duty day.  “Flight time” includes but is not limited to:  military flight time; charter; flight instruction; 14 CFR Part 61.56 flight review; flight examinations by FAA designees; any flight time for which a flight crewmember is compensated; or any other flight time of a commercial nature, whether compensated or not.

B3.7.2  Pilot flight time computations shall begin at liftoff and end at touchdown and will be computed from the flight hour meter installed in the aircraft.

B3.8  Flight crewmembers shall be limited to the following restrictions which fall within their duty hour limitations:

B3.8.1  A maximum of eight hours flight time during any assigned duty period.

B3.8.2   When a pilot acquires 36 or more flight hours in a consecutive six-day period, he/she shall be given the following 24-hour period off for rest, after which a new six-day cycle will begin. A maximum of 42 hours flight time during any consecutive six-day period.

B3.9  During times of prolonged heavy fire activity, federal agencies may issue a notice reducing the pilot duty day and/or increasing days off on a geographical or agency-wide basis.

B3.10  Two-pilot crew flight time.

B3.10.1  A maximum of 10 hours flight time for a flight crew consisting of two pilots (8 hours for fire missions) during any assigned duty period.

B3.10.2   A maximum of 50 hours flight time during any consecutive six-day period.  When a pilot acquires 40 or more flight hours in a consecutive six-day period, the pilot shall be given the following one calendar day off (24 hours in Alaska) for rest, after which a new six-day cycle shall begin.

B3.11	Aircraft Maintenance Personnel Requirements

B3.11.1	The maintenance person shall possess a valid FAA Certificate with both Airframe and Powerplant ratings, and must have held the certificate with both ratings for a minimum of 24 months and meet the following experience requirements:

B3.12.2   18 of the last 24 months:  Total time actively involved in aircraft maintenance as a certificated Airframe and Powerplant maintenance person immediately preceding the start of this contract.

B3.12.3    12 months:  Total experience maintaining helicopters (3 of those 12 must have been in the 2 years immediately preceding the contract start date).  of the same category specified in this agreement.

B3.12.4   12 months:  Total time maintaining an aircraft of the same make and model offered on this agreement or (satisfactory completion of the manufacturer's maintenance course or an equivalent FS or AMD approved Contractor’s training  program for the make and model aircraft offered will meet this requirement).

B3.12.5  One field season:  Total time maintaining an aircraft of the same make and model as offered under field conditions (three months maintaining the aircraft away from the contractor’s base of operations with minimal supervision will meet this requirement).

B3.12.6  The Contractor shall make available, prior to the initial inspection, a mechanic qualification form (OAS-41) for each mechanic that will perform maintenance during the Availability Period on any helicopters covered by this contract.  The qualification form, available from the Contracting Officer, shall list the mechanic’s qualifications with reference to the specifications listed above.

B3.13  Availability of Mechanic.  The mechanic shall be present at the designated base of operations and, when ordered by the Government, accompany the helicopter to alternate bases of operations.  The mechanic shall be present to service, inspect, and repair the helicopter.

B3.15  Mechanic Duty Limitations  Mechanics shall not exceed the following duty time limitations:

B3.15.1  Within any 24 hour period, mechanics shall have a minimum of eight consecutive hours off duty immediately prior to the beginning of any duty day.  Travel, not local in nature, may be counted as duty time.

B3.15.2 Mechanics will have two full 24 hour periods off during any 14 day period during the performance of this contract.  Off duty periods need not be consecutive.

B3.15.3  Duty time includes availability and work or alert status at any job site.

B3.15.4  The government may further restrict daily duty hours and may remove mechanics for fatigue or other causes before reaching their daily duty limitations.

B3.15.5  The mechanic will be responsible for keeping the Government apprised of his/her duty limitation status.

B3.15.6 When the contractor’s approved maintenance program requires a daily (24 hour) maintenance inspection/release, the contractor  shall provide a relief mechanic when requested by the government.  Payment shall be in accordance with C13.

B3.15.7  Relief or substitute mechanics reporting for duty under any contract may be required to furnish a record of all duty time during the previous 14 days.

## B4.   Aircraft Requirements

B4.1.  Condition of Equipment

B4.1.1  Contractor-furnished aircraft and equipment shall be operable, free of damage, and in good repair.  Aircraft systems and components shall be free of leaks except where limits are specified by the manufacturer.

B4.1.2  Prior to inspection and acceptance, the Contractor shall permanently repair or replace all windows and windshields that have been temporarily repaired.   All windows and windshields shall be maintained and  be clean and free of scratches, cracks, crazing, distortion or repairs, which hinder visibility.  Repairs, such as safety wire lacing and stop drilling of cracks, are not acceptable permanent repairs.

B4.1.3  The aircraft interior shall be clean and neat.  There shall be no unrepaired tears, rips, cracks, or other damage to the interior. The exterior finish, including the paint, shall be clean, neat, and in good condition. Any corrosion shall be within manufacturer or FAA acceptable limits.

B4.1.4  These conditions of equipment concerns are in addition to airworthiness requirements.

B4.2  Equipment and Accessories

The following equipment and accessories are required for all items:

B4.2.1  Navigational publications to include the Supplement for the area of operations and a complete set of current sectional aeronautical charts covering the area of operation.

B4.2.2  First aid kit containing items specified in Attachment B1 shall be carried aboard the aircraft on all  flights.

B4.2.3  A survival kit containing items specified in the Exhibit shall be carried aboard the aircraft on all flights and shall be included in weight and balance/load calculations.

B4.2.4  Tents and sleeping bags for the aircraft's crew shall be Contractor-furnished for use in  camps and staging areas.

B4.2.5  Free air temperature gauge.

B4.2.6  Aircraft shall have approved lighting for night operation in accordance with 14 CFR Part 91, including instrument lights.

B4.2.7  Lap belt and Shoulder Harness condition.  The following items are not acceptable:

Webbing

Frayed webbing: 5 percent or more

Torn webbing

Crushed webbing

Swelling: twice the thickness of original web, or if difficult to operate through hardware

Creased webbing: no structural damage allowed

Sun deterioration: severe fading, brittleness, discoloration, and stiffness

Hardware

Inoperable buckle

Other inoperative hardware

Nylon bushing at shoulder harness-to-lap belt connection missing or damaged

Fabricated bushings or tie wraps used as bushings

Rust/corrosion: only minor surface rust/corrosion allowed

Wear: wear beyond normal use

Stitches

Broken or missing stitches

Severe fading or discoloring

Inconsistent stitch pattern

TSO Tags (see FAR 21.607)

Missing

Illegible

Age

B4.2.7.1 Belts/fabric over 10 years from date of manufacture require close inspection because of the elements they are exposed to, but do not have to be replaced if it can be determined they are in serviceable condition

B4.2.8  Double strap shoulder harness with automatic or manual locking inertia reel for each front seat occupant. Single or double strap shoulder harness and lap belt for remaining seats is a requirement of this contract.  Shoulder straps and lap belts shall fasten with one single-point metal-to-metal, quick-release mechanism.  Heavy-duty (military style) harnesses with fabric loop connecting the shoulder harness to the male portion of the lap belt buckle, similar to those installed in transport category helicopters, are acceptable.

B4.2.9  One flight meter (Datcon P/N 102149 or equal) recording in hours and tenths, and activated by an oil pressure switch wired in series with collective switch or equivalent system to record flight time only.  The meter shall be installed in a location readable from the front observer's seat.

B4.2.10  Fire extinguisher(s), as required by 14 CFR 135.155, shall be a hand-held bottle with a minimum 2-B: C: rating, mounted and accessible to the flight crew while seated.  The fire extinguisher shall be maintained in accordance with NFPA Manual #10, Standards for Portable Fire Extinguishers or the Contractor’s 135 operations manual.

B4.2.11  Dual controls are required for initial pilot performance evaluation.  Dual controls shall be removed prior to contract performance.

B4.2.12  Flight instruments for low visibility flight conditions, including gyroscopic bank and pitch indicator (ADI), directional gyro, vertical speed indicator and rate of turn indicator or skid/slip indicator or inclinometer.

B4.2.13  Cabin heater with windshield defogger.

B4.2.14  High skid-type landing gear.

B4.2.15  Personnel access step.  A personnel access step for aircraft with a floor height greater than 18 inches to assure safe entrance and exit from each door. A section of external cargo rack may be utilized as a step by providing a clear space covered with nonskid material.  Steps shall be available in the field to be installed when cargo racks are removed for weight reduction.

B4.2.16  Tundra boards or snow pads.

B4.2.17  Thirty five cubic feet of internal enclosed baggage space to include:

B4.2.17.1  Bell 206 Only. Fifteen cubic foot baggage compartment within the aircraft fuselage specifically designed to carry cargo separate from the cabin.  This compartment must be capable of accommodating 58-inch long shovels, rakes, and other tools (requiring rear bulkhead modification of baggage compartment of some models).

B4.2.17.2  Baggage compartments for the AS-350 series aircraft shall include the Canadian Eurocopter cargo pod P/Ns ECL-018LH and ECL-019RH.

B4.2.17.3  Bell 206 Series Only.  External cargo racks with tie-down nets, straps, or bungees shall be provided for installation if requested by the Contracting Officer. The Contractor shall be notified prior to the start of each season if external racks shall be installed. The racks shall meet the following requirements:  Cargo racks shall be at least 2.5 inches deep with a horizontal surface area of at least 48 x 15 inches, and meet construction methods and procedures prescribed by Advisory Circulars 43.13-1A and 43.13-2A or an approved supplemental type certificate.  The Alaskan Skycraft style Transporters meet this requirement.

B4.2.18  Aircraft manufactured with a parcel/storage area behind the rear passenger seats shall be equipped with a cargo restraint system for that area.

B4.2.19  A white strobe light system visible from above is required.  If the aircraft certification requires the anti-collision light to be aviation red, then a white strobe light with an independent activating switch shall be provided in addition to the red strobe.  A ½ white and ½ red lens is acceptable.

B4.2.20  The aircraft  shall be equipped with a forward-facing recognition pulse light system.  The system shall pulse alternating on and off.  The Bell series helicopters requires improved light positioning such as the Field Support Services P/N LLP-6. The AS-350 standard landing light/taxi light position is acceptable.  A pulselite model 1220/2410-2 will provide for the pulse requirement.

B4.2.21    Reserved

B4.2.22 Approved engine air intake filtering devices capable of filtering sand and dust particles (Bell 206 only).

Note:  Contractor is cautioned that the helicopter will be expected to operate in a dirty environment.  Rotorwash can be expected to include sand, ash, dust, and other abrasive particulate.

B4.2.23  Snow kit or necessary equipment to allow flight during falling snow.

B4.2.24  Locking caps on all fuel ports.

B4.2.25  Main rotor tie-down kit for AS-350 similar to Dart Aerospace Kit ECL-013 or equal.

B4.2.26  Operation with the AS-350 Pocket Door removed shall be FAA approved.

B4.2.27	 One FAA approved cargo hook installation that automatically closes and resets the release mechanism after use and that employs both electric and manual release systems or one cargo hook that may be loaded and locked in a single motion with one hand, and is rated at the maximum lifting capacity of the aircraft. (On-Board Systems TALON LC Keeperless hook meets this requirement.)

B4.2.27.1  The cargo hook and associated systems (including any remote hook systems) shall be completely disassembled, inspected, lubricated, if required, and subjected to an operations check in all operating modes at 2-year intervals.  The inspection and maintenance shall be accomplished in accordance with the manufacturers operating and maintenance instructions as supplemented by this requirement.

B4.2.28   Counterwound or rotation resistant wire rope with swaged fittings shall have a minimum breaking strength of 3.75 times the working load with appropriate placards.

B4.2.28.1  When requested by the government, “sling gear” is as follows: three 50’ lengths of wire rope.

B4.2.28.2  Electric cables shall be protected from pinching by hooks or shackles, and damage caused by stretching of the line.  The electrical wire shall be long enough at the aircraft cargo hook end to prevent a swinging load from unplugging the electrical connector.

B4.2.29  Two (2)  “Barrel slings” or lifters to transport two 55-gallon drums by external load.

B4.2.30  The aircraft shall be equipped with a convex mirror for observation of the sling load by the pilot.  For aircraft equipped and modified for vertical reference external load operation (i.e., door gauges, modified seat, alternate cargo hook release positions, bubble window, etc.) or for helicopters such as the MD Model 500 where direct vertical reference is possible the convex mirror is not required.

B4.2.31  An MS 3101E-24-11S, nine-pin connector shall be provided as the power source for a helitorch or remote cargo hook.  Pin D shall be airframe ground.  Pin E shall be switched 28VDC, protected by a manually operable, 50-amp circuit breaker.  The water bucket open switch shall also activate this circuit.  The connector shall be mounted adjacent to the cargo hook (within 12 inches) and be supported in such a way that jettisoning the load will not damage the connector.  A lanyard shall be provided for support of the connector.

NOTE:  This connector has multiple circuit capacity sufficient to provide power and control for contractor-furnished equipment.  It is required that the long line remote hook, fixed tank, or water bucket be wired through this connector.  A list of water buckets with required pin wiring can be found in FS/OAS Drawing A-16 as furnished in the attachments.  Wiring diagrams for various equipment configurations are available from USDI Aviation Management, 300 E. Mallard Drive , Suite 200, Boise, ID 83706 or USDA Forest Service, 3833 S. Development Avenue, Boise, ID 83705-5354.

B4.2.32  An accessory power source consisting of an MS 3112E-12-3S three-pin connector, accessible near the right rear exit.  Pin B shall be airframe ground; pin A shall be +28VDC (for 28-volt aircraft); and pin C shall be +14VDC (for 14-volt aircraft).  The circuit shall be protected by a 5-amp circuit breaker.

B4.2.33  All installations and modifications prescribed above shall comply with 14 CFR Part 43 and shall be FAA-approved.

B4.3   reserved

B4.4.   Portable fuel servicing equipment  The Contractor shall furnish with each aircraft a listed (UL/FM) portable fuel pump, barrel stem, hoses and filtration system for refueling in remote areas.

B4.4.1 The filtration system must be qualified to Institute of Petroleum (IP) effluent quality.

B4.4.2  All filter cartridges shall be changed when fuel flow is reduced from normal flow rates.  Fuel filter cartridges shall be changed annually.  The filter cartridge change date will be placarded on the filter vessel.

B4.4.3  The Contractor shall have on the aircraft two spare refueling system filter cartridges.  The filter cartridges shall be new and stored in sealed containers to prevent contamination.

B4.4.4  The pump can be hand or electrically operated.

B4.4.5 Aircraft refueling systems must have a bonding system with cable and clips to allow system bonding with aircraft.

## B5.  Avionics Requirements

B5.1  General.  The following systems shall be furnished, installed and maintained by the Contractor in accordance with the manufacturer’s specifications and the installation and maintenance standards of section B5.3.  Detailed avionics systems performance requirements are listed in Avionics Operational Test Standards (copies available upon request from DOI AM Avionics, or at http://www.oas.gov/library/handbooks/aots.pdf

B5.1.1 All Aircraft solicited by DOI (which are required to be VHF-FM radio equipped) shall be furnished with at least one P25 Phase-I, (digital-capable) aviation radio by January 1, 2010. In aircraft required to be furnished with more than one VHF-FM radio, all such radios must be P25 Phase-I compliant by January 1, 2010 date.

B5.2  Communication/Navigation/Other Systems

B5.2.1   One automatic portable emergency locator (ELT/AP) or an automatic fixed/portable emergency locator (ELT AF/AP) meeting TSO-C91A or TSO0C126 utilizing an external antenna and meeting the same requirements as those detailed for airplanes in 14 CFR Part 91.207 (excluding section f.) shall be installed per the manufacturer’s installation manual, in a conspicuously marked location that is easily accessible, and readily removable in the event of an accident.

B5.2.1.2  In lieu of the ELT requirement above, an automatic fixed emergency locator transmitter (ELT AF) meeting TSO-C91A or an ELT that requires tools to remove from the aircraft may be acceptable when a handheld portable ELT/EPIRB is furnished.  The ELT/EPIRB shall be compact and easily carried by the PIC.

B5.2.2  One VHF/AM airways communication transmitter/receiver system, minimum 760 transmit and receive channels, 118.000 to 136 MHz in 25 kHz increments, minimum 5 watts transmit carrier power.  Weatherproof external broadband antennas of applicable frequency shall be used, mounted on the exterior of the helicopter.

B5.2.3  One VHF-FM multi-mode aeronautical transceiver (FM-1), which provides selection of  both  narrowband (12.5 kHz) and wideband (25.0 kHz) bandwidth operation on each channel.

B5.2.3.1  The transceiver's operational frequency range shall include the band of 150 to 174 MHz. The operator shall be able to program any of a minimum of 15 preset channels with any usable frequency within that band while in flight.

B5.2.3.2  Carrier output power shall be 10 watts nominal value (original design specification).  The transceiver shall be capable of displaying receiver and transmitter operating frequency, and shall provide both receiver and transmitter activation indicators for main and guard.  Simultaneous monitoring of both main (150-174 MHz) and guard (168.625 MHz) receivers is required.   Single bandwidth guard receivers which operate in the wideband (25.0 kHz) mode are acceptable.   Scanning of the guard frequency is not acceptable.  The transceiver's/encoder's operational controls must be located and arranged so that both the pilot and observer/co-pilot, when seated, have full and unrestricted movement of each control without interference from their clothing, the cockpit structure, or the flight controls.

B5.3 Satellite Phone System.  The Contractor shall furnish  and install an Iridium Satellite Phone system.  The  installation shall be  approved by the FAA. The primary use of this system shall be to maintain flight following with a ground base while the helicopter is in flight and out of radio range.

B5.3.1  The Iridium handset, or remote dialer, shall be mounted in a convenient location in the cockpit.  The location should provide ready and unencumbered access to its controls by both front seat occupants.

B5.3.2  The Iridium phone system audio shall be permanently wired into the aircraft audio system, to integrate the Iridium phone into it.  The configuration shall allow, as a minimum, either or both front seat occupants to use the phone through their headsets.  It is preferred that all occupants of the aircraft be able to converse over the Iridium phone through their headsets, though keypad access may be limited to the two front seat occupants.

B5.3.3  The Iridium phone system shall include the ability to pre-program at least six (6) phone numbers that can be quickly selected by either front seat occupant while in flight.

B5.3.4  A TSO C-129a L-band antenna, acceptable to the manufacturer of the Iridium phone system, shall be installed on top of the fuselage, giving as much a view of the overhead hemisphere as possible.

B5.3.5  The Iridium phone system may be integrated into the Automated Flight Following system (see B5.9.4), either using the same Iridium communicator or having a separate Iridium communicator.  In the former case, it is acceptable for phone calls to interrupt the transmission of AFF position reports for brief periods of time, and flight crews will be instructed as to this conflict.

B5.4    One CTCSS sub-audible tone encoder (which may be an integral part of the transceiver), with the lowest 32 TIA/EIA-603 standard tone frequencies (from 67.0 to 203.5 Hz, less 69.3 Hz) being selectable, shall be interfaced to the above transceiver. It is desired that the encoder provide a display of the selected tone or tone frequency.

B5.4.1   The encoder/transceiver system shall be capable of encoding a 110.9 Hz tone on all guard (168.625 MHz) transmissions.

B5.5   The following models of VHF-FM aeronautical transceivers are known to meet the above requirements:

Eureka Radio ERS-96000NB w/external tone encoder

NAT(Northern Airborne Technology) NPX-138N-050

NAT(Northern Airborne Technology) NTX-138-050

Technisonics TFM-138 (serial number 1540 and up)

Technisonics TFM-138B (all)

Technisonics TFM-138C (all)

Technisonics TFM-500    (all)

Wulfsberg  RT-5000/C-5000 with Guard option

Wulfsberg RT-9600N w/C-962A control head

B5.5.1   Bendix-King/BK Radio model KFM-985 multi-mode transceivers do not meet the referenced requirements for Interagency Fire helicopters.

B5.5.2  The National Fire and Aviation Executive Board (NFAEB) has directed that all DOI and USDA Forest Service fleet and contract aircraft (required to be VHF-FM radio-equipped) shall be furnished with a P25 (digital) aviation radio by January 1, 2010.  The NFAEB has also directed that the National Wildfire Coordinating Group (NWCG) will determine when VHF-FM radio usage will begin in the pure P25 digital format, at some later date.   Accordingly, no later than January 1, 2010, at least one P25-compliant VHF-FM radio shall be furnished in DOI contract aircraft that are required to be VHF-FM equipped.

B5.5.3  In aircraft equipped with more than one VHF-FM radio, all additional radios must be P25-compliant by the (post-2010) date to be determined for use under the pure P25 digital format by NWCG. Contractually required VHF-FM mobile radios for use in fuel service vehicles and portable VHF-FM radios furnished for pilot call-back shall also be P25 compliant by the date set by NWCG.

B5.6   Provisions for auxiliary VHF-FM (AUX-FM)  portable radio:

B5.6.1   Interface for installing and properly operating an auxiliary VHF-FM portable radio through the aircraft's audio control system(s).  The interface shall consist of the appropriate wiring from the audio control system, terminated in an ITT/Cannon type MS3112E12-10S 10-pin connector conveniently located for use by the observer/copilot, and utilizing the contact assignments as specified by drawing FS/OAS-17 in the exhibits.

B5.6.2   One weatherproof, external, broadband antenna covering the 150-174 MHz band, with associated RG-58A/U (or equivalent) coaxial cable and connector, terminated in a bulkhead-mounted, female BNC connector (type UG-290A), conveniently located for use by the observer/copilot adjacent to the above 10-pin connector (Comant model CI-177 or equal).

B5.6.3   Mounting facilities  for securely installing the auxiliary VHF-FM portable radio in the cockpit in accordance with the FAA AC 43.13-2A specifications. Locate and arrange the mounting facilities so that a seated observer/copilot has full and unrestricted movement of the radio's controls, without interference from the 18-inch adapter cable, clothing, cockpit structure, or flight controls.

B5.6.4    Positive-polarity microphone excitation voltage shall be provided to the AUX-FM system from the aircraft DC power system through a suitable resistor network.  A blocking capacitor shall be provided to prevent the portable radio microphone excitation voltage from entering the system.  Sidetone for the AUX-FM shall also be provided (NAT model AA34-300, Premier model PA-34, or equivalent).

Note: In lieu of the above AUX-FM requirements, the Contractor may substitute one VHF-FM aeronautical transceiver (FM-2) which meets the requirements (less guard) for the Aux VHF-FM aeronautical transceiver (FM-1), as detailed above.

B5.7   One Global Positioning System (GPS) meeting the following requirements

B5.7.1   One panel-mounted GPS shall be permanently installed in the aircraft.  The GPS shall utilize the WGS-84 datum, reference latitude and longitude coordinates in the DM (degrees/minutes/decimal minutes) mode for aircraft positioning, utilize an approved, fixed, external aircraft antenna, and be powered by the aircraft electrical system.  The GPS installation shall be FAA-approved (or approval pending). Handheld and/or marine type equipment is not acceptable.

B5.7.2   The GPS unit shall be mounted in the aircraft's radio/instrument panel.  The unit shall be convenient for use by both the pilot and front seat observer.

B5.8   Audio Systems

B5.8.1  Two separate audio control systems (which may be combined in a single unit) for the pilot and observer/co- pilot to select receiver audio outputs and transmitter microphone/push to talk (PTT) audio inputs for all installed radios and PA systems.  Each system shall also allow the pilot and observer/copilot to independently adjust both ICS and receiver audio output levels (NAT AMS-42F or equivalent).

B5.8.2  Transmitter selection and operation.  Separate transmitter selection controls for the pilot’s and observer/ copilot’s microphone/PTT inputs.  Configure the system so the pilot and observer/copilot may each simultaneously select and utilize a different transmitter (or PA system when installed) via their respective microphone/PT.  Whenever a transmitter is selected, the companion receiver audio shall automatically be selected for the corresponding earphone.  Transmitter sidetone audio shall be provided for the user as well as for cross-monitoring via the corresponding receiver selection switch on the other audio control system.

B5.8.3    Receiver selection and operation.   Separate controls for both pilot and observer/copilot to select audio from one or any combination of available receivers.  The ICS-equipped aft passenger positions shall monitor the receiver(s) as selected by the observer/copilot.  The receiver audio output shall be free of excessive distortion, hum, noise, and crosstalk, and shall be amplified sufficiently to facilitate ease of use in a noisy cockpit/cabin  environment.

B5.8.4  The audio system(s) controls must be located and arranged so that both the pilot and observer/copilot, when seated, have full and unrestricted movement of their respective controls without interference from their clothing, the cockpit structure, or the flight controls. Labeling and marking of controls shall be clear, understandable, legible, and permanent. Electronic label maker marking is acceptable.

B5.8.5   An intercommunications system (ICS) for the pilot, observer/copilot, and  the two aft cabin exit positions.  ICS audio shall mix with, but not mute, selected receiver audio.  An ICS audio level control shall be provided for each position above. Adjustment of the ICS audio level at any position shall not affect the level at any other position.  A "hot mic" capability, controlled via an activation switch or voice activation (VOX), shall be provided for the pilot and observer/copilot positions.   ICS sidetone audio shall be provided for the earphones corresponding with the microphone in use.  The ICS audio output shall be free of excessive distortion, hum, noise, and crosstalk; and shall be amplified sufficiently to facilitate ease of use in a noisy cockpit/cabin environment.

B5.8.6   Earphones, microphones, PTT’s, and jacks designed for operation with  600-ohm earphones and carbon-equivalent, noise-canceling boom type microphones (Gentex electret type model 5060-2, military dynamic type M-87/AIC with type CE-100 TR preamplifier, or equivalent) with U-174/U (single/male) type connector plug.  The pilot position only may be configured for low impedance (dynamic) operation.

B5.8.6.1  All earphone/microphone jacks in the aircraft (except the pilot's) shall be U-92A/U (single/female) type, which will accept U-174/U type plugs.

B5.8.6.2   Separate PTT switches for radio transmitter and ICS microphone operation at the pilot, observer/copilot, and the two aft exit passenger positions.  The pilot's PTT switches shall be mounted on the cyclic control.  The observer/copilot's and aft exit passengers' PTT switches shall be mounted on the cord to the earphone/microphone connector. In lieu of the observer/copilot's cord-mounted PTT switches, a footswitch-operated PTT system may be utilized.  ICS PTT switches for the other required positions shall be mounted on the cord to the earphone/ microphone connector.

B5.8.7   Although the contract aircraft may not be certified for IFR flight, the aircraft's static pressure system, altimeter instrument system , and automatic pressure altitude reporting system shall be maintained in accordance with the IFR requirements of 14 CFR 91.411 and inspected and tested every 24 calendar months as specified by 14 CFR Part 43, appendices E and F.

B5.9   Other Avionics:

B5.9.1  One ATC transponder and altitude reporting system meeting the requirements of 14 CFR Part 91.215 (a)and (b) and tested and inspected per 14 CFR Part 91.413.

B5.9.2  A complete set of schematic and wiring diagrams, covering all installed avionics systems shall be carried aboard each aircraft or the aircraft's dedicated service vehicle or at the aircraft’s designated base.

B.5.9.3 Avionics Installation and Maintenance Standards:

B5.9.3.1  All avionics systems used in or on the aircraft for this contract and their installation and maintenance shall comply with all manufacturers’ specifications and applicable Federal Aviation Regulations contained within 14 CFR regardless of any exclusions for public aircraft allowed in 14 CFR.

B5.9.3.2  Strict adherence to the recommendations in FAA AC 43.13-1B Chapter 11, "Aircraft Electrical Systems", and  Chapter 12, "Aircraft Avionics Systems," as well as AC 43.13-2A Chapter 1, "Structural Data", Chapter 2, "Radio Installation," and Chapter 3,"Antenna  Installation," is required.

B5.9.3.3   All avionics systems requiring an antenna shall be installed with a properly matched, aircraft-certified antenna unless otherwise specified.  Antennas shall be polarized as required by the avionics system, and have a VSWR of 2.5 to 1 or better.

B5.9.3.4  Avionics equipment mounting location and installation shall not interfere with passenger safety, space, and comfort.  Avionics equipment will not be mounted under seats designed for deformation during energy attenuation. In all instances, the designated areas for collapse shall be protected.

B5.9.3.5  The Contractor will furnish a cell phone for the Pilot and Mechanic for call back when away from the desiginated base.

B5.9.4  Automatic Flight Following System

B5.9.4.1  The AFF system shall be powered by the aircraft’s electrical system, installed per the manufacturer’s installation manual, and operational in all phases of flight.  AFF equipment shall utilize as a minimum:  Satellite communications, an externally mounted antenna, provide data to the Government’s Webtracker software, use aircraft power via a dedicated circuit breaker for power protection, and be mounted so as to not endanger any occupant from AFF equipment during periods of turbulence.  Any AFF manufacturer required pilot display(s) or control(s) shall be visible/selectable by the pilot(s).  Remote equipment having visual indicators should be mounted in such a manner as to allow visual indicators to be easily visible.

B5.9.4.2  AFF communications shall be fully operational  and provide coverage compatible with operations in Alaska and the lower 48 states and those portions of Canada through which travel may be conducted.  Not all manufacturers’ AFF equipment communication links will operate effectively in all geographic areas.

B5.9.4.3  The contractor shall maintain a subscription service through the AFF equipment provider allowing AFF position reporting for satellite tracking via Webtracker.  The position-reporting interval shall be every two minutes while the aircraft is in flight.  The contractor shall register their AFF equipment with the Boise Help Desk providing:  Complete tail number, manufacturer and serial number of the AFF transceiver; aircraft make and model; and Contractor contact information.  If the Contractor relocates previously registered AFF equipment into another aircraft, then the Contractor shall contact the Boise Help Desk making the appropriate changes prior to aircraft use.  In all cases, the contractor shall ensure that the correct aircraft information is indicated within Webtracker.  The Contractor shall contact the Boise Help Desk of system changes, scheduled maintenance, and planned service outages.

B5.9.4.4  Registration contact information, a web accessible feedback form, and additional information is available at: https://www.aff.gov.  The Boise Help Desk can be reached at (800) 253-5559 or (208) 387-5290.

B5.9.4.5  Prior to the aircraft’s annual Contract inspection, the Contractor shall ensure compliance with all AFF systems requirements.  The Contractor shall additionally perform an operational check of the system.  As a minimum, the operational check shall consist of confirming the aircraft being tested is displayed in Webtracker (indicating it is currently transmitting data to Webtracker) and that all information displayed in Webtracker is current.  A username and password is required to access Webtracker.  Log on to the AFF website at https://www.aff.gov to request a username and password, or contact the Boise help desk.  When the aircraft passes the operational check, an aircraft log book entry shall be made.

B5.9.4.6  This clause incorporates Specification Section Supplement available at:https://www.aff.gov/contractspecs with the same force and effect as if they were presented as full text herein.

B5.10    Drawings:

Exhibit FS/AMD A-17:  wiring diagram for AUX-FM connector.

Exhibit	FS/AMD A-16   ACCESSORY CONNECTOR PIN ASSIGNMENTS

## B6.  Maintenance Requirements

B6.1  General  The Contractor shall insure the aircraft and all required equipment shall be operated and maintained in accordance with the manufacturer’s specifications and applicable FARs.

B6.1.1 Any unscheduled maintenance events during the performance of this contract that affects the airworthiness of the aircraft or impacts the mission requires notification of the COTR or the Alternate COTR by the most expeditious means possible.  The COTR or the Alternate COTR will issue a Return to Availability (AMD 68) upon confirmation the aircraft has been Returned to Service by the appropriate contractor personnel.

B6.1.2  Transportation of required support personnel and supplies to bases of operation shall be provided by the Contractor.  However, Government transportation may be made available on a space available basis.  There is no guarantee as to the availability, frequency, or available space on such flights.

B6.2  Inspection  Aircraft shall be maintained in accordance with the Contractor’s 14 CFR Part 135 certificate.

B6.2.1  All maintenance, including inspection, rebuilding, alteration, and installation shall be accomplished by a person authorized to perform maintenance in accordance with 14 CFR Part 43.

B6.2.2  The Contractor’s maintenance facility shall be capable of providing field maintenance support for each aircraft during extended periods of heavy use.  The Contractor may have arrangements with other appropriately rated facilities to perform maintenance for which the Contractor is not qualified.

B6.2.3 The Contractor shall ensure that a mechanic who meets the contract qualification requirements inspects the contract helicopter in accordance with the procedures outlined in the operator’s FAA approved/accepted maintenance program.  This inspection shall be entered in the aircraft maintenance records in accordance with 14 CFR Part 43.9 and shall include the aircraft time in service.

B6.3  Routine maintenance shall be performed before or after the daily use or as approved by the CO or the COR.

B6.4  Maintenance Test  The Contractor shall, at their own expense, perform a functional maintenance check flight following installation, overhaul, major repair, or replacement of any engine, power train, rotor system, flight control system, or when requested by the CO.  This shall be accomplished before the aircraft resumes service under the contract.

B6.4.1 The Contractor shall immediately notify the COR of any change to any engine, power train, flight control or major airframe component or of any major repair following an incident or accident and shall describe the circumstances involved.

B6.5  Time Between Overhaul (TBO) and Life Limited Parts  All components, including engines, shall be replaced upon reaching the factory recommended TBO or FAA approved extension.  Life limited parts shall be replaced at the specified time in service hours or cycles.  Unless otherwise authorized by the Contracting Officer, time/life limited components, including engines, transmissions, main rotor head components and rotating controls, shall have 270 hours remaining to retirement or overhaul at the start of the first day of availability for each exclusive use period.  This does not include items that can easily be changed overnight (10 hours or less) in the field without resulting in unavailability.

B6.5.1  Aircraft operated with components or accessories on approved TBO extension programs are acceptable provided, (1) the Contractor is the holder of the approved extension authorization (not the owner if the aircraft is leased), and (2) the Contractor operates in accordance with the extension authorization.

B6.5.2  The Contractor shall supply, at the time of the agency inspection, a list of all items installed on the aircraft which are required to be overhauled or replaced on a specified time basis.  This list shall include the components name, part number, serial number, total time, service life (or inspection/overhaul time interval), and time and date when component was overhauled, replaced, or inspected. The format of this list will be similar to that found in AC 43-9C, as revised.

B6.6  Airworthiness Directives (ADs) & Manufacturer’s Mandatory Service Bulletins (MMSBs)  All applicable FAA ADs and required MMSBs shall be complied with prior and during  the performance of this contract.  A list of FAA ADs and required MMSBs on the make and model of the aircraft offered shall be made available.  The list will include items described in 14 CFR 91.417 and signature of persons verifying accuracy of the list.  All ADs and required MMSBs published during the contract shall be complied with.

B6.7  Weight and Balance  The aircraft’s required weight and balance data shall be determined by actual weighing of the aircraft within 24 calendar months preceding the starting date of the contract, or renewal period, and following any major repair or major alteration or change to the equipment list which significantly affects the center of gravity of the aircraft.

B6.7.1  All weighing of aircraft shall be performed on scales that have been certified as accurate within the preceding 24 calendar months.  The certifying agency may be any accredited weights and measures laboratory.

B6.7.2  A list of equipment installed in the aircraft at the time of weighing must be compiled.  The equipment list shall include the name of each item installed.  Items which may be easily removed or installed for aircraft configuration changes (seats, doors, radios, cargo hook, baskets, special mission equipment, survival kit etc.) shall also be listed including the name, the weight and arm of each item.  Each page of the equipment list must identify the specific aircraft by at least serial number or registration number of the aircraft.  Each page of the equipment list shall be dated indicating the last date of weighing or computation. The weight and balance must be revised each time new equipment is installed or old equipment is removed. Weight and balance procedures under 14 CFR 135.23(b) and 135.185 are acceptable.

B6.8  Manuals/Records  The Contractor shall ensure that all maintenance performed on the contact aircraft is recorded in the affected aircraft’s maintenance record in accordance with 14 CFR Parts 43 and 91 (reference 14 CFR Parts 43.9, 43.11 and 91.417 and 135.439).

B6.8.1  The Contractor shall keep with the aircraft a copy of the aircraft's current maintenance record as required by 14 CFR Part 91.417.

B6.8.2  If requested by the Government, a copy of the Contractor’s Procedures Manuals, as outlined in 14 CFR Part 135.21, shall be furnished to the CO or the COR. Along with any revisions made during the contract period.

B6.8.3 Before the start date of the contract, all maintenance deficiencies shall be corrected or deferred in accordance with the operator’s Accepted/Approved Maintenance Program.  Deferred discrepancies will be evaluated and the aircraft approved for contract use on a case-by-case basis. In accordance with the appropriate FAR’s or the Approved Maintenance Program, the Contractor shall correct deficiencies that occur during contract performance.

B6.9   Preventive Maintenance

B6.9.1  The pilot, under the terms of this contract, may perform preventive maintenance in accordance with 14 CFR Part 43.3(h).  All maintenance performed will be recorded in accordance with 14 CFR Part 43.9.

B6.9.2   Routine maintenance shall be performed before or after the daily use or as approved by the CO or the COR.

B6.10  Turbine Engine Power Assurance Checks  ON the first day of operation and no more than each ten hours of operation thereafter, the contractor shall perform a power assurance check in accordance with the helicopter flight manual (pilots operating handbook) or approved company performance monitoring program.  The results shall be recorded and kept with the aircraft.  Engines with power output below minimum approved limits shall be removed from contract use until the cause of the condition is corrected.

## B7.  Servicing Requirements

B7.1  Fuel Requirements.  All aircraft fuel to be used by the aircraft during the contract period shall be supplied by the Government in Alaska.  When dispatched to the conterminous 48 states fuel will be furnished by the vendor.

B7.1.1  Grades of Government-furnished fuel vary from location to location, and the Contractor shall use the grade available.  Jet fuel in one of the following grades, will be available at each location.

Jet Fuel  	Jet A, Jet A-50,Jet B,JP-4,JP-5,JP-8

B7.1.2  All lubricating oil, parts and supplies shall be furnished and transported by the Contractor to the designated base or any alternate bases.

B7.1.3 All fuel, commercial or military, shall be approved for use by the airframe and engine manufacturer.  Aviation fuel must meet American Society for Testing and Material (ASTM) or Military specifications [ASTM D-1655 (Jet A, A-1, or B), Mil T-5624 (JP-4, JP-8, JP-5), ASTM-D-910 or MIL T-910 (Grade 80,100,or 100LL)].

B7.1.4  Contractors obtaining bulk fuel directly from the distributors shall obtain certification that the fuel delivered to the Contractor’s vehicle or storage tanks meets the specifications of paragraph B7.1.3.  Certificates will be kept with the aircraft records until the completion of the contract period or 30 days after the delivery date of the fuel, whichever comes first.

B7.1.5  Fueling operations, including storage and handling, shall comply with the airframe and engine manufacturer’s recommendations and all applicable FAA standards.  The contractor shall have a fuel quality assurance program.  The National Fire Protection Association fuel-handling handbook shall be used as a guide.  Copies of “Aircraft Fuel Servicing: NFPA Manual #407, can be obtained from the National Fire Protection Association, Batterymarch Park, Quincy, MA 02269.  Maintenance and security of fueling facilities is the Contractor’s responsibility.

B7.1.6  If Contractor storage facilities contain more than 1320 gallons total or any one container contains more than 660 gallons, the regulations of the EPA shall apply (40 CFR 112).

B7.1.7  Fuel shall pass through a filtering system in accordance with the filter manufacturer’s recommendations.

B7.2  Helicopters shall not be refueled while engines are running or rotor blades are turning unless the helicopter and refueling facility is equipped with an approved closed-circuit refueling system.

# SECTION C – CONTRACT TERMS AND CONDITIONS

## C1  Contract Terms and Conditions – Commercial Items (52.212-4 SEPT 2005) [Tailored SEPT 2005]

(SEE ADDENDA WHICH FOLLOWS IMMEDIATELY AFTER CLAUSE 52.212-5)

(a) Inspection/Acceptance. The Contractor shall only tender for acceptance those items that conform to the requirements of this contract. The Government reserves the right to inspect or test any supplies or services that have been tendered for acceptance. The Government may require repair or replacement of nonconforming supplies or reperformance of nonconforming services at no increase in contract price. The Government must exercise its post-acceptance rights (1) within a reasonable time after the defect was discovered or should have been discovered; and (2) before any substantial change occurs in the condition of the item, unless the change is due to the defect in the item.

(b) Assignment. The Contractor or its assignee's may assign its rights to receive payment due as a result of performance of this contract to a bank, trust company, or other financing institution, including any Federal lending agency in accordance with the Assignment of Claims Act (31 U.S.C. 3727).  However, when a third party makes payment (e.g., use of the Governmentwide commercial purchase card), the Contractor may not assign its rights to receive payment under this contract.

(c) Changes. Changes in the terms and conditions of this contract may be made only by written agreement of the parties.

(d) Disputes. This contract is subject to the Contract Disputes Act of 1978, as amended (41 U.S.C. 601-613). Failure of the parties to this contract to reach agreement on any request for equitable adjustment, claim, appeal or action arising under or relating to this contract shall be a dispute to be resolved in accordance with the clause at FAR 52.233-1, Disputes, which is incorporated herein by reference. The Contractor shall proceed diligently with performance of this contract, pending final resolution of any dispute arising under the contract.

(e) Definitions. The clause at FAR 52.202-1, Definitions, is incorporated herein by reference.

(f) Excusable delays. The Contractor shall be liable for default unless nonperformance is caused by an occurrence beyond the reasonable control of the Contractor and without its fault or negligence such as, acts of God or the public enemy, acts of the Government in either its sovereign or contractual capacity, fires, floods, epidemics, quarantine restrictions, strikes, unusually severe weather, and delays of common carriers. The Contractor shall notify the CO in writing as soon as it is reasonably possible after the commencement of any excusable delay, setting forth the full particulars in connection therewith, shall remedy such occurrence with all reasonable dispatch, and shall promptly give written notice to the CO of the cessation of such occurrence.

(g) Invoice.

(1) The Contractor shall submit an original invoice and three copies (or electronic invoice, if authorized,) to the address designated in the contract to receive invoices. An invoice must include--

(i) Name and address of the Contractor;

(ii) Invoice date and number;

(iii) Contract number, contract line item number and, if applicable, the order number;

(iv) Description, quantity, unit of measure, unit price and extended price of the items delivered;

(v) Shipping number and date of shipment, including the bill of lading number and weight of shipment if shipped on Government bill of lading;

(vi) Terms of any discount for prompt payment offered;

(vii) Name and address of official to whom payment is to be sent;

(viii) Name, title, and phone number of person to notify in event of defective invoice; and

(ix) Taxpayer Identification Number (TIN).  The Contractor shall include its TIN on the invoice only if required elsewhere in this contract.

(x) Electronic funds transfer (EFT) banking information.

(A)  The Contractor shall include EFT banking information on the invoice only if required elsewhere in this contract

(B) If EFT banking information is not required to be on the invoice, in order for the invoice to be a proper invoice, the Contractor shall have submitted correct EFT banking information in accordance with the applicable solicitation provision, contract clause (e.g., 52.232-33, Payment by Electronic Funds Transfer -Central Contractor Registration, or 52.232-34, Payment by Electronic Funds Transfer-Other Than Central Contractor Registration), or applicable agency procedures

(C)  EFT banking information is not required if the Government waived the requirement to pay by EFT.

(2) Invoices will be handled in accordance with the Prompt Payment Act (31 U.S.C. 3903) and Office of Management and Budget (OMB) prompt payment regulations at 5 CFR part 1315.

(h) Patent indemnity. The Contractor shall indemnify the Government and its officers, employees and agents against liability, including costs, for actual or alleged direct or contributory infringement of, or inducement to infringe, any United States or foreign patent, trademark or copyright, arising out of the performance of this contract, provided the Contractor is reasonably notified of such claims and proceedings.

- Payment. –

- Items accepted. Payment shall be made for items accepted by the Government that have been delivered to the delivery destinations set forth in this contract.

- Prompt Payment. The Government will make payment in accordance with the Prompt Payment Act (31 U.S.C. 3903) and prompt payment regulations at 5 CFR part 1315.

- Electronic funds transfer (EFT). If the Government makes payment by EFT, see 52.212-5(b) for the appropriate EFT clause.

- Discount. In connection with any discount offered for early payment, time shall be computed from the date of the invoice. For the purpose of computing the discount earned, payment shall be considered to have been made on the date which appears on the payment check or the specified payment date if an electronic funds transfer payment is made.

- Overpayments. If the Contractor becomes aware of a duplicate contract financing or invoice payment or that the Government has otherwise overpaid on contract financing or invoice payment, the Contractor shall immediately notify the Contracting Officer and request instructions for disposition of the overpayment.

(j) Risk of loss.  Unless the contract specifically provides otherwise, risk of loss or damage to the supplies provided under this contract shall remain with the Contractor until, and shall pass to the Government upon:

- Delivery of the supplies to a carrier, if transportation is f.o.b. origin; or

- Delivery of the supplies to the Government at the destination specified in the contract, if transportation is f.o.b. destination.

(k) Taxes. The contract price includes all applicable Federal, State, and local taxes and duties.

(l) Termination for the Government's convenience. The Government reserves the right to terminate this contract, or any part hereof, for its sole convenience. In the event of such termination, the Contractor shall immediately stop all work hereunder and shall immediately cause any and all of its suppliers and subcontractors to cease work. Subject to the terms of this contract, the Contractor shall be paid a percentage of the contract price reflecting the percentage of the work performed prior to the notice of termination, plus reasonable charges the Contractor can demonstrate to the satisfaction of the Government using its standard record keeping system, have resulted from the termination. The Contractor shall not be required to comply with the cost accounting standards or contract cost principles for this purpose. This paragraph does not give the Government any right to audit the Contractor's records. The Contractor shall not be paid for any work performed or costs incurred which reasonably could have been avoided.

(m) Termination for cause. The Government may terminate this contract, or any part hereof, for cause in the event of any default by the Contractor, or if the Contractor fails to comply with any contract terms and conditions, or fails to provide the Government, upon request, with adequate assurances of future performance. In the event of termination for cause, the Government shall not be liable to the Contractor for any amount for supplies or services not accepted, and the Contractor shall be liable to the Government for any and all rights and remedies provided by law.  If it is determined that the Government improperly terminated this contract for default, such termination shall be deemed a termination for convenience.

(n) Title.  Unless specified elsewhere in this contract, title to items furnished under this contract shall pass to the Government upon acceptance, regardless of when or where the Government takes physical possession.

(o)  Warranty.  The Contractor warrants and implies that the items delivered hereunder are merchantable and fit for use for the particular purpose described in this contract.

(p) Limitation of liability. Except as otherwise provided by an express warranty, the Contractor will not be liable to the Government for consequential damages resulting from any defect or deficiencies in accepted items.

(q) Other compliances. The Contractor shall comply with all applicable Federal, State and local laws, executive orders, rules and regulations applicable to its performance under this contract.

(r) Compliance with laws unique to Government contracts. The Contractor agrees to comply with 31 U.S.C. 1352 relating to limitations on the use of appropriated funds to influence certain Federal contracts; 18 U.S.C. 431 relating to officials not to benefit; 40 U.S.C 3701, et seq., Contract Work Hours and Safety Standards Act; 41 U.S.C. 51-58, Anti-Kickback Act of 1986; 41 U.S.C. 265 and 10 U.S.C. 2409 relating to whistleblower protections; 49 U.S.C 40118, Fly American; and 41 U.S.C. 423 relating to procurement integrity.

(s) Order of precedence. Any inconsistencies in this

solicitation or contract shall be resolved by giving precedence in the following order: (1) the schedule of supplies/services; (2) the Assignments, Disputes, Payments, Invoice, Other Compliances, and Compliance with Laws Unique to Government Contracts paragraphs of this clause; (3) the clause at 52.212-5; (4) addenda to this solicitation or contract, including any license agreements for computer software; (5) solicitation provisions if this is a solicitation; (6) other paragraphs of this clause; (7) the Standard Form 1449; (8) other documents, exhibits, and attachments; and (9) the specification.

(t) Central Contractor Registration (CCR).

(1) Unless exempted by an addendum to this contract, the Contractor is responsible during performance and through final payment of any contract for the accuracy and completeness of the data within the CCR database, and for any liability resulting from the Government's reliance on inaccurate or incomplete data. To remain registered in the CCR database after the initial registration, the Contractor is required to review and update on an annual basis from the date of initial registration or subsequent updates its information in the CCR database to ensure it is current, accurate and complete. Updating information in the CCR does not alter the terms and conditions of this contract and is not a substitute for a properly executed contractual document.

(2)(i) If a Contractor has legally changed its business name, "doing business as" name, or division name (whichever is shown on the contract), or has transferred the assets used in performing the contract, but has not completed the necessary requirements regarding novation and change-of-name agreements in FAR Subpart 42.12, the Contractor shall provide the responsible Contracting Officer a minimum of one business day's written notification of its intention to (A) change the name in the CCR database; (B) comply with the requirements of Subpart 42.12; and (C) agree in writing to the timeline and procedures specified by the responsible Contracting Officer. The Contractor must provide with the notification sufficient documentation to support the legally changed name.

(ii) If the Contractor fails to comply with the requirements of paragraph (q)(2)(i) of this clause, or fails to perform the agreement at paragraph (q)(2)(i)(C) of this clause, and, in the absence of a properly executed novation or change-of-name agreement, the CCR information that shows the Contractor to be other than the Contractor indicated in the contract will be considered to be incorrect information within the meaning of the "Suspension of Payment" paragraph of the electronic funds transfer (EFT) clause of this contract.

(3) The Contractor shall not change the name or address for EFT payments or manual payments, as appropriate, in the CCR record to reflect an assignee for the purpose of assignment of claims (see Subpart 32.8, Assignment of Claims). Assignees shall be separately registered in the CCR database. Information provided to the Contractor's CCR record that indicates payments, including those made by EFT, to an ultimate recipient other than that Contractor will be considered to be incorrect information within the meaning of the "Suspension of payment" paragraph of the EFT clause of this contract.

(4) Offerors and Contractors may obtain information on registration and annual confirmation requirements via the internet at http://www.ccr.gov or by calling 1-888-227-2423 or 269-961-5757.

## C2  Contract Terms and Conditions Required to Implement Statutes or Executive Orders-Commercial Items (52.212-5 NOV 2006)

(a) The Contractor shall comply with the following Federal Acquisition Regulations (FAR) clauses, which are incorporated in this contract by reference, to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1)   52.233-3, Protest after Award (AUG 1996) (31 U.S.C. 3553).

(2)  52.233-4, Applicable Law for Breach of Contract Claim (OCT 2004) Public L. 108-77, 108-78)

(b) The Contractor shall comply with the FAR clauses in this paragraph (b) that the Contracting Officer has indicated as being incorporated in this contract by reference to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1) 52.203-6, Restrictions on Subcontractor Sales to the Government (SEPT 2006), with Alternate I (SEPT 2006) (41 U.S.C. 253g and 10 U.S.C. 2402).

(2) 52.219-3, Notice of Total HUBZone Small Business Set-Aside (JAN 1999) (15 U.S.C 657a).

(3) 52.219-4, Notice of Price Evaluation Preference for HUBZone Small Business Concerns (JULY 2005) (if the offeror elects to waive the preference, it shall so indicate in its offer) (15 U.S.C. 657a).

(4 [Reserved]

(ii) Alternate I (MAR 1999) of 52.219-5.

(iii) Alternate II (JUNE 2003) of 52.219-5.

(5) 52.219-6, Notice of Total Small Business Set-Aside (JUNE 2003)(15 U.S.C. 644).

(ii) Alternate I (OCT 1995) of 52.219-6.

(iii) Alternate II (MAR 2004) of 52.219-6.

(6)(i) 52.219-7, Notice of Partial Small Business Set-Aside (JUNE 2003)(15 U.S.C. 644).

(ii) Alternate I (OCT 1995) of 52.219-7.

(iii) Alternate II (MAR 2004 of 52.219-7.

(7) 52.219-8, Utilization of Small Business Concerns (MAY 2004)(15 U.S.C. 637 (d)(2) and (3)).

(8)(i) 52.219-9, Small Business Subcontracting Plan (SEPT 2006)(15 U.S.C. 637(d)(4)).

(ii)Alternate I (OCT 2001) of 52.219-9.

(iii) Alternate II (OCT 2001) of 52.219-9.

(9) 52.219-14, Limitations on Subcontracting (DEC 1996) (15 U.S.C. 637(a)(14)).

(10)(i) 52.219-23, Notice of Price Evaluation Adjustment for Small Disadvantaged Business Concerns (SEPT 2005)(10 U.S.C. 2323) (if the offeror elects to waive the adjustment, it shall so indicate in its offer).

(ii) Alternate I (JUNE 2003)of 52.219-23.

(11) 52.219-25, Small Disadvantaged Business Participation Program-Disadvantaged Status and Reporting (OCT 1999)(Pub. L. 103-355, section 7102, and 10 U.S.C. 2323).

(12) 52.219-26, Small Disadvantaged Business Participation Program-Incentive Subcontracting (OCT 2000) (Pub. L. 103-355, section 7102, and 10 U.S.C. 2323).

(13) 52.219-27, Notice of Total Service-Disabled Veteran-Owned Small Business Set-Aside (MAY 2004).

(14) 52.222-3, Convict Labor (JUNE 2003)(E.O. 11755).

(15) 52.222-19, Child Labor-Cooperation with Authorities and Remedies (JAN 2006)(E.O. 13126).

(16) 52.222-21, Prohibition of Segregated Facilities (Feb 1999).

(17) 52.222-26, Equal Opportunity (APR 2002)(E.O. 11246).

(18) 52.222-35, Equal Opportunity for Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212).

(19) 52.222-36, Affirmative Action for Workers with Disabilities (JUN 1998) (29 U.S.C. 793).

(20) 52.222-37, Employment Reports on Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212).

(21)(i) 52.222-39, Notification of Employee Rights Concerning Payment of Union Dues or Fees (DEC 2004)(E.O. 13201).

(22)(i) 52.223-9, Estimate of Percentage of Recovered Material Content for EPA-Designated Products (AUG 2000)(42 U.S.C. 6962(c)(3)(A)(ii)).

(ii) Alternate I (AUG 2000) of 52.223-9 (42 U.S.C. 6962(i)(2)(C)).

(23) 52.225-1, Buy American Act-Supplies (JUNE 2003)(41 U.S.C. 10a - 10d).

(24)(i) 52.225-3, Buy American Act - Free Trade Agreements-Israeli Trade Act (NOV 2006) (41U.S.C. 10a - 10d, 19U.S.C. 3301 note, 19U.S.C. 2112 note, Pub. L. 108-77, 108-78, 108-286,  109-53 and 109-169).

(ii) Alternate I (JAN 2004) of 52.225-3.

(iii) Alternate II (JAN 2004) of 52.225-3.

(25) 52.225-5, Trade Agreements (NOV 2006)(19U.S.C. 2501, et seq., 19 U.S.C. 3301 note).

(26) 52.225-13, Restriction on Certain Foreign Purchases (FEB 2006) (E.o.s, proclamations and statutes administered by the Office of Foreign Assets Control of the Department of the Treasury).

(27)52.226-4, Notice of Disaster or Emergency Area Set-Aside (42 U.S.C. 5150).

(28) [Reserved]

(29) 52.232-29, Terms for Financing of Purchases of Commercial Items (FEB 2002)(41 U.S.C. 255(f), 10 U.S.C. 2307(f)).

(30) 52.232-30, Installment Payments for Commercial Items (OCT 1995)(41 U.S.C. 255(f), 10 U.S.C. 2307(f)).

(31) 52.232-33, Payment by Electronic Funds Transfer-Central Contractor Registration (OCT 2003)(31 U.S.C. 3332).

(32) 52.232-34, Payment by Electronic Funds Transfer-Other than Central Contractor Registration (MAY 1999)(31 U.S.C. 3332).

(33) 52.232-36, Payment by Third Party (MAY 1999)(31 U.S.C. 3332).

(34) 52.239-1, Privacy or Security Safeguards (AUG 1996)(5 U.S.C. 552a).

(35)(i) 52.247-64, Preference for Privately Owned U.S.-Flag Commercial Vessels (FEB 2006)(46 U.S.C. Appx 1241 and 10 U.S.C. 2631).

(ii) Alternate I (APR 2003) of 52.247-64.

(c) The Contractor shall comply with the FAR clauses in this paragraph (c), applicable to commercial services, which the Contracting Officer has indicated as being incorporated in this contract by reference to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1) 52.222-41, Service Contract Act of 1965, as Amended (JULY 2005)(41 U.S.C. 351, et seq.).

(2) 52.222-42, Statement of Equivalent Rates for Federal Hires (MAY 1989)(29 U.S.C. 206 and 41 U.S.C. 351, et seq.).  (See Exhibit)

(3) 52.222-43, Fair Labor Standards Act and Service Contract Act-Price Adjustment (Multiple Year and Option Contracts) (NOV 2006) (29 U.S.C. 206 and 41 U.S.C. 351, et seq.).

(4) 52.222-44, Fair Labor Standards Act and Service Contract Act-Price Adjustment (FEB 2002)(29 U.S.C. 206 and 41 U.S.C. 351, et seq.).

(5) 52.222-47, SCA Minimum Wages and Fringe Benefits Applicable to Successor Contract Pursuant to Predecessor Contractor Collective Bargaining Agreement (CBA) (MAY 1989)(41 U.S.C. 351, et seq.).

(d) Comptroller General Examination of Record. The Contractor shall comply with the provisions of this paragraph (d) if this contract was awarded using other than sealed bid, is in excess of the simplified acquisition threshold, and does not contain the clause at 52.215-2, Audit and Records-Negotiation.

(1) The Comptroller General of the United States, or an authorized representative of the Comptroller General, shall have access to and right to examine any of the Contractor's directly pertinent records involving transactions related to this contract.

(2) The Contractor shall make available at its offices at all reasonable times the records, materials, and other evidence for examination, audit, or reproduction, until 3 years after final payment under this contract or for any shorter period specified in FAR Subpart 4.7, Contractor Records Retention, of the other clauses of this contract. If this contract is completely or partially terminated, the records relating to the work terminated shall be made available for 3 years after any resulting final termination settlement. Records relating to appeals under the disputes clause or to litigation or the settlement of claims arising under or relating to this contract shall be made available until such appeals, litigation, or claims are finally resolved.

(3) As used in this clause, records include books, documents, accounting procedures and practices, and other data, regardless of type and regardless of form. This does not require the Contractor to create or maintain any record that the Contractor does not maintain in the ordinary course of business or pursuant to a provision of law.

(e)(1) Notwithstanding the requirements of the clauses in paragraphs (a), (b), (c) and (d) of this clause, the Contractor is not required to flow down any FAR clause, other than those listed in paragraphs (i) through (vii) of this paragraph in a subcontract for commercial items. Unless otherwise indicated below, the extent of the flow down shall be as required by the clause –

(i) 52.219-8, Utilization of Small Business Concerns (MAY 2004)(15 U.S.C. 637 (d)(2) and (3)), in all subcontracts that offer further subcontracting opportunities. If the subcontract (except subcontracts to small business concerns) exceeds $550,000 ($1,000,000 for construction of any public facility), the subcontractor must include 52.219-8 in lower tier subcontracts that offer subcontracting opportunities.

(ii) 52.222-26, Equal Opportunity (APR 2002)(E.O. 11246);

(iii) 52.222-35, Equal Opportunity for Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212);

(iv) 52.222-36, Affirmative Action for Workers with Disabilities (JUNE 1998)(29 U.S.C. 793);

(v) 52.222-39, Notification of Employees Rights Concerning the Payment of Union Dues or Fees (DEC 2004)(E.O. 13201);

(vi) 52.222-41, Service Contract Act of 1965, As Amended (JULY 2005), flow down required for all subcontracts subject to the Service Contract Act of 1965 (41 U.S.C. 351, et seq.).

(vii) 52.247-64, Preference for Privately Owned U.S.- Flag Commercial Vessels (FEB 2006)(46 U.S.C. Appx 1241 and 10 U.S.C. 2631). Flow down required in accordance with paragraph (d) of FAR clause 52.247-64).

(viii) 52.245.4 Government Furnished Property (Short Form) (June 2003)

(2) While not required, the contractor may include in its subcontracts for commercial items a minimal number of additional clauses necessary to satisfy its contractual obligations.

# ADDENDA TO CONTRACT TERMS AND CONDITIONS

## C3  Inspection/Acceptance (52.212-4(a)), the following is added:

C3.1 Inspection Scheduling and Process

C3.1.1  After either contract award or renewal, the COTR will schedule a date to inspect the Contractor's proposed aircraft, equipment and personnel to ensure contract compliance.  The inspection will be conducted at the designated base, Contractor's facility or other location acceptable to the Government.  The inspection will be scheduled to commence as early as 60 days and not later than three days (excluding weekends and holidays) prior to the established reporting date, unless otherwise mutually agreed upon by the COTR and the Contractor.  The inspection time and date will be scheduled for between 0730 and 1630 local time, Monday through Friday, unless otherwise agreed upon by the COTR.  The COTR will confirm the inspection details in writing.  Contractor written requests for inspection rescheduling that are received by the COTR at least 10 days prior to the originally scheduled inspection date may be accommodated by the COTR, depending upon their work schedule.

C3.1.2 The Contractor must provide information specific to the aircraft, equipment, and personnel being proposed for use during each year of the contract when requested by the COTR.

C3.1.3  Approved aircraft,  pilots and mechanics will be issued an  Aircraft Data Card, Pilot Qualification card and Mechanic Qualification Card, as applicable.  The aircraft and pilot cards detail the activities for which they are authorized.

C3.1.3.1  The aircraft data card is kept in the aircraft and available for inspection at all times.

C3.1.3.2  The pilot qualification card is kept in the possession of the pilot and available for inspection at all times.

C3.1.3.3  The mechanic qualification card is kept in the possession of the mechanic and available for inspection at all times.

C3.1.4  If the COTR determines any aircraft/equipment/personnel and records/documents presented for inspection are not completely ready for the inspection or are determined to be nonconforming as required by the contract, the COTR may suspend the inspection(s) and schedule a reinspection for another time/date/site.  The Contractor may be charged for the cost of reinspection, in accordance with Section C3.5.

C3.2 Equipment

C3.2.1  The aircraft will be inspected to ensure compliance with all contract requirements. The Government may require in-flight dynamic testing of aircraft systems.  This testing may be conducted in conjunction with pilot evaluation flight(s), and  will be performed at no cost to the Government.

C3.3  Personnel

C3.3.1 Key Personnel:

C3.3.1.2  Award of this contract was made in part by the contractor’s offer of specific personnel and or skill levels and experience offered to perform the required services.  Such personnel are considered to be Key Personnel and are essential to the work to be performed.  The contractor hereby agrees to furnish those Key Personnel in the performance of this contract.  Prior to diverting the specified individuals to other projects or programs, the contractor shall notify the Contracting Officer reasonably in advance and shall submit justification (including proposed substitutions) in sufficient detail to permit evaluation of the impact of the program.  No diversion shall be made by the contractor without written consent of the Contracting Officer.

C3.3.1.3 Replacement personnel shall meet or exceed the skill, experience, and knowledge possessed by the key individual the contractor is intending to replace.  A complete resume, equal to the detail provided in the contractor’s original proposal shall be submitted for any proposed substitutions.  The Contracting Officer shall determine acceptability of a replacement.

C3.3.1.4  Key Personnel identified under this contract are as follows: (Names to be inserted at time of award.)

C3.3.2  Pilots.  Only those individuals whose past flight time and experience can be verified from log books, employment records, etc., will be approved for contract use. The Contractor cannot substitute satisfactory completion of any pilot flight evaluation time for any of the total pilot flight hour requirements listed in this contract

C3.3.3  The COTR will conduct a pilot flight evaluation to further verify pilot(s)' ability to perform under this contract, when determined necessary.  The evaluation may include but is not limited to:  weight and balance performance, center of gravity limitations, aircraft performance charts, density altitude considerations, load calculation preparation and actual flying of the aircraft.  Portions of the evaluation may be evaluated orally.  A pilot must also be capable of demonstrating proficient operation of all aircraft equipment identified in Section B during an evaluation flight.

C3.3.3.1  The aircraft used for the evaluation(s) must be the same make, model, and series awarded for this contract and be equipped with dual controls.  Flight evaluation(s) will usually be performed in areas that provide access to terrain similar to that to be flown during the contract period.  Flight evaluations are conducted at the Contractor’s expense.

C3.3.3.2  During the flight evaluation, pilot inspectors retain discretionary authority in determining the competency of the pilot and may add, delete, or revise elements of the flight evaluation to determine competency.  The Government will make the final determination as to the pilot’s ability to successfully meet contract requirements.

C3.3.4  Services provided under this contract require DOI special use flight activities as identified herein.  Pilots must have satisfactorily completed an agency initial and/or periodic flight evaluation(s) for these activities before being approved for use under the contract, unless otherwise indicated in the contract.  The COTR will provide detailed information concerning the types and frequency of special use pilot flight evaluations when requested.

Low-level flight (within 500’ of the surface)

Mountain flying (helicopter)

Resource reconnaissance

External load - short line (50' (helicopter)

External load - longline >50' (helicopter) with remote hook

C3.3.5  Mechanics will be inspected to ensure they meet the contract requirements.  Only those individuals whose past experience can be verified from log books, employment records, etc., will be approved for contract use.

C3.4  Substitute Personnel, Aircraft, or Equipment

C3.4.1   The Contractor may request the use of substitute personnel, aircraft, or equipment that were not initially approved for use.  All proposed substitutes must meet pertinent contract specifications and be subject to inspections and approvals identified herein prior to use.   The Contractor must submit a written request for inspections of substitutes to the COTR seven days prior to the scheduled arrival at the site.  Requests received with fewer than seven days’ notice will be accomplished as permitted by the COTR’s schedule. The Government may charge the Contractor for the cost of any substitute inspections in accordance with Section C3.5

C3.4.2   The Contractor must transport substitute personnel, aircraft, or equipment to the point of use at their expense.

### C3.4.3  The bureau may require substitute pilots to obtain up to three hours each of training or orientation flight time at Contractor's expense.  (This flight time is in addition to any necessary pilot evaluation flight(s)).

C3.5  Re-inspection Expenses

C3.5.1  The Contractor must be liable for all Government incurred re-inspection costs.  Inspection expenses may be deducted from payments due the Contractor.

C3.5.2  Costs may include, but are not limited to, inspector(s)’ time to include travel time at $75.00 per hour, and transportation and subsistence at actual cost.

C3.5.3  Government user time.  Costs will be based upon actual employee time and hourly salary expense.

## C4  Personal Identity Verification of Contractor Personnel (52.204-9 NOV 2006)

(a) The Contractor shall comply with agency personal identity verification procedures identified in the contract that implement Homeland Security Presidential Directive-12 (HSPD-12), Office of Management and Budget (OMB) guidance M-05-24, as amended, and Federal Information Processing Standards Publication (FIPS PUB) Number 201, as amended.

(b) The Contractor shall insert this clause in all subcontracts when the subcontractor is required to have routine physical access to a Federally-controlled facility and/or routine access to a Federally-controlled information system.

C4.1  Contractor Personnel Security Requirements

C4.1.1  It has been determined that Contractor personnel utilized in the support of this contract will not be allowed routine and regular unsupervised access to a Federally controlled facility for more than 180 days, nor will they need unsupervised access to a Federally controlled Level 3 or 4 information system.

C4.1.2  Contractor employees utilized in support of this contract, will be treated as visitors (uncredentialed Contractor) and not be required to receive background investigations and credentialing. However, uncredentialed Contractors may be subject to the screening processes utilized at each Federally controlled facility where the Contractor services are required.  As a minimum, Contractor employees will be issued a temporary/visitor badge and shall display it at all times during contract performance when accessing a Federally controlled facility.  The COR is responsible for ensuring that all Contractor employees are issued a temporary/visitor badge.

## C5  Availability of Funds for the Next Fiscal Year  (52.232-18 APR 1984)

Funds are not presently available for this contract.  The Government’s obligation under this contract is contingent upon the availability of appropriated funds from which payment for contract purposes can be made.  No legal liability on the part of the Government for any payment may arise until funds are made available to the Contracting Officer for this contract and until the Contractor receives notice of such availability, to be confirmed in writing by the Contracting Officer.

## C6  Aircraft Insurance

The Contractor must maintain as a minimum, aircraft insurance coverage required by 14 CFR, Part 205, during contract performance.  See Section C32 Regarding Working on Military Installations)

## C7  Government Furnished Property

C7.1 The Government will retain full ownership and control of all property furnished.  Government furnished property not consumed in performance shall be surrendered upon demand (i.e., during performance, or end of the exclusive use period).

C7.2  The Contractor shall execute receipt of property documents for any property furnished by the Government.  During the term of the contract, certain Government owned equipment may be assigned to the Contractor.  If the equipment is lost, damaged or totally destroyed as a result of the Contractor's negligence; or as a result of any accident, the fair market value of the equipment will be charged to the Contractor and withheld from payments due under this contract.  The value of such equipment will not exceed $10,000.

## C8  Prework Meeting

A prework meeting between the Government and the Contractor along with their primary crew members is typically held at or near the starting designated base and is usually in conjunction with the start of the exclusive use period.  The Contractor’s primary crew members must attend any prework meeting that is scheduled.  The meeting may include, but is not limited to:  (1) review of the contract in detail; (2) operational procedures (dispatch, flight following, hazard/risk assessment and reduction, airspace coordination, incident/accident reporting, etc.; and  (3) review of the local base procedures.

## C9 Authority of Government Representatives

C9.1  Contracting Officer (CO)

The CO is the appointed Government official with authority to enter into, administer and terminate this contract.  No one but the CO is authorized under any circumstances to:

C9.1.1  Award, agree to, or execute any contract, contract modification, or notice of intent.

C9.1.2  Obligate in any way the payment of money by the Government.

C9.1.3  Make a final decision on any contract matter that is subject to the Disputes clause of this contract.

C9.1.4  Terminate, for any cause, the Contractor's right to proceed.

C9.2  Contracting Officer's Technical Representative (COTR)

The COTR is authorized to take any or all actions necessary to ensure compliance with the technical portions of the contract.  The COTR will conduct all requested or required inspections.

The COTR for this contract is:

Mr. Doug Drury

U.S. Department of the Interior

Aviation Management

4405 Lear Court

Anchorage, AK 99502

Phone:  907-271-5021

Fax:      907-271-4788

The DOI – Aviation Management Aviation Safety Manager (ASM) is responsible for all matters concerning accident and incident with potential investigations.  The ASM is:

Mr. Robert Galloway

DOI – Aviation Management

300 E. Mallard Dr., Ste. 200

Boise, ID 83706-3991

Phone:	208-433-5071

Fax:	208-433-5007

C9.3 Contracting Officer's Representative (COR)

The COR is authorized to take any or all actions with respect to administrative functions.

The COR for this contract is:

COR will be designated at the time of award

# ADMINISTRATIVE MATTERS

## C10  Personnel Conduct

C10.1  Replacement of Contractor Personnel

### C10.1.1  Contractor employees required to work or reside on Federal property (National Parks, Refuges, Indian Reservations, etc.) are expected to follow the facility manager’s rules of conduct that apply to both Government or non-Government personnel working or residing at these facilities.  The COR will make available a copy of such rules. The Contractor may be required to replace employees who do not comply with these rules of conduct.

C10.1.2  The Contractor must replace any employee who performs unsafely, ineffectively; refuses to cooperate; is unable or unwilling to adapt to field living conditions; or whose general performance is unsatisfactory, disruptive or detrimental to the purpose for which contracted.

C10.1.3  The CO will notify the Contractor of all known unsatisfactory personnel conduct or unsafe performance.  The employee may be afforded an opportunity for corrective action when the conditions warrant.  When directed by the CO, the Contractor must replace unacceptable personnel not later than 24 hours after such notification, or as otherwise mutually agreed. The decision as to unacceptability  will be at the sole discretion of the CO.

C10.2  Suspension of Pilot

C10.2.1  Upon receipt of written correspondence which indicates a serious safety concern, the Government may suspend the pilot.

C10.2.2  Upon involvement in an Aircraft Accident or National Transportation Safety Board (NTSB) Reportable Incident (see 49 CFR Part 830), a pilot will be suspended from pilot duties and from any other activity authorized under the Interagency Pilot Qualification card(s), pending the investigation outcome.

C10.2.3  Upon involvement in an Incident with Potential as defined under Mishaps, a pilot may be suspended from pilot duties and from any other activity authorized under the Interagency Pilot Qualification card(s), pending the investigation outcome.

C10.2.4  When requested, a suspended pilot must surrender all Interagency Pilot Qualification card(s) to the COTR or other authorized agency representative.  Pilot suspension will continue until the investigation findings and decision indicate no further suspension is required and the Interagency Pilot Qualification card(s) is returned to the pilot;  or revoked by the issuing agency.

## C11  Safety and Accident Prevention

C11.1  The Contractor must submit a copy of all reports required by the Federal Aviation Regulations that relate to pilot and maintenance personnel performance, aircraft airworthiness or operations to the Aviation Safety Manager (ASM).

C11.1.1  Examples of these reports are shown in paragraphs 14 CFR Part 135.415 Mechanical Reliability Reports and Part 135.417 Mechanical Interruption Summary Reports required of the Federal Aviation Regulations, 49 CFR Part 830.5 and 49 CFR 830.15, and FAA Form 8010-4, Malfunction or Defect Report.

C11.2  Following a mishap, the CO will evaluate whether the Contractor was in compliance with contract provisions or with the Federal Aviation Regulations applicable to the Contractor's operations, company policy, procedures, practices, or programs, or whether there was negligence on the part of the company officers or employees that may have caused or contributed to the mishap.  The Contractor must fully cooperate with the CO during this evaluation.

C11.3  The Contractor must develop  and maintain programs necessary to ensure safe practices during ground and flight operations.  These programs are a material part of contract performance.

C11.3.1  Examples of such programs are (1) personnel activities, (2) maintenance, (3) safety, and (4) compliance with regulations.

## C12  Mishaps

C12.1  Mishap Definitions

As used throughout this contract, the following terms will have the meanings set forth below.

C12.1.1  The following terms are as defined in 49 CFR Part 830:

Aircraft Accident

Fatal Injury

Incident.

Operator

Serious Injury

Substantial Damage

C12.1.2  Airspace Conflict.  A near mid-air collision, intrusion, or violation of airspace rules.

C12.1.3  Aviation Hazard.  Any condition, act, or set of circumstances that exposes an individual to unnecessary risk or harm during aviation operations.

C12.1.4  Incident with Potential.  An incident that narrowly misses being an accident and in which the circumstances indicate significant potential for substantial damage or serious injury.  Classification of an incident as an "Incident with Potential" is determined by the agency ASM.

C12.1.5  Maintenance Deficiency.  An equipment defect or failure which affects or could affect the safety of operations, or that causes an interruption to the services being performed.

C12.1.6  SafeCom.  An agency Aviation Safety Communique used to report any condition, observance, act, maintenance problem, or circumstance which has potential to cause an aviation related accident (Form AMD-34 or FS 5700-14).

C12.2  Mishap Reporting

The Contractor must immediately, and by the most  expeditious means available, notify the NTSB AND the agency ASM when an "Aircraft Accident" or NTSB reportable "Incident" occurs.

C12.2.1  The ASM must immediately be notified when an "Incident with Potential" occurs.

C12.2.2  The toll free 24-hour Interagency Aircraft Accident Reporting Hot Line number is:

1-888-4MISHAP (1-888-464-7427)

C12.3  Forms Submission

C12.3.1  Following an "Aircraft Accident" or when requested by the NTSB following notification of a reportable "Incident," the Contractor must provide the agency ASM with information necessary to complete a NTSB Form 6120.1/2 “Pilot/Operator Aircraft Accident Report”.

C12.3.2  The Contractor must submit a "SafeCom" to the agency ASM within 5 days upon the occurrence of any condition, observance, act, maintenance problem, or  circumstance which has potential to cause an aviation-related mishap. Submission via the internet at  http://www.safecom.gov/ is preferred.  Blank SafeComs can be obtained from agency ASMs. The submission of an NTSB Form 6120.1/2 does not replace the Contractor's responsibility to submit a “Safecom”.

C12.4  Pilot Suspension

See Suspension of Pilot clause above.

C12.5  Preservation Requirements

C12.5.1  The Contractor must not permit removal or alteration of the aircraft, aircraft equipment, or records following an Aircraft Accident, Incident, or Incident with Potential until authorized to do so by the CO or other authorized agency representative.  Permitted exceptions to this requirement may be when life or property are threatened, when the aircraft is blocking an airport runway, etc.  The Contractor must immediately notify the CO when taking such actions.

C12.5.2  The NTSB's release of the wreckage does not constitute a release by the CO.

C12.6  Mishap Investigations

C12.6.1  The Contractor must maintain an accurate record of all aircraft accidents, incidents, aviation hazards, and injuries to Contractor or Government personnel arising during this contract.

C12.6.2  Following a mishap, the Contractor must ensure that pilots, mechanics or other personnel associated with the aircraft remain in the vicinity of the mishap until released by the CO or their designated representative.  The Contractor must cooperate with the agency during any investigation and make available personnel and aircraft records, and any equipment, damaged or undamaged, that the agency deems necessary.

C12.7  Costs Related to Investigation

The NTSB or agency will determine their individual agency’s investigation cost responsibility.  The Contractor  will be fully responsible for any cost associated with the reassembly, approval for return-to-service, and return transportation of any items disassembled by the Government.

C12.8  Rescue and Salvage Responsibilities

The Contractor must be responsible for the cost of search, rescue, and salvage operations made necessary due to causes other than negligent acts of a Government employee.

## C13  Federal Airport and Airway Excise Taxes

Chapters 31 and 33 of the Internal Revenue Code, (26 U.S.C. 4041, 4261 et seq )  impose an excise tax on aviation in one of two ways (1) as a fuel tax or (2) as a transportation tax on transportation of passengers and cargo for aircraft having maximum certificated weights in excess of 6,000 pounds.

C13.1  	Fuel Tax.  Fuel tax is applicable, and this contract requires Contractor-furnished fuel. The Contractor is responsible for paying the fuel tax and including such taxes in their bid price.

## C14   Fuel

C14.1 Government Furnished -  The Government will furnish, transport, and store all aircraft fuel required at no expense to the contractor for operations within Alaska and Canada, or reimburse the Contractor for fuel purchases as set forth in Section C14.2, Contractor Furnished Fuel.

C14.1.2  Government furnished fuel used by the Contractor for maintenance flights, repositioning aircraft, crew transportation, or any other flight for the convenience of the Contractor, will be deducted from amounts due the Contractor.   Deductions will be at the current cost of fuel either provided by the Government or reimbursed to the contractor by the Government.  (See Exhibits for fuel consumption rates.)

C14.2 Contractor-Furnished Fuel & Lubricants

C14.2  Fuel.  The cost of fuel furnished by the Contractor in lieu of Government-furnished fuel will be reimbursed to the Contractor as provided below:

C14.2.1  General.  The Contractor shall not charge any fuel acquired under this contract directly to the Government.  All fuel not otherwise furnished by the Government must be paid by or charged to the Contractor.  The purchase shall be approved by the Contracting Officer's Administrative Representative.  Fuel-related costs shall be recorded as a line entry (i.e. dates, fuel charge, dollar amount, and use Pay Item Code "FC"),  shall be summarized under "Other Charges/Credits" on the Aircraft Use Report (AMD-23), AND shall be supported by paid legible, itemized invoices from the supplier.  Certified true copies may be submitted in lieu of the original invoice.

# CONTRACT PERIOD AND RENEWAL

## C15  Contract Period

The contract period will be one year from date of award..

## C16  Option to Extend the Term of the Contract (48 CFR 52.217-9, Mar 2000)

(a)  The Government may extend the term of this contract by written notice to the Contractor at least 30 days prior to expiration of the contract.

(b)  If the Government exercises this option, the extended contract shall be considered to include this option clause.

(d)  The total duration of this contract, including the exercise of any options under this clause, shall not exceed        48 months.

## C17  Reserved

## C18  Exclusive Use Period

C18.1  The exclusive use period is 90 calendar days.  The CO must authorize by modification any use outside the exclusive use period and any extension thereof. The exclusive use period will start on either (1) the date stipulated in Section A; (2) the effective date established by a Notice to Proceed issued by the CO or COR 10 days in advance of the start date  (the effective date established by a Notice to Proceed will not commence more than 14 days prior to nor 14 days after the date stipulated in Section A.); or (3) the date determined according to the following paragraph.

C18.2  The exclusive use period start date is based on the assumption that the Contractor will receive notification of contract award at least 30 days before the exclusive use period begins.  If notice of award is not received at least 30 days in advance of the start date, the exclusive use period will start when service begins or 30 calendar days after notice of award is received, whichever occurs first.

C18.3  The Government will not consider any contract aircraft to be under its operational control when the Contractor is not available or capable of providing Government scheduled services.

## C19   Mutual Extension of Exclusive Use Period

Upon mutual agreement by the parties, the CO will modify the contract to extend the exclusive use period on a day-to-day basis, either prior to the established starting date or subsequent to the ending date. The contract terms, conditions, specifications and prices will apply to such extension; however, in accordance with the Federal Travel Regulations (FTRs), the Government will pay subsistence daily for each authorized crew member while operating at the designated or an alternate base.

# AVAILABILITY REQUIREMENTS

## C20  Availability Requirements

During the exclusive use period and any extension, the Contractor must be in compliance with all contract requirements and available and capable of providing service up to 14 hours each day, as scheduled by the Government.    Pre- and post-flight activities must be accomplished within the 14- hour duty day.  Routine maintenance must be performed before or after the scheduled 14-hour period, or as permitted elsewhere in the contract.

## C21  Schedule of Operations and Reaction Time

The Government will schedule daily operations with the pilot.  The Contractor's personnel must provide service, as directed by the Government, in one of the following categories:

C21.1  Standby.  Personnel must be on standby each day as scheduled and must be ready for takeoff/dispatch within 15 minutes (or longer as authorized by the Government; e.g. flight planning purposes for long range dispatch) after the Government attempts to contact the Contractor's representative.

C21.2  Alert.  After standby Contractor personnel may be authorized to leave the immediate vicinity of the work site, but remain in an on call status subject to call back.  When authorized to leave, they must maintain communications acceptable to the Government and must be ready for takeoff/dispatch within 60 minutes (or longer, if authorized by the Government) after the Government attempts to contact the Contractor's representative.  Failure to return to service as required will result in loss of availability status and extended standby, as applicable.

C21.3  Release From Duty. Contractor personnel may be released and considered to be off duty prior to lapse of their individual crew duty limitation period.  Once released, they cannot be required to return to duty status that day and service will be recorded as fully available status, provided the COR has approved in advance release of the Contractor's personnel.

## C22   Maintenance During Availability Period

C22.1  The COR may approve Contractor requests to remove the aircraft from service to permit the Contractor to perform scheduled or unscheduled maintenance.  The Government will continue to measure and pay for service availability throughout periods approved for maintenance.  The COR may require the Contractor to resume service within 60 minutes or any other agreed upon time period.  Failure to do so would result in unavailability status.

C22.2    If the aircraft is not scheduled for service or service is unavailable, the aircraft may be removed from the operating base for maintenance, provided the Contractor:  (1) Obtains the schedule of operations from the COR, (2) returns the aircraft to service before the beginning of the next availability period, AND (3) uses the aircraft for maintenance test flights, or flight to and from maintenance facilities, only.

## C23  Unavailability and Damages

C23.1  The Contractor will be considered to be unavailable when they are not in compliance with all contract requirements or are not capable of providing service as scheduled by the Government.   Unavailability status will continue until the Contractor has notified the COR that they are available.

C23.2  During periods of Contractor unavailability, the Government may obtain replacement services elsewhere and charge the Contractor for any resulting excess costs.  The Contractor may be liable for any additional actual damages to the Government resulting from such failure to perform.

# MEASUREMENT AND PAYMENT

## C24  Daily Availability

C24.1 Availability is measured in full days for the daily period of time (maximum of 14 hours) scheduled by the Government and provided by the Contractor.  Availability will be paid as actual services are provided and paid at the rate and number of days set forth in Section A.  Payment will be reduced for each hour, or portion thereof, in accordance with the Unavailability Conversion Chart Exhibit, when services are unavailable or when the aircraft has been released for the Contractor’s benefit.

C24.2  Unavailability.  Payment for daily availability shall be made at the bid price set forth in Section A and as measured above except that availability for the aircraft, and equipment will be reduced for each hour or portion thereof if service is listed as unavailable as shown below.

SINGLE CREW:  1/10 per hour not to exceed 10/10 per day

DOUBLE CREW:  1/20 per hour not to exceed 20/20 per day

C24.3  Availability will be measured for payment on the crew’s mandatory days off.

## C25  Flight Time

C25.1  Measurement of Flight Time.  Flight time will be measured from lift-off to touchdown in hours and tenths.  Flight time will be measured by means of an approved electrical time recorder, as required in Section B.

C25.2  Payment for Flight Time.  The Government will pay for all flights ordered by the CO and flown by the Contractor at the rates set forth in Section A. The Government does not guarantee any minimum or maximum number of flight hours during this contract.

C25.3  Flights Associated with Inspections.  Flight time associated with the DOI – Aviation Management (agency) inspection  will be at the expense of the Contractor and will not be measured for payment.

C25.4  Flights for Contractor's Benefit.  The Government will not pay for flights benefiting the Contractor, such as flights for maintenance testing, for ferrying to and from maintenance facilities, flights required following an engine change, commercial charters, and flights solely for transporting Contractor's personnel.

## C26  Mobilization/Demobilization

C26.1  The Contractor is be responsible for all mobilization and demobilization costs to and from the designated base(s) stipulated in Section A.  The Government may, at its discretion, release the Contractor from other than the base stipulated in Section A.  The contract price will be adjusted as described below whenever the distance from the point of release to the Contractor's home base is greater than or less than the distance between the Contractor's home base and the designated base stipulated in Section A.

C26.2  Flight distance will be measured using the most direct route taken from low level en route aeronautical charts.  The net distance will be converted into hours of flight using the most economical cruise speed of the aircraft.  The adjustment will be determined by multiplying the difference in distance (hours of flight) by the flight rate stipulated in Section A.

C26.3 Distances that are greater than home base to the base stipulated in the Section A will result in a payment to the Contractor.  Distances that are less than home base to the base stipulated in Section A will result in a decrease to the Contractor.

## C27  Additional Pay Items (from Schedule of Items)

Claims for additional pay items addressed herein must be documented on the invoice for payment and supported by invoice(s) and/or document(s), as required below.  The Government will not pay claims submitted with incomplete or missing supporting documentation.

C27.1  Subsistence Allowance.  Each authorized crewmember may claim a subsistence allowance (lodging and meals) for each overnight stay, including mandatory days off, when assigned to a base away from the designated base.

C27.1.1  The Government, at its option, may provide meals and/or lodging (which may be remote field or fire camp accommodations).  If not Government provided, the Contractor will be paid an overnight allowance equal to the standard Federal Travel Regulation (FTR) rate (or high rate, if applicable).  The Contractor may claim overnight expenses using either of the two following methods:

C27.1.1.1  Payment of the Standard or High Rate, if applicable) lodging and M&IE rate EXCLUDING lodging tax (does not require lodging receipts to be submitted with the invoice) or;

C27.1.1.2  Payment of actual lodging amount and M&IE rate not to exceed that authorized in accordance with the FTR plus lodging tax. An itemized lodging invoice detailing lodging cost and tax must be submitted with the invoice.

(a)  The  lodging and payment invoices must clearly show the county or city where the overnight stay occurred.  High rate claims for subsistence that do not include this information will be reduced to the standard rate.

C27.1.2  If the Contractor does not use Government provided meals and/or lodging, the Government will not pay for contractor costs incurred for travel to alternate meal or lodging locations.

C27.1.3  Unless the Government makes three meals available to the Contractor's employees, the appropriate total rate for meals and incidental expenses will be paid.

C27.1.4  If partial subsistence, either three meals or lodging, is provided by the Government, the Contractor will be paid at current FTR rates for the portion that is Contractor provided.  Lodging will be handled as stated above.  Current rates established by the FTR are:

STANDARD

Meals and Incidental Expense: $39.00

Lodging: $60.00

Total:  $99.00

HIGH RATE

For current FTR per diem rates see Internet site http://www.gsa.gov and select - Per Diem Rates, Domestic.

C27.2 Transportation Costs Associated with Operating Away From the Designated Base.  When operating from an alternate base, the Contractor is required to provide for transporting additional personnel, unless otherwise directed by the Government.  Prior to the exchange, the Contractor must advise the COR of the anticipated costs. The Contractor will be paid actual necessary and reasonable costs for transporting personnel and required equipment listed below.

Maintenance personnel and equipment required to accomplish scheduled maintenance, i.e. 50 and 100 hour inspections.

C27.4.1  The Contractor must complete and submit the Transportation Worksheet Exhibit, attach supporting invoices identified above to the invoice for payment, and enter the total dollar amount as a line entry on the invoice for payment (SC pay item code).  Claims that do not include these items or other documents necessary to verify incurred costs will be returned to the Contractor for proper completion.

C27.2.2  Unless approved in advance by the CO, payment for crew member exchanges is limited to one round trip for two crew members once every 12 days.  Additional payment may be appropriate for circumstances such as crew members’ reaching flight or duty time limits or agency imposed temporary flight or duty restrictions  as specified in Section B.

C27.2.3  Examples of acceptable expenses are airline tickets; car rentals; privately owned vehicle (POV) at the government mileage rate (currently 48.5 cents) (Internet site http://www.gsa.gov ) and charter airplane showing aircraft make/model, flight time, hourly rate and departure and destination locations.  Unless authorized in advance by the COR, the expense for charter resources must not exceed reasonable costs by common carrier.  The Government will not reimburse the Contractor for salary and subsistence costs for Contractor personnel in travel status.

C27.5 Miscellaneous Contractor Costs.  Miscellaneous unforeseeable costs that cannot be recovered through the contract payment rates and that are the direct result of ordered services away from the designated base may be paid at actual costs, when authorized in advance by the COR.   Examples of such items are airport use costs (tie-downs) and truck permits at ports-of-entry.  The Contractor must support any cost exceeding $75.00 with an itemized, paid invoice.

C27.6 Landing Fees at Designated Base.  The Government will pay the Contractor for all landing fees the Contractor is required to pay.  The Contractor must support any cost exceeding $75.00 with an itemized, paid invoice.

## C28  Government Miscellaneous Charges

The Government will deduct payment for miscellaneous charges for goods or services furnished to the Contractor.

# BILLING AND REPORTING REQUIREMENTS

## C29  Billing Office

The contracting office shown on SF 1449 is the designated billing office for submission of invoices, unless the COR directs that a local office will become the designated billing office.

## C30  Invoice Submissions

The Contractor may submit invoices every two weeks starting the first day services begin.  Services provided must be shown on a daily basis.

## C31  Aircraft Use Report

The Contractor, or Contractor's representative, and the Government must complete and sign an Aircraft Use Report, AMD-23 form.  Instructions for proper completion of the Aircraft Use Report are contained in the AMD-23 booklet.  The Contractor may use the completed and signed Aircraft Use Reports as their invoice.

# C32  Department Of Defense Approval To Utilize Military Airfields Within The State Of Alaska.

C32.1  Aircraft Landing Permits

Performance under this contract may require that the Contractor use military airfields within the State of Alaska as either reporting and/or operating base.  As a condition of this use, the contractor must comply with the following requirements imposed by the Department of Defense.  The following forms must be completed and submitted to the Contracting Officer:

a.  Civil Aircraft Landing Permit, DD Form 2401

b.  Civil Aircraft Certificate of Insurance, DD Form 2400

c.  Civil Aircraft Hold Harmless Agreement, DD Form 2402

C32.1.2  Civil Aircraft Landing Permit, DD Form 2401, and Civil Aircraft Hold Harmless Agreement, DD Form 2402.  The contractor must submit these forms within ten calendar days after receipt of contract award, to the Contracting Officer.

C32.1.3  Civil Aircraft Certificate of Insurance, DD Form 2400.  Contractor shall be required to submit a DD Form 2400, Civil Aircraft Certificate of Insurance within ten calendar days after receipt of contract award or the award of a subsequent option period.  The minimum limits required to be carried during the performance of this contract are specified below.

| TABLE 15-1 ARMY REGULATION 95-2 Minimum aircraft liability coverage requirements for privately owned business or commercial aircraft (including passengers) |
| --- |
| RULE NO. | IF THE MGTOW IS | THEN FOR | THE MINIMUM FOR BODILY INJURY IS | THE MINIMUM FOR PROPERTY DAMAGE IS | THE MINIMUM LIABILITY FOR PASSENGERS IS |
| 1 | 12,500 LBS. AND UNDER | EACH PERSON EACH ACCIDENT | $100,000 $200,000 | $100,000 | $100,000 $100,000 X NUMBER OF PASSENGER SEATS |
| 2 | OVER 12,500 POUNDS | EACH PERSON EACH ACCIDENT | $100,000 $1,000,000 | $1,000,000 | $100,000 $100,000 X 75% X NUMBER OF PASSENGER SEATS |

# C33.  Contractor Responsibilities — Conduct of Business on a Military Installation.

Performance under this contract may involve basing aircraft, support equipment and personnel on military installations.  The Department of the Interior, Bureau of Land Management, Alaska Fire Service has Support Agreements covering the use of the grounds and facilities.  The Contractor agrees to cooperate in the adherence to the terms of said agreements as a condition of performing under this contract.

C33.1 Rules of Conduct and Regulations

The Contractor and its employees are expected to adhere to the rules of conduct and regulations prescribed by the military installation Commander applicable to civilians entering or doing business with the Government on military installations.  The contractor and its employees shall be required to maintain automobile insurance on company and personal owned vehicles that are used on the military installation.

C33.1.1   The minimum vehicle insurance levels are those prescribed by the State of Alaska.  A certificate of insurance is required for entry to Ft. Wainwright.  Vehicle operators shall be prepared to show proof of insurance upon request of the Military or BLM personnel.

C33.1.2  Contractor shall submit the vehicle identification number (VIN) for all restricted Bureau of Land Management retardant ramp site vehicles to the Contracting Officer 10 days prior to award or when such vehicles are presented to the site.  The Government will reserve the right to require insurance on the restricted ramp site vehicles.

C33.1.3  The Government will issue Fort Wainwright base vehicle passes.  Passes are available at the Ft. Wainwright front gate and/or  Army Vehicle Registration Office.  A driver’s license, current registration, and auto insurance must be presented to the Provost Marshal’s Office to obtain the pass.

C33.2  Government Identification Cards – Contractor Employees

C33.2.1  Contractor employees, who are assigned to operate in and out of Ft. Wainwright, Alaska may be issued an U.S. Government Identification Card.  The Bureau of Land Management, Alaska Fire Service, will issue this card.  The card will be clearly marked as “Contractor Employee” and include the name of the contractor they are employed by.  This Identification Card is the property of the U.S. Government.

C33.2.2  Identification cards shall be returned to the COR upon request at any time.  Cards shall also be returned to the COR upon the employee’s release either at the end of each exclusive use period or upon permanent dispatch to an alternate base.

C33.2.3  The Government may withhold final payment to the contractor until such time as all cards have been turned in.

C33.2.4  Contractor Employee Background Investigation.  Contractor employees, who are assigned to operate in and out of Ft. Wainwright, Alaska may be subject to a background investigation by the Government.  This background investigation shall be at the expense of the Government.  At the request of the Contracting Officer, the Contractor shall submit information on each employee to facilitate this investigation.  Failure to provide such information or upon receipt of an unsatisfactory background check, the employee shall be denied access to Ft. Wainwright or other Federal Installations.  The contractor agrees to replace employees who refuse to provide information, or those who, in the Government’s opinion result in an unsatisfactory background check.

C33.3  Weapons.

All weapons in the aircraft survival kit shall be registered with the Ft Wainwright Provost Marshal.

C33.4  Use of support/staging and storage space at Ft. Wainwright, Alaska. (If required & authorized)

C33.4.1  The Government will assign the Contractor a limited amount of space on or adjacent to the aircraft/fire suppressant material ramp for supporting its aircraft.  The space is limited and will be apportioned (by the COR) based upon the number of aircraft furnished by the Contractor, as well as the total space available for this purpose.  Only serviceable spare parts and support equipment will be permitted to be stored in this area.  The Contractor will be required to keep their designated area clean and orderly.  All items must be properly stored and/or disposed.  The use of this space is limited to the direct support of the contract aircraft.  No other use is permitted.

C33.4.2  The Contractor shall be required to comply with all State, Federal and local Environmental Protection (EPA) laws and regulations as well as those prescribed by the military installation Commander in the handling, storage, transportation, utilization and disposal of hazardous materials and waste such as oil solvents, etc.  At the time of space assignment, the Contractor shall designate an individual responsible for hazardous waste management.

C33.4.3  Occupancy of the space shall be limited to a period not to exceed 5 calendar days prior to and after the exclusive use period stated in the schedule or as established in the Notice to Proceed.  Storage of a limited number of items outside this time period (i.e., winter period between contract options) shall only be permitted with the written permission of the COR.  In the event that the Government does not exercise an option to renew, all items must be removed within 5 calendar days notice, or as otherwise agreed upon.  At the end of the contract term, including all options all Contractor equipment, supplies, automobiles, and aircraft must be removed within 5 calendar days after the end of the exclusive use period.

C33.4.4  All usage of the assigned area is subject to the approval of the COR.

C33.4.5  The Government assumes no responsibility/liability for loss of or damage to the Contractor's equipment stored at the site.

C33.5  Contract Retainage.

The Government reserves the right to withhold interim or final payments under this contract pending compliance with the provisions contained in this section.

# C34 EXHIBITS

The following exhibits are attached and made part of this solicitation:

Section B Exhibits

1.- Unacceptable Lap Belt and Shoulder Harness Conditions

2.- Acceptable Paint Schemes

3- First Aid Kit --Survival Kit

4- Drawing FS/AMD 17 Auxilliary FM Ratio Interface

5- Helicopter Makes and Models

6-Interagency Load Calculation Method & Form

7.-Helicopter Fuel Consumption and Weight Reduction                 Chart

Section C Exhibits

8-Statement of Equivalent Rates for Federal Hires

9-Department of Labor Wage Determination Information

10-Unavailability Conversion Chart

11-Transportation Worksheet

EXHIBIT 1

## Unacceptable Lap Belt and Shoulder Harness Conditions

| 1. a. b. c. d. e. f. 2. a. b. c. d. e. 3. a. b. c. 4. a. b. 5. | Webbing Frayed: 5 percent or more Torn Crushed Swelling: twice the thickness of original web, or if difficult to operate through hardware Creased: no structural damage allowed Sun deterioration: severe fading, brittleness, discoloration, and stiffness Hardware Inoperable buckle or other hardware Nylon bushing at shoulder harness-to-lap belt connection missing or damage Fabricated bushings or tie wraps used as bushings Rust/corrosion: only minor surface rust/corrosion allowed Wear: wear beyond normal use Stitches Broken or missing Severe fading or discoloring Inconsistent pattern Technical Service Order (TSO) Tags (see FAR 21.607) Missing Illegible Age Belts/fabric over 10 years from date of manufacture will be closely inspected for possible damage from exposure to the elements, but do not have to be replaced if they can be determined to be in serviceable condition. |
| --- | --- |

EXHIBIT 2

## Acceptable Paint Schemes

- Starting at the blade tip, paint the first 1/6 of the blade length with gloss white.  Paint the second 1/6 of the blade length with yellow or orange.  Paint the third 1/6 of the blade length with gloss white.  Paint the next 1/3 of the blade length with yellow or orange.  Paint the remaining 1/6 of the blade length with gloss white.

| W | Y | W | Y | W | HUB | W | Y | W | Y | W |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1/6 | 1/6 | 1/6 | 1/3 | 1/6 |  | 1/6 | 1/3 | 1/6 | 1/6 | 1/6 |

- One black and one white blade (two-bladed rotor systems).

- Paint schemes previously approved under a U.S. Forest Service or DOI Aviation Management contract.

- High visibility paint schemes and color variations specified by manufacturer in a service bulletin, instruction, or other manufacturer-published document or text.

EXHIBIT 3

## First Aid & Survival Kits

These are minimum required items for Special Use Activities in the United Sates and U.S. Possessions.

Additional survival kit items are required for flight activities conducted in Canada and Alaska.

Minimum First Aid Kit Items Each kit must be in a dust-proof and moisture-proof container. The kit must be readily accessible to the pilot and passengers. Passenger Seats Passenger Seats Item 0-9 10-50 Adhesive bandage strips, (3"long) 8 16 Antiseptic or alcohol wipes (pkts) 10 20 Bandage compresses, 4" 2 4 Triangular bandage, 40" (sling) 2 4 Roller bandage, 4"x 5 yds (gauze) 2 4 Adhesive tape, 1"x 5 yds (std roll) 1 2 Bandage scissors 1 1 Body Fluids Barrier kit: 1 1 2 - pair latex gloves 1 - face shield 1 - mouth-to-mouth barrier 1 - protective gown 2 - antiseptic towelettes 1 - biohazard disposable bag NOTE: Splints are recommended if space permits.

MINIMUM AIRCRAFT SURVIVAL KIT ITEMS

These are minimum required items for special use activities in the conterminous United States (including Alaska) and U.S. possessions.

Fire starter (can be two boxes of matches in a waterproof container)                          Magnesium fire starter

One knife	                                    Signal Mirror

Signal flares (six each)	                                    Food (two days emergency rations per occupant)

Candles	                                    Water purification tablets

Collapsible water bag	                                    Whistle

Space blanket (one per occupant)	                                     Nylon rope or parachute cord (50 feet)

These are additional items for the contiguous U.S. and U.S. Possessions:

Water (one quart per occupant required when operating over areas without adequate drinking water)

These are additional items for Alaska only:

Rations for each occupant sufficient to sustain life for one week.

One axe or hatchet

One first aid kit

One mosquito headnet for each occupant

Insect repellant

An assortment of tackle such as hooks, flies, lines, sinkers, etc.

October 15 to April 1

One pair of snowshoes

One sleeping bag

One wool blanket or equivalent for each occupant over four years of age.

Note: Operators of multiengine aircraft licensed to carry more than 15 passengers need carry only the food, mosquito nets, and signaling equipment at all times other than the period from October 15 to April 1 of each year, when two sleeping bags and one blanket for every two passengers shall also be carried.  All of the above emergency rations and equipment requirements are the minimum requirements under current law.

EXHIBIT 4

## Auxiliary FM Radio Interface

EXHIBIT 5

## Helicopter Like Makes and Models

| For Exclusive Use Contracts |
| --- |
| Make | Model |
| Bell | 47 series (all Recips) |
| Bell | 47 series Soloy |
| Bell | 206A, 206B, series |
| Bell | 206L series |
| Bell | 212, 412, |
| MD | 369 (500) series |
| MD | 520N, 600 |
| MD | MD-900, 902 |
| Enstrom | 28, 280 series |
| Eurocopter | SA 315, SA 316, SA 319 |
| Eurocopter | AS 350/355 series |
| Hiller | 12 series (Recips) |
| Hiller | 12 series (Soloy) |
| Schweizer | 269, 300 series (Recips) |

This list does not specifically follow the FAA guidelines as it relates to 14 CFR 135.293 competency.

Similar military aircraft are not acceptable for grouping.

Grouping of like makes and models of aircraft allows determination of pilot authority.  Differences training must be completed for each of the makes/models in a grouping.  Make/model qualification and currency are met with time flown in any aircraft in grouping.

EXHIBIT 6

## Standard Interagency Load Calculation Method and Form

| INTERAGENCY HELICOPTER LOAD CALCULATION OAS-67/FS 5700 (11/03) | MODEL |
| --- | --- |
|  | N# |
| PILOT(S) |  | DATE |
| MISSION |  | TIME |
| 1 DEPARTURE PA OAT |  |
| 2 DESTINATION PA OAT |
| 3 HELICOPTER EQUIPPED WEIGHT |  |
| 4 FLIGHT CREW WEIGHT |  |
| 5 FUEL WT (_______gallons X _______ lb per gal) |  |
| 6 OPERATING WEIGHT (3 + 4 + 5) |  |
|  | Non-Jettisonable | Jettisonable |
|  | HIGE | HOGE | HOGE-J |
| 7a PERFORMANCE REF (List page/chart from FM) |  |  |  |
| 7b COMP GROSS WT (FM performance section) |  |  |  |
| 8 WT REDUCTION (Req for all non-jettisonable) |  |  |  |
| 9 ADJUSTED WEIGHT (7b minus 8) |  |  |  |
| 10 GROSS WT LIMIT (FM limitations section) |  |  |  |
| 11 SELECTED WEIGHT (Lowest of 9 or 10) |  |  |  |
| 12 OPERATING WEIGHT (From line 6) |  |  |  |
| 13 ALLOWABLE PAYLOAD (11 minus 12) |  |  |  |
| 14 PASSENGERS/CARGO MANIFEST |  |
| 15 ACTUAL PAYLOAD (Total of all weights listed in Item 14) Line 15 must not exceed line 13 for the intended mission. |  |
| PILOT SIGNATURE |  |
| MGR SIGNATURE | Hazmat Yes ___ No ___ |

EXHIBIT 6a

Interagency Helicopter Load Calculation Instructions

A load calculation must be completed for all flights.  A new calculation is required when operating conditions change (±1,000' in elevation or ±5 oC in temperature) or when the helicopter operating weight changes (such as changes to the equipped weight, changes in flight crew weight, or a change in fuel load).

All blocks must be completed.  Pilot must complete all header information and items 1-13.  Helicopter manager completes items 14 and 15.

1.  Departure.  Name of departure location and current pressure altitude (PA, read altimeter when set to 29.92) and outside air temperature (OAT, in Celsius) at departure location.

2.  Destination.  Name of destination location and PA and OAT at destination.  If destination conditions are unknown, use MSL elevation from a map and standard lapse rate of 2 oC/1,000' to estimate OAT.

Check the box in line 1 (departure) or line 2 (destination) to indicate the most restrictive values used to obtain computed gross weight in line 7b.

3.  Helicopter equipped weight.  Equipped weight equals the empty weight (as listed in the weight and balance data) plus the weight of lubricants and onboard equipment required by contract (i.e., survival kit, rappel bracket).

4.  Flight crew weight.  Weight of the pilot and any other assigned flight crewmembers on board (i.e., copilot, flight engineer, navigator) plus the weight of their personal gear.

5.  Fuel weight.  Number of gallons on board X the weight per gallon (jet fuel = 7.0 lb/gal; AvGas = 6.0 lb/gal).

6.  Operating weight.  Add items 3, 4 and 5.

7a.  Performance references.  List the specific flight manual supplement and hover performance charts used to derive computed gross weight for line 7b.  Separate charts may be required to derive HIGE, HOGE, and HOGE-J.  HIGE:  Use hover-in-ground-effect, external/cargo hook chart (if available).  HOGE and HOGE-J:  Use hover-out-ground-effect charts for all HOGE operations.

7b.  Computed gross weight  Compute gross weights for HIGE, HOGE, and HOGE-J from appropriate flight manual hover performance charts using the pressure altitude (PA) and temperature (OAT) from the most restrictive location, either departure or destination.  Check the box in line 1 (departure) or line 2 (destination) to indicate which values were used to obtain computed gross weight.

8.  Weight reduction.  The Government weight reduction is required for all “non-jettisonable” loads.  The weight reduction is optional (mutual agreement between pilot and helicopter manager) when carrying jettisonable loads (HOGE-J) where the pilot has total jettison control.  The appropriate weight reduction value, for make and model, can be found in the current helicopter procurement document (contract).

9.  Adjusted weight.  Line 7b minus line 8.

10.  Gross weight limitation.  Enter applicable gross weight limit from limitations section of the basic flight manual or the appropriate flight manual supplement.  This may be maximum gross weight limit for takeoff and landing, a weight/altitude/temperature (WAT) limitation or a maximum gross weight limit for external load (jettisonable).  Limitations may vary for HIGE, HOGE, and HOGE-J.

11.  Selected weight.  The lowest weight, either line 9 or 10, will be entered for all loads.  Applicable limitations in the flight manual must not be exceeded.

12.  Operating weight.  Use the value entered in line 6.

13.  Allowable payload.  Line 11 minus line 12.  The maximum allowable weight (passengers and/or cargo) that can be carried for the mission.  Allowable payload may differ for HIGE, HOGE, and HOGE-J.

14.  Passengers and/or cargo.  Enter passenger names and weights and/or type and weights of cargo to be transported.  Include mission accessories, tools, gear, baggage, etc.  A separate manifest may be used.

15.  Actual payload.  Total of all weights listed in item 14.  Actual payload must not exceed allowable payload for the intended mission profile; i.e., HIGE, HOGE, or HOGE-J.

Both pilot and helicopter manager must review and sign the form.  Check if hazmat is being transported.  Manager must inform the pilot of type, quantity, and location of hazmat on board.

EXHIBIT 7

## Helicopter Fuel Consumption and Weight Reduction Chart

|  | Fuel Consumption | Load Calculation |
| --- | --- | --- |
|  | Gallon/Hour | Weight Reduction-Lb |
| EUROCOPTER AS-330J | 179 | NOT ESTABLISHED |
| AS-332L-1 | 160 | NOT ESTABLISHED |
| AS-350B | 45 | 130 |
| AS-350B-1 | 46 | 160 |
| AS-350B-2 | 48 | 160 |
| AS-350B-3 | 50 | 175 |
| AS-350D | 38 | 130 |
| AS-355F-1 | 58 | 140 |
| AS-355F-2 | 58 | 140 |
| AS-365N-1 | 87 | 275 |
| BK-117 | 77 | 160 |
| BO-105CBS | 55 | 180 |
| SA-315B | 58 | 180 |
| SA-316B | 58 | 170 |
| SA-318C | 56 | 80 |
| SA-319B | 55 | NOT ESTABLISHED |
| SA-341G | 56 | 170 |
| EC-135 | 64 | 220 |
| BELL 47 | 17A | 90 |
| 47/SOLOY | 23 | 120 |
| 204B (UH-1 SERIES) | 88 | 200 |
| 205A-1 | 89 | 260 |
| 206B-II | 25 | 100 |
| 206B-III | 27 | 130 |
| 206L-1 | 32 | 150 |
| 206L-3 (Incl L-1 C30P) | 38 | 180 |
| 206L-4 | 38 | 180 |
| 212 | 100 | 390 |
| 214B | 160 | 380 |
| 214ST | 133 | NOT ESTABLISHED |
| 222A | 70 | NOT ESTABLISHED |
| 222B | 83 | NOT ESTABLISHED |
| 222UT | 83 | NOT ESTABLISHED |
| 407 | 45 | 155 |
| 412 | 110 | 390 |
| 412HP | 110 | 390 |
| MD 500C | 23 | 110 |
| 500D/E | 28 | 120 |
| 520N | 32 | 100 |
| 530F | 34 | 120 |
| 600N | 41 | 155 |
| 900/902 | 69 | 210 |
| HILLER SL-3/4 | 21A | 90 |
| UH-12 | 17A | 90 |
| 1100B | 22 | 130 |
| UH-12/SOLOY | 23 | 100 |
| SIKORSKY S-55T | 47 | 170 |
| S-58D/E | 83A | OGE 000 IGE 400 |
| S-58T/PT6T-3 | 115 | OGE 000 IGE 400 |
| S-58T/PT6T-6 | 115 | OGE 000 IGE 600 |
| S-62A | 70 | 300 |
| S-70 | 160 | N/A |

"A" after the gallons indicates Avgas; all others are turbine.	12/01

EXHIBIT 8

## Statement of Equivalent Rates for Federal Hires (48 CFR 52.222.42)

IS FOR INFORMATION ONLY AND IS REQUIRED TO BE INCLUDED IN THE SOLICITATION BY THE SERVICE CONTRACT ACT

THIS IS NOT A DEPARTMENT OF LABOR WAGE DETERMINATION

(See following page)

Set forth below are wage rates and fringe benefits that would be paid by the contracting activity for the various classes of service employees expected to be utilized under the contract if 5 U.S.C. 5332 (General Schedule-white collar) and/or 5 U.S.C. 5341 (Wage Board-blue collar) were applicable.

A.	EMPLOYEE CLASS			MONETARY WAGE

Aircraft Pilot, GS-12 (Alaska)			$ 27.71 plus 24% = $34.34

Aircraft Mechanic WG 10 (Alaska)			$ 29.05

B.	Fringe benefits such as, life, accident and health insurance, and sick leave, are not less than 5.1 percent of the basic hourly rate.

C.	Paid holidays are:

1.	New Year's Day		6.	Labor Day

2.	Martin Luther King, Jr.'s Birthday		7.	Columbus Day

3.	President's Day		8.	Veterans Day

4.	Memorial Day		9.	Thanksgiving Day

5.	Independence Day		10.	Christmas Day

D.	The amount of paid vacation time allowed is as follows:

1.	Two (2) hours of annual leave each week for an employee with less than three (3) years of service.

- Three (3) hours of annual leave each week for an employee with three (3) but less than fifteen (15) years of service.

3.	Four (4) hours of annual leave each week for an employee with fifteen (15) or more years of service.

E.	The percentage of the basic hourly rate that is contributed by the contracting agency for retirement is currently 7 to 17.5 percent.

EXHIBIT 9

Department of Labor Wage Determination Information

This solicitation includes Department of Labor (DOL) wage determinations as identified below.  In order that this solicitation may be accessed electronically, the following DOL wage determination information has been extracted from the wage determination(s) listed below and identifies the occupations of service employees that would typically be employed on this type of a solicitation.  This information should be considered when submitting an offer.  The DOL wage determination information identified herein will be included in the awarded contract with complete copies of the wage determinations being provided to the successful Contractor.  To receive the wage determinations in their entirety, please contact the issuing office at 208-433-5026 or submit a written facsimile request to 208-433-5030.

## Wage Determination No. 2003-0344 Rev 2, dated 02/02/2005

Employed on U.S. Department of the Interior contracts only.

Area:  		Alaska, Statewide

Occupation	Airplane Pilot:

Helicopters				Minimum Daily Wage:  	$172.26

Multi-Engine				Minimum Daily Wage:	$203.84

Single Engine				Minimum Daily Wage: 	$170.01

Daily Rate cannot be computed to an hourly rate

All occupations listed above receive the following benefits:

1.  Vacation:  2 weeks paid vacation after 1 year of service with a contractor or successor; 3 weeks after 15 years, Length of service includes the whole span of continuous service with the present contractor or successor, wherever employed, and with the predecessor contractors in the performance of similar work at the same federal facility.  (Reg. 29 CFR 4.173).

2.  Uniform Allowance:  If employees are required to wear uniforms in the performance of this contract (either by the terms of the Government contract, by the employer, by the state or local law, etc.), the cost of furnishing such uniforms and maintaining (by laundering or dry cleaning) such uniforms is an expense that may not be borne by an employee where such cost reduces the hourly rate below that required by the wage determination.  The Department of Labor will accept payment in accordance with the following standards as compliance:

The contractor or subcontractor is required to furnish all employees with an adequate number of uniforms without cost or to reimburse employees for the actual cost of the uniforms.  In addition, where uniform cleaning and maintenance is made the responsibility of the employee, all contractors and subcontractors subject to this wage determination shall (in the absence of a bona fide collective bargaining agreement providing for a different amount, or the furnishing of contrary affirmative proof as to the actual cost), reimburse all employees for such cleaning and maintenance at a rate of $3.35 per week (or $.67 cents per day).  However, in those instances where the uniforms furnished are made of “wash and wear” materials, may be routinely washed and dried with other personal garments, and do not require any special treatment such as dry cleaning, daily washing, or commercial laundering in order to meet the cleanliness or appearance standards set by the terms of the Government contract, by the contractor, by law, or by the nature of the work, there is no requirement that employees be reimbursed for uniform maintenance costs

## Wage Determination No.  2005-2017 Rev. 2 Dated 12/08/2006

Area:  		Alaska, Statewide

Occupation	Aircraft Mechanic I				Minimum Hourly Wage: $ 24.70

Aircraft Mechanic Helper				Minimum Hourly Wage: $ 19.36

Aircraft Servicer	`				Minimum Hourly Wage: $ 21.63

Aircraft Worker					Minimum Hourly Wage: $ 22.75

All occupations listed above receive the following benefits:

1.  Health & Welfare:  $3.01 an hour or $120.40 a week or $521.73 a month.

2.  Vacation:  2 weeks paid vacation after 1 year of service with a contractor or successor; 3 weeks after 5 years, and 4 weeks after 15 years.  Length of service includes the whole span of continuous service with the present contractor or successor, wherever employed, and with the predecessor contractors in the performance of similar work at the same federal facility.  (Reg. 29 CFR 4.173).

3.  Holidays:  A minimum of eleven paid holidays per year: New Year’s Day, Martin Luther King JR’s Birthday, Washington’s Birthday, Good Friday, Memorial Day, Independence Day, Labor Day, Columbus Day, Veterans’ Day, Thanksgiving Day, and Christmas Day.  A contractor may substitute for any of the named holidays another day off with pay in accordance with a plan communicated to the employees involved.  (See 29 CFR 4.174)

4.  HAZARDOUS PAY DIFFERENTIAL:  An 8 percent differential is applicable to employees employed in a position that represents a high degree of hazard when working with or in close proximity to ordinance, explosives, and incendiary materials.  This includes work such as screening, blending, dying, mixing, and pressing of sensitive ordnance, explosives, and pyrotechnic compositions such as lead azide, black powder and photoflash powder.  All dry-house activities involving propellants or explosives.  Demilitarization, modification, renovation, demolition, and maintenance operations on sensitive ordnance, explosives and incendiary materials.  All operations involving regarding and cleaning of artillery ranges.

A 4 percent differential is applicable to employees employed in a position that represents a low degree of hazard when working with, or in close proximity to ordinance, (or employees possibly adjacent to) explosives and incendiary materials which involves potential injury such as laceration of hands, face, or arms of the employee engaged in the operation, irritation of the skin, minor burns and the like; minimal damage to immediate or adjacent work area or equipment being used.  All operations involving, unloading, storage, and hauling or ordnance, explosive, and incendiary ordnance material other than small arms ammunition.  These differentials are only applicable to work that has been specifically designated by the agency for ordnance, explosives, and incendiary material differential pay

5.  Uniform Allowance:  If employees are required to wear uniforms in the performance of this contract (either by the terms of the Government contract, by the employer, by the state or local law, etc.), the cost of furnishing such uniforms and maintaining (by laundering or dry cleaning) such uniforms is an expense that may not be borne by an employee where such cost reduces the hourly rate below that required by the wage determination.  The Department of Labor will accept payment in accordance with the following standards as compliance:

The contractor or subcontractor is required to furnish all employees with an adequate umber of uniforms without cost or to reimburse employees for the actual cost of the uniforms.  In addition, where uniform cleaning and maintenance is made the responsibility of the employee, all contractors and subcontractors subject to this wage determination shall (in the absence of a bona fide collective bargaining agreement providing for a different amount, or the furnishing of contrary affirmative proof as to the actual cost), reimburse all employees for such cleaning and maintenance at a rate of $3.35 per week (or $.67 cents per day).  However, in those instances where the uniforms furnished are made of “wash and wear” materials, may be routinely washed and dried with other personal garments, and do not require any special treatment such as dry cleaning, daily washing, or commercial laundering in order to meet the cleanliness or appearance standards set by the terms of the Government contract, by the contractor, by law, or by the nature of the work, there is no requirement that employees be reimbursed for uniform maintenance costs.

Request for Authorization of Additional Classification and Wage Rate (Standard Form 1444 (SF 1444)):  If the offeror intends to employ a class of service employee that is not listed above, the offeror should immediately contact the issuing office of this solicitation and request a complete copy of the wage determination.  The offeror can than view the wage determination in its entirety and if needed can make a request for authorization of an additional classification and wage rate through the conformance process as set forth in the wage determinations.

To receive a wage determination in its entirety or from an area other than Alaska, please contact the issuing office at 907-271-6061 or submit a written facsimile request to 907-271-4788.

ARO 12/14/2006

EXHIBIT 9

## Unavailability Conversion Chart

| HOURS UNAVAILABLE | UNITS OF AVAILABILITY RECORDED AS: | UNITS OF UNAVAILABILITY RECORDED AS: |
| --- | --- | --- |
| 0 | 1.00 | 0.00 |
| 1 | .90 | .10 |
| 2 | .80 | .20 |
| 3 | .70 | .30 |
| 4 | .60 | .40 |
| 5 | .50 | .50 |
| 6 | .40 | .60 |
| 7 | .30 | .70 |
| 8 | .20 | .80 |
| 9 | .10 | .90 |
| 10 | .00 | 1.00 |

EXHIBIT 10

## Transportation Worksheet

| When assigned to an alternate base, the Contractor will be paid for actual necessary and reasonable costs associated with transporting authorized personnel. The Contractor is responsible for advising the on-site Government representative(s) of the anticipated cost associated with transporting relief (and/or maintenance) personnel to the alternate base prior to the relief exchange. Claims must be supported by itemized invoices. See contract clause “Transportation Costs Associated with Operating Away From the Designated Base” for detailed information |
| --- |
| DATE | ALTERNATE BASE LOCATION |
| Relief Exchange – Involved Crew Member(s) |
| ( Pilot Name | ( Fuel Servicing Vehicle Driver Name | ( Mechanic (If required by contract) Name |
| Scheduled Maintenance |
| ( Mechanic Name | ( Other Name |
| Maintenance Accomplished | Reason for providing additional personnel |
| ITEMIZATION OF COSTS – Invoices and/or receipts are attached (copies are acceptable) |
| Airline Transportation | Name | $ |
| Airline Transportation | Name | $ |
| Charter Aircraft | Invoice to include aircraft make/model, flight time, hourly rate, passengers, and departure/destination location, date and time | $ |
| Rental Car |  | $ |
| Rental Car Fuel |  | $ |
| POV | Total Mileage | From | To | $ |
| Other (explain) | $ |
|  | $ |
|  | $ |
|  | $ |
|  | $ |
| Total ACTUAL Cost | $ |
| Yes, the COR was notified of the anticipated cost for this alternate base transportation expense prior to mobilization of the relief personnel Contractor Representative Signature | Date |

Project Description:

Support of the Bureau of Land Management, Anchorage Field Office resource projects including archaeology, hydrology, realty, fisheries, wildlife, geology, recreation and a variety of natural resource projects. Transport of personnel, supplies and equipment (internal and external) to remote field camps and work locations throughout Alaska. Subsistence and lodging in villages will generally be arranged by the Government with the Contractor making payment and claiming reimbursement in accordance with the terms of the contract. Some work may be based out of remote field camps where sleeping in tents with sleeping bags is required.

# section d – instructions to offerors

# INTRODUCTION

## D1.  General Information

D1.1  The services of this Request for Proposals (RFP) are being acquired under the authority of Federal Acquisition Regulations (FAR), Part 12, Acquisition of Commercial Items and FAR Subpart 13.5, Test Program for Certain Commercial Items.

D1.2  If you wish to compete for the contract described in Sections A through C of this RFP, you must submit a proposal that includes a signed and dated offer and other requested information by the time and date shown on the SF1449.

# INSTRUCTIONS TO OFFERORS--COMMERCIAL ITEMS (52.212-1 JAN 2006) [Tailored JAN 2005]

## D2 North American Industry Classification System (NAICS) Code and Small Business Size Standard

This procurement is open to both small and large business concerns.

## D3  Proposals

To be considered as a prospective Contractor for the requirement identified in this solicitation, an offeror must submit a proposal consisting of a valid offer and the Offeror Capability Information identified below.  Send proposals to:

By mail, hand carried or express delivery service:

Ms Caroline  A. Wallace

Department of the Interior

Aviation Management

4405 Lear Court

Anchorage, AK 99502

By facsimile:	907-271-4788  It is the offeror’s responsibility to ensure that a complete proposal is received.  To verify receipt call  907-271-6061.

## D4   Offer Contents

D4.1  SF 1449, Solicitation/Contract/Order for Commercial Items, completed and signed.

D4.2  Solicitation Section A, pricing page(s) completed where indicated with unit rates offered in U.S. dollars.  The Government will compute the extended yearly amounts for availability  by multiplying the unit prices offered times the quantities shown.  Enter an extended amount for each year as well an amount for the total for all years. Unit prices must be offered for all variable priced items.  There are no totals to compute for flight time or other variable priced items.

D4.3  Reserved

D4.4  A completed copy of the Offeror’s Representations and Certifications included in Section E (see FAR 52.212-3(j) for those representations and certifications that the offeror must complete electronically).

D4.5  A completed copy of Offeror’s Miscellaneous Information included in Section E.

D4.6  Acknowledgment of Solicitation Amendments (if any).

D4.7  A completed copy of the Aircraft Questionnaire included in Section E.  The aircraft make, model, and payload we confirm will be made a part of your offer and will be binding if your offer is accepted for award.  The confirmed information will be identified in Section A of the conformed contract.

D4.8  Offeror Capability Information.  Offeror must include: A completed copy of the Reference Questionnaire included in Section E.  This will be used to evaluate your organizational experience and past performance.

D4.9 A completed copy  of the Pilot Questionnaire included in Section E. Pilots.  Personnel (pilots) offered will be made part of your offer and will be binding if your offer is accepted for award. The confirmed information will be identified in Section C of the conformed contract.

## D5  Late Submissions, Modifications, Revisions, and Withdrawals of Offers

Late Submissions, Modifications, Revisions and Withdrawals of Offers are subject to the terms of Federal Acquisition Regulation (FAR) clause 52.212-1(f), which is incorporated by reference, except that offers may be withdrawn at any time before award is made.

## D6  Data Universal Numbering System (DUNS) Number)

Data Universal Numbering System (DUNS) Number. (Applies to all offers exceeding $25,000, and offers of $25,000 or less if the solicitation requires the Contractor to be registered in the Central Contractor Registration (CCR) database. The offeror  shall enter, in the block with its name and address on the cover page of its offer, the annotation "DUNS" or "DUNS+4" followed by the DUNS or DUNS+4 number that identifies the offeror's name and address. The DUNS+4 is the DUNS number plus a 4-character suffix that may be assigned at the discretion of the offeror to establish additional CCR records for identifying alternative Electronic Funds Transfer (EFT) accounts (see FAR Subpart 32.11) for the same parent concern. If the offeror does not have a DUNS number, it should contact Dun and Bradstreet directly to obtain one. An offeror within the United States may contact Dun and Bradstreet by calling 1-866-705-5711 or via the internet at http://www.dnb.com. An offeror located outside the United States must contact the local Dun and Bradstreet office for a DUNS number.

## D7  Special Notice to Offerors

D7.1 Central Contractor Registration

Unless exempted by an addendum to this solicitation, by submission of an offer, the offeror acknowledges the requirement that a prospective awardee shall be registered in the CCR database prior to award, during performance and through final payment of any contract resulting from this solicitation.  Failure to register in the CCR database prior to award may affect your ability to be awarded a contract and the Contracting Officer may proceed to award to the next otherwise successful registered Offeror. Offerors may obtain information on registration and annual confirmation requirements via the internet at http://www.ccr.gov or by calling 1-888-227-2423 or 269-961-5757.

# EVALUATION--COMMERCIAL ITEMS (48 CFR 52.212-2 JAN 1999)

The Government will evaluate proposals and select the Contractor based on (1) offer acceptability, (2) evaluated price, (3) consideration for like make/model aircraft, (4) aircraft target requirements, (5) Proposed Pilots and (6) offeror capability, as explained below.

## D8  Offer Acceptability

The Government must deem offers to be acceptable to consider them further and will base determinations of offer acceptability on the following two subfactors:

D8.1  Assent to Solicitation Terms. Your offer must assent to all terms of this request for proposals and you must provide all information requested.  Your offer will be unacceptable if you take exception to any term of this solicitation.

D8.2  Aircraft Requirements.  Your offer must propose an aircraft in response to the target Aircraft Requirements  in Section A of this solicitation.  Your offer will be unacceptable if you propose an aircraft that fails to address the target requirements specified in Section A of this solicitation.

D8.3 Unacceptable offers will be eliminated without considering aircraft requirements, offeror capability or price.

## D9  Evaluated Price

D9.1  The Government will apply the unit prices in acceptable offers, including option year unit prices, including the estimated cost of the variable priced items, in accordance with the following evaluation model.

D9.1.1For evaluation purposes the following  workload estimate will be used: (These are not guaranteed quantities)

1b Flight Time: 235 hours per year

The totals for availability, estimated flight  and other variable bid items as described above, for all years will be added together to arrive at the estimated evaluated price for each offeror.  Once the estimated evaluated prices of all acceptable offers have been determined, the Government will compare the evaluated prices, by item, and eliminate any offer with an unreasonably high-evaluated price, without considering aircraft payload or offeror capability. The Government will then perform a tradeoff analysis, as described below in D3.5 with the remaining offers.

D9.2  The Government reserves the right to reject offers that have materially unbalanced prices.  An offer is materially unbalanced when it is based on prices significantly less than cost for some work and prices which are significantly overstated in relation to cost for other work, and there is a reasonable doubt that the offer will result in the lowest overall cost to the Government even through it may be the low evaluated offer, or if it is so unbalanced as to be tantamount to allowing an advance payment.

## D10  Aircraft  Requirements

The Government will evaluate your proposed aircraft to determine whether it is above, at, or below the Target  Aircraft Requirements specified in Section A of this RFP. The higher your aircraft rates against target requirements, the better the evaluation you will receive for this factor.  However, an aircraft payload that is unsupported by the offeror’s aircraft current weight and balance report, equipment list, or charts will be evaluated as high risk and will subsequently impact the evaluation of your aircraft payload.

## D11 Pilot Qualifications And Past Performance.

We will evaluate your proposed pilots based on the extent to which they have performed services similar to those contained in this solicitation and in make and model of aircraft offered.  Pilots possessing qualifications less than the minimum required in paragraph B3 will not be considered.  Pilots exceeding the requirements and those with more recent experience will receive a better evaluation.  If your offer is accepted for award, the pilots offered on the questionnaire will be added as key personnel under the resultant contract.  If other than the proposed pilots are to be used, the replacement pilots shall meet or exceed the skill, experience, and knowledge possessed by the originally proposed pilot.  (See also Section C for replacement approval.)

## D12  Offeror Capability

The Government  will evaluate your capability based on the following two subfactors:

D12.1  Organizational Experience. The Government will base its evaluations of your experience on the extent to which you have performed services of the kind described in paragraph B1.1 of the Technical Specifications of this RFP and under similar contract terms. The more recent your experience, and the broader and deeper, the better the evaluation you will receive. Only your firm’s experience as an organization will be considered.  We will not consider experience more than three (3) years old.

D12.2  Organizational Past Performance. The Government will evaluate your past performance in rendering services of the kind described in paragraph B1.1 of the Technical Specifications of this RFP. “Past Performance” refers to the quality of your work in the past.  Your past performance will be evaluated on the basis of information obtained from references and other sources. The Government will give greater weight to its own experiences with you, if any, than it will give to reports obtained from others, and it will not consider past performance more than three years old.

## D13  Tradeoff Analysis and Contractor Selection

The Government will select the Contractor by comparing the acceptable offers on the basis of proposed aircraft target elements, offeror capability, and reasonability of evaluated prices. If one offer is best on all the factors, then that offer will be selected as being the best value to the Government. If no offer is best on all the factors, then the Government will consider the differences among offers and make tradeoffs in order to determine which offer is the best value. The Government will award the contract to the offer that has the best combination of aircraft payload, offeror capability, and evaluated price.

## D14  Notice of Award

The Government will provide the successful Contractor with a written notice of award, either by mail or other means, upon selection.  This notice will result in a binding contract without further action by either party.

# section e – offeror’s representations, certifications and other statements

# 52.212-3 OFFEROR REPRESENTATIONS AND CERTIFICATIONS—COMMERCIAL ITEMS (NOV 2006)

An offeror shall complete only paragraph (k) of this provision if the offeror has completed the annual representations and certifications electronically at http://orca.bpn.gov. If an offeror has not completed the annual representations and certifications electronically at the ORCA website, the offeror shall complete only paragraphs (b) through (j) of this provision.

(a) Definitions. As used in this provision-

"Emerging small business" means a small business concern whose size is no greater than 50 percent of the numerical size standard for the  NAICS code designated.

"Forced or indentured child labor" means all work or service--

(1) Exacted from any person under the age of 18 under the menace of any penalty for its nonperformance and for which the worker does not offer himself voluntarily; or

(2) Performed by any person under the age of 18 pursuant to a contract the enforcement of which can be accomplished by process or penalties.

“Manufactured end product” means any end product in Federal Supply Classes (FSC) 1000-9999, except-

- FSC 5510, Lumber and Related Basic Wood Materials;

- Federal Supply Group (FSG) 87, Agricultural Supplies;

- FSG 88, Live Animals

- FSG 89, Food and Related Consumables;

- FSC 9410, Crude Grades of Plant Materials;

- FSC 9430, Miscellaneous Crude Animal Products, Inedible;

- FSC 9440, Miscellaneous Crude Agricultural and Forestry Products;

- FSC 9610, Ores;

- FSC 9620, Minerals, Natural and Synthetic; and

- FSC 9630, Additive Metal Materials.

“Place of Manufacture” means the place where an end product is assembled out of components, or otherwise made or processed from raw materials into the finished product that is to be provided to the Government.  If a product is disassembled and reassembled, the place of reassembly is not the place of manufacture.

“Service-disabled veteran-owned small business concern”-

- Means a small business concern-

- Not less than 51 percent of which is  owned by one or more service-disabled veterans or, in the case of any publicly owned business, not less than 51 percent of the stock of which is owned by one or more service-disabled veterans; and

- The management and daily business operations of which are controlled by one or more service-disabled veterans or, in the case of a service-disabled veteran with permanent and severe disability, the spouse or permanent caregiver of such veteran.

(2) Service-disabled veteran means a veteran, as defined in 38 U.S.C. 101(2), with a disability that is service connected as defined in 38 U.S.C. 101(16).

"Small business concern" means a concern, including its affiliates, that is independently owned and operated, not dominant in the field of operation in which it is bidding on Government contracts, and qualified as a small business under the criteria in 13 CFR Part 121 and size standards in this solicitation.

“Veteran-owned small business concern” means a small business concern-

- Not less than 51 of which is owned by one or more veterans (as defined by 38 U.S.C. 101(2)) or, in the case of publicly owned business, not less than 51 percent of the stock of which is owned by one or more veterans; and

- The management and daily business operations of which are controlled by one or more veterans.

"Women-owned business concern" means a concern which is at least 51 percent owned by one or more women; or in the case of any publicly owned business, at least 51 percent of its stock is owned by one or more women; and whose management and daily business operations are controlled by one or more women.

"Women-owned small business concern" means a small business concern--

(1) Which is at least 51 percent owned by one or more women or, in the case of any publicly owned business, at least 51 percent of the stock of which is owned by one or more women; and

(2) Whose management and daily business operations are controlled by one or more women.

(b) Taxpayer Identification Number (TIN) (26 U.S.C. 6109, 31 U.S.C. 7701).  (Not applicable if the offeror is required to provide this information to a central contractor registration database to be eligible for award.)

(1)  All offerors must submit the information required in paragraphs (b)(3) through (b)(5) of this provision to comply with debt collection requirements of 31 U.S.C. 7701(c) and 3325(d), reporting requirements of 26 U.S.C 6041, 6041A, and 6050M, and implementing regulations issued by the Internal Revenue Service (IRS).

(2) The TIN may be used by the Government to collect and report on any delinquent amounts arising out of the offeror's relationship with the Government (31 U.S.C. 7701(c)(3)).  If the resulting contract is subject to the payment reporting requirements described in FAR 4.904, the TIN provided hereunder may be matched with IRS records to verify the accuracy of the offeror's TIN.

(3)  Taxpayer Identification Number (TIN).

TIN: _____________________.

TIN has been applied for.

TIN is not required because:

Offeror is a nonresident alien, foreign corporation, or foreign partnership that does not have income effectively connected with the conduct of a trade or business in the United States and does not have an office or place of business or a fiscal paying agent in the United States;

Offeror is an agency or instrumentality of a foreign government;

Offeror is an agency or instrumentality of a Federal Government.

(4) Type of Organization

Sole proprietorship;

Partnership;

Corporate entity (not tax-exempt);

Corporate entity (tax-exempt);

Government entity (Federal, State, or local);

Foreign Government;

International organization per 26 CFR

1.6049-4;

Other ________________________________.

(5)Common Parent.

Offeror is not owned or controlled by a common parent;

Name and TIN of common parent:

Name_______________________________

TIN________________________________

(c) Offerors must complete the following representations when the resulting contract will be performed in the United States or its outlying areas. Check all that apply.

(1) Small business concern. The offeror represents as part of its offer that it  is , is not  a small business concern.

(2) Veteran-owned small business concern.[Complete

only if the offeror represents itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents as part of its offer that it  is ,  is not  a veteran-owned small business concern.

- Service-disabled veteran-owned small business

concern. [Complete only if the offeror represents itself as a small business concern in paragraph (c)(2) of this provision.]  The offeror represents as part of its offer that it  is ,  is not  a  service-disabled veteran-owned small business concern.

- Small disadvantaged business concern. [Complete only if the offeror represented itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents, for general statistical purposes, that it is ,  is not  a small disadvantaged business concern as defined in 13 CFR 124.1002.

(5) Women-owned small business concern. [Complete only if the offeror represented itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents that it  is ,  is not  a women-owned small business concern.

Note:  Complete paragraphs (c)(6) and (c)(7) only if this solicitation is expected to exceed the simplified acquisition threshold.

(6) Women-owned business concern. (other than small business concern).  [Complete only if the offeror is a women-owned business concern and did not represent itself as a small business concern in paragraph (c)(1) of this provision.]  The offeror represents that it  is  a women-owned business concern.

(7) Tie bid priority for labor surplus area concerns.   (Not applicable to this solicitation.)

(8) Small Business Size for the Small Business Competitiveness Demonstration Program and for the Targeted Industry Categories under the Small Business Competitiveness Demonstration Program. (Not applicable to this solicitation.)

(9) Complete only if the solicitation contains the clause at FAR 52.219-23, Notice of Price Evaluation Adjustment for Small Disadvantaged Business Concerns, or FAR 52.219-25, Small Disadvantaged Business Participation Program-Disadvantaged Status and Reporting, and the offeror desires a benefit based on its disadvantaged status.]  (Not applicable to this solicitation.)

(10) HUBZone small business concern. [Complete only if the offeror represented itself as a small business concern in paragraph (c)(1) of this provision.] The offeror represents as part of its offer that--

(i) it  is ,  is not  a HUBZone small business concern listed, on the date of this representation, on the List of Qualified HUBZone Small Business Concerns maintained by the Small Business Administration, and no material change in ownership and control, principal office, or HUBZone employee percentage has occurred since it was certified by the Small Business Administration in accordance with 13 CFR part 126; and

(ii) it  is ,  is not  a joint venture that complies with the requirements of 13 CFR part 126, and the representation in paragraph (c)(9)(i) of this provision is accurate for the HUBZone small business concern or concerns that are participating on the joint venture. [The offeror shall enter the name or names of the HUBZone small business concern or concerns that are participating in the joint venture: __________________________.] Each HUBZone small business concern participating in the joint venture shall submit a separate signed copy of the HUBZone representation

(d) Representations required to implement provisions of Executive Order 11246--

(1) Previous Contracts and Compliance. The offeror represents that--

(i) It  has ,  has not , participated in a previous contract or subcontract subject to the Equal Opportunity clause of this solicitation, and

(ii) It  has ,  has not , filed all required compliance reports.

(2) Affirmative Action Compliance. The offeror represents that--

(i) It  has developed and has on file ,  has not  developed and does not have on file , at each establishment, affirmative action programs required by rules and regulations of the Secretary of Labor (41 CFR Subparts 60-1 and 60-2), or

(ii) It  has not  previously had contracts subject to the written affirmative action programs requirement of the rules and regulations of the Secretary of Labor.

(e) Certification Regarding Payments to Influence Federal Transactions (31 U.S.C. 1352). (Applies only if the contract is expected to exceed $100,000.) By submission of its offer, the offeror certifies to the best of its knowledge and belief that no Federal appropriated funds have been paid or will be paid to any person for influencing or attempting to influence an officer or employee of any agency, a Member of Congress, an officer or employee of Congress or an employee of a Member of Congress on his or her behalf in connection with the award of any resultant contract.

(f) Buy American Act Certificate. (Not applicable to this solicitation.)

(g) Buy American Act - Free Trade Agreements - Israeli Trade Act Certificate.  (Not applicable to this solicitation.)

(h) Certification Regarding Debarment, Suspension or Ineligibility for Award (Executive Order 12689). (Applies only if the contract value is expected to exceed the simplified acquisition threshold.) The offeror certifies, to the best of its knowledge and belief, that the offeror and/or any of its principals--

(1)  Are ,  are not  presently debarred, suspended, proposed for debarment, or declared ineligible for the award of contracts by any Federal agency; and

(2)  Have ,  have not , within a three-year period preceding this offer, been convicted of or had a civil judgment rendered against them for: Commission of fraud or a criminal offense in connection with obtaining, attempting to obtain, or performing a Federal, state or local government contract or subcontract; violation of Federal or state antitrust statutes relating to the submission of offers; or Commission of embezzlement, theft, forgery, bribery, falsification or destruction of records, making false statements, tax evasion, or receiving stolen property; and

(3)  Are ,  are not  presently indicted for, or otherwise criminally or civilly charged by a government entity with, commission of any of these offenses.

(i) Certification Regarding Knowledge of Child Labor for Listed End Products (Executive Order 13126). (Not applicable to this solicitation)

(j) Place of manufacture.  (Does not apply unless the solicitation is predominantly for the acquisition of manufactured end products.)  For statistical purposes only, the offeror shall indicate whether the place of manufacture of the end products it expects to provide in response to this solicitation is predominantly-

(1)  In the United States (Check this box if the total anticipated price of offered end products manufactured in the United States exceeds the total anticipated price of offered end products manufactured outside the United States); or

(2)  Outside the United States.

(k)(1) Annual Representations and certifications. Any changes provided by the offeror in paragraph (k)(2) of this provision do not automatically change the representations and certifications posted on the Online Representations and Certifications Application (ORCA) website.

(2) The offeror has completed annual representations and certifications electronically via the ORCA website at http://orca.bpn.gov. After reviewing the ORCA database information, the offeror verifies by submission of this offer that the representations and certifications currently posted electronically at 52.212-3, Offeror’s Representations and Certifications – Commercial Items, have been entered or updated in the last 12 months, are current, accurate, complete, and applicable to this solicitation (including the business size standard applicable to the NAICS code referenced for this solicitation), as of the date of this offer and are incorporated in this offer by reference (see FAR 4.1201), except for paragraphs____________________________.

[Offeror to identify the applicable paragraphs at (b) through (j) of this provision that the offeror has completed for the purposes of this solicitation only, if any.

These amended representation(s) and/or certification(s) are also incorporated in this offer and are current, accurate, and complete as of the date of this offer.

Any changes provided by the offeror are applicable to this solicitation only, and do not result in an update to the representations and certifications posted on ORCA.]

(End of Provision)

OFFEROR NAME _______________________________________

# SECTION E EXHIBITS

#### OFFEROR’S MISCELLANEOUS INFORMATION

AIRCRAFT QUESTIONNAIRE

REFERENCE QUESTIONNAIRE

PILOT QUESTIONNAIRE

## OFFEROR’S MISCELLANEOUS INFORMATION

| Offeror’s DUNS Number |  |
| --- | --- |
| Offeror’s Complete E-mail Address 1. Contract Issues Point of Contact 2.Financial Issues Point of Contact |  |
| Offeror’s Office Telephone Number |  |
| Offeror’s Facsimile (FAX) Number |  |
| Offeror Contact Representative(s) | 1. Name | Telephone |
|  | 2. Name | Telephone |

## AIRCRAFT QUESTIONNAIRE

You may recreate this form but it must include all the information listed – COMPLETE FOR EACH AIRCRAFT

This Questionnaire completely and accurately completed will be used to determine your aircraft payload capability.

REPRODUCE AND SUBMIT FOR EACH AIRCRAFT OFFERED - COMPLETE SHADED BLOCKS

| Target Aircraft Characteristics: -- Seating: Five passenger seats -- Cruising airspeed: 115 nautical miles per hour at sea level -- Useful load: (HIGE) 1,500 pounds at 80 degrees F at 4,000 feet pressure altitude -- Range: 280 statute miles at sea level (not including 20 minutes reserve (fuel). -- Turbine engine rated at 641 shaft horsepower exclusive of installation limitations. |
| --- |
| Aircraft Make and Model | FAA Registration # | Serial # |
| # of Insured Passenger Seats (excludes pilot seat) | Aircraft Equipped Weight (Your aircraft weight & balance report & equipment list will be used to substantiate this weight – see note 1. below) |
| Currently Installed Aircraft Equipment to be Removed to Achieve My Proposed Payload Below (If none, indicate NONE below) | Equipment to be Added to Meet the Aircraft Specifications Requirements (If none, indicate NONE below) |
| EQUIPMENT ITEM | WEIGHT | EQUIPMENT ITEM | WEIGHT |
| ENTER YOUR PROPOSED HOGE AIRCRAFT PAYLOAD (The aircraft make, model and HOGE payload that we confirm with you will be made a part of your offer and will be binding if your offer is accepted for award |  |

NOTE

1.  By signing below, I acknowledge that I have included the aircraft’s

- Latest aircraft weight and balance report,

- Aircraft equipment list,

- Aircraft appropriate hover ceiling charts used to arrive at the above payload.

Failure to include the above information, will effect the evaluation you receive for your aircraft.

2.  By signing below, I certify to the best of my knowledge that the above aircraft information is accurate.

| Name and Signature of Representative Completing this Form | Date |
| --- | --- |
| OFFEROR’S NAME |

## REFERENCE QUESTIONNAIRE

You may recreate this form but it must include all the information listed

If  you fail to include all requested information or we are unable to contact your references based on the information you provide, you may not receive consideration for the work done.  Include recent (not more than 3 years old) experience of the kind described in paragraph B1.1 of the specifications.

| OFFEROR NAME: | DATE |
| --- | --- |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2006 2005 2004 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2006 2005 2004 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2006 2005 2004 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2006 2005 2004 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |
| Primary Type of Work Done: |
| Location of Work Done: | A/C Make/Model Used: |
| Contract #: None | Exclusive Use Call When Needed | Use Dates: TO | CHECK ALL THAT APPLY 2006 2005 2004 |
| Est. Annual Value of Work: | Estimated Annual Flight Hours: | Client Name/ Point of Contact: |
| Client Telephone #: | Client Facsimile #: |

## PILOT QUESTIONNAIRE –

Complete for each pilot and relief pilot proposed for use.  Pilot skills and specific (or project) experience can be a significant element to successful performance.  That experience should be highlighted through the identification of a specific pilot (by name) or by the minimum skill levels (project types, make and model, geographic area experience, or tasks such as long line) that are offered for any pilot the contractor proposes to assign to this contract.  Reproduce this sheet as necessary.

| COMPLETE THIS SHEET FOR EACH PROPOSED PILOT |
| --- |
| Pilot Name: Airman Certificate #: |
| Indicate if Individual is to be Primary or Relief Pilot: [ ] PRIMARY [ ] RELIEF |
| Meets Minimum PIC Time Requirements at B3.1 | Yes[ ] No[ ] |
| Previous or Current Possession of an Interagency Card: | Yes[ ] No[ ] |
| If YES to above, Identify Issuing Government Office: |
| Enter Expiration Date of Card: |
| Xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx | List Hours |
| Total /Helicopter Time |  |
| Total Time in Make and Model Offered |  |
| Briefly explain locations and type flying accomplished which demonstrates pilot’s actual experience appropriate to the type work referenced in the solicitation. |
| Describe pilot's Helicopter related experience (within last 3 years) in the format shown below. Experience/Description Aircraft Type Location Dates Hours Logged |
| Customer References Customer’s Name and Company Phone Number |
| Description of all violations, license suspensions or revocations, and accident history for the pilot for the past three years. |

NOTE:  This form will be used to confirm that the pilots meet the minimum requirements of the solicitation.

# Text boxes

DRAWING FS/OAS A-17

AUXILIARY VHF-FM RADIO INTERFACE