CALIFORNIA

GEOGRAPHIC

COORDINATE

DATA BASE

(GCDB)

USERS'

GUIDE

Bureau of Land Management

California State Office

Branch of Cadastral Survey - GCDB Section

Sacramento, California

916-978-4340

GEOGRAPHIC COORDINATE DATA BASE USERS' GUIDE

TABLE OF CONTENTS

INTRODUCTION	4

The files you will be most interested in	4

TOWNSHIP NAMING CONVENTIONS	5

ERROR ELLIPSES (GMM) AND RELIABILITIES (PCCS)	5

POINT IDENTIFICATION SYSTEM	5

SUMMARY	9

Point Identifier Standards	9

Segment Identifiers	9

CONTROL	10

KEY TO RELIABILITY OF CONTROL POINTS	11

GMM REGIONAL ADJUSTMENT INFORMATION	13

COMPARABLE FILES FOR PCCS AND GMM	15

C36N01E	16

R36N01E	17

T06N08E.SCR	18

X36N01E	19

TABLE A	20

TABLE B	20

GMM FILES	21

T06SR20E.CON	21

T06SR20E.CTL	22

T06SR20E.COR	23

T06SR20E.DXF	24

T06SR20E.GEO	25

T06SR20E.LX	26

T06SR20E.PGC	28

T06SR20E.RAW	29

T06SR20E.SID	30

T06SR20E.UTM	31

APPENDIX A - GMM Glossary	32

NO WARRANTY IS MADE BY THE BUREAU OF LAND MANAGEMENT FOR USE OF THE DATA FOR PURPOSES NOT INTENDED BY THE BUREAU OF LAND MANAGEMENT.

November 29, 1999

This page intentionally left blank.

INTRODUCTION

The Geographic Coordinate Data Base (GCDB) contains the geographic coordinates, and their associated attributes, for the Public Land Survey System (PLSS).  Coordinates are available for all rectangular corners down to the 1/16 section corner level, and all special survey corners (meanders, mining claims, HES, etc).  It provides the foundation for the BLM's Automated Land and Mineral Record System (ALMRS) and will be useful to anyone trying to attach data to points on the earth's surface.  These coordinates were calculated using the most recent survey information available for a township and control points from various sources.  Two different software packages were used, PLSS Coordinate Computation System (PCCS) and GCDB Measurement Management (GMM).  PCCS was used first, until May 1993.  The file names for the two software packages are different but the contents are essentially the same.

The PCCS files have coordinates in Latitude/Longitude NAD 27, and Universal Transverse Mercator projection (UTMs - x,y in meters).  State plane coordinates can be generated if needed.  GMM files have coordinates in all three formats.

The files you will be most interested in will be:

PCCS - L06N08E, U06N08E, X06N08E

GMM  - T03SR39E.LX, T03SR39E.UTM, T03SR39E.COR, T03SR39E.DXF, 	              T03SR39E.PGC, T03SR39E.GEO, T03SR39E.TPR

Descriptions of some of the files are included for your information even though you won't be using them. (We know you'll be curious.)

You need to know how the point identification system works, the difference between the meaning of reliability in PCCS versus GMM, and some information on control points.  These topics are discussed below.

The geographic coordinates and their associated products have NO LEGAL SIGNIFICANCE.  They should be used for record keeping, mapping, graphics and planning purposes only.

We can't promise you that the data is flawless.  Let us know if you find any problems.  This will help us to improve the quality of the data base.  If you have questions about anything, give us a call.  We aim to please!

TOWNSHIP NAMING CONVENTIONS

BLM has various township naming conventions.  They are listed below.

SURVEY PLATS/NOTES		GMM		PCCS L FILE	ALMRS DED*

T. 22 N., R. 1 W.		T22NR01W	L22N01W		0220N0010W

T. 14 N., R. 4 E.		T14NR04E	L14N04E		0140N0040E

T. 11-1/2 S., R. 6 W.	T112S06W	L11206W		0112S0060W

T. 12 N., R. 24-1/2 E. 	T12N242E	L12N242E		0120N0242E

* Data Element Dictionary										ERROR ELLIPSES (GMM) AND RELIABILITIES (PCCS)

In GMM, the error region (ellipse) is available, the first value is the (semi-major) axis of maximum error within the ellipse, and the second value is the (semi-minor) axis of minimum error within the ellipse.  The values are in feet.  The error ellipses are internal to that particular township only. See Appendix A.  They are not a reflection of true (absolute) coordinate reliability but are relative to each other within a township reflecting the integrity of the survey information used.

In PCCS, the two values reflect the average and maximum reliability, in feet, for each point.  These values are comparable from one township to another and are an estimate of the true positional reliability.

POINT IDENTIFICATION SYSTEM

Point IDs are used to show where in a township a point is located and generally what kind of point it is (i.e. township exterior, interior, offset, meander, tract, special survey, mile post).  It is a 6 digit number composed of 2 parts, XxxYyy, related to the x,y axis.  In Xxx or Yyy, X or Y is the line number and xx or yy is the number of chains* from the section corner, going west to east and south to north.  The diagrams on the next 2 pages show how the numbering scheme works.

Numbers greater than 700700 are reserved for the following special situations.

Xxx = 711 -799	Boundaries with Mileposts

800 -836	Meanders

837 -899	Tracts

900 -999	Mineral Surveys, Homestead Entries, etc.

Yyy	Numbered sequentially along the survey in increments of 10.  The prefix (Xxx) may be the same for all points in a similar survey.

In PCCS files, intersections of section lines and special survey lines will have two IDs, the "rectangular" (+4) and the segment identifier.

SUMMARY

Point Identifier Standards

! Each XxxYyy has a prefix, Xxx, and a suffix, Yyy.

! X and Y start at 1 and increase by miles east or north.

! xx and yy increase by tens of chains within each

mile.

! The one's place (Xxx or Yyy) is reserved for:

0	a rectangular corner point.

1,2,8 or 9 (1,2) offset corners in Township interior.

3 or 7 (3)        offset corners on Township boundaries,

3,4,6 or 7 (3,4) intersection with special surveys.

5	for 1/256th corners.

SUMMARY

Segment Identifiers

!  For each XxxYyy, Xxx =

100 - 710  Rectangular

711 - 799  Boundaries with Mileposts

800 - 836  Meanders

837 - 899  Tracts

900 - 999  Mineral Surveys, Homestead Entries, etc.

!  Yyy increments by tens, sequentially along the survey.

!  Groups of similar surveys may have one segment

identifier prefix.

CONTROL

Geographic control for GCDB is derived from a variety of sources, the various sources having a particular reliability.  (e.g. Digitized points from USGS maps have a reliability of 40,40 (feet) whereas NGS first order points have reliabilities of 1,1 (foot).)  The control points are handled differently by PCCS and GMM.  In PCCS the control points are assigned a reliability and the values for latitude and longitude are held fixed during the computational process.  In GMM the control points are not held fixed, but are assigned error estimates (weights), and allowed to adjust during the adjustment process.

In GMM, the published values of control established by NGS and USGS are assigned error estimates of .001 feet, which is the most accurate the GMM software allows.  In PCCS computed townships, the values for published control should be identical to the published values.  For the townships computed using GMM the values should be the same to four decimal places.  YOU ARE ADVISED TO ALWAYS REFER TO THE PUBLISHED VALUES rather than using the value from the PCCS or GMM files.

Many of the control points in GCDB are digitized values for PLSS corners shown as "found crosses" on USGS 7-1/2 minute quads.  These digitized points are assigned a reliability of 40,40 (feet) in PCCS or GMM.  PCCS will retain the digitized values during the computation process.  GMM will not retain the digitized values, but will allow the digitized control to float and will adjust it.

GMM control is assigned an error estimate and provided to the computing surveyor, the estimate can only be changed where warranted.  Some control is imported from adjacent townships to facilitate the merging of single township data sets during the regional adjustment.  This type of control is given an error estimate of .001, .001 and is called Merge Control.  For more information on control used during regional processing see page 13.  On page 11 is a list of the control reliabilities you'll find in the data files and their possible sources.

We can provide more information on particular control points if you need it.  We have a control data base (in ORACLE software) which contains the following information on each control point.

Point ID #,  Station Name,   Latitude & Longitude in NAD 27,

Elevation in feet (not all points),  NGS Order,   which USGS Quad it's on,  Source,  Township,   Range,   Section,   comments about what it is.

We can query on any of these fields to obtain data.

We also have a Plat and Special Survey data base (in ORACLE software) which contain the following information about Cadastral Plats.

Township,  Range,  BLM District,   BLM Resource Area,  Forest,

Other (i.e. Indian Reservation, National Park, etc.),

Surveyors,  Survey Year,  Survey Type,  Number of sections,  Comments

For Mineral Surveys, HES, etc  we also have county, some acreage.

Again, we can query on any of these fields.

Our SUMMARY Report includes all the above mentioned data for a particular township.  See the example on page 12.

KEY TO RELIABILITY OF CONTROL POINTS

RELIABILITY1	SOURCE2	DESCRIPTION

(1,1)	NGS	From National Geodetic Survey (NGS) tape, 1st order.

(3,3)	NGS	From NGS Tape, 2nd order.

(10,10)	USGS	Supplemental Files, or source stated in comments

(1,1)	GPSF	Forest Service Global Positioning System (GPS)

(1,1)	USFS	Forest Service

(1,1)	G027	Canyon County GPS 1990 (027 is Data Element Dictionary (DED) code for C.Cnty)

(1,1)	GPSU	From USGS GPS Project

(1,1)	GPSB	BLM GPS

(1,1)	GPSP	Private GPS, D.Evans & Associates work for City of Coeur d' Alene 1988.

(10,10)	FSC	FS Plat conventional tie moving control to a section corner

(10,10)	BLMC	BLM Plat conventional tie moving control to a section corner

(16,16)	GPSB	BLM GPS done with PATHFINDER, good to 16 Feet

(25,25)	DOPU	USGS Doppler From USGS GPS Project

(25,25)	NGS	From NGS Tape

(25,25)	USGS	Supplemental files, USGS-GPS Project, or other

(40,40)	MCI	Digitized points (found corners) off USGS 7-1/2' quads.

1	(10,10)  the average and maximum error, in feet, of the point.

2	Source is a code found in the control data base, not in the data files.  If you need more information on a control point we can provide it.

Summary Report For T. 0360N, R. 0010E, 21 Principal Meridian

Task: 2                                                   25-JUN-92

Complexity: 2

SURVEYOR             Year Survey       Lotting   Source ID   #Sec Comments

-------------------- ---- ------------ --------- ---------- ----- -------------

HOLMAN ET AL         1870 Original     Irregular

MAGEE                1873 Dependent    Irregular

BAKER                1882 Dependent    Irregular

BERDAN               1882 Dependent    Irregular

SANDOW               1882 Dependent    Irregular

SANDOW               1882 Original     Irregular

GLEAVES              1891 Dependent    Irregular

GLEAVES              1891 Original     Irregular

GLEAVES              1892 Dependent    Irregular

DENT                 1908 Dependent    Irregular

DENT                 1908 Original     Irregular

ENGLISH              1922 Dependent    Irregular

HIESTER ET AL        1938 Dependent    Irregular

SYDLIK ET AL         1957 Dependent    Irregular

HAMON ET AL          1983 Dependent    Irregular

Special     Surveys   Sections Number

-------- ---------- ---------- ------

Mineral           1          2 4547

Min Survey Lode Name

---------- ----------------

4547       EXCELSIOR PLACER

Quad Name                                ID #

---------------------------------------- --------

Big Bend                                 41121-A8

Chalk Mountain                           40121-H7

Roaring Creek                            40121-H8

Skunk Ridge                              41121-A7

Base Control Data in Township

Point      Latitude     Longitude Source          Attribute

------ ------------ ------------- --------------- --------------------

100100  405534.1387  1215435.8411 Dig 7.5 or Tie  Digtzd BLM method

100300  405719.0499  1215437.0445 Dig 7.5 or Tie  Digtzd BLM method

100440  405837.5472  1215437.8898 Dig 7.5 or Tie  Digtzd BLM method

100600  405958.0784  1215438.7778 Dig 7.5 or Tie  Digtzd BLM method

100700  410050.2440  1215438.5597 Dig 7.5 or Tie  Digtzd BLM method

200200  405624.9365  1215329.6398 Dig 7.5 or Tie  Digtzd BLM method

200300  405717.3398  1215329.6551 Dig 7.5 or Tie  Digtzd BLM method

200400  405812.0896  1215328.2236 Dig 7.5 or Tie  Digtzd BLM method

200640  410022.5311  1215329.0548 Dig 7.5 or Tie  Digtzd BLM method

300400  405811.9842  1215220.3723 Dig 7.5 or Tie  Digtzd BLM method

300700  410050.7404  1215219.3157 Dig 7.5 or Tie  Digtzd BLM method

400100  405532.9234  1215113.9848 Dig 7.5 or Tie  Digtzd BLM method

GMM REGIONAL ADJUSTMENT INFORMATION

The GMM software allows for the adjustment of blocks of townships.  For administrative purposes these blocks are given the designation Txxa, where T = Task, xx = number of the task, and a = block of tps. within task.  The number of townships in a block varies.

As of November 9, 1994, in order to maintain seamless edge match between blocks of townships the edges of blocks may be held rigid.  This procedure will be changed in the future.  As of July 16, 1995, edge match is accomplished by holding the edge of a buffer of townships fixed.  Where buffer townships are one tier of previously processed townships, adjacent to the region being adjusted.  The buffer townships are included in the adjustment, but the edge is held fixed with the adjacent townships that are also from the previous adjustment. See the diagram on page 14.  For example, block 1 is adjusted first, block 2 is adjusted with one tier of from block 1 included and a fixed boundary.  Block 3 is adjusted with one tier from block 1 (includes township that was adjusted with block 2) and a fixed boundary.  Block D is adjusted with one tier from blocks 1, 2, and 3 and 2 fixed boundaries.

Many of the files for a regional adjustment are the same as those for a single township adjustment.  These files do not exist for the regional adjustment: <block>.RAW, <block>.CON, <block>.SID, or any of the files relating to subdivision of sections.  This is because the GMM software assembles the data for a block of townships, from the single township files into block files.  After the regional adjustment is completed the GMM software is used to update the single township files with the regional adjustment data.  A <block>.DXF file may exist which includes all the townships in a block, but without any section subdivision.

Merge Control Points

Control points imported as Merge Control are thrown out during the merging process.  All other control points used in a regional adjustment, are the same control points as those used for the single township adjustment. Only the regionally adjusted coordinate are useful.

As of August 1, 1995, the following regions have protracted data included in them: TASK0, TASK1, TASK2, TASK3, TASK4 and TASK21.  Some of TASK21 and most of TASK22 does not include protracted data.  Task 23 does not include any protracted data.  For information on what areas a task covers, or what the data exists, contact the California GCDB Data Steward.

COMPARABLE FILES FOR PCCS AND GMM

PCCS	GMM

Bxxx N/A	none

Cxxx	xxx.CTL

Dxxx N/A	none

Fxxx N/A	none

Hxxx N/A	xxx.CON

Lxxx N/A	xxx.LX

Pxxx N/A	none

xxx.LL and xxx.QQ 	xxx.LL and xxx.QQ

Rxxx	xxx.RAW

xxx.SCR	xxx.DXF

Uxxx N/A	xxx.UTM

Xxxx	xxx.PGC

Zxxx N/A	xxx.SID

none	xxx.COR

none	xxx.GEO

none	xxx.SD

none	xxx.SUB

none	xxx.INT

none	xxx.TPR or xxx.INR

Any files not shown are for use of the software and are only useful to the GCDB. PCCS files marked N/A are not available.

PCCS	C36N01E

Geographic Coordinate File.  Could be useful outside GCDB.

TWP 0360  RNG 0010  PM Mnt Diablo  California(CA)        DATE 05/01/92

ORIGIN    405834.0000 1215135.0000 4000.000   0    0  2000.0000 5000.0000

100100    405534.1387 1215435.8411 4000.000  40   40  1789.6264 4724.2048

100300    405719.0499 1215437.0445 4000.000  40   40  1788.3196 4885.1090

100440    405837.5472 1215437.8898 4000.000  40   40  1787.4067 5005.5022

100600    405958.0784 1215438.7778 4000.000  40   40  1786.4466 5129.0154

100700    410050.2440 1215438.5597 4000.000  40   40  1786.7468 5209.0231

200200    405624.9365 1215329.6398 4000.000  40   40  1866.6672 4802.0777

200300    405717.3398 1215329.6551 4000.000  40   40  1866.6787 4882.4492

200400    405812.0896 1215328.2236 4000.000  40   40  1868.3734 4966.4193

200640    410022.5311 1215329.0548 4000.000  40   40  1867.4797 5166.4808

300400    405811.9842 1215220.3723 4000.000  40   40  1947.2530 4966.2377

400100    405532.9234 1215113.9848 4000.000  40   40  2024.4472 4722.2813

400500    405903.7140 1215110.7006 4000.000  40   40  2028.2428 5045.5741

573700    410049.7263 1214857.5151 4000.000  40   40  2182.9608 5208.2126

600198    405624.8651 1214856.4271 4000.000  40   40  2184.4296 4801.9903

643100    405533.0275 1214817.0702 4000.000  40   40  2230.2540 4722.5126

700100    405532.9005 1214747.1030 4000.000  40   40  2265.1153 4722.3414

700113    405541.8552 1214747.7486 4000.000 100  100  2264.3544 4736.0747

683700    410050.0031 1214749.3533 4000.000  40   40  2262.1487 5208.6854

693700    410057.7226 1214749.3687 4000.000  40   40  2262.1223 5220.5250

700700    410057.7276 1214744.2319 4000.000 100  100  2268.0898 5220.5370

140700    410050.3760 1215403.6100 4000.000  10   10  1827.3502 5209.2041

404700    410049.6960 1215107.4800 4000.000  10   10  2031.9718 5208.1218

|----|    |----------------------| |------|  ||   ||  |-----------------|

1                  2                 3      4    5           6

1 -	Point ID

2 -	NAD 27 Latitude/Longitude.  The decimal is located after the seconds.

3 -	Project elevation in feet.

4 -	Average Minimum Reliability in feet.

5 -	Maximum Reliability in feet.  (Control points have equal ave/max.)

6 -	(X,Y)  Cartesian tangent plane coordinates in chains unit.  Origin is at Point ID 400400 or near the center of the township which is assigned a false departure of 2000 chs. and latitude of 5000 chs.

Description:

Contains all the available control for a township.  Not all of the control will necessarily be used.  The control resides in the GCDB Control Data Base.

PCCS	R36N01E

Raw Data File.  Only useful to GCDB.

TWP 0360  RNG 0010  PM Mnt Diablo  California(CA)        DATE 05/01/92

999999

700100   700113   14.700  1     4400.  1908

700113   700120    5.360  1     5000.  1908

700120   700133   14.730  1     5000.  1908

700133   700140    5.330  1     5000.  1908

700140   700153   14.760  1     2500.  1908

700153   700160    5.345  1        0.  1908

700160   700193   14.730  1        0.  1908

700193   700200    5.375  1        0.  1908

700200   700213   14.700  1        0.  1892

700213   700220    5.300  1        0.  1892

700220   700240   20.000  1        0.  PROTRCTION

and then further down in the file....

700100   667100   11.966  4   892800.  1908

667100   660100    8.319  4   892800.  1908

660100   643100   14.535  4   892800.  1908

643100   640100    5.750  4   894200.  1908

640100   623100   15.455  4   900000.  1908

623100   620100    3.985  4   900000.  1908

620100   603100   17.220  4   900000.  1908

603100   600100    2.780  4   900000.  1908

600100   563100   16.685  4   900000.  1892

563100   543100   19.465  4   900000.  1892

|-------------|   |----|  |   |-----|  |--|

1             2    3      4       5

1 -	From and to station Point IDs.

2 -	Horizontal distance in chains.

3 -	Bearing quadrant ( 1=NE, 2=SE, 3=SW, 4=NW)

4 -	Bearing in degrees, minutes, and seconds. The decimal is located after the seconds.  The first example shows 5 minutes, the last shows 90 degrees.

5 -	Source Identifier number (SID)  Each data source, whether it is an official cadastral survey plat, state or local survey plat, deeds, etc., utilized in generating coordinates for the GCDB, will be assigned a unique SID number.

Description:

This is the raw data on which PCCS performs it computations.  It is abstracted from the survey records and entered into PCCS.

PCCS	T06N08E.SCR

Script File.  For use in AutoCAD.

layer

new

twp,sect,int,annot,points

color

magenta

twp

color

blue

sect

color

green

int

and further down in the file.....

layer

set

sect

pline

0.61534236000E+06,0.48512767700E+07

0.61533369000E+06,0.48516727400E+07

0.61532502000E+06,0.48520687000E+07

0.61531634000E+06,0.48524646700E+07

0.61530767000E+06,0.48528606400E+07

0.61530015000E+06,0.48532574500E+07

0.61529263000E+06,0.48536542700E+07

0.61528511000E+06,0.48540510800E+07

0.61527759000E+06,0.48544479000E+07

0.61527007000E+06,0.48548447100E+07

0.61526255000E+06,0.48552415200E+07

0.61525502000E+06,0.48556383400E+07

0.61524750000E+06,0.48560351500E+07

Description:

AutoCAD script files are created from PCCS Lxx files.  They can then be brought into AutoCAD to generate a drawing of the township.

PCCS	X36N01E

Geographic Coordinate File.  Only useful to GCDB.

TWP 36N   RNG 01E   PM Mnt Diablo       California(CA)   DATE 06/11/92

ORIGIN    405834.0000 1215135.0000 4000.000   0    0  2000.0000 5000.0000

100100    405534.1387 1215435.8411 4000.000  40   40  1789.6264 4724.2048

100120    405547.2527 1215435.9914 4000.000 154  363  1789.4630 4744.3178

100140    405600.3666 1215436.1420 4000.000 153  363  1789.2996 4764.4309

100160    405613.4806 1215436.2923 4000.000 154  363  1789.1362 4784.5439

100200    405626.5944 1215436.4428 4000.000 153  363  1788.9729 4804.6570

100220    405639.7084 1215436.5932 4000.000 153  363  1788.8095 4824.7700

100240    405652.8222 1215436.7437 4000.000 153  363  1788.6461 4844.8830

100260    405705.9361 1215436.8940 4000.000 153  363  1788.4829 4864.9960

100300    405719.0499 1215437.0445 4000.000  40   40  1788.3196 4885.1090

100320    405732.1328 1215437.1853 4000.000 154  363  1788.1674 4905.1745

100340    405745.2157 1215437.3263 4000.000 153  363  1788.0152 4925.2401

100360    405758.2986 1215437.4671 4000.000 154  363  1787.8630 4945.3056

100400    405811.3815 1215437.6080 4000.000 153  363  1787.7109 4965.3712

100420    405824.4644 1215437.7488 4000.000 153  363  1787.5588 4985.4367

100440    405837.5472 1215437.8898 4000.000  40   40  1787.4067 5005.5022

100460    405850.9691 1215438.0377 4000.000 153  363  1787.2467 5026.0878

100500    405904.3910 1215438.1858 4000.000 153  363  1787.0866 5046.6733

100520    405917.8128 1215438.3338 4000.000 153  363  1786.9265 5067.2588

100540    405931.2347 1215438.4818 4000.000 153  363  1786.7665 5087.8443

100560    405944.6565 1215438.6298 4000.000 153  363  1786.6065 5108.4298

100600    405958.0784 1215438.7778 4000.000  40   40  1786.4466 5129.0154

100620    410011.3044 1215438.9352 4000.000 154  363  1786.2755 5149.3006

100640    410024.5305 1215439.0927 4000.000  12   35  1786.1045 5169.5859

100660    410037.3873 1215438.8262 4000.000 153  363  1786.4256 5189.3045

100700    410050.2440 1215438.5597 4000.000  40   40  1786.7468 5209.0231

113100    405534.0717 1215424.7054 4000.000 153  363  1802.5806 4724.0949

120100    405534.0374 1215419.0198 4000.000 153  363  1809.1947 4724.0387

120120    405547.0734 1215419.1658 4000.000 154  363  1809.0352 4744.0321

120140    405600.1087 1215419.3119 4000.000 154  363  1808.8757 4764.0246

120160    405613.1429 1215419.4582 4000.000 154  363  1808.7159 4784.0154

120200    405626.1765 1215419.6046 4000.000 158  429  1808.5562 4804.0053

120220    405639.2876 1215419.7086 4000.000 158  429  1808.4456 4824.1139

120240    405652.3983 1215419.8128 4000.000 158  429  1808.3351 4844.2220

120260    405705.5083 1215419.9168 4000.000 158  429  1808.2246 4864.3290

120300    405718.6179 1215420.0209 4000.000 158  429  1808.1142 4884.4355

120320    405731.8552 1215420.1064 4000.000 154  363  1808.0254 4904.7378

|----|    |----------------------| |------| |-|  |-|  |-----------------|

1                  2                 3     4    5            6

1 -	Point ID

2 -	NAD 27 Latitude/Longitude.  The decimal is located after the seconds.

3 -	Project elevation in feet.

4 -	Average Minimum Reliability in feet.

5 -	Maximum Reliability in feet. (Control points have equal ave/max.)

6 -	(X,Y)  Cartesian tangent plane coordinates in chains unit.  Origin is at Point ID 400400 or a point near the center of the township which is assigned a false departure of 2000 chs. and latitude of 5000 chs.

Description:

Contains the above described values for every PCCS point in the township, including sixteenths and special surveys.

TABLE A

SOURCE AGENCY:  (3-6 characters) Generally, this will be a three letter abbreviation for the agency which created the document.  Below are some examples.  If other agencies are needed, contact the BLM.

BLM		Bureau of Land Management - 1946 to present

GLO		General Land Office - pre 1946

BOR		Bureau of Reclamation

CGS		Coast and Geodetic Survey

NGS		National Geodetic Survey

USC&GS	US Coast & Geological Survey

USCE		US Corp of Engineers

USGS		US Geological Survey

USFS		US Forest Office

NPS		National Park Services

DMA		Defense Mapping Agency

FAA 		Federal Aviation Administration

CALT		California Dept. of Transportation

NOAA		National Oceanic & Atmosphere Administration

LAWP		Los Angeles Water and Power

MWD		Metropolitan Water District

CAnn		Local Agency Codes for California from the Data Element Dictionary, Appendix A.

For countries other than the USA, use the first three letters.

TABLE B

SURVEY TYPE:  (1 character) This attribute describes the method or procedure used to determine the measurement value for a line.  It is possible that one .SID may relate to several of these survey types.  Select the one that best describes the record.

| A LOCATION SURVEY B RETRACEMENT SURVEY C CORRECTIVE RESURVEY D DEPENDENT RESURVEY E ACQUIRED LANDS SURVEY F OMITTED LANDS SURVEYS I INDEPENDENT RESURVEY J OTHER |  | K SUPPLEMENTAL PLAT M INTERNATIONAL BOUNDARY N NO SURVEY PLAT, MAP ONLY O ORIGINAL SURVEY P PROTRACTION DIAGRAM Q EXCHANGE SURVEY R SEGREGATION SURVEY Z UNKNOWN |
| --- | --- | --- |

GMM FILES	T06SR20E.CON

Geographic Coordinate File.  Only useful to GCDB.

TWP 0060  RNG 0200  PM Mnt Diablo  California(CA)        DATE 11/29/93

ORIGIN    382203.0000 1194647.0000 4000.000   0    0  2000.0000 5000.0000

100600    382307.7693 1194931.8103 7000.000  40   40

200640    382332.7680 1194828.7847 7000.000  40   40

240700    382400.8530 1194755.8351 7000.000  40   40

400240    382018.8930 1194629.4619 7000.000  40   40

540100    381904.6360 1194447.6905 7000.000  40   40

673700    382400.8530 1194308.4194 7000.000 100  100

700100    381902.9946 1194311.0783 7000.000 100  100

700700    382400.8530 1194303.3975 7000.000 100  100

|----|    |----------------------| |------|  |-----|  |-----------------|

1                  2                 3        4               5

1 -	Point ID

2 -	NAD 27 Latitude/Longitude.  The decimal is located after the seconds.

3 -	Project elevation in feet.

4 -	Error estimates in feet.

5 -	These are meaningless values.

Description:

This file contains all the control used in the township.

GMM	T06SR20E.CTL

Geographic Coordinate File.  Only useful to GCDB.

TWP 0060  RNG 0200  PM Mnt Diablo  California(CA)        DATE 11/29/93

ORIGIN    382203.0000 1194647.0000 4000.000   0    0  2000.0000 5000.0000

100100    381903.0022 1194947.6793 4000.000 283  283  1781.7713 4724.1200

100100    381903.0090 1194948.0308 4000.000 100  100  1781.3468 4724.1306

100600    382307.7693 1194931.8103 4000.000  40   40  1801.1243 5099.3422

100700    382359.9451 1194931.8103 4000.000 100  100  1801.1640 5179.3292

117100    381902.8935 1194930.9747 4000.000  57   57  1801.9475 4723.9429

117100    381902.9410 1194931.5416 4000.000 100  100  1801.2628 4724.0160

200640    382332.7680 1194828.7847 4000.000  40   40  1877.1887 5137.6354

240700    382400.8530 1194755.8351 4000.000  40   40  1916.9539 5180.6803

400240    382018.8930 1194629.4619 4000.000  40   40  2021.1768 4840.4027

540100    381904.6360 1194447.6905 4000.000  40   40  2144.1039 4726.5912

673700    382400.8530 1194308.4194 4000.000 100  100  2263.7064 5180.7585

700100    381902.9946 1194311.0783 4000.000 100  100  2260.7952 4724.1337

700700    382400.8530 1194303.3975 4000.000 100  100  2269.7651 5180.7625

|----|    |----------------------| |------|  |-----|  |-----------------|

1                  2                3         4              5

1 -	Point ID

2 -	NAD 27 Latitude/Longitude.  The decimal is located after the seconds.

3 -	Project elevation in feet.

4 -	Error estimates in feet.

5 -	(X,Y)  Cartesian tangent plane coordinates in chains unit.  Origin is assigned a false departure of 2000 chs. and latitude of 5000 chs.

Description:

This is a backup control file.  It contains all the control available in the township but does not include transferred points.

GMM	T06SR20E.COR

Coordinate File.  Useful to State Plane Coordinate users.

100100             2622610.193    244477.950

100200             2622538.727    249720.785

100300             2622665.686    254734.966

100320             2622710.389    255952.257

100340             2622755.095    257169.537

100363             2622799.793    258386.817

100383             2622844.492    259604.098

100400             2622863.104    260523.291

100403             2622860.824    260850.571

100423             2622922.320    262200.202

100443             2622983.814    263549.823

100463             2623045.306    264899.445

100500             2623043.731    265271.658

100513             2623059.312    266086.242

100540             2623094.754    267150.628

100560             2623130.200    268215.014

100600             2623165.641    269279.390

100640             2623044.672    271936.176

100660             2622998.748    273259.782

100700             2622952.826    274583.377

|----|              |----------------------|

1                           2

1 -	Point ID.

2 -	State Plane Coordinates (x,y) easting & northing in feet and NAD 27.

Description:

These are the State Plane coordinates for the township.  GMM does all its computations in SPCs and then converts them into UTMs and Lat/Long.

GMM	T06SR20E.DXF

Line Data File for CAD (Computer Aided Design) packages and other software.  For CAD users.

0

SECTION

2

HEADER

9

$ACADVER

1

AC1004

9

$INSBASE

10

0.0

and then to the end of the file.....

1

N90- 0W

50

0.13

0

ENDSEC

0

EOF

Description:

This drawing interchange file can be brought into many software packages to produce a drawing of the township.

GMM	T06SR20E.GEO

Geographic Coordinate File.  For those who need only latitude & longitude of points.

100100              38-19-  3.17160        119-49- 47.46953

100200              38-19- 55.00114        119-49- 46.79509

100300              38-20- 44.52412        119-49- 43.69914

100320              38-20- 56.54346        119-49- 42.77309

100340              38-21-  8.56279        119-49- 41.84701

100363              38-21- 20.58211        119-49- 40.92089

100383              38-21- 32.60141        119-49- 39.99472

100400              38-21- 41.68105        119-49- 39.48527

100403              38-21- 44.91592        119-49- 39.41571

100423              38-21- 58.23917        119-49- 38.23878

100443              38-22- 11.56242        119-49- 37.06179

100463              38-22- 24.88563        119-49- 35.88475

100500              38-22- 28.56438        119-49- 35.79272

100513              38-22- 36.61094        119-49- 35.35251

100540              38-22- 47.12141        119-49- 34.58787

100560              38-22- 57.63186        119-49- 33.82319

100600              38-23-  8.14230        119-49- 33.05850

100640              38-23- 34.42685        119-49- 33.77916

100660              38-23- 47.51830        119-49- 33.95818

100700              38-24-   .60973        119-49- 34.13721

|----|              |-------------|        |--------------|

1                        2                       3

1 -	Point ID

2 -	NAD 27 Latitude

3 -	NAD 27 Longitude

Description:

Latitude and Longitude in NAD 27 of the points.

GMM	T06SR20E.LX

Geographic Coordinate Line File.  For most Users.

T06NR20E             MDM                  CA

ORIGIN    382203.0000 1194647.0000                    257142.504250042.92

100100 381903.1716 1194947.4695  7000.00  69   83  1 1 2  252591.89  4244632.03

100120 381916.1290 1194947.3009  7000.00  72  237  1 1 3  252608.23  4245031.38

100140 381929.0864 1194947.1323  7000.00  72  237  1 1 3  252624.57  4245430.73

100160 381942.0438 1194946.9637  7000.00  72  237  1 1 3  252640.91  4245830.08

100200 381955.0011 1194946.7951  7000.00  72  237  1 1 3  252657.25  4246229.43

100220 382007.3819 1194946.0211  7000.00  75  237  1 1 3  252687.75  4246610.55

100240 382019.7626 1194945.2471  7000.00  75  237  1 1 3  252718.25  4246991.67

100260 382032.1434 1194944.4731  7000.00  75  237  1 1 3  252748.74  4247372.79

100300 382044.5241 1194943.6991  7000.00  75  109  1 1 3  252779.24  4247753.91

100320 382056.5435 1194942.7731  7000.00 882  378  1 1 3  252813.08  4248123.78

100340 382108.5628 1194941.8470  7000.00 450 1789  1 1 3  252846.92  4248493.64

100363 382120.5821 1194940.9209  7000.00 436 1790  1 1 4  252880.77  4248863.51

100383 382132.6014 1194939.9947  7000.00 727  324  2 1 2  252914.61  4249233.37

100400 382141.6810 1194939.4853  7000.00 224  148  2 1 3  252935.56  4249512.92

100403 382144.9159 1194939.4157  7000.00 224  163  2 1 4  252940.31  4249612.60

100463 382224.8856 1194935.8847  7000.00 225  153  3 1 2  253063.79  4250842.24

100500 382228.5644 1194935.7927  7000.00 225  131  3 1 3  253069.50  4250955.59

100513 382236.6109 1194935.3525  7000.00 687  278  3 1 4  253087.78  4251203.33

100540 382247.1214 1194934.5879  7000.00 932  353  4 1 2  253116.27  4251526.80

100560 382257.6319 1194933.8232  7000.00 846  318  4 1 3  253144.76  4251850.27

100600 382308.1423 1194933.0585  7000.00  95   83  4 1 3  253173.25  4252173.74

100620 382321.2846 1194933.4188  7000.00  96  339  4 1 3  253176.93  4252579.19

100640 382334.4268 1194933.7792  7000.00  96  339  4 1 3  253180.60  4252984.63

100660 382347.5183 1194933.9582  7000.00  96  271  4 1 3  253188.64  4253388.38

100700 382400.6097 1194934.1372  7000.00  96   72  4 1 4  253196.67  4253792.12

|----| |----------------------|  |-----|  |-----|  | | |  |------------------|

1              2                 3        4     5 6 7           8

1 -	Point ID

2 -	NAD 27 Latitude/Longitude.  The decimal is located after the seconds.

3 -	Project elevation in feet.

4 -	Error error ellipse axis rounded to the nearest foot.

5 -	Line number code - see Index diagram on page 13.

6 -	Line type code - 0 = solid (continuous), 2 = dashed, 3 = centerline

7 -	Line draw code - 1 = skip, 2 = pen down, 3 = draw, 4 = pen up

8 -	Universal Transverse Mercator (UTM) coordinates in meters.  Cartesian format - x,y.

Description:

This is a graphics line file.  It can be imported into a GIS.  Usually used to produce graphic displays of the data

xxx.LX (GMM) FILE INDEX DIAGRAM

This is the sequence of line information as it shows up in the Lxx file.  It goes from South to North and then West to East.

GMM	T06SR20E.PGC

Geographic Coordinate File.  Only useful to GCDB.

T06NR20E             MDM                  CA

ORIGIN    382203.0000 1194647.0000 7000.000   0    0  2000.0000 5000.0000

100100    381903.1716 1194947.4695 7000.000  69   83

100200    381955.0011 1194946.7951 7000.000  72  237

100300    382044.5241 1194943.6991 7000.000  75  109

100320    382056.5435 1194942.7731 7000.000 882  378

100340    382108.5628 1194941.8470 7000.000 450 1789

100363    382120.5821 1194940.9209 7000.000 436 1790

100383    382132.6014 1194939.9947 7000.000 727  324

100400    382141.6810 1194939.4853 7000.000 224  148

100403    382144.9159 1194939.4157 7000.000 224  163

100423    382158.2392 1194938.2388 7000.000 224  273

100443    382211.5624 1194937.0618 7000.000 224  272

100463    382224.8856 1194935.8847 7000.000 225  153

100500    382228.5644 1194935.7927 7000.000 225  131

100513    382236.6109 1194935.3525 7000.000 687  278

100540    382247.1214 1194934.5879 7000.000 932  353

100560    382257.6319 1194933.8232 7000.000 846  318

100600    382308.1423 1194933.0585 7000.000  95   83

100640    382334.4268 1194933.7792 7000.000  96  339

100660    382347.5183 1194933.9582 7000.000  96  271

100700    382400.6097 1194934.1372 7000.000  96   72

|----|    |----------------------| |------|  |-----|  |-----------------|

1                  2                 3        4               5

1 -	Point ID

2 -	NAD 27 Latitude/Longitude.  The decimal is located after the seconds.

3 -	Project elevation in feet.

4 -	Error error ellipse axis rounded to the nearest foot.

5 -	(X,Y)  Cartesian tangent plane coordinates in chains unit.  Origin is assigned a false departure of 2000 chs. and latitude of 5000 chs.

Description:

This is a geographic coordinate file used by GMM programs.

GMM	T06SR20E.RAW

Raw Data File.  Only useful to GCDB.

T06SR20E             MDM                 CA

999999

100100   100200   80.000  1         .0 1879WB

100200   100300   80.000  1         .0 1879WB

100300   100320   20.000  1         .0 A1879WB

100320   100340   20.000  1         .0 A1879WB

100340   100363   20.000  1         .0 A1879WB

100363   100383   20.000  1         .0 A1879WB

100383   100400   15.059  1         .0 A1879WB

100400   100403    4.941  1         .0 1879WB

and a little further down...

700100   657100   19.300  3   900000.0 1874SB

657100   637100   20.150  3   900000.0 1874SB

637100   617100   20.150  3   900000.0 1874SB

617100   600100   20.400  3   900000.0 1874SB

600100   577100     .091  3   900000.0 1874SB

577100   557100   20.492  3   900000.0 1874SB

557100   540100   19.417  3   900000.0 1874SB

540100   537100    1.075  3   890725.0 26RS084

and a little further down.....

240700   200700   40.000  3   900000.0 PROT122

200700   100700   80.000  3   900000.0 PROT122

400240   300240   79.000  4   874200.0 1981

200640   240640   40.000  1   900000.0 1879

240640   240700   40.000  1         .0 1879

999998

|-------------|   |----|  |   |------| |------|

1            2     3       4        5

1 -	From and to Point IDs.

2 -	Distance, in chains, between the points.

3 -	Bearing quadrant ( 1=NE, 2=SE, 3=SW, 4=NW)

4 -	Bearing in degrees, minutes, and seconds.  The decimal point is located after the seconds.

5 -	Source Identifier number (SID).  Each data source, whether it is an official cadastral survey plat, state or local survey plat, deeds, etc., utilized in generating coordinates for the GCDB, will be assigned a unique SID number.  A SID with a letter prefix has augmented error estimates.  A SID with a letter suffix denotes that there is more than one survey for the same year.  A SID with boundary designations will have a NB, EB, SB or WB for a suffix.

Description:

This is the raw data on which GMM performs it computations.  It is abstracted from the survey records and entered into GMM.

GMM	T06SR20E.SID

Information File.  Only useful to GCDB.

S26RS084              .100   100.0    11.0   40.000   40.000

C CA109 1982 D

S1981                 .100   100.0    11.0   40.000   40.000

C BLM 13-DEC-1982 D JEPSON, WOODROW L.

S1928                 .100   333.3    31.0   40.000   40.000

C GLO 02-MAR-1932 D AVERILL, DUPREE R.

S1879                 .100 18000.0  4500.0   40.000   40.000

C GLO 21-JAN-1880 O ANDERSON, J.M.

S1874SB               .100  1000.0   300.0   40.000   40.000

C GLO 21-JAN-1880 O BENSON & GLOVER

SPROT122              .100   100.0  6300.0   40.000   40.000

C BLM 27-JAN-1970 P

S1879WB               .100  1562.5 18000.0   40.000   40.000

C GLO 21-JAN-1880 O ANDERSON, J.M.

S1879NB               .100  3125.0  3000.0   40.000   40.000

C GLO 21-JAN-1880 O ANDERSON, J.M.

SA1879WB              .100300000.0 28200.0   40.000   40.000

C GLO 21-JAN-1880 O ANDERSON, J.M.

SA1879                .100  1562.5 12000.0   40.000   40.000

C GLO 21-JAN-1880 O ANDERSON, J.M.

S1879       -	SID code (Year the survey was conducted if BLM/GLO)

0.100       -	Constant error estimate.

100.0       -	Distance error estimate in PPM (parts per million).

11.0       -	Error estimate in seconds.

40.000      -	These 2 fields are not used.  The numbers are irrelevant.

C           -	Comment line.

GLO         -	Agency source code, See Table A on page 20.

10-OCT-1916 -	Date of approval of the SURVEY, put in by data abstractor.

O          -	Code for type of survey.  See Table B on page 20.

Bardsley,HG -	Name of Surveyor.

Description:

This file contains information about the surveys used for this township.  It shows the SID number, survey source, date of survey, surveyor and some reliability values.

GMM	T06SR20E.UTM

Geographic Coordinate File.  Useful to UTM users.

TWP 03S   RNG 39E   PM   Boise               Idaho(ID)   DATE 92/12/03

ORIGIN    430900.0000 1115300.0000  6107.00   0    0  428174.124777635.76

700100    430627.6337 1114932.5922  6107.00  22   22  432812.504772887.89

700117    430638.0782 1114932.5901  6107.00  22   21  432815.734773210.07

700120    430640.6688 1114932.5900  6107.00  22   21  432816.514773289.98

700137    430651.1165 1114932.5878  6107.00  21   21  432819.744773612.26

700140    430653.7038 1114932.5877  6107.00  21   21  432820.534773692.08

700157    430704.1548 1114932.5856  6107.00  21   21  432823.754774014.46

700160    430706.7389 1114932.5854  6107.00  21   21  432824.544774094.17

700197    430717.1931 1114932.5833  6107.00  20   20  432827.764774416.65

700200    430719.7739 1114932.5831  6107.00  20   20  432828.554774496.27

and further down in the file.....

100640    431114.6980 1115634.3899  6107.00   0    0  423378.514781843.65

100660    431127.7231 1115634.3490  6107.00   0    0  423383.964782245.44

100700    431144.1412 1115634.2974  6107.00   0    0  423390.834782751.89

640100    430627.6855 1115008.1917  6107.00  23   23  432007.884772897.46

540100    430627.7967 1115119.3741  6107.00  23   23  430399.024772917.11

440100    430627.9004 1115230.5835  6107.00  22   22  428789.554772936.92

340100    430627.9789 1115341.8584  6107.00  20   20  427178.594772956.35

240100    430628.0397 1115453.1879  6107.00  18   18  425566.394772975.63

140100    430628.1010 1115604.5570  6107.00   7    7  423953.304772995.31

120100    430628.1248 1115622.3762  6107.00   4    5  423550.554773000.55

|----|    |----------------------|  |-----|  |-----|  |-------||--------|

1                  2                 3        4         5         6

1 -	Point ID

2 -	NAD 27 Latitude/Longitude.  The decimal is located after the seconds.

3 -	Project elevation in feet.

4 -	Error error ellipse axis rounded to the nearest foot.

5 -	Universal Transverse Mercator (UTM) coordinates in meters, x value.

6 -	UTMs in meters, y value.

Description:

This file contains UTM coordinates for all the points in the township.

APPENDIX A - GMM Glossary

Observation - a fancy word for measurement

Simultaneous Solution - this means all coordinates are being solved for in one solution;  In the compass rule process you must adjust one traverse into another traverse which is held as "fixed".  This is not correct since the fixed traverse contains error.

System of Equations - in a least squares adjustment you solve an "n x n" system of equations each iteration where n equals the number of unknown quantities.  In a 20 station traverse there are 40 unknowns (20 N, 20 E coordinates).  This means a 40 equations, 40 unknowns system of equations must be solved.  Even for a computer this is a slow process.

Bandwidth Optimization - There are many ways to speed up the solution of a system of equations and reduce the number of terms in the equations. Some methods other than bandwidth optimization include column profile minimization, Helmert blocking, and recursive partitioning.  If a computer program does not use one of these methods the results will be produced very slowly.  LSAQ uses a bandwidth optimization routine which has been extensively modified for better performance.  For most survey networks the bandwidth will probably range from 5-30% of the total number of stations.  This process enables more efficient solution of least squares problems, and especially allows "big" problems to be solved on a personal computer

Solution Convergence - the last iteration has insignificant updates and thus the solution terminates.

Solution Divergence - blunders or poor initial approximations will cause updates to grow as iterations proceed;  This indicates something is wrong with the data, and it needs to be corrected.

Number of measurements - equals # of distances + number of angles + number of azimuths + number of control coordinates

Degrees of freedom - number of measurements minus number of unknowns; or the number of measurements beyond what is necessary to uniquely define coordinates for each station

Residual - the difference between a measurement and its computed quantity based on coordinates; It is how much the measurement adjusted.

Error estimate - A surveyor's error estimates of measurements assigns appropriate weighting of measurements in a least squares adjustment.  An angle with an error estimate of 2 seconds will be treated as more weighted (stronger, less chance of adjustment) than an angle with an error estimate of 10 seconds.  This does not mean the angle with the smaller error estimate will always get a smaller adjustment since geometric constraints ( such as sum of angles in a closed figure) also play a major role in dictating amount of adjustment.  A distance error estimate is usually modeled by a constant plus a ppm addition to account for larger errors generally occurring in longer lines.  An angle or azimuth error estimate is a function of the instrument's least count, the number of repetitions, the instrument operator's abilities, and the prevailing environmental conditions.  Experience with instrumentation and the least squares adjustment will allow the surveyor to develop confidence in error estimation.  Error estimating allows the simultaneous analysis of different measurement types (distances, angles, azimuths, control coordinates).

RMS error - root mean square error - it is the average of a series of residuals in which the sign of the residual is eliminated through summing squared residuals, dividing by the number of that type of measurement, then computed that value's square root.

Residual vs. error estimate - These quantities should be of approximately the same magnitude.  Since measurements contain random error a plot of residuals should look like the "bell-shaped" curve from statistics which centers about zero.  If residuals tend to be predominantly of one sign this means systematic error may exist.  This would occur if your survey tied into two precise control coordinates and your EDM was measuring systematically long.  All adjusted distances would be shorter than their measured values.  It could also occur if horizontal angles were only measured in the direct position and a large horizontal collimation error existed.  Residuals which are larger than three times their respective error estimate are generally considered suspect.

Standard error of unit weight - This is a number which tells you how well it appears you that you are estimating your measurement errors.  It is generated by the summing the squares of all residuals divided by their error estimates.  That quantity is divided by the degrees of freedom and the square root is taken.  If a residual and error estimate are of the same magnitude note that the residual divided by the error estimate will generally produce a number close to one.  The standard error of unit weight is a number that evaluates all residuals and corresponding error estimates.  If the standard error of unit weight is near one (0.7-2.5) you are estimating your errors well.  Uncorrected systematic errors, blunders, or generally poor measurements will result in larger residuals and thus a large standard error of unit weight. If you are pessimistic in error estimation or you have very few redundant measurements a very small standard error of unit weight will result.

Standard error of adjusted coordinates - these are the least squares error estimates of adjusting N,E coordinates.  They are a function of proximity to existing control points.  The statistical significance of these quantities is that if you went and made the same measurements with the same instrument using the same procedures, you would have a one sigma (68.3% confidence) chance of being within plus or minus the standard error of the first solution's coordinate.  It has nothing to do with additional traverse legs and readjustment, comparing to someone else's coordinates, or evaluating retracement evidence.

Error ellipses - It should be apparent that the reliability of a traverse point's position will not usually be the same in all directions.  The position is generally stronger in the traverse direction, and weakest away from the traverse directions.  The error region is an ellipse, defined by a radius (semi-major axis) of maximum error (SU), radius (semi-minor axis) of minimum error (SV), and the angle from north (positive clockwise) of the direction of maximum error (T).  Since an error ellipse is two-dimensional, the one sigma error ellipse only denotes 35% confidence (roughly 68.3% squared).  The same statistical significance reasoning for coordinate standard errors applies to error ellipses - it is an internal evaluation of your data and does not relate to external information such as other surveys or existing coordinates.

Robustness - This is a method of using least squares as a filtering mechanism for detection of blunders.  Robustness averages the absolute value of a measurement's residual with its error estimate, and that average becomes the new error estimate in a readjustment.  The measurements with large residuals get reassigned larger error estimates, and vice-versa.  This enables the adjustment to be filtered to the suspect measurement.  The success of robustness in blunder detection is a function of size of the blunder, number of blunders, and the geometry and redundancy of the traverse network.

NAD 27 - North American Datum of 1927 - a datum based on the Clarke Ellipsoid of 1866, and fixed position and orientation at Meade's Ranch in Kansas.  Based upon this information latitudes and longitudes were calculated for all National Geodetic Survey control points based primarily on triangulation.  The calculation involved a least squares adjustment by hand calculations!

NAD 83 - North American Datum of 1983 - a datum based on the GRS 80 Ellipsoid, and fixed position and orientation at the center of the earth.  The measurements used in NAD 27, and additional measurements made by the National Geodetic Survey subsequent to 1927, were subjected to a least squares adjustment - this time using a computer.  This results in a different latitude and longitude for a station when compared to its NAD 27 values, with the difference often amounting to hundreds of feet.

State Plane Coordinates - projections which uniquely relates a geodetic position (latitude, longitude) to a plane coordinate pair (N,E).  The relation is truly a one-to-one correspondence; for a unique state plane coordinate pair there is only one latitude, longitude pair, and vice-versa.  The two type of projections that exist are Lambert - a conic projection for states elongated east-west, and Mercator - a cylindrical projection for states elongated north-south.  The size of a zone was limited by defining a a state plane distance will not differ from its geodetic counterpart by 1/10000 of the distance.  Thus larger states are covered by more than zone.

NAD 27 state plane coordinates - These are based on zone constants which include false northings and eastings so that negative coordinates do not result.  The published units are U.S. Survey Feet.

NAD 83 state plane coordinates - These are based on different zone constants than NAD 27.  The most notable change is that different values were assigned for false northings and eastings, and the coordinates published by NGS are in meters instead of U.S. Survey Feet.  Even when converted to feet, NAD 83 coordinates look dramatically different than the NAD 27 coordinates for the same point because the false northings and eastings are different.

# Footnotes

Townships with 26 or more Special Surveys may not have Special Surveys included, but will have the PLSS rectangular surveys included.

Chains are a unit of measure used by surveyors.  A regular section is 80 chains square.  One chain equals 66 feet.  One hundred links equal one chain.