RFJ 1241 Specifications

Laser diode, 32 W – Specifications:  Collimated laser diode.  Power Output:  32 W continuous or more.  Wavelength 0.790+/-0.003 Micrometer.  Beam Size:  11.0 by 11.0 mm full width at half maximum or less.  Beam Divergence: 3.0 by 3.0 mrad full width at half maximum or less.

Polarization:  Transverse magnetic