Section 9

# Uploading Data Into GPS Devices

Uploading Waypoints into Garmin GPS using ArcView 3.X……………………….2

Loading MapSource Data into Garmin GPS…………………………………….…..4

Uploading Waypoints into PLGR using Rockwell MPS…………………………….6

Uploading Waypoints into PLGR using Wellston Track Plan…………………...…8

Uploading Waypoints into Garmin using ArcView 3.X

In this exercise you will learn how to upload waypoints into your Garmin GPS device from ArcView 3.2 using a shapefile.    This is easily accomplished using the DNR Garmin extension.

- Open ArcView and open the uploadex.apr file.

- Connect your Garmin GPS using the Garmin to PC cable.

- Turn on GPS device and ensure the transfer format is Grmn/Grmn.

Warning:  Any existing waypoints with the same number will be overwritten.

- From the DNR Garmin menu, select Open Garmin GPS.  Your device will be detected and you will be informed of the status in the lower left portion of the dialog.

- From the File menu in the ArcView – Garmin interface, choose Load…Waypoints From…ArcView Theme.

- Select WP as the IDENT field.  Click OK.

- Select Codes for the COMMENT field.  Click OK.

NOTE:  This shapefile used in this sample contain the points used in the TEC7132 navigation exercise.

- You will be notified the number of points which have been loaded into the program.  You now need to transfer to your GPS device.  From the Waypoint menu, select Upload.   The status of your upload is presented in the lower center of the dialog.

Loading MapSource Data into Garmin GPS

Several Garmin GPS devices, including the GPS III Plus, allow you to upload base map data to be displayed on your Map Page.   These data are provided on the Garmin MapSource CD ROM products.  In this exercise, you will upload a digital topographic map of the NCTC campus from the MapSource – United States TOPO CD.    These maps are comparable to the United States U.S. Geological Survey’s (USGS) 1:100,000 scale paper maps.

NOTE: You cannot load USGS products such as Digital Raster Graphics (DRGs) or Digital Orthophotographic Quarter Quadrangles (DOQQs) into any Garmin GPS device.

- Use your PC Interface cable to connect your Garmin GPS device to your  computer’s COM port.

- Insert the Eastern United States CD into your CD-ROM drive.

- Double click on the MapSource  icon to open the program.

- Turn your GPS device on.

NOTE:  Since map data transfers can take several minutes, check the battery levels on your GPS device before uploading base map data.

- From the View menu, select Region and choose US TOPO – East.

- From the View menu, click Find.  Type Shepherdstown in the text box and click  Center on City.

- From the View menu, select Zoom Scale and choose 7 mi.

- Click the Map Tool  icon.   Now move the cursor over the map and notice the yellow lines appear around the boundary of the map set.  Click on the city of Shepherdstown to select the map set for this area.  Notice the area inside the boundary now is selected (highlighted in pink).  The topo map for this area  is named  FREDERICK., MD-VA-WV (WEST– NW).  The name appears in the window to the left of the map.

- You are now ready to transfer this map set to your GPS device.  From the File menu, click Save to Device.

- The Save to Device dialog appears.  Ensure the correct COM port is selected.  You can leave the baud rate setting at 115200.  Now, in the What to Save section check Maps.   When you are ready to begin transferring this map set to your GPS device, click Save.

11.	This process takes several minutes.  You will be notified when finished.

Uploading Waypoints into PLGR using Rockwell MPS

Instead of manually entering waypoints into the PLGR, you can easily transfer waypoints from a comma delimited text file.   This is especially useful if you have numerous points to enter.  In this exercise we will transfer several waypoints to the PLGR using Rockwell’s Mission Planning software (MPS).

- Use Notepad to create a text file in the same format as a waypoint file downloaded using Hyperterminal.  This is a comma delimited text file.

For UTM coordinates:

You must include values for fields 1,2,5,6,7,8,11 (see Appendix A for description of these fields) .

NP,WP001,   ,UTM/UPS ,18S,258493,4374429,NAR  ,,,WGD,,,,

NP,WP002,    ,UTM/UPS ,18S,258448,4374455,NAR  ,,,WGD,,,,

NP,WP003,   ,UTM/UPS ,18S,258387,4374517,NAR  ,,,WGD,,,,

NP,WP004,   ,UTM/UPS ,18S,258001,4374454,NAR  ,,,WGD,,,,

NP,WP005,   ,UTM/UPS ,18S,258211,4374778,NAR  ,,,WGD,,,,

For Lat/Lon coordinates:

NP,WP001,  ,L/L-dms ,,39.4855807,-77.8081154,NAR  ,,,WGD,0.0,,,

NP,WP002,  ,L/L-dms ,,39.4858045,-77.8086467,NAR  ,,,WGD,0.0,,,

NP,WP003,  ,L/L-dms ,,39.4863462,-77.8093775,NAR  ,,,WGD,0.0,,,

NP,WP004,   ,L/L-dms ,,39.4856678,-77.8138386,NAR  ,,,WGD,0.0,,,

NP,WP005,   ,L/L-dms ,,39.4886436,-77.8115170,NAR  ,,,WGD,0.0,,,

You must include values for fields 1,2,6,7,8,11 (see Intro course book for description of these fields) .

Ensure the file you create is saved with the WAY extension.

NOTE:  For this exercise, the file is already created for you. It is stored in the d:\tec7133\waypoints folder.   The file is named:   plgrpnts.way

- Put the file containing the waypoints into the c:\mps\libray folder.

- Ensure PLGR I/O format is set to Standard.

- Connect your PLGR to COM 1 port on your PC.  Turn PLGR on.

- Using Windows Explorer, navigate to the c:\mps folder and double click on the mps.exe file to launch the program.

TIP:  You can easily create a shortcut on your desktop to launch the program.

- At the top right of the next screen, ensure RCVR Connected appears.  If not, check your cable connection and ensure the PLGR is on.

- Use arrow keys on keyboard and select F3/Mission.  Hit ENTER.

- Load will be selected, hit ENTER again.

- Arrow down to select Waypoint Data, hit ENTER.

- Load will be selected, hit ENTER again.

- Arrow over to select the file, in this case PLGRPNTS.  Hit ENTER to load this file.

- This step is optional.  If you wish to view your points before sending, arrow over to F3/NAV and hit ENTER.  F1/Waypoint should be selected, hit ENTER again to display the PLGRPNTS file on the screen.  Hit the ESC key twice to get back to the Perform Mission Planning screen.

- Arrow over to select F7/Send.  Hit ENTER.

- Arrow down to Navigation Data.  Hit ENTER.

- Arrow down to End Waypoint, type 5 and hit ENTER.

- Initiate Transfer will now be selected.  Hit ENTER.

- Hit ESC twice.  Use arrow to select QUIT and hit ENTER to close the program.

Uploading Waypoints into PLGR using Wellston Track Plan

Instead of manually entering waypoints into the PLGR, you can easily transfer waypoints from a previously downloaded PLGR file.   This is especially useful if you have to navigate back to several points.  In this exercise we will transfer several waypoints to the PLGR using Wellston Track Plan software.

- You must have an ASCII delimited text file that was downloaded previously from a PLGR.   The file for this exercise is located in the d:\tec7133\waypoints folder.  The filename is:  rawplgr.txt

- Ensure PLGR I/O format is set to Standard.

- Connect your PLGR to COM 1 port on your PC.  Turn PLGR on.

- Launch  the Wellston Track Plan MPS for PLGR+96 software.

- Click on the Waypoints menu.

- Put your mouse over the blue line near the top of the window.  A new set of button icons appear.   From the File menu, select Import and choose  ASCII-OUT (*.txt) File.   Navigate to the location of the text file containing the waypoint information (d:\tec7133\waypoints).  Select the rawplgr.txt file and click OK.

- From the File menu, choose Save to Disk.  Save this file in the d:\tec7133\waypoints folder with the name:   rawplgr.wpf

Click OK.

- Click the Delete All button at the bottom of the window.

- Move up to the blue line and click on the Load Waypoints from Disk  button.  Choose the file you just created in step 7 and then click  OK.

- Move up to the blue line and click on the Next Window  button.

- Click on the top line of the waypoints list on Waypoints Database section and hold down the Shift key on you keyboard.  Now while holding the Shift key, click on the last record you wish to upload to the PLGR.   Once all the records you wish to transfer are selected, click in the empty cell of the first record in the RCVR Waypoints section. All waypoints selected from the Waypoints Database section now appear now in the RCVR Waypoints section.

- Move up to the blue line and click on the Next Window  button.

- Move up to the blue line  and click on the Upload Waypoints/Routes to RCVR  button.

- Put your mouse in the Ending WPT: section and select 5, your screen should match the example below.   Click OK when finished.

- Your points will be transferred to the PLGR.  A “Xfer OK” message will appear next to the waypoints in the RCVR Waypoints section.

- Exit out of program by moving up to the blue line and clicking the previous window arrow all the way out to the main progarm.   Exit out by clicking the File menu and choosing Exit.