Specifications for PR RCF.1193

The following specifications must be met at a minimum:

- The item is a tunable laser.

- The tuning range must span from 1510 to 1570 nanometers.

- The laser must have a FC/PC or FC/APC connector output.

- The laser must have a variable power setting.

- The laser must have some form of communication protocol to control at a minimum the laser setup parameters (i.e. start and stop wavelength, power setting, etc.)

- The laser must be ruggedized to withstand a 4g shock load.

The following specifications must be met during the entire tuning process from 1510 – 1570 nanometers:

- A tuning rate of 70 nanometers per second or greater must be possible.

- The laser must tune monotonically over the entire tuning range.  In other words, the laser must increase (or decrease) in wavelength in a continuous manner with no discontinuous jumps in wavelength.  The laser cannot stop, reverse direction, and repeat wavelengths during tuning, regardless of how small the reversal.

- The laser must be able to maintain a minimum power setting of 5 dBm.

- The laser must exhibit 0.1 dB power stability.

- The laser must remain mode-hop-free.

- The laser must maintain a linewidth of 500 kHz or less.