Statement of Work for Requisition # 0673505705

Product Restrictions: Only Hitachi Brand and models mentioned will be accepted as a comparable replacement part, no other brands are acceptable.  These are components parts of a Bohn Chilled water condensing unit. Controls for these units were designed around the Hitachi SRM Semi-Hermetic Screw Compressors.  These chillers have been setup to accommodate only Hitachi parts.  No other Brand will work in this application.   There are 4 items to be quoted below:

#1

HITACHI- SRM Semi-Hermetic Screw Compressor

| 60 hp Compressor – QUANTITY 2 |
| --- |
| MODEL 5002SC-H |  |  |
| 50 HZ OPERATION | KCAL/H | 138,000 |
| 60 HZ OPERATION | KCAL/H | 166,000 |
| 50 HZ OPERATION | Btu/h | 547,500 |
| 60 HZ OPERATION | Btu/h | 658,500 |
| MOTOR INPUT |  |  |
| 50 HZ OPERATION | kW | 40.0 |
| 60 HZ OPERATION | kW | 48.0 |
| OVERALL DIMENSIONS |  |  |
| HEIGHT | mm | 536 |
|  |  |  | (ft-in) | (1-9) |
| WIDTH | mm | 465 |
|  |  |  | (ft-in) | (1-6-1/4) |
| LENGTH | mm | 1,190 |
|  | (ft-in) | (3-10-3/4) |
| NET WEIGHT | kg | 430 |
|  | (lbs) | (950) |
| SHIPPING WEIGHT | kg | 476 |
|  | (lbs) | (1,050) |
| DISPLACEMENT |  |  |
| 50 HZ OPERATION | m/h | 169.5 |
|  | (cfm) | (99.8) |
| 60 HZ OPERATION | m/h | 204.2 |
|  |  |  | (cfm) | (120.2) |
| PIPING CONNECTION |  |  |
| SUCTION PIPING O.D. | mm | 60.5 |
| I.D. | (in) | (2) |
| DISCHARGE PIPING O.D. | mm | 48.6 |
| I.D. | (in) | (1-1/2) |
| ELECTRICALREQUIREMENTS: | 480 VOLTS 3PHASE 60HZ |
| MUST INCLUDE: |
| 1. NEW MOTOR PROTECTORS |  |
| 2. CRANKCASE HEATERS |  |  |
| 3. OIL CHANGE KITS |  |  |
| 4. OIL SAMPLE BOTTLES |  |  |
| 5. SIX MONTH WARRANTY |  |  |

#2

HITACHI- SRM Semi-Hermetic Screw Compressor

| 70 hp Compressor – QUANTITY 2 |
| --- |
| MODEL 6002 SC-H |  |  |
| 50 HZ OPERATION | KCAL/H | 170,000 |
| 60 HZ OPERATION | KCAL/H | 204,500 |
| 50 HZ OPERATION | Btu/h | 674,500 |
| 60 HZ OPERATION | Btu/h | 811,500 |
| MOTOR INPUT |  |  |
| 50 HZ OPERATION | kW | 49.5 |
| 60 HZ OPERATION | kW | 59.5 |
| OVERALL DIMENSIONS |  |  |
| HEIGHT | mm | 536 |
|  |  |  | (ft-in) | (1-9) |
| WIDTH | mm | 465 |
|  |  |  | (ft-in) | (1-6-1/4) |
| LENGTH | mm | 1,220 |
|  | (ft-in) | (4-0-0) |
| NET WEIGHT | kg | 450 |
|  | (lbs) | (995) |
| SHIPPING WEIGHT | kg | 508 |
|  | (lbs) | (1,120) |
| DISPLACEMENT |  |  |
| 50 HZ OPERATION | m/h | 208.8 |
|  | (cfm) | (122.8) |
| 60 HZ OPERATION | m/h | 251.5 |
|  |  |  | (cfm) | (148.0) |
| PIPING CONNECTION |  |  |
| SUCTION PIPING O.D. | mm | 60.5 |
| I.D. | (in) | (2) |
| DISCHARGE PIPING O.D. | mm | 48.6 |
| I.D. | (in) | (1-1/2) |
| ELECTRICAL REQUIREMENTS: | 480 VOLTS 3PHASE 60HZ |
| MUST INCLUDE: |
| 1. NEW MOTOR PROTECTORS |  |
| 2. CRANKCASE HEATERS |  |  |
| 3. OIL CHANGE KITS |  |  |
| 4. OIL SAMPLE BOTTLES |  |  |
| 5. SIX MONTH WARRANTY |  |  |

#3

Trade-In Credit:  Compressor Hitachi, SRM Semi-Hermetic Screw Type Model 5002

SC-H MFG NO COE17242.

#4

Trade-In Credit:  Compressor Hitachi, SRM Semi-Hermetic Screw Type Model 6002

SC-H MFG NO COE19354.