RECOMMENDATION FOR SPACE

DATA SYSTEM STANDARDS

FINAL DRAFT NAVIGATION DATA

CCSDS 501.0-WB-1

DRAFT – WHITE BOOK

May 2000

AUTHORITY

| Issue: | DRAFT – White Book, Issue 1.3 |
| --- | --- |
| Date: | May 2000 |
| Location: | Annapolis, Maryland, USA |

This document has to be approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and reflects the consensus of technical panel experts from CCSDS Member Agencies. The procedure for review and authorization of CCSDS Reports is detailed in reference [1].

This document is published and maintained by:

CCSDS Secretariat

Program Integration Division (Code MG)

National Aeronautics and Space Administration

Washington, DC  20546, USA

DOCUMENT CONTROL

This document is a CCSDS Report that contains technical material to supplement the CCSDS Recommendations for the standardization of data utilized for spacecraft navigation generated by space data systems of the Agencies of the Consultative Committee for Space Data Systems (CCSDS).

The topic areas covered herein include radio metric data content, spacecraft ephemeris, planetary ephemeris, tracking station locations, co-ordinate systems, and attitude data. This recommendation deals explicitly with the technical definitions and conventions associated with inter-Agency cross-support situations involving the transfer of ephemeris, tracking, and attitude data.

Through the process of normal evolution, it is expected that expansion, deletion or modification to this Report may occur. This Report is therefore subject to CCSDS document management and change control procedures. Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/ccsds/

Questions relative to the contents or status of this document should be addressed to the CCSDS Secretariat.

At time of publication, the active Member and Observer Agencies of the CCSDS were

Member Agencies

–	Agenzia Spaziale Italiana (ASI)/Italy.

–	British National Space Centre (BNSC)/United Kingdom.

–	Canadian Space Agency (CSA)/Canada.

–	Centre National d’Etudes Spatiales (CNES)/France.

–	Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

–	European Space Agency (ESA)/Europe.

–	Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

–	National Aeronautics and Space Administration (NASA)/USA.

–	National Space Development Agency of Japan (NASDA)/Japan.

–	Russian Space Agency (RSA)/Russian Federation.

Observer Agencies

–	Austrian Space Agency (ASA)/Austria.

–	Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

–	Centro Tecnico Aeroespacial (CTA)/Brazil.

–	Chinese Academy of Space Technology (CAST)/China.

–	Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

–	Communications Research Laboratory (CRL)/Japan.

–	Danish Space Research Institute (DSRI)/Denmark.

–	European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

–	European Telecommunications Satellite Organization (EUTELSAT)/Europe.

–	Federal Service of Scientific, Technical & Cultural Affairs (FSST&CA)/Belgium.

–	Hellenic National Space Committee (HNSC)/Greece.

–	Indian Space Research Organization (ISRO)/India.

–	Communications Research Centre (CRC)/Canada.

–	Institute of Space and Astronautical Science (ISAS)/Japan.

–	Institute of Space Research (IKI)/Russian Federation.

–	KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

–	MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

–	Korea Aerospace Research Institute (KARI)/Korea.

–	Ministry of Communications (MOC)/Israel.

–	National Oceanic & Atmospheric Administration (NOAA)/USA.

–	National Space Program Office (NSPO)/Taipei.

–	Swedish Space Corporation (SSC)/Sweden.

–	United States Geological Survey (USGS)/USA.

DOCUMENT CONTROL

| Document | Title | Date | Status/Remarks |
| --- | --- | --- | --- |
| CCSDS 501.0-B-1 | Recommendation for Space Data System Standards: Radio Metric and Orbit Data, Issue 1 | January 1987 | Original Issue |
| CCSDS - TBD | Recommendation for Navigation Data, Issue 1 | May 1999 | Revised issue for panel P1J |
| CCSDS - TBD | Recommendation for Navigation Data, Issue 1.1 | December 1999 | Revised issue for panel P1J (Winter 99) |
| CCSDS - TBD | Recommendation for Navigation Data, Issue 1.2 | March 2000 | Revised issue for panel P1J (Feb 2000) |
| CCSDS - TBD | Recommendation for Navigation Data, Issue 1.3 | May 2000 | Revised issue for panel P1J (May 2000) |

TABLE OF CONTENTS

Section										Page

1.	Introduction ……………………………………………………………………………………1-1

1.1	Purpose and Scope …………………………………………………………………..1-2

1.2	Applicability …………………………………………………………………………1-3

1.3	References ……………………………………………………………………………1-4

2.	SCOPE OF NAVIGATION  …………………………………………………………………………..2-1

2.1 DEFINITION OF NAVIGATION ……….…………………………….………………………2-2

2.2 NAVIGATION  PROCESS ……………………………………………………….….………. 2-3

2.3 NAVIGATION DATA TYPES………………………………………………..……………….2-4

3.	NAVIGATION MESSAGE EXCHANGE FRAMEWORK ……………………………………………3-1

3.1 Definitions of Navigation Message Exchange Elements ………………………….3-2

3.2 Navigation Data Exchange Participants …………………….………...……………..3-3

3.3 NAVIGATION EXCHANGE DATA TYPES………………..………………….……………..3-4

3.4 Navigation  DATA Exchange Scenarios ……………………………………………….3-5

4.	ANCILLARY DATA  …………………………………………………………………………………..4-1

4.1 Rationale ……………………………………………………………………………….	4-2

4.2 UNITS………………………………………………………………………………………...…4-3

4.3 QUALITY ……………………………………………………………………………………... 4-4

4.4  COORDINATE FRAME IDENTIFICATION ……………………………………………….. 4-5

4.5  TIME …………………………………………………………………………………………..4-6

4.6  ASTRODYNAMIC CONSTANTS………………………… ………………………..……….4-7

4.7 ENVIRONMENTAL MODELS ……………………………. ………………………………..4-8

5.       PROPERTIES ………………………………………………………………………………………….5-1

5.1 Rationale ………………………………………………………………………………	5-2

5.2  Position and Orbit Data …………………………………………………………………5-3

5.3  Tracking STATION COORDINATES ……………………………………..……………….5-4

5.4 SPACECRAFT Attitude data…………..…………………………………………………5-5

5.5 SPECIAL CONSIDERATIONS ………………………………………………….…………….5-6

5.6 Data Transmission Delays ………………………………………………………………. 5-7

6.	MEASUREMENTS 	6-1

6.1 Rationale …………………………………………………………..…………………………6-2

6.2 Measurement Data Types ……………………………………………………………..	6-3                                                          	  6.3 Earth Tracking…………………………………………………………………………….	6-4

6.4 GPS ………. …………………………………………………………………………………..	6-5

6.5 Recommendations …………………………………………………………………..	6-6

TABLE OF CONTENTS   (continued)

Section										Page

7.	SATELLITE-BASED GLOBAL NAVIGATION SYSTEMS …………………………………………7-1

7.1 Rationale ………………………………………………………………………………	7-1

7.2 Recommendations ………………………………………………..………………	7-2

8.	NAVIGATION MESSAGE FORMAT RECOMMENDATION ………………………………………8-4

8.1 RATIONALE……………………………………………………………………………………8-2

8.2 SPKE Description ………………………………………………………………………	8-3

8.3 SPKE Recommendations …………………………………………………………	8-4

8.4 SPKE FOR SPACE APPLICATIONS……………………………………………………….. 	8-5

AnnEX A   Navigation data message EXAMPLE………………………………………………...A-1

Annex b   Glossary	B-1

index 	C-1

LIST OF FIGURES

[To be revised]

Figure 2-1: Real-time or near real-time navigation process …………………………………………………..2-1

Figure 3-1: Navigation data message exchange ……………………………………………………………….3-1

Figure 3-2: Navigation message in a CCSDS frame …………………………………………………………..3-2

Figure 4-1: Differences between time  relevant scales…………………...…………………………………….4-1

Figure 5-1: Data transmission delays  ……………………………………………………………………...….5-1

Figure A-1: Example of a NORAD TLE file …………………………………………………………………A-1

Figure A-2: Graphical representation of the NORAD TLE file format ………………………………………A-2

LIST OF TABLES

[To be revised]

Table 2-1: Navigation data types ………………………………………………………………………………2-1

Table 3-1: Measurement data types	3-1

Table 3-2: Property data types	3-2

Table 3-3: Ancillary data types …………………………………………………………………………..……3-3

Table 4-1: Coordinate frames	4-1

Table 4-2: Coordinate frames ???	4-2

Table 4-3: Environmental models	4-3

Table 5-1: Classical Keplerian elements	5-1

Table A-1: Structure of first row of the NORAD TLE file ………………………………………………...…A-1

Table A-2: Structure of the second row of the NORAD TLE file …………………………………………….A-2

This page intentionally blank

# 1. Introduction

## Purpose and Scope

The purpose of this document is to establish common recommendations for adequately exchanging data involved in spacecraft navigation. This exchange of navigation data occurs in situations in which cross-support among space missions and facilities of member Agencies of the CCSDS is required. In addition, the Recommendation provides focusing for the development of multi-mission support capabilities within the respective Agencies to eliminate the need for arbitrary, unique capabilities for each mission. This Recommendation can also be used within any Agency, for a specific project in which exchange of navigation data is required.

The document defines the navigation data and the format in which they are transferred. The data to be covered include (among others):

- Properties and measurements of spacecraft dynamics

- Ground station information

- Environmental models

- radiometric data

## Applicability

This document applies to navigation data exchange for the classical cases flight-to-ground, ground-to-flight, and ground-to-ground but it also comprises the case flight-to-flight (formation flying, and rendezvous and docking situations).

In particular, this document contemplates the exchange of processed radio metric and orbital parameters between CCSDS Agencies in cross-support situations. In addition, it serves as a guideline for the development of compatible internal Agency standards in this field. This Recommendation is not retroactive, nor does it commit any Agency to implement the recommended radio metric and orbit data concepts at any future time. Nevertheless, all CCSDS Agencies accept the principle those all-future implementations of radio metric and orbit data exchange, which are used in cross-support situations will be based on this Recommendation.

Where preferred options or mandatory capabilities be clearly indicated herein, the indicated sections of the specification must be implemented when this Recommendation is used as a basis for cross-support. Where optional subsets or capabilities are allowed or implied in this specification, implementation of these options or subsets is subject to specific bilateral cross-support agreements between the Agencies involved.

The recommendations in this document are to be invoked through the normal standards programs of each member Agency, and are applicable to those missions for which cross-support, based on capabilities described in these recommendations, is anticipated.

1.3 REFERENCES

[Note: References are subject to change.]   [A.I. 1 workshop #6]

[1] Procedures Manual for the Consultative Committee for Space Data Systems, Issue 1, Consultative Committee for Space Data Systems, August 1985 or later issue.

[2] Introduction of the Improved IAU System of Astronomical Constants, Time Scales, and Reference Frames into the Astronomical Almanac, Supplement to the Astronomical Almanac 1984, U.S. Government Printing Office, Washington, D.C., 1983.

[3] Time Code Formats, Recommendation CCSDS 301.0-B-1, Issue 1, Blue Book, Consultative Committee for Space Data Systems, January 1987 or later issue.

[4] CCSDS Strategic Plan, Volume 1: Vision, Mission, Strategic Goals, Preliminary Draft, Revision 1, October 1998.

[5] CCSDS Strategic Plan, Volume 2: Operation Plan for Standards Development, Preliminary Draft, Revision 1, October 1998.

[6] Celestial Mechanics and Dynamical Astronomy, J. Heward and M. Morris, 1995-96, Vol. 63 No. 2.

[7] McCarthy D.D, 1996, "IERS Conventions", IERS Technical Notes 13 and 21, Observatoire de Paris, Paris.

[8] Reference for COSPAR Standards.

[9] Global Positioning Systems: Theory and Applications (Volumes I and II). Progress in Astronautics and Aeronautics, B. W. Parkinson, J.J. Spilker Jr., P. Axelrad, P. enge, and Paul Zarchan, volume 163, 1996.

[10] Understanding GPS Principles and Applications, E. D. Kaplan, Artech House Publishers, 1996.

[11] GPS Interface Control Document, ICD-GPS-200, IRN-200B-PR-OOJ, Rev. B-PR, anonymous, U.S. Air Force, July 1, 1992.

[12] Marine Navigation: Piloting and Celestial and Electronic Navigation, R.R. Hobbs, Naval Institute Press Annapolis, Maryland, 1990.

[13] Bauersima, I. (1983): "Navstar/Global Positioning System (II)*. Mitteilungen der Satelltenbeobachtungsstation Zimmirwald, Nr. 10.

[14] Summary of the Workshop on GPS Exchange Formats, Evans, A. (1989),  Proceedings of the Fifth International Geodetic Symposium on Satellite Systems, pp. 917ff, Las Cruces

[15] A Common Exchange Format for GPS Data, Gurtner, W., G. Mader, D. MacArthur (1989), Proceedings of the Fifth International Geodetic Symposium on Satellite Systems,pp. 917ff, Las Cruces.

[16] A Proposed Standardized Exchange Format for Navstar GPS Geodetic Data, Scott, V.D., J. Clynch (1986), Proceedings of the Fourth International Geodetic Symposium on Satellite Systems, pp. 513ff, Austin, Texas.

[17]  Remondi, B. W. 1985: Distribution of Global Positioning System Ephemerides by the National Geodetic Survey, Presented at the First Conference on Civil Applications of GPS - Institute of Navigation, September 12, 1985, 8 pp.

[18] Remondi, B. W. 1989: Extending the National Geodetic Survey Geodetic Orbit     Formats, NOAA Technical Report 133 NGS 46, 85 pp.

[19] Remondi, B. W., 1991: NGS Second Generation ASCII and Binary Orbit Formats and Associated Interpolated Studies, Proceedings of the Twentieth General Assembly, International Union of Geodesy and Geophysics, Vienna, Austria, August 11-24, 1991, 28 pp.

[20] Gurtner, W., G. Mader (1990):  "Receiver Independent Exchange Format Version 2." CSTG GPS Bulletin Vol.3 No.3, Sept/Oct 1990, National Geodetic Survey, Rockville.

[21]  Remondi, B. W. 1985: Distribution of Global Positioning System Ephemerides by the National Geodetic Survey, Presented at the First Conference on Civil Applications of GPS - Institute of Navigation, September 12, 1985, 8 pp.

[22] Bauer et al., 1997. Bauer, F., Bristow, J., Folta, D., Hartman, K., and Quinn, D. (1997). Satellite formation flying using an innovative autonomous control system (AUTOCON) environment. In American Institute of Aeronautics and Astronautics.

[23] Corazzini et al., 1997. Corazzini, T., Robertson, A., Adams, J., Hassibi, A., and How, J. (1997). GPS sensing for spacecraft formation flying. In Proceedings of the Institute of Navigation GPS-97, Kansas City, Missouri, USA.

[24] Crippen and Hauck, 1983. Crippen, R. L. and Hauck, F. H. (1983). Orbiter operations in close proximity to free-flying satellites or formation flying in space. In Proceedings of the Twenty-seventh Symposium of the Society of Experimental Test Pilots, Beverly Hills, CA, USA, pages 314–334.

[25] Fromm and Lucas, 1998. Fromm, H. H. and Lucas, R. (1998). The European contribution to GNSS-2: A status report on the technical preparations. In International Conference on the European GNSS-2 System. European Space Agency.

[26] Hart et al., 1996. Hart, R., Gramling, C., Deutschmann, J., Long, A., Oza, D., and Steger, W. (1996). Autonomous navigation initiatives at the NASA GSFC flight dynamics division. In ISTS Gifu, number 20 in Paper 96-c-23.

[27] Scolese et al., 1991. Scolese, C., Folta, D., and Bordi, F. (1991). Field of view location and formation flying for polar orbiting missions. In Proceedings of the 1st AAS/AIAA Annual Spaceflight Mechanics Meeting, Houston, TX, Feb. 11-13, 1991, pages 949–966.

[28] Ulybyshev, 1998. Ulybyshev, Y. (1998). Long-term formation keeping of satellite constellation using linear-quadratic controller. Journal of Guidance, Control, and Dynamics, 21(1):109–115.

[29] Zimmerman and Cannon, 1994. Zimmerman, K. and Cannon, R. (1994). Differential carrier phase GPS techniques for space vehicle rendezvous. In Proceedings of the Institute of Navigation, Salt Lake City, Utah, USA.

[30] Zimmerman and Cannon, 1995. Zimmerman, K. and Cannon, R. (1995). Experimental demonstration of GPS for rendezvous between two prototype space vehicles. In Proceedings of the Institute of Navigation, Palm Springs, California, USA.

[31] Clohessy, W. and Wiltshire, R. (1960). Terminal guidance system for satellite rendezvous. Aerospace Sciences, 27, pages 653-658, 674.

[32]  McCarthy D.D (ed.), 1992, "IERS Standards", IERS Technical Note 13, Observatoire de Paris, Paris.

[33] Fricke W. et al., 1988, "Fifth Fundamental Catalogue, Part I", Veröff. Astron. Rechen Inst., Heidelberg.

[34] Arias et al. 1995.

[35] Lieske et al. 1977.

[36] Seidelmann 1982.

[37] Aoki et al. 1982.

[38] Long et al., 1989 ‘GTDS mathematical theory, Rev. 1’, Computer Science Corp., FDD/552-89/001.

The latest issues of CCSDS documents may be obtained from the CCSDS Secretariat at the address indicated on page i.

# 2. scope of navigation

2.1  DEFINITION OF NAVIGATION

The word {navigate} is derived from the Latin words {navis} meaning ship, and {agere}, meaning to move or direct.

The common definition of navigation establishes that it is the science of getting a craft or person from one place to the other. In order to establish a solid recommendation for the exchange of navigation data among space agencies, it is of crucial importance to clearly set the definition of terms like navigation, navigation data, navigation message, etc.

In the following, several definitions are given together with some explanations about the nature of the navigation tasks and the formation of the navigation messages.

Navigation is the process to find the present and imminent future position and orbit of a spacecraft using a series of measurements.

Guidance is the process to define a path to move a spacecraft from one point to another.

Control is the process to maintain a spacecraft within the prescribed path and attitude.

The process of navigation includes the exchange of orientation information.

The responsibilities for guidance and control will not be covered in these recommendations.

2.2 NAVIGATION PROCESS

Figure 2-1: Real-time or near real-time navigation process

The first part of the navigation process starts with the acquisition of a set of measurements. This set is properly stored to allow the calculation of the orbit in the second step. The third step accounts for the prediction of the future state based on the measurements taken and the calculation of the orbit.

In a real-time or near real-time scenario the previous definition implies a three steps task as depicted in Figure 2-1. In a non-real time scenario any kind of data may be transferred (past, current or predicted data).

2.3 NAVIGATION DATA TYPES

To accomplish the navigation process information is required.  The type of data may comprise orbit, attitude, radiometric, global navigation systems (GNS) and corresponding quality data, etc. Table 2-1 shows the different types of navigation data that can be transmitted. The following sections describe with detail the different navigation data types, together with their type of data.

Table 2-1: Navigation data types

| Navigation data types | Type of navigation data involved |
| --- | --- |
| Orbit data | Position, velocity, time. |
| Attitude data | Angle orientations and its derivatives |
| Radio-metric data | Doppler, range. |
| Data from global navigation systems | GNS navigation messages |
| Ground stations data | Co-ordinates, status |
| Co-ordinate systems data | Description, conventions, units |
| Astrodynamic values | Constants, planetary data. |
| Auxiliary data | Central body potential etc. |
| Qualifiers | Quality of the data, accuracy of the data. |

# 3. NAVIGATION MESSAGE EXCHANGE FRAMEWORK

## 3.1 Navigation Data Exchange Scenarios

This section contains different scenarios for the applicability of exchange of navigation data.

## (aL, add Drawing  with explanations)

An Interface Control Document (ICD) should be jointly produced by both Agencies participating in a cross-support involving tracking data orbital elements. The ICD should precisely define the data to be transferred, the formats, calibrations for tracking data, a description of any ancillary data, and the complete description of the station location, including the earth-centered coordinates with their defining system, and the relative geometry of the tracking point and cross-axis of the antenna mount.

## 3.2 Definitions of Navigation Message Exchange Elements

This document describes the interaction of two or more participants in the interchange of navigation data.

Participant is an entity which has the ability to acquire or broadcast navigation messages.

Examples of participants can be a spacecraft, a ground station, a control center, etc. All kinds of combinations are possible as the exchange of navigation data is allowed between all kinds of participants.

Figure 3-1: Navigation data message exchange

Object is an entity of the environment.

Property of a participant is a data type, which allows describing the state of an object.

Measurement is the output of a sensor or equipment.

Ancillary Information is any data type used for the correct interpretation of measurements and properties.

Navigation Data is a set of measurements and properties exchanged between participants during a navigation session.

The navigation data are packed into a navigation message, as shown in Figure 3-2.

Figure 3-2: Navigation message in a CCSDS frame

Navigation Message is a particular arrangement of the navigation data whose structure and content are the subjects of this recommendation.

The contents and the format of the navigation message are the scope of this Recommendation. The way and the means by which the navigation message are broadcasted or acquired are not the subject of this document and will not be discussed here.

The navigation message must fit inside a standard CCSDS data transmission message. Therefore, this recommendation shall be compliant with the rest of the CCSDS standards.

Navigation Session is the process of the interchange of data between participants for navigation purposes.

## 3.3 Navigation Exchange Data Types   [a.i. 3]

The following Tables contain a list of the most typical measurement, property, and ancillary  information data types, which may be transferred during a navigation session within a navigation message.

Measurement data will be exchanged in SI units.  However, there are cases where it is not possible to convert raw measurements from hardware specific units to SI units, without risking some degradation of measurement quality. For example, for Doppler and range measurements collected during periods when the transmitter frequency is time varying, a conversion to SI units is only possible with accurate trajectory information.  In this case, the recommendation is for the participating agencies to agree upon a hardware-specific unit.

Table 3-1: Measurement data types

| Type | Units | Comments |
| --- | --- | --- |
| Range | km | It is the distance between two participants |
| Range rate | km/s | It is the derivative of the distance between two participants |
| Variable Transmitter Range | Range Units | Ref. DSN doc |
| Antenna angles | deg |  |
| Doppler (coherent) | MHz |  |
| Doppler (non-coherent) | MHz |  |
| Variable Transmitter Doppler |  |  |
| Alan variance |  |  |
| Integrated Doppler count | - |  |
| Quality of measurements |  | depending on quantity |
| IMU output | deg/s2 |  |

Table 3-2: Property data types

| Type | Units | Comments |
| --- | --- | --- |
| Position | km |  |
| Angular Velocity | deg/s |  |
| Linear Velocity | km/s |  |
| Angular acceleration | deg/ s2 |  |
| Acceleration | km/s2 |  |
| Epoch | Sec | Gregorian Format, UTC, sec+J2000 |
| Attitude | deg |  |
| Attitude rate | deg/s |  |
| Length | M | Lateral dimension of a participant |
| Moment of Inertia | kgm2 |  |
| Force | kgm/ s2 |  |
| Torque | kgm2/ s2 | Moment of force |
| Mass | kg |  |
| Energy, work, or heat | kgm2/ s2 | Same dimension as torque |
| Power | kgm/s³ |  |
| Pressure | kgm/ s2 | For per unit area |
| Temperature | K |  |
| Transmitter delay | ms |  |
| Receiver delay | ms |  |
| Surface | m2 |  |
| Antenna angles | deg |  |
| Oscillator frequency | MHz |  |
| Oscillator stability | ns |  |
| Ballistic coefficient | m2/kg | Cd A / m, solar pressure, albedo |
| Aerodynamic coefficient |  | Depends on the spacecraft |
| Reflectivity |  |  |

Table 3-3: Ancillary information data types

| Type | Units | Comments |
| --- | --- | --- |
| Physical constants |  | Ref. IERS |
| Transmitter ID |  | Ref. IERS |
| Receiver ID |  | Ref. IERS |
| Co-ordinate system description | - |  |
| Time system description | - |  |
| Quality of property |  | Depending on quantity |

3.4 NAVIGATION DATA EXCHANGE SCENARIOS

3.4.1 SPACECRAFT RENDEZVOUS AND DOCKING OPERATIONS

Spacecraft rendezvous and docking is defined as the set of tasks which allow the approach, the mating, and the separation in a controlled manner of two or more spacecraft.

A typical rendezvous and docking scenario is the mating of a servicing spacecraft with a space station. Servicing to a space station comprises the tasks of assembly, re-supply, repair and maintenance of manufactured space parts in-orbit.

With space programs like the U.S. Space Shuttle, the Russian MIR station, and the International Space Station (ISS), rendezvous and docking operations are starting to become frequent.  In the near future, a big system like the International Space Station will require dozens of flights a year to accomplish in-orbit servicing. In such a scenario, inter-spacecraft communications, formation flying and rendezvous and docking task will be a routine.

For the typical case of the servicing to a space station, the in-orbit servicing requires the assembly of small chasers in comparison with the big target  (space station). Usually, the chaser is the active element, and has a guidance, navigation, and control (GNC) system which allows active servicing. The GNC system has sensors to measure the spacecraft's position and orientation in space. It determines the present state of the vehicle, and computes the control actions required to maintain or achieve a desired position and orientation.  The target is the passive element during these operations. It has also sensors to measure the distance and orientation with respect to the chaser.  However, in most of the time, it does not perform any maneuvers.

The rendezvous is completed in several phases: homing, closing, final approach, docking and structural latching .

Attitude determination and control plays a relevant role during the last part of the approach and the beginning of the departure. Typical distances between chaser and target start in the order of hundreds of meters. A set of sensors for very close measurement, allows the fine alignment between vehicles.

The relative translational motion of two spacecraft orbiting around the Earth can be mathematically described using the Clohessy-Wiltshire-Hill (C-W-H) equations (Ref. 31). This is a set of non-linear differential equations with constant coefficients, describing the movement of two small masses in a near-circular orbit around a third big mass. These equations have as input the chaser's initial position and velocity. The output is the chaser's position and velocity after a time interval.

The translation and rotation of the servicing vehicle (chaser) may be realized by means of thrust impulses. In general, during the docking maneuvers the space station is maintained passive.

3.4.2 SPACECRAFT CONSTELLATION AND FORMATION FLYING

In most of the technical literature, the terms spacecraft constellation and spacecraft formation flying are used to describe grouping of satellites. In what follows, the term formation flying will be reserved for satellite sets with inter-spacecraft communication.

The reasons for using satellites flying in formation are:

- Reduce the cost and/or the risk of a mission by splitting the payload on smaller platforms. Each satellite can be developed by different entities (Agencies, companies, etc).

- Enhance the result of two already self-consistent missions by bringing some added value through the synergy of the measurements or add a new type of measurements to a more advanced mission scenario.

In addition, collateral benefits of formation flying missions are:

- The implicit reduction of the risk of delay on an important program due to only one instrument by setting the instrument on a small companion.

- The possibility of the replacement of a failed key instrument on a large platform by adding a companion flying in formation with a spare instrument.

Therefore, the most important requirement of a formation-flying mission is to ensure that the desired synergy of observations is obtained. This requirement can be translated in a set of requisites in terms of spatial co-registration and on simultaneity of measurements.

The mission requirements are often expressed in terms of formation requirement in having the same ground track for all the satellites of the formations. The literature established three different types of formations: Close, Ideal and Dynamic Formations. In the Close Formation, the satellites are on the same orbit only separated by a small bias in argument of latitude resulting in an along-track direction ranging from a few tens of meters to less than a kilometer. In the Ideal Formation, the satellites are separated by a larger constant bias in argument of latitude resulting in an along-track separation of greater than a kilometer to hundreds of kilometers. The Dynamic Formation is in fact a derivation of the Ideal formation, where the along-track separation will not be kept constant, for example, under the action of different ballistic coefficients between each formation maintenance maneuver.

3.4.3 APPLICABILITY OF FORMATION FLYING SCENARIOS

The applications of formation flying in the space environment can be catalogued depending on the type of the mission considered (science, telecommunications, Earth observation). However, the mathematical and physical principles behind are identical. This strength allows repeatability across platforms facilitating substantial reductions in cost.

The applications in Astronomy and Astrophysics allow the deployment of a constellation of satellites, which can carry all together a distributed payload. The virtual payload is in fact distributed among several quasi-identical satellite payloads. Scientist can benefit of the fantastic aperture for observations granted by instruments, which could resemble a huge telescope in space, etc.

The applications for Earth observation are focused in the possibility to have dual observations of a single common Earth phenomenon. A satellite (SAT1) carrying certain payload is in charge of measuring phenomenon A. Another similar satellite (SAT2 ) is in charge of measuring another phenomenon B. For reasons of launch cost and operations, at a given point in time payload users of SAT2 want also to measure phenomenon A but at a rigorous time intervals between observations of both satellites. This scenario is more and more common as the demand for frequent and high quality observations is increasing every.  In that case, both satellites have to keep a strict formation in their relative positions making periodic observations, etc.

The applications for In Orbit Infrastructure (IOI) covered by rendezvous and docking. The problem of the space rendezvous is about the mating of two spacecraft in orbit. An active chaser spacecraft (servicing vehicle) will dock with a passive target (normally a space station.

The deployment and maintenance of a satellite constellation inside the same orbital window could represent some of the applications for telecommunications satellites. Every year, more and more satellites are placed in the geostationary ring. The demand for broadcasting and telecommunications is forcing commercial and government entities to place a high number of satellites inside the same orbital window.

# 4. ancillary data

## 4.1 Rationale

This chapter describes the ancillary data types: these are the pieces of information needed to interpret measurements and properties of navigation participants.  In general, ancillary information makes it possible to take properties or measurements and incorporate them in numerical computations correctly. In some cases, very detailed modeling information is passed along so that measurements and properties can be used in state-of-the-art high-fidelity computations.  For each ancillary data type covered, descriptions of formats and systems supported by member agencies are included in a unified manner, and recommendations made where applicable.

### 4.2 units

The default units for any values in a navigation message are those listed in Tables 3-1 and 3-3, unless otherwise specified in the message.

### 4.3 quality

The quality of properties or measurements can be defined as necessary.  Examples are provided in Annex A.3.

### 4.4 coordinate frame identification   [A.I. 5]

Table 4-1 Coordinate frames  [To be combined with table 4-2?]

| CASE | RECOMMENDATION | EXAMPLE |
| --- | --- | --- |
|  | Ascent/Descent | Body center fixed |
|  | Interplanetary cruise orbit |  |
|  | Rendezvous Formation Flying | Spacecraft centered |

Usually, docking operations are accomplished using a reference coordinate system known as local vertical, local horizontal (LVLH).  This system has its origin in the docking port of the station, and is defined as follows: +X (roll) in the direction of target flight, +Z (yaw) in the direction of the center of Earth, and +Y (pitch) orthogonal to these two.  The chaser is approaching the target using the V-bar technique, where the docking axis lies along the velocity vector of the space station and against the radial velocity of the station.

4.4.1. COORDINATE SYSTEM DEFINITIONS

4.4.1.1 INTERNATIONAL CELESTIAL REFERENCE SYSTEM (ICRS)

Since 1991 the concept of the  International Celestial Reference System (ICRS) was established by the IAU as the fundamental inertial coordinate system (Ref. 32). The origin of the ICRS is defined as the solar system barycenter within a relativistic framework and its axes are fixed with respect to distant extragalactic radio objects. The fundamental plane of the ICRS is closely aligned with the mean Earth equator at J2000 and the origin of right ascension is defined by an adopted right ascension of the quasar 3C273.

The practical realization of the ICRS is designated the International Celestial Reference Frame (ICRF) (Ref. 7).

4.4.1.2 INTERNATIONAL TERRESTRIAL REFERENCE SYSTEM (ITRS)

Complementary to the ICRS, the International Terrestrial Reference System (ITRS) provides the conceptual definition of an Earth-fixed reference system (Ref. 7). Its origin is located at the Earth's center of mass (including oceans and atmosphere) and its unit of length is the SI meter. The orientation of the IERS Reference Pole (IRP) and Meridian (IRM) are consistent with the previously adopted BIH system at epoch 1984.0 and the former Conventional International Origin (CIO).

The time evolution of the ITRS is such that it exhibits no net rotation with respect to the Earth's crust. Realizations of the ITRS are given by the International Terrestrial Reference Frame (ITRF).

New versions of the ITRF are published annually and exhibit global differences on the centimeter level.

The transformation of a vector between ITRF and ICRS is performed as follows:

rITRF		=	((t) ((t) N(t) P(t) rICRS

[HKK:  velocity vector to be included]   [A.I. 4]

with:

(:	Polar Motion Transformation Matrix

(:	Earth Rotation Transformation Matrix

N:	Nutation Transformation Matrix

P:	Precession Transformation Matrix

Details for these transformations are given in Ref. 7.

4.4.1.3 TRUE OF DATE COORDINATE SYSTEM (TOD)

The True of Date (TOD) coordinate system is frequently used for astrodynamical applications.

The transformations between the International Celestial Reference System (ICRS), the International Terrestrial Reference Frame (ITRF), and the True of Date (TOD) coordinate system are performed as follows:

rTOD		=	N(t) P(t) rICRS

rITRF		=	((t) ((t) rTOD

4.4.2  RECOMMENDATIONS

Table 4-2

| Case | Recommendation | Examples |
| --- | --- | --- |
| Ascent/Descent (launch support/re-entry) | Body-centered/Body-fixed | Earth (ITRF), Mars |
| Interplanetary cruise Planetary/Body orbiter | Barycentric/Inertial | EME2000 MMEdate |
| Rendezvous/Re-entry/Formation Flying | ž-nadir/ ŷ-orbital normal spacecraft centered | LVLH/RTW |

  - TIME

4.5.1	Rationale

The exact definition and understanding of time systems is essential for

- the modeling of satellite orbits and attitude,

- exchange of navigation data, and

- satellite ground operations.

In this section definitions of time scales are given which are of relevance for navigation messages.  The relative differences between time frames appear as (1) step functions (for example, when leap seconds are added), or (2) monotonically increasing differences (when relativistic effects are added), or (3) periodic differences (due to solar system dynamics).

4.5.2	Time Scales

Figure 4-1 gives an overview about the differences between the most relevant time scales described in the following.

Fig. 4-1:	Differences between relevant time scales between 1950 and 2020. Periodic terms in TCB and TDB have been exaggerated by a factor of 100 to make them discernible. (Adapted from Seidelmann & Fukushima 1992)

4.5.2.1	Time Scales for Earth Orbiting Satellites

The following time scales are of relevance for Earth orbiting satellites:

Terrestrial Time (TT)

The Terrestrial Time is a conceptually uniform time scale that would be measured by an ideal clock on the surface of the geoid and is a rename of the previously used Terrestrial Dynamical Time TDT. TT is measured in days of 86400 SI seconds.

International Atomic Time (TAI)

The TAI provides the practical realization of a uniform time scale based on atomic clocks and agrees with TT except for a constant offset of 32.184 s and the imperfections of existing clocks.

Between TAI and TT the following relation holds:

TAI = TT - 32.184 s

Global Positioning System (GPS) Time

GPS time is an atomic time scale like TAI but differs in the chosen offset and the choice of atomic clocks used in its realization.

The origin of GPS was arbitrarily chosen as

GPS = UTC on 1980 January 6.0,

i.e. GPS time differs from TAI by a constant offset of

GPS = TAI(GPS) - 19 s

Greenwich Mean Sideral Time (GMST)

The GMST is defined as the Greenwich hour angle of the mean vernal equinox of date.

Universal Time (UT1)

UT1 is the today's realization of a mean solar time, which is derived from GMST by a conventional relation.

Coordinated Universal Time (UTC)

UTC is tied to International Atomic Time (TAI) by an offset of integer seconds (leap seconds) that is regularly updated to keep UTC in close agreement with UT1 within 0.9 s. Leap seconds may be introduced on Jan 1 and Jul 1 (as well as Apr 1 and Oct 1).

At the beginning of the year 2000, the difference between UTC and TAI was

UTC - TAI = -32 s

4.5.2.2	Time Scales for Interplanetary Missions

In addition to the above time scales the following scales are of relevance for interplanetary missions (and Space Geodesy).

Barycentric Dynamical Time (TDB)

The TDB is the independent variable of current barycentric solar system ephemerides (e.g. DE405). This time was introduced by the IAU in 1976 and defined to deviate from the Terrestrial Dynamical Time TDT (which is now identical with TT) by periodic terms ((2 ms), only.

Barycentric Coordinated Time (TCB)

The Barycentric Coordinated Time is the relativistic time coordinate of the 4-dimensional barycentric frame. TCB and TDB exhibit a scale difference of

LB = 1.5505197487(10-8

which results in a secularly increasing difference of

TCB - TDB  (  46.7s/cy (year-1977.0)

4.5.3	Recommendations

UTC shall be used for the interagency exchange of navigation data; except for participants beyond Earth orbit.

4.6 ASTRODYNAMIC CONSTANTS

Speed of light, GM, and reference radius.  Complete list of constants as referenced in IERS.

## 4.6.1 Recommendations

To follow IAU84 and IERS standards.

### 4.7 ENVIRONMENTAL MODELS

Listed below are various models and data that are used for spacecraft trajectory determination. Some models have been derived to help compute effects on measurements, while others help to compute effects on the equations of motion.

Table 4-3 Environmental models

| Models and data | Measurements | Properties |
| --- | --- | --- |
| Gravity |  | √ |
| Orientation of spin axis |  | √ |
| Rotation state |  | √ |
| Time history of precession |  | √ |
| Solar flux |  | √ |
| Central body ionosphere | √ |  |
| Central body atmosphere |  | √ |
| Central body magnetic flux |  | √ |
| Central body troposphere | √ |  |
| Solar plasma | √ |  |
| Solar radiation pressure |  | √ |

## 4.8 Recommendations

The following recommendations are made:

- Use of metric units ( km, kg and seconds )

# 5. properties

## 5.1 Rationale

Transfers of navigation data, as described in Table 3-2, are required for purposes such as:

- Pre-flight planning of mission support, orbit covariance analysis, tracking station planning and preparation, etc.

- In-flight inter-agency comparison of the estimated spacecraft flight path, or trajectory, including software compatibility checkout, comparisons of orbit determination solutions, etc.

- Tracking station preparation (often referred to as predicts) in support of radio metric data interchanges.

In all cases it is important that Agencies participating in the interchange of navigation data have a common understanding of the choice of parameters and the reference systems employed. The required resolution of each parameter is dependent on its intended use and should be jointly specified. The major items of the consensus proposal of the CCSDS are provided below.

[Add new text here, per A.I. 7]

## 5.2 position and orbit data

### 5.2.1 Spacecraft State Vector (Position, Velocity and Time)

For the transmission of a spacecraft state vector, the following recommendations are applicable:

- The Cartesian state vector (position and velocity) x, y, z, x_dot, y_dot, z_dot shall be given at a specified epoch t (Gregorian format) in a specified reference frame.

- SI units (kilometers and kilometers/second) are to be used.

- The epoch t is to be specified in Coordinated Universal Time (UTC) and given by year, month, day of month, hour, minute, seconds and decimal fractions of seconds.]

### 5.2.2 Spacecraft Classical Orbital Elements

For the transmission of spacecraft classical orbital elements, the following recommendations are applicable:

- The elements shall be given as osculating Keplerian elements (Ref. Table 5-1) at a specified epoch t (Gregorian format) in a specified reference frame.

- SI units (kilometers and degrees) are to be used.

- The epoch t is to be specified in Coordinated Universal Time (UTC) and given by year, month, day of month, hour, minute, seconds and decimal fractions of seconds.

Table 5-1: Classical Keplerian elements

| Description | Mathematical Symbol | Units |
| --- | --- | --- |
| Semimajor axis | a | km |
| Eccentricity | e | - |
| Inclination | i | deg |
| Right ascension of ascending node | Ω | deg |
| Argument of perigee |  | deg |
| True anomaly |  | deg |

5.3 TRACKING STATION COORDINATES

## 5.3.1 Rationale

Spacecraft tracking and communications is possible by a network of  stations located around the world.  Whenever an orbiting spacecraft passes across the field of coverage of a ground station, it collects tracking data which determines the spacecraft position and velocity.

The location of the tracking station on earth should be specified by its geocentric spherical or cylindrical coordinates referred to the mean pole, equator, and zero degree meridian of 1903.0 (CIO).  The x axis is along the intersection of the zero degree meridian (passing through the mean north pole of 1903.0) and the mean equator of 1903.0, the z axis is along the mean pole of 1903.0, directed north, and the y axis completes the right-handed rectangular coordinate system.  The source of polar motion values (e.g., BIH or Naval Observatory) and their use should be included in the ICD.

## 5.3.2 recommendations

The tracking station geodetics will be defined based on the International Terrestrial Reference Frame (ITRF, http:\\www.ngs.noaa.gov/CORS/itrf.html).

5.3.3  TBD

5.4 SPACECRAFT ATTITUDE DATA

[Add revised text, per A.I. 9]

## 5.4.1 Rationale

Attitude of a rigid spacecraft is its orientation in a 3-dimensional space at a given time.  Attitude motion describes the attitude evolution around its center of mass.

Spacecraft attitude is the pointing orientation at each time of an orbiting spacecraft with respect to known references (celestial objects, frame, etc.). Attitude determination is the process of computing a set of parameters that describes this orientation using onboard measurements.

The process of attitude determination also includes evaluating the telemetry from the various onboard attitude sensors for any sign of physical deterioration, improper configuration, or changes in calibration or alignment. All available attitude telemetry can be processed to compute a best-estimate time history of what the spacecraft attitude was. This history is called definitive attitude.

Most spacecraft carry on-board-computers (OBC) with the capability of computing their own attitude parameters. The attitude data can come via the telemetry from on board or from ground processed attitude determination.

Transfers of spacecraft attitude data from one Agency to another are useful for the following

scenarios:

1)  To ensure scientific observations of specific targets.

2)  To maximize solar energy collection for onboard power usage.

- To ensure successful on orbit, deorbit, or rendezvous operations and maneuvers.

- To ensure and evaluate efficient ground/on-board communication links connected with on-board antenna pattern.

## 5.4.2 Recommendations

The following is a list of recommendations for the transfer of attitude data between Agencies:

Depending on the attitude mode of the spacecraft

- single axis

- three axis

- uncontrolled

- gravity gradient

The attitude evolution can be modelized as kinematic or dynamic

For kinematic models the participant needs

Inertia matrix of the spacecraft

Initial conditions (quaternion) at a given time

Kinematic conditions at the same time

For dynamic models the participant needs

Inertia matrix of the spacecraft

Initial conditions (quaternion) at a given time

Kinematic conditions at the same time

Dynamic conditions at the same time

Applied torques (perturbations or maneuvers)

### 5.4.2.1 Quaternions

The mathematical representation of rigid body rotations is based on EULER angles convenient for attitude kinematics and can be used for rotation or three axis configuration.

It can be defined by:

Q1=e1*sin (Φ/2)

Q2=e2*sin (Φ/2)

Q3=e3*sin (Φ/2)

Q4=cos (Φ/2)

And it must verify Q1*Q1+Q2*Q2+Q3*Q3+Q4*Q4=1

Quaternions are defined in dimensionless units.  Where Φ is the rotation angle between the body frame and the reference frame and e1, e2, e3 are the components of the rotation vector.

### 5.4.2.2 Units

Use of :

- degrees for angles

- degrees/sec for angular velocity

- m**2/kg for inertia matrix

- Tu time for initial conditions

- Tu time for interval of validity

## 5.5 Special Considerations

Many specific cases.

    - RESTITUTION FOR NON-REAL-TIME DATA.

(TBD)

## 5.5.2 Attitude Determination for Spacecraft in Closed Vicinity

Docking missions share in common kinematics and dynamics for orbit and attitude.  For docking missions the attitude information can be absolute or relative.

For formation flying missions the attitude can be connected with one the other partnered spacecraft and can be given relative to a common external reference frame, or to the reference frame of the master satellite in the formation.

In the majority of the cases, the attitude control of the assembly of spacecraft is three axis stabilized.

For these missions, several strategies can be followed to perform the attitude determination tasks: centralized, de-centralized, and mixed. When the spacecraft formation is centralized, one spacecraft (the master) collects information of all others, and solves the problem of the determination of the attitude  for the entire constellation. In a decentralized approach, each spacecraft solves it own attitude state and communicates it to the rest of the constellation. The mixed approach uses features of the other two by multiplexing in time and space the algorithms of the centralized and de-centralized solutions.

For each of the strategies chosen, attitude determination for a spacecraft constellation is a cyclic function which can be split in three fundamental steps: attitude measurements acquisition, attitude propagation, and attitude filtering update. The measurements acquisition comprises the process of extracting the raw data out of the sensors. The attitude propagation function computes the relative quaternions and the relative attitude rates between the spacecraft of the formation. The attitude filtering update prepares the sub-system for the next cycle computations. Attitude determination tasks rely heavily on Kalman filtering techniques and fast propagation algorithms.

### 5.6 DATA TRANSMISSION DELAYS

Data transmission delays must be taken into account in the navigation message broadcasting.

Figure 5-1 shows a typical scenario with data transmission delays: at time T1 a ground station transmits data to a spacecraft. During the transmission of the message the spacecraft has moved to the point T2. Indeed, if this first spacecraft broadcast the same navigation message to another one a further transmission delay can occur.

Figure 5-1: Data transmission delays

# 6. measurements

6.1 RATIONALE

Spacecraft navigation is based on measurements of velocity, distance, and angular direction.

Data for orbit determination is obtained from telemetry or radar tracking signals.

6.2 MEASUREMENT DATA TYPES

6.2.1 ANGLES

Tracking stations on separate locations around the Earth track a single spacecraft simultaneously. High-rate recordings are made of the downlink's wave fronts by each station, together with precise timing data. Antenna pointing angles are also recorded; and the antennas slew directly to the position of  any extragalactic object whose position is known with high accuracy. Then they slew back to the spacecraft. Correlation and analysis of the recorded data yields a very precise triangulation from which both angular position and radial distance may be determined.

6.2.2 RADIO METRIC/TRACKING DATA

Tracking of a spacecraft is a process to establish where the spacecraft actually is in its orbital trajectory at any particular time. Tracking data is obtained from the spacecraft in flight as it passes within the field of signal acquisition from one participant to another.

6.2.3 RANGE

Measurement of distance between the flying spacecraft and other participant(s).

6.2.4 RANGE-RATE

Measurement of relative velocity between the flying spacecraft and other participant(s). Normally the integrated Doppler count is converted to range-rate in a suitable way (Ref. 38).

6.2.5 PHASE

Phase is the relative measure of the alignment of two waveforms of similar frequency, expressed in degrees from 0 to 360.

6.2.6 ACCELERATION

Measurement of body acceleration provided normally by accelerometers or other specific devices.

6.3 EARTH TRACKING (?)

6.4 GPS

NAVSTAR and GLONASS navigation systems provide several observable quantities to the user´ s receivers: the code, the carrier, etc. From the phase of the code, the receiver can extract the pseudorange.  From the frequency of the carrier the receiver can extract the Integrated Doppler Count.  Apart from this observables, the receiver can get the GPS system time. The final output is the so-called PVt (Position, Velocity and time) solution.

[Add text]

## 6.5 Recommendations

The objective here is to facilitate exchanges of tracking data. Tracking data, however, are submitted to a variety of different computational devices. The philosophy now should be more oriented to the simplicity of exchange and the nature of data transmitted. This would guarantee correct usage.

The CCSDS recommends the following items relating to the exchange of tracking data:

- Tracking data should be available for inter-agency support with all parameters given in powers of 10.

- Data should be tagged in UTC by year, month, day, hour, minutes, seconds and decimal fractions of seconds.

- The exact reference time within the measurement window shall be defined in the ICD.

- Differenced observables, which may be derived when two stations are tracking (i.e., VLBI), should be provided in units analogous to Doppler and range.  See Table 3-2.

- Tracking antenna angle data should be provided in degrees and decimal fractions in a system best suited to the antenna mount and defined in the ICD.

- Agencies are encouraged to calibrate for tracking station delay in the tracking data. Initial estimates to be defined in the ICD.  Subsequent measurements to be provided in ancillary messages.

- Agencies are encouraged to provide local measurements of atmospheric conditions (temperature, pressure, and humidity) to aid users in their own media calibration.

- For tracking data transfers in a cross-support activity flags can be defined to indicate data that is substandard. These flags shall be documented in an ICD.

# 7. SATELLITE-BASED GLOBAL NAVIGATION SYSTEMS

## 7.1 Rationale

There is a growing dependency in space applications on orbiting systems such as GLONASS, NAVSTAR, and GalileoSAT.  These systems will be referred to as Global Navigation Systems (GNS).

The development of the present three satellite-based global navigation systems (the U.S.’s NAVSTAR, the former U.S.S.R.’s GLONASS and the European GalileoSAT) represent a huge change in the technology of navigation and positioning. Although initially planned for military purposes, the civil sector (non military) has quickly recognized the potential value of these positioning systems in the areas of civil aviation, marine and ground navigation, spacecraft navigation, and surveying and geodesy. The development of products and services has opened a new market with rapid growth.

The two active constellations for global positioning are the US NAVSTAR system and the Russian GLONASS system. The European GalileoSAT will join these two, officially, in the year 2010.

The USA GPS system NAVSTAR is managed by the U.S. Air Force (USAF) for the Government of the United States. The NAVSTAR satellite constellation is composed of 27 satellites deployed in near-elliptical orbits around the Earth. The satellites are located in 4 orbital planes where each orbital plane contains 6 active satellites.

The Russian GNS system GLONASS is similar to the American NAVSTAR. GPS uses code division multiple access (CDMA) to broadcast its data. Presently, GLONASS is operated by the air command of the Russian military forces. GLONASS is formed also of 24 satellites having 3 orbital planes, with 8 satellites per plane. Unlike GPS, GLONASS uses the Frequency  Division Multiple Access (FDMA) technique to broadcast the data. In Spring 1999, the Council of the European Space Agency has approved the space mission GalileoSAT. At the time of this writing, the definition of the Galileo system is planned to be  completed by the end of the year 2000. Galileo shall be fully operational by the year 2008. It will be inter-operable with the NAVSTAR system. The GalileoSAT constellation will consist of a medium Earth orbit satellite constellation and a number of geostationary satellites plus some other local complements.

Several factors make these global navigation systems attractive to spacecraft navigation:

- Its coverage: It has an almost complete coverage of the Earth for LEO orbits, and a reasonable coverage for HEO orbits.

- Its accuracy: All these systems can or will provide accuracy in orders of magnitude better than conventional ground tracking.  (Refs. 11 and 25).

- Its integrity: The system is guaranteed to function  continuously without performance  degradation.

- Its price: The degraded signal of NAVSTAR is gratis, as well as the GLONASS signals. GalileoSAT will carry both commercial and non-commercial signals.

7.2 RECOMMENDATIONS

RINEX format is recommended for the exchange of GNS measurement in ground to ground scenarios.

# 8. NAVIGATION MESSAGE FORMAT RECOMMENDATION

[A.I.  11]

8.1 RATIONALE

(Why SPKE)

  - SPKE DESCRIPTION

  - SPKE RECOMMENDATION

  - SPKE FOR SPACE APPLICATIONS

# annex a

[A.I. 13]

NAVIGATION DATA MESSAGE EXAMPLE

(THIS ANNEX IS NOT PART OF THE RECOMMENDATION)

A.1  PURPOSE

This annex contains an example of  a navigation message data exchange format for particular applications.

This example should be taken into account during the discussion for a particular recommendation of a more generic format of navigation data message exchange.

## A.2  NORAD Two Line Elements Format

NORAD two line element set is a file containing 3 rows of 69 characters of data which can be used to determine the position and velocity for a space object rotating the Earth.

Figure A-1: Example of a NORAD TLE file

The example of the TLE format is taken from the Orbital Information Group (OIG).

The TLE format contains three lines, namely line 0, line 1 and line 2. Line 0 provides the catalog number and/or possibly other information such as the common name assigned to the satellite. In the example of Figure A-1 the line 0 describes the satellite number, its name, etc.

The structure of the NORAD TLE file format is described in

Table A-1, Table A-2 and Figure A-2.

Table A-1: Structure of first row of the NORAD TLE file

| First Column | Number last | Number of characters | Description |
| --- | --- | --- | --- |
| 1 | 1 | 1 | Line No. Identification |
| 3 | 7 | 5 | Catalog No. |
| 8 | 8 | 1 | Security Classification |
| 10 | 17 | 8 | International Identification |
| 19 | 32 | 14 | YRDOY.FODddddd |
| 34 | 34 | 1 | Sign of first time derivative |
| 35 | 43 | 9 | 1st Time Derative |
| 45 | 45 | 1 | Sign of 2nd Time Derivative |
| 46 | 50 | 5 | 2nd Time Derivative |
| 51 | 51 | 1 | Sign of 2nd Time Derivative Exponent |
| 52 | 52 | 1 | Exponent of 2nd Time Derivative |
| 54 | 54 | 1 | Sign of Bstar/Drag Term |
| 55 | 59 | 5 | Bstar/Drag Term |
| 60 | 60 | 1 | Sign of Exponent of Bstar/Drag Term |
| 61 | 61 | 1 | Exponent of Bstar/Drag Term |
| 63 | 63 | 1 | Ephemeris Type |
| 65 | 68 | 4 | Element Number |
| 69 | 69 | 1 | Check Sum, Modulo 10 |

Table A-2: Structure of the second row of the NORAD TLE file

| First Column | Number last | Number of characters | Description |
| --- | --- | --- | --- |
| 1 | 1 | 1 | Line No. Identification |
| 3 | 7 | 5 | Catalog No. |
| 9 | 16 | 8 | Inclination |
| 18 | 25 | 8 | Right Ascension of Ascending Node |
| 27 | 33 | 7 | Eccentricity with assumed leading decimal |
| 35 | 42 | 8 | Argument of the Perigee |
| 44 | 51 | 8 | Mean Anomaly |
| 53 | 63 | 11 | Revolutions per Day (Mean Motion) |
| 64 | 68 | 5 | Revolution Number at Epoch |
| 69 | 69 | 1 | Check Sum Modulo 10 |

Figure A-2: Graphical representation of the NORAD TLE file format

A.3  EXAMPLES OF QUALITY

# ANNEX B

GLOSSARY

(THIS ANNEX IS NOT PART OF THE RECOMMENDATION)

B.1 PURPOSE

This annex provides a glossary of navigation terminology.

Ancillary data: Data other than instrument data required to perform an instrument's data processing. They include orbit data, attitude data, time information, spacecraft engineering data, calibration data, data quality information, and data from other instruments.

Apogee: The point in an orbit furthest away from the Earth. The point in an orbit when the geometric distance is a maximum.

Attitude: The direction in which a spacecraft is oriented in space.

Doppler:  The apparent change in the frequency of a signal caused by the relative motion of the transmitter and receiver.

Eccentricity:  The ratio of the distance from the center of an ellipse to its focus to the semimajor axis.

Ephemeris:  A list of (accurate) positions and velocities of satellite as a function of time.

Epoch: Epoch signifies the beginning of an era (or event) or the reference date of a system of measurements.

Global Positioning System (GPS): A highly accurate, global satellite navigation system based on a constellation of 24 satellites orbiting the earth at a very high altitude. In addition to navigation, the system also provides very precise time.

Inclination:  The angle between the orbital plane of a body and its equatorial plane.

Orbit: The path followed by a celestial body.

Orbital elements:  A set of parameters describing any astronomical  or spacecraft orbit.

Phase angle: The angle between the Sun, an object, and an observer.

Perigee: The point in an orbit of closest approach to the Earth. The point in an orbit when the geometric distance is a minimum.

Nutation: The short-period oscillations in the motion of the pole of rotation of a freely rotating body that is undergoing torque from external gravitational forces. Nutation of the Earth's pole is difined in terms of components in obliquity and longitude.

Polar motion:  Motion of the instantaneous axis of the rotation of the Earth with respect to the solid body of the Earth.  Irregular but more or less circular motion with an amplitude  of about 15m and a main period of about 430 days (called Chandler Wobble).

Precession: The change in orientation of a spinning body's rotational axis.

Range rate:  The rate of change of range between the satellite and receiver.  The range to a satellite changes due to satellite and observer motions. Range rate is determined by           measuring the Doppler shift of the satellite beacon carrier.

Right ascension of ascending node:  The angular distance measured from the vernal equinox, positive to the east, along the celestial equator to the ascending node.

RINEX:  A set of standard definitions and formats to promote the free exchange of GPS data and facilitate the use of data from any GPS receiver with any software package.

SPK: "Spacecraft and Planet Kernel". It is a file element of the SPICE system devised and maintained by the NAIF (Navigational and Ancillary Information Facility) team at JPL. SPK files may hold ephemerides for any kind of spacecraft, vehicle, or solar system body.

SPICE kernel contents are summarized below:

S- Spacecraft ephemeris, or more generally, location of an observer, given as a function of time.

P- Planet, satellite, comet, or asteroid ephemerides, or more generally, location of a target body, given as a function of time.

The ephemeris data for spacecraft and target bodies are normally combined in a single file called the SPICE SPK file. (But either target ephemerides alone or a spacecraft ephemeris alone can be held in an SPK file; it is not necessary that both types be present.)

The P kernel also logically includes certain physical, dynamical and cartographic constants for target bodies, such as size and shape specifications, and orientation of the spin axis and prime meridian. These target body physical and cartographic constants are found in the SPICE PCK file.

I- Instrument description kernel, containing descriptive and operational data peculiar to a particular scientific instrument, such as mounting alignment, internal timing relative to the spacecraft clock, and field-of-view model parameters. This instrument information is contained in the SPICE IK file.

C- Pointing kernel, containing a transformation traditionally called the C-matrix that provides time-tagged pointing (orientation) angles for a spacecraft structure upon which science instruments are mounted. Attitude data are contained in the SPICE CK file.

E- Events kernel, the principal contents of which are derived from the integrated sequence of events used to produce actual spacecraft commands. Events data are contained in the SPICE EK file set. (There are three components to the EK).

INDEX

(THIS CHAPTER IS NOT PART OF THE RECOMMENDATION)

Index to be added here.

# Text boxes

25107 Iridium 48

1 25107U 97082D   98151.26839894 -.00007632  00000-0 -27359-2 0  1321

2 25107  86.3970 282.3520 0003565  65.4476 294.7132 14.34205441 23251

!>Line Number 1

!   !>Catalog Number (NORAD)

!   !  !>Security Classification for this Element Set

!   !  !    !>International Identification for this Object (COSPAR)

!   !  !    !     !>Two Digit Year

!   !  !    !     !  !>Day of Year

!   !  !    !     !  !     !>Fraction of 24 Hour Day

!   !  !    !     !  !     !     !>Sign of 1st Time Derivative

!   !  !    !     !  !     !     !    !>1st Time Derivative

!   !  !    !     !  !     !     !    !     !>Sign of 2nd Time Derivative

!   !  !    !     !  !     !     !    !     !  !>2nd Time Derivative

!   !  !    !     !  !     !     !    !     !  !  !>Sign of exponent

!   !  !    !     !  !     !     !    !     !  !   !>Exponent 2ndTimeDerivative

!   !  !    !     !  !     !     !    !     !  !     !>Sign of BSTAR drag term

!   !  !    !     !  !     !     !    !     !  !     !  !>BSTAR/Drag Term

!   !  !    !     !  !     !     !    !     !  !     !  !  !>Sign of Exponent

!   !  !    !     !  !     !     !    !     !  !     !  !  !!>Exponent BstarDrg

!   !  !    !     !  !     !     !    !     !  !     !  !  !! !>Ephemeris Type

!   !  !    !     ! ---    !     !    !     !  !     !  !  !! ! !>Element No.

! -----! -------- --|||--------- !--------- !-----   !-----!! ! ----!>Checksum

1 25107U 97082D   98151.26839894 -.00007632  00000-0 -27359-2 0  1321 = Line 1

2 25107 086.3970 282.3520 0003565 065.4476 294.7132 14.34205441 23251 = Line 2

123456789012345678901234567890123456789012345678901234567890123456789 = columns

! ----- ---.---- ---.---- ------- ---.---- ---.---- --.--------|||||!>Checksum

!   !   Incl     RAAN     Ecc     AoP      MA       RpD        -----

!   !   !        !        !       !        !        !          !>Rev # @ Epoch

!   !   !        !        !       !        !        !>MeanMotion(Revolutions/Day)

!   !   !        !        !       !        !>Mean Anomaly

!   !   !        !        !       !>Argument of Perigee

!   !   !        !        !>Eccentricity, with assumed decimal point leading

!   !   !        !>Right Ascension of Ascending Node

!   !   !>Inclination

!   !>Catalog Number (NORAD)

!>Line Number 2