Tracking Wildlife from Space

by Patrick Barry

It's 10 o'clock, and do you know where your Oriental Honey Buzzard is?

Tracking the whereabouts of birds and other migrating wildlife across thousands of miles of land, air, and sea is no easy feat. Yet to protect the habitats of endangered species, scientists need to know where these roving animals go during their seasonal travels.

Rather than chasing these animals around the globe, a growing number of scientists are leveraging the bird's-eye view of orbiting satellites to easily monitor animals' movements anywhere in the world.

The system piggybacks on weather satellites called Polar Operational Environmental Satellites, which are operated by the National Oceanic and Atmospheric Administration (NOAA), as well as a European satellite called MetOp. Sensors aboard these satellites pick up signals beamed from portable transmitters on the Earth's surface, 850 kilometers below. NOAA began the project—called Argos—in cooperation with NASA and the French space agency (CNES) in 1974. At that time, scientists placed these transmitters primarily on buoys and balloons to study the oceans and atmosphere. As electronics shrank and new satellites' sensors became more sensitive, the transmitters became small and light enough by the 1990s that scientists could mount them safely on animals. Yes, even on birds like the Oriental Honey Buzzard.

“Scientists just never had the capability of doing this before,” says Christopher O'Connors, Program Manager for Argos at NOAA.

Today, transmitters weigh as little as 1/20th of a pound and require a fraction of a watt of power. The satellites can detect these feeble signals in part because the transmitters broadcast at frequencies between 401 and 403 MHz, a part of the spectrum reserved for environmental uses. That way there's very little interference from other sources of radio noise.

“Argos is being used more and more for animal tracking,” O’Connors says. More than 17,000 transmitters are currently being tracked by Argos, and almost 4,000 of them are on wildlife. “The animal research has been the most interesting area in terms of innovative science.”

For example, researchers in Japan used Argos to track endangered Grey-faced Buzzards and Oriental Honey Buzzards for thousands of kilometers along the birds' migrations through Japan and Southeast Asia. Scientists have also mapped the movements of loggerhead sea turtles off the west coast of Africa. Other studies have documented migrations of wood storks, Malaysian elephants, porcupine caribou, right whales, and walruses, to name a few.

Argos data is available online at www.argos-system.org, so every evening, scientists can check the whereabouts of all their herds, schools, and flocks. Kids can learn about some of these endangered species and play a memory game with them at spaceplace.nasa.gov/en/kids/poes_tracking.

This article was provided by the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration.

Caption:

The ARGOS program tracks the whereabouts of endangered migrating animals via miniature transmitters on the animals and the POES satellites in orbit.

Note to editors:

This image may be downloaded at http://spaceplace.nasa.gov/news_images/argos_tracking.jpg.