Specifications/Requirements for Purchase Request RBD.1183

| Item | Description | Qty |
| --- | --- | --- |
| 1 | Digital Pressure Indicator Range: 1 psi differential or lower Precision: 0.004% of FS Resolution: 0.001 inH20 or better Stability: 0.01% per year Zero Drift: 0.005% of full scale per 24 hours Re-zeroing capability Digital Display Display Resolution: 0.000001 Pressure Medium: air or nitrogen Programmable via IEEE-488 Interface LabVIEW driver NIST traceable calibration Rack mount | 1 |
| 2 | Digital Pressure Indicator Range: 1 psi differential Precision: 0.004% of FS Resolution: 0.001 inH20 or better Stability: 0.01% per year Zero Drift: 0.005% of full scale per 24 hours Re-zeroing capability Digital Display Display Resolution: 0.000001 Pressure Medium: air or nitrogen Programmable via IEEE-488 Interface LabVIEW driver NIST traceable calibration Rack Mount | 1 |
| 3 | Digital Pressure Indicator Range: 5 psi differential Precision: 0.003% of FS Resolution: 0.001 inH20 or better Stability: 0.01% per year Zero Drift: 0.005% of full scale per 24 hours Re-zeroing capability Digital Display Display Resolution: 0.000001 Pressure Medium: air or nitrogen Programmable via IEEE-488 Interface LabVIEW driver NIST traceable calibration Rack Mount | 1 |