WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A11138 | In-Flight Anomaly Number -- | Contractor Report Number S-074 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title MANHOLE COVER BOLT THREADS WERE DISTORTED ON LWT 24 |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT 1 | Sys_Lvl N | Misc Codes A (2) B (X) C D E (X) F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE ET COMPLETE | PART# 80901000000 | SER/LOT# NOTED | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE MAN HOLE COVER | PART# 80911001449 | SER/LOT# TBD | MANUFACTURER MMC |
| HARDWARE NCA | NOMENCLATURE BOLT | PART# 26L2-5H10 | SER/LOT# N/A | MANUFACTURER UNKNOWN |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U UC | Fail Mode UC - UNSAT | Cause MAW - MFG-ASY-WORK |
| System PROPULSION | Defect MA - ME ADJ | Material L - FASTNR | Work Contact C. VOGEL | Fail Date 12/14/1987 |
| Received at MSFC 12/21/1987 | Date Isolated -- | FMEA Reference 2.10.6.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom UC - UNSAT | Time Cycle N/A |
| Effectivity Text LWT 16, 20, 21, 22, 24 AND UP |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 09/10/1992 | CN RSLV SBMT 03/14/1988 | Defer Date -- | Add Date 12/23/1987 | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design F. HUNEIDI | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| Approval |
| Design F. HUNEIDI | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 04/28/1988 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description AFTER REMOVAL OF THE MANHOLE COVER BOLTS ON LWT-24 TO PERFORM ECO SENSOR BRACKET MODIFICATIONS, ONE BOLT OUT OF NINETY TWO WAS DISCOVERED TO HAVE A MAJOR PART OF THE THREADS DISTORTED. IT IS SUSPECTED THAT THIS CONDITION WAS CAUSED BY INTERFERENCE WITH THE NAFLEX INCONEL SEAL |
| Contractor Investigation/Resolution RECURRENCE CONTROL: MANUFACTURING PROCESS PLANS HAVE BEEN REVISED TO IMPROVE INSTRUCTIONS ON PROPER SEAL ALIGNMENT AND USE OF ALIGNMENT PINS AND BOLT INSTALLATION. AND, THE DESIGN OF THE ALIGNMENT PIN WAS IMPROVED AND THE NEW DESIGN FABRICATED CAUSE OF FAILURE: IMPROPER INSTALLATION OF THE BOLT (POSITION 43 ON THE MANHOLE COVER). THE BOLT THREADS WERE DISTORTED BY AN INTERFERENCE WITH THE NAFLEX INCONEL SEAL DURING INSTALLATION GENERAL DURING KSC REMOVAL OF THE LH2 AFT MANHOLE COVER ON LWT-24, IT WAS OBSERVED THAT ONE OF THE 92 ATTACHING BOLTS HAD ALL THREADS DISTORTED EXCEPT THE LEADING THREE. KSC PERSONNEL GENERATED PR PV6-087153 (ET-31-ST-00-0023) TO DOCUMENT THIS DISCREPANCY. EVIDENCE SHOWED THAT THE SLOTTED HOLE ON THE SEAL RECEIVED SOME DAMAGE WHERE THE BOLT WAS LOCATED (POSITION 43, -Y AXIS). IT WAS DECIDED, AT THAT TIME, THAT FAILURE ANALYSIS WOULD TAKE PLACE AT KSC WITH SUPPORT BY MMC, AND THAT MMC WOULD DETERMINE AND IMPLEMENT CORRECTIVE ACTION. THIS CAPS SHALL REPORT THE RESULTS OF THE FAILURE ANALYSIS AND DOCUMENT THE CORRECTIVE ACTIONS INVESTIGATIONS TOOK PLACE AT MMC TO DETERMINE THE APPROPRIATE CORRECTIVE ACTION. THIS LED TO THE FOLLOWING CONCLUSIONS WHICH ARE ALSO DOCUMENTED IN THE RESPONSE TO AR NO. K7184 TOLERANCE STUDY: O .003 INCH MAXIMUM BOLT TO SEAL INTERFERENCE AT +/- Y AXIS (PROPER USE OF GUIDE PINS) O .064 INCH MAXIMUM BOLT TO SEAL INTERFERENCE AT +/- Y AXIS (IMPROPER USE OF GUIDE PINS) PROCEDURE STUDY: O PROPER USE OF THE GUIDE PINS WOULD REQUIRE THAT THE PINS BE INSTALLED IN THE SLOTTED HOLES, THAT THE SLOTTED HOLES BE ALIGNED WITH THE +/- Y AND +/- Z AXIS, AND THAT THE GUIDE PINS BE REMOVED ONE AT A TIME AND A BOLT BE INSTALLED SNUGGLY PRIOR TO REMOVAL OF THE NEXT GUIDE PIN O THE MANUFACTURING PROCESS PLAN (MPP) DID NOT SPECIFICALLY REQUIRE THE PROCEDURES DEFINED ABOVE DAMAGED BOLT STUDY: O 8300 POUND PULL STRENGTH WAS ACHIEVED WITH DAMAGED BOLTS HAVING ONLY THREE LEADING THREADS (SIMILAR TO LWT-24) O 8300 POUNDS IS FAR IN EXCESS OF FLIGHT LOADS DUPLICATION OF FAILURE STUDY: O .025 INCH MAXIMUM INTERFERENCE FROM BOLT TO SEAL EDGE COULD BE ACCOMPLISHED WITH THE BOLT ENGAGED INTO THE KEENSERT O .020 INCH INTERFERENCE FROM BOLT TO SEAL EDGE RESULTED IN DAMAGE TO THE BOLT ALMOST IDENTICAL TO LWT-24 A DETAILED ACCOUNTING OF THE ABOVE INFORMATION WAS PROVIDED BY THE RESPONSE TO AR NO. K7184 WHICH IS TASK I.B. IN THIS CAPS TASK I FAILURE/PROBLEM INVESTIGATION A. FAILURE ANALYSIS BY KSC KSC (NASA) HAS BEEN TASKED TO PERFORM THE FAILURE ANALYSIS ON THE DAMAGED BOLT FROM LWT-24 LH2 MANHOLE COVER PER A TELECON MEETING BETWEEN KSC, MSFC, AND MMC (MAF) PERSONNEL. THE RESULTS OF THAT FAILURE ANALYSIS SHALL BE OBTAINED AND PRESENTED TO RELIABILITY ASSURANCE, DEPARTMENT 3741 CLOSURE STATEMENT A REPORT WAS FORWARDED FROM KSC TO MMC, MAF. REFERENCE REPORT NO. MAB-229-87. THIS REPORT CONCLUDED THAT THE DAMAGED THREADS SEEN ON THE LWT-24 MANHOLE COVER BOLT WERE THE RESULT OF MACHINING THE BOLT THREADS PRIOR TO FINAL INSERTION. INVESTIGATIONS MADE AT MAF COULD NOT AFFIRM THIS CONCLUSION, AND IT IS THE CONCLUSION FROM THE INVESTIGATIONS MADE AT MAF THAT ARE REFLECTED IN THIS CAPS (I.E. THE BOLT THREADS WERE DAMAGED BY AN INTERFERENCE WITH THE NAFLEX INCONEL SEAL DURING INSTALLATION) B. RESPONSE TO AR NO. K7184 A MSR ACTION RESPONSE, K7184, WAS INITIATED AT KSC AS A RESULT OF THE PROBLEM WITH THE LH2 MANHOLE COVER. MMC (MAF) RESPONDED TO THIS AR AND PROVIDED ADDITIONAL RESPONSE, PER "PART B" ON THE AR. THIS TASK DOCUMENTS THAT RESPONSE CLOSURE STATEMENT THE RESPONSE TO AR NO K7184 WAS MADE ON THAT DOCUMENT WITH "PART B" ATTACHED. THAT RESPONSE IS ALSO REFLECTED IN THIS CAPS UNDER THE "GENERAL" SECTION ITEM CLOSED TASK II CORRECTIVE ACTION A. REVISE MANUFACTURING PROCESS PLANS (MPPS) REVISE THE MPPS (FOR ALL MANHOLE COVERS) TO INCLUDE WHERE THE SLOTTED HOLES IN THE SEAL SHALL BE LOCATED, AND TO REQUIRE THE REMOVAL OF ALIGNMENT PINS AND THE INSTALLATION OF BOLTS ONE AT A TIME AFTER THE OTHER 88 FASTENERS ARE INSTALLED CLOSURE STATEMENT THE MPPS WERE REVISED FOR ALL COVER INSTALLATIONS (TWO LO2 LOCATIONS AND THREE LH2 LOCATIONS), IMPLEMENTED FOR LWT-44 AND UP WITH PARTIAL IMPLEMENTATION AS PRODUCTION PERMITTED FOR LWTS 41, 42, AND 43. REFERENCE INTEROFFICE MEMORANDUM 3614-88-030 ITEM CLOSED B. IMPROVE ALIGNMENT PIN DESIGN REVIEW THE ALIGNMENT PIN DRAWING AND REVISE THE DESIGN OF THE ALIGNMENT PIN TO REDUCE THE THREAD LENGTH AND INCREASE THE SHANK DIAMETER CLOSURE STATEMENT THE ALIGNMENT PIN THREAD LENGTH WAS CHANGED FROM .50 TO .20 AND THE SHANK DIAMETER WAS CHANGED FROM .312 TO .320 (INCHES). THIS WILL PROVIDE A CLOSER FIT IN THE SLOTTED HOLES AND THUS ADDED ASSURANCE AGAINST AN INTERFERENCE FIT. IMPLEMENTED AS OF LWT-42. REFERENCE INTEROFFICE MEMORANDUM 3614-88-030 AND TOOL ORDER TL-0620-010A TASK III CLEARANCE OF EFFECTIVITIES LWTS 16, 20, 21, 22, 24 AND UP NO CONTRAINTS. ENGINEERING ANALYSIS, IN AR NO. K7184, DETERMINED THAT THE DAMAGE TO THE BOLT THREADS, AS SEEN ON LWT-24, IS NOT DETRIMENTAL TO THE FLIGHT PERFORMANCE OF THE ET. THIS ANALYSIS JUSTIFIES THE POSITION NOT TO INSPECT THE FLEET FOR BOLT DAMAGE ON MANHOLE COVER. THIS SPECIFIC ANALYSIS ALSO JUSTIFIES THE CLASSIFICATION OF THIS CAPS AS A CRITICALITY 3 RATHER THAN CRITICALITY 1 PER FMEA ITEM CODE 2.10.6.1 AND 6.2.1.1 TASK IV. CAPS CLOSEOUT SUMMARY * IN THE PROCESS OF EVALUATING APPROPRIATE CORRECTIVE ACTION, INVESTIGATIONS WERE CONDUCTED AT MAF TO EVALUATE THE CAUSE OF THE BOLT THREAD DEFORMATION AS SEEN IN POSITION 43 ON THE LWT-24 LH2 AFT MANHOLE COVER. THESE INVESTIGATIONS CONCLUDED THAT THE BOLT DAMAGE WAS CAUSED BY INTERFERENCE WITH THE EDGE OF THE SLOTTED HOLE IN THE SEAL DURING INSTALLATION OF THE MANHOLE COVER AT MAF. IN TURN, THE IMPROPER BOLT INSTALLATION PROBABLY RESULTED FROM THE ASSEMBLY GUIDE PINS BEING PLACED IN THE WRONG LOCATIONS AND/OR THE GUIDE PINS BEING IMPROPERLY CHANGED OUT FOR BOLTS DURING INSTALLATION CORRECTIVE ACTIONS WERE IMPLEMENTED TO PRECLUDE THE RE- OCCURRENCE OF THIS PROBLEM. MANUFACTURING PROCESS PLANS WERE REVISED TO IMPROVE INSTRUCTIONS ON PROPER SEAL ALIGNMENT AND USE OF ALIGNMENT PINS AND BOLT INSTALLATION. AND, THE DESIGN OF THE ALIGNMENT PIN WAS IMPROVED AND THE NEW DESIGN FABRICATED. THESE IMPROVEMENTS WERE INCORPORATED IN THE INSTALLATION OF ALL MANHOLE COVERS AS REFLECTED HERE: A. UPDATED BY REDLINE: LWT-41 L02 AFT COVER INST. 80911001204-009 LWT-42 L02 FWD COVER INST. 80911001206-010 LWT-42 L02 AFT COVER INST. 80911001204-009 LWT-42 L02 AFT NON-SIPHON COVER INST. 80911001449-010 LWT-43 L02 AFT COVER INST. 80911001204-009 LWT-43 L02 FWD COVER INST. 80911001206-010 LWT-43 L02 AFT NON-SIPHON COVER INST. 80911001449-010 LWT-44 L02 FWD COVER INST. 80914081490-009 B. INCORPORATED BY WORD PROCESSOR UPDATE: LWT-44 & UP L02 AFT COVER INST. 80911001204-009 LWT-44 & UP L02 FWD COVER INST. 80911001206-010 LWT-44 & UP LH2 AFT SIPHON COVER INST. 80911001449M019 LWT-44 & UP LH2 AFT NON-SIPHON COVER INST. 80911001449-019 LWT-45 & UP LH2 FWD COVER INST. 80914081490-009 THE CORRECTIVE ACTIONS TAKEN HERE ARE CONSIDERED TO BE ADEQUATE WITH NO FURTHER ACTION NEEDED TO ADDRESS THE FLEET (BUILT HARDWARE). BY TESTING, IT WAS SHOWN THAT THREE THREAD ENGAGEMENT (SAME CONFIGURATION AS ON LWT-24) PROVIDED PULL STRENGTH OF 8300 POUNDS FAR IN EXCESS OF FLIGHT LOADS OF 6340 POUNDS. FINALLY, IT MAY ALSO BE NOTED THAT THE PROBABILITY OF THE OCCURRENCE OF THIS TYPE OF DAMAGE DURING INSTALLATION IS CONSIDERED TO BE VERY LOW |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A11138 | IFA# -- | Contractor RPT# S-074 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 26L2-5H10 | Asmnt Part Name BOLT | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE UC - UNSAT |
| Asmnt FMEA 2.10.6.1 | Asmnt FM 1 | FMEA CSE A | FMEA SCSE 1 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |