Oral Presentation 6A-04

Corn Fiber Pretreatment Scale-up and Evaluation in an

Industrial Corn to Ethanol Facility

Nathan S Mosier1,2, Richard Hendrickson2, Gary Welch3, Richard Dreschel 3,

Bruce Dien4, and Michael Ladisch1,2,5*

1Department of Agricultural and Biological Engineering

Purdue University, West Lafayette, IN 47907

Phone: 765-494-7022; Fax: 765-494-7023; E-mail: ladisch@ecn.purdue.edu

2Laboratory of Renewable Resources Engineering

Purdue University

3Williams Bioenergy

1300 S. 2nd Street, P.O. Box 10

Pekin, IL 61555-0010

4USDA NCAUR Laboratories

Peoria, IL 61604

5Department of Biomedical Engineering

Purdue University

The design and scale-up of an effective pretreatment process has been tested in a commercial fuel ethanol plant using commercial scale equipment.  This pretreatment process requires multiple steps and unit operations.  First the substrate feed enters a mixing tank where the solids (corn fiber at 60% moisture) and liquid (stillage) are combined.  The resulting slurry is heated through a combination of stem injection and heat exchange.  The heat exchanger transfers heat from the fiber/stover stream leaving the pretreatment reactor to the fiber/stover entering the pretreatment reactor, and the second injection served to attain the final operating temperature 160(C.  The hot fiber/stover stream entered a plug-flow reactor (snake coil) and was held for less than a half hour.  This was sufficient to dissolve about 60% of the dry weight of the corn fiber.  The resulting oligosaccharides gave both hexoses and pentoses upon enzyme hydrolysis.  Subsequent fermentation trials showed that the hydrolysate was fermentable without any obvious inhibition.  This paper reports physical and compositional changes of the fiber as a consequence of the pretreatment, as well as material and energy balances for the process.  A model that relates pretreatment conditions to changes in the fiber structure, composition, and hydrolysis upon subsequent addition of enzyme is described.  A first estimate of the economics for the process will also be discussed.