Trends in Chromium and Lead Concentrations in Petroleum Refinery Waste

Regulatory Developments

On September 8, 1994, EPA issued a final MACT rule that eliminated the use of chromium-based water treatment chemicals and subsequently chromium compound emissions from IPCTs.

On October 18, 2005, EPA proposed no changes to a rule that governs emissions of toxic air pollutants from IPCTs.

(EPA required to assess the residual risk remaining after the implementation of the 1994 standards.)

Waste Characterization Data

Land Disposal Restrictions – BDAT Background Documents

## Concentration Ranges of Selected Metals in Petroleum Refinery Listed Wastes (mg/kg)*

|  | Chromium | Lead |
| --- | --- | --- |
| K048 | 0.04 - 3435 | 0.05 - 1250 |
| K049 | 28.9 - 1400 | 21.95 - 3900 |
| K050 | 11 – 1600 | 0.5 – 1100 |
| K051 | 0.1 - 6790 | 0.25 - 2480 |
| K052 | 1.0 - 504 | 11 - 5800 |
| K169 | 9.7 - 310 | 44 - 870 |
| K170 | 8.4 - 34 | 17 - 47 |
| F037 | 12 - 2020 | 22 - 4570 |
| F038 | 2.5 - 2990 | <1 - 3900 |
| Composite Range | 0.04 – 6790**** | 0.05 – 5800***** |
| Petroleum Coke **** | 1.3 | 1.5 |

*         Total waste characterization data from the Land Disposal Restrictions (LDR) Background Documents for K048-K052 (1988),

F037-F038(1992), and K169-172 (1998).

**        If ND or BDL was reported, the next largest value was used in determining the range.

## ***      If the concentration was reported as a “less than” , the reported value was used without the “less than” designation.

## ****    Data from Jacobs Engineering Company.  Assessment of Hazardous Waste Practices in the Petroleum Refining Industry, June 1976

*****  American Petroleum Institute.  1983.  1982 Refinery Solid Waste Survey.  Prepared by Environmental Resources Management

Recent Waste Characterization Data

Tesoro Mandan Refinery

K051 - API Separator Sludge

| Analyte | Tesoro Material 1996 Tesoro Lab Analyses 2001 Sample Conc. (mg/kg TOTAL) | Tesoro Material 1996 Tesoro Lab Analyses 2001 Sample Conc. (mg/L TCLP) | Tesoro Material 2004 DGC Annual Report (Table 2) Avg. Concentration (mg/kg TOTAL) | Tesoro Material 2004 DGC Annual Report (Table 2) Avg. Concentration (mg/L TCLP) | Tesoro Material NDDH Lab Analyses Avg. Concentration (mg/kg-TOTAL) |
| --- | --- | --- | --- | --- | --- |
| Chromium (total) | 475 | <0.05 | 47.33 (90% reduction) | <0.05 | 110 (76% reduction) |
| Lead | 6550 | 1.5 | 1686 (74% reduction) | 0.485 | 1760.23 (73% reduction) |

From: Revised Constituent List for a “Revised DGC/Tesoro RCRA Treatability Study Sampling and Analysis Plan”

Sinclair Casper Refining Company Evansville, Wyoming

Heat Exchanger Cleaning Sludge and Leaded Tank Bottoms (K050/K052) Waste Characteristics

| Compound | Sinclair Material 1993 (mg/kg) | Sinclair Material 1994 (mg/kg) | Sinclair Material 2006 (mg/kg) |
| --- | --- | --- | --- |
| BTU | --- | --- | 7844 BTU/lb |
| Chromium, total, | 576 | 230 | 78 (86% and 66% reductions) |
| Lead, total | 210 | 810 | 251 |

From:  State of Wyoming Department of Environmental Quality, Solid and Hazardous Waste Division, Hazardous Waste Management

Facility Permit for Sinclair Casper Refining Company, Evansville Wyoming.  July 5, 2006

Sinclair Casper Refining Company Evansville, Wyoming

API Separator Sludge (K051) -- Laboratory Analytical Reports

(02.14.2003)

| Metal – Total Concentration | Concentration (mg/kg) |
| --- | --- |
| Chromium | 155 |
| Lead | 74 |

From:  State of Wyoming Department of Environmental Quality, Solid and Hazardous Waste Division, Hazardous Waste Management Facility Permit for Sinclair Casper Refining Company, Evansville Wyoming.  July 5, 2006

Sinclair Oil Corporation

Crude Oil Tank Sediment (K169-Solids) – Report of Analysis

Analysis Date 06.18.2003

| Metal - Total | Concentration (mg/kg) 1995 Listing Document | Concentration (mg/kg) |
| --- | --- | --- |
| Chromium | 51 | 90 (76% increase) |
| Lead | 320 | 172 (46% reduction) |

From:  State of Wyoming Department of Environmental Quality, Solid and Hazardous Waste Division, Hazardous Waste Management Facility Permit for Sinclair Casper Refining Company, Evansville Wyoming.  July 5, 2006

Sinclair Oil – Caspar Refinery

Clarified Slurry Oil Sediment (K170) - Laboratory Analytical Report

Collection 03.20.2006  Analyzed 03.2006

| Metal – Total | Concentration (mg/kg) 1995 Listing Document | Concentration (mg/kg) |
| --- | --- | --- |
| Chromium | 25 | 13 (48% reduction) |
| Lead | 23 | 28 (21% increase) |

From:  State of Wyoming Department of Environmental Quality, Solid and Hazardous Waste Division, Hazardous Waste Management Facility Permit for Sinclair Casper Refining Company, Evansville Wyoming.  July 5, 2006

Chromium and Lead Trend Data (1988-2007)

BP Whiting Refinery, Whiting, Indiana

| BDAT List Constituent | K048 (1988) mg/kg | K048/F038 Mean (2000-2006) mg/kg | K048/F038 Range (2000-2006) mg/kg | K051 (1988) mg/kg | K051/F037 Mean (2000-2006) mg/kg | K051-F037 Range (2000-2006) mg/kg | F037/F038/ K048/K051 Mean (1995-1999) mg/kg | F037/F038/ K048/K051 Range (1995-1999) mg/kg | F037/F038/ K048/K051 Mean (2003-2006) mg/kg | F037/F038/ K048/K051 Range (2003-2006) mg/kg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Chromium (total) | 810-960 | 6.18 (54 data pts) | <1-75.3. | 730-1100 | 35.37 (54 data pts) | 0.32-89.9- | 4.98 (27data pts) | 0.24-6.5 | 20.2 (23 data pts) | 10-87.6 |
| Lead | 330-410 | 91.8 (54 data pts) | 0.8-444 | 640-940 | 92.81 (54 data pts) | 0.8-571 | 112.3 (27 data pts) | 19-460 | 346.8 (23 data pts) | 164-1220 |

References:

1.  Best Demonstrated Available Technology (BDAT) Background Document for K048, K049, K050, K051, K052.  August 1988.

2.  EPA/530-SW-88-031C.  (USEPA.  Onsite Engineering Report of Treatment Technology Performance and Operation for Amoco Oil Company, Whiting Indiana.  February 29, 1998.)

3.  BP Whiting Refinery Incinerator Feed Data. 1995-2006.  January 2007.

4.  Heat of Combustion ranges between <100 - 6400 BTU /lb.

K048   Dissolved air flotation (DAF) float from the petroleum refining industry

F038   Secondary oil/water/solids separator sludge

K051   API separator sludge from the petroleum refining industry

F037   Primary oil/water/solids separator sludge

From:  Final Best Demonstrated Available Technology (BDAT) Background Document for Newly Listed Refinery Wastes F037 and F038.  June 30, 1992

“A comparison of F037 and F038 characterization data with those for K051 and K048 indicates that many of the constituents identified in K051 and K048 are also present at similar concentration in F037 and F038.  Based on the similarities of industry, processing stages, and waste characterization data between F037,F038,K048 and K051, the Agency believes that F037 and F038 can be treated to similar concentrations using identical technologies as those identified for K048 and K051.  EPA is therefore placing F037 and F038 into the same waste treatability group as K048-K052.”

Analysis of Waste Characterization Data

## Comparison of Concentration Ranges of Selected Metals in Petroleum Refinery

## Wastes (mg/kg) Between LDR Data and Newly Acquired Data*

|  | Chromium | Lead |
| --- | --- | --- |
|  | LDR Data 1976-1994 | New Data 1995-2006 | LDR Data 1976-1994 | New Data 1995-2006 |
| K048 | 0.04-3435 | <1-75.3 | 0.05-1250 | 0.8-444 |
| K049 | 28.9-1400 | ----- | 21.95-3900 | ----- |
| K050 | 11-1600 | 78 | 0.5-1100 | 251 |
| K051 | 0.1-6790 | 0.32-155 | 0.25-2480 | 0.8-1760 |
| K052 | 1.0-504 | 78 | 11-5800 | 251 |
| K169 | 9.7-310 | 51-90 | 44-870 | 172-320 |
| K170 | 8.4-34 | 13-25 | 17-47 | 23-28 |
| F037 | 12-2020 | 0.32-89.9 | 22-4570 | 0.8-571 |
| F038 | 2.5-2990 | <1-75.3 | <1-3900 | 0.8-444 |
| Composite Range | 0.04-6790 | 0.32-155 | 0.05-5800 | 0.8-1760 |

Relative Ranking of Generated Waste Quantities for Listed Petroleum Refinery Wastes

2003 Biennial Report

| Waste Code | Description of Waste | Relative Rank Calculated Quantity Generated (tons) | Concentration Range Reported Chromium | Concentration Range Reported Lead |
| --- | --- | --- | --- | --- |
| F037 | Primary oil/water/solids separator sludge | 107,175 | 0.32-89.9 | 0.8-571 |
| K048 | Dissolved air flotation (DAF) float | 34,918 | <1-75.3 | 0.8-444 |
| K169 | Crude oil tank sediment | 23,456 | 51-90 | 172-320 |
| K051 | API separator sludge | 8,198 | 0.32-155 | 0.8-1760 |
| K170 | Clarified slurry oil sediment | 4,238 | 13-25 | 23-28 |
| K050 | Heat exchange bundle cleaning sludge | 2,375 | 78 | 251 |
| K052 | Tank bottoms(leaded) | 1,334 | 78 | 251 |
| F038 | Secondary oil/water/solids separator sludge | 903 | <1-75.3 | 0.8-444 |
| K049 | Slop oil emulsion solids | 645 | 28.9-1400 (LDR data) | 21.95-3900(LDR data) |

K171 – Spent hydrotreating catalyst (30,209  tons) and K172 – Spent hydrorefining catalyst (7,206 tons) are not included in this ranking.

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 2000 MTD Gasifier Feeding 90% Petroleum Coke/10% Petroleum Waste Composite

LOWER BOUND

|  | Chromium | Lead |
| --- | --- | --- |
| Characteristic Level (mg/L TCLP) | 5.0 | 5.0 |
| UTS (mg/L TCLP) | 0.60 | 0.75 |
| Lower Bound Petroleum Waste Composite (mg/kg) | 0.04 | 0.05 |
| Concentration in Petroleum Coke (mg/kg) | 1.3 | 1.5 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 11.54 | 13.55 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 0.577 | 0.6775 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | 0.01154 | 0.01355 |

UPPER BOUND

|  | Chromium | Lead |
| --- | --- | --- |
|  | LDR Data | Post 1996 Data | LDR Data | Post 1996 Data |
| Upper Bound Petroleum Waste Composite(mg/kg) | 6790 | 155 | 5800 | 1760 |
| Concentration in Petroleum Coke (mg/kg) | 1.3 | 1.3 | 1.5 | 1.5 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 6801.7 | 166.7 | 5813.5 | 1773.5 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 340.1 | 8.33 | 290.7 | 88.7 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | 6.8 | 0.167 (0.067)* | 5.81 | 1.77 (0.7)* |

## *The value in parenthesis illustrates a mean leachate value representative of actual testing data of untreated waste (0.0004).

BP Whiting Refinery, Whiting , Indiana

Mean of K048, F037, F038, and K051 Waste Composite– DAF Float + Biosolids + API Separator Sludge)

|  | Chromium | Lead |
| --- | --- | --- |
| Mean Petroleum Waste Composite (mg/kg) | 18.3 (158 data points) | 185.3 (158 data points) |
| Concentration in Petroleum Coke (mg/kg) | 1.3 | 1.5 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 30.2 | 198.5 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 1.5 | 9.92 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | 0.03 (0.012)* | 0.04 (0.07)* |

## *The value in parenthesis illustrates a mean leachate value representative of actual testing data of untreated waste (0.0004).

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 20 MTD Gasifier Feeding 100% Petroleum Waste With 10% of Mass to Gasifier Bottoms

LOWER BOUND

|  | Chromium | Lead |
| --- | --- | --- |
| Characteristic Level (mg/L TCLP) | 5.0 | 5.0 |
| UTS (mg/L TCLP) | 0.6 | 0.75 |
| Lower Bound Waste Composite (mg/kg) | 0.04 | 0.05 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 0.4 | 0.5 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 0.02 | 0.025 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 0.0004 | 0.0005 |

UPPER BOUND

|  | Chromium | Lead |
| --- | --- | --- |
|  | LDR Data | Post 1996 Data | LDR Data | Post 1996 Data |
| Upper Bound Waste Composite (mg/kg) | 6790 | 155 | 5800 | 1760 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 67900 | 1550 | 58000 | 17600 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 3395 | 77.5 | 2900 | 880 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 67.9 | 1.55 (0.62)* | 58 | 17.6 (7.04)* |

## *  The value in parenthesis illustrates a  mean leachate value representative of actual testing data of untreated wastes.

BP Whiting Refinery, Whiting , Indiana

Mean of K048, F037, F038, and K051 Waste Composite– DAF Float + Biosolids + API Separator Sludge

|  | Chromium | Lead |
| --- | --- | --- |
| Mean Petroleum Waste Composite (mg/kg) | 18.3 (158 data points) | 185.3 (158 data points) |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 183 | 1853 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 9.15 | 92.65 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | 0.183 (0.073)* | 1.85 (0.74)* |

## *  The value in parenthesis illustrates a mean leachate value representative of actual testing data of untreated wastes.

Sample Calculations

Sample Calculation (Lead):

(20 MT)(1000kg/MT) = 20,000 kg waste

(20,000 kg waste)(1760 mg/kg) =35,200,000 mg Leady

In 20 MTD gasifiers 20% mass goes to syngas; 80% to bottoms with 100% of metals

Therefore; 16 MTD of bottoms generated.

18,800,000 mg Lead/(16 MT)(1000kg/MT) = 2200 mg/kg of Lead

Apply 20:1 TCLP ratio (multiply by 0.05) = 110 mg/L TCLP;   Apply 1000:1 (multiply by 0.001) =  2.2 mg/L TCLP

Sample Calculation – Method 1:

(1800 MT of petcoke)(3.53/10E6) + (200 MT of secondary material) (0.05/10E6) = 0.006354 + .00000005 = .00635405/200tons x 10E6 = 31.77 = 31.8 mg/kg Arsenic in bottoms

Application of 20:1 ratio from TCLP (multiply by 0.05):  31.77 x .05 = 31.8 x 0.05 = 1.59 mg/L TCLP

Application of 1000:1 ratio from TCLP (multiply by 0.001):  31.77 x .001 = 31.8 x 0.001 = 0.0318 mg/L TCLP

Sample Calculation – Method 2

(1800 MT of petroleum coke)(1000kg/MT) = 1.8 x 10E6 kg petroleum coke     (200 MT of secondary material)(1000kg/MT) = 2.0 x 10E5 kg secondary material.

(1.8 x 10E6 kg petroleum coke)(3.53 mg Arsenic in petroleum coke/kg) = 6.3 54x 10E6 mg Arsenic

(2.0 x 10E5 kg secondary material)(0.05 mg Arsenic/kg secondary material) = 1 x 10E4 mg Arsenic

6.354 x 10E6 mg Arsenic +.01 x 10 E6 mg Arsenic = 6.364 x 10E6 mg Arsenic

200 MT of gasifier bottoms

6.364 x 10E6/(200MT)(1000 kg/MT) = 31.8 mg/kg Arsenic in bottoms.

Application of 20:1 ratio from TCLP (multiply by 0.05):  31.8 x .05 = 1.59 mg/L TCLP

Application of 1000:1 ratio from TCLP (multiply by 0.001):  31.8 x 0.001 = 0.0318 mg/L TCLP

## Sample Calculation – Method 1 (Arsenic):

2000 MT (3.53/10E6) = 0.00706 MT of Arsenic

0.00706 MT of Arsenic/200 MT of bottoms = 0.0000353 x 10E6 = 35.3 mg/kg Arsenic in bottoms

(35.3)(.05) = 1.76 mg/L TCLP

(35.3)(.001) = 0.0353 mg/L TCLP

Sample Calculation – Method 2 (Arsenic):

(2000 MT)(1000 kg/MT) = 2,000,000 kg of petroleum coke

(2,000,000 kg)(3.53mg Arsenic/kg) = 7,060,000 mg Arsenic

7,060,000 mg Arsenic/(200 MT)(1000kg/MT) = 35.3 mg/kg Arsenic in gasifier bottoms

(35.3)(.05) = 1.76 mg/L TCLP

(35.3)(.001) = 0.0353 mg/L TCLP