POLAR Spacecraft Status As of: Tues, 25 Nov 03  12:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-11H Standby PM STIP data only | NOAA-12D Standby AM STIP data only | NOAA-14J Standby AM STIP data only | NOAA-15K BACKUP AM GAC data only | NOAA-16L PRIMARY PM GAC&LAC data | NOAA-17M PRIMARY AM GAC&LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 09/23/88 | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 |
| CNTL OBP | OBP2 | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 |
| BUS | A-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS | RGYRO Mode (Y, Z-Gyros Failed) Reduced Gyro S/W. X &S gyros only | YGC Mode Gyro chans=XYZ Yaw updates disabled 10/1 RGmode=Monitor | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off/Anom Gyro chans=AAB | Nominal Mode Rgmode=Disabled Gyro chans=AAA Gyro3 deselected Gyro3 TOAR 427 | Nominal Mode Rgmode=Disabled Gyro chans=BBB |
| RXO | PRI BU random enables daily bias +70mSec (control side only) | PRI BU random enables +1000mS on 10/17 Plan daily ETCUP bias of –6.5 mS | PRI BU random enables daily bias–7.3 mSec | PRI daily bias -8 mSec | PRI Daily Bias –5.1 mSec | PRI Daily Bias –1.7 mSec |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | ON | External Synch Rephase Enabled | External Synch Rephase Daily | External Synch Rephase Daily. | External Sync Rephase Daily | Internal Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 1 | 2 Since 4/24/03 | 1 Analog telem drifting | 1 |
| DTRs | 1A, 2B, 3, 4A Safestate - 2B, | 1, 3, 4, 5B Safestate- 1B | 1, 2B, 3A, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B TOAR 418 (STIP only) | 1,2,3,4 Safestate=1B DTR2-SSR DTR5 TOAR 420 |
| VTX (APT data) | OFF | OFF 3 Nov until 7 Dec Conflict with N15 | OFF Since 8/14/02 | #1 137.50 MHZ | INOP OFF since 11/15/00 | #2 137.62 MHZ |
| BTX | #2 137.77 MHZ | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 3 – TIP 1,2 - Playback | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 1, 2, 3 - degraded; 2 Omni–HRPT; 4- Playback | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 1&2 Playback 4 – TIP STX4 tests at Sval |
| POWER (Array offset, charge and eclipse states, sun angle) SOLAR ECLIPSE 23&24 Nov 03 No adverse effects on any spacecraft | Array Off -30 Since 6/19/02 Eclipse all year Sun angle 77 Start Downtrend to 71 degs on 1 Feb 04 Batts1,2,3=LRC VT1,2=6/8 VT3 = 8/11 Charge state safe trip disabled | ArrayOff -60 since 7/30/03 FULL SUN Sun Angle at 20 Uptrend started to 25 degs mid-Jan 04. Sun sensor shading Until 12/5/03 Batts 1&2=LRC V/T=4 | Array Off -55 Since 8/21/03 FULL SUN Sun Angle at 26 Uptrend to 26 in End Uptrend Steady Trend Batts 1-3= LRC Batts 1&3V/T=8/11 Batt2 VT=9/11 ) Shunt Degraded | Array Off -45 Since 1/25/01 FULL SUN Sun Angle at 17 Uptrend to 18 in mid-Dec Batts 1-3= LRC V/T=7/9 | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 55 UpTrend to 59 in mid Feb 04 Batts 1-3= LRC V/T=4/8 | Array Off. –35 Since 7/1/02 Eclipse all year Sun Angle at 67 Start down trend to 60 early Feb 04 Batts 1-3= LRC V/T= 4/8 |
| AVHRR | INOP Failed Power Supply. Powered Off since 1994 | Nominal | DEGRADED Scan motor erratic performance STATUS=RED | Nominal Rare Scan motor surges. Last Incident 8/9/03 | Recovering occasional scan motor current surges. Last surge 11/11/03 Chan 3B only. | Nominal 3A-B switch enabled |
| AMSU-A1 |  |  |  | ON Ch14 inoperative Ch11 inoperative | ON TOAR 415 on primary PLLO chans 9-14 bias shift. TOAR 417 on Backup PLLO inop | OFF/INOP Since 10/30/03 Inoperable Red in status. Survival heat on. TOAR 431 |
| AMSU-A2 |  |  |  | ON | ON Space Position-2 | ON |
| AMSU-B |  |  |  | ON Bias in All Chans. Motor current surges, most recent 11/20/03 | ON Space Position-3 | ON |
| HIRS | OFF Filter Wheel Anomaly | INOP Filter Wheel turned OFF 10/17/02. Electronics On | ON Operational | Recovering From 12 Nov Major FW anomaly .Imagery improved FW Heaters OFF 18 Nov FW in Hi power, | ON Nominal | ON 1 Pixel cross track misalignment . |
| MSU | INOP OFF, Antenna Failed | INOP Scan Motor OFF since 3/12/03 Electronics ON. | ON Scan motor and antenna problems |  |  |  |
| SSU | ON |  | ON |  |  |  |
| DCS | ON | ON | ON | ON | ON Nominal | ON Nominal |
| SARR | ON Low signal |  | ON | ON-A All AGC Mode Intermittent failures for 243MHz A&B | ON-A All AGC Mode (B-side in FG mode) 243 MhZ INOPERATIVE. | ON-A Nominal All AGC Mode |
| SARP | ON Nominal |  | OFF Failed Power Supply | ON Nominal RCVR B/W = 2 | ON Nominal RCVR B/W = 2 | ON Nominal |
| SEM |  | ON Elec-CH-HVPS=4 Prot-CH-HVPS=0 | ON Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | ON Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | ON Nominal E-CDEM-HVPS=4 Plans to change e-cdem to level 5 P-CDEM-HVPS=4 | ON Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 |
| SBUV | INOP Grating motor OFF since 5/29/03 Electronics and Heater remain ON |  | Recovering Major grating drive anomaly started on 11/20 at 01:50. Recovery ops successful on 11/20 at 19:30. Plan Flex Memory reconfig on 11/25 in response to anomaly. Reducing Grating drive “low end” range to –730 (from –750). Reduced operations started 6/5/03 |  | ON Backup Diffuser in use since 6/16/03.) Primary =TOAR 426 antenna deploy anomaly, AMSU EMI causing erratic Behavior in PMT cathod, range 3 | ON Nominal Anode Mode |
| SADPOS |  |  |  | N/A | ON ENABLED Disabled 23 Nov RE-Enabled 24 Nov MFactor =50% | ON ENABLED |
| THERMAL Heaters, louvers TCE’s | Nominal | Nominal | Nominal | HIRS FW Heater OFF 18 Nov 03 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Cold season ended, trend reversed | Nominal TCE24 turned off (AVHRR H&L) 9/23/03 AVHRR in warming trend | TCE3H Batt 2A heater turned off 8/26/03 TOAR 428 AMSU-A1 survival heaters on 10/29/03 |
|  | N11 | N12 | N14 | N15 | N16 | N17 |

COMMENTS/CHANGES:

NOAA-11	N11 went through the solar eclipse on 23 Nov (at 22:51Z) with no mission impacting effects.  In preparation for this

eclipse, EMOSS engineers commanded batteries 1 & 2 to Medium Rate Charge (battery 3 remained at Low Rate because it is degraded) approximately 1 hour before the eclipse event began.  There were some concerns about the potential for N11 attitude control mode to autonomously switch into gyroless control but, using the EMOSS solar eclipse model as a guide, engineers determined that this eventuality should not occur and recommended plans to NOAA accordingly.  Ultimately, the autonomous swap did not occur.  Once the eclipse event was completed, batteries 1 & 2 were commanded back to Low Rate Charge.  Subsequent analysis of stored telemetry revealed that the eclipse did draw battery-1 charge state down to 20.25 amp hours, a level that is very close to power safe state trigger point of 19.6.  Therefore it is possible that the switch to Medium Rate charge prior to the eclipse might have made the difference between going into safe state and remaining out of it.  EMOSS engineers Jim Sheperd and Jeff Devine remained at the SOCC for the duration of preparation and completion reconfigurations for this solar eclipse event.

NOAA-12.  	N12  (a full sun spacecraft) also experienced the solar eclipse event on two successive revs on 23 Nov starting at

21:47Z.  Using the EMOSS solar eclipse model, engineers recommended to NOAA that no reconfigurations would be necessary for N12 during this eclipse.  Subsequent analysis of stored telemetry on N12 since this event has shown that there were no mission impacting effects on this spacecraft during the eclipse.

Using the EMOSS developed Time Stamp File process, for the first time, engineers have been able to determine the actual clock drift rate for N12 (approximately -6.5 msecs daily) after analyzing several weeks of N12 TSF data.  (N12 was incorporated into the POES TSF process approximately 7 weeks ago.)  With this knowledge, EMOSS engineers can now stop the clock drift on N12 as it has done with all the other POES spacecraft with operational AVHRR’s.  Therefore, engineers will be implementing a new, first time daily ETCUP value of +6.5 mSecs sometime within the next three weeks.  Jim Sheperd is POC.

NOAA-14:	The N14 AVHRR scan motor remained anomalous throughout the past reporting period.  PIDES remains inoperable

for the second week in a row so no imagery analysis could be conducted by EMOSS engineers.

N14 (a full sun spacecraft) experienced 2 minor and 1 major solar eclipses on successive orbits starting at 20:55Z on 23

Nov.  Like N12, analysis by EMOSS engineers determined that no reconfigurations would be necessary prior to this eclipse event to protect the N14 spacecraft and recommended to NOAA that no changes be made.  Subsequent analysis of stored telemetry on N14 since this event has shown that there were no mission impacting effects on this spacecraft from this eclipse including on the power subsystem where bus voltage remains steady and shunt voltage less than maximized (illustration 1).

On 20 Nov at 01:50, a major anomaly occurred on the N14 SBUV.  At that time the N-14 SBUV was commanded by the stored command table to go from Flex Memory 0 to Flex Memory 3; the giant step memory segment (grating positions 600, -750). After going to a grating position of 600, the grating drive then moved on to –900 where it apparently ceased.  At that point, the drive (and other SBUV component) temperatures began to rise.  At 03:45Z, the grating drive temperature reached 25.9 degree, the threshold which triggers an automatic on board safety macro that powered off the grating drive.  Just before commanding itself off, the grating position shifted further to -936.  Recovery operations began at 16:00Z where the grating motor power was toggled on and off several times in the hope of “breaking though” whatever might be obstructing the drive.  This toggling operation was repeated on the next support at 17:40Z.  In neither support was anything other than rudimentary movement on the grating drive observed.  However, on a support at 19:30Z, prior to toggling the grating motor power on, the SBUV grating drive was switched to Flex memory 3 and the giant step memory segment.  Thereupon, the grating motor power was again toggled on and off several times.  On the 4th toggle on, the drive broke through and began to show the full range of Flex 3, (600 to –750) movement.  Several minutes later, the SBUV was commanded back to Flex 0, after which it read all twelve correct values for that memory segment, ranging from 526 to –673.  It has continued to operate nominally since that time (illustration 2a & b).

On 24 Nov an N14 SBUV anomaly resolution meeting was convened and supported by EMOSS POC Will Kent.  At

this meeting, a consensus was reached to change half of the mini giant step memory segment (Flex 3) words from position -750 to -730.  Over the past half year we have been going to Flex 3 for about 10 minutes a week (Thursday blind orbits).  This is a maintenance procedure that is supposed to "push obstructions clear” from the current full operating range of the grating drive. The full operating range of this instrument is now less than it was originally (primarily because of its 9+ years of operation).  Currently Flex Memory 0’s operates between positions 526 and –673 while Flex 3 is between +600 to –750.  (Although the recent anomaly demonstrated that FM3 range actually goes beyond those ranges by ~75 positions on either side.)  The anomaly resolution team proposed that because the +600 side has not shown errors and the -750 side has shown an increasing number of errors over the last 6 months (and is also the area where the anomaly occurred) that the new “low end” area of the operating range should be “brought in” slightly to –730.  On 25 Nov at 20:00Z, EMOSS POC Will Kent will direct an upload to the N14 SBUV of a CP he created that will make this change to -730.  With this new operating range in place (hopefully clear of any obstructions) it is possible that the operational life of this SBUV may be prolonged well beyond that which might have been expected just a week earlier.

NOAA-15:	The N15 HIRS recovered nicely during the past reporting period (after the filter wheel heater was turned off on 18

Nov), with the filter motor current retreating back to nominal (illustration 3), synch status steady, period monitor values nominal and imagery improving throughout the week. (NOTE: EMOSS could not perform HIRS imagery analysis because the PIDES system has been inoperable for the past 2 weeks.  Various product users provided the imagery quality information to EMOSS.)  No additional operations or reconfiguration are planned at this time for this instrument.

At almost the exact time that the N14 SBUV was returning to nominal operation, on 20 Nov the N15 AMSU-B scan motor current surged to the second highest level seen in the past 3 years, accompanied by a surge in scan motor temp.  No reports of imagery degradation were received by EMOSS in regard to this surge (and, as stated, PIDES has not been available to EMOSS engineers for 2 weeks).  However, by 01:00 on 21 Nov, the scan motor had returned to nominal values where it has remained since (illustration 4).  In addition, the N15 AVHRR was nominal throughout the week.

N15 (a full sun spacecraft) also experienced the solar eclipse event on two successive revs on 23 Nov starting at

21:21Z.  Using the EMOSS solar eclipse model, engineers recommended to NOAA that no reconfigurations should be necessary for N15 during this eclipse.  Subsequent analysis of stored telemetry on N15 since this event has shown that there were no mission impacting effects on this spacecraft from the eclipse (illustration 5).

Coordination on N15 Rgyro testing continues although no date has yet been determined for this test.  EMOSS engineers are awaiting the result of node tests to be performed at the factory in order to advance the pre-test analysis for what can be expected during an actual N15 Rgyro operation.  EMOSS engineer Carl Gliniak drafted a letter requesting this nodal testing and submitted to NOAA management for their review and approval.

While investigating the requirements and implications of increasing the command watchdog timer on N15 to 10.5 hours (from its current 9 hours) EMOSS engineer Jon Woodward determined that a flight software patch would need to be generated and uploaded to the spacecraft before this change can be implemented.  Rather than spend the time/money on such a project, EMOSS engineers have determined several “lower tech” methods by which the objective of preventing an autonomous swap to clear mode can be avoided.  These methods involve the use of Greta, STK, MS Excel and SITARS to flag schedule gaps where the risk of such a swap could occur thus allowing the controllers more opportunity to call up a pass to send N15 a command before a swap occurs.  Jon Woodward, Kim Kolb and Jeff Devine are EMOSS POC for meeting this objective.

NOAA-16: 	The N16 AVHRR scan motor current was generally nominal although less stable than desired during the past week

The scan motor current continues to show a tendency to trend higher although it remains within what could be considered nominal values, most of the time (illustration 6).  However, EMOSS has heard no reports of AVHRR imagery degradation, synch delta values are very stable (illustration 7), and the AVHRR thermal trend has “topped out” and appears to be reversing itself thus negating the concern about overheating the payload (illustration 8).  Unfortunately, this thermal reversal may also prove problematic since keeping the AVHRR warmer has been the objective for keeping the scan motor lubricant less viscous.  Monitoring continues.

There were no out-of-spec yaw updates experienced by N16 during the past week (illustration 9) which was especially auspicious since one of the yaw updates occurred right in the middle of the solar eclipse with the solar array occluded by more than 50%.  In the weeks preceding this eclipse the EMOSS model predicted that a yaw update would occur right in the middle of this rather significant event for N16 (90% array occlusion).  With that possibility in mind, there was some consideration given to commanding the spacecraft to “Unforced” YGC mode in order to prevent an autonomous switch to YGC mode when the yaw update occurred in the middle of the eclipse.  Ultimately NOAA decided not to command to YGC mode and instead had EMOSS engineers standing by in the SOCC following the eclipse to command the spacecraft back to nominal if it indeed had swapped itself to YGC.  As predicted (illustration 10) the update did occur during the eclipse but the update was nominal anyway and no switch to YGC occurred.

A second area of concern during the eclipse was the N16 SADPOS software module.  The EMOSS model predicted that the triggering conditions of this module taking control of the solar array would come very close to being met during the eclipse (9 minutes at 80% occlusion).  Rather than risk this eventuality which could be disruptive to operations, NOAA directed EMOSS engineers to disabled the SADPOS for the duration of the eclipse event.  Therefore, EMOSS POC Jeff Devine directed SADPOS disable at 22:30Z on 23 Nov and re-enable at 02:00Z on 24 Nov.

The final area of concern for N16 during the eclipse event was power generation.  Even though the spacecraft was to experience a very deep solar eclipse, when that event was completed, the spacecraft would re-emerge into sunlight for at least 45 minutes before going back into its normal eclipse.  Although NOAA and EMOSS engineers believed that would be more than enough time to regenerate the batteries to full capacity, as an added measure of precaution the battery charge rates were increased to Medium Rate at 22:30Z. Once the eclipse was over, at 02:00 on 24 Nov, they were commanded back to their original configuration of Low Rate Charge.  Originally, the batteries were to be

N16 (cont):	commanded to Medium Rate Charge on Friday and remain that way throughout the weekend.  However, concerns

about battery heating (especially 2A) convinced engineers that it might be more prudent to leave medium rate charge for the minimum time necessary to fullfill safety objectives.  As illustrations 11a & b show, N16 weathered this eclipse event with no problems occurring in the power subsystem.

SEM reconfiguration planned.  Per request of Bob Muckle (SEM user) , EMOSS engineer Will Kent will be reconfiguring the N16 SEM electron channeltron from its current level 4 to level5.  This operation will be planned for mid week, next week.

NOAA-17:	No new information on AMSU-A1 the past week.  The instrument remains powered off and inoperable.  No new testing is currently planned.

N17 also experienced the solar eclipse on 23 Nov although to a less significant degree than N16.  As with N16, EMOSS recommended and NOAA directed that the batteries be commanded to Medium Rate charge for the duration of the event as a safety precaution.  This commanding was performed on 23 Nov at 21:10Z.  Once the eclipse was over, the batteries were returned to Low rate Charge at 01:55Z.  Originally, the batteries were to be commanded to Medium Rate Charge on Friday and remain that way throughout the weekend.  However, like N16, concerns about battery heating (especially 2A) convinced engineers that it might be more prudent to leave medium rate charge for the minimum time necessary to fulfill safety objectives.  As illustrations show 12a & b, N17 barely even registered the effects of this eclipse since it occurred very close to the time that N17 was entering its normal eclipse.

Regarding power, EMOSS engineers are starting to notice that the N17 shunt is running hotter than it ever has before (illustration 13a) and that the bus voltage is starting to “spike upwards” occasionally (illustration 13b).  This may be indicative of an over stressed shunt.  With the AMSU-A1 recently powered off, it is probable that N17 is now having to shunt all the power that was previously going into that instrument.  On the positive side of this issue, the solar angle on the spacecraft is in a slow downtrend which will not bottom out until mid Feb 04 and may reduce power generation somewhat.  However, close vigilance of the shunts and bus voltage will be maintained by EMOSS engineers and the possibility of a solar array offset move to alleviate some of the effects of this excess power generation may be necessary in the future (although is not currently planned).

NOAA-N	Discussions are being conducted between NOAA and other agencies as to the best time to conduct the NOAA-N end to

end test.  Current indications are that it will not occur until Feb 04.  The PACS software being developed to support NOAA-N is scheduled for completion in time for an early December test.  Other dates mentioned include early and mid-January of 2004.  EMOSS engineers are awaiting a final disposition.

MISC:

CWS was installed in the EMOSS analysis area and comparison testing by all EMOSS engineers was supposed to commence on 19 Nov.  However, technical difficulties with the software have delayed testing somewhat.  Comparison testing will entail EMOSS engineers performing all their routine tasks on both a 3100 and CWS simultaneously and determining the ability of CWS to enter parallel ops in the SOCC in early December.  Kim Kolb and Jon Woodward are leading this effort.

EMOSS engineer Andy Miller generated a new pseudo mnemonic for each POES spacecraft that will be included in a new lim proc that will be employed to prevent a lim proc for one spacecraft to be run on a pass for a different spacecraft.

Kim Kolb in addition to his standard engineering duties performed the network engineering function (currently vacant) in helped plan and operate a data flow end to end test with Goldstone on 20 Nov and an MHS/MIU test on 21 Nov.

EMOSS engineer Jon Woodward supported flight code management testing on 19 and 20 Nov.

The EMOSS solar eclipse model once again provided highly accurate predictions of the time, duration and extent of the recent solar eclipse upon the POES constellation.  Developed primarily by Kim Kolb, this tool enabled EMOSS engineers to recommend reconfigurations (or not) to help increase the safety of the various spacecraft during the eclipse event.  For confirmation of these results refer to the predicted vs actual graphs at the end of this report.

Carl Gliniak and Angelique Riley continue with their investigation of the data quality at low elevation Barrow supports.

Illustration 1: N14 Power Analysis.  Note Eclipse effects at the end of day 327

Illustration 2a:  N14 SBUV Anomaly and recovery

Illustration 2b:  N14 SBUV thermal profiles during anomaly and recovery.

Illustration 3:  N15 HIRS Filter Wheel Recovery Continues

Illustration 4:  N15 AMSU-B surge analysis (near term and long term)

NOTE:  No imagery available for inclusion in this report because of SOCC PIDES outage at the time of publication.

Illustration 5:  N15 Power Analysis leading up to and including solar eclipse on 23 Nov

Illustration 6:  N16 AVHRR Scan Motor Health

(has been more stable in the past)

(No imagery available because of SOCC PIDES outage)

RECENT CLOSE VIEW				LONG VIEW

Illustration 7:  N16 AVHRR Synch Delta Values (Mean) and Stability (Standard Deviation) Analysis

Recent values are very encouraging

Illustration 8:  N16 AVHRR Thermal Profile.

Looks like the warming trend is over.  Hopefully the coming cooling trend will not increase the viscosity of the scan motor lubricant.

Illustration 9:  N16 Gyro performance relative to Yaw Update.

(note solar eclipse at end of the week)

Illustration 10:  N16 Yaw Update relative to solar eclipse

(update occurred right in the middle of the eclipse and it was still a good update.)

Illustration 11a:  N16 Power Analysis leading up to and including the solar eclipse.

Illustration 11b:  N16 Power Analysis leading up to and including the solar eclipse.

Illustration 12a:  N17 Power Analysis  leading up to and including the solar eclipse.

Illustration 12b:  N17 Power Analysis #2 leading up to and including the solar eclipse.

# Illustration 13a:  N17 Shunt temp trends

# Illustration 14:  N17 Shunt temp vs bus voltage history

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING November 21, 2003

| DAY/DATE | NOAA-11 | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 11/14 | -1511 msec | +129 msec | +025 msec | +036 msec | +037 msec | +027 msec |
| SAT. 11/15 | -1740 msec | +119 msec | +025 msec | +037 msec | +036 msec | +028 msec |
| SUN. 11/16 | -1870 msec | +111 msec | +023 msec | +037 msec | +037 msec | +029 msec |
| MON. 11/17 | -1600 msec | +103 msec | +025 msec | +036 msec | +040 msec | +028 msec |
| TUE. 11/18 | -1630 msec | +103 msec | +025 msec | +036 msec | +041 msec | +030 msec |
| WED. 11/19 | -1760 msec | +095 msec | +026 msec | +036 msec | +041 msec | +032 msec |
| THU. 11/20 | -1290 msec | +088 msec | +027 msec | +035 msec | +041 msec | +034 msec |

NOAA-11  	As of 09/03/02 the Control Side TIP clock is corrected daily by +70 msec to compensate for drift.

As of 11/03/03 Non control side clock is no longer supported

NOAA-12  	ADDED 1000 mSecs to spacecraft command clock on 10/17/03.

N12		Plan daily ETCUP bias of +6.5 mSec on Date TBD

NOAA-14:  	As of 04/23/03 the TIP clock is corrected daily by –-7.3 msec to compensate for drift.

SUBTRACTED 150 msec from spacecraft command on 10 June.

NOAA-15:  	As of 04/23/03 the TIP clock is corrected daily by –-8 msec to compensate for drift.

ADDED 100 msec to spacecraft command clock on 10 June.

NOAA-16:  	As of 04/23/03 the TIP clock is corrected daily by –5.1 msec to compensate for drift.

SUBTRACTED 100 msec from spacecraft command clock on 10 June.

NOAA-17:  	As of 10/21/03 the TIP clock is corrected daily by –1.7 msec to compensate for drift.

SUBTRACTED 50 MS on 10/21

Weekly N17 CPU Error Scrubs

NOAA-17 Scrubber Hits from 17 Nov 2003 through 24 Nov 2003:

Red/Circle = CPU#1

Black/X = CPU#2

PACS DATA AVAILABILITY (%)

November 14, 2003 through November 20, 2003

JDAY 318-324

|  |  |  | NOAA15 | NOAA14 | NOAA11 | NOAA16 | NOAA17 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Friday | 11/14 | 318 | 100.0 | 100.0 | 92.1(a) | 100.0 | 94.2(b) |
| Saturday | 11/15 | 319 | 100.0 | 100.0 | 100.0 | 100.0 | 100.0 |
| Sunday | 11/16 | 320 | 93.5(c) | 100.0 | 85.6(d) | 100.0 | 100.0 |
| Monday | 11/17 | 321 | 100.0 | 100.0 | 70.1(e) | 100.0 | 100.0 |
| Tuesday | 11/18 | 322 | 87.1(f) | 100.0 | 84.7(g) | 100.0 | 100.0 |
| Wednesday | 11/19 | 323 | 100.0 | 100.0 | 100.0 | 100.0 | 100.0 |
| Thursday | 11/20 | 324 | 100.0 | 100.0 | 100.0 | 100.0 | 94.7(h) |

EMOSS POC for this chart: Angelique Riley

Comments:

- Rev 78077/W: S2B noisy; 98.0% recovered 2DL 1PE.

- Rev 07216/F: G3B noisy; 97.9% recovered.

- Rev 28643/W: G3B noisy; 97.8% recovered.

- Rev 78110/F: S3B noisy; 98.4% recovered 7DL 27PE.

- Rev 78121/W: S3B noisy; 99.4% recovered 3DL 10 PE.

- Rev 28661/F: G2B noisy 96.6% recovered 2DL.

- Rev 78139/F: S4A noisy 96.2% recovered 10DL.

- Rev 07309/F: G2B noisy 98.0% recovered.

DTR Inf. (*):

NOAA-11        	DTR 1B -Inoperative.

DTR 2A/B -Frequently noisy

DTR 4B -Frequently noisy

DTR 5A/B -Inoperative

NOAA-12	DTR 5A -Inoperative.

DTR 2B -Occasionally noisy and short

NOAA-14	DTR 4A/B -Inoperative.

DTR 3B -Unreliable playbacks, Removed from operations.

DTR 2A -Inoperative, DOY/200

NOAA-15	DTR 5A/B - Inoperative

NOAA-16            DTR 5A/B -Inoperative

DTR 3A -safe state change 1B

DTR 4B –Inoperative 1/12/03

NOAA-17	DTR 5A/B-Inoperative 2/16/03 Anomaly

Acronyms:

DL – Drop lock(s)	PE - Parity Error(s)			DQR - Data Quality Report

BE - Bit Error(s)	DAR - Data Accountability Report	MFR - Multi-Function Receiver

NOAA12:

No spacecraft data available for NOAA-12.