Introduction

The data provided is from a high fidelity system level engine simulation designed to simulate nominal and fault engine degradation over a series of flights. The flights are full flight recording sampled at 1 Hz and consists of 30 engine and flight condition parameters. Each flight contains 7 unique flight conditions for an approximately 90 min flight including ascent to cruise at 35K ft and descent back to sea level. The simulated data was created with a Matlab Simulink tool called C-MAPSS.

Background

C-MAPSS stands for ‘Commercial Modular Aero-Propulsion System Simulation’ and it is a tool for the simulation of a realistic large commercial turbofan engine. The code is a combination of Matlab (The MathWorks, Inc.) and Simulink (The MathWorks, Inc.) with a number of graphical user interface (GUI) screens that allow point-and-click operation and with editable fields that allow the user to enter specific values of his/her own choice. In addition to the engine model (called the 90K because it is produces about 90,000 lb of thrust), the package includes an atmospheric model capable of operation at (i) altitudes from sea level to 40,000 ft, (ii) Mach numbers from 0 to 0.90, and (iii) sea-level temperatures from -60 to 103 °F. The package also includes a power-management system that allows the engine to be operated over a wide range of thrust levels throughout the full range of flight conditions.

A comprehensive control system is included that consists of (i) a fan-speed controller for which the user specifies the throttle-resolver angle (TRA), (ii) three high-limit regulators that prevent the engine from exceeding its design limits for core speed, engine-pressure ratio, and HPT exit temperature, (iii) a fourth limit regulator that prevents the static pressure at the HPC exit from going too low, (iv) acceleration and deceleration limiters for the core speed, and (v) a comprehensive logic structure that integrates these control-system components in a manner similar to that used in real engine controllers such that integrator-windup problems are avoided. Furthermore, all of the gains for the fan-speed controller and the four limit regulators are scheduled such that the controller and regulators perform as intended over the full range of flight conditions and power levels.

The inputs are fuel flow and a set of 13 health-parameter inputs that allow the user to simulate the effects of faults and deterioration in any of the engine’s five rotating components (fan, LPC, HPC, HPT, and LPT).

Fault types

- Fan:  inlet engine fan

- LPC:  Low pressure compressor

- HPC:  High pressure compressor

- HPT:  High pressure turbine

- LPT:  Low pressure turbine

Simulation Setup

The simulation was designed as follows:  Each flight is a combination of a series of flight conditions with a reasonable linear transition period to allow the engine to change from one flight condition to the next. The flight conditions are arranged to cover a typical ascent from sea level to 35K ft and descent back down to sea level.  7 unique flight conditions are used with a total of 14 total states for a 90 minute flight sampled at 1 Hz. Each engine is given an exponentially degrading fuel flow and efficiency profile that describes 300 flights. The engine is then assigned 1 of the 5 possible faults (fan, LPC, HPC, HPT, and LPT).  For nominal runs the standard fuel flow and efficiency degradation profiles are used.  During fault runs the fault is set to randomly occur during the first 60 flights.  During that flight the fault is introduced at a random time sample.  The fault is manifested by increasing the fuel flow and efficiency parameters degradation by 25% or 50% for the 2 fault engines runs from the fault time point on till the end of the simulation for the remaining flights.  After a flight is simulated a snapshot of all engine parameters are taken in the middle of cruise and used to calculate the health parameter for the engine. If the health parameter drops below 0 no further flights are simulated for that engine.

Data

There are 5 types of faults simulated. Each fault has 5 examples of nominal engines and 2 examples of faulty engines, one at 25% increased degradation and the other at 50%. Each engine directory will have a series of flights FlightXXX.csv in csv format. The first row of each flight will contain the engine flight condition parameters and the rows represent time samples. Each engine directory will also contain Engine_Fuel_Effic.csv, which is the engine fuel and efficiency profile used as input for the simulator for all flights. EngineHealth.csv contains the calculated engine health for each flight based on the snapshot of the engine parameters at cruise.  Finally the Simulation_Info.txt contains a summary of the number of flights, the fault type that was simulated, if it is nominal or not, and if not what flight and time sample the fault was introduced.

Parameter descriptions

| Parameter Name | Description | Units |
| --- | --- | --- |
|  | Flight Conditions |  |
| time | Flight time | sec |
| alt | Altitude | ft |
| MN | Mach number | pct |
| TRA | Throttle resolver angle | deg |
| Wf | Fuel flow | pps |
| Fn | Net thrust | lbf |
|  | Health Indicators |  |
| SmHPC | HPC stall margin | -- |
| SmLPC | LPC stall margin | -- |
| SmFan | Fan stall margin | -- |
|  | Measurement Temperatures |  |
| T48 | Total temperature at HPT outlet | R |
| T2 | Total temperature at fan inlet | R |
| T24 | Total temperature at LPC outlet | R |
| T30 | Total temperature at HPC outlet | R |
| T50 | Total temperature at LPT outlet | R |
|  | Pressure Measurements |  |
| P2 | Pressure at fan inlet | psia |
| P15 | Total pressure in bypass-duct | psia |
| P30 | Total pressure at HPC outlet | psia |
|  | Other Measurements |  |
| Nf | Physical fan speed | rpm |
| Nc | Physical core speed | rpm |
| epr | Engine pressure ratio (P50/P2) | -- |
| phi | Ratio of fuel flow to Ps30 | pps/psiu |
| Ps30 | Static pressure at HPC outlet | psia |
| NfR | Corrected fan speed | rpm |
| NcR | Corrected core speed | rpm |
| BPR | Bypass ratio | -- |
| farB | Burner fuel-air ratio | -- |
| htBleed | Bleed enthalpy | -- |
| PCNfRdmd | Percent corrected fan speed | pct |
| W31 | HPT cooland bleed | lbm/s |
| W32 | HPT cooland bleed | lbm/s |