Pacific Northwest Hydrography

Framework Clearinghouse

Hydrography Data Dictionary

Physical Data Model

Version 1.1

Prepared by the

Washington and Oregon

Hydrography Framework

Technical Work Groups

September 28, 2004

Table of Contents

Section 1 Database Overview	1

Data Layer Descriptions	1

Database Listing and Naming Conventions	4

Database File Relationships	6

Database File Diagram – Water Bodies	8

Database File Diagram - Water Shoreline	9

Database File Diagram – Water Points	10

Section 2 Washington Hydrography Framework Data Descriptions	11

Watercourse Data Layer Description	11

Arc Attribute Table	11

Section Table	12

Route Attribute Table	13

Line Type Event Table	14

Name Event Table	15

Feature Type Event Table	16

River Reach File Event Table	17

Stream Flow Event Table	18

Feature History Event Table	20

Water Body Data Layer Description	23

Polygon Attribute Table	23

Shoreline Data Layer Description	25

Arc Attribute Table	25

Section Table	26

Route Table	27

Shoreline Type Event Table	28

Feature History Event Table	29

Water Point Layer Data Description	32

Point Attribute Table	32

Feature History Relate Table	34

Section 3 Appendix	36

Acknowledgements	36

Data Dictionary Code Tables	37

Data Dictionary Format Sheet Explanations	58

Format Sheet Explanation - Section Table	60

Format Sheet Explanation - Route Table	61

Format Sheet Explanation - Linear Event Table	62

Format Sheet Explanation - Point Relate Table	63

Section 1	Database Overview

Background and Document Contents

This data dictionary describes data for the Washington and Oregon Framework Hydrography data and the standard system used to identify the states surface water.

The Framework goal was to utilize an existing data model that would enable various participants to locate and identify the state's marine and fresh surface water.  The system was developed to provide a standard for referencing surface water bodies and watercourses, and to provide a vehicle for cross-referencing existing surface water data between agencies and groups in both GIS and tabular formats.

It is intended that this physical data model provide the backbone whereby users may each attach and retain their own particular surface water data.  The standard identifiers provided by this system will ideally facilitate data exchange on a wide scale amongst water management entities and reduce redundancy in data collection.

For additional information about Dynamic Segmentation and/or the rules and procedures for applying this model, please refer to the companion document titled “Oregon and Washington State Framework Hydrography Concepts, Rules & Procedures.”

Document Contents

Section 1 is comprised of a description of the data layers, database listings and naming conventions.

Section 2 describes the working physical data model, how system identifiers and indexing are carried, the database contents, the imbedded metadata, and an explanation of naming standards and coding structure.

Section 3 contains an explanation of the format of the data dictionary sheets and the larger detailed code tables.

Data Layer Descriptions

The Framework model allows for the storage of all hydrographic features.   Successful implementation of the Framework Hydrography data model requires that participants understand the way in which the different features are modeled and that they have a common understanding of the terms and definitions contained in the document.  This section addresses the way in which these features are modeled.

Hydrographic features are modeled in four layers:

Water Points (WP)

Watercourses (WC)

Water Bodies (WB)

Water Body Shorelines (WS)

The desired source scale for all layer acquisition is 1:24,000 or better.  1:100,000 data may be substituted where layers at the desired source scale have not been developed.  All data is stored in NAD83 geographic coordinates, double precision.

A longitude/latitude identifier (LLID) uniquely identifies each hydrographic feature in the model.   This 13-character identifier is composed of the concatenated decimal degree longitude and latitude of the feature.  The identifier is unique within each layer but there is no requirement that it be unique between the layers. The geographic location used to generate the LLID varies depending on the data layer.  Consult the detailed layer attribute table definitions (Section 2) to determine the location used to generate the LLID for that layer.

Each feature in the Water Point (WP), Watercourse (WC) and Water Body (WB) layers share the following attributes:

- a unique LLID identifier.

- a generalized classification of the hydrographic feature type (e.g. spring, stream, lake etc.)

- a classification of the type of cartographic element.  This is a more detailed classification of the feature useful for mapping or more detailed database queries.

- a classification of seasonal, or periodic behavior of the water feature (e.g. perennial, intermittent or ephemeral)

- a robust set of attributes that describe the history of spatial edits to each feature.  See detailed layer attribute table definitions (Section 2) for a complete description of these feature history attributes.

What follows is a short description of each of the four layers present in the model, the type(s) of features included in each layer and the relationships between the related information.

The Water Point (WP) layer is the repository for springs, seeps and other hydrographic features with limited spatial extent (i.e. most easily represented by a point).  This layer consists of a point coverage and a single related table.  The related table describes the history of spatial edits to the feature.

The Watercourse (WC) layer consists of stream, canal, flume, pipeline and other linear hydrographic feature centerlines.  Where these features (especially streams) are represented as double lined features at the source scale they will be represented in this layer by their centerline.  Streams that flow through water bodies such as lakes and reservoirs will also be represented by a centerline.  This feature has been modeled to allow for flow modeling.  All arcs must point downstream.  This layer will be routed using the LLID identifier for the stream. All associated attributes are stored as event tables on the LLID routes.  The stream routes are indexed starting from 0 at the mouth of the stream to some maximum value at the headwaters.  All route measures will be initially calibrated in kilometers to three decimal places.  As these routes are edited, every effort will be made to keep the measure value at a given map location from shifting.  This will be accomplished by stretching or shrinking the measure values to accommodate lengthening or shrinking along the route as its X,Y coordinates are edited.  Thus, over time, the measures will only approximate kilometers along a watercourse or shoreline.  These measures are simply an indexing scheme for linear referencing, not a stored attribute of shoreline or watercourse length.

The Water Body (WB) layer consists of sounds, bays, lakes, ponds, wetlands, reservoirs, inundation areas, the double lined portions of streams and other hydrographic features best represented as areas.   For ease of managing these features they have been modeled as regions rather than simple polygons in the Framework model.  However, by agreement, each water body will be stored as a non-overlapping, non-multi-part region (i.e. there will be one polygon per region).  The advantages of this approach will be described in detail in document titled “Oregon and Washington State Framework Hydrography Concepts, Rules & Procedures.”  Water body attributes will be stored in the WB region attribute table (PATWB.)  Changes to the water body shape will be made and tracked in the water body shoreline coverage.

The Water Body Shoreline (WS) layer consists of one or more representations of the shoreline of each water body.  One representation of the shoreline for each water body will be flagged in the Framework database as the “default” shoreline.  This default shoreline will be coincident with the water body perimeter in the water body (WB) layer.  This layer is modeled in the Framework to accommodate those instances where multiple shorelines based on different datum (e.g. mean high water, mean low water etc.) are useful, especially marine shorelines.  This layer is modeled as a routed linear feature.  Water will be on the right side of each route and each shoreline will be represented by one or more non-overlapping routes.  However, most simple water bodies (e.g. small lakes and ponds) will likely be represented by a single route.  The history of spatial edits to each water body will be stored as an event on the route(s) on the default shoreline.  Our agreement is that unless there is good justification to do so, all other shoreline attributes will be stored as events on the default shoreline.  Non-default shorelines are intended to accommodate specialized requirements.

Database Listing and Naming Conventions

This section contains a list of the data files and diagrams depicting the relationships that exist between the files.

Database Layers and Coverages

| Layer Description | Feature Class | Attribute Table Name |
| --- | --- | --- |
| Water bodies areas | Region | WB.PATWB |
| Water body shorelines | Route | WS.RATWS |
| Watercourses | Route | WC.RATWC |
| Water points | Point | WP.PAT |

Naming Conventions

Table Names:

COVERAGE NAME  . TOPOLOGY TYPE  _   DESCRIPTION

Examples:	WC.EVT_NAME

WS.EVT_SL_TYPE

WP.REL_FTR_HST

Lookup Table Names:

COVERAGE NAME  . TOPOLOGY TYPE  _   ITEM DESCRIPTION

Examples:  	WC.LUT_FTR_ORG_CD

Column Names or Items in Lookup Table

ITEM NAME			FTR_ORG_CD

ITEM NAME_LU		FTR_ORG_LU

(replace_CD with _LU for short description)

ITEM NAME_DS		FTR_ORG_DS

(replace _CD with _DS for long description)

Item or Field Names:

COVERAGE NAME  .  DESCRIPTION  _  CLASS/KEY

Example: 	WC.LN_TYP_CD

Table and Attribute Requirements

All tables are mandatory and must be present in order to be placed in the Clearinghouse.  In Section 2, you will find a description of each table and whether the attributes or fields contained within those tables should be applied to all the features on stream network or just on a portion of the features.  We refer to this as the “Attributes Extent” and it’s intended to help users identify the extent of coverage.  In some cases attributes are available for only some stream/water body features, in those cases you are not required to populate the database if information is not available.

The data described below is provided in ARC/INFO format.  All data is stored in NAD83 geographic coordinates, double precision.

#### Watercourses

###### Coverage/Table		File Name

Coverage		WC

Line attribute table		WC.AAT

Section table		WC.SECWC

Route attribute table		WC.RATWC

Event table		WC.EVT_NAME

Event table		WC.EVT_LN_TYPE

Event table		WC.EVT_FTR_TYPE

Event table		WC.EVT_RRF

Event table		WC.EVT_STRM_FLOW

Event table		WC.EVT_FTR_HST

#### Water Bodies

###### Coverage/Table		File Name

Coverage		WB

Region attribute table		WB.PATWB

#### Water Shorelines

###### Coverage/Table		File Name

Coverage		WS

Line attribute table		WS.AAT

Section table		WS.SECWS

Route attribute table		WS.RATHYD

Event table		WS.EVT_SL_TYPE

Event table		WS.EVT_FTR_HST

### Water Points

## Coverage/Table		File Name

Coverage		WP

Point attribute table		WP.PAT

Point relate table		WP.REL_FTR_HST

Please refer to Section 3 - Appendix for a full listing of associated code tables. There you will find the actual code tables as they're reflected in the four data coverage’s (watercourses, water shorelines, water bodies and water points) with the similarities and differences between them noted.

Database File Relationships

The following diagrams depict the relationships between the data files comprising the three layers:

Figure 1-1  Watercourse

Figure 1-2  Water Body

Figure 1-3  Water Shoreline

Figure 1-4  Water Point

Figure 1-1

Database File Diagram - Watercourses

Figure 1-2

Database File Diagram – Water Bodies

Figure 1-3

Database File Diagram - Water Shoreline

Figure 1-4

Database File Diagram – Water Points

Section 2	Washington Hydrography Framework Data Descriptions

Watercourse Data Layer Description

This layer consists of stream, canal, flume, pipeline and other linear hydrographic feature centerlines.  Where these features (especially streams) are represented as double lined features at the source scale they will be represented in this layer by their centerline.  Streams that flow through water bodies such as lakes and reservoirs will also be represented by a centerline.

Line Layer:  Watercourses		Layer Name:  WC

Table Name: WC.AAT

Arc Attribute Table

Defined		Item

Item Name		Definition

FNODE#		4,5,B

TNODE#		4,5,B

LPOLY#		4,5,B

RPOLY#			4,5,B

LENGTH		8,18,F,5

WC#			4,5,B

WC-ID		4,5,B

Data Classification - AAT

FNODE#

Arc from node internal number

TNODE#

Arc to node internal number

LPOLY#

Internal identifier of polygon to left of arc.

RPOLY#

Internal identifier of polygon to right of arc.

LENGTH

Arc length, units in decimal degrees.

WC#

Arc internal number, software assigned.

WC-ID

Arc identifier assigned by user.  This item is not used nor is it changed.  Presence required by the software.

Section Table:  Watercourses			Table Name:  WC.SECWC

Section Table

Defined		Item

Item Name		Definition

ROUTELINK#		4,5,B

ARCLINK#		4,5,B

F-MEAS		4,12,F,3

T-MEAS		4,12,F,3

F-POS		4,12,F,3

T-POS		4,12,F,3

WC#		4,5,B

WC-ID		4,5,B

Data Classification - SEC

ROUTELINK#

Route link number. Route internal number from RAT; identifies the route to which the section belongs.

ARCLINK#

Arc link number.  Arc internal number from the AAT; identifies the arc to which the section belongs.  It’s provided to enable keyfile selections within ARCPLOT.  Links with the item WC#.

F-MEAS

From measure. Measure of start position of section.

T-MEAS

To measure. Measure of end position of section.

F-POS

From position. Start position in terms of percentage of existing arc.

T-POS

To position. End position in terms of percentage of existing arc.

WC#

Internal sequence number of the sections.

WC-ID

User assigned section identifier set to equal the interval section identifier.  This item is not used nor is it changed.  Presence required by the software.

Route Table:  Watercourses			Route Table Name: WC.RATWC

Route Attribute Table

Defined		Item

Item Name		Definition

WC#		4,5,B

WC-ID		4,5,B

WC_LLID_NR		13,13,C

Data Classification - RAT

WC#

Route system internal sequence number

WC-ID

Route-system ID, user defined.  This item is not used nor is it changed.  Presence required by the software.

WC_LLID_NR

Watercourse longitude/latitude identifier number.  The 13 character longitude/latitude derived unique watercourse route identifier (this is also known as LLID in the federal arena.)  All watercourse segments are grouped into watercourse routes. The identifier is based on position of the downstream point (mouth) of the watercourse. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points).  LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

Linear Event Table: Watercourses	Table Name:  WC.EVT_LN_TYPE

Line Type Event Table

Event Table Outline

Defined		Item

Item Name		Definition		Attribute Extent

WC_LLID_NR		13,13,C

WC_BEGIN_AD		4,12,F,3

WC_END_AD		4,12,F,3

WC_LN_TYPE_CD		2,2,I	Fully populated

WC_FLOW_PATH_CD	2,2,I	Fully populated

Data Classification - EVT

WC_LLID_NR

Watercourse longitude/latitude identifier number.  The 13 character longitude/latitude derived unique watercourse route identifier (this is also known as LLID in the federal arena.)  All watercourse segments are grouped into watercourse routes. The identifier is based on position of the downstream point (mouth) of the watercourse. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points).  LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

WC_BEGIN_AD

Watercourse begin address.  The beginning, or downstream, index of the watercourse segment. The address or index at which an event or attribute can be associated to a route.

Example: 000.000

WC_END_AD

Watercourse end address.  The ending, or upstream, index of the watercourse segment. The address or index at which an event or attribute can be associated to a route.

Example: 036.025

WC_LN_TYPE_CD

Watercourse line type code.  The type of watercourse feature that is represented in the database.  Code used to differentiate the primary cartographic function of the lines regardless of the hydrographic feature or hydrologic function they represent

Example: 20

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

WC_FLOW_PATH_CD

Watercourse flow path code.  Defines the flow hierarchy of stream centerline that are within water body features.  This code is used to define and segregate out the various flow pathways though water bodies.  These centerlines usually have a WC_LN_TYPE_CD of 20 or 21. For single line watercourses code the event as “not applicable.”

Example: Primary

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

Linear Event Table: Watercourses	Table Name:  WC.EVT_NAME

Name Event Table

Event Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WC_LLID_NR		13,13,C

WC_BEGIN_AD		4,12,F,3

WC_END_AD		4,12,F,3

WC_GNIS_NM		50,50,C	Partially populated

WC_GNIS_NR		8,8,I	Partially populated

Data Classification - EVT

WC_LLID_NR

Watercourse longitude/latitude identifier number.  The 13 character longitude/latitude derived unique watercourse route identifier (this is also known as LLID in the federal arena.)  All watercourse segments are grouped into watercourse routes. The identifier is based on position of the downstream point (mouth) of the watercourse. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points). LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

WC_BEGIN_AD

Watercourse begin address. The index measure of the beginning, or downstream, extent of the event.  The address or index at which an event or attribute can be associated to a route.

Example: 000.000

WC_END_AD

Watercourse end address. The index measure of the ending, or upstream, extent of the event. The address or index at which an event or attribute can be associated to a route.

Example: 036.025

WC_GNIS_NM

Watercourse GNIS name.  The name of the feature as represented within the Geographic Names Information System (GNIS).  The USGS is the mandated source of this information.  Not all features contained within the coverage will have GNIS names.

Example:  Deschutes River

WC_GNIS_NR

Watercourse GNIS (Geographic Names Information System) number.  The unique identifier number assigned to each feature name represented within the GNIS database.  This number is used to insert and/or update watercourse names stored in the framework hydrography database. Not all features contained within the coverage will have GNIS number.

Linear Event Table: Watercourses	Table Name: WC.EVT_FTR_TYPE

Feature Type Event Table

Event Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WC_LLID_NR		13,13,C

WC_BEGIN_AD		4,12,F,3

WC_END_AD		4,12,F,3

WC_HYDR_FTR_CD		2,2,C	Fully populated

WC_CART_FTR_CD		4,4,I	Fully populated

Data Classification - EVT

WC_LLID_NR

Watercourse longitude/latitude identifier number.  The 13 character longitude/latitude derived unique watercourse route identifier (this is also known as LLID in the federal arena.) The identifier is based on position of the downstream point (mouth) of the watercourse. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points).  LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

WC_BEGIN_AD

Watercourse begin address. The index measure of the beginning, or downstream, extent of the event. The address or index at which an event or attribute can be associated to a route.

Example:  000.000

WC_END_AD

Watercourse end address. The index measure of the ending, or upstream, extent of the event. The address or index at which an event or attribute can be associated to a route.

Example: 036.025

WC_HYDR_FTR_CD

Watercourse hydrographic feature code.  The code used to describe the hydrographic feature type that the watercourse represents.

Example:  ST

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

WC_CART_FTR_CD

Watercourse cartographic feature code.  The code used to describe the cartographic feature type that the watercourse represents.  This represents feature codes developed initially by the USGS and used on the DLG’s.

Example:  412

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

Linear Event Table: Watercourses	Table Name:  WC.EVT_RRF

River Reach File Event Table

Event Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WC_LLID_NR		13,13,C

WC_BEGIN_AD		4,12,F,3

WC_END_AD		4,12,F,3

WC_RRF_NR		17,17,C	Partially populated

Data Classification - EVT

WC_LLID_NR

Watercourse longitude/latitude identifier number.  The 13 character longitude/latitude derived unique watercourse route identifier (this is also known as LLID in the federal arena.)  All watercourse segments are grouped into watercourse routes. The identifier is based on position of the downstream point (mouth) of the watercourse. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points).  LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

WC_BEGIN_AD

Watercourse begin address. The index measure of the beginning, or downstream, extent of the event. The address or index at which an event or attribute can be associated to a route.

Example:  000.000

WC_END_AD

Watercourse end address. The index measure of the ending, or upstream, extent of the event. The address or index at which an event or attribute can be associated to a route.

Example:  036.025

WC_RRF_NR

Watercourse River Reach File number. This represents the unique identifier used by the USEPA.  A unique identifiers is carried on individual stream segments, running confluence to confluence. The identifier is comprised of 3 components – the watercourse hydrographic unit code number, the watercourse river reach file segment number, and the watercourse river reach file mile number.   The source of this data will be USGS National Hydrography Database (NHD) once Washington State 100K hydrography is incorporated into that database. Not all stream segments have been assigned a RRF number by the USGS.  In some cases this information in not necessarly available.

Linear Event Table: Watercourses	Table Name: WC.EVT_STRM_FLOW

Stream Flow Event Table

Event Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WC_LLID_NR		13,13,C

WC_BEGIN_AD		4,12,F,3

WC_END_AD		4,12,F,3

WC_CONTU_CD		3,3,C	Fully populated

WC_PERIOD_CD		3,3,C	Fully populated

Data Classification - EVT

WC_LLID_NR

Watercourse longitude/latitude identifier number.  The 13 character longitude/latitude derived unique watercourse route identifier (this is also known as LLID in the federal arena.)  All watercourse segments are grouped into watercourse routes. The identifier is based on position of the downstream point (mouth) of the watercourse. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points).  LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

WC_BEGIN_AD

Watercourse begin address. The index measure of the beginning, or downstream, extent of the event. The address or index at which an event or attribute can be associated to a route.

Example:  000.000

WC_END_AD

Watercourse end address. The index measure of the ending, or upstream, extent of the event. The address or index at which an event or attribute can be associated to a route.

Example:  036.025

WC_CONTU_CD

Watercourse continuity code.  This is the classification of stream flow primarily in relation to its expression at the earth’s surface. The most common condition is that a stream is continuous in space.

With respect to continuity, streams may be divided into continuous streams and interrupted steams. An interrupted stream is one that contains (a) perennial stretches with intervening intermittent or ephemeral stretches or (b) intermittent stretches with intervening ephemeral stretches. These two classes of interrupted streams are designated respectively, perennial interrupted streams and intermittent interrupted streams.   A continuous stream is one that does not have interruptions in space.

Example of use with Periodicity Code:

You do not need to separate out each small segment of perennial, intermittent or ephemeral stream.   If they sporadically exist along a "reach" the hydrologist chooses the dominant periodicity and calls the continuity interrupted.     If the reach is not continuously perennial or intermittent we are noting it through the use of the interrupted attribute.   It may be a scale issue but it also says a lot about the channel itself.

These codes can be found in the associated lookup table in Section 3 - Appendix.

WC_PERIOD_CD

Watercourse periodicity code. This is a classification for watercourses in terms of the seasonal behavior of the feature over time or in terms of its surface flow.

Example: int

These codes can be found in the associated lookup table in Section 3 – Appendix.

Linear Event Table: Watercourses 		Table Name: WC.EVT_FTR_HST

Feature History Event Table

Event Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WC_LLID_NR		13,13,C

WC_BEGIN_AD		4,12,F,3

WC_END_AD		4,12,F,3

FTR_MOD_CD		3,3,C	Fully populated

FTR_INPUT_CD		2,2,I	Fully populated

FTR_INTRP_CD 		2,2,I	Fully populated

FTR_SRC_CD		3,3,I	Fully populated

FTR_SRC_DT		8,8,D	Fully populated

FTR_SRCSCALE_NR		7,7,I	Fully populated

FTR_ACCUR_NR		4,12,F,3	Fully populated

FTR_ORG_CD		12,12,C	Fully populated

FTR_EDIT_DT		8,8,D	Fully populated

Data Classification - EVT

WC_LLID_NR

Watercourse longitude/latitude identifier number.  The 13-character longitude/latitude derived unique watercourse route identifier (this is also known as LLID in the federal arena.)  All watercourse segments are grouped into watercourse routes. The identifier is based on position of the downstream point (mouth) of the watercourse. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points).  LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

WC_BEGIN_AD

Watercourse begin address. The index measure of the beginning, or downstream, extent of the event.

Example:  000.000

WC_END_AD

Watercourse end address.  The index measure of the ending, or upstream, extent of the event.

Example:  036.025

FTR_MOD_CD

Feature modify code.  Identifies the type of change that occurred to hydrography watercourse feature. Tracks the type of modification performed on the database. These codes can be found in the associated lookup table.

Example:  add

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_INPUT_CD

Feature input code.  The manner in which the hydrography watercourse data is entered or updated in the spatial database. These codes can be found in the associated lookup table.

Example:  Scan

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_INTRP_CD

Feature interpretation code.  The methodology used to compose the hydrography watercourse information and how it was derived prior to data entry into the spatial coverage.

Example:  1

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_SRC_CD

Feature source code.  The compilation map or image source used when adding or updating hydrography watercourse data.

Example:  12

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_SRC_DT

Feature source date.  The compilation map or image source date used for the addition or update of hydrography watercourse data. A default date code should be used when no source date is available for historical information.

Example:  19990515 (CCYYMMDD = May 15, 1999)

Default:  14520101 (CCYYMMDD = January 1, 1452

FTR_SRCSCALE_NR

Feature source scale number.  Describes the scale denominator of the map or image source for the hydrography watercourse data additions or updates in the database.  Exact scale can be input.  The density of hydrography features displayed will vary by the base map scale.  A default scale of “0” should be used when the source scale is unknown.

Example:  2400

Default:  0

FTR_ACCUR_NR

Feature accuracy number.  Describes the positional accuracy of the hydrography watercourse data being added or updated in the database.   Describes the correctness of the measurement.   Use actual value e.g. .001; 3; 100.   All units are entered in meters.  A default code of “0.000” should be used when the accuracy is unknown.

Example:  24000

Default:  0.000

FTR_ORG_CD

Feature organization code.  The organization that compiled, entered, updated or deleted the hydrography watercourse data.  This list will grow as new organizations begin to add or update information and are certified by the clearinghouse.  The Clearinghouse Manager will maintain the list of organizations authorized to participate in the editing of Hydrography Framework data.

Example:  cothurwa

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_EDIT_DT

Feature edit date.  The date the feature was either entered, updated or deleted in the hydrography coverage.  Represents the date when the data was incorporated into the database.  This item is utilized to track changes in the database.

Example: 19980515 (CCYYMMDD = May 15, 1998)

Water Body Data Layer Description

This layer consists of sounds, bays, lakes, ponds, reservoirs, inundation areas, the double lined portions of streams and other hydrographic features best represented as areas.

Polygon Attribute Table

Polygon Layer:  Water Bodies	Layer Name: WB

Table Name: WB.PATWB

Region Attribute Table Outline

Defined		Item

Item Name		Definition		Attribute Extent

AREA		8,18,F,5

PERIMTER		8,18,F,5

WB#		4,5,B

WB-ID		4,5,B

WB_LLID_NR		13,13,C

WB_HYDR_FTR_CD		2,2,C	Fully populated

WB_CART_FTR_CD		4,4,I	Fully populated

WB_GNIS_NM		50,50,C	Partially populated

WB_GNIS_NR		8,8,I	Partially populated

WB_PERIOD_CD		3,3,C	Fully populated

Data Classification - REGION

AREA

Water body area in decimal degrees.

PERIMETER

Water body perimeter length in decimal degrees.

WB#

Water body region internal number; software assigned.

WB-ID

Water body region user-defined ID. This item is not used nor is it changed.  Presence required by the software.

WB_LLID_NR

Water body longitude/latitude identifier number.  The 13-character longitude/latitude derived unique identifier of the water body.  All water bodies and islands represented as polygonal features are assigned an identifier. The identifier is based on position of the polygon label point. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points). LLID numbers are not unique across the four coverages.  There is no valid default value for this field and it must be populated.

Example:  1234567890987

WB_HYDR_FTR_CD

Water body hydrographic feature code.  The code used to describe the hydrographic feature type that the water body polygon represents.

Example:  LA

These codes can be found in the associated lookup table listed in Section, pg. 51.

WB_CART_FTR_CD

Water body cartographic feature code.  The code used to describe the cartographic feature type that the water body polygon represents.  This represents feature codes developed initially by the USGS and used on the DLG’s.

Example:  101

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

WB_GNIS_NM

Water body GNIS name.  The name of the water body as contained within the Geographic Names Information System (GNIS) which is maintained by the USGS. Not all features contained within the coverage will have GNIS names.

Example:  Ross Lake

Default: blank or null

WB_GNIS_NR

Water body GNIS (Geographic Names Information System) number.  The unique identifier number assigned to each feature name represented within the GNIS database.  This number is used to insert and/or update water body names stored in the framework hydrography database. Not all features contained within the coverage will have GNIS number

Example:  12345678

Default: 0

WB_PERIOD_CD

Water body periodicity code.  This is a classification of a water bodies in terms of the seasonal behavior of the feature over time or in terms of its surface flow.

Example:  per

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

Shoreline Data Layer Description

This layer consists of one or more representations of the shoreline of each water body.

Arc Attribute Table

Line Layer:  Water Shoreline	Layer Name: WS

Table Name: WS.AAT

Arc Attribute Table Outline

Defined		Item

Item Name		Definition

FNODE#		4,5,B

TNODE#		4,5,B

LPOLY#		4,5,B

RPOLY#		4,5,B

LENGTH		8,18,F,5

WS#			4,5,B

WS-ID			4,5,B

Data Classification - AAT

FNODE#

Arc from node internal number

TNODE#

Arc to node internal number

LPOLY#

Internal identifier of polygon to left of arc.

RPOLY#

Internal identifier of polygon to right of arc.

LENGTH

Arc length, units in decimal degrees.

WS#

Arc internal number, software assigned.

WS-ID

Arc identifier assigned by user.  This item is not used nor is it changed.  Presence required by the software.

Section Table:  Water Shoreline			Table Name:  WS.SECWS

Section Table

Section Table Outline

Defined		Item

Item Name		Definition

ROUTELINK#		4,5,B

ARCLINK#		4,5,B

F-MEAS		4,12,F,3

T-MEAS		4,12,F,3

F-POS		4,12,F,3

T-POS		4,12,F,3

WS#		4,5,B

WS-ID		4,5,B

Data Classification - SEC

ROUTELINK#

Route link number. Route internal number from RAT; identifies the route to which the section belongs.

ARCLINK#

Arc link number.  Arc internal number from the AAT; identifies the arc to which the section belongs.  It’s provided to enable keyfile selections within ARCPLOT.  Links with the item WS#.

F-MEAS

From measure. Measure of start position of section.

T-MEAS

To measure. Measure of end position of section.

F-POS

From position. Start position in terms of percentage of existing arc.

T-POS

To position. End position in terms of percentage of existing arc.

WS#

Internal sequence number of the sections.

WS-ID

User assigned identifier set equal to the interval section identifier. This item is not used nor is it changed.  Presence required by the software.

Route Table:  Water Shoreline			Table Name: WS.RATWS

Route Table

Route Attribute Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WS#		4,5,B

WS-ID		4,5,B

WS_LLID_NR		13,13,C

WS_DATUM_CD	4,4,C	Fully populated

WS_DFLT_SHORE_CD	1,1,C	Fully populated

Data Classification - RAT

WS#

Route system internal sequence number

WS-ID

Route-system ID, user defined.  This item is not used nor is it changed.  Presence required by the software.

WS_LLID_NR

Water shoreline longitude/latitude identifier number.  The 13-character longitude/latitude derived unique identifier of the shoreline.  All water body shorelines and island shorelines are assigned an identifier. All shoreline segments are grouped into shoreline routes. The identifier is based on beginning of the route and is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points). LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1234567890987

WS_DATUM_CD

Water shoreline datum code.  The character code that describes the type and level that the water body shoreline was mapped at.   The framework model is designed to store multiple shorelines; some of them are complete for a state’s coastline while others are short segments.  Shorelines consist of water body perimeters (lakes, ponds, and reservoirs) as well as linear segments like marine shorelines.

Example:  mhw

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

WS_DFLT_SHORE_CD

Water shoreline default shoreline code.  The character code that designates the shoreline that’s used to build water body area features.  The default shoreline is comprised of the mean-high water line (mh) and the fresh water (fw) shoreline.  This field is included to unambiguously designate the default shoreline regardless of the future changes or exceptions to the business rules.

Example:  y

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

Linear Event Table: Water Shoreline		Table Name: WS.EVT_SL_TYPE

Shoreline Type Event Table

Event Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WS_LLID_NR		13,13,C

WS_BEGIN_AD		4,12,F,3

WS_END_AD		4,12,F,3

WS_TYPE_CD		2,2,I	Fully populated

Data Classification - EVT

WS_LLID_NR

Water shoreline longitude/latitude identifier number.  The 13-character longitude/latitude derived unique identifier of the shoreline.  All water body shorelines and island shorelines are assigned an identifier. All shoreline segments are grouped into shoreline routes. The identifier is based on beginning of the route and is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points). LLID numbers are not unique across the four coverages.

There is no valid default value for this field and it must be populated.

Example:  1215613480987

WS_BEGIN_AD

Water shoreline begin address.  The beginning, or downstream, index of the segment.  The address or index at which an event can be associated to a route

Example: 020.035

WS_END_AD

Water shoreline end address.  The ending, or upstream, index of the segment.  The address or index at which an event can be associated to a route.

Example: 002.326

WS_TYPE_CD

Water shoreline type code.  The type of water body shoreline feature that is represented.

Example:  1

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

Linear Event Table: Water Shoreline		Table Name: WS.EVT_FTR_HST

Feature History Event Table

Event Table Outline

Defined		Item

Item Name		Definition	Attribute Extent

WS_LLID_NR		13,13,C

WS_BEGIN_AD		4,12,F,3

WS_END_AD		4,12,F,3

FTR_MOD_CD		3,3,C	Fully populated

FTR_INPUT_CD		2,2,I	Fully populated

FTR_INTRP_CD 		2,2,I	Fully populated

FTR_SRC_CD		3,3,I	Fully populated

FTR_SRC_DT		8,8,D	Fully populated

FTR_SRCSCALE_NR		7,7,I	Fully populated

FTR_ACCUR_NR		4,12,F,3	Fully populated

FTR_ORG_CD		12,12,C	Fully populated

FTR_EDIT_DT		8,8,D	Fully populated

Data Classification - EVT

WS_LLID_NR

Water shoreline longitude/latitude identifier number.  The 13-character longitude/latitude derived unique identifier of the shoreline.  All water body shorelines and island shorelines are assigned an identifier. All shoreline segments are grouped into shoreline routes. The identifier is based on beginning of the route and is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points). LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1234567890987

WS_BEGIN_AD

Water shoreline begin address.  The index measure of the beginning, or lowest address, of the event. The address or index at which an event or attribute can be associated to a route.

Example:  034.066

WS_END_AD

Water shoreline end address.  The index measure of the ending, or highest address, of the event. The address or index at which an event or attribute can be associated to a route.

Example:  123.099

FTR_MOD_CD

Feature modify code.  Identifies the type of change that occurred to hydrography water shoreline feature.  Tracks the type of modification performed on the database.

Example:  del

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_INPUT_CD

Feature input code.  The manner in which the hydrography shoreline data is added or updated in the spatial database.

Example:  1

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_INTRP_CD

Feature interpretation code.  The methodology used to compose the hydrography shoreline information and how it was derived prior to data entry into the spatial coverage.

Example:  6

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_SRC_CD

Feature source code.  The compilation map or image source used when adding or updating hydrography shoreline data.

Example:  8

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_SRC_DT

Feature source date.  The compilation map or image source date used for the addition or update of hydrography shoreline data.  A default date code should be used when no source date is available for historical information.

Example: 19990515(CCYYMMDD = May 15,1999)

Default: 14520101 (CCYYMMDD = January 1, 1452)

FTR_SRCSCALE_NR

Feature source scale number.  Describes the scale denominator of the map or image source for the hydrography shoreline data additions or updates in the database.  Exact scale can be input.  The density of hydrography features displayed will vary by the base map scale.  A default scale of “0” should be used when the source scale is unknown.

Example:  24000

Default:  0

FTR_ACCUR_NR

Feature accuracy number.  Describes the positional accuracy of the hydrography shoreline data being added or updated in the database.   Describes the correctness of the measurement.  Refer to USGS map accuracy standards for more information.  Use actual value e.g. .001; 3; 100.   All units are entered in meters.  A default code of “0.000” should be used when the accuracy is unknown.

Example:  24000

Default:  0.000

FTR_ORG_CD

Feature organization code.  The organization that compiled, entered, updated or deleted the hydrography shoreline data.  This list will grow as new organizations begin to add or update information and are certified by the clearinghouse. The Clearinghouse Manager will maintain the list of organizations authorized  to participate in the editing of Hydrography Framework data.

Example:  ctyolywa

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_EDIT_DT

Feature edit date.  The date the feature was either entered, updated or deleted in the hydrography coverage.  Represents the date when the data was incorporated into the database.  This item is utilized to track changes in the database.

Example:  19980515 (CCYYMMDD = May 15, 1998)

Water Point Layer Data Description

This layer is the repository for springs, seeps and other hydrographic features with limited spatial extent (i.e. most easily represented by a point.)

Point Attribute Table

Point Layer:  Water Points	Layer Name:  WP

Table Name:  WP.PAT

Point Attribute Table

Defined  		Item

Item Name  		Definition	Attribute Extent

AREA			8,18,F,5

PERIMETER		8,18,F,5

WP#			4,5,B

WP-ID		4,5,B

WP_LLID_NR		13,13,C

WP_HYDR_FTR_CD		2,2,C	Fully populated

WP_CART_FTR_CD		4,4,I	Fully populated

WP_PERIOD_CD		3,3,C	Fully populated

Data Classification - PAT

AREA

Water point area in decimal degrees.

PERIMETER

Water point perimeter length in decimal degrees.

WP#

Arc internal number, software assigned.

WP-ID

Water point identifier assigned by user. This item is not used nor is it changed.  Presence required by the software.

WP_LLID_NR

Water point longitude/latitude identifier number.  The 13-character longitude/latitude derived unique identifier of the water point.  All water point features are assigned an identifier. The identifier is based on position of the point feature on the source material. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points). LLID numbers are not unique across the four coverages.

There is no valid default value for this field and it must be populated.

Example:  1215613480987

WP_HYDR_FTR_CD

Water point hydrographic feature code.  The code used to describe the hydrographic feature type that the water point represents.

Example:  SP

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

WP_CART_FTR_CD

Water point cartographic feature code.  The code used to describe the cartographic feature type that the water point represents.  This represents feature codes developed initially by the USGS and used on the DLG’s.

Example:  300

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

WP_PERIOD_CD

Water point periodicity code.  This is a classification of a water point in terms of the seasonal behavior of the feature over time or in terms of its surface expression.

Example:  int

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

Point Relate Table:  Water Points	Table Name: WP.REL_FTR_HST

Feature History Relate Table

Point Relate Table

Defined  		Item

Item Name  		Definition	Attribute Extent

WP_LLID_NR		13,13,C

FTR_MOD_CD		3,3,C	Fully populated

FTR_INPUT_CD		2,2,I	Fully populated

FTR_INTRP_CD 		2,2,I	Fully populated

FTR_SRC_CD		3,3,I	Fully populated

FTR_SRC_DT		8,8,D	Fully populated

FTR_SRCSCALE_NR		7,7,I	Fully populated

FTR_ACCUR_NR		4,12,F,3	Fully populated

FTR_ORG_CD		12,12,C	Fully populated

FTR_EDIT_DT		8,8,D	Fully populated

Data Classification - REL

WP_LLID_NR

Water point longitude/latitude identifier number.  The 13-character longitude/latitude derived unique identifier of the water point.  All water point features are assigned an identifier. The identifier is based on position of the point feature on the source material. The identifier code is composed by concatenating the decimal degree values (to four places of precision) of the coordinates (minus the decimal points).  LLID numbers are not unique across the four coverages. There is no valid default value for this field and it must be populated.

Example:  1215613480987

FTR_MOD_CD

Feature modify code.  Identifies the type of changes that occurred to hydrography water point feature. Tracks the type of modification performed on the database.

Example:  add

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_INPUT_CD

Feature input code.  The manner in which the hydrography water point data is entered or updated in the spatial database.

Example:  3

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_INTRP_CD

Feature interpretation code.  The methodology used to compose the hydrography water point information and how it was derived prior to data entry into the spatial coverage.

Example:  2

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_SRC_CD

Feature source code.  The compilation map or image source used when adding or updating hydrography water point data.

Example:  5

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_SRC_DT

Feature source date.  The compilation map or image source date used for the addition or update of hydrography water point data.  A default date code should be used when no source date is available for historical information.

Example:  19990515 (CCYYMMDD = May 15, 1999)

Default:  14520101 (CCYYMMDD = January 1, 1452

FTR_SRCSCALE_NR

Feature source scale number.  Describes the scale denominator of the map or image source for the hydrography water point data addition or update in the database.  Exact scale can be input.  The density of hydrography features displayed will vary by the base map scale.  A default scale of “0” should be used when the source scale is unknown.

Example:  24000

Default:  0

FTR_ACCUR_NR

Feature accuracy number.  Describes the positional accuracy of the hydrography water point data being added or updated in the database.   Describes the correctness of the measurement.   Use actual value e.g. .001; 3; 100.   All units are entered in meters.  A default code of “0.000” should be used when the accuracy is unknown.

Example:  24000

Default:  0.000

FTR_ORG_CD

Feature organization code.  The organization that compiled, entered, updated or deleted the hydrography water point data. This list will grow as new organizations begin to add or update information and are certified by the clearinghouse. The Clearinghouse Manager will maintain the list of organizations authorized  to participate in the editing of Hydrography Framework data.

Example:  waecy

These codes can be found in the associated lookup table listed in Section 3 - Appendix.

FTR_EDIT_DT

Feature edit date.  The date the feature was either entered, updated or deleted in the hydrography coverage.  Represents the date when the data was incorporated into the database.  This item is utilized to track changes in the database.

Example:  19980515 (CCYYMMDD = May 15, 1998)

Section 3 Appendix

Acknowledgements

A very special thanks to the authors and reviewers of this document.  Many years have gone into the development of the data dictionary and physical data model.

The basic framework for this system was developed out of the efforts of the Washington Surface Water Identification Study Subcommittee of the Water Resources Data Management Task Force.  Subcommittee members included representatives from tribes; environmental and agricultural groups; federal, state, and local government agencies; and other interested entities.

This work was embraced and further efforts were continued by the US Forest Service, WA Department of Fish and Wildlife, Pacific State Marine Fisheries Commission, WA Department of Ecology, WA Department of Natural Resources and the Oregon and Washington Hydrography Framework participants.

Authors:

Joy Denkers and Dan Saul - WA Department of Ecology

Contributors and Reviewers:

Deborah Naslund, Carl Harris, Ken Reister, Tim Young - WA Dept. of Natural Resources

Dick O’Connor, Martin Hudson – WA Dept. of Fish & Wildlife

Rick Jordan, Bill Wettengel, Ken Adee, Dale Guenther – US Forest Service

Bob Harmon – OR Water Resources Department

Dan Wickwire – US Bureau of Land Management

Mike Beaty – US Bureau of Reclamation

David Fox – US Army Corps of Engineers

Jack Horton – Environmental Systems Research Institute, Inc.

And Various Oregon & Washington Hydrography Framework Participants

Data Dictionary Code Tables

### Watercourse

Code Table Name:  wc.lut_wc_ln_type_cd

1

WC_LN_TYPE_CD              =  5

WC_LN_TYPE_LU              = Artificial connector

WC_LN_TYPE_DS              = Watercourse line projected for connectivity purposes (stream short of the

shoreline due to scale or subsurface flow)

2

WC_LN_TYPE_CD              = 10

WC_LN_TYPE_LU              = Single

WC_LN_TYPE_DS              = Single-line representing a watercourse segment

3

WC_LN_TYPE_CD              = 20

WC_LN_TYPE_LU              = Interior - in water body

WC_LN_TYPE_DS              = Watercourse interior line represented within a water body (lake, reservoir)

4

WC_LN_TYPE_CD              = 21

WC_LN_TYPE_LU              = Interior - double banked stream

WC_LN_TYPE_DS              = Watercourse interior line represented within a double banked watercourse

(Columbia River)

5

WC_LN_TYPE_CD              = 30

WC_LN_TYPE_LU              = Watercourse/body perimeter

WC_LN_TYPE_DS              = Watercourse segment and water body perimeter (stream & marsh bank

share the same line)

6

WC_LN_TYPE_CD              = 99

WC_LN_TYPE_LU              = Unknown/Unclassified

WC_LN_TYPE_DS              = Unknown or Unclassified

##### Code Table Name:  wc.lut_wc_flow_path_cd

1

WC_FLOW_PATH_CD              = 1

WC_FLOW_PATH_LU              =  Primary

WC_FLOW_PATH_DS              =  Primary path of the watercourse centerline that flows through the

waterbody.   The linear path representing the flow of water from the     main inlet to the main outlet of a polygonal water body.

2

WC_FLOW_PATH_CD              = 2

WC_FLOW_PATH_LU              = Secondary

WC_FLOW_PATH_DS              = Secondary path of the watercourse centerline that flows through

the water body. The linear path that represent additional flow paths of water, usually from secondary tributaries entering and connecting to the primary path.

3

WC_FLOW_PATH_CD              = 3

WC_FLOW_PATH_LU              = Not applicable

WC_FLOW_PATH_DS              =  Not applicable because the watercourse line doesn’t flow through a

water body.  Codes are not applied to single lines representing a watercourse.

Code Table Name:  wc.lut_wc_contu_cd

1

WC_CONTU_CD                = con

WC_CONTU_LU                = Continuous

WC_CONTU_DS                = Continuous. A channel with no interruptions in space.

2

WC_CONTU_CD                = int

WC_CONTU_LU                = Interrupted

WC_CONTU_DS                = Interrupted. A perennial flow with intervening intermittent or

ephemeral segments or intermittent flow with intervening ephemeral    segments

3

WC_ CONTU _CD               = sub

WC_ CONTU _LU               = Sub-surface

WC_ CONTU _DS               = Sub-surface.  Watercourse reach that represents a sub-surface flow.

4

WC_CONTU_CD                = unk

WC_CONTU_LU                = Unknown/Unclassified

WC_CONTU_DS                = Unknown or unclassified

Code Table Name:  wc.lut_wc_period_cd

1

WC_PERIOD_CD               = eph

WC_PERIOD_LU               = Ephemeral

WC_PERIOD_DS               = Ephemeral.  Watercourse that exist only as a result of storm precipitation.

2

WC_PERIOD_CD               = int

WC_PERIOD_LU               = Intermittent or seasonal

WC_PERIOD_DS               = Intermittent or seasonal.  Watercourse that is dry during certain times of the

year.

3

WC_PERIOD_CD               = per

WC_PERIOD_LU               = Perennial

WC_PERIOD_DS               = Perennial.  Watercourse that essentially exist year round

4

WC_PERIOD_CD               = unk

WC_PERIOD_LU               = Unknown/Unclassified

WC_PERIOD_DS               = Unknown or unclassified.  Used when condition information is unknown or

unclassified

### Water Body

Code Table Name:  wb.lut_wb_period_cd

1

WB_PERIOD_CD               = dry

WB_PERIOD_LU               = Dry land

WB_PERIOD_DS               = Dry land.  Indicates an island.

2

WB_PERIOD_CD               = eph

WB_PERIOD_LU               = Ephemeral

WB_PERIOD_DS               = Ephemeral.  Water bodies that exist only as a result of storm precipitation.

3

WB_PERIOD_CD               = int

WB_PERIOD_LU               = Intermittent or seasonal

WB_PERIOD_DS               = Intermittent or seasonal.  Water bodies that are dry during certain times of

the year.

4

WB_PERIOD_CD               = per

WB_PERIOD_LU               = Perennial

WB_PERIOD_DS               = Perennial.  Water bodies that essentially exist year round.

5

WB_PERIOD_CD               = unk

WB_PERIOD_LU               = Unknown/Unclassified

WB_PERIOD_DS               = Unknown or Unclassified.  Used when condition information is unknown or

unclassified.

### Water Shoreline

Code Table Name:  ws.lut_ws_datum_cd

1

WS_DATUM_CD                = ehw

WS_DATUM_LU                = Extreme high

WS_DATUM_DS                = Extreme high water

2

WS_DATUM_CD                = elw

WS_DATUM_LU                = Extreme low

WS_DATUM_DS                = Extreme low water

3

WS_DATUM_CD                = fw

WS_DATUM_LU                = Fresh water

WS_DATUM_DS                = Fresh water shoreline

4

WS_DATUM_CD                = mhhw

WS_DATUM_LU                = Mean higher high

WS_DATUM_DS                = Mean higher high water

5

WS_DATUM_CD                = mhw

WS_DATUM_LU                = Mean high

WS_DATUM_DS                = Mean high water

6

WS_DATUM_CD                = mllw

WS_DATUM_LU                = Mean lower low

WS_DATUM_DS                = Mean lower low water

7

WS_DATUM_CD                = mlw

WS_DATUM_LU                = Mean low

WS_DATUM_DS                = Mean low water

8

WS_DATUM_CD                = na

WS_DATUM_LU                = Not a shoreline

WS_DATUM_DS                = Does not constitute a shoreline.  No datum associated.

Code Table Name:  ws.lut_ws_dflt_shore_cd

1

WS_DFLT_SHORE_CD           = n

WS_DFLT_SHORE_LU           = No

WS_DFLT_SHORE_DS           = No, it is not the default shoreline

2

WS_DFLT_SHORE_CD           = y

WS_DFLT_SHORE_LU           = Yes

WS_DFLT_SHORE_DS           = Yes, it is the default shoreline

Code Table Name:  ws.lut_ws_type_cd

1

WS_TYPE_CD                 =  1

WS_TYPE_LU                 = Marine mainland

WS_TYPE_DS                 = Marine mainland shoreline

2

WS_TYPE_CD                 =  2

WS_TYPE_LU                 = Marine island

WS_TYPE_DS                 = Marine island shoreline

3

WS_TYPE_CD                 =  3

WS_TYPE_LU                 = Freshwater

WS_TYPE_DS                 = Freshwater shoreline

4

WS_TYPE_CD                 =  4

WS_TYPE_LU                 = Freshwater island

WS_TYPE_DS                 = Freshwater island shoreline

5

WS_TYPE_CD                 =  5

WS_TYPE_LU                 = Artificial

WS_TYPE_DS                 = Artificial line

6

WS_TYPE_CD                 =  6

WS_TYPE_LU                 = Estuarine

WS_TYPE_DS                 = Estuarine (bays) shoreline

7

WS_TYPE_CD                 = 99

WS_TYPE_LU                 = Unknown/Unclassified

WS_TYPE_DS                 = Unknown or unclassified. Used when information is unknown or unclassified.

### Water Point

Code Table Name:  wp.lut_wp_period_cd

1

WP_PERIOD_CD               = eph

WP_PERIOD_LU               = Ephemeral

WP_PERIOD_DS               = Ephemeral.  Water features that exist only as a result of storm precipitation.

2

WP_PERIOD_CD               = int

WP_PERIOD_LU               = Intermittent/seasonal

WP_PERIOD_DS               = Intermittent or seasonal.  Water features that are dry during certain times of

the year.

3

WP_PERIOD_CD               = per

WP_PERIOD_LU               = Perennial

WP_PERIOD_DS               = Perennial.  Water feature that essentially exist year round

4

WP_PERIOD_CD               = unk

WP_PERIOD_LU               = Unknown/Unclassified

WP_PERIOD_DS               = Unknown or unclassified.  Used when condition information is unknown or

unclassified.

### Multiple Coverage Code Tables

The following code tables are reflected in each of the water coverages described in this physical data model - points, bodies, shorelines, and courses.  These represent the common codes between all layers (wc, wb, ws, wp) and are collectively referred to with the "wx" abbreviation.

The "x" in "wx" reflects the variable that is replaced depending on the code table that is used for the respective coverage.

Example: wx.lut_wx_hydr_ftr_cd	wc.lut_wx_hydr_ftr_cd

wb.lut_wx_hydr_ftr_cd

ws.lut_wx_hydr_ftr_cd

wp.lut_wx_hydr_ftr_cd

Code Table Name:  wx.lut_wx_hydr_ftr_cd

1

WX_HYDR_FTR_CD             = DC

WX_HYDR_FTR_LU             = Ditches/canals

WX_HYDR_FTR_DS             = Ditches, canals, flumes

2

WX_HYDR_FTR_CD             = ES

WX_HYDR_FTR_LU             = Bays/estuaries

WX_HYDR_FTR_DS             = Bays, estuaries, and oceans

3

WX_HYDR_FTR_CD             = GL

WX_HYDR_FTR_LU             = Glaciers/snowfields

WX_HYDR_FTR_DS             = Glaciers or permanent snowfields

4

WX_HYDR_FTR_CD             = IM

WX_HYDR_FTR_LU             = Impoundments

WX_HYDR_FTR_DS             = Impoundments

5

WX_HYDR_FTR_CD             = IS

WX_HYDR_FTR_LU             = Islands

WX_HYDR_FTR_DS             = Islands

6

WX_HYDR_FTR_CD             = IW

WX_HYDR_FTR_LU             = Impounded wet areas

WX_HYDR_FTR_DS             = Impounded wet areas

7

WX_HYDR_FTR_CD             = LA

WX_HYDR_FTR_LU             = Lakes/ponds

WX_HYDR_FTR_DS             = Lakes and ponds

8

WX_HYDR_FTR_CD             = PP

WX_HYDR_FTR_LU             = Pipelines/water conveyance

WX_HYDR_FTR_DS             = Pipelines and water conveyance structures

9

WX_HYDR_FTR_CD             = SC

WX_HYDR_FTR_LU             = Side channels

WX_HYDR_FTR_DS             = Side channels to rivers or stream

10

WX_HYDR_FTR_CD             = SP

WX_HYDR_FTR_LU             = Springs/seeps

WX_HYDR_FTR_DS             = Springs and seeps

11

WX_HYDR_FTR_CD             = ST

WX_HYDR_FTR_LU             = Streams/rivers

WX_HYDR_FTR_DS             = Streams and rivers

12

WX_HYDR_FTR_CD             = UN

WX_HYDR_FTR_LU             = Unknown/Unclassified

WX_HYDR_FTR_DS             = Unknown or unclassified

13

WX_HYDR_FTR_CD             = WT

WX_HYDR_FTR_LU             = Wet areas

WX_HYDR_FTR_DS             = Wet areas

Code Table Name:  wx.lut_wx_cart_ftr_cd

1

WX_CART_FTR_CD             =  100

WX_CART_FTR_LU             = Alkali flat

WX_CART_FTR_DS             = Alkali flat

2

WX_CART_FTR_CD             =  101

WX_CART_FTR_LU             = Reservoir

WX_CART_FTR_DS             = Reservoir

3

WX_CART_FTR_CD             =  103

WX_CART_FTR_LU             = Glacier/snowfield

WX_CART_FTR_DS             = Glacier or permanent snowfield

4

WX_CART_FTR_CD             =  105

WX_CART_FTR_LU             = Inundation

WX_CART_FTR_DS             = Inundation

5

WX_CART_FTR_CD             =  106

WX_CART_FTR_LU             = Fish hatchery/farm

WX_CART_FTR_DS             = Fish hatchery or farm

6

WX_CART_FTR_CD             =  107

WX_CART_FTR_LU             = Industrial water impoundment

WX_CART_FTR_DS             = Industrial water impoundment

7

WX_CART_FTR_CD             =  109

WX_CART_FTR_LU             = Sewage pond/filtration bed

WX_CART_FTR_DS             = Sewage disposal pond or filtration bed

8

WX_CART_FTR_CD             =  110

WX_CART_FTR_LU             = Tailings pond

WX_CART_FTR_DS             = Tailings pond

9

WX_CART_FTR_CD             =  111

WX_CART_FTR_LU             = Marsh/wetland

WX_CART_FTR_DS             = Marsh, wetland, swamp, bog

10

WX_CART_FTR_CD             =  114

WX_CART_FTR_LU             = Cranberry bog

WX_CART_FTR_DS             = Cranberry bog

11

WX_CART_FTR_CD             =  115

WX_CART_FTR_LU             = Flats

WX_CART_FTR_DS             = Flats (tidal, mud, sand, gravel)

12

WX_CART_FTR_CD             =  116

WX_CART_FTR_LU             = Bay/estuary

WX_CART_FTR_DS             = Bay, estuary, gulf, ocean or sea

13

WX_CART_FTR_CD             =  117

WX_CART_FTR_LU             = Shoal

WX_CART_FTR_DS             = Shoal

14

WX_CART_FTR_CD             =  300

WX_CART_FTR_LU             = Spring/seep

WX_CART_FTR_DS             = Spring or seep

15

WX_CART_FTR_CD             =  400

WX_CART_FTR_LU             = Rapids

WX_CART_FTR_DS             = Rapids

16

WX_CART_FTR_CD             =  401

WX_CART_FTR_LU             = Falls

WX_CART_FTR_DS             = Falls

17

WX_CART_FTR_CD             =  402

WX_CART_FTR_LU             = Gravel pit/quarry with water

WX_CART_FTR_DS             = Gravel pit or quarry filled with water

18

WX_CART_FTR_CD             =  406

WX_CART_FTR_LU             = Dam/weir

WX_CART_FTR_DS             = Dam or weir

19

WX_CART_FTR_CD             =  407

WX_CART_FTR_LU             = Canal lock/sluice

WX_CART_FTR_DS             = Canal lock or sluice gate

20

WX_CART_FTR_CD             =  408

WX_CART_FTR_LU             = Spillway

WX_CART_FTR_DS             = Spillway

21

WX_CART_FTR_CD             =  410

WX_CART_FTR_LU             = Exposed rock

WX_CART_FTR_DS             = Exposed rock

22

WX_CART_FTR_CD             =  412

WX_CART_FTR_LU             = Stream/river

WX_CART_FTR_DS             = Stream or river

23

WX_CART_FTR_CD             =  414

WX_CART_FTR_LU             = Ditch/canal

WX_CART_FTR_DS             = Ditch or canal

24

WX_CART_FTR_CD             =  415

WX_CART_FTR_LU             = Aqueduct

WX_CART_FTR_DS             = Aqueduct

25

WX_CART_FTR_CD             =  417

WX_CART_FTR_LU             = Penstock

WX_CART_FTR_DS             = Penstock

26

WX_CART_FTR_CD             =  418

WX_CART_FTR_LU             = Siphon

WX_CART_FTR_DS             = Siphon

27

WX_CART_FTR_CD             =  419

WX_CART_FTR_LU             = Channel in water

WX_CART_FTR_DS             = Channel in water area

28

WX_CART_FTR_CD             =  420

WX_CART_FTR_LU             = Wash/ephemeral

WX_CART_FTR_DS             = Wash or ephemeral drain

29

WX_CART_FTR_CD             =  421

WX_CART_FTR_LU             = Lake/pond

WX_CART_FTR_DS             = Lake or pond

30

WX_CART_FTR_CD             =  422

WX_CART_FTR_LU             = Reef

WX_CART_FTR_DS             = Reef

31

WX_CART_FTR_CD             =  423

WX_CART_FTR_LU             = Sand/gravel in open water

WX_CART_FTR_DS             = Sand or gravel in open water

32

WX_CART_FTR_CD             =  425

WX_CART_FTR_LU             = Fish ladder

WX_CART_FTR_DS             = Fish ladder

33

WX_CART_FTR_CD             =  466

WX_CART_FTR_LU             = Pier/jetty

WX_CART_FTR_DS             = Pier, jetty, breakwater, dock, wharf or causeway

34

WX_CART_FTR_CD             =  901

WX_CART_FTR_LU             = Impoundment

WX_CART_FTR_DS             = Impoundment

35

WX_CART_FTR_CD             =  902

WX_CART_FTR_LU             = Island

WX_CART_FTR_DS             = Island

36

WX_CART_FTR_CD             =  999

WX_CART_FTR_LU             = Unknown/Unclassified

WX_CART_FTR_DS             = Unknown or unclassified

Code Table Name:  wx.lut_ftr_mod_cd

1

FTR_MOD_CD                 = add

FTR_MOD_LU                 = Addition

FTR_MOD_DS                 = Addition of spatial feature

2

FTR_MOD_CD                 = del

FTR_MOD_LU                 = Deletion

FTR_MOD_DS                 = Deletion of existing spatial feature.  Documents the historical ID which

maybe referenced in an orphaned event row that will have no matching spatial record.

3

FTR_MOD_CD                 = upd

FTR_MOD_LU                 = Update

FTR_MOD_DS                 = Update of existing spatial feature

Code Table Name:  wx.lut_ftr_input_cd

1

FTR_INPUT_CD               =  1

FTR_INPUT_LU               = Automatic

FTR_INPUT_DS               = Automatic via computer software

2

FTR_INPUT_CD               =  2

FTR_INPUT_LU               = Scan

FTR_INPUT_DS               = Scanning

3

FTR_INPUT_CD               =  3

FTR_INPUT_LU               = Table digitize

FTR_INPUT_DS               = Tablet digitizing

4

FTR_INPUT_CD               =  4

FTR_INPUT_LU               = Coordinate File

FTR_INPUT_DS               = Spatial coordinate file

5

FTR_INPUT_CD               =  5

FTR_INPUT_LU               = Line tracking

FTR_INPUT_DS               = Automatic line tracing

6

FTR_INPUT_CD               =  6

FTR_INPUT_LU               = Heads-up digitize

FTR_INPUT_DS               = Heads-up digitizing

7

FTR_INPUT_CD               = 99

FTR_INPUT_LU               = Unknown/unclassified

FTR_INPUT_DS               = Unspecified map feature input method

Code Table Name:  wx.lut_ftr_intrp_cd

1

FTR_INTRP_CD               =  1

FTR_INTRP_LU               = Photogrammetric

FTR_INTRP_DS               = Photogrammetric interpretation

2

FTR_INTRP_CD               =  2

FTR_INTRP_LU               = GPS

FTR_INTRP_DS               = Global Position System (GPS)

3

FTR_INTRP_CD               =  3

FTR_INTRP_LU               = Photointerp

FTR_INTRP_DS               = Photointerpretation

4

FTR_INTRP_CD               =  4

FTR_INTRP_LU               = Crenulation

FTR_INTRP_DS               = Interpretation of streams from contour crenulation

5

FTR_INTRP_CD               =  5

FTR_INTRP_LU               = Surface modeling

FTR_INTRP_DS               = Surface flow modeling

6

FTR_INTRP_CD               =  6

FTR_INTRP_LU               = Transect

FTR_INTRP_DS               = Transect along a stream channel

7

FTR_INTRP_CD               =  7

FTR_INTRP_LU               = Existing work

FTR_INTRP_DS               = Existing line work

8

FTR_INTRP_CD               =  8

FTR_INTRP_LU               = Best guess

FTR_INTRP_DS               = Stream not directly observable so stream location is estimated

9

FTR_INTRP_CD               = 99

FTR_INTRP_LU               = Unknown/unclassified

FTR_INTRP_DS               = Unknown or unclassified

Code Table Name:  wx.lut_ftr_src_cd

1

FTR_SRC_CD                 =   1

FTR_SRC_LU                 = USGS Map

FTR_SRC_DS                 = USGS Topographic Map

2

FTR_SRC_CD                 =   2

FTR_SRC_LU                 = Orthophoto

FTR_SRC_DS                 = Orthophotography

3

FTR_SRC_CD                 =   3

FTR_SRC_LU                 = Aerial photo

FTR_SRC_DS                 = Aerial Photograph

4

FTR_SRC_CD                 =   4

FTR_SRC_LU                 = MSS Imagery

FTR_SRC_DS                 = Multi-Spectral Satellite Imagery

5

FTR_SRC_CD                 =   5

FTR_SRC_LU                 = Field Survey

FTR_SRC_DS                 = Field Survey of on the ground observation

6

FTR_SRC_CD                 =   6

FTR_SRC_LU                 = Plan Map

FTR_SRC_DS                 = Planning Map

7

FTR_SRC_CD                 =   7

FTR_SRC_LU                 = Field Map

FTR_SRC_DS                 = Field Map

8

FTR_SRC_CD                 =   8

FTR_SRC_LU                 = DEM

FTR_SRC_DS                 = Digital Elevation Model (DEM)

9

FTR_SRC_CD                 =   9

FTR_SRC_LU                 = Radar Imagery

FTR_SRC_DS                 = Radar Imagery

10

FTR_SRC_CD                 =  10

FTR_SRC_LU                 = Laser Imagery

FTR_SRC_DS                 = Laser Imagery

11

FTR_SRC_CD                 =  11

FTR_SRC_LU                 = CFF

FTR_SRC_DS                 = Cartographic Feature File (CFF)

12

FTR_SRC_CD                 =  12

FTR_SRC_LU                 = NWI Map

FTR_SRC_DS                 = National Wetlands Inventory (NWI) Map

13

FTR_SRC_CD                 =  13

FTR_SRC_LU                 = Imagery - Unspecified

FTR_SRC_DS                 = Imagery – Unspecified Source

14

FTR_SRC_CD                 =  99

FTR_SRC_LU                 = Unknown/Unclassified

FTR_SRC_DS                 = Unknown or unclassified

Code Table Name:  wx.lut_ftr_org_cd

1

FTR_ORG_CD                 = bcmelp

FTR_ORG_LU                 = BC Ministry of Environ

FTR_ORG_DS                 = British Columbia Ministry of Environment Lands and Parks

2

FTR_ORG_CD                 = calwater

FTR_ORG_LU                 = CALWATER

FTR_ORG_DS                 = The California Interagency Watershed Mapping Committee

3

FTR_ORG_CD                 = caspam

FTR_ORG_LU                 = CASPAM

FTR_ORG_DS                 = California Sierra Province Area Management

4

FTR_ORG_CD                 = clams

FTR_ORG_LU                 = CLAMS

FTR_ORG_DS                 = Coastal Landscape Analysis and Modeling Study

5

FTR_ORG_CD                 = coclrkwa

FTR_ORG_LU                 = Clark Co WA

FTR_ORG_DS                 = Clark County WA

6

FTR_ORG_CD                 = cokingwa

FTR_ORG_LU                 = King Co WA

FTR_ORG_DS                 = King County WA

7

FTR_ORG_CD                 = copierwa

FTR_ORG_LU                 = Pierce Co WA

FTR_ORG_DS                 = Pierce County WA

8

FTR_ORG_CD                 = cosnohwa

FTR_ORG_LU                 = Snohomish Co WA

FTR_ORG_DS                 = Snohomish County WA

9

FTR_ORG_CD                 = cospokwa

FTR_ORG_LU                 = Spokane Co WA

FTR_ORG_DS                 = Spokane County WA

10

FTR_ORG_CD                 = cothurswa

FTR_ORG_LU                 = Thurston Co WA

FTR_ORG_DS                 = Thurston County WA

11

FTR_ORG_CD                 = coyakwa

FTR_ORG_LU                 = Yakima Co WA

FTR_ORG_DS                 = Yakima County WA

12

FTR_ORG_CD                 = ctyolywa

FTR_ORG_LU                 = Olympia WA

FTR_ORG_DS                 = City of Olympia WA

13

FTR_ORG_CD                 = ctyseawa

FTR_ORG_LU                 = Seattle WA

FTR_ORG_DS                 = City of Seattle WA

14

FTR_ORG_CD                 = ctyvanwa

FTR_ORG_LU                 = Vancouver WA

FTR_ORG_DS                 = City of Vancouver WA

15

FTR_ORG_CD                 = id

FTR_ORG_LU                 = IDAHO

FTR_ORG_DS                 = Idaho

16

FTR_ORG_CD                 = lvwfbr

FTR_ORG_LU                 = Longview Fiber

FTR_ORG_DS                 = Longview Fiber Company

17

FTR_ORG_CD                 = nwifc

FTR_ORG_LU                 = NWIFC

FTR_ORG_DS                 = Northwest Indian Fisheries Commission

18

FTR_ORG_CD                 = ordeq

FTR_ORG_LU                 = ODEQ

FTR_ORG_DS                 = OR Dept. of Environmental Quality

19

FTR_ORG_CD                 = ordf

FTR_ORG_LU                 = ODF

FTR_ORG_DS                 = Oregon Dept. of Forestry

20

FTR_ORG_CD                 = ordwr

FTR_ORG_LU                 = ODWR

FTR_ORG_DS                 = Oregon Dept. of Water Resources

21

FTR_ORG_CD                 = orit

FTR_ORG_LU                 = OIT

FTR_ORG_DS                 = Oregon Institute of Technology

22

FTR_ORG_CD                 = psrc

FTR_ORG_LU                 = PSRC

FTR_ORG_DS                 = Puget Sound Regional Council

23

FTR_ORG_CD                 = raynr

FTR_ORG_LU                 = Rayonier

FTR_ORG_DS                 = ITT Rayonier

24

FTR_ORG_CD                 = reo

FTR_ORG_LU                 = REO

FTR_ORG_DS                 = HUC 5 lines used as a starting basis

25

FTR_ORG_CD                 = smpsn

FTR_ORG_LU                 = Simpson

FTR_ORG_DS                 = Simpson Timber Company

26

FTR_ORG_CD                 = titan

FTR_ORG_LU                 = TITAN

FTR_ORG_DS                 = Titan Geospatial

27

FTR_ORG_CD                 = unknown

FTR_ORG_LU                 = Unknown/Unclassified

FTR_ORG_DS                 = Unknown or unclassified input organization

28

FTR_ORG_CD                 = usace

FTR_ORG_LU                 = USACE

FTR_ORG_DS                 = U.S. Army Corps of Engineers

29

FTR_ORG_CD                 = usblm

FTR_ORG_LU                 = USBLM

FTR_ORG_DS                 = U.S. Bureau of Land Management

30

FTR_ORG_CD                 = usblm-bns

FTR_ORG_LU                 = USBLM-Burns

FTR_ORG_DS                 = U.S. Bureau of Land Management - Burns District

31

FTR_ORG_CD                 = usblm-cby

FTR_ORG_LU                 = USBLM-Coos Bay

FTR_ORG_DS                 = U.S. Bureau of Land Management - Coos Bay District

32

FTR_ORG_CD                 = usblm-eug

FTR_ORG_LU                 = USBLM-Eugene

FTR_ORG_DS                 = U.S. Bureau of Land Management - Eugene District

33

FTR_ORG_CD                 = usblm-lak

FTR_ORG_LU                 = USBLM-Lakeview

FTR_ORG_DS                 = U.S. Bureau of Land Management - Lakeview District

34

FTR_ORG_CD                 = usblm-med

FTR_ORG_LU                 = USBLM-Medford

FTR_ORG_DS                 = U.S. Bureau of Land Management - Medford District

35

FTR_ORG_CD                 = usblm-oso

FTR_ORG_LU                 = USBLM-Oregon State Office

FTR_ORG_DS                 = U.S. Bureau of Land Management - Oregon State Office

36

FTR_ORG_CD                 = usblm-pri

FTR_ORG_LU                 = USBLM-Prineville

FTR_ORG_DS                 = U.S. Bureau of Land Management - Prineville District

37

FTR_ORG_CD                 = usblm-rsb

FTR_ORG_LU                 = USBLM-Roseburg

FTR_ORG_DS                 = U.S. Bureau of Land Management - Roseburg District

38

FTR_ORG_CD                 = usblm-slm

FTR_ORG_LU                 = USBLM-Salem

FTR_ORG_DS                 = U.S. Bureau of Land Management - Salem District

39

FTR_ORG_CD                 = usblm-spo

FTR_ORG_LU                 = USBLM-Spokane

FTR_ORG_DS                 = U.S. Bureau of Land Management - Spokane District

40

FTR_ORG_CD                 = usblm-val

FTR_ORG_LU                 = USBLM-Vale

FTR_ORG_DS                 = U.S. Bureau of Land Management - Vale District

41

FTR_ORG_CD                 = usbor

FTR_ORG_LU                 = USBR

FTR_ORG_DS                 = U.S. Bureau of Reclamation

42

FTR_ORG_CD                 = usbpa

FTR_ORG_LU                 = USBPA

FTR_ORG_DS                 = U.S. Bonneville Power Administration

43

FTR_ORG_CD                 = usepa

FTR_ORG_LU                 = USEPA

FTR_ORG_DS                 = U.S. Environmental Protection Agency

44

FTR_ORG_CD                 = usepa-r10

FTR_ORG_LU                 = USEPA-10

FTR_ORG_DS                 = U.S. Environmental Protection Agency - Region 10

45

FTR_ORG_CD                 = usfs

FTR_ORG_LU                 = USFS

FTR_ORG_DS                 = U.S. Forest Service

46

FTR_ORG_CD                 = usfs-col

FTR_ORG_LU                 = USFS-Colville

FTR_ORG_DS                 = U.S. Forest Service - Colville NF

47

FTR_ORG_CD                 = usfs-des

FTR_ORG_LU                 = USFS-Deshutes

FTR_ORG_DS                 = U.S. Forest Service - Deschutes NF

48

FTR_ORG_CD                 = usfs-fre

FTR_ORG_LU                 = USFS-Fremont

FTR_ORG_DS                 = U.S. Forest Service - Freemont NF

49

FTR_ORG_CD                 = usfs-gip

FTR_ORG_LU                 = USFS-Gifford Pinchot

FTR_ORG_DS                 = U.S. Forest Service - Gifford Pinchot NF

50

FTR_ORG_CD                 = usfs-gstc

FTR_ORG_LU                 = USFS-Geospatial Service and Technology

FTR_ORG_DS                 = U.S. Forest Service - Geospatial Service and Technology Center

51

FTR_ORG_CD                 = usfs-kla

FTR_ORG_LU                 = USFS-Klamath

FTR_ORG_DS                 = U.S. Forest Service - Klamath NF

52

FTR_ORG_CD                 = usfs-mal

FTR_ORG_LU                 = USFS-Malheur

FTR_ORG_DS                 = U.S. Forest Service - Malheur NF

53

FTR_ORG_CD                 = usfs-mbs

FTR_ORG_LU                 = USFS-Mt.  Baker Snoqualmie

FTR_ORG_DS                 = U.S. Forest Service - Mt. Baker-Snoqualmie NF

54

FTR_ORG_CD                 = usfs-mth

FTR_ORG_LU                 = USFS-Mt. Hood

FTR_ORG_DS                 = U.S. Forest Service - Mt. Hood NF

55

FTR_ORG_CD                 = usfs-och

FTR_ORG_LU                 = USFS-Ochoco

FTR_ORG_DS                 = U.S. Forest Service - Ochoco NF

56

FTR_ORG_CD                 = usfs-oka

FTR_ORG_LU                 = USFS-Okanogan

FTR_ORG_DS                 = U.S. Forest Service - Okanogan NF

57

FTR_ORG_CD                 = usfs-oly

FTR_ORG_LU                 = USFS-Olympic

FTR_ORG_DS                 = U.S. Forest Service - Olympic NF

58

FTR_ORG_CD                 = usfs-sis

FTR_ORG_LU                 = USFS-Siskiyou

FTR_ORG_DS                 = U.S. Forest Service - Siskiyou NF

59

FTR_ORG_CD                 = usfs-siu

FTR_ORG_LU                 = USFS-Siuslaw

FTR_ORG_DS                 = U.S. Forest Service - Siuslaw NF

60

FTR_ORG_CD                 = usfs-six

FTR_ORG_LU                 = USFS-Six Rivers

FTR_ORG_DS                 = U.S. Forest Service - Six Rivers NF

61

FTR_ORG_CD                 = usfs-uma

FTR_ORG_LU                 = USFS-Umatilla

FTR_ORG_DS                 = U.S. Forest Service - Umatilla NF

62

FTR_ORG_CD                 = usfs-ump

FTR_ORG_LU                 = USFS-Umpqua

FTR_ORG_DS                 = U.S. Forest Service - Umpqua NF

63

FTR_ORG_CD                 = usfs-waw

FTR_ORG_LU                 = USFS-Wallowa-Whitman

FTR_ORG_DS                 = U.S. Forest Service - Wallowa-Whitman NF

64

FTR_ORG_CD                 = usfs-wen

FTR_ORG_LU                 = USFS-Wenatchee

FTR_ORG_DS                 = U.S. Forest Service - Wenatchee NF

65

FTR_ORG_CD                 = usfs-wil

FTR_ORG_LU                 = USFS-Willamette

FTR_ORG_DS                 = U.S. Forest Service - Willamette NF

66

FTR_ORG_CD                 = usfs-win

FTR_ORG_LU                 = USFS-Winema

FTR_ORG_DS                 = U.S. Forest Service - Winema NF

67

FTR_ORG_CD                 = usfws

FTR_ORG_LU                 = USFWS

FTR_ORG_DS                 = U.S. Fish and Wildlife Service

68

FTR_ORG_CD                 = usgs

FTR_ORG_LU                 = USGS

FTR_ORG_DS                 = U.S. Geological Survey

69

FTR_ORG_CD                 = usgs-nmd

FTR_ORG_LU                 = USGS-NMD

FTR_ORG_DS                 = U.S. Geological Survey - National Mapping Division

70

FTR_ORG_CD                 = usnmfs

FTR_ORG_LU                 = USNMFS

FTR_ORG_DS                 = U.S.National Marine Fisheries Service

71

FTR_ORG_CD                 = usnps

FTR_ORG_LU                 = USNPS

FTR_ORG_DS                 = U.S. National Park Service

72

FTR_ORG_CD                 = usnrcs

FTR_ORG_LU                 = USNRCS

FTR_ORG_DS                 = Natural Resources Conservation Service

73

FTR_ORG_CD                 = wadfw

FTR_ORG_LU                 = WDFW

FTR_ORG_DS                 = Washington Department of Fish and Wildlife

74

FTR_ORG_CD                 = wadnr

FTR_ORG_LU                 = WDNR

FTR_ORG_DS                 = Washington State Department of Natural Resources

75

FTR_ORG_CD                 = wadot

FTR_ORG_LU                 = WDOT

FTR_ORG_DS                 = Washington Department of Transportation

76

FTR_ORG_CD                 = waecy

FTR_ORG_LU                 = Ecology

FTR_ORG_DS                 = Washington Department of Ecology

77

FTR_ORG_CD                 = weyhsr

FTR_ORG_LU                 = Weyerhaeuser

FTR_ORG_DS                 = Weyerhaeuser Company

Cross Reference Code Table Name:  wx.xrf_hydr_cart

Record  WX_HYDR_FTR_CD WX_CART_FTR_CD

1  dc              407

2  dc              408

3  dc              414

4  dc              425

5  es              115

6  es              116

7  es              117

8  es              419

9  es              422

10  es              466

11  gl              103

12  im              101

13  im              105

14  im              106

15  im              107

16  im              109

17  im              466

18  im              901

19  is              410

20  is              423

21  is              902

22  iw              111

23  iw              114

24  la              100

25  la              110

26  la              402

27  la              421

28  la              466

29  pp              415

30  pp              417

31  pp              418

32  sc              412

33  sp              300

34  st              117

35  st              400

36  st              401

37  st              406

38  st              412

39  st              419

40  st              420

41  st              466

42  un              999

43  wt              111

Data Dictionary Format Sheet Explanations

The formatting sheets provide the users with a road map with a description of how information is stored in the various data layers and coverages described in this data dictionary. Each coverage type is listed and its various components explained in detail.

Polygon Layer:1

Line . . .

Feature Attribute Table Outline

Begin	Defined	Item
  Column4	Item Name5	Definition7

13*	Cover-ID	4,5,B

17	VARIABLE1	1,1,I

* Redefined Items*8

VARIABLE1

This is a description of Variable1, including any coding scheme and permissible values 
(e.g., 1 = good, 2 = bad, 3 = ugly).

Notes:

1The type of coverage, either polygon, line, or point; or type of table, either route, section, event, or reference.

2A descriptive variable (item) name.

3In a Polygon Attribute Table (PAT), there are four items automatically assigned.  
  Only the last item, Cover-ID, is shown above.  They are:

Area 	(units in square coverage units)	4,12,F

Perimeter 	(units in coverage units)	4,12,F

Cover# 	(polygon internal number; computer assigned)	4,5,B

Cover-ID 	(user defined ID; if not assigned by user, will 	4,5,B
	usually default to Cover#)

*13 for PAT, 25 for AAT

In an Arc Attribute Table (AAT), there are seven items automatically assigned.  
Only the last item, Cover-ID, is shown above.  They are:

Fnode#	(from node internal number)	4,5,B

Tnode#	(to node internal number)	4,5,B

Lpoly#	(left polygon; if only a line coverage, then set to zero)	4,5,B

Rpoly#	(right polygon)	4,5,B

Length	(units in coverage units)	4,12,B

Cover#	(arc internal number)	4,5,B

Cover-ID	(arc user ID)	4,5,B

4The variable begins in this column in the INFO record.  An INFO record can be 4,096 columns (bytes) wide.  This limit applies also to records so that the combined length of selected and related records cannot exceed 4,096.

5The defined variable name.  This is how INFO will read the item.  The item name can be up to 16 characters long, no spaces, must begin with a letter, and is case sensitive.

6An alternative name can be assigned to the item. This is sometimes done to shorten the item name.

7The item definition consists of four elements:

1.  Item name (see Note 5)

2.  Item width - the number of bytes to store the variable

3.  Output width - the number of columns to display the item value

4.  Item type

The Item width and Output width may be different because decimal and binary representations of the same numeric value have different widths.  If no output width is specified, the default width is the item width.

There are 11 possible INFO item types:

Type	Permissible 	Uses	Stored 
	   Width		   As

1. B = Binary	2 or 4	Store large/small numbers economically	Binary

2. C = Character	4,096 	Store alphanumeric data	ASCII
			(ARC imposes a 320 limit)

3. D = Date	8		Store dates	ASCII

4. F = Floating	4 or 8	Store extremely large/small numbers	Binary

5. I = Integer	1 to 16	Codes	ASCII

6. N = Numeric	1 to 16	Store decimal numbers as characters	ASCII

7. L = Leading fill	1 to 16	Store leading zeroes in numbers such as	ASCII
			Zip Codes (i.e., 01234)

8. V = Implied 	1 to 16       	decimal point

9. O = Overpunch	1 to 16

10. T = Training sign	1 to 16

11. P = Packed decimal	1 to 16

The range for a 2-byte binary is plus/minus (use symbol) 32,767; for a 4-byte binary is plus/minus 2,147,483,648 (display for this would be 4,10,B).

Types L, V, O, T, and P are not supported by ARC.  In general, the more that items are stored in binary format, the less storage space is required.

8A redefined item is a new name, type, or width for previously defined items or subsets of items in the FAT.  Commonly used to create unique relate items to access data in a lookup table.

Format Sheet Explanation - Section Table

Section Table:  	Table Name:

Section Table Outline

Begin	Defined	Item

Column	Item Name	Definition

1	ROUTELINK#	4,5,B

5	ARCLINK#	4,5,B

9	F-MEAS	4,12,F,3

13	T-MEAS	4,12,F,3

17	F-POS	4,12,F,3

21	T-POS	4,12,F,3

25	<subclass>#	4,5,B

29	<subclass>-ID	4,5,B

Data Classification - SEC

In a section attribute table (SEC), there are eight items automatically assigned. The items found in a SEC are:

Routelink# 	(route internal # from RAT; identifies the route 	4,5,B
	to which the section belongs)

Arclink#	(arc internal # from the AAT; identifies the arc to 	4,5,B
	which the section belongs)

F-meas	(measure of start position of section)	4,12,F,3

T-meas	(measure end position of section)	4,12,F,3

F-pos	(start position in terms of percentage of existing arc) 	4,12,F,3

T-pos	(end position in terms of percentage of existing arc) 	4,12,F,3

<subclass>#	(internal sequence number of the sections)	4,5,B

<subclass>-ID	(section ID; if not assigned by user, will default to subclass #)	4,5,B

Please see the ARC/INFO User's Guide, “Dynamic Segmentation,” for an explanation of routes, sections, and event tables.

Format Sheet Explanation - Route Table

Route Table:  	Table Name:

Route Attribute Table Outline

Begin	Defined	Item

Column	Item Name	Definition

1	<subclass>#	4,5,B

5	<subclass>-ID	4,5,B

9	<Route key item>	User defined

Data Classification - RAT

In a Route Attribute Table (RAT), the <subclass># is software assigned.  The <subclass>-ID is also software assigned, but can be re-assigned by the user.  The route key item is user defined and assigned.  The items in a RAT are defined as:

<subclass>>#	(internal sequence number of the sections)	4,5,B

<subclass>>-ID	(route-system ID; if not assigned by user, 	4,5,B
	will default to subclass #)

<Route key item>	(relates RAT to event databases)                                          User defined

Please see the ARC/INFO User's Guide, “Dynamic Segmentation,” for an explanation of routes, sections, and event tables.

Format Sheet Explanation - Linear Event Table

Linear Event Table:	Table Name:

Event Table Outline

Begin	Defined	Item

Column	Item Name	Definition

1	<event key item>	User defined

7	FROM	4,12,F,3

11	TO	4,12,F,3

Data Classification - RAT

In a linear event table (EVT), there are three items always present. The event key item is user defined. They are:

<event key item>	(relates event table to RAT)                                                    User defined

(The event key items for WAHYD are defined as 13,13,C)

From	(start measure in terms of index on existing route)	4,12,F,3

To	(end measure in terms of index on existing route)	4,12,F,3

Please see the ARC/INFO User's Guide, “Dynamic Segmentation,” for an explanation of routes, sections, and event tables.

Format Sheet Explanation - Point Relate Table

Point Event Table:	Table Name:

Event Table Outline

Begin	Defined	Item

Column	Item Name	Definition

1	<relate key item>	User defined

7	Location	4,12,F,3

Data Classification - REL

In a point relate table (REL), there are at least two items always present. The relate key item is user defined. They are:

<relate key item>	 (relates table to PAT)  	User defined

(The relate key items for WAHYD points are defined as 13,13,C)

Please see the ARC/INFO User's Guide, “Dynamic Segmentation,” for an explanation of routes, sections, and event tables.