Answers

Sampling Grain (Pelican)

- A leather pouch, approximately 7 inches deep and 18 inches long with a band of iron inserted along the edge to hold the pouch open.

- To sample a free-falling stream of grain.

- The type of carrier and size of the grain stream.

- A cut.

- Once each 500 bushels.

6.	Hopper car - 2 cuts per compartment; boxcar - 4 cuts; truck - 2 cuts; and barge/ship - 1 cut per 500 bushels.

- Step 1 - Assure that the loading spout is positioned so that the pelican may easily

be swung through the entire falling stream.

Step 2 - Station yourself next to the spout. (Be sure to check your footing.)

Step 3 - Hold the pelican next to the falling stream.

Step 4 - Grasp the pelican firmly and swing it completely through the stream in

one continuous motion.

Step 5 - Pour the contents into a sieve and check for unusual conditions, such as

odor, infestation, or non-uniformity.

Step 6 - If no unusual conditions are found, pour the grain into the sample

container.

Step 7 - If unusual conditions are found, place the contents in a separate sample

container, immediately take another cut and notify the supervisor or elevator

personnel.

8.	--Never tie the line to yourself or any other person!

--Always coil the retrieving line and place it so that you will not become entangled in the

coil!

9.	In a manner to avoid distorting the leather pouch.

10.	The nature of the discrepancy, quantity of grain represented, the grain's location in the carrier, and the person notified.

11.	An 8/64-inch round-hole sieve.