# Overview of Accelerator Physics Integration

## Talk outline

- Beam physics integration: Aims and Objectives

- Optics

- Beam physics and instrumentation

- Basic accelerator physics problems

## 1. Beam physics integration: Aims and Objectives

- Three major objectives:

  - (1) Building the model, (2) Machine studies and (3) General beam physics coordination

- Physics model of the entire complex

  - Optics

    - Software for optics design, optics meas. and data analysis

    - Repository of optics files

      - Set of rules and requirements to the files

  - Basic accelerator physics problems

    - The work is mainly performed in system departments

    - Certain coordination and help are required

    - Avoiding the duplication of efforts

  - Instrumentation

    - Instrumentation problems which require deep insight into physics of the device operation

## Aims and Objectives (continue)

- Machine Studies

  - Develop and prioritize study plans

  - Monitor the study proposals and write-ups of System departments

  - Enforce an effective use of study time

- Coordination

  - Department to department, and Tevatron to CDF and D0

  - Accelerator physics task forces

  - Prioritization of the accelerator physics issues for the accelerator complex

  - Weekly meetings (together with Jean Slaughter)

    - Run II accelerator physics

    - Beam physics in instrumentation

## 2. Optics

- Optics tools and software

  - Presently, a number of optics codes are used. Each of them has its own drawbacks.

  - We are building new optics code which should address our present and future needs

    - Main features

      - Integrated GUI

      - MAD-8 extension for lattice description

      - Runable in Linux and Windows

    - We have all the peaces. Need to glue them together

      - Schedule

        - First public use - this summer.

        - Total duration of active phase - < 2 years

- Optics files repository

  - Will address long-standing problem of saving and exchange of optics info/files. It is in line with effort to improve magnet and survey databases

- Optics measurements

  - Differential optics measurements

    - Present measurements are optimized to minimize study time. It fits well for transfer line measurements.

      - Data taking is fully atomized

      - Analysis half-manual requires significant time

        - ~2 hours for 8 GeV Accumulator-to-MI pbar transport

        - ~2 days for Tevatron but better accuracy is required

    - Analysis can be improved if data is sufficiently redundant

      - In collaboration with ANL we build new software

      - Data acquisition is under testing

      - Computational engine tests with real machine data are expected within month

      - First, the project is aimed for Tevatron and Debuncher where “the optics perfection” is the must. Other machines will follow later.

- Optics measurements (continue)

  - Turn-by turn

    - Greatest advantage that it allows one to perform measurements much faster

      - Significant advantage in the case when study time is limited

    - Present

      - Used at limited number of machines which have reliable measurements: MI & Recycler

      - Coupling and signal decoherence due to chromaticity are ignored

    - Solving Tevatron problems requires expansion of the scope

      - Coupling

      - Non-linearities

      - Effects of signal decoherence due to chromaticity/tune spread need to be alleviated

- Optics status/priorities

  - Tevatron

    - Low beta optics and helix need to be corrected

    - Measurements of Tevatron nonlinearities is highly desirable

  - Electron cooling

    - The beam is recirculateing but better understanding of machine optics is required

    - Optics redesign for MI-30 is under way

      - Means of optics correction need to be addressed

  - Debuncher and AP-2 line

    - Detailed knowledge of optics and orbits is required to maximize the machine admittance

    - Chromatic correction for AP2 line

  - Optics correction in the booster and the linac-booster line are under study

## 3.Beam physics and instrumentation

- Many instrumentation problems require deep insight into underlying physics

- We have a weekly meeting to facilitate an interaction of the instrumentation department with physicists

  - Problems to be addressed for the entire accelerator complex

    - Transverse and longitudinal emittance measurements

    - Tune measurements

    - Intensities and efficiencies

## Beam physics and instrumentation (continue)

- A few problems where the help/coordination has been highly valuable

  - Tevatron BPM project

    - Suppression of head-tail motion effects on turn-by-turn operation

  - BLT measurements

    - Algorithms for signal decomposition and many more

  - Longitudinal emittance measurements through entire complex

    - Obtaining quantitative emittance information for the beam in strongly non-linear longitudinal potential

  - Sync-light operation

    - Radiation from the magnet body

  - Bunch-by-bunch tune measurements in Tevatron

    - Significant efforts are required to reach desirable accuracy

## 4. Basic accelerator physics problems

- Recycler

  - Analysis of pbar deceleration due to collisions with residual gas atoms was helpful in building strategy for vacuum improvements

  - Careful analysis of Recycler operation with stochastic cooling was performed

    - It was found that putting Recycler into operation with stochastic cooling only can yield only modest improvements for stacking.

      - Experimental studies carried out now will yield more quantitative answer.

      - Updating the collider scenario with stochastic cooling alone will follow

    - Achieving successful operation of electron cooling has one of the highest priorities for the Run II success

  - Obtaining required small longitudinal emittance with electron cooling is based on reduced IBS in the case of equal longitudinal and transverse temperatures

    - Experimental studies of mechanisms responsible for the beam heating is under way in Recycler

- Recycler (continue)

  - There is considerable progress in measurements of long. emittance in barrier buckets

  - Transverse instabilities

    - Broad-band transverse damper: setting requirements and design

- Electron cooling

  - Recently we found out that single IBS (Touschek effect) in the electron beam leads to particle loss from recirculation

  - Optics has been redesigned to alleviate it.

    - Calculations yield lass reduction by almost factor ~6

    - Further optics improvements are under way.

  - Procedures and software for optics correction need to be worked out

  - Absolute energy calibration for Recycler and Electron Cooler needs further work

- Antiproton source

  - Optics

    - Optics design

      - Suppression of chromatic effects in AP2 line

      - Optics correction for AP2 - P1 8 GeV and 120 GeV to the target to accommodate quad tilts in P1 line

    - Optics measurements and optics matching

      - Debuncher

      - D-to-A line

        - Has not been measured with present settings. Both empirical tune-up with reverse protons and dif. orbit data needs to be acuired

      - ·	Accumulator

        - Chromaticity in Accumulator (operationally has not been an issue, but does have the wrong sign at the core for stability in the vertical plane.  Is there a fix?)

- Antiproton source (continue)

  - Fast pbar transfers

    - Power supply regulation for AP1 (running AP1 at 8 GeV off of 120 GeV supplies with ramp cards)

    - Pbar injection damper in MI:  specs on kick and voltage required to minimize emittance growth

  - 8 GeV energy definition

    - Power supply settings for AP2, Debuncher, D-to-A, Accumulator, AP3, AP1, P2, P1 with redefined energy (from Recycler)

  - Quad BPM in Accumulator

  - Stochastic cooling

    - Understanding of limitations of the stack-tail system and recommendation for improvements

- Booster

  - Optics

    - Understand and improve the 400 MeV beam transfer line

    - Understand and improve booster lattice

  - Optimize RF capture and early acceleration ramps

  - Commissioning the collimation system

  - Orbit control with ramped correctors

  - Dampers

  - Transition crossing

- Main injector

  - Slip stacking

    - Beam loading compensation and instabilities

      - Feedforward

      - Longitudinal damper

  - Transition crossing

  - Single bunch instabilities

  - Slow extraction optimization

- Tevatron

  - Tevatron optics

    - Linear optics correction

      - Done at Injection and Flat top

      - Low Beta optics and helix are in a process of correction

    - Building non-linear Tevatron model

      - Presently there is large difference between model predictions and observations

    - Study of sources of orbit drifts

      - Sources of data: BPMs, water gauges

    - Feeddown correction of coupling and dif. chromaticities

      - Additional octupole and sextupole circuits were installed at the 2003 shutdown

    - Further optimization of helices and increase of separation

- Tevatron (continue)

  - Model for the luminosity evolution

    - Measurements of bunch-by-bunch tune shifts and chromaticities and comparison with computations

    - Simulation of beam-beam effects in the presence of diffusion

    - Experimental study of longitudinal and transverse dynamics driven by IBS and beam-beam effects

  - Instabilities

    - Transverse instabilities

      - ( impedance reduced, beam is stable for pos. chromaticities

      - Introducing tune shift by octupoles should improve stability

    - Longitudinal instabilities

      - Longitudinal impedance measurements

      - What is the shortest bunch which Tevatron can support

## Conclusions

- We are making steady progress with luminosity growth and with understanding of Tevatron complex operation

- There is still large potential for further growth of both peak and integrated luminosities

- The progress has been and will be supported by both improvements in operations and better understanding of underlying physics

- Good coordination of beam physics efforts is essential for the Run II success

# Text boxes

DoE Review

Feb. 24-25, 2005

Fermilab

###### Valeri Lebedev

FNAL