|  | A. NUMBER | B. PHASE | C. DATE |
| --- | --- | --- | --- |
| FLIGHT PAYLOAD STANDARDIZED HAZARD CONTROL REPORT | STD- | AMS-02-F02 | Phase II | May 25, 2007 |
| D. PAYLOAD, DTO, DSO or RME (Include Part Number(s), if applicable) | HAZARD TITLE | E. VEHICLE |
| Alpha Magnetic Spectrometer (AMS-02) Orbiter Interior Elements–See Attached List | STANDARD HAZARDS |  |
| F. DESCRIPTION OF HAZARD: | G. HAZARD CONTROLS: (complies with) | H. APP. | I. VERIFICATION METHOD, REFERENCE, AND STATUS: |
| Structural Failure (payloads must comply with the listed requirements for all phases of flight) Note: Locker and Soft Stowage items only. | Designed to meet the standard modular locker stowage requirements of NSTS 21000-IDD-MDK or equivalent IDD . |  | 1.1.1. SVM: Review of Installation drawings for Middeck Stowage. 1.1.2. SVM: Weight/CG Analysis for Stowage for Middeck Stowage 1.1.1 STATUS: Open 1.1.2 STATUS: Open |
| Structural Failure of Sealed Containers Note 1: Only sealed containers made of conventional metal (metal alloy) can use the 1230 form. Sealed containers made of unconventional metals or non-metallic materials shall be documented on Unique Hazard Reports. Note 2: The 1230 form is not applicable for “sealed container”(s) employed in levels of containment control of hazardous fluid. | Sealed containers must meet the criteria of NASA-STD-5003, Para. 4.2.2.4.2.3a, contain a substance which is not a hazard if released, be made of conventional metals (e.g. Al, inconel, monel, steel or titanium), contain less than 14,240 foot-pounds (19,130 Joules) of stored energy due to pressure, and have a maximum delta pressure of 1.5 atm. |  | N/A. – No Sealed Containers used as structure (No Sealed Containers for any purpose) |
| APPROVAL | PAYLOAD ORGANIZATION | SSP/ISS |
| PHASE I |  |  |
| PHASE II |  |  |
| PHASE III |  |  |
| Structural Failure of Vented Containers | For intentionally vented containers, vents are sized to maintain a 1.4 factor of safety for Shuttle or a 1.5 factor of safety for Station with respect to pressure loads. Meets all of the applicable pressure rates defined for one or more of the following. Shuttle payload bay – ICD 2-19001, Para. 10.6.1 b) Station environment – SSP 52005, paragraph 4.3 or equivalent payload specific ICD . c) Station PFE discharge – SSP 57000, Para. 3.1.1.4K, or equivalent payload specific ICD . d) Shuttle Middeck – NSTS 21000-IDD-MDK, Section 6.1. |  | N/A. – No confined volumes in hardware design. |
| Sharp Edges, Corners, and/or Protrusions. | Meets the intent of one or more of the following: NASA-STD-3000 / SSP 50005 SLP 2104 NSTS 07700 Vol. XIV App. 7 (EVA hardware) NSTS 07700 Vol. XIV App. 9 (IVA hardware) / SSP 57000 e) SSP 41163, Para. 3.3.6.12.3 (EVA), Para. 3.3.6.12.4 (IVA). |  | 4.a.1 SVM: Inspection of flight hardware for sharp edges, corners and protrusions. 4.a.1 STATUS: Open |
| 5. Shatterable Material Release | All materials are contained. Optical glass (i.e. lenses, filters, etc.) components of crew cabin experiment hardware that are non-stressed (no delta pressure) and have passed both a vibration test at flight levels and a post-test visual inspection. Payload bay hardware shatterable material components that weigh less than 0.25 lb and are non-stressed (no delta pressure) or non-structural. |  | N/A. No Identified Shatterable Materials |
| 6. Flammable Materials | A-rated materials selected from MAPTIS, or Flammability assessment per NSTS 22648 |  | 6.b.1 SVM: Review of design for appropriate use of non-flammable materials. 6.b.2 SVM: Review and approval of flammability assessment by JSC/ES4. 6.b.1 STATUS: Open 6.b.2 STATUS: Open |
| 7. Materials Offgassing | Offgassing tests of assembled article per NASA-STD-6001 (previously published as NHB 8060.1C). |  | Reference Hazard Report AMS-02-F02 |
| 8. Nonionizing Radiation 8.1 Non-transmitters | Meets all that apply: Pass ICD-2-19001, 10.7.3.2.2 / SSP 30238 EMI compatibility testing, or NSTS/USA approved analysis ICD Section 20, or ISS/EMEP approved TIA Meets SSP 41163, Para. 3.3.6.6 and SSP 50094, Para. 3.4. |  | 8.1.a.1 SVM: EMI testing results reviewed and approved by JSC/EV4 8.1.a.1 STATUS: Open |
| Lasers NOTE: Lasers operating at class levels 3b and 4, meeting ANSI Z136.1, shall be documented on Unique Hazard Reports. | Meet ANSI Z136.1-2000 for class 1, 2, or 3a Lasers (as measured at the source). |  | N/A. Internal elements of AMS-02 do not generate coherent light. |
| 9.1 Alkaline cells and batteries made of alkaline cells, connected in series or in parallel, up to 12 V and with up to 60 Watt-hours capacity, no potential charging source and cells are not in a gas-tight compartment. | Cells and batteries pass acceptance tests that include loaded and open circuit voltage measurements, visual examination, and leakage check under vacuum (e.g. 6 hours at 0.1 psia). |  | N/A. AMS-02 Interior elements utilize no batteries. Submission of EP-Form-03(including the form’s approved reference number) for EP5 approval Information to be included on the EP5 reviewed/approved Form-03: application and protective circuit schematics |
| 9.2 Primary button cells such as Li-(CF)x, Li-iodine, LiV2O5, LiMnO2, Ag-Zn and rechargeable button cells such as LiV2O5, Li-ion, Ni-Cd, Ni-MH, Ag-Zn cells or batteries, which have a capacity of 300 mAh or less and no more than 3 cells per common circuit, and cells are not in a gas-tight compartment. | Cells and batteries pass acceptance tests that include loaded and open circuit voltage measurements, visual examination, and leakage check under vacuum (e.g. 6 hours at 0.1 psia). Note: Above acceptance testing for button cells in Section 9.2 which are soldered to a circuit board in commercial equipment (not applicable to those button cells in a spring-loaded clip) is limited to a functional check of the equipment utilizing the subject battery. |  | N/A. AMS-02 Interior elements utilize no batteries. Submission of EP-Form-03(including the form’s approved reference number) for EP5 approval Information to be included on the EP5 reviewed/approved Form-03:: application and protective circuitry. |
| 9.3 COTS NiMH, NiCd and Ag/Zn cells and batteries for IVA use up to 20 V and 60 Wh | Cells and batteries purchased in one lot; pass acceptance tests that include loaded and open circuit voltage measurements, visual examination, leakage check under vacuum (e.g 6 hours at 0.1psia) and vibration to workmanship levels with functional checks which include charge/discharge cycles for rechargeable batteries. |  | N/A. AMS-02 Interior elements utilize no batteries. Submission of EP5 Form-03(including the form’s approved reference number) for approval Information to be included on the EP5 reviewed/approved Form-03: manufacturer’s specification, battery protective features and charger schematics |
| 9.4 COTS Li-ion batteries up to 10 V and 60 Wh for IVA use | Batteries and charger shall be from a single lot; shall show one-fault tolerance at battery level and shall pass acceptance tests that include loaded and open circuit voltage measurements, visual examination, leakage check under vacuum (e.g 6 hours at 0.1psia) and vibration to environment or double the workmanship level, whichever is higher; and functional checks which include charge/discharge cycles. |  | N/A. AMS-02 Interior elements utilize no batteries. Submission of EP-Form-03(including the form’s approved reference number) for EP5 approval. Information to be included on the EP5 reviewed/approved Form-03: battery protective features and charger features Note: For hardware using batteries, and/or chargers additional levels of control shall be provided by the hardware . |
| 10. Touch Temperature | Within IVA touch temperature range of –18 Degrees C. (0 Degrees F.) and 49 Degrees C. (120 Degrees F.) and satisfies the intentional contact constraints of letter MA2-95-048 (if applicable). Meets EVA touch temperature criteria of NSTS 07700 Vol. XIV App. 7. |  | 10.a.1 SVM: Review of design to confirm power consuming elements inaccessible to the crew. 10.a.2 SVM: Analysis to confirm that interface card will not induce excessive thermal load on PGSC/NGLS. 10.a.1 STATUS: Open 10.a.2 STATUS: Open |
| 11. Electrical Power Distribution | Shuttle-powered payloads – Meets all circuit protection requirements of Letter TA-92-038. Station-powered payloads – Meets station interface circuit protection requirements of SSP 57000 and payload circuit protection requirements of Letter TA-92-038. |  | 11.a.1 SVM: Review of Design 11.a.1 STATUS: Open Note: The USB422 makes its interface is with the PGSC/NGLS and is not directly interfaced with the Shuttle power systems. |
| 12. Ignition of Flammable Atmospheres in Payload Bay | All ignition sources in the Payload bay, for launch and landing, are controlled as required in Letter NS2/81-MO82, and MLI grounded per ICD 2-19001. |  | N/A. Hardware addressed in this hazard report is within the crew habitable environment and not exposed to a flammable atmosphere in the Shuttle Payload Bay |
| 13. Rotating Equipment | Rotating equipment meets criteria of NASA-STD-5003 for obvious containment. |  | N/A. AMS-02 Internal hardware does not utilize any rotating equipment. |
| 14. Mating/demating powered connectors | Meets the low power criteria of letter MA2-99-170 or, b) Meets the paragraph 1 criteria of letter MA2-99-170 (e.g., IVA and open circuit voltage no greater than 32 volts). |  | 14.a.1 SVM: Review of Design. T 14.a.1 STATUS: Open |
| 15. Contingency Return and Rapid Safing | Shuttle Environment: If middeck payload – can be stowed within 50 min. (see paragraph 3 of letter MA2-96-190). b) If SPACEHAB transfer item – can establish a safe for return configuration within 3 min. (see paragraph 5 of letter MA2-96-190). Station Environment: c) Payload design does not impede emergency IVA egress to the remaining adjacent pressurized volumes. |  | 15a.1 SVM: Rapid Safing Assessment to establish that the PGSC/NGLS and data cables can be stowed within 50 minutes. 15.a.1 STATUS: Open |
| 16. Release of Mercury from bulbs into crew habitable environment. | a) Mercury vapor bulbs contain less than 30 mg of Mercury per bulb, and No more than one bulb could break due to a single failure. |  | N/A. AMS-02 internal hardware elements do not utilize mercury containing bulbs. |

Alpha Magnetic Spectrometer –02 (AMS-02) Orbiter Interior Hardware Elements:

- DDRS-02 Elements

  - Digi USB422 Interface (interface for PGSC/NGLS USB connectivity)

  - USB422 to PDIP Cables  P/N SED 3939136111

  - COTS USB A-B cable, wrapped in Teflon tape (connects USB422 to PGSC/NGLS)

NOTE:

- Payload General Support Equipment (PGSC)/ Next Generation Laptop System (NGLS), not considered in STD-AMS-02-02, GFE is being used in accordance with its GFE certification.

- Spare Hard Disk (GFE) for PGSC/NGLS, not considered in STD-AMS-02-02, GFE is being used in accordance with its GFE certification.

- Other Hardware

  - Cable SED 39136112-301 – PDIP J103 to J105 Patch Cable – Patches RS422 to T0 umbilical for GSE monitoring and control of the AMS-02 prior to launch.

| About USB422 The USB422 interface provides inline conversion of RS422 synchronous serial signals to a USB 2.0 interface. The unit is powered by the USB 5.0 volt bus provided power and draws less the 0.5 amp. USB422 is a single PCB based on a Cypress FX2 chip and a gate array. This card will be hand conformal coated with Dow Corning 3140 or equivalent. USB422 is housed in a rugged aluminum enclosure with Twinax style connections on one end and a commercial USB cable Teflon wrapped on the other. The USB cable plugs into the NGLS USB connection and is strain relieved by a Velcro strap to the power connection cable (TBC). | Picture is representation of USB422 and Non-Flight cables |
| --- | --- |

DDRS-02 – Cable RS422 to PDIP (P/N SED 3939136111)

DDRS-02 Cable – RS422 to PDIP Schematic

PDIP J103 to J105 Patch Cable (SED 39136112-301) NOTE: Dimensions are not accurately reported in this preliminary drawing, final length should be approximately 12 inches.

PDIP J103 to J105 Patch Cable Schematic