| Loads: Use the WECC 2004 L&R forecast for 2008, with the exception that the load forecast developed for RMATS is used for the Rocky Mountain states. (The RMATS load forecast was based on WECC’s 2003 L&R, with updates and corrections by RMATS participants.) Translate the WECC load forecast (22 bubbles) to the SGG-WI topology (33 bubbles). SSG-Wi topology includes two NW bubbles, two PG&E bubbles, and the Rocky Mountain bubbles per RMATS except that Montana bubbles are consolidated Adopt 2002 as the sample year to determine hourly load shapes for each bubble in the SSG-Wi topology. Each bubble’s shape will be applied to all busses in that bubble. Exceptions: use the hourly load shapes developed in RMATS for the Rocky Mountain bubbles. Use load shapes produced by GENESYS/HELMS using 2002 temperatures for the NW bubbles | Done. Large California pumps (non agricultural) were disaggregated from loads and modeled as pumps. Done. Note: There is an inconsistency between the load shapes in RMATS and the 2002 actual load shapes for the Rocky Mountain states, and an inconsistency between the load shapes developed in HELMS and 2002 actual load shapes for the NW states Irena developed new load shapes that reflects the operation of the large pumps. Currently, we’re working with ABB to make sure all adjustments to incorporating the pumps are done correctly. No adjustment to load forecast for transmission losses | Updated loads to be submitted and used for PacifiCorp – East (consistent with recently filed IRP). R. Wilson continues to have problems with the RMATS PACE loads for year 2008. Becky has no problem with the load growth factors used in RMATS, applied to 2008 to generate 2013; consensus was reached on the Load Forecasting Workgroup call on Monday to use the same factors for generating the 2015 forecast. Re-examine whether 2002 actual load shapes should be used across the board To adjust for losses, run GridView with loss calculator on, but make no change to load forecast. Observe GV results, then decide whether peak demand and energy in load forecast should be adjusted upward based on GV loss calculations . |
| --- | --- | --- |
| Power flow case(s): Use the WECC 2004 summer –heavy power flow case (HS2A PF) (default for all months) Identify a winter power flow case, and test its impact. | Employ summer power flow case only. Case is rerun to account for updates to transmission representation in CA, CO, NW, AZ, ID | SPGs complete their review of transmission representation for remaining geographic areas Pending is the review of PACE transmission Identify a winter power flow case (WECC) Test the impact of adding a winter case for the winter time period Decide to include or not include the winter case in the base case study. The winter case would used to distribute loads to busses for the winter period (summer case is used for the full year in preliminary study). To generate a winter case, consideration should be given to the customization applied to the summer case; of issue is creating a process to automate the task.--+-- |
| Existing resources: Map all units to busses | Of the ~2600 units in the West, the number unmapped has been driven down to almost zero. One exclusion: units < 10 MW. These units are associated with busses and they are assumed in this study to be gas-fired. For the units that are mapped, a number of assumptions have been made - with no review by SPGs or states Units with negative capacities were grouped with units<10 MW and modeled as thermal; given high gas prices. We’re in the process of segregating original units with negative capacities to reinstate them as pumps. | Mapping should be reviewed by SPGs and states |
| Existing resources: Merge and reconcile the units identified by the states with the units identified by WECC in the power flow case. Ensure state review/concurrence | Resources in this run are the resources in the WECC power flow case. The units identified by states were reconciled with those identified in the WECC case. No major discrepancies were found; the states’ input was particularly helpful in identifying and locating generators. Default to WECC power flow depiction of resource attributes if discrepancy is less than 10 MW. | Obtain review by states and company experts before finalizing |
| Incremental resources | Resources in this run are the resources in the WECC power flow case. No additional resources and no review by SPGs or states. No target planning margin was applied, nor were RPSs | Determine load/resource balances and RPS conformance based on preliminary analyses. If any state has a resource adequacy standard, ensure there are sufficient resources to meet that standard. Coordinate with states and SPGs to identify and specify a complete list of new resources. Include additional wind resources per NREL’s recommendation, as appropriate. |
| Thermal unit capacity ratings: Net of station service and/or on-site direct use of electricity. Thermal rating should also be adjusted for summer derates | Unit ratings extracted from summer power flow case. The case is net of station service/direct use, but it is not net of summer derates Summer derates reside in the WECC L&R report; WECC maps the L&R report to EIA but not to Powerflow. | Unit capacity ratings need to be adjusted for summer derates. Power flow case to be re-run, with capacity ratings uploaded to GV |

| Thermal unit commitment: Create categories of units (like fuel types, technologies, elevations, etc.). Develop generic assumptions for heat rate curves, planned outages, ramp rates, min/max up and down times, start-up costs, etc. Generic assumptions based on actual data available from public sources (EIA/EPA databases) | No thermal unit commitment data | Create generic unit commitment assumptions based on historical data that is publicly available, i.e., based on EIA/EPA databases. Work with DOE, NWPCC and other experts to develop most reasonable unit commitment assumptions. Obtain review by states and subject matter experts before using this data. |
| --- | --- | --- |
| Fuel prices: Gas: $5/MMBtu in 2004$; sensitivities: $6 and $4 Coal: Develop forecast that reflects publicly available sources | $5/MMBtu only – no gas price sensitivities Use the NWPCC transportation costs. EIA forecast of coal prices based on historical trends. Also use EIA forecast of 2-tier transportation costs depending on demand location and coal source location | Include $6 and $4 sensitivities. Review, refine transportation cost assumptions. Circulate the NWPCC transportation costs and assumptions to SPGs for buy in. Review and approve of coal price forecast |
| Wind generation shapes: Adopt wind shapes prepared by NREL | Shapes received and implemented for existing wind units | Add shapes for new wind additions |
| Hydro generation: GENESYS will not be used to model hydro generation in the base case study because it cannot disaggregate hourly hydro generation to individual hydro plants. ABB is working to include this algorithm in the GridView model for future use. Instead: NW: recent historical hydro generation that is fairly reflective of latest Biological Opinion. Three historical years chosen: M (2002), L (2003), H (2000) Central Valley Project: modified hourly historical data from WAPA; however, may need to go to same approach as NW because generation for CVP system is not available for individual plants Other California: CEC monthly hydro data, to which GridView’s peak shaving algorithm is applied; at a minimum, PG&E, SCE and municipal hydro plants that are operated in essentially run-of-the-river mode need to be identified and not included in peak shaving Colorado: Bureau of Reclamation--Upper and Lower Colorado Regions provided monthly forecasted data, which reflects recent severe drought in terms of updated hydrology and operational algorithms, to which GV peak shaving algorithm is applied. Obtain non-Federal Hydro data. Canada: Data request into BC Hydro Arizona/Desert SW: Obtain non-Federal Hydro Data from Salt River Project and other projects. | Initial study is for average hydro conditions only: NW: Federal and non-Federal historical hourly net generation has been obtained for years 1999, 2002 and 2003. NW loads associated with average hydro year temperatures are included in load forecast CVP: WAPA historical hourly data modified to reflect changed operational paradigm. Expiration of WAPA-PG&E Interconnection Agreement is included, but needs to be disaggregated to individual plants Other California: CEC monthly energy and capacity. Use GV peak shaving to generate hourly generation. Still need to either pursue historical hourly hydro generation from PG&E, SCE and Munis or, at a minimum, identify base-loaded generation. Colorado: Received monthly hydro generation from USBR Canada: Currently using 2003 assumptions as default; still trying to obtain better data from BC Hydro | Need to obtain either monthly or hourly hydro generation to fill gaps. NW: Obtain PacifiCorp actual data for the 3 sample years PAC’s hydro generators are being mapped to busses; should be done today. CA: Continue quality control effort and identify base-loaded hydro, or obtain historical hourly hydro generation; need credible operation for Helms Pump-Storage Irena is working on aggregating plants by river system; generating aggregate hourly data files covering non-public hydro in California. BC: Continue pursuing hydro data in most disaggregated form that is not market sensitive AZ, CO and other SW States: fill in hydro data gaps FOR ALL HYDRO: need to understand whether to include just net generation with any pumping load subtracted out, or whether pumping load is contained in loads It has been confirmed that WECC’s loads incorporates pumps. As been stated earlier, Irina is in the process of disaggregating the Large CA pumps to model as pumps. Review accuracy of data and treatment in model Run low and high hydro cases for the NW and other areas, where appropriate Need to determine “high” and “Low” hydro. |
| Transmission representation | Detailed update for CA. Updates also submitted for, AZ, NW, CO, ID Power flow case rerun to capture these changes | SPGs complete their reviews and updates to transmission representation for remaining geographic areas. Rerun summer power flow case |
| Transmission path ratings and nomograms: Derates to recognize historical OTC limitations will be applied to specified paths. Nomograms to be included are listed in Notes for the 3/29 TSG. Derates to reflect historical operational scheduling limitations will be not applied in the 2008 study. | Derates to recognize historical OTC limitations to be applied per Dean’s analysis. Nomograms consistent with 3/29 TSG decisions. | TSG review and approve treatment TSG to submit Nomograms |
| Wheeling rates | No wheeling rates included | Transmission sub-group to identify the interfaces to represent with wheeling rates and the wheeling rates that should be used |