PART 9.	EO-1 FIRSTS

When considering the large number of accomplishments resulting from the EO-1 mission, a sizable number can be classed as “firsts”.  Listed below are those “firsts” that are considered most significant.

1.	Hyperion Science Validation

First to:

- Acquire spaceborne hyperspectral observations of the Earth with Landsat spatial resolution (30 m) and AVIRIS spectral resolution (10 nm) over the entire Landsat reflective range.

- Accurately map and characterize temperature distributions of active lava flows and forest fire “hot spots” from space.

- Track re-growth in partially logged Amazon forests and reliably estimate Amazon forest drought stress.

- Demonstrate that spaceborne hyperspectral sensors can identify and map vegetation species (including invasive species), canopy nitrogen concentrations, and minerals.

- Map several fire fuel classes from space at very high accuracies, including senesced grass, soil, and chamise.

- Separate total carbon into living biomass, dead biomass, and soil background with high accuracy.

2.	ALI SCIENCE VALIDATION

Relative to Landsat, first to:

- Demonstrate sequentially-sampled push-broom detector array technology.

- Provide superior SNR and 12-bit A/D to capture the full dynamic range of Earth imagery.

- Provide Pan-band-enhanced imagery of exceptional quality.

- Provide additional SWIR band 5p (1.200-1.300 µm) to supply new information for identifying forest and crop types.

- Provide additional VNIR blue band 1p (0.433-0.453 µm) to supply new information for coastal studies and aerosol estimation.

- Provide improved SNR to track subtle changes in the velocity of ice sheet flows.

3.	SPACECRAFT BUS

First to:

- Use high data rate electronically steerable antenna at X-band frequency.

2.	Use NASA very high data rate solid-state recorder (> 1 Gbps).

- Use Reed-Solomon error detection and correction chip that operates at 1 Gbps.

- Validate non-linear autonomous, long term formation flying and use of software that incorporates fuzzy logic.

- Use pulsed plasma thruster as precision attitude control actuator.

- Use shape memory alloy for system hinge and deployment mechanism.

- Use panel with Carbon-Carbon as facesheet material where panel is utilized both as a radiator and as part of spacecraft primary structure.

4.	OPERATIONS

First to:

1.	Reduce cost of imagery 10-fold in the first 18 months of operation.

2.	Generate a comprehensive space-borne hyperspectral imagery archive.

- Implement an on-board cloud detection algorithm.

4.	Demonstrate use of onboard autonomy and autonomous ground coordination to enable sensor web capabilities.

5.	Experiment with adaptive algorithms coupled to a low cost ground-based scanning antenna array to dramatically lower the cost of communicating with low earth orbiting satellites.

6.	Use onboard feature detection to autonomously modify onboard imagery tasking decisions.