PIXEL DETECTOR PROJECT

Test Beam 2002 Readout Electronics Plan

Document # ESE-PIX-20011203

Rev 1.6

September 10, 2003

Bradley Hall, Guilherme Cardoso, David Christian, Gabriele Chiodini, Lorenzo Uplegger, Sergio Zimmermann

Revision History

| Rev | Name | Date | Comments |
| --- | --- | --- | --- |
| 1.0 | B. Hall | 12/28/01 | Draft |
| 1.1 | B. Hall | 02/12/02 | Original release |
| 1.2 | B. Hall | 04/30/02 | Updated PMC/PTA Interface Updated waveforms in Fig 7. Updated Registers |
| 1.3 | B. Hall | 06/07/02 | Updated Registers and Data Formats |
| 1.4 | B. Hall | 08/05/02 | Updated FPIX Data Formats, waveforms to PTA memory, and register definitions. |
| 1.5 | B. Hall | 11/04/02 | Updated register definitions, added startup sequence section. |
| 1.6 | B. Hall | 9/10/03 | Updated register definitions to include calibration features. |

Table of Contents

1	Introduction	6

2	Assumptions	6

3	Electronics Overview	6

3.1	Scintillation Counters & Coincidence	7

3.2	PTA/PMC	7

3.3	FPIX0 Planes	8

3.4	FPIX1 Planes	8

3.5	PreFPIX2 Planes	8

3.6	Module	8

3.7	PCI Bus	9

4	Clock Distribution & BCO Count Alignment	9

4.1	Master PMC	9

4.2	BCO Clock Distribution	9

4.3	BCO Count Alignment & Reset	10

5	PMC FPGA Firmware	11

5.1	FPIX Interface Block	11

5.2	Extended BCO Counter	11

5.3	Fine Resolution BCO Counter	11

5.4	Triggers	11

5.5	Receive Window Counter	11

5.6	Data Formatter	13

5.6.1	Data Blocks	13

5.6.2	Triggered Header Word Format	14

5.6.3	Untriggered Header Word Format	14

5.6.4	FPIX0 Data Format	14

5.6.5	FPIX1 Data Format	14

5.6.6	preFPIX2tb Data Format	14

5.6.7	preFPIX2i Data Format	14

5.6.8	FPIX2 Data Format	15

5.7	PTA Memory Interface	15

5.8	FPIX Configuration Path	15

5.9	Startup Sequence	15

5.10	Pulse Out	16

6	Registers	18

6.1	PMC Standard Registers	18

6.1.1	Firmware Type: Address 0x0000 (read only)	18

6.1.2	Firmware Revision: Address 0x0004 (read only)	18

6.2	PMC Test Beam ’02 Specific Registers	18

6.2.1	Control Register A:  Address 0x0008 (read/write)	19

6.2.2	Control Register B:  Address 0x000C (read/write)	19

6.2.3	Control Register C:  Address 0x0010 (read/write) – Not Implemented	20

6.2.4	Control Register D:  Address 0x0014 (read/write) – Not Implemented	20

6.2.5	Control Register E:  Address 0x0018 (read/write) – Pulse Out Control	21

6.2.6	Control Register F:  Address 0x001C (read/write) – Pulse Out Train Length	21

6.2.7	Control Register G:  Address 0x0020 (read/write) – Calibration Control	21

6.2.8	Plane A ID Register: Address 0x0030 (read/write)	22

6.2.9	Plane B ID Register: Address 0x0034 (read/write)	22

6.2.10	Receive Window Register: Address 0x0038 (read/write)	22

6.2.11	Max Data Register: Address 0x003C (read/write) – Not Implemented	22

6.3	FPIX0 Specific Registers	22

6.4	FPIX1 Specific Registers	23

6.4.1	FPIX1 Interface Plane A:  Address 0x0100 (read/write)	23

6.4.2	FPIX1 Interface Plane B:  Address 0x0104 (read/write)	23

6.5	preFPIX2tb Specific Registers	24

6.5.1	preFPIX2tb Interface Plane A:  Address 0x0100 (read/write)	24

6.5.2	preFPIX2tb Interface Plane B:  Address 0x0104 (read/write)	24

6.5.3	preFPIX2tb Interface Plane A:  Address 0x0108 (read only)	25

6.5.4	preFPIX2tb Interface Plane B:  Address 0x011C (read only)	25

6.6	preFPIX2i Specific Registers	26

6.6.1	preFPIX2i Interface Plane A:  Address 0x0100 (read/write)	26

6.6.2	preFPIX2i Interface Plane B:  Address 0x0104 (read/write)	26

6.6.3	preFPIX2i Interface Plane A:  Address 0x0108 (read only)	27

6.6.4	preFPIX2i Interface Plane B:  Address 0x011C (read only)	27

7	PTA/PMC Interface	28

8	FPIX0 Interface	32

9	FPIX1 Interface	32

10	PreFPIX2 Interface	33

11	References	33

Figures and Tables

Fig. 1.  Test beam electronics schematic.	7

Fig. 2.  PTA card (left) and PMC (right).	8

Fig. 3.  PMC FPGA block diagram.	10

Fig. 4. Waveforms with locally generated async accelerator clock.	12

Table 1.  Possible data words.	13

Fig. 5.  Triggered header word and four FPIX1 words.	13

Fig. 6.  Untriggered FPIX1 word.	13

Fig. 7.  Triggered header word.	14

Fig. 8.  Untriggered header word.	14

Fig. 9.  FPIX0 data word.	14

Fig. 10.  FPIX1 data word.	14

Fig 11.  preFPIX2tb data word.	14

Fig. 12.  preFPIX2i data word.	15

Fig. 13.  FPIX2 data word.	15

Fig. 14.  Waveforms for PMC to PTA memory interface.	15

Fig. 15.  Example Pulse Train of Length 4.	17

Table 2.  JN1 pin assignment PTA/PMC interface.	28

Table 3.  JN2 pin assignment PTA/PMC interface.	31

Fig. 16.  Pin assignment for FPIX0 interface.	32

Fig. 17.  Pin assignment for FPIX1 interface.	32

Fig. 18.  Pin assignment for FPIX2i and FPIX2tb interface.	33

# Introduction

This document describes the readout electronics implementation plan for the pixel detector telescope for the 2002 test beam at Fermilab.  The scope of this document includes the hardware from and including the PCI bus up to and including the pixel telescope planes and the planes under test.  Topics covered include descriptions of the hardware components, the interface between the Programmable Mezzanine Cards (PMCs) and the FPIX planes, the interface between the PMC and the PCI Test Adapter (PTA) cards, the formatting of the data words that will be sent to memory banks on the PTA cards, the timing signals for synchronizing multiple planes, and the triggering technique.

# Assumptions

This document assumes the following:

- Event rate no more than ~100kHz.

- Beam structure will provide beam for approximately one second followed by five seconds of no beam.

- DAQ software will be capable of reading out all data stored in PTA memory and issuing a reset within the beam structure period of approximately six seconds (one second of beam followed by five seconds of no beam).

# Electronics Overview

The test beam instrumentation will consist of an eight-plane telescope and up to four planes and/or a module under test (see Fig. 1).  Each telescope plane will consist of an FPIX1 chip bump bonded to a pixel sensor array and mounted on an inner board.  The planes under test will consist of an FPIX0 or preFPIX2 chip bump bonded to a sensor array and mounted on an inner board.  One scintillation counter upstream and one scintillation counter downstream will serve as a minimum coincidence trigger configuration.  A PCI based PTA card with a mated PMC card will serve to control and readout two planes.  This section describes each of the components shown in Fig. 1.

Fig. 1.  Test beam electronics schematic.

## Scintillation Counters & Coincidence

Two scintillation counters, one upstream and one downstream, will serve as the minimum trigger configuration.  Coincidence electronics located in the counting room distribute the coincidence signal to each of the PMCs.  The coincidence signal should be NIM level and connect to one of the four LEMO header inputs on the PMC.  How the PMC card uses this coincidence signal is described in section 5.

## PTA/PMC

The PTA (PCI Test Adapter)[1] and PMC (Programmable Mezzanine Card)[2] (see Fig. 2) are used to control and receive data from the telescope planes (FPIX1) and the planes under test (FPIX0 or preFPIX2).  Different PMC firmware will be developed for each type of plane.  Firmware in the PTA cards will be common across the entire system.  A single PTA/PMC can control up to two planes.  The PTA card has two banks of 1MByte memory for a total of 2MBytes.  Event data from the pixel planes is stored in the PTA card memory until it is read out from the PC via the PCI bus.  The PTA/PMC cards will be located in the counting room.

Fig. 2.  PTA card (left) and PMC (right).

## FPIX0 Planes

Up to four FPIX0 planes will be under test.  FPIX0 planes will consist of a single FPIX0 chip bump bonded to a sensor and mounted in the center of the inner board.  All signaling to/from the FPIX0 board will be LVDS.  The FPIX0 inner board will have LVDS transmitters/receivers for driving/receiving signals to/from the PMC boards 30m away in the counting room.  Details of the FPIX0 inner board can be found in reference [3].

## FPIX1 Planes

A total of eight FPIX1 planes will be used to construct the test beam telescope.  FPIX1 planes will consist of a single FPIX1 chip bump bonded to a sensor and mounted in the center of the inner board.  All signaling to/from the FPIX1 board will be LVDS.  The FPIX1 inner board will have LVDS transmitters/receivers for driving/receiving signals to/from the PMC boards 30m away in the counting room.  Details of the FPIX1 inner board can be found in reference [4].

## PreFPIX2 Planes

Up to four preFPIX2 planes will be under test.  PreFPIX2 planes will consist of a single preFPIX2i or preFPIX2b chip bump bonded to a sensor and mounted in the center of the inner board.  Jumpers on the preFPIX2 inner board will be used to accommodate either a preFPIX2i or preFPIX2b.  All signaling to/from the preFPIX2 board will be LVDS.  The preFPIX2 inner board will have LVDS transmitters/receivers for driving/receiving signals to/from the PMC boards 30m away in the counting room.  Details of the preFPIX2 inner board can be found in reference [5].

## Module

An FPIX module consisting of multiple FPIX chips possibly will be tested.  All signaling to/from the module will be LVDS. The FPIX module will have LVDS transmitters/receivers for driving/receiving signals to/from the PMC boards 30m away in the counting room.  If an FPIX module is used in the test beam, a maximum of three FPIX planes under test can be in the system.

## PCI Bus

The PTA cards plug into a SBS Technologies PCI expansion unit with 13 PCI slots.  A PTA/PMC plugs into a single PCI slot, but physically interferes with the adjacent slot.  This interference causes each PTA/PMC to occupy 2 PCI slots resulting in a maximum of 6 PTA/PMCs in a single PCI expansion unit.  With each PTA/PCI card capable of connecting to two planes, a single PCI expansion unit is capable of connecting 12 planes.

The PCI bus will be located in the counting room in close proximity to the PC.  Data cables of approximately 30m in length will send/receive signals to/from the hut and plug into the PMC.  Having the PCI bus in the counting room allows easy access for debugging.  If, however, the 30m cable length results in too many technical challenges the PCI bus can be placed in the hut allowing for much short cables, but poor access.

# Clock Distribution & BCO Count Alignment

It is important that each of the planes in the telescope and planes under test be synchronized and phase aligned with the same BCO clock and BCO count.  This section describes the BCO clock and BCO count alignment technique.

## Master PMC

One of the PMCs will be designated the Master PMC.  A PMC is set to a master by software setting a bit in its control register (see section 6).  The Master PMC is responsible for distributing the BCO clock and reset signal to all PMCs.  The master and slave PMCs will have the same firmware, however, the Master PMC will have the termination resistors at the Low Skew General and Low Skew Clock Distribute resources removed [2].  The only time the DAQ software needs to distinguish between a Master PMC and the Slave PMCs is during the initializing (when setting the control bit), when issuing a reset (a reset is only wrote to the Master PMC), and when phase adjusting the BCO clock (in the case where a synchronous accelerator beam is available).

## BCO Clock Distribution

Either the master accelerator clock will be available in the counting room for distribution to each PMC or a locally generated BCO clock that is asynchronous to the beam will be used.  In either case, the BCO clock is sent to the Master PMC.  In the synchronous BCO clock case, the Master PMC uses its Digital Clock Manager (DCM) to phase shift the BCO clock with PERIODBCOCLK/256 resolution (520ps with 132ns BCO clock).   The magnitude of the phase shift is set via a register and is used to tune the phase of the BCO clock at the hut relative to the arrival of the beam.  In the case where the master accelerator clock is not available and an asynchronous locally generated BCO clock is used, the phase shifting feature on the DCM is unused.  The Master PMC distributes the BCO clock to the other PMCs in the PCI bus via its Low Skew Clock Distribute resource (see Fig. 1).  The distributed BCO clock passes through each FPGA on the PMC and is driven via the data cable to the each plane in the hut (see Fig. 3).  With matched cable lengths each plane in the hut should receive phase aligned BCO clocks.

If the above technique does not provide adequate phase alignment of the BCO clocks at the planes, the alignment can be adjusted on a plane to plane basis by using additional Xilinx Digital Clock Manager resources to tune each BCO clock phase with PERIODBCOCLK/256 resolution (520ps with 132ns BCO clock).  This fine phase tuning can be done by software setting PMC registers.

## BCO Count Alignment & Reset

With a BCO clock distributed and in phase at each of the FPIX planes a common reset signal must be distributed.  This common reset signal is distributed much like the BCO clock distribution technique.  The Master PMC uses the reset bit in a register (see section 6 for register definitions) to distributed the reset signal to all other PMCs via the Low Skew General Distribute resource (see Fig. 1).  The reset signal then passes through each FPGA on the PMC and is driven via the data cables to the planes in the hut (see Fig. 3).  With match cable lengths, each plane in the hut should receive the reset signal in phase and therefore have their BCO counts in phase.

Fig. 3.  PMC FPGA block diagram.

# PMC FPGA Firmware

The FPGA on the PMC will function to interface to two FPIX planes, the trigger, the BCO clock, and the PTA card as shown in Fig. 3.  This section describes the PMC FPGA functional blocks shown in Fig. 3, the technique used to record coincidence signals, and the format of the data words.  Refer to Fig. 4 for waveforms showing events described in this section.

## FPIX Interface Block

Fig. 3 shows two FPIX interface blocks in the PMC FPGA.  The FPIX interface provides all the necessary digital control signals to and from FPIX and is responsible for receiving the FPIX data.  FPIX is operated in continuous readout mode (free running BCO clock and free running readout clock).  Different FPGA firmware will be used for interfacing to FPIX0, FPIX1, preFPIX2i, or preFPIX2b.  The interface formats the FPIX data into a word as shown in Fig. 3 that is then sent to the Data Formatter block.

## Extended BCO Counter

The Extended BCO Counter in the PMC FPGA is 26 bits and is clock by the BCO clock.  With a 26 bit Extended BCO Counter and BCO clock period of 132ns, there is ~8.8 seconds of unique Extended BCO Counter states.  The value of this counter is used in the formatted data words.

## Fine Resolution BCO Counter

The Fine-Res BCO Counter is a Gray-code counter clocked by a multiple of the BCO clock frequency.  Fig. 3 shows this as a multiple of 20 of the BCO clock.  The Fine-Res BCO Counter is reset to 0 every rising edge of BCO clock.  In the case where the BCO clock is the accelerator clock synchronous to the beam, the Fine-Res BCO Counter ideally should be at the same count value at each trigger.  The Fine-Res BCO Counter is intended to be used in the asynchronous BCO clock case.  With the example frequencies shown in Fig. 3, the counter will give 1/144Mhz  = ~7ns timing resolution to measure the trigger time relative to the BCO edge.

## Triggers

The trigger received by the PMC is used to latch the current count of the Extended BCO Counter, latch the current count of the Fine-Res BCO Counter, to initiate data transfer to the PTA memory starting with the header word (see Fig. 4), and to start the Receive Window counter.

## Receive Window Counter

When a trigger (coincidence signal) is received by a PMC, the Receive Window Counter begins.  The Receive Window Counter is clocked by the BCO clock and will count up to the value stored in the Receive Window Register (defined in section 6).  If another trigger is received while the Receive Window Counter is counting, the count will restart.  This counter is used to determine if the received FPIX data is tagged as triggered data, or untriggered data by the Data Formatter.

Fig. 4. Waveforms with locally generated async accelerator clock.

## Data Formatter

The Data Formatter is responsible for assembling a data header word and formatting the incoming FPIX data.  All words are 32 bits wide.  The possible word types indicated by the four most significant bits of the data word are described in Table 1.

Table 1.  Possible data words.

| Data Type Bits | Meaning |
| --- | --- |
| 0000 | Illegal |
| 1XXX | Triggered header word. Triggered Extended BCO Count, Fine-Res count |
| 0001 | Untriggered header word. Untriggered Extended BCO Count |
| 0010 | FPIX0 Data |
| 0011 | FPIX1 Data |
| 0100 | preFPIX2tb Data |
| 0101 | preFPIX2i Data |
| 0110 | FPIX2 Data |

### Data Blocks

When a trigger occurs, the data formatter immediately creates a data type ‘1XXX’ (most significant bit is ‘1’) word and sends it to the PTA Memory Interface.  This data word includes the 26 bit extended BCO count and Fine-Res Count state at the time the trigger was received.  The Data Formatter then receives the incoming FPIX data from the FPIX Interface and formats it with the appropriate data type (data type will be set by the firmware based on the FPIX interface type) as long as the Receive Window Counter has not reached its value store in the Receive Window Register.  Fig. 5 shows an example sequence of words that would appear in the PTA memory that include a header word with the extended BCO number followed by four FPIX1 data words.

Fig. 5.  Triggered header word and four FPIX1 words.

In the event the PMC receives data from an FPIX plane outside the Receive Window, the FPIX data can be passed onto the PTA memory in the format shown in Fig. 6.  A register (described in section 6) controls whether or not these untriggered FPIX data words are passed onto the PTA card memory.  Untriggered FPIX data words are distinguished from those that were received after a trigger by their header data word.

Fig. 6.  Untriggered FPIX1 word.

### Triggered Header Word Format

The format for the Triggered Header Word is shown in Figure 7.

Fig. 7.  Triggered header word.

### Untriggered Header Word Format

The format for the Untriggered Header Word is shown in Figure 8.

Fig. 8.  Untriggered header word.

### FPIX0 Data Format

The format for the FPIX0 data word is shown in Figure 9.  Note that the 8 bit ADC is in the position the BCOs are for FPIX1, preFPIX2tb, preFPIX2i, and FPIX2 data formats.

Fig. 9.  FPIX0 data word.

### FPIX1 Data Format

The format for the FPIX1 data word is shown in Figure 10.  Bit 6 is the LSB of the four-bit Chip ID.  The Chip ID is important if a multi-chip module is under test.

Fig. 10.  FPIX1 data word.

### preFPIX2tb Data Format

The format for the preFPIX2tb data word is shown in Figure 11.

Fig 11.  preFPIX2tb data word.

### preFPIX2i Data Format

The format for the preFPIX2i data word is shown in Figure 12.  Note that it is the same as the preFPIX2tb format except for the 4-bit data type.

Fig. 12.  preFPIX2i data word.

### FPIX2 Data Format

The format for the FPIX2 data word is shown in Figure 12.

Fig. 13.  FPIX2 data word.

## PTA Memory Interface

The PTA Memory Interface block is responsible for passing the 32 bit data word from the PMC to the FPGA on the PTA card.   The Altera FPGA on the PTA card receives the 32 bit data word from the PMC and is responsible for moving the data to the appropriate bank of memory and the appropriate memory address.  Fig. 14 shows example waveforms that the PTA Memory Interface might send to the PTA card.  DATA0, DATA1, DATA2, DATA3, and DATA4 would all be placed in PTA card memory.

Fig. 14.  Waveforms for PMC to PTA memory interface.

## FPIX Configuration Path

The FPIX configuration will be accomplished by software toggling the appropriate SHIFT_IN and Clock signals.  Section 6 describes the registers required to achieve this.

## Startup Sequence

To insure proper synchronization of BCO clocks and counters, the following startup sequence must be followed:

| General Clocks and Counters Startup Sequence |
| --- |
| Step | Description | Plane | Register |
| 1 | Set Master PMC | Master PMC only | 0x0008 |
| 2 | Set BCO Phase Offsets – Plane A | Each PMC | 0x0010 |
| 3 | Set BCO Phase Offsets – Plane B | Each PMC | 0x0014 |
| 4 | Reset Master Clock Manager | Master PMC only | 0x000C |
| 5 | Reset Plane A Clock Manager | Each PMC | 0x000C |
| 6 | Reset Plane B Clock Manager | Each PMC | 0x000C |
| 7 | Reset and Sync Counters | Master PMC only | 0x0008 |

An example startup sequence that would be for a single PTA/PMC card connected to two pixel planes (both Plane A and Plane B) is shown below:

| Example Clocks and Counters Startup Sequence |
| --- |
| Step | Description | Register | Value |
| 1 | Set Master PMC and Disable Planes | 0x0008 | 0x000D |
| 2 | Set BCO Phase Offset – Plane A | 0x0010 | 0x0028 |
| 3 | Set BCO Phase Offset – Plane B | 0x0014 | 0x010C |
| 4 | Assert Master Clock Reset | 0x000C | 0x1000 |
| 5 | De-assert Master Clock Reset | 0x000C | 0x0000 |
| 6 | Wait >20ms |  |  |
| 7 | Assert Plane-A Clock Reset | 0x000C | 0x2000 |
| 8 | De-assert Plane-A Clock Reset | 0x000C | 0x0000 |
| 9 | Wait >20ms |  |  |
| 10 | Assert Plane-B Clock Reset | 0x000C | 0x4000 |
| 11 | De-assert Plane-B Clock Reset | 0x000C | 0x0000 |
| 12 | Wait >20ms |  |  |
| 13 | Assert Counter Reset | 0x0008 | 0x000F |
| 14 | De-assert Counter Reset | 0x0008 | 0x000D |
| 15 | Enable Both Planes | 0x0008 | 0x0001 |

Note that the “wait” steps (steps 6, 9, and 12) are to allow the Digital Clock Managers (DCMs) in the PMC FPGA sufficient time to establish a stable locked condition.  Failure to wait for at least 20ms can cause erroneous clocks.

## Pulse Out

Both J1 pin 1 and pin 13 on the PMC offer a TTL pulse that is synchronous to the BCO Clock and controlled with registers 0x0018 and 0x001C (see section 6).  Use register 0x0018 to select the pulse frequency (119Hz to 3.91Mhz with BCO Clk = 7.8125MHz), edge sensitivity, and for reset.  Register 0x001C is used to set the number of pulses in the pulse train (1 to 65535).  All pulses are of width equal to one BCO clock cycle.

When register 0x001C (Pulse Train Length) is set to 0x0000, Pulse Out is free running at a frequency equal to the register 0x0018 Pulse Frequency selection.

Figure 15 shows an example waveform when the following sequence is used:

| Example Pulse Out Setup |
| --- |
| Step | Description | Register | Value |
| 1 | Set Pulse Train Length to ‘4’. | 0x001C | 0x0004 |
| 2 | Select Pulse Freq to ‘BCO Clk/4’, Clk Edge to ‘Negative’, and set reset ‘1’ | 0x0018 | 0x8002 |
| 3 | De-assert reset to begin pulse train | 0x0018 | 0x0002 |

Fig. 15.  Example Pulse Train of Length 4.

To restart the pulse train, re-assert the reset by repeating steps 2 and 3 above.

# Registers

All registers in the PMC are read and some read/write via the DAQ software interface.  This section describes the registers in the PMC FPGA.

## PMC Standard Registers

These registers are standard on all PMC cards regardless of their function.

### Firmware Type: Address 0x0000 (read only)

| Bit # | Meaning |
| --- | --- |
| 15..0 | PMC Type: 0x0000 = Undefined 0x0001 = Cable loop back test 0x0002 = FPIX0 test beam ‘02 0x0003 = FPIX1 test beam ‘02 0x0004 = preFPIX2tb test beam ‘02 0x0005 = preFPIX2i test beam ‘02 |

### Firmware Revision: Address 0x0004 (read only)

| Bit # | Meaning |
| --- | --- |
| 7..0 | Minor revision number. |
| 15..8 | Major revision number. |

## PMC Test Beam ’02 Specific Registers

Registers described in this section are unique to the PMC used in the 2002 test beam.  These registers are common to all the 2002 test beam PMCs.

### Control Register A:  Address 0x0008 (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | 0 = Slave, 1 = Master |
| 1 | Master Distributed Reset (clear and re-sync counters) |
| 2 | 1 = Disable Plane A |
| 3 | 1 = Disable Plane B |
| 4 | Send untriggered FPIX data (not implemented) |
| 5 | Ignore all data (not implemented) |
| 6 | Generate fake data |
| 7 | Clear fake data counter |
| 10..8 | Fake data clock selection 000 = M/2 = 25Mhz 001 = M/4 = 12.5Mhz 010 = M/8 = 6.25Mhz 011 = M/16 = 3.13Mhz 100 = M/32 = 1.56Mhz 101 = M/64 = 781kHz 110 = M/128 = 391kHz 111 = M/256 = 195kHz M is the frequency of the PMC on board oscillator (X1)…50Mhz. |
| 14..11 | Unused |
| 15 | TTL pulse out. This bit is connected to pin 11 of TTL header (J5) on the PMC. |

### Control Register B:  Address 0x000C (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | Master Clock Source 0 = 50Mhz PMC Oscillator 1 = NIM1 input Master Clk is set to Master Clock Source *5/8 (31.25Mhz with 50Mhz Oscillator). |
| 1 | BCO Clock to FPIX Plane A 0 = Send Master Clk/4 to FPIX Plane A (7.81Mhz w/ 50Mhz Oscillator). 1 = Send Software Toggle to FPIX Plane A |
| 2 | BCO Source to FPIX Plane B 0 = Send Master Clk/4 to FPIX Plane B (7.81Mhz w/ 50Mhz Oscillator). 1 = Send Software Toggle to FPIX Plane B |
| 3 | Readout Clock Source to FPIX Plane A 0 = Send Readout Clock equal to Master Clk/2 to FPIX Plane A (15.63Mhz w/ 50Mhz Oscillator). 1 = Send Readout Clock Software Toggle to FPIX Plane A |
| 4 | Readout Clock Source to FPIX Plane B 0 = Send Readout Clock equal to Master Clk/2 to FPIX Plane B (15.63Mhz w/ 50Mhz Oscillator). 1 = Send Readout Clock Software Toggle to FPIX Plane B |
| 5 | Data Latch CLK select Plane A (used to latch incoming FPIX data from Plane A) 0 = Data Latch CLK is same as Readout Clk to Plane A 1 = Data Latch CLK is inverse of Readout Clk to Plane A |
| 6 | Data Latch CLK select Plane B (used to latch incoming FPIX data from Plane B) 0 = Data Latch CLK is same as Readout Clk to Plane B 1 = Data Latch CLK is inverse of Readout Clk to Plane B |
| 7 | Readout Clock x2 selection 0 = Master Clk * 32/5 (200Mhz with 50Mhz Oscillator). 1 = FPIX readout Clk A doubled via delay element |
| 11..8 | Unused |
| 12 | DCM Reset – Master Clk Distribute |
| 13 | DCM Reset – Plane A Clks |
| 14 | DCM Reset – Plane B Clks |
| 15 | Unused |

### Control Register C:  Address 0x0010 (read/write) – Not Implemented

| Bit # | Meaning |
| --- | --- |
| 7..0 | Phase Adjust Magnitude BCO Clk FPIX Plane A |
| 8 | Phase Adjust Direction BCO Clk FPIX Plane A 0 = Positive 1 = Negative |
| 15..9 | Unused |

### Control Register D:  Address 0x0014 (read/write) – Not Implemented

| Bit # | Meaning |
| --- | --- |
| 7..0 | Phase Adjust Magnitude BCO Clk FPIX Plane B |
| 8 | Phase Adjust Direction BCO Clk FPIX Plane B 0 = Positive 1 = Negative |
| 15..9 | Unused |

### Control Register E:  Address 0x0018 (read/write) – Pulse Out Control

| Bit # | Meaning |
| --- | --- |
| 3..0 | Pulse Frequency Selection. Sets frequency of pulses. Formula is BCO freq/(2^(N+1)) where N is 4 bit value from 0 to 15. Frequencies shown below are with BCO freq = 7.8125Mhz 0000 = 3.91MHz 0001 = 1.95MHz 0010 = 977kHz 0011 = 488kHz 0100 = 244kHz 0101 = 122kHz 0110 = 61kHz 0111 = 31kHz 1000 = 15kHz 1001 = 7.6kHz 1010 = 3.8kHz 1011 = 1.9kHz 1100 = 954Hz 1101 = 477Hz 1110 = 238Hz 1111 = 119Hz |
| 4 | Clk Edge Selection. Selects BCO Clock edge Pulse Out is sensitive to 0 = Pulse Out on falling edge of BCO Clock 1 = Pulse Out on rising edge of BCO Clock |
| 14..5 | Unused |
| 15 | Pulse Out Reset. When Pulse Out Reset transitions from ‘1’ to ‘0’, pulse train count begins. |

### Control Register F:  Address 0x001C (read/write) – Pulse Out Train Length

| Bit # | Meaning |
| --- | --- |
| 15..0 | Length (number of pulses) of Pulse Train. When set to 0x0000, Pulse Out is free running. |

### Control Register G:  Address 0x0020 (read/write) – Calibration Control

| Bit # | Meaning |
| --- | --- |
| 7..0 | Number of sequential BCO Clocks sent after Pulse Out if Calibration Mode is enabled. |
| 8 | Enable “Calibration Mode” |
| 15..9 | Unused |

### Plane A ID Register: Address 0x0030 (read/write)

| Bit # | Meaning |
| --- | --- |
| 3..0 | Four bit Plane ID for Plane A |
| 15..4 | Unused |

### Plane B ID Register: Address 0x0034 (read/write)

| Bit # | Meaning |
| --- | --- |
| 3..0 | Four bit Plane ID for Plane B |
| 15..4 | Unused |

### Receive Window Register: Address 0x0038 (read/write)

| Bit # | Meaning |
| --- | --- |
| 15..0 | Size of receive window in terms of readout clock cycles after a trigger signal is received. |

### Max Data Register: Address 0x003C (read/write) – Not Implemented

| Bit # | Meaning |
| --- | --- |
| 15..0 | Maximum number of sequential FPIX data words allowed to receive in terms of readout clock cycles. If this value is reached, the remaining FPIX data is ignored until a reset is received. 0xFFFF = Default. This value indicates no maximum sequential words. |

## FPIX0 Specific Registers

This section TBD.

## FPIX1 Specific Registers

### FPIX1 Interface Plane A:  Address 0x0100 (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | Token_In Plane A |
| 1 | Shift_In Plane A |
| 2 | Shift_CLK Plane A |
| 3 | Trigger_Accept Plane A |
| 4 | Program Reset Plane A |
| 5 | Data Reset Plane A |
| 6 | Load Kill Plane A |
| 7 | ReadClk Plane A |
| 8 | Undefined |
| 9 | BCOClk Plane A |
| 10 | Undefined |
| 11 | Undefined |
| 12 | Reg0 Plane A |
| 13 | Reg1 Plane A |
| 14 | Reg2 Plane A |
| 15 | Undefined |

### FPIX1 Interface Plane B:  Address 0x0104 (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | Token_In Plane B |
| 1 | Shift_In Plane B |
| 2 | Shift_CLK Plane B |
| 3 | Trigger_Accept Plane B |
| 4 | Program Reset Plane B |
| 5 | Data Reset Plane B |
| 6 | Load Kill Plane B |
| 7 | ReadClk Plane B |
| 8 | Undefined |
| 9 | BCOClk Plane B |
| 10 | Undefined |
| 11 | Undefined |
| 12 | Reg0 Plane B |
| 13 | Reg1 Plane B |
| 14 | Reg2 Plane B |
| 15 | Undefined |

## preFPIX2tb Specific Registers

### preFPIX2tb Interface Plane A:  Address 0x0100 (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | Shift_Control Plane A |
| 1 | Shift_In Plane A |
| 2 | Undefined |
| 3 | Undefined |
| 4 | Program Reset Plane A |
| 5 | Reset Plane A |
| 6 | MasterReject Plane A |
| 7 | ReadClk Plane A |
| 8 | Undefined |
| 9 | BCOClk Plane A |
| 10 | Undefined |
| 11 | ChipSend Plane A |
| 15..12 | Undefined |

### preFPIX2tb Interface Plane B:  Address 0x0104 (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | Shift_Control Plane B |
| 1 | Shift_In Plane B |
| 2 | Undefined |
| 3 | Undefined |
| 4 | Program Reset Plane B |
| 5 | Reset Plane B |
| 6 | MasterReject Plane B |
| 7 | ReadClk Plane B |
| 8 | Undefined |
| 9 | BCOClk Plane B |
| 10 | Undefined |
| 11 | ChipSend Plane B |
| 15..12 | Undefined |

### preFPIX2tb Interface Plane A:  Address 0x0108 (read only)

| Bit # | Meaning |
| --- | --- |
| 0 | KillShiftOut Plane A |
| 1 | CoreHasData Plane A |
| 2 | CoreHit Plane A |
| 15..3 | Undefined |

### preFPIX2tb Interface Plane B:  Address 0x011C (read only)

| Bit # | Meaning |
| --- | --- |
| 0 | KillShiftOut Plane B |
| 1 | CoreHasData Plane B |
| 2 | CoreHit Plane B |
| 15..3 | Undefined |

## preFPIX2i Specific Registers

### preFPIX2i Interface Plane A:  Address 0x0100 (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | Shift_Select Plane A |
| 1 | Shift_In Plane A |
| 2 | Shift Clk Plane A |
| 3 | Undefined |
| 4 | Ki Reset Plane A |
| 5 | Reset Plane A |
| 6 | MasterReject Plane A |
| 7 | ReadClk Plane A |
| 8 | Undefined |
| 9 | BCOClk Plane A |
| 10 | Undefined |
| 11 | ChipSend Plane A |
| 15..12 | Undefined |

### preFPIX2i Interface Plane B:  Address 0x0104 (read/write)

| Bit # | Meaning |
| --- | --- |
| 0 | Shift_Select Plane B |
| 1 | Shift_In Plane B |
| 2 | Shift Clk Plane B |
| 3 | Undefined |
| 4 | Ki Reset Plane B |
| 5 | Reset Plane B |
| 6 | MasterReject Plane B |
| 7 | ReadClk Plane B |
| 8 | Undefined |
| 9 | BCOClk Plane B |
| 10 | Undefined |
| 11 | ChipSend Plane B |
| 15..12 | Undefined |

### preFPIX2i Interface Plane A:  Address 0x0108 (read only)

| Bit # | Meaning |
| --- | --- |
| 0 | ShiftOut Plane A |
| 1 | CoreHasData Plane A |
| 2 | CoreHit Plane A |
| 3 | Inj_ShiftOut Plane A |
| 15..4 | Undefined |

### preFPIX2i Interface Plane B:  Address 0x011C (read only)

| Bit # | Meaning |
| --- | --- |
| 0 | ShiftOut Plane B |
| 1 | CoreHasData Plane B |
| 2 | CoreHit Plane B |
| 3 | Inj_ShiftOut Plane B |
| 15..4 | Undefined |

# PTA/PMC Interface

Tables 2 and 3 describe the pin assignments for the JN1 and JN2 interface respectively.

Table 2.  JN1 pin assignment PTA/PMC interface.

| JN1 on PTA (“old” PTA) and PMC |
| --- |
| Pin # | Schematic Signal Name | Functional Signal Name |  |  | Pin # | Schematic Signal Name | Functional Signal Name | I/O* |
| 1 | JN1_S0 | LAD_IN(0) |  |  | 2 | -12V |  |
| 3 | Ground |  |  | 4 | JN1_S1 | LAD_IN(1) | I |
| 5 | JN1_S2 | LAD_IN(2) |  |  | 6 | JN1_S3 | LAD_IN(3) | I |
| 7 | JTAG_TDI |  |  | 8 | 5V |  |
| 9 | JN1_S4 | LAD_IN(4) |  |  | 10 | JN1_S5 | LAD_IN(5) | I |
| 11 | Ground |  |  | 12 | JN1_S6 | LAD_IN(6) | I |
| 13 | CLK2 | SHIFT_CLK |  |  | 14 | Ground |  |
| 15 | Ground |  |  | 16 | CLK2LK |  |
| 17 | CLK2FB |  |  | 18 | 5V |  |
| 19 | 3.3V(I/O) |  |  | 20 | JN1_S9 | LAD_IN(7) | I |
| 21 | JN1_S10 | LAD_IN(8) |  |  | 22 | JN1_S11 | LAD_IN(9) | I |
| 23 | JN1_S12 | LAD_IN(10) |  |  | 24 | Ground |  |
| 25 | Ground |  |  | 26 | JN1_S13 | LAD_IN(11) | I |
| 27 | JN1_S14 | LAD_IN(12) |  |  | 28 | JN1_S15 | LAD_IN(13) | I |
| 29 | JN1_S16 | LAD_IN(14) |  |  | 30 | 5V |  |
| 31 | 3.3V(I/O) |  |  | 32 | JN1_S17 | LAD_IN(15) | I |
| 33 | JN1_S18 | LAD_OUT(0) |  |  | 34 | Ground |  |
| 35 | Ground |  |  | 36 | JN1_S19 | LAD_OUT(1) | O |
| 37 | JN1_S20 | LAD_OUT(2) |  |  | 38 | 5V |  |
| 39 | Ground |  |  | 40 | JN1_S21 | LAD_OUT(3) | O |
| 41 | JN1_S22 | LAD_OUT(4) |  |  | 42 | JN1_S23 | LAD_OUT(5) | O |
| 43 | JN1_S24 | LAD_OUT(6) |  |  | 44 | Ground |  |
| 45 | 3.3V(I/O) |  |  | 46 | JN1_S25 | LAD_OUT(7) | O |
| 47 | JN1_S26 | LAD_OUT(8) |  |  | 48 | JN1_S27 | LAD_OUT(9) | O |
| 49 | JN1_S28 | LAD_OUT(10) |  |  | 50 | 5V |  |
| 51 | Ground |  |  | 52 | JN1_S29 | LAD_OUT(11) | O |
| 53 | JN1_S30 | LAD_OUT(12) |  |  | 54 | JN1_S31 | LAD_OUT(13) | O |
| 55 | JN1_S32 | LAD_OUT(14) |  |  | 56 | Ground |  |
| 57 | 3.3V(I/O) |  |  | 58 | JN1_S33 | LAD_OUT(15) | O |
| 59 | JN1_S34 | WR_EN |  |  | 60 | JN1_S35 | ALE | I |
| 61 | JN1_S36 | PCI_CLK |  |  | 62 | 5V |  |
| 63 | Ground |  |  | 64 | EEDATA |  |
| * Relative to PMC |

Table 3.  JN2 pin assignment PTA/PMC interface.

| JN2 on PTA (“old” PTA) and PMC |
| --- |
| Pin # | Schematic Signal Name | Functional Signal Name | I/O* |  | Pin # | Schematic Signal Name | Functional Signal Name | I/O* |
| 1 | 12V |  |  | 2 | JN2_S0 | DATA(0) | O |
| 3 | JN2_S1 | DATA(1) | O |  | 4 | JN2_S2 | DATA(2) | O |
| 5 | JN2_S3 | DATA(3) | O |  | 6 | Ground |  |
| 7 | Ground |  |  | 8 | JN2_S4 | DATA(4) | O |
| 9 | JN2_S5 | DATA(5) | O |  | 10 | JN2_S6 | DATA(6) | O |
| 11 | JTAG_TCK |  |  | 12 | 3.3V |  |
| 13 | JN2_S7 | DATA(7) | O |  | 14 | JTAG_TMS |  |
| 15 | 3.3V |  |  | 16 | JTAG_TDO |  |
| 17 | JN2_S8 | DATA(8) | O |  | 18 | Ground |  |
| 19 | JN2_S9 | DATA(9) | O |  | 20 | JN2_S10 | DATA(10) | O |
| 21 | Ground |  |  | 22 | JN2_S11 | DATA(11) | O |
| 23 | JN2_S12 | DATA(12) | O |  | 24 | 3.3V |  |
| 25 | JN2_S13 | DATA(13) | O |  | 26 | JN2_S14 | DATA(14) | O |
| 27 | 3.3V |  |  | 28 | JN2_S15 | DATA(15) | O |
| 29 | JN2_S16 | DATA(16) | O |  | 30 | Ground |  |
| 31 | JN2_S17 | DATA(17) | O |  | 32 | JN2_S18 | DATA(18) | O |
| 33 | Ground |  |  | 34 | JN2_S19 | DATA(19) | O |
| 35 | JN2_S20 | DATA(20) | O |  | 36 | 3.3V |  |
| 37 | Ground |  |  | 38 | JN2_S21 | DATA(21) | O |
| 39 | JN2_S22 | DATA(22) | O |  | 40 | Ground |  |
| 41 | 3.3V |  |  | 42 | JN2_S23 | DATA(23) | O |
| 43 | JN2_S24 | DATA(24) | O |  | 44 | Ground |  |
| 45 | JN2_S25 | DATA(25) | O |  | 46 | JN2_S26 | DATA(26) | O |
| 47 | Ground |  |  | 48 | JN2_S27 | DATA(27) | O |
| 49 | JN2_S28 | DATA(28) | O |  | 50 | 3.3V |  |
| 51 | JN2_S29 | DATA(29) | O |  | 52 | JN2_S30 | DATA(30) | O |
| 53 | 3.3V |  |  | 54 | JN2_S31 | DATA(31) | O |
| 55 | JN2_S32 | DATAVALID | O |  | 56 | Ground |  |
| 57 | JN2_S33 | SHIFT_IN | I |  | 58 | JN2_S34 | SHIFT_OUT | O |
| 59 | Ground |  |  | 60 | JN2_S35 | SHIFT_SEL | O |
| 61 | JN2_S36 | Unused |  |  | 62 | 3.3V |  |
| 63 | Ground |  |  | 64 | CLK4 | DATA_CLK | O |
| * Relative to PMC |

# FPIX0 Interface

This section TBD.

Fig. 16.  Pin assignment for FPIX0 interface.

# FPIX1 Interface

Fig. 17.  Pin assignment for FPIX1 interface.

# PreFPIX2 Interface

Fig. 18.  Pin assignment for FPIX2i and FPIX2tb interface.

# References

[1] PTA documentation

[2] PMC documentation

[3] FPIX0 inner board documentation

[4] FPIX1 inner board documentation

[5] FPIX2 inner board documentation