# WASTE TREATMENT LAGOON

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 359

### WASTE TREATMENT LAGOON

A waste treatment lagoon is an impoundment made by excavation or earth fill to provide storage for biological treatment of animal or other agriculture waste.

### PRACTICE INFORMATION

The purpose of this practice is to store and biologically treat organic waste, reduce pollution, and protect water quality.

The three general types of waste treatment lagoons are:

- Anaerobic―require less surface area than naturally aerobic lagoons, but may give off offensive odors

- Naturally aerobic―require more surface area, but are relatively odor free

- Mechanically aerated―comparable in size to anaerobic lagoons, but require energy for aeration

Waste treatment lagoons are located as near the source of waste as possible but as far from human dwellings as possible. The location should also be where prevailing winds will carry odors away from residences and public areas.

To improve efficiency and reduce sludge buildup, solids should be removed from the waste before it enters the lagoon. A solids trap or separator should be installed between the waste source and the lagoon.

### COMMON ASSOCIATED PRACTICES

Waste Treatment Lagoon is commonly used in a Conservation Management System with practices such as Solid/Liquid Waste Separation Facility (632), Waste Utilization (6330, and Nutrient Management (590).

For further information, refer to the practice standard in the local Field Office Technical Guide and associated specifications and job sheets.

# Text boxes

Note:  Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

Associated practice

I. 3 (+) Lagoon failure, seepage

I.2 (+) Meeting air quality standards

C.2 (+) (-) Air Quality of the air shed (depending on objectives/resource of concern)

Aerobic

D.4 Air Quality

(-) Greenhouse
     gas

(-) Odor

(+) (-) Ammonia

(+) (-) HAP

(+) (-) Pathogens

Anaerobic

Cover

D.4 Air Quality

(-) Greenhouse
     gas

(-) Odor

(+) (-) Ammonia

(+) (-) HAP

(+) (-) Pathogens

D.4 Air Quality

(+)Greenhouse
     gas

(+) Odor

(+) (-) Ammonia

(+) (-) HAP

(+) (-) Pathogens

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

LEGEND

D.3 (+) Perceived nuisance

C.5 (-) Health/ habitat suitability for humans

Start

Waste Treatment Lagoon

5/2002

Uncover

Waste Utilization (633)

Nutrient Management (590)

D.2 (+) Manure stored in lagoon

Initial setting: AFO is

established and wants a

lagoon for treating wastes

2. Structure/site dedicated

C.3 (+) Stream fauna, e.g., fish, invertebrates

D.1 (+) Infrastructure and operational costs

C.1 (+) Income stability (individuals and community)

I.1 (+) Agribusiness

I.6 (+) Meeting water quality standards

I.5 (-) Noxious algal growth

C.4 (+) Aquatic health for humans and domestic and wild animals

I.4 (+) Dissolved oxygen surface waters

D.5 (-) Pesticides, nutrients, and organics to surface water

Waste Treatment Lagoon (359)

D.6 (-) Suspended sediment, metals, pathogens, salinity to surface water

1. Manure-transfer system purchased/dedicated