POLAR Spacecraft Status As of: Tues Aug 09, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1651=AN STIP data only | NOAA-14J AM: 2039=AN STIP data only | NOAA-15K AM: 1806=AN GAC data only | NOAA-16L PM: 1441=AN GAC&LAC data | NOAA-17M AM: 2225=AN GAC&LAC data | NOAA-18N Trans PM 14:00=AN APT/HRPT/GAC |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=DTR 1B | SSRs 1,2,3,4,5 Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ Conflict with N15 | OFF Conflict with N17 VTX-2 off 8/2/05 | OFF Conflict with N12 7/29 – 8/30 | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ Conflict with N14 | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT Power drop TOAR 446 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 3 - HRPT 1&2 Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/04 Eclipse season 21Apr-20Aug Sun Angle 30 downtrend to 12 mid-Oct 05 Batts 1&2=LRC Batt !&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 48 Steady trend Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Eclipse Season ended 7/28/05 Sun Angle 25 downtrend to 2 degs on 10 Oct 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 55 Downtrend to 41 on 30 Oct 05 Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 PSSS enabled 30May |
| AVHRR | Nominal | Nominal Channels 2 & 4 to APT 8/2/05 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Degraded TCE24 OFF 4/14/04 Imagery improved since 6 Aug 05 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Space view 1 Since 6/7/05 |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Space view-2 |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal TOAR 445 CLOSED 7/12/05 FW mode=Hi Powr FW Heater OFF | Operational High levels of imagery radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | ON TOAR 448 Noise in long wave channels 1-12. Some improvement reported. Tested in high power mode 12 July |
| MHS/MIU |  |  |  |  |  | Nominal Final config 6/4/05 |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | ON DRU’s 1-7 On DRU-8 TOAR 449 turned off 6/13 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | ON A-Side 121, 243, 406 FIXED GAIN MODE Since 18 Jul 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | ON A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | ON Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations No data reported by products division 7/25/05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z OV testing continues |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12	No change from last week.  EMOSS engineers are analyzing the efficacy of turning on failed payloads for use as

resisters in the power balance equation.  Carl Gliniak is EMOSS POC.  On 29 July, N12 entered into a VTX conflict with N15 with N15 VTX-1 being turned off as a result.

NOAA-14:	No changes since previous report.  AVHRR health remains nominal and stable (illustration 1).  Turning off VTX-2

(APT data) on 2 Aug resulted in a minor improvement in N14’s power balance situation without any additional shunt stress (illustration 2).

NOAA-15:	The N15 AMSU-A1 and A-2 payloads were nominal and stable last week although the AMSU-B did show some minor signs of less than stable behavior within its scan motor current value (illustration 3) as did the N15 AVHRR (illustration 4).  This behavior did not have any apparent impact on imagery products (illustration 5) and no concerns were forwarded to EMOSS engineers from the products community.  Conversely, the N15 HIRS, until not too long ago a very erratically performing payload, remained rock solid stable during the past week for the 12th week since self correcting from a major malfunction (illustration 6).

On 29 July at 14:00z, VTX-1 on N15 was turned off through 30 Aug 07:00z because on an RF conflict with N12.  Therefore, for almost the entire month of August there will be no N15 APT data.

N15 power situation remained nominal now that the eclipse season has ended.  No reconfigurations are expected or planned.

NOAA-16:	N16 AMSU’s were all nominal during the past week (illustration 7) while the AVHRR continued to perform

with a little less stability and at slightly worse levels than the previous week (illustration 8).  On the other hand, even

with the AVHRR operating at historically anomalous scan motor current and synch delta levels during the past 4-5

days, its imagery has cleared up with no bar codes or wave patterns evident since 6 Aug (illustration 9, 10 and 11).  This is an unprecedented development in the life cycle of this particular AVHRR and there is currently no explanation for the improvement in imagery while telemetry remains so marginal.  Conversely, earlier in the week the N16 HIRS started to show a trend toward higher filter motor current values only to reverse itself later in the week and return back to more recent stable levels (illustration 12).

The N16 ADACS remained stable throughout the past week (illustration 13).

NOAA-17:	There were no changes from last week.  The remaining N17 AMSU’s, the AVHRR and HIRS were all nominal and

stable during the past week as was the ADACS, including gyro-2 motor current whose surge several weeks ago resulted in a TOAR investigation (illustrations 14-16).

NOAA-18:	The N18 AMSU’s remained parked in space view and performed in a nominal and stable manner during the past

week (illustration 17).

The N18 AVHRR and HIRS were also nominal and stable during the past week (illustration 18).  However, on 5 Aug, the AVHRR automatic 3A-B switch was disabled and the payload was configured for 3B only.  This is expected to be a permanent configuration.  Sally House was EMOSS POC for this operation.

On August 10th 2005, EMOSS engineer Jon Woodward will be replacing all of the CPU-A (backup CPU)  telemetry with MIMU raw telemetry.  This is planned for Rev 1160, at 17:49z.  The tables are being changed to gather data at a 10 Hz rate for additional information in the ongoing pitch anomaly investigation (TOAR 447).  The new table will only be onboard for the duration of a single contact.  It will be uplinked at the start of the contact, and another table uplinked at the end.  The second table uplinked will be to restore the table to its previous value.  Two changes are being made.  One replaces the values in CPU telemetry table 1 with MIMU raw data (MDATABUF) and the other changes how the CPU telemetry tables are read.  Usually the tables are read in this fashion, one read per minor frame; Table 1, 2 then 1, 3 then 1, 4 and so on.  This will be changed for the contact to read only Table 1.  This change will also be backed out at the end of the contact.  Additionally, the SAD status word will be inserted into CPU-B telemetry table 1, replacing the pitch torquer command point.  This point already replaces the MSH of command time and will also be backed out at the end of the contact.  During the time that this new table is onboard, no CPUA telemetry will be valid.  Also, the CPU sync words will be overwritten, and therefore CPU-A sync will be lost.  Data will be gathered using a raw dump of the telemetry data.

Two weeks previously, The SEDL reported dropouts in the SARR signal on N18.  EMOSS engineer Will Chadwick investigated this situation and discovered no spacecraft problems relating to this event.  Further investigation has led to the consensus that the problem lies with the receiving ground equipment (as documented by Xuan Nguyen in his letter documenting this investigation entitled “NOAA-18 Downlink Anomaly” dated 8/8/2005).

31 August is currently the proposed date for making N18 operational but this has not yet been finalized.

Illustration 1:  NOAA-14 AVHRR Health Analysis

(nominal and stable)

Illustration 2:  N14 Power Analysis

(Nominal and stable.  Note the improvement in Battery voltage that occurred with the VTX-2 turnoff on JDAY 214.

Illustration 3:  N15 AMSU Health Analysis

(A1 and A2 are nominal and stable but AMSU-B may warrant some additional scrutiny.

Illustration 4:  N15 AVHRR Health Analysis

(Less stable than desired.  May also warrant additional scrutiny.)

Illustration 5:  N15 AVHRR Imagery & Synch Delta Analysis

(No apparent impact of scan motor instabilities on imagery and only minor impact on synch delta, so far.)

Illustration 6:  N15 HIRS Health Analysis

(Nominal and stable.)

Illustration 7:  N16 AMSU’s Health Analysis

(All three nominal and stable.)

Illustration 8:  N16 AVHRR Health Analysis

(Not better than the week previous.)

Illustration 9:  N16 AVHRR HRPT Imagery Analysis

(For some unexplained reason, HRPT imagery has been completely clean since early on 5 Aug.)

Illustration 10:  N16 AVHRR GAC Imagery Analysis

(Also, for some unexplained reason, GAC imagery has been completely clean since early on 6 Aug. Even though MIRP rephase is required on every orbit.)

Illustration 11:  N16 HRPT Imagery Wave Pattern and Synch Delta Analysis

(Even more unexplained, no wave patterns observed in the limited number of sample analyzed for this perturbation even though synch delta remains pegged and scan motor current is well within the range where wave patterns are typically sustained.

Illustration 12:  N16 HIRS Health Analysis

(After giving pause for concern last week, the filter motor seems to have settled back into a more nominal and stable pattern.)

Illustration 13:  N16 ADACS Health Analysis

(Appears nominal and stable from this limited perspective.)

Illustration 14:  N17 AMSU’s Health Analysis

(Nominal and stable, except for AMSU-A1 which is inoperative.)

Illustration 15:  N17 AVHRR & HIRS Health Analysis

(Nominal and stable.)

Illustration 16:  N17 ADACS Health Analysis

(Nominal and stable, especially gyro-2 which has provided reason for concern in past weeks.)

Illustration 17:  N18 AMSU’s Health Analysis

(Nominal and stable.)

Illustration 18:  N18 AVHRR & HIRS Health Analysis

(Nominal and stable.)

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING August 5, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 07/29 | -300 msec | +220 msec | -235 msec | +141 msec | +083 msec | -035 msec |
| SAT. 07/30 | -300 msec | +220 msec | -236 msec | +142 msec | +083 msec | -034 msec |
| SUN. 07/31 | N/A | +221 msec | -236 msec | +146 msec | +085 msec | -033 msec |
| MON. 08/01 | -299 msec | +220 msec | -237 msec | +146 msec | +085 msec | -030 msec |
| TUE. 08/02 | -301 msec | +221 msec | -238 msec | +146 msec | +087 msec | -030 msec |
| WED. 08/03 | -305 msec | +224 msec | -240 msec | +147 msec | +087 msec | -028 msec |
| THU. 08/04 | N/A | +224 msec | -241 msec | +147 msec | +085 msec | -027 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of -500 milliseconds on 04/17/05 due to fractional second daily ETCUP. A clock

jump of +500 milliseconds on 07/01/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 09/15/05.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Mickey Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015