WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A11289 | In-Flight Anomaly Number -- | Contractor Report Number E-113 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TUMBLE VALVE ARM AND FIRE CIRCUIT FAILED DURING TESTING AT MAF |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT 1 | Sys_Lvl Y | Misc Codes A (3) B C D E (X) F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LWT-16 | PART# 80901010000-050 | SER/LOT# 16 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE TUMBLE VALVE ARM CIR | PART# PD71000082-009 | SER/LOT# N/A | MANUFACTURER MMC |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EV - NOT-TO-SPEC | Cause ETT - EI-TEST-EQUP |
| System ELECTRICAL | Defect -- | Material E - EL C/W | Work Contact J. ADAMS | Fail Date 02/25/1988 |
| Received at MSFC 03/04/1988 | Date Isolated -- | FMEA Reference 3.5.X.X | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EF - INTERMITTENT | Time Cycle N/A |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/13/1995 | CN RSLV SBMT 05/18/1988 | Defer Date -- | Add Date 03/09/1988 | R/C Codes 3 - F/TE -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR G. BRIDWELL |
| Approval |
| Design A. JACKMAN | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR G. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 06/07/1988 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE TUMBLE VALVE ARM AND FIRE CIRCUITS ON LWT-16 WERE BEING TESTED PER TEST PROCEDURE-6R105-FT FOLLOWING THE MODIFICATIONS AND REPAIR TO THE ET AT MAF. THE ARMED INDICATION LAMP ON THE TEST CONSOLE DID NOT SHOW AN ARMED CONDITION UNTIL TWO MINUTES HAD ELAPSED FROM THE TIME THE ARM POWER SWITCH WAS ACTIVATED. THE FAILURE DID NOT REPEAT UPON LATER RETEST. DURING VENDOR ACCEPTANCE TEST OF THE SWITCH MODULE THE MAXIMUM ALLOWABLE TIME IS 100 MILLISECONDS (REF. MARS T98519). THIS TEST WAS THE FIRST USED OF THE NEW TEST CONSOLE ON FLIGHT HARDWARE |
| Contractor Investigation/Resolution R/C: THE ARM SWITCH AND THE SAFE SWITCH ON THE TEST CONSOLE INVOLVED WITH THE TEST FAILURE HAVE BEEN REPLACED WITH AN IMPROVED TYPE OF SWITCH CAUSE: THE CAUSE OF THE LWT-16 TEST FAILURE COULD NOT BE DETERMINED WITH CERTAINTY. A POSSIBLE CAUSE WAS THE ARM SWITCH ON THE TEST CONSOLE WHICH HAD POOR TACTILE INDICATION OF CONTACT OPERATION 5/18/88 GENERAL - THE TUMBLING SYSTEM COMPRISES A PYROTECHNIC VALVE, A LANCE, AND ELECTRICAL CONTROL CIRCUITS. THE ELECTRICAL CIRCUITS UTILIZE THREE WIRE HARNESSES AND A SWITCH MODULE. THE SWITCH MODULE CONTAINS A RELAY WHICH, WHEN ENERGIZED BY THE "ARM" SIGNAL FROM THE ORBITER, COMPLETES CIRCUITS TO SEND AN "ARMED INDICATION" SIGNAL TO THE ORBITER AND TO CONNECT THE PYROTECHNIC VALVE EXPLOSIVE INITIATOR TO THE "FIRE" SIGNAL WIRING. DURING TESTING OF THE ELECTRICAL CIRCUITS OF COMPLETED ET'S, TEST EQUIPMENT CAPABLE OF SIMULATING THE ORBITER IS CONNECTED TO THE ET/ORBITER ELECTRICAL UMBILICALS TASK I. FAILURE INVESTIGATION A. FAILURE ANALYSIS T-98524 WAS PERFORMED ON THE SWITCH MODULE WHICH HAS BEEN REMOVED FROM LWT-16. THE MODULE HAD BEEN REMOVED FROM THE ET AS PART OF THE DISPOSITION OF MARS T-98519, WHICH COVERED THE ORIGINAL TEST FAILURE ANALYSIS OF THE SWITCH MODULE FOUND THAT IT MET THE PERFORMANCE REQUIREMENTS FOR A NEW UNIT. THERE WAS NOTHING TO INDICATE THAT THE MODULE COULD HAVE IN ANY WAY, CAUSED THE TEST FAILURE ON THE ET B. FAILURE ANALYSIS OF THE TEST CONSOLE AND THE ELECTRICAL TEST HARNESS COULD FIND NO CLEAR INDICATION AS TO THE CAUSE OF THE TEST FAILURE. THE WIRE HARNESSES AND TEST CONSOLE WERE EXAMINED IN DETAIL WITHOUT RESULT. THE RELAYS, TRANSISTOR, RESISTOR, LED, AND SWITCH IN THE TEST CONSOLE ARM AND ARMED INDICATION CIRCUITS UNDERWENT COMPLETE DISASSEMBLY AND ANALYSIS, ALSO WITHOUT RESULT IT WAS NOTED HOWEVER THAT THE ARM SWITCH WOULD BE REPLACED WITH ONE WITH "A MORE POSITIVE ACTION WHEN PLACED IN THE ARM POSITION" (REFERENCE: INTEROFFICE MEMO 3613-88-109 AND 3613-88-134) TASKED CLOSED TASK II CORRECTIVE ACTION THE ARM SWITCH AND THE SAFE SWITCH ON THE TEST CONSOLE INVOLVED WITH THE TEST FAILURE HAVE BEEN REPLACED WITH AN IMPROVED TYPE OF SWITCH (REFERENCE: TOOL CHANGE NOTICE TO TOOL DRAWING NO F78-2358, CHANGE NO. 3) TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES LWT-16 MARS T-98519 ADDRESSES THE TEST FAILURE LWT-20, 21, 22, THE ETS PASSED ALL IN PROCESS TESTS AND 24/SUBSEQUENT ACCEPTANCE TESTS OF THE TUMBLE VALVE ARM CIRCUITS. FAILURE ANALYSIS OF THE SWITCH MODULE REMOVED FROM LWT-16 FOUND THAT IT EXCEEDED THE PERFORMANCE REQUIREMENTS FOR NEW UNITS TASK CLOSED TASK IV CAPS CLOSURE SUMMARY A TEST FAILURE ON THE TUMBLE VALVE ARM CIRCUITS OCCURRED DURING RETEST OF LWT-16 FOLLOWING MODIFICATIONS TO THE VEHICLE AT MAF. THIS WAS THE FIRST SUCH FAILURE IN THE ET PROGRAM. SUFFICIENT TESTS OF THE ARM CIRCUITS EXIST AT MAF AND KSC TO ASSURE PERFORMANCE OF THE SYSTEM ON ALL VEHICLES TASK CLOSED THIS CLOSURE IS SUBMITTED FOR MSFC REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A11289 | IFA# -- | Contractor RPT# E-113 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD71000082-009 | Asmnt Part Name TUMBLE VALVE ARM CIR | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD UU - UNK-UND | FAIL MODE EA - FAILS OFF |
| Asmnt FMEA 3.5.1.2 | Asmnt FM 2 | FMEA CSE A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |