Notes on “CO Concrete Water Control Structures” (Jan 16 '08 - Paula Baty) and

“CO Irrigation Pipeline App Details” (Jan 16 '08 - Paula Baty) DWG Detailed Drawings by Paula Baty, Agricultural Engineer, NRCS, Glenwood Springs Office, (970) 945-5494, Ext. 110.

- Notes are in paperspace (that way they are properly sized if you print them on

24” x 36” put the dimensions in with the tool palette sized for 24” x 36”).

- Dimensions are in paperspace.

- Viewports are locked, but can be unlocked.  For now, they allow you to work in the

model from paperspace without messing up the scale.

- Steel is drawn in the center.  The steel is drawn in at actual lengths (10" or 11"

spacing), so you can use the drawing to tell you the number of bars in a cross-

section, but not the length.  It makes the quantities go faster if you have to figure

them.

- Something I left off, but you may want in there, is the cover requirements.