MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A08081 | In-Flight Anomaly Number -- | Contractor Report Number E-001 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LH2 ULLAGE PRESSURE TRANSDUCER FAILED ATP TEMP TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 ULL PRES TRNSDCR | PART# PD7400098-019 | SER/LOT# 0000036 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion -- | F / U F | Fail Mode -- | Cause -- |
| System ELECTRICAL | Defect -- | Material -- | Work Contact R. JACKSON | Fail Date 04/11/1977 |
| Received at MSFC 07/01/1979 | Date Isolated -- | FMEA Reference 3.1.1.9 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EV - NOT-TO-SPEC | Time Cycle -- |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 07/01/1979 | Defer Date -- | Add Date -- | R/C Codes 1 - DES -- -- |
| Assignee |
| Design G. PLATT | Chief Engineer -- | S & MA D. NEWMAN | Project R. ABRAHAM | Project MGR -- |
| Approval |
| Design N/A | Chief Engineer -- | S & MA N/A | Project N/A | Project MGR -- |
| PAC Assignee M. GLASS | PAC Review Complete MG | MSFC Closure Date 07/01/1979 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE TRANSDUCERS FAILED DURING THE TEMP CYCLING ACCEPTANCE PORTION OF THE GULTON ATP-3031-13801 "C" WHILE UNDERGOING ACCEPTANCE TESTING AT GULTON SERVONICS. S/N 0000036 HAD AN OUTPUT READING OF -3.3% AT 16.0 PSIA DURING DITHER CALIBRATION; SHOULD BE +/- 3.0%, PARA. 6.1.4.1. S/N 0000038 HAD AN OUTPUT READING OF -0.85% AT 3.5 PSIA DURING DITHER CALIBRATION; SHOULD BE +/-.075%, PARA. 6.1.4.1. S/N 0000041 READ 4,705 OHMS; SHOULD BE 5000 +/- 250 OHMS, PARA. 6.3.4.2 |
| Contractor Investigation/Resolution CAUSE - 1. S/N 0000041 WAS CAUSED BY A LOW RESISTANCE OF THE ELE DURING INITIAL BUILD. 2. S/N 0000036 & S/N 0000038 WAS CAUSED BY NOT CHECKING THE NITIAL SETUP PRIOR TO FINAL ASSY. CLOSURE ACTION - 1. S/N 0000041 (RESISTANCE CHANGE). THE RESISTANCE WIRE UTILIZED IN THE RESISTANCE ELE. IS SIGMOND COHN ALLOY 479 WHICH HAS A TEMP COEFFICIENT OF RESISTANCE OF 0.000133 OHMS/OHMS/DEG F, AT -170 DEGS: R = 4,927 (0.00013) (170 + 70) = 157 OHMS. THE WEAR-IN OF THE UNIT CAUSES THE WIPER TO BE IN CONTACT WITH MORE WIRE TURNS WHICH ACCOUNTS FOR ADDITIONAL 30 OHMS DELTA. ADDITIONAL INVESTI- GATION REQ'D TO DETERMINE LOSS OF 55 OHMS. THE ADDITIONAL 55 OHMS CANNOT BE EXPLAINED DIRECTLY BUT THE FOLLOWING FACTORS SHOULD BE CONSIDERED. 1. A LINEAR FUNCTION CANNOT BE ASSUMED FOR THE SIGMOND COHN ALLOY 479 TEMP COEFFICIENT. 2 TELECON WITH SIGMOND COHN DISCLOSED THAT ACTUAL DATA ON ALLOY 479 IS NOT AVAILABLE AT TEMPS BELOW -100 DEGS F & IS NOT PREDICTABLE & COULD POSSIBLY ENTER THE AREA OF SUPER CONDUCTIVITY. 3. THE RESISTANCE CHANGE FOR IDENTICAL UNITS S/N 0000034, S/N 0000037, S/N 0000043 & S/N 0000045 SHOWED A RESISTANCE CHANGE OF 180 TO 240 OHMS. 4. THE PREDICTED OPERATING ENVIRONMENT FOR THE PD7400098 IS -155 DEGS F & THE UNITS ARE TESTED TO -170 DEGS F. GULTON SERVONICS STD PRODUCTION INSTRUCTIONS, RELATING TO RESISTANCE ELE. BUILD, HAVE BEEN CHANGED FROM +/- 250 OHMS TO +200, OR -0 OHMS. 2. S/N 0000036 & S/N 0000038. THE CALIBRATION CURVES INDICATE THE THE DRIVE BAND WAS SIDE LOADED CAUSING FRICTION AT THE 16 & 52 PSIA POINTS. DESIGN OF THE UNIT WOULD INDICATE THAT THE CAPSULE WOULD HAVE THE LEAST AMOUNT OF TORQUE WHEN APPROACHING OR GOING INTO THESE 2 POINTS. ANY FRIC- TION OF SIDE LOADING ON THE DRIVE BAND WOULD CAUSE A REDUCED OUTPUT AS INDICATED ON THE CALIBRA- TION CURVES THE 33 PSIA SETPOINT WAS SET CORRECTLY BUT THE FRICTION CAUSED THE OUT OF TOL. CONDITION. GULTON SERVONICS HAS INCORP'D A ROOM TEMP DITHERED CALIBRATION TO CHECK BAND SIDE LOADING FRICTION & THE CURVE IS LIMITED TO +/- 1% OF FULL SCALE. ON THE INCREASING PRESS. RUN THE 33 PSIA POINT INTERCEPT WILL BE HELD TO A -0.3% MAX. BELOW 0%. THE INCORP'D CHANGES WILL ENSURE THAT FRICTION SETUP & SLOPE PROBS WILL BE CORRECTED PRIOR TO FINAL ASSY & THEREFORE ELIMINATE THE OUT OF TOL. EXPERIENCED DURING ATP |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A08081 | IFA# -- | Contractor RPT# E-001 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# -- | Asmnt Part Name -- | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD -- | CAUSE CD -- | FAIL MODE EV - NOT-TO-SPEC |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |