A Simple Solution to the Multiple Cooling Requirements for Vertical Cryostats used for 1.8K - 4.2K Superconducting Magnet Testing

A. F. Lietzke

Abstract

The motivation for an improved heat exchanger for vertical magnet test cryostats is presented.  The basic system design constraints, challenges and conflicts are described, including issues around dual usage for 80K and 1.8K cool-downs.  A conceptual design is presented that meets the challenges in a novel way by using some of the annular space surrounding the top of the magnet for a heat exchanger.  Practical implementation problems are discussed and possible solutions are presented.

I)  Introduction

In recent times there has been an increased interest in operating some accelerator magnets at temperatures below 4.2K.  This not only allows the magnet to train more quickly, run more reliably and/or operate at a higher field strength, but the presence of the superfluid (T < 2.17K @ 1 Atm) improves the ability to remove heat from the magnet.  The improved thermal conductivity is especially desirable for magnets subjected to volumetric heating (as from synchrotron radiation), permitting operation under conditions that would otherwise preclude superconducting magnets, or require the construction of relatively expensive cooling schemes.  Hence there is a desire for a simple, inexpensive, and reliable system to remove heat at sub atmospheric pressures.

One solution is to simply pump on the entire system.  This however, entails some risk of solid air plugging (in the presence of a leak), and usually provides inadequate cooling for the magnet current-leads at the lowest temperatures.  The other solution is to provide a small, sub-atmospheric heat exchanger that allows the magnet chamber to operate above 1 Atm.

Operationally, it is desirable to test such magnets in a vertical cryostat in order to simplify magnet insertion and removal operations, by permitting the use of warm pressure and vacuum seals.  The minimum thermal leak-path required with this design, coupled with lifting device height limitations and minimum desired magnet lengths, often places a premium on vertical real-estate.  Hence, there is often some desire to place the evaporator off to one side of the magnet, usually at some penalty in complexity, cost, thermal leakage, and/or operational reliability.  	A second reason to place the evaporator off to one side involves one’s desire to protect its relatively thin walls from damage during the insertion and removal of rather heavy (1 - 10 ton) magnets.

There is usually a desire to cool these magnets from 300K to 80K in a rather slow and benign fashion (to reduce the effects of differential thermal contraction), within a helium atmosphere (to reduce the effects of solid nitrogen within the magnet structure).  This requires some kind of heat exchanger to cool the helium gas.  Hence, one either installs a second heat exchanger for 80K cooling, or finds a way to use one heat exchanger for both operations.

The purpose of this paper is to describe the conceptual design of a heat exchanger that is simple, rugged, takes up very little expensive real estate, and can be used for 80K cool-down operations within vertical cryostats.

II)  General Design Considerations

Super-fluid operation of a cryostat places some severe constraints on the cryostat design.  Due to the decreasing cooling capability as the temperature is lowered, a premium exists for low thermal leakage.  This not only requires some attention to insulating blanket details, but it requires considerable attention to insuring super-fluid-tight seals at all penetrations into the super-fluid volume.  In particular, for magnets which are inserted with 300K seals, some kind of low conductivity plate (“lambda plate”) is used to separate the superfluid/magnet system from the normal stratified helium above it.  This kind of geometry requires that the lambda-plate diameter exceed the diameter of the largest magnet to be tested.  It also means that the magnet must be inserted (and removed) past some kind of sealing ring with enough sealing length to meet the super-fluid sealing requirements (2-4 cm is usually considered to be adequate).  The axial location of this ring depends upon the maximum allowed thermal gradient within the cryostat wall material (controlling the heat load to the 4.5K system), plus the desired local 4.5K liquid helium reservoir height (above the Lambda-plate).  Typical lambda-plate locations range between 0.5 - 1.2 m below the top of the cryostat.  Several penetrations are required and need to be sealed adequately: 1) supports for the magnet’s weight, 2) current-supply leads for the magnet, 3) pressure relief ports, 4) non-vapor-lock liquid helium supply ports, 5) diagnostic access.  Care must be taken to avoid over-constraining the penetrations as this may interfere with the quality of the superfluid seal.

One also needs the refrigeration capability to handle the heat-load at the desired operating conditions.  Cooling a 1 Atm helium system below 4.2K requires an evaporator from which heat is evaporatively removed after conduction across some portion of the evaporator’s outer surface.  This not only requires some minimum pumping capability, but the Kapitza thermal impedance at each surface of the heat exchanger, plus the thermal impedance within the heat exchanger wall material require a minimum heat exchanger area for satisfactory operation.  A heat exchanger system at the Lawrence Berkeley Laboratory, having 1 m2 of 100 mm long, 0.4 mm wall electrolytic copper tubes effectively removed 35 watts at 1.8K.

To reduce the heat load to the evaporator, the in-coming liquid helium should be single phase, so as to be precooled as much as practical by heat exchanging with the low pressure evaporant.  This inlet should be metered by a valve that is controlled by the liquid level within the evaporator.  Redundant valves will increase the operational reliability.

To keep the 1.8K cool-down time reasonable, the pumping conductance should be adequate for 35 watts of cooling at 1.7K.

Using the evaporator to cool the system from 300K to 80K without a second valve would require injecting LN into the chamber above the Lambda-plate.  This is not recommended as one could not assure that LN would stay out of the lower chamber.  Hence, a second valve is required to inlet liquid nitrogen into the evaporator chamber.  As one also desires to remove excess LN without excessive pumping and have absolutely no chance of plugging the evaporator during 1.8K operation, the LN entrance into the evaporator needs to be at the very bottom of the chamber (to allow pressurized LN removal) and LN control valve needs to be reasonably super-fluid tight, with the volume above the valve connected to the evaporator pumping (for insurance against plugging the system with solid air).

Laboratory pressure safety requirements place a lower limit on the strength and number of reinforcement rings that are required for any proposed heat-exchanger wall thickness.  The thickness of the copper wall is influenced by the need for an adequately small thermal impedance, yet a reasonable number of reinforcing rings and a reasonable freedom from accidental puncture during magnet insertion or removal.

Differential thermal expansion must be considered at all superfluid joints.  Namely, a tight fit at 300K does not necessarily insure a tight fit when cold.  Furthermore, a tight fit when cold may mean a shrunk-stuck joint when warmed up.

III)  Specific Design Features:

A rugged, beveled, 3 cm wide, stainless-steel Lambda-plate sealing-ring is used approximately 1 meter below the top of the cryostat.  The bevel extends all the way to the wall and is fairly close (15 degrees) to vertical for four reasons:  1) to facilitate blind centering of the magnet during its insertion,  2) to facilitate blind centering of the lambda plate,  3) to provide a tight seal when cold (as the stainless shrinks more than the lambda-plate during cool-down), and 4) to reduce the chance of debris lying on the sealing surface and degrading the super-fluid seal.

The lambda-plate is a 40 mm thick Nema-Glass disk and has a matching outer bevel.  There are eight penetrations of this plate which have to be superfluid-sealable:

Three stiff (25 mm), nearly vertical stainless-steel rods support the magnet’s weight.  Their exact position depends upon their attachment to the magnet, the magnet temperature and the natural hanging location of the magnet (which may vary from magnet to magnet).  Hence, each rod has a spring-loaded seal that can adjust itself to its circumstances.  Each rod is polished in the neighborhood of the sliding seal, which is made from teflon that is sized to be tight when cold and loose when warm.  The teflon is backed by a stiff plate that helps center the spring and distribute its force more uniformly.  Stop-rings are present to help pop the lambda-plate loose during magnet removal and are positioned to keep the springs in their seats when relaxed.

Two high-current magnet supply leads are made flexible enough to permit permanent seals (swaged Teflon)

The diagnostic umbilical (300 small, stranded, copper wires) is also flexible enough to permit a permanent seal (swaged Teflon).

A spring-loaded pressure relief valve serves as a cold-gas or liquid cryogen supply valve when forced open against its spring (during gaseous cool-down and liquid accumulation).  It lies near the outside of the lambda plate in order to minimize cold-gas/hot-gas mixing during gaseous cool-down.

A second spring-loaded pressure relief valve, lies diametrically opposite and as far as practical from the above-mentioned cold-supply valve.  When forced open against its spring, it serves as a return path for warm gas during a gaseous cool-down and circumvents vapor-lock during liquid accumulation.

Some of the annular volume immediately beneath the lambda-plate sealing-ring is used for the annular evaporator.    with the inner (copper) wall of the reservoir serving as a heat-exchanger for the magnet volume.  In order to provide dual temperature (80K or 1.8K) operation, plumbing is supplied which allows the injection of either liquid nitrogen or precooled liquid helium into the reservoir.  Plumbing is also supplied to provide a pumping capability that is adequate for 35 watts of cooling at 1.7K.

Conclusions