# Test Ring for Ionization Cooling

Beta-functions and dispersions

Beam envelopes for acceptance of =4106 mm mrad and momentum spread of p/p=0.01

Parameters at the end of the lattice (target center)

BetaX[cm]=25.0109 	BetaY[cm]=25.0365

AlfaX=3.24266e-07     	AlfaY=-1.45101e-07  Qx=1.73298  Qy=1.73861

DispX[cm]=223.904 	DispY[cm]=0

DispPrX=7.11707e-07 	DispPrY=0

Energy=999.405

Momentum Compaction=-0.367054

### Optim file

$P0=1100;  =>        1100

$m=105.658;  =>     105.658

$E0=sqrt($P0*$P0+$m*$m)-$m;  =>  999.404719

$gamma=1+$E0/$m;  =>  10.4588646

$beta=sqrt(1-1/$gamma/$gamma);  => 0.995418614

$Hr=$P0/$c*1e11;  =>  3669.20453

$F=201.25e6;  =>   201250000

$Lambda=$c/$F;  =>  148.965217

#Cooling

$LenCool=60;  =>          60

$BetaStar=25;  =>          25

$BetaStarOpt=$LenCool/2/sqrt(3);  =>  17.3205081

$BetaEff=$BetaStar+$LenCool*$LenCool/$BetaStar/12;  =>          37

$EnLoss=0.28*$LenCool;  =>        16.8

$NCool=2*$E0/$EnLoss;  =>  118.976752

#Equilibrium emittance

$EmitN=$Me/$m*$BetaEff*$beta;  =>  0.17812755

$Emit=$EmitN/$gamma/$beta;  => 0.017109637

$Accept=$Emit*6*4;  => 0.410631288

# Beam life time due to decay

$TauDecay=2.2e-6;  =>     2.2e-06

$C=3724.53;  =>     3724.53

$NTurn=$gamma*$TauDecay*$beta*$c/$C;  =>  184.358119

# Synchrotron frequency

$FiAccel=60/180*$PI;  =>  1.04719755

$V0=$EnLoss/sin($FiAccel) ;  =>   19.398969

$Alpha=0.367;  =>       0.367

$q=$C/$Lambda;  =>  25.0026823

$NuS=sqrt($q*$V0*cos($FiAccel)*$Alpha/(2*$PI*$E0));  => 0.119052914

$dPoverP=0.002;  =>       0.002

$SigmaS=$Alpha/$NuS*$C/(2*$PI)*$dPoverP;  =>  3.65466556

$SigmaFi=$SigmaS/$Lambda*360;  =>   8.8321262

$SigmaFiTot=$SigmaFi*2.5*2;  =>   44.160631

$dPoverPTot=$dPoverP*2.5*2;  =>        0.01

#

$B=13;  =>          13

$L=$Hr/$B*$PI/4;  =>  221.675885

$bb="g bb g od g bb g";  =>g bb g od g bb g

OptiM

Energy[MeV]=999.40472   Mass[MeV]=105.658

Emittance: ex[cm]=$Accept  ey[cm]=$Accept  DP/P=$dPoverPTot

Initial:	BetaX[cm]=25.011 	BetaY[cm]=25.0364

AlfaX=-4.18726e-17 	AlfaY=-2.08701e-16

DispersX[cm]=223.904 	DispersY[cm]=0

Dsp_PrimeX=7.63326e-16 	DspPrimeY=0

X[cm]=0.000    	Y[cm]=0.000    	Z[cm]=0.000    	S[cm]=0.000

tetaX[deg]=0        	tetaY[deg]=0

#  Elements: O,I-drift, D,B-sector dipole, G-magnet edge

#       Q-quad, S-sextipole, C,CC-solenoid and its focusing part only

#       M-multipole(length=0), K,Z-transverse and longitudinal correctors

#       A,W-RF cavity(standing wave), E-electroctatic acc.section

#       X-transfer matrix (next 6 lines have to hold the matrix itself)

#       R-combined magneto-electrostatic bend, L - electrostatic quad

#       F-Litium lens, H-Scraper or aperture

begin lattice. Number of periods=1

iAbsorb o cc1 o2 $bb  o1 q2f  o1 $bb o3 cc2 o4

o4 cc2 o3 $bb  o1 q2f  o1 $bb o2 cc1 o iAbsorb

end lattice

begin list

iAbsorb	L[cm]=30

o          	L[cm]=20

od          	L[cm]=10

o1         	L[cm]=60

o2         	L[cm]=212.78

o3         	L[cm]=100

o4         	L[cm]=212.78

bb         	L[cm]=$L   	B[kG]=$B         	G[kG/cm]=0   	Tilt[deg]=0

g          	B[kG]=$B          Angle[deg]=11.25  EffLen[cm]=0  Tilt[deg]=0

cc1        	L[cm]=130        	B[kG]=72         	Aperture[cm]=20

cc2        	L[cm]=80         	B[kG]=49         	Aperture[cm]=20

q2f        	L[cm]=50         	G[kG/cm]=-0.004  	Tilt[deg]=0

end list of elements